|  | Department of the Interior Bureau of Land Management |  |
| --- | --- | --- |

COMMUNICATIONS SITE PLAN

BOULDER

BUTTE FIELD OFFICE

Prepared by the United States Bureau of Land Management

Butte Field Office

State of Montana

Approved: _______________________________________________    _________________

Field Manager						Date

BOULDER COMMUNICATIONS

SITE PLAN

I.	INTRODUCTION	1

A.	Terms and Definitions	1

B.	Purpose	2

C.	Site Description	2

D.	Area Served	2

E.	Access	3

F.	Site History and Development	3

G.	Goals and Objectives of Site Management Plan	3

II.	AUTHORITY AND DIRECTION	3

A.	Authority	3

B.	Relationship to Communications Site Lease	4

III.	GENERAL RESPONSIBILITIES	4

A.	The Bureau of Land Management	4

B.	Facility Owners and Facility Managers	4

C.	FCC and NTIA/IRAC	5

IV.	AUTHORIZED USES AND USERS WITHIN A FACILITY	5

A.	Exclusive Use of a Facility By a Single User	5

B.   Use by Multiple Users	5

V.	FEES	6

VI.	General Operation and Maintenance Direction	6

A.	Unique Resource Considerations at this Communication Site	6

B.	Wiring and Grounding	6

C.	Communications Equipment	7

D.	Cables and Transmission Line (Wave Guides)	9

E.	Radiation	9

F.	Utilities-Availability of and Requirements for:	10

G.	Sanitary Facilities	10

H.	Security And Law Enforcement	10

I.	Site Maintenance	11

J.	Inspections	11

K.	Fire Prevention and Hazard Reduction Requirements	12

L.	Access Maintenance and Restrictions	12

VII.	CONDITIONS FOR CONSTRUCTION, MODIFICATIONS OR EXPANSION	13

A.	Application Processing / Requirements / Responsibilities	13

B.	Construction Methods and Resource Protection	15

C.	Construction Inspection	16

D.	New or Remodeled/Expanded Buildings	16

E.	New or Remodeled/Expanded Towers	17

VIII.	SITE ASSOCIATION/ADVISORY GROUP	18

IX.	APPENDICES	19

A.	Site Map	19

B.	Authorized Facilities	19

C.	Site Photographs	19

D.	Inspection Checklist	19

E.	Communication Site Tenant/Customer Use Inventory	19

F.	Technical Data Report	19

INTRODUCTION

## Terms and Definitions

The terms used in this communications site management plan conform to the definitions listed in the April 22, 2005, Federal Register notice “Rights-of-Way, Principles and Procedures: Rights-of-Way Under the Federal Land Policy and Management Act and the Mineral Leasing Act” and clarifications provided in Bureau of Land Management (BLM) Handbook 2860-1 and the United States Code of Federal Regulations (CFR) 43 CFR 2801-2806.  In the event of a conflict, between the plan and these sources, the Federal Register notice and the BLM Handbook will govern. The words “lease” and “lessee” as used in this plan refer to the relationship between the Bureau of Land Management and the communications use leaseholder, the lessee.  The words “customer” and “tenant” refer to the relationship between the lessee and the occupants in the lessee’s facilities.

LEASE – An authorization issued to a communication facility owner or facility manager, allowing for the use of Public Lands to construct and or operate a communications facility and unless specifically prohibited, to sublease to occupants in that facility.

LEASEHOLDER OR LESSEE – Facility Owner/Facility Manager

CUSTOMER – Entities that pay a facility owner, facility manager or tenant for communications services and are not re-selling or broadcasting communications services to others

TENANT – A communications user who rents space in a communications facility and operates communication equipment for the purpose of re-selling, or broadcasting communications services to others for profit.

COMMUNICATIONS SITE – An area of Bureau of Land Management administered public land designated through the land and resource management planning process.  A communications site may be limited to a single communications facility, but most often encompasses more than one.  Each site is identified by name; usually a local prominent landmark, such as Boulder Communication Site.

FACILITY MANAGER – The holder of a Bureau of Land Management communications use authorization who leases space for other communication users.  A facility manager does not directly provide communications services to third parties.

FACILITY OWNER – Individual, commercial activities, organizations, or agencies that owns a communication facility on Federal land; own and operate their own communications equipment; and hold a communication use authorization.

NON-BROADCAST – This category includes Commercial Mobile Radio Service (CMRS), Facility Managers, Cellular Telephone, Private Mobile Radio Service (PMRS), Microwave, Local Exchange Network, and Passive Reflector.

BROADCAST – This category includes Television Broadcast, AM and FM Radio Broadcast, Cable Television, Broadcast Translator, Low Power Television, and Low Power FM Radio.

## Purpose

This plan is intended to be used by Bureau of Land Management (BLM) officials administering communication uses at Boulder, existing lessees, and applicants desiring a lease or a lease amendment.  The plan will be kept updated by amending pages or sections of the plan rather than issuing a revised edition of the plan.  When a revision is necessary, the plan will be amended by letter from the Butte Field Office Manager enclosing a copy of revised pages or sections.  The amendments will be consecutively numbered.

Overall management direction for the administration of communications sites is outlined in the Headwaters Resource Management Plan (RMP)(1984),  the U.S. Code of Federal Regulations (CFRs) and the BLM Handbook and applicable Instruction Memoranda.  Specific direction for site management planning on designated communications sites is contained in BLM Handbook 2860-1.  Primary regulations and policy pertaining to issuance of rights-of-way and leases by the BLM are found in Title 43, Code of Federal Regulations (CFR), Sections 2801-2806 and BLM Handbook 2860-1.

The Headwaters RMP does not specifically address communications uses.  Boulder lies within Management Unit #23.  Lands and Rights-of-Way (ROW) guidelines are contained on page 159 which states the unit:  “includes important seasonal wildlife habitat and high value forest land in the Eight Mile Creek and Boulder-Clancy areas.”  Lands are available for utility corridors.  This RMP is scheduled to be revised by October of 2006 and will address all communication sites in the Butte Field Office. The revision will recognize and designate the Boulder Site for low-power broadcast and low-power non-broadcast uses.

Primary management of this site is to ensure the integrity and usefulness of the senior two-way radio, low-power broadcast translator, point to point microwave and cellular uses at this site.  The maximum power output for the Boulder Communication Site is based on the maximum output allowed for two-way radio under the Federal Communications Commission’s rules at Title 47, Code of Federal regulations, Part 90.

There has never been a communication site plan prepared for this site.  This plan has technical standards for better management of the Boulder Communication Site.  This plan governs development and management of the site and will be modified in the future as needs and conditions warrant.  Any future uses must be designed, installed, operated, and maintained to be compatible and not interfere with the primary uses.

This site-specific plan is administrative in nature and is Categorically Excluded from further review under the National Environmental Policy Act (NEPA) (516 DM2, Appendix 1, 1.7).  Any additional development of the site will be addressed in a site-specific NEPA document.

## Site Description

The Boulder Communication Site is located on lands which are administered by the Butte Field Office, and located north of Boulder, Montana.  The legal description of the site is as follows:

T. 6 N., R. 4 W., Section 19 SE¼NE¼ , Principal Meridian Montana

Approximately 46º 15’ 34” North Latitude and 112º 09’ 08” West Longitude

The elevation of the site is approximately 5880 feet above mean sea level (msl).

Four facilities are currently located at the site.  A site map is provided as Appendix A.

## Area Served

This site does not serve a Ranally Metro Area (RMA).  The largest community served is Boulder, Montana.  Zone #9 in the fee schedule will be used for fee calculation purposes.  Fee determination is based in part on the population zone which may be adjusted annually based upon changes in population and growth or designation of an RMA.

## Access

Access to the site is from Interstate 15 through Boulder west on city streets to Depot Road and then to the Boulder Communication Site on BLM administered Lands.  The right-of-way across the BLM administered lands is part of the lease.  Maintenance on county roads is provided by Jefferson County.

## Site History and Development

## Boulder communication site was first developed by the Forest Service in 1975.  Jefferson County utilizes their facility for two-way public repeaters (MTM-25413).  Boulder TV Association operates a low-power TV translator facility (MTM-25024).  In 1994, WWC Holding was authorized to place a separate cellular facility at the site (MTM-82864).  Verizon Wireless built their facility in 2004 (MTM-94130).

Ample land area is available for future site development, but it is predicted that the existing buildings and towers should meet the projected demand at this site.

## Goals and Objectives of Site Management Plan

1.	To document site management policy, procedures, and standards which are not specified in BLM’s standard Communications Use Lease or Right-of-Way (ROW) grants.

2.	To manage Boulder as a low-power broadcast and non-broadcast site.  Future authorizations and additional uses must be designed to prevent degradation of the two-way public use which is the senior use at this site.

4.	To establish communication guidelines for operations within the communication site.

5.	To protect the interest of authorized site users by preserving a safe and electronically “clean” environment.

6.	To encourage efficient development and joint use of space and facilities whenever possible. New facilities will only be allowed after appropriate site-specific NEPA analysis, coordination with current lease holders and users, and once the existing facilities are filled to near capacity.

7.	The site will be systematically developed to maximize the number of compatible uses while ensuring the safety and protection of resources.

8.	The overall appearance of the site and the integrity of the natural environment will be improved through stringent maintenance requirements.   The BLM must pre-approve the paint color that is proposed for use on all exterior surfaces.  Surfaces must meet this new standard when the current surface needs to be repainted.

9.	Communication equipment located at the site will managed to be consistent with the RMP’s Visual Resource Management (VRM) guidelines as viewed from major travel corridors.

10.	This Communication Site Plan shall be amended as necessary to be consistent with the RMP and any subsequent revisions.

AUTHORITY AND DIRECTION

## Authority

Authorization of communications uses on Federal (BLM) land is granted by the Federal Land Policy and Management Act of 1976, 90 Stat. 2776 (43 U.S. C. 1761-1771) and is reflected in Title 43, Code of Federal Regulations (CFR), Sections 2801-2806

and WO IB 98-23.

Bureau of Land Management authority for communications site management planning is contained in Bureau of Land Management Handbook 2801-1, Plan of Development.  Direction on and policy for communication use authorizations is contained in Bureau of Land Management Manual (BLM Manual) section 2860.

Authority for the issuance of authorizations and/or licenses for the transmission and reception of electronic radiation for communication purposes is granted by Congress and administered by the Federal Communications Commission (FCC) and/or the National Telecommunication and Information Administration – Interagency Radio Advisory Committee (NTIA/IRAC).

## Relationship to Communications Site Lease

This site plan will be incorporated into all leases now and in the future issued for this communications site and must be used in conjunction with the lease. PROVISIONS OF THE SITE PLAN ARE ENFORCED THROUGH THE LEASE. Each lessee is expected to include the requirements of the lease and the site plan into any documents which describe the business relationship between the lessee and the lessee's tenants and customers. The lessee is responsible for enforcing those provisions.

GENERAL RESPONSIBILITIES

## The Bureau of Land Management retains the responsibility for:

Issuing and amending authorizations to Facility Owners and Facility Managers, only for the areas actually occupied by the authorized improvements.  Granting, occupancy and use of Public Lands rests exclusively with the Bureau of Land Management Title 43, CFR, Sections 2801-2806.  The issuance of a FCC license (authorization), or frequency assignment, does not authorize occupancy of Public Lands.

1.   Approving any new/modified facility(ies) at the site.

2.   Approving assignments or amendments to leases to qualified buyers of facilities on the site.

## Facility Owners and Facility Managers (or designated representatives) are responsible for:

- Complying with their authorization and all sections of the Site Management Plan.

- Ensuring that all new facilities, expansions, or improvements are consistent with the Headwaters RMP (1984); future revisions of the Headwaters RMP; any environmental document(s)/decisions for the site; and this Site Plan.

- Ensuring facilities/equipment not complying with Federal/State/local laws/regulations/ ordinances will be removed or modified within one year of the approval of this plan.  Any modification needs pre-approval by the BLM.

- Keeping all facilities within the established limits of their authorized area.

- Providing the BLM with the name, address and phone number for a local contact person.  The Facility Owner/Manager and the contact person may be the same individual.  The contact person will be available for emergencies and will have the authority to make decisions about construction issues, facility maintenance and all equipment within the facility.

- Adhering to the terms of the Facility Owner/Manager Lease or ROW as follows:

  - Facility Owners and Facility Managers with Communications Use Leases are authorized to rent building/tower space to tenants and/or customers without prior written approval from the BLM.

  - Tenants and/or customers using a facility covered by a Communications Use Lease will not have separate BLM Leases/ROWs to authorize their use except in situations where regulations or policy require them.

  - Facility Owners and Facility Managers are responsible for complying with the terms and conditions of the Facility Lease/ROW.  Facility Owner/Managers are also responsible for ensuring that their tenants and customers are in compliance with the terms and conditions of the Lease/ROW, and applicable FCC or NTIA/IRAC license terms and conditions.

  - Facility Owners and Facility Managers may not place any unreasonable restrictions nor any restriction restraining competition or trade practices on tenants and/or customers, or potential tenants and/or customers.

  - Tenants and/or customers may not construct their own equipment shelter (building, shelter or cabinet) or antenna support structure (tower or mast).  The Facility Owner/Manager must own all communication shelters and towers under their lease. [If that is not possible, a separate SF-299 application, cost-recovery deposit, analysis, and authorization are required.  This will also result in the use being a tenant/customer of the original lease holder in additional to being a separate facility for billing purposes.]

- Ensuring that all communication equipment is properly installed, operated, and maintained.

- Ensuring that all communication equipment meets ANSI, FCC and BLM regulations, guidelines and standards concerning radiation limitations.

  - Monitoring radiation levels at their facility and;

  - Immediately correcting any radiation levels that are, or could be a hazard to human health. (FCC 47CFR sections 1.1307(b), 1.1310 and 2.1093) and FCC OET Bulletin 54, August 1999.

- Providing a certified copy of their use and the category of use along with the current phone numbers and addresses of all tenants and customers as of September 30th each year.  This report is due by October 15th.  Facility Owners/Managers are responsible for submitting this information is submitted on time; BLM is not responsible for requesting the information. A Tenant/Customer Use Inventory Form is provided as Appendix E.

- Keeping the premises around their buildings free of trash and debris.

- Placing the Lessee/ROW holder’s name, address, phone number, BLM and FCC authorization numbers on their facility.

## FCC and NTIA/IRAC are responsible for:

The responsibilities of the FCC and NTIA/IRAC are frequency management.  Correcting interference problems is the responsibility of the affected licensees.  The FCC and NTIA/IRAC are not normally responsible for the resolution of conflicts when the licensees or agencies are operating within the limits of the authorizations.

AUTHORIZED USES AND USERS WITHIN A FACILITY

## Exclusive Use of a Facility By a Single User

All facilities are currently designed to accommodate multiple users.

## B.   Use by Multiple Users

The capacity of the current facilities is adequate on both the towers and within the existing buildings for future tenants/customers. Any future proposals must be designed to include multiple users.  This includes multiple use of buildings, towers, back-up generators, grounding systems, fuel containers, access ways and parking areas.

Due to the availability of building and tower space at the site, new facilities, or major modifications to existing facilities will generally not be approved until the empty space is utilized even if other users are, or could be, competitors.

Facility Owners and Facility Managers are not required to lease facility space to others if they can prove to the authorized officer of the BLM that:

- Space is not available;

- The use is incompatible with the existing facilities;

- Additional space is needed by the Facility Owner/Manager;

- Additional users would violate system security needs; or,

- Potential interference is not resolvable.

Any substantial expansion activities will require additional BLM approval and preparation of a site-specific NEPA analysis.  BLM reserves the right to approve a new facility through the NEPA process if current facilities cannot meet the new need.

FEES

The BLM will charge Facility Owners and Facility Managers annual fees based on the Fee Schedule for Communications Uses on Public Lands as adjusted annually.  These fees will be fair market value for the use of public lands.  Since this site is not within an established RMA, the population zone of less than 25,000 will be used for these calculations unless specifically agreed to by the authorizing officer.

Fees that Facility Owners and Facility Managers may charge their tenants and “customers” are to be:

Reasonable (consistent with, and not in excess of, other fees for similar facilities) and commensurate with the uses and occupancy of the facilities and services provided to the tenants and “customers”.

General Operation and Maintenance Direction

Upon renewal of expiring authorizations, existing communication site holders/lessees will not be required to upgrade or retrofit exiting installations to meet current building code requirements or new standard site plan requirements unless a safety issue or interference issue is identified.

## Unique Resource Considerations at this Communication Site

- There are no currently identified special resource considerations with on-site or adjacent resource values.  Should special conditions arise through the revision process of the RMP; this plan will be amended accordingly.

## Wiring and Grounding

1.	All equipment is to be installed within existing buildings and on equipment racks that are grounded and shielded.  Grounding is to be installed in accordance with accepted standards.

2.	All electrical wiring and grounding must meet the ‘National Electrical Code” and applicable state codes.  All permanent wiring shall be installed in metallic conduit.  Surge protection shall be installed on all power distribution panels.

3.	Lightning protection “down” conductors installed upon communications towers shall be treated as “Transmission lines”.  Therefore, they shall have an insulating jacket.  Periodic bonding of the down conductor to the tower (Galvanized) steel shall be made with proper bonding connectors that are tin plated or made of brass.

4.	Each building is to have its own separate grounding system for all users in that structure.  Wherever practical, interconnection of individual grids and/or the simultaneous placement of a large sized copper ground wire with any new grounding systems that are buried on the site will be required.

5.	Site or facility grounding must be constructed of copper, with #2 AWG or larger wire or 2” or larger solid copper strap, connected to an adequate site/facility ground electrode system.  The site/facility ground electrode system shall be bonded to the power service entrance grounding electrode conductor.  Guy wires should also be grounded using manufacturers approved methods to preclude bi-metallic junction and corrosion.  All equipment on the site (buildings, towers, power units, transmitters, receivers, antennas, combiners, telephone systems, power cabinets, HVAC units, etc) must be connected to the site/facility ground by direct connection.  Electrical system ground wiring is required for electrical ground fault protection and circuit breaker coordination.  The grounding systems shall comply with applicable laws, codes and in accordance with standard engineering practice.  Below ground connections must use either an exothermic welding process (i.e. Cadweld, Thermoweld, etc.), copper wedge pressure devices (i.e. Ampact, Wrench-lock, etc.), or brazed copper connections in conjunction with a mechanical UL listed connector (to be used as a physical strength enhancement component).  Brazing by itself is not an acceptable method of bonding below earth grade (buried).

## Communications Equipment

Equipment Ownership

All equipment shall be labeled with:

- The owner’s name;

- Transmitter frequency(ies);

- A valid FCC, or IRAF, authorization;

- Transmitting power output(s); and

- A current 24-hour phone contact number.

Transmitting Equipment

All transmitters will have protective devices (shields, filters, isolation components), designed into or externally installed, to prevent interference with other users.  All transmitters will meet FCC licensing requirements.

The re-radiation of intercepted signals from any unprotected transmitter and its associated antenna system will be prevented by the use of appropriate filters (wide band and narrow band broadcast transmitters).

The direct radiation of out-of-band emissions (i.e. noise or spurious harmonics) will be reduced to a level such that they may not be identified as a source of interference as defined in the FCC Rules and Regulations (e.g. Part 90.209(e)).  If electromagnetic noise becomes an issue at this site, prior to any additional uses, noise threshold limits must be established, and amended into the Site Plan.

All transmitters not in immediate use and not specifically designated as standby equipment shall be removed.  Loads connected to circulators are to be capable of dissipating the total power output of the transmitter.

Receiving Equipment

All receivers shall comply with all applicable parts of the FCC rules, including Parts 2 and 15.

All receivers shall have sufficient “front end” pre-selection to prevent receiver spurious response.  The use of bandpass, band-reject cavity or crystal filters may be required to prevent receiver-produced intermodulation or adjacent-channel interference is recommended at the input of all receiving devices.

Where duplexing is used, use of a notch type device should be avoided.  In situations where a notch type device is used, a bandpass filter must be used with the transmitter.

Tower

- All new construction, reconstruction and modifications to towers will require pre-approval by the BLM prior to implementation.

- Generally only one tower is authorized for each facility.  Facility Owners and Facility Managers may obtain permission to construct a second tower only after submitting evidence that demonstrates that their existing tower is completely filled and full use has been made of combining systems.  When a single equipment building is required, multiple antenna support structures may need to be designed and authorized to accommodate all uses without interference.

- All new and replacement towers shall be self supporting (lattice or monopole), and be made of non-reflective galvanized steel which will not require painting.  Guy wires will not be permitted.

- To avoid possible impacts to birds or bats, follow the most current version of the U.S. Fish & Wildlife Service’s Interim Guidelines on the Siting, Construction, Operation and Decommissioning of Communication Towers (available at http://migratorybirds.fws.gov/issues/towers/comtow.html).

- The maximum tower height for this site is 120 feet including the antenna.

- Anti-climb devices, removable steps, or other means to discourage unauthorized climbing, are highly recommended for facilities which are not enclosed by security fencing.

- No red and white striping, lights, beacons or strobes will be allowed on towers or antennas unless specifically required by the FCC or the FAA.

- All new and replacement towers will be treated for low to non-reflectance.  Paint is required only if they have a shiny (i.e. reflective) surface.

- All new and replacement towers will comply with current structural and safety specifications and design standards.

- All new and replacement towers will be designed using maximum wind, snow, and /or tower loading anticipated for the site.

Antennas

            - The maximum antenna height (including tower) will be 120 feet.

            - All antennas must meet all OSHA safety standards.  If an antenna exceeds FCC public or occupation standards (see FSS OET Bulletin 57), it will be remedied within 24 hours after measures are taken or isolated (e.g., fencing, signing, relocation, lowering power levels are all possible remedies).  Ground measurements of Radio Frequency Radiation (RFR) levels will be taken before mitigation measures are implemented.

            - Microwave (dish) antennas (other than ground mounted satellite dishes) will be limited to a maximum of ten (10) feet in diameter.  Smaller diameter dishes are preferred if technically feasible.

            - All radiating parabolic dish antennas need to be equipped with a radome (cover) for the prevention of perching on the feedhorn within the near-radiating field.  Manufacturer’s trademark on the radome shall not stand out.  Fences or other structures associated with the antenna shall be at a height to prevent perching in direct line with the beam.

            - Color(s) for dish antennas, or covers must be pre-approved by the BLM.  White dish antennas and/or covers will not be approved.  Existing white dishes and covers must be repainted or replaced with earthtone colors as repairs or replacements become necessary.

            - Antennas will be treated for low to non-reflectance.

            - High-power omni broadcast antennas placed on tapered towers will be installed with the least face width feasible.

            - Low-Power transmit and receive antennas will be located as close to the ground as feasible.

Interference

The responsibility for correcting interference problems is a matter for resolution between the Facility Owners or Facility Mangers, the user causing the interference, and the affected party(ies).  Generally, the first users on a site have seniority with respect to the resolution of interference complaints.  Senior holders have an obligation to maintain their equipment to industry standards, to operate their systems in accordance with the terms of both the FCC license and NTIA/IRAC frequency authorization, and to comply with the BLM authorization.  New users on a site must correct, at their expense, interference problems that they create.  They may be required to furnish an intermodulation study or other interference-related data and agree to accept financial responsibility for elimination or prevention of any interference caused by the facility before their application can be evaluated. They must cease operation of the suspect equipment until the problem is corrected.  If interference problems cannot be resolved or corrected within a reasonable time, the new use that is causing the interference may be terminated and the equipment removed.

The BLM does not have authority for correcting interference problems, but can act as a mediator to help all affected parties.  Interference problems must be coordinated with the FCC or NTIA/IRAC, whichever is appropriate.

Interference with law enforcement and/or emergency communications must be corrected immediately.  The operation of equipment covered by this Site Plan shall not interfere with United States Government radio or electronic operations already in existence on public land within two (2) miles of the site to which this authorization refers.  The user causing this interference, shall, at its own expense, take all action necessary to prevent or eliminate such interferences.  If it does not eliminate such interference within ten (10) days after receipt of notice from the BLM to do so, the use will be terminated.

If electromagnetic noise becomes an issue, noise thresholds will be established and this Site Plan will be amended accordingly.

## Cables and Transmission Line (Wave Guides)

All new cabling will be jacketed and shielded and shall either be flexible or semi-rigid type.  Existing substandard cables will be upgraded as repairs or replacement become necessary.

Cables will be properly installed and will be strapped and fastened down.

When attaching cables onto a tower, conduits should be used and cable runs should be equally divided among all tower legs.

All transmission lines (wave guides) are to be supported in accordance with manufacturer’s specifications.

Unjacketed transmission lines of any type are prohibited. No transmission lines shall be left unterminated.

Double shielded braided or solid shielded cable will be used.  No RG-8 type cable is permitted.  No connector-type adapters will be used on transmission lines.  Only correct connectors that will mate to connected devices are to be used.

Conduits will be shared when they service common areas and will be buried where possible.

## Radiation

All communications uses must meet ANSI, FCC and BLM regulations, guidelines and standards concerning radiation limitations.

Monitoring radiation levels at the site is the responsibility of all site users and will occur at intervals to comply with FCC regulations and guidelines.  A copy of the monitoring report will be provided to the BLM within 30 days of its completion.

Onsite RFR measurements will be taken using appropriate equipment that can adequately measure both on-tower and on the ground levels before mitigation measures related to RFR are implemented.

Security fences with RFR notice signs are required around areas that exceed public use levels.  All fencing location and design will require pre-approval by the BLM.

Warning signs will comply with ANSI C95.2 color, symbol, and content conventions.  Contact information including name and telephone number will also be included on warning signs.

Lowering power levels for on-tower access during maintenance will be coordinated between affected users.

Any identified RFR radiation problems that are, or could be, a human health hazard must be corrected within 24 hours after measurement tests have been completed or be removed from the site by the site user(s).  If the proposed corrective action involves any new ground disturbance, it will require pre-approval by the BLM.

## Utilities-Availability of and Requirements for:

Commercial Electrical Power

Commercial power is provided to the site under separate ROW grant to Northwestern Corporation      (MTM-22227).  The distribution line to the site and portions of the service drops are aerial.   Future service drops and future modifications will be buried.

Telephone Service

No hardwire, telephone service is provided to the site.  If this service is ever deemed necessary, site users will pay for the cost of:

- The necessary resource surveys and NEPA documentation reports for service connection, and

- The cost of constructing service connections.

For visual reasons, overhead utility poles will not be authorized.

Fuel Tanks

All Facility Owners/Managers are responsible for providing fuel storage (propane and diesel) and emergency power for their tenants.  No tenants/customers will be authorized the use of their own fuel tank and/or generator.  Fuel storage will preferably be consolidated into a tank large enough to accommodate all tenants/customers by each Facility Owner/Manager.  At a minimum, tanks will be grouped together in a consolidated area adjacent to their facilities.  All fuel, storage tanks (e.g. LPG, propane and diesel) must meet current fire department, Federal, State, and County safety and hazardous materials requirements.

- All tanks will be:

a.	Signed in red letters, “SMOKING OR OPEN FLAME PROHIBITED WITHIN 20 FEET”;

b.	In conformance with National Fire Protection Association (NEPA) requirements; and,

c.	Painted an approved color, or screened by an enclosure to blend in with the natural environment.  (If an enclosure is used, it must be pre-approved and painted an approved color).

2.	Diesel tanks will also be:

a.	Enclosed in BLM and fire department approved secondary containment vault that is painted an approved color.

b.	Constructed with underground fuel lines.  Fuel line must be constructed of black, treated pipe and fittings, and must be posted.

## Sanitary Facilities

Plans for any new sanitary facilities require pre-approval by the BLM.  If it is determined by the BLM that the user needs such facilities, they will be provided by the Lease/ROW holder in a manner and location satisfactory to the BLM and within the requirements of the County Health Department.

## Security And Law Enforcement

The Jefferson County Sheriff’s Department is the key law enforcement agency for the area.  They are responsible for most civil and criminal matters.  The BLM will be responsible for enforcing matters related to uses of BLM lands (e.g. resource protection issues).

Patrol and policing for security purposes is the holder’s responsibility.  If holders desire to have the protection of fencing, BLM approval must be obtained first.  To reduce visual clutter and efficiently utilize existing space, fencing groups of buildings will be encouraged.

Any access gates must be adequate for BLM and Fire Department access needs.

Fencing

Two facilities are currently fenced (MTM-82864 and MTM-91430).  Any new fences or future modifications to existing fences must meet the following criteria:

1.	All fences must meet health and safety requirements.

2.	All fence locations and design require pre-approval from the BLM.  The standard fencing type will be chain-link (i.e. cyclone).

3.	The standard fence height will be eight (8) feet.

4.	Fencing will be designed, maintained, and of a type to minimize interference issues.

5.	Fences will be signed with RFR notices if RFR is above public levels.

## Site Maintenance

The objective of maintenance activities is to present a clean, neat, and orderly appearance at the site and have all of the authorized improvements safe for workers and the public.  All users will keep up the overall appearance of the site.

Miscellaneous debris remaining after any construction and/or equipment installation, removal or modification, is not only a hazard, but can cause interference or intermodulation problems.  In particular, all loose wire or metal objects are to be removed from the site.

The users of the site will remove all graffiti within 10 working days of finding it (weather permitting).  If graffiti is on natural features (e.g. rocks), the graffiti will be removed in a method approved by the BLM.

Site users will not be permitted to leave or dispose of trash, garbage or cut brush on public lands.  No outside trash or litter containers will be allowed.  Site users will remove litter from the site as it is produced.

Policing of litter in common areas (i.e. areas between buildings and developed sites) is the shared responsibility of the users bordering these areas.

During construction and/or maintenance, paintbrushes will not be cleaned off on the rocks around the site and excess materials (e.g. cement) will be removed from public lands.

Peeling paint on buildings and/or towers will be re-painted within thirty (30) days of notification of the holder by the BLM (weather permitting).

Users are collectively and individually responsible for the control of noxious weeds within their authorized lease area.  Noxious weed management will be consistent with the goals and objectives of the BLM’s Partners Against Weeds Action Plan.

## Inspections

Unless waived in writing by the BLM, the holder is to provide, annually, a certified inspection of the facilities and equipment covered by the authorization.  The inspection will include technical review that assures that authorized equipment is operating within the specifics of this Site Plan, the FCC authorization, ANSI Standards, and the manufacturer’s specifications.  In addition, the inspection must assure that the authorized equipment is secure, free of rust, properly grounded, and otherwise properly operated and maintained.  This inspection should also review general good "housekeeping". A copy of the inspection report, certified by a telecommunication specialist, is to be provided to the Butte Field Office within 30 days of completion.  Appendix D provides an example of an inspection checklist.

The BLM may also conduct un-announced periodic reviews to monitor for authorization compliance.

## Fire Prevention and Hazard Reduction Requirements

Any fire will be immediately reported to “911”, the Helena Interagency Dispatch Center (HIDC) at (406) 444-4242 or the Jefferson County Sheriff’s Department at (406) 225-4075.

***************************************************************************************

Facility Owners/Managers will be required to maintain a minimum clearance of thirty (30) feet around the buildings and a minimum of ten (10) feet clearance around any propane tanks to serve as a vegetative gap or fire break.

Vegetative clearing must not negatively impact threatened, endangered, or sensitive plant species within the clearance areas.

Smoking is prohibited while walking in flammable vegetation.  Smoking materials must be properly disposed of.

Roof structures shall be kept reasonably clear of leaves, twigs, and other debris at all times.

No explosives will be stored at this site.  Flammable materials shall be stored in conformance with the requirements of local fire regulations.  Flammables will be placed in closed containers and stored away from sources of ignition and combustible materials.  If flammables are stored within a building, the building will be locked, properly signed and well ventilated.

Approved spark arresters will be required and maintained on all internal combustion engines.

At least one (1) U.L. rated 40 B:C dry chemical fire extinguisher is required inside each building.  Prior to each June, fire extinguisher(s) shall be inspected and refilled by holders, if necessary.

BLM Officers will make periodic fire prevention inspections.  They will call to your attention any lack of compliance with the above regulations, plus any other existing hazards.  Compliance with these inspections is required within the time limits specified in the inspection report.

## Access Maintenance and Restrictions

Roads

The current access is entirely on roads maintained by Jefferson County or on roads administered by the BLM.   BLM roads receive periodic surface maintenance as funding is available. The access roads are included in the Communication Use Lease.

Holders who damage or disturb the access road, or any associated structures, such as ditches, culverts, roadside vegetation, signs and/or underground utilities or facilities, will be required to repair the road or associated structures to conditions equal to or superior to those prior to any damage or disturbance.  These actions may require a new NEPA analysis.

Interior Site Driveways/ Parking Areas

Roads within the communications site will be maintained by the site users.  Interior roads will be planned and approved during establishment of new facilities.  Interior roads will be maintained in a manner to allow only one entrance to the site.  The intent is to discourage off-road vehicle use in and around the site.

Road Closures

Native surface roads are subject to periodic closures to entry during periods of extreme fire danger, inclement weather, or wet conditions.  Authorized users may use the site during these periods if advance approval is obtained from the BLM.

- Holder/Lessee Review

Facility Owners and Facility Managers will be given the opportunity to review and comment on new communication uses proposed for Boulder.  Applications and technical data information filed with the Butte Field Office will be copied and forwarded to each Facility Owner/Manager at the site, and processed as described in Section VII.

Facility Owners/Mangers proposing to accommodate additional tenants/customers within their facility will be responsible for sharing information regarding the proposed additions/changes with other site users. It is strongly suggested that the Facility Owners/Managers involve any tenants and customers in this review process.

Generally, the advanced notification/review period shall be a minimum of 30 days, but this time frame may be adjusted by the Butte Field Office depending on specific circumstances.  A Technical Data Report is provided as Appendix F

CONDITIONS FOR CONSTRUCTION, MODIFICATIONS OR EXPANSION

## Application Processing / Requirements / Responsibilities

When a new customer or tenant use cannot be accommodated by existing leases within existing facilities the following application process will be followed:

- Application Submissions:

Application forms are available from any BLM office and on the web at

http://www.fs.fed.us/recreation/permits/commsites/comm_forms.html

Note:  An application is not considered complete and cannot be processed until all information deemed necessary by the BLM Authorized officer is provided in an acceptable format.  Submission of an application does not guarantee approval of a Communications Use Lease or issuance of a Right-of-way grant.

a.   Pre-application Activity:

Applicants interested in occupying the Boulder Communication Site are encouraged to discuss proposals, prior to filing a formal application, with the BLM-Butte Field Office.  Guidance and information will be shared at the pre-application meeting and the application process will be explained.

b.   Need or Justification for a project:

New applicants will be required to demonstrate a valid need to occupy Boulder and the reasons why the existing communication facilities will not reasonably accommodate that need.  In addition, it is the applicant’s responsibility to show that any new facilities will make the most efficient use of space at the site.

c.   When An Application (SF-299) is Required:

--New facilities (sites, buildings, antenna, etc).

--Significant building modifications (size, shape, additions).

--Significant tower modifications.

--Changes in Type of Use (e.g. PCS to Microwave site).

--Changes in the ownership of existing facilities (assignments).

--Renewals of expiring authorizations.

Applications must be accompanied by the following items:

--Completed application form (SF-299).

--Copy of FCC license, construction permit, frequency assignment, station license, or NTIA/IRAC authorization.  If a license has not been issued, then a copy of the applicant’s application is required.

--Copy of FAA form 7460-1 or FAA approval letter (if required).

--Complete BLM Technical Data Report listing the applicant’s authorized frequencies.

--Documentation that shows proposed facilities will not be obstructing or interfering with, any existing fixed point to point antennas, omni directional broadcast antennas, or microwave beam paths in the directions of primary population targets.

--Documentation that the proposal will not cause undue interference with any existing uses.

--Complete Site/Plot Plan showing:

- Ties to existing site monuments (if available).

- Size (acreage & dimensions) of proposed (new) facilities (buildings, tower, auxiliary equipment, etc.) to be located within the proposed communication site.

- Land ownership of lands to be impacted (including ownership of land crossed by any needed access road or utility lines).

- Legal description (Township, Range, Meridian, Section, Aliquot parts (to 40 acres), of the proposed communication site, access road, utility lines, or other appurtenances.

- Identification of any microwave beam paths, a plot of their azimuth(s), and their proposed elevation(s) on the tower (if applicable).

- Estimated time frame for commencement and completion of construction.

Applications for proposed communication facilities on Boulder should be filed with the following office:

Bureau of Land Management

Butte Field Office

Attn:  Realty Specialist / Boulder Communication Site

106 North Parkmont

Butte, Montana 59701

Telephone inquiries should be directed to a Realty Specialist at (406) 533-7600.

d.  User Notification:

In addition to the items listed in “c” above, Facility Owners/Managers will be required to notify all communication site users in the vicinity when the following activities are contemplated:

--Additions of frequencies.

--Changes in frequencies.

--Changes in transmitter power output (TPO).

--Changes in antenna efficiency or ERP.

--Type or Class of Service changes.

--Changes in location of transmitters.

--Other conditions or situations as required by the BLM Authorized Officer.

2.	Application Processing:

Note:  In order to accelerate the processing of an application, an applicant may be asked to contribute to the environmental documentation or inventory process.  This contribution may consist of contracting cultural resource inventories, contracting biological inventories, (e.g. Threatened & Endangered Species), or in some cases, contracting the preparation of an entire environmental document.

--Application is filed with the Butte Field Office.

--Applicant is notified of a required, non-refundable filing fee.  The non-refundable filing fee must be paid prior to any formal application processing.  The establishment of a filing fee is an appealable action subject to review by the Interior Board of Land Appeals.

--County governments, impacted right-of-way holders, and other affected or interested publics are notified of the filed application.

--Inventory work is completed and an environmental document is prepared to fulfill the requirements of the National Environmental Policy Act of 1969 (NEPA) and other applicable laws and regulations.

--Unless the applicant’s application is rejected, a Communications Use Lease or ROW grant is prepared and forwarded to the applicant for review, acceptance of stipulations, signature, and payment of the required monitoring fee and rental charges.

--Upon return of the items to the Butte Field Office, an authorizing document is issued to the applicant from the BLM.

## Construction Methods and Resource Protection

Plans submitted by an applicant for any new construction or modifications shall specify provisions for soil rehabilitation measures including, but not limited to, soil replacement and stabilization and for proper handling of runoff from buildings, parking area, access roads, and undeveloped common areas.

The following methods and resource protection measures will be required to minimize impacts during construction:

1.	Avoid and protect sensitive resource areas, as identified by the BLM.

2.	Compliance with any Erosion Control Plan set forth by the BLM.

3.	During construction and/or maintenance, paintbrushes will not be cleaned off on rocks around site and no marks of any kind (including survey marks) will be permitted on rocks.

4.	Minimize ground disturbance and vegetation removal as much as possible during construction activities.  All ground-disturbing activities require pre-approval by the BLM.

5.	Any extensive cut and fill slopes will be re-vegetated with vegetation species approved by BLM as soon as possible after construction.  If necessary, reseeding will be required until vegetation is successfully established as determined by the BLM.

6.	No grading material will be cast off during construction/reconstruction activities. Excess soil can be used for fill material on road and/or building/tower pads.

7.	Temporary, on-site storage of construction materials will require pre-approval by the BLM.  However; if construction materials and supplies are left unattended, it will be at the owner’s risk.

8.	Hazardous materials, including, but not limited to all fuels, oils, and lubricants are not to be left unattended at the site at any time.  During construction, these materials are to be removed from the site at the end of each workday, or temporarily stored inside a locked and signed building until the following workday.

9.	All surplus construction materials and/or waste debris must be removed from the site no later than thirty (30) days after construction has been completed.

10.	Any earth moving or heavy equipment (e.g. dozers, graders, cranes, backhoes, etc.) leaving the designated roadway and/or approved parking area(s) to perform authorized activities at the site, will be washed off prior to being brought onto public land to prevent the introduction and spread of noxious weeds into the area.

## Construction Inspection

1.	All new construction, reconstruction, or major modification shall conform to the established technical standard and accepted engineering standards (i.e., the Uniform Building Code).  Where a conflict exists between Federal, State, or local sources, the most stringent requirements will dictate.

2.	Any construction inspections required by other applicable agencies are the responsibility of the holder.  Copies of completed inspections are to be provided to the Butte Field Office, either as they occur or as part of the final as-built plan.  Inspection information shall become a permanent part of the Lease/ROW holders’ case file.

3.	The Facility Owner/Manager agrees that corrective work detailed in BLM, or other agency required compliance inspections, would be completed by the scheduled completion date.  If the Lessee/Holder disagrees or has questions about specific items, they must contact the BLM in order that the disagreement or item may be resolved.

4.	A final set of as-built plans will be submitted to the Butte Field Office within 90 days of acceptance of structure (if contracted) or of completion date.

## New or Remodeled/Expanded Buildings

New proposals shall be designed as much as possible to take advantage of vegetative and topographic screening.  Proposals must provide sufficient data so that visual compatibility of the proposal, landform, vegetation changes, and lighting can be evaluated.  Consideration of a vegetative gap or fire break around of the proposed facility, to reduce wildfire hazards, shall be included in the design of any new proposals or to significant modifications to existing facilities.

  - Buildings are required to be one-story, flat roofed.  Proposals for wooden structures will not be approved.  The roof must be constructed of fire resistant materials (see 3c below).  Roofs can be equipped with antenna support structures, such as poles and railings that can extend up to 25-feet above ground level.

  - Facility owners and Facility Managers are encouraged to construct the interior of their buildings in a modular fashion, so that they can:

  - Sublease sections to others;

  - Provide tenants and customers with internal separation and security;

  - Reduce physical interference; and

  - Increase management effectiveness.

- The following materials are approved for construction of new/replacement facilities (i.e. buildings).

        - Floors – Concrete slab with drainage.

        - Walls – Concrete block, pre-fabricated concrete, or other pre-approved fire resistant materials.

        - Roof - Concrete slab or non-reflective metal, or other fireproof material as approved by the BLM.

        - Partitions - Concrete block, reinforced concrete, or properly grounded expanded metal. Other materials will be considered provided a minimum 3-hour fire exposure rating can be assured.

        - Color - Exterior colors should make the building as inconspicuous as possible.  The intent is to eliminate glare from reflective and/or illuminated surfaces such as window panes, sheeting and reflective paints.  Non-reflective, earthtone colors will be used on all equipment shelters and color selection will require pre-approval from the BLM.  Surfaces must meet this new standard when the facilities need repainting.

        - Pre-fabricated equipment shelters which meet the above requirements shall be preferred.

Building entry lights must:

a.   Only light the immediate area in the vicinity of the door;

b.   Be motion activated and have a limited time duration (e.g., 3-5 minutes); and

c.   Have a shielded beam that is pointed at the building door.

Requests for all-night (i.e. “dusk-to-dawn”) lighting, or entry lighting that would be visible from outside of the site will not be approved.

## New or Remodeled/Expanded Towers

- All new construction, reconstruction, and modifications to towers require pre-approval by the BLM prior to implementation.

- All new and replacement antenna support structures/towers shall be self supporting (lattice or monopole), and be constructed of non-reflective galvanized steel which will not require painting.  Guy wires will not be permitted.

- Anti-climb devices, removable steps, or other means to discourage unauthorized climbing, are highly recommended for facilities which are not enclosed by security fencing.

- No red and white striping, lights, beacons or strobes will be allowed on towers or antennas unless specifically required by the FCC or the FAA.

- All new and replacement towers will be treated for low to non-reflectance.

- It is the Facility Owner/Managers responsibility to assure that a new, or modified, structure will not unduly interfere electronically or physically with any existing equipment at the site.  Towers must be spaced, so as to prevent ground level radiation and/or interference problems.  This must be clearly demonstrated in writing to the BLM prior to issuance of a Lease/ROW, or amendment.

- All new and replacement towers should be as narrow and “open” as safety and structural integrity allow.

- New towers will be designed and constructed in accordance with the current addition of the EIA/TIA-RS-222 standards.

- All new and replacement towers will comply with current structural and safety specifications and design standards.

- Every structure shall be designed and constructed to resist stresses produced by lateral forces generated by seismic activity as per all applicable state and county seismic standards.

- All new and replacement towers will be designed using maximum wind, snow, and/or tower loading anticipated for the site.

- Antennas, dishes or other incidental communications equipment shall be securely attached to the antenna support structure/tower so that they remain attached under any and all events for which the structure was designed.

SITE ASSOCIATION/ADVISORY GROUP

A Site Association is not recommended for the Boulder Communication Site.  If formed in the future, the Site Association would be responsible for access maintenance and upkeep of internal roads and parking areas.  The Site Association would also be responsible for ensuring cooperation between users for on-tower access.  A Site Safety officer would be identified within the Site Association. The Site Association would be expected to develop a Radiofrequency Radiation Plan/Agreement and recommend measures to reduce interference issues (e.g., through use of filters).

The goal of the Site Association would also be to maximize the effective use of the site.  The objective of a sanctioned association will be to represent all site users as a group when dealing with the Butte Field Office on matters relating to the Site administration.  The association would be able to work in cooperation with the BLM, and County to identify problems or opportunities and make recommendations to these entities for any changes in management strategies at the site.  The association could also provide input to these entities regarding the future addition of equipment and facilities at the site. While the advice and recommendations of the association would not be binding on these entities, they could use the input for administration of the site.  The BLM and County or their representatives would be a member of such a group and would help jointly develop the charter (i.e., the ground rules).

In the absence of a formal Site Association, the BLM may utilize a Site Advisory Group that can make suggestions and/or recommendations to specific problems associated with the administration of the site.

APPENDICES

## Site Map

## Authorized Facilities

## Site Photographs

## Inspection Checklist

## Communication Site Tenant/Customer Use Inventory

## Technical Data Report

APPENDIX A

SITE MAP

APPENDIX B

LEASEE FACILITY TABLE

(See associated User’s Table on this Website)

|  | Auth # | Use | Building | Tower | Access/Parking | Other |
| --- | --- | --- | --- | --- | --- | --- |
| Facility 1 Jefferson County | MTM 25413 | PMRS | 11’x 10’ concrete | 40’ guyed | Access and parking |  |
| Facility 2 Boulder TV Association | MTM 25024 | LPTV | 8’x 8’ block | 40’ guyed Ground receiving Ground TV antenna | Access and parking |  |
| Facility 3 WWC Holding | MTM 82864 | CEL | 12’x 24’ block | 60’ lattice | Access and parking | Fence Propane Generator |
| Facility 4 Verizon Wireless | MTM 94130 | CEL | 20’x 30’ block | 120’ lattice | Access and parking | Fence Propane Generator |

APPENDIX C

SITE PHOTOGRAPHS

APPENDIX D

INSPECTION CHECKLIST

“Boulder Annual Technical Inspection”

Date Inspected: _____________________________   	Time Inspection: ________________________________

Permit Holder: ______________________________  	Authorization # _________________________________

Site Technician : ____________________________   	 Phone # _______________________________________

Number of Transmitters ______________________   	 License Posted _________________________________

Please mark the following Items as Acceptable (A) or Unacceptable (U).

Electrical Wiring ------------------- (A)     (U)        	Grounding --------------------- (A)     (U)

Equipment Installation ------------ (A)     (U)	Housekeeping ----------------- (A)     (U)

Building Repair -------------------- (A)     (U)	Tower Repair ------------------ (A)     (U)

Please mark the following Items as Yes (Y) or NO (N) or (NA)

Isolators ---------------------------- (Y)     (N)     (NA)	Circulators --------------------- (Y)     (N)     (NA)

Cavities ----------------------------- (Y)     (N)     (NA)	Terminators -------------------- (Y)     (N)     (NA)

Filters ------------------------------- (Y)     (N)     (NA)	Lightning Protection ---------- (Y)     (N)     (NA)

Comments: __________________________________________________________________________________

____________________________________________________________________________________________

Recommended Corrective Action:  ________________________________________________________________

_____________________________________________________________________________________________

_____________________________________________________________________________________________

Required Corrective Action To Be Taken:  __________________________________________________________

_____________________________________________________________________________________________

_____________________________________________________________________________________________

_____________________________________________________________________________________________

_____________________________________________________________________________________________

Committee Representatives:  _____________________________________________________________________

BLM Representatives: _______________________________________________________

Please make the required corrective action within the next 120 days.

Please make a written report of corrective action taken and submit to the BLM in Butte.  If  you should have any questions, please call the BLM office.

APPENDIX  E

COMMUNICATION SITE TENANT/CUSTOMER USE INVENTORY

COMMUNICATIONS SITE TENANT/CUSTOMER INVENTORY

CERTIFICATION OF FACILITY OWNER OR MANAGER

(as required by 43 CFR 2806.31(c) & clause III(A), Form 2800 - 18)

Name of Communication Site:  _________________________________________________________________

Name of Facility Owner or Manager:  ____________________________________________________________

Lease Authorization Number:  ___________________________

Do you, as the owner of this communications facility, operate any communications equipment in this facility? ____
If yes, what is your type of use (category & code)*?  _________________________________________________

List all occupants (users with a formal or informal agreement to lease space) of your facility on September 30 of this year.  Include occupants in your facility that may have a contractual agreement with someone other than you.

| OCCUPANT (Commercial Name) | TYPE OF USE (Category & Code)* | CUSTOMER or TENANT** |
| --- | --- | --- |

*See attached category and code descriptions.  Please review the definitions specific to cellular and microwave uses.

**"Customers" are individuals, businesses, organizations, or agencies that pay a facility owner, facility manager or tenant for communications services and do not resell communication services to others.  PMRS, “Internal Microwave” , and uses in the “Other” category, are considered “customer” uses when located in someone else’s facility,  "Tenants" are communications users that rent space in a facility and operate equipment for the purpose of reselling communications services to others.

NOTICE: The undersigned understands that it is a crime for any person to knowingly and willfully make false, fictitious, or fraudulent statements to matters under the jurisdiction of the United States Government (18 U.S.C. 1001).

I certify that to the best of my knowledge the information provided above is true, correct, and complete.

| Signature: |  | Date: |  |
| --- | --- | --- | --- |

According to the Paperwork Reduction Act of 1995, no persons are required to respond to a collection of information unless it displays a valid OMB control number.  The valid OMB control number for this information collection is 1004-0188 and 1004-0189.

This information is needed by the Bureau of Land Management to evaluate requests to use public lands and manage those lands to protect natural resources, administer the use, and ensure public health and safety.  This information is required to obtain or retain a benefit.  The authority for that requirement is provided by the Federal Land Policy and Management Act of 1976, which authorize the Secretary of the Interior to promulgate rules and regulations for authorizing and managing public lands.  This statute, along with the Mineral Leasing Act, , Wilderness Act,  Archaeological Resources Protection Act, and Alaska National Interest Lands Conservation Act, authorize the Secretary of the Interior to issue authorizations for the use and occupancy of public lands.  The Secretary of the Interior's regulations at 43 CFR 2801 and 2880 establish procedures for issuing those authorizations.

The Privacy Act of 1974 (5 U.S.C. 552a) and the Freedom of Information Act (5 U.S.C. 552) govern the confidentiality to be provided for information received by the Bureau of Land Management.  Public reporting burden for this collection of information is estimated to average 1 hour per response, including the time for review instruction, searching existing data sources, gathering and maintaining the data needed, and completing and reviewing the collection of information

Description of Communications Site Uses

###### BLM’s Communication Use Rent Schedule covers the following types of communication uses, including related technologies, which are located in a facility authorized by a BLM right-of-way grant or lease.  All use categories include ancillary communications equipment, such as microwave or internal one-or two-way radio, that are directly related to operating, maintaining, and monitoring the primary uses listed below.  The Federal Communications Commission (FCC) may or may not license the primary uses.  The type of use and community served, identified on an FCC license, if one has been issued, do not supersede either the definitions below or the procedures for calculating rent pursuant to 43 CFR 2801-2806 and subsequent interim directives for communication facilities and uses located on public land.

###### Broadcast Uses

AM and FM Radio Broadcast (AM or FM) means a use that broadcasts amplitude modulation (AM) or frequency modulation (FM) audio signals for general public reception.  Users include radio stations that generate revenues from commercial advertising and public radio stations whose revenues are supported by subscriptions, grants, and donations.  Broadcast areas often overlap State boundaries.  This category of use relates only to primary transmitters and not to any rebroadcast systems such as translators, microwave relays serving broadcast translators, or holders licensed by the FCC as low power FM radio.

Broadcast Translator, Low Power Television, and Low Power FM Radio (BT) means a use of translators, low power television (LPTV), low power FM radio (LPFM).  Broadcast translators receive a television or FM radio broadcast signal and rebroadcast it on a different channel or frequency for local reception.  In some cases the translator relays the signal to another amplifier or translator.  LPTV and LPFM radio stations are broadcast translators that originate programming.  This category of use includes translators associated with public telecommunication services.

Cable Television (CT) means a use that transmits video programming to multiple subscribers in a community over a wired or wireless network. These systems normally operate as a commercial entity within an authorized franchise area.  This category does not include rebroadcast devices or personal or internal antenna systems, such as private systems serving hotels or residences.

Television Broadcast (TV) means a use that broadcasts UHF and VHF audio and video signals for general public reception.  Users include television stations (major and independent networks) that generate income through commercial advertisement and public television stations whose operations are supported by subscriptions, grants, and donations.  Broadcast areas may overlap State boundaries.  This category does not include LPTV or rebroadcast devices, such as translators, or transmitting devices, such as microwave relays serving broadcast translators.

Non-Broadcast Uses

Cellular Telephone (CEL) means a system of mobile or fixed communication devices that use a combination of radio and telephone switching technology and provide public switched network services to fixed or mobile users, or both within a defined geographic area.  The system consists of one or more cell sites containing transmitting and receiving antennas, cellular base station radio, telephone equipment, or microwave communications link equipment utilized as back haul for that site.  The following uses may be categorized as Commercial Mobile Radio Service (CMRS) on an FCC license, however, for rent determination purposes these are all considered Cellular uses:  (1) Enhanced Specialized Mobile Radio (ESMR), (2) Improved Mobile Telephone Service (IMTS), (3) Air-to-Ground, (4) Offshore Radio Telephone Service, (5) Cell Site Extender, (6) Local Multipoint Distribution Service and (7) Personal Communication Service (PCS).  When both analog and digital equipment are operated at a site, two cellular(CEL) uses are inventoried to determine the appropriate fee.

Commercial Mobile Radio Service (CMRS) means commercial mobile radio uses that provide mobile radio communications service to individual customers.  Examples of CMRS include: Community repeaters, trunked radio (specialized mobile radio), two-way radio voice dispatch, public switched network (telephone/data) interconnect service, microwave communications link equipment, and other two-way voice and paging services.

Facility Manager (FAM).  A facility manager does not directly provide communications services and does not hold an FCC license to operate communications equipment.  “Facility Managers” are lease holders that lease building, tower, and related facility space to a variety of tenants and customers as part of the holder’s business enterprise, but do not own or operate communication equipment in the facility for their own uses.

Local Exchange Network (LEN) means a radio service that provides basic telephone service primarily to rural communities.  Rent for LEN uses, as well as wireless internet service provider uses for populations less than 1,000, are determined from regional rent schedules developed by the US Forest Service.

Microwave (MIC & INT MIC) means communication uses that (1) provide long-line intrastate and interstate public telephone (including relay of cellular traffic from other cellular sites), television, and data transmissions (common carrier, code MIC), or (2) support the primary business of pipeline and power companies, railroads, and land resource management companies by providing the companies’ internal communication system (internal microwave or INT MIC), or wireless internet service provider (MIC-ISP).  When a portion of the microwave bandwidth is used as a separate, commercial enterprise, a separate microwave use shall be inventoried for fee calculation purposes.

Other Communications Uses (OT) means private communications uses, such as amateur radio, personal/private receive-only antennas, natural resource and environmental monitoring equipment, and other small, low-power devices used to monitor or control remote activities.  These facilities are personally owned and not operated for profit.

Passive Reflector (PR) includes various types of non-powered reflector devices used to bend or ricochet electronic signals between active relay stations or between an active relay station and a terminal.  A passive reflector commonly serves a microwave communications system.  The reflector requires point-to-point line-of-sight with the connecting relay stations, but does not require electric power.

Private Mobile Radio Service (PMRS) means uses supporting private mobile radio systems primarily for a single entity for mobile internal communications.  PMRS service is not sold to others and is limited to the user.  Services generally include local internal radio dispatch for municipalities, utilities, and non-communications businesses, private paging services, and ancillary microwave communications equipment for the control of the mobile facilities.

Wireless Internet Service Provider (MIC-ISP) utilizes wireless technology to connect subscription users to the internet.  The ISP is a microwave use for rent determination purposes, except for populations served of less than 1,000 when the FS regional rent schedules for the Local Exchange Networks may be used if it is advantageous to the holder.

APPENDIX  F

BLM TECHNICAL DATA REPORT

USDI - BLM

TECHNICAL DATA REPORT

FOR NEW OR ADDITIONAL COMMUNICATION SITE USE

| 1. Applicant’s Name & Address: Address: Telephone No.: ( ) | 2. Right-of-Way MTM- | 3. State Montana | 4. County |
| --- | --- | --- | --- |
|  | 5. Field Office Butte | 6. District | 7. Elevation |
|  | 8. (a) Township | (b) Range | (c) Section |
|  | 9. LOCATION APPLIED FOR: Site Name: Latitude: Longitude: | 10. FCC OR NTIA SERVICE APPLIED FOR: |
| 11. Type of Application: Federal ; State ; County ; City ; Utility ; Corporation ; Farm ; Business ; Company_________;Other (Specify) |
| 12. Name, Address, & Telephone No. of Person(s) to Contact In Case of Emergency: |
| 13. Will a Telephone Be Available At The Site? YES NO IF YES, WHAT IS THE TELEPHONE NUMBER? |
| 14. Type of Electrical Power Planned: Commercial? YES NO # Phases ______ Solar w/battery? YES NO ; Wind w/battery? YES NO ; Battery Only YES NO____; 15. Standby Power: NO YES TYPE: |
| 16. Type of Operational Local Control: Automatic Repeater: Wire Remote: Control Planned:_______ Radio Link Remote: Other: ________ |
| 17. Is Repeater Tone Protected? YES NO |
| 18. Antenna Mounting Structure: Wood Pole: YES NO Steel Tower: YES NO Treated: YES NO Manufacturer: Number Planned: Model Number: Number Planned: Height Above Ground: ft. Diameter of Pole or Tower: ft. Distance from Building: ft. Space for Other Users? YES NO On a separate sheet, draw a site sketch showing building and antenna structure placement. Show height above ground on each on sketch. Orange stakes, showing the exact location of planned structures, will be required at the site prior to construction. |
| 19. REMARKS: |

TRANSMITTER EQUIPMENT TECHNICAL INFORMATION

20. Transmitter: Manufacturer: Model No.: Serial No.: ___________ Type Accepted No.: Age: (years) New: Model Year: _________

21. Combiner Manufacturer: ___________ Model No.: _____________ Duplexer________ Cavity Age: (years) Serial No.: __________ New: Model Year: No. of Tx’s on System: _______ Rack Mount? YES NO Cabinet Mount? YES NO___ Free Standing? YES NO Type Fittings Used: N UHF BNC________

22. Transmitter Isolators or Circulators Used: Manufacturer: ______ Model No.: ______________ Age: (years) Serial No.: ___________________ New: Model Year: Number ISO Used: ___________ Total Isolation Achieved: db.

23. ANTENNA SYSTEM: CABLE SYSTEM: Manufacturer: Manufacturer: ______________________ Type: Cable Diameter: ____________________ Model: Cable Length Inside Building: ft. Gain: db Age: (years) New: Cable Length Outside Building: ft. Direction: (degrees) Cable Fittings Type: N UHF BNC Height: (AGL) Top: ft. Bottom: ft. Cable Type: _______________________ Polarization: Horizontal: Vertical: Circular: ________________ NUMBER OF FITTING ADAPTERS USED IN TRANSMITTER SYSTEM: _______________________

24. Emission: Call Sign: Emission Type: _______________________ True Power: (watts) Emission Bandwidth: (watts) ERP: (watts)

25. FREQUENCIES: (Mhz, Ghz, Khz) It is understood the transmitter will NOT be placed in service without a license. Initial: _______

26. OTHER RELATED DATA: (tones, etc.)

RECEIVER EQUIPMENT TECHNICAL INFORMATION

| 27. Receiver: Manufacturer: ________________________________ Model No.: __________________ Type Accepted No.: Serial No.: __________________ Age: (years) New: Model Year: |
| --- |
| 28. Multicoupler: Manufacturer: Model No. ________________ Duplexer: ____________ Cavity: Age: (years) Serial No.: _________________________ New: Model Year: Number of Px’s on System: __________________ Rack Mount? YES NO Cabinet Mount? YES NO _________ Free Standing? YES NO Type of Fittings Used: N UHF BNC _____ |
| 29. ANTENNA AND CABLE SYSTEM USED: Same as transmit antenna and cable system? YES NO ANTENNA: CABLE: Manufacturer: Manufacturer: _______________________ Type: Type: _______________________________ Model No.: Diameter: Direction: Length Inside Building: ft. Height (AGL) Top: ft. Length Outside Building: ft. Height (AGL) Bottom: ft. Type of Fittings: N UHF BNC__ Polarization: Vertical Horizontal ________________________ NUMBER OF FITTING ADAPTERS USED IN RECEIVE SYSTEM: ______________________________ |
| 30. FREQUENCIES: (Mhz, Ghz, Khz) |
| 31. OTHER RELATED DATA: (tones, etc.) |
| 32. SIGNATURE: | TITLE: | DATE: |

# Text boxes

Facility 1

Jefferson County

Facility 2

Boulder TV Association

Facility 3

WWC Holding

Facility 4

Verizon Wireless