USDA Rural Development

Tennessee State Office

(Single Family Housing Loan Programs)

All approved dealer/contractors shall provide evidence to Rural Development that the following conditions have been met in order to qualify for Rural Development financing:

- Each manufactured unit financed by Rural Development shall be new and must be constructed to meet HUD’s, Federal Manufactured Home Construction and Safety Standards (the HUD Code-FMHCSS).

- The manufactured housing units must meet all local, state and federal requirements and statutes for the manufacture and installation of those units.

- All manufactured units and their sites must meet all requirements of RD Regulation 7 CFR Part 3550, Section 3550.73 and all applicable parts of RD Instructions 1924-A, 1980-D, and HB-1-3550.

- A one (1) year “Builders Warranty”, Form RD 1924-19, or a ten (10) year Warranty with 1 Year Workmanship/2 Year Systems & 10 Year “Structural” Coverage must be executed at the completion of the development, in addition to furnishing all applicants with a copy of all manufacturer’s warranties.

- All manufactured houses must be set up on permanent foundations constructed in accordance with the Department of Housing and Urban Development’s (HUD’s) Permanent Foundation Guide for Manufactured Housing or RD Instruction 1924-A, Exhibit J.  Permanent foundations shall consist of a continuous reinforced concrete or masonry perimeter wall, reinforced concrete or masonry piers, and anchoring/tie down systems, in accordance with the referenced standards and must include the following:

- A continuous footing for all permanent foundation walls shall run along the entire perimeter of the manufactured housing unit.  The perimeter footing shall be reinforced concrete and extend to below the frost line.  All load-bearing masonry walls shall be a minimum of 6 inches thick. Non-load-bearing masonry perimeter walls shall be a minimum of 4 inches (nominal) thick.  All permanent perimeter foundation walls constructed of pre-cast concrete masonry block or bricks shall have mortared head and bed joints.

- Footings for piers that are required to support the steel chassis beams/girders shall be poured, reinforced concrete. Size and spacing of the footings and the locations of the support piers shall be according to the HUD-approved Manufacturer’s Set-Up Manual.  Support piers shall be constructed of poured, reinforced concrete or concrete masonry units (blocks) with mortared head and bed joints.  Piers shall be capped across their entire surface by 4inches (nominal) of solid masonry, two inches (nominal) of hardwood, or steel plates.  Plywood or soft wood species are not permissible.  Dry-stacked masonry block piers shall not be permitted.

- Anchors for the units shall consist of steel straps tied directly to anchors embedded in the poured concrete footings.  These straps must be tightened to secure the unit against wind and seismic forces.  Ground or screw-in anchors shall not be permitted.  However, other State-approved anchoring systems may be allowed, if documentation of State approval is submitted prior to the installation.

- The Dealer/Contractor must provide a legible and dimensioned set of drawings and specifications in order for the inspector to make an informed inspection of the foundation work.  Drawings and specifications for the foundation and anchoring system must be certified to meet the approved Manufacturer’s Set-Up Manual on each loan by a plan reviewer recognized by RD.  All structural design must be completed by a licensed engineer and shall meet the requirements of the HUD Permanent Foundation Guide for Manufactured Housing or RD Instruction 1924-A, Exhibit J.

- Thermal performance of each manufactured housing unit must meet or exceed the HUD Uo Climate Zone II insulation requirements.  Prior to the manufactured unit being delivered to the site and/or placed on the permanent foundation, a Manufacturer’s “Comfort Heating and Cooling Certificate” must be provided to Rural Development showing the thermal specification for the unit.  If a manufactured housing unit is constructed with an insulation thickness exceeding the HUD Uo Climate Zone II insulation requirements, then the additional insulation and framing may be recorded as an upgrade in the appraisal to reflect the additional cost/value.

- Each new unit financed shall have a rain guttering and downspout system and concrete splash blocks installed as part of the basic sales package.

- At a minimum, each new unit financed will include a basic landscaping package consisting of a minimum of two (2) six-foot trees and the lawn will be seeded and strawed with the seed variety and application rate consistent with other homes in the immediate neighborhood.

- The front, primary entrance will have a concrete porch or stoop with a minimum width and depth of 48-inches by 48-inches, with the reinforced concrete footing connected to the perimeter footing for the permanent foundation.  All steps, which may include pre-cast concrete steps, from the porches or stoops to entry doors shall have hand rails that comply with the current version of the International Residential Code.  Decks that are a minimum width and depth of 48-inches by 48-inches are acceptable for side and rear entrances.  Decks must be site built and meet the requirements of the current version of the International Residential Code.  Railings are required around the porches, stoops, or decks if the floor surface is higher than 30 inches above grade.

- The front entrance walkway must be poured concrete with a minimum width of thirty-six (36) inches extending from the porch or stoop to the driveway.  Pre-cast concrete stepping stones are acceptable for walks leading to side and rear entrances.

- Driveways shall have a wear surface consistent with other drives in the development or area.  If other driveways in the development are paved with asphalt or concrete, the driveway for the subject units shall be the same type of construction.  In some locations, gravel will be an acceptable surface material.  Drives will be a minimum of 8 feet in width and, when possible, extend to at least the front edge of the dwelling.

- Roof pitch shall be a minimum of 4/12 (nominal).