HT/2000

Rugged Hand-Held Terminal

Engineered for Toughness

The rugged HT™/2000 is designed to provide reliable and continuous operation in the harshest operating environments. Packaged in an appealing low-profile, impact resistant Lexan® case, the HT/2000 is engineered to withstand repeated drops to concrete and to resist liquid and other contaminants, without sacrificing ergonomic detail. For even further protection in extremely harsh environments, a rubber boot and extended temperature components can be added, and the electronics conformally coated.

The HT/2000 features a 4 x 20 supertwist LCD; a sealed, membrane or elastomeric keypad (up to 66 keys); RS-232, RS-422 or RS-485 serial communications; and a rugged integral interface cable with various connector choices. HT/2000 options include an 8 x 26 supertwist graphics LCD, a bar code interface, wide-range power input, display and/or keypad backlighting, and an emergency stop and/or liveman switch.

WPI

WPI Termiflex, Inc.—

ISO 9001 Certified

WPI Termiflex designs and manufactures rugged hand-held and panel-mount operator interface terminals for service/setup, control and/or data collection applications. Our customers include commercial, industrial, medical, and military OEMs of microprocessor-based equipment all over the world. We specialize in tailoring and customizing our units to your specifications to solve all your man-machine interface challenges. Our entire product line may be customized with corporate logos, colors and serial number tags, as well as customer-defined keycodes, display prompts, keypad legends, cables and connectors. Several models are also PC programmable for even greater flexibility.

WPI Termiflex is ISO 9001 certified—an achievement recognized worldwide as a measure of an organization's design, development, production, installation and service quality.

TERMIFLEX, INC. MICRO PALM, INC.

WPI Group Companies

FEATURES

Rugged industrial package

Low-profile, 1” Lexan case

4 x 20 or 8 x 26 supertwist LCD

Display/keypad/backlighting optional

Membrane or elastomeric keypad

User-selectable parameters

RS-232, RS-422, RS-485 or TTL serial interface

150 to 19.2 baud communication

Retractile cable

Factory-customizable by design

Emergency-stop and liveman switches available

3-year warranty

HT/2000 Product Specifications

Factory-Set Options

EL Backlight Display/Keypad

8x26 STN LCD

Bar Code Interface

Custom Key Codes*

Key Repeat Rate*

Audible Keys*

Keystrings*

Character Transmit on Make/Break*

Serial Interface

Interface Cable Configuration

Custom Logo Graphics

Custom Keypad Graphics

Custom Serial Number Label

Custom Optional Label

Custom Firmware Operation

Custom Terminal Emulations

Emergency-stop Switch

Liveman Switch

Wide Range Power

Extended Temperature Operation

Moisture/Dust Resistance

* Selectable per key

TERMIFLEX, INC.

MICRO PALM, INC.

WPI  Group Companies

316 Daniel Webster Highway, Merrimack NH  03054-4166  USA

Telephone: 603-424-3700  Facsimile: 603-424-0330

HT is a trademark of WPI Termiflex.

Lexan is a registered trademark of General Electric.

WPI Termiflex reserves the right to change specifications without notice. If this information does not meet your application, please contact the factory to discuss the necessary changes.

Spec 994   Copyright 1994

| DISPLAY |
| --- |
|  | Technology: | Supertwist LCD, dot matrix |
| Format: | 4 x 20 standard; 8 x 26 optional |
| Displayable ASCII: | 96 |
| User-defined Characters: | 3 (4 x 20 LCD only) |
| Visual Indicators: | Flashing characters |
| Backlight: | Electroluminescent, optional |
| KEYPAD |
|  | Type: | Sealed membrane or elastomeric |
| Number of Keys: | 34 membrane; 66 elastomeric |
| Transmittable ASCII: | 128 |
| Programmable Function Keys: | 4, up to 16 ASCII characters each |
| Key Legends: | Catalog or customer-defined |
| Response: | Tactile, audible, visual (if local echo on) |
| Backlight: | Electroluminescent, optional (membrane only) |
| INTERFACE |
|  | Type: | RS-232, RS-422, RS-485 or simplified RS-232 (TTL) |
| Baud rate: | 150-19.2K |
| Parity: | Even, odd, space, mark, none |
| Stop Bits: | 1 or 2 |
| Data Bits: | 7 or 8 |
| Connector: | DE-9, DA-15, DB-25, or 9-pin circular |
| Cable Length: | 6 ft. retractile (optional lengths available) |
| Cable Type: | 6-conductor, shielded |
| Detachable Cable: | Optional, with case-mounted DE-9, DA-15, or telco modular jack connector |
| POWER |
|  | External Power: | +5 Vdc (+5%); +7 to +28 Vdc optional |
| Enhanced Brownout Protection: | Full RESET for host voltage drop below tolerance specification |
| Current (Max): | RS-232—50 mA; RS-422—70 mA; add 40 mA for optional backlight |
| MECHANICAL |
|  | Dimensions: | 8.0" x 4.25" x 1.0"(203.2 mm x 107.9 mm x 25.4 mm) |
| Weight: | 12 oz (340.2 g) |
| Case: | Lexan® plastic (gray/black) |
| ENVIRONMENTAL |
|  | Operating Temperature: | 0°C to +50°C; -20°C to +70°C optional |
| Storage Temperature: | -20°C to +70°C |
| Humidity: | 95% noncondensing |
| Moisture/Dust Resistance: | Optional |

AGENCY APPROVALS

FCC Class A, Part 15 CENELEC (CISPR 22) EN 55 022

User-Selectable Options

Baud Rate

Parity and Parity Error

Detection

Data/Stop Bits

Backlight On/Off (option)

Backlight Intensity (option)

Cursor On/Off

Audible Key Response

Function Key Content

Local Echo

Key Repeat

Display Control Characters

Self-Test On/Off

Shift Disable

Cursor Positioning

User-defined Characters

Save Options

Flashing Characters

XON/XOFF Flow Control

Accessories

Carrying Case

Rubber Boot

Mounting Bracket

Hanging Clip