APPENDIX A

Glossary

Terms are given in alphabetical order with numbers preceding letters, lower-case preceding upper-case letters, and Greek Letters following.

| Parameter | Definition | Chapter |
| --- | --- | --- |
| a | Parameter used in the Watt spectrum. | 5 |
| al | lth Legendre coefficient. | 4,6,14 |
| Ak,l | Probability of emission of a γ ray of energy Eγ=εk-εl as a result of the residual nucleus having a transition from the kth to the lth level. | 11 |
| Al | Legendre coefficients (LANG=0) or μ,pi pairs for tabulated angular distribution (LANG>0). | 6 |
| An | Mass of the nth type atom; Ao is mass of the principal scattering atom in molecule. | 7 |
| ABN | Abundance (weight fraction) of an isotope in this material. | 2,32 |
| AC | Channel radius | 2 |
| AC1, AC2, AC3, AC4, BC1, BC2 | Background constants for the Adler-Adler radiative capture cross section. | 2 |
| AF1, AF2, AF3, AF4, BF1, BF2 | Background constants for the Adler-Adler fission cross section. | 2 |
| AG | Reduced-width amplitude. | 2 |
| AJ | Floating-point value of compound nucleus spin, J (resonance spin). | 2,32 |
| AL | Floating point value of the angular momentum, l. | 2 |
| ALAB | Mnemonic of laboratory originating evaluation. | 1 |
| ALRE1…ALRE4 | Exit-l-value for reaction. | 2 |
| AMUF | Number of degrees of freedom used in fission-width distribution. | 2 |
| AMUG | Number of degrees of freedom used in radiation-width distribution. | 2 |
| AMUN | Number of degrees of freedom used in neutron-width distribution. | 2 |
| AMUX | Number of degrees of freedom used in competitive-width distribution. | 2 |
| AP | Scattering radius. | 2,32 |
| APL | l-dependent scattering radius. | 2 |
| APSX | Total mass in neutron units of the n particles being treated by LAW=6. | 6 |
| AS | Floating point value of channel-spin s. | 2 |
| AT1, AT2, AT3, AT4, BT1, BT2 | Background constants for the Adler-Adler total cross section. | 2 |
| AUTH | Author of evaluation. | 1 |
| AVGG | Statistical R-matrix parameter. | 2 |
| AWD | Atomic mass (not a ratio) of the daughter nucleus. | 2 |
| AWI | Projectile mass in neutron units. | 1 |
| AWP | Product mass in neutron units. | 6 |
| AWR | Ratio of mass of atom (or molecule) to that of the neutron. | all |
| AWRI | Ratio of mass of particular isotope to that of the neutron. | 2,32 |
| AWRIC | Mass-ratio for charged-particle exit channel (see page D.40). | 2 |
| AWT | Nuclear mass (not a ratio) of outgoing particle. | 2 |
| AZD | Atomic number of daughter nucleus. | 2 |
| AZP | Atomic number of outgoing particle. | 2 |
| b | Parameter used in Watt spectrum. | 5 |
| bi(E,E') | Representation of angular part of fi(μ,E,E'). | 6 |
| Bi(N) | List of constants. | 7,12 |
| BC | Boundary-condition parameter. | 2 |
| BR | Branching ratio for production of a particular nuclide and level. | 8 |
| Cn | Coefficients of a polynomial; NC coefficients are given. | 1 |
| Cn(Ei) | Array of yield data for the ith energy point; contains 4 parameters per fission product. | 8 |
| CI | Channel index. | 2 |
|  | Coefficient of the cross section for a reaction contributing to the value of a "derived" cross section (usually ±1.0). | 31,33 |
| CONT | Smallest possible ENDF record, a "control" record. | all |
| CT | Chain indicator. | 8 |
| D | Mean level spacing for a particular J-state. | 2,32 |
| DDATE | Original distribution date of the evaluation. | 1 |
| DE2 | Variance of the resonance energy ER. | 32 |
| DECr* | Resonance energy for the radiative capture cross section. | 2 |
| DEFr* | Resonance energy for the fission cross section. | 2 |
| DETr* | Adler-Adler resonance energy for the total cross section. | 2 |
| DF2 | Variance of GF. | 32 |
| DG2 | Variance of GG. | 32 |
| DGDF | Covariance of GG and GF. | 32 |
| DJ2 | Variance of AJ. | 32 |
| DJDF | Covariance of AJ and GF. | 32 |
| DJDF | Covariance of AJ and GF. | 32 |
| DJDG | Covariance of AJ and GG. | 32 |
| DJDN | Covariance of AJ an GN. | 32 |
| DN2 | Variance of GN. | 32 |
| DNDF | Covariance of GN and GF. | 32 |
| DNDG | Covariance of GN and GG. | 32 |
| DWCr* | Value of Γ/2, (ν), used for the radiative capture cross section. | 2 |
| DWFr* | Value of Γ/2, (ν), used for the fission cross section. | 2 |
| DWTr* | Value of Γ/2, (ν), used for the total cross section. | 2 |
| DYC | 1-σ uncertainty in cumulative fission-product yield. | 8 |
| DYI | 1-σ uncertainty in fractional independent fission-product yield. | 8 |
| {Ek} | List of energies for a covariance file energy grid | 32-40 |
| E | Energy of the incident neutron (eV). | all |
| E | Secondary neutron energy (eV). | 5,6,7 |
| E1,E2 | Range of neutron energies. | 31,33 |
| Eavail | Available energy. | 5 |
| Eint | Interpolation scheme for each energy range (Appendix E). | all |
| Eth | Threshold energy. | 3 |
| E"x" | Average decay energy (eV) of "x" radiation for decay heat applications. | 8 |
| EB | Total energy released by delayed β's. | 1 |
| EBAR | Statistical R-matrix parameter | 2 |
| EBI | Binding energy for subshell (eV) | 28 |
| ED | Logarithmic parameter for a R-matrix element | 2 |
| EDATE | Date of evaluation. | 1 |
| EFH | Constant in energy-department fission spectrum | 5 |
| EFL | Constant in energy-department fission spectrum | 5 |
|  | Fluorescence yield (eV/photo-ionization). Value is zero if not photoelectric subshell ionization cross section. | 23 |
| EFR | Kinetic energy of the fragments. | 1,5 |
| EGk | Photon energy or Binding Energy. | 12,13,14 |
| EGD | Total energy released by the emission of delayed γ rays. | 1 |
| EGP | Total energy released by the emission of "prompt" γ-rays. | 1 |
| EH | Upper limit for a resonance region energy range. | 2,32 |
| EI | Energy points where the weighting of the standard cross is given. | 31,33 |
| EL | Lower limit for a resonance region energy range. | 2,32 |
| ELFS | Excitation energy of the reaction product. | 8 |
| ELIS | Excitation energy of the target nucleus. | 1 |
| ELN | Number of electrons in subshell when neutral. | 28 |
| EMAX | Upper limit of energy range for evaluation | 1 |
| END | Kinetic energy of the delayed fission neutrons. | 1 |
|  | End-point energy of the particle or quantum emitted. | 8 |
| ENDATE | Master file entry date (yyyymmdd). | 1 |
| ENP | Kinetic energy of the "prompt" fission neutrons. | 1 |
| ENU | Energy carried away by neutrinos. | 1 |
| EPE | Sub-shell binding energy (equal to photoelectric edge energy) in eV. The value is zero if MT(534-599. | 23 |
| ER | Total energy release due to fission minus neutrino energy. | 1 |
|  | Resonance energy (in the laboratory system). | 2,32 |
|  | Energy (eV) of radiation produced. | 8 |
| ERAV | Average decay energy of radiation produced. | 8 |
| ESi | Energy of the ith level. | 12 |
| ESk | Energy of the level from which the photon originates. | 12,13,14 |
| ES(N) | Energy of Nth point used to tabulate energy-dependent widths. | 2 |
| ET | Total energy release due to fission. | 1 |
| ET(E) | Energy transfer during electro-atomic excitation or bremsstrahlung | 26 |
| ETR | Energy of transition (eV) | 28 |
| EU | Logarithmic parameter for a R-matrix element | 2 |
| fi(μ,E,E) | Normalized product energy-angle distribution | 6 |
| fk(E  E) | kth partial energy distribution; definition depends on LF value. | 5 |
| F(q;Z) | Form factor for coherent photon scattering. | 27 |
| Fx,k,k(LB) | Covariance components correlated over the energy interval with lower edges Ek and Ek (exact definition depends on LB value. | 31-40 |
| FC | Continuum spectrum normalization factor. | 8 |
| FD | Discrete spectrum normalization factor. | 8 |
| FPS | Floating-point value of state designator for a fission product nuclide. | 8 |
| FTR | Fractional probability for transition. | 28 |
| g(Eγ  E) | Particular class of the functions gj(Eγ  E) tabulated in File 15; in units eV-1. | 15 |
| gj(Eγ  E) | jth normalized partial distribution; in units eV-1. | 15 |
| GE | Eliminated width. | 2 |
| GF | Fission width Γf evaluated at resonance energy ER. | 2,32 |
|  | Average fission width - may be energy dependent. | 2 |
| GFA | First partial fission width | 2 |
| GFB | Second partial fission width | 3 |
| GG | Radiation width Γγ evaluated at resonance energy ER. | 2,32 |
|  | Average radiation width - energy dependent if LRU=2. | 2 |
| GICr | Asymmetrical capture parameter. | 2 |
| GIFr | Asymmetrical fission parameter. | 2 |
| GITr | Related to the asymmetrical total cross section parameter. | 2 |
| GN | Neutron width Γn evaluated at resonance energy ER. | 2,32 |
| GN0 | Average reduced neutron width; energy dependent. | 2 |
| GPj,i  Gpi | Conditional probability of photon emission in a direct transition from level j to level i, i < j. | 12 |
| GRCr | Symmetrical capture parameter. | 2 |
| GRE1GRE4 | Partial widths. | 2 |
| GRFr | Symmetrical fission parameter. | 2 |
| GRTr | Related to symmetrical total cross section parameter. | 2 |
| GT | Resonance total width Γ evaluated ate resonance energy ER. | 2,32 |
| GX | Competitive width Γx evaluated at resonance energy ER, or, average competitive reaction width. | 2 |
| H(q;Z) | Form factor or incoherent scattering function; either F(q;Z) or S(q;Z), respectively. | 27 |
| H(N) | Array containing text information that describes evaluated data set. | 1 |
| HEAD | First record in a section | all |
| HL | Half life of the reaction product. | 8 |
| HSUB | Library identifier (eye-readable) | 1 |
| I | Normalizing denominator (see 5.3). | 5 |
| Ii | Interpolation scheme (see Appendix E) to be used between the Ei-1 and Ei energy points. | 8 |
| IDP | Resonance parameter identification number. | 2,32 |
| INT | Statistical parameter for R-matrix element (LRU=1, LRF=5), or, interpolation scheme used for interpolating between cross sections obtained from average resonance parameters (LRU=2). | 2 |
| INT(m) | Interpolation scheme identification number used in mth range. | 0 |
| IPS | Imaginary part of a non-hard-sphere phase shift. | 2 |
| IPS(e) | Real part of PS(E). | 2 |
| IR0(e) | Imaginary part of R0(E). | 2 |
| IRP | Imaginary part of background-R-matrix element. | 2 |
| ISG | Spin group index. | 2 |
| ISH | Shift function flag. | 2 |
| k | Boltzmann's constant. | 7 |
| L | Value of the l state (neutron angular momentum). |  |
| LA | Value of l (for the lth coefficient). |  |
| LAD | Angular distribution flag |  |
| LANG | Angular distribution indicator |  |
| LASYM | Flag indicating whether asymmetric S(α,β) is given. |  |
| LAT | Flag indicating which temperature has been used to compute α and β. | 7 |
| LAW | Distinguishes between different representations of fi, the normalized product energy-single distribution | 6 |
| LB | Flag which determines meanings of the F-numbers in the arrays {Ek,Fk}{El,Fl} . | 8,31,33, 34,40 |
| LBK | Background R-matrix parameter (LRU=1, LRF=5), or, background-R-function flag (LRU=1, LRF=6). | 2 |
| LCOMP | Indicates ENDF-5 compatible format. | 32 |
| LCON | Continuum spectrum flag. | 8 |
| LCOV | Indicates whether covariance data are given. | 8 |
| LCT | Indicates which reference frame is used for both secondary angles and energies. | 4,6 |
| LDRV | Distinguishes between different evaluations with the same material keys | 1 |
| LE | Indicates whether energy-dependent fission-product yields are given. | 8 |
| LEP | Selects interpolation scheme for secondary energy. | 6 |
| LF | Specifies the energy distribution law that is used for a particular subsection (partial energy distribution). | 5,6,12,13, 15 |
| LFI | Indicates whether this material is fissionable. | 1 |
| LFS | Indicator that specifies the final excited state of the residual nucleus produced by a particular reaction. | 3,8,9,10,40 |
| LFW | Indicates whether average fission widths are given in the unresolved resonance region for this isotope. | 2,32 |
| LG | Transition probability array flag for distinguishing between doublet and triplet arrays in File 12. | 12 |
| LI | Indicates kind of Adler-Adler parameters given. | 2 |
|  | Isotropy flag. | 4,14 |
|  | Temperature interpolation flag. | 7 |
| LIBF | Sub-library where some data are sensitive to the same model parameters as data in present sub-library/material. | 30 |
| LIDP | Identifies identical particles for LAW=5. | 6 |
| LIP | Product modifier flag. | 8 |
| LIS | State number of the target nucleus (for materials that represent nuclides). | 1,3,8,9,10, 40 |
| LISO | Isomeric state number of the target nucleus. | 1,8 |
| LIST | Record used to list a series of numbers. | all |
| LLN | Indicates form for storing S(α,β). | 7 |
| LMF | File number for this MT containing multiplicity or cross section. | 8 |
| LNU | Indicates representation of (E) used. | 1 |
| LO | Indicates whether multiplicities or transition probability arrays given. | 12 |
| LP | Indicates whether particular photon is a primary. | 12,13 |
| LPS | Optical model phase shift flag | 2 |
| LR | Defines x in (n,n'x); used in the reactions MT=51, 52, 53,, 90, and 91. (See Section 3.4.4.) | 3 |
| LREL | Release number | 1 |
| LRF | Indicates which resonance parameter representation used for energy range; definition depends on value of LRU for range. | 2,32 |
| LRP | Indicates whether resolved and/or unresolved resonance parameters given in File 2. | 1 |
| LRU | Indicates whether energy range contains data for resolved or unresolved resonance parameters. | 2,32 |
| LRX | Indicates whether a competitive width is given. | 2 |
| LS | Indicates whether Fk,k, matrix is asymmetric or symmetric (LB=5 or 7). | 31,33,35 |
| LSSF | Indicates how File 2 and File 3 are to be combined. | 2,32 |
| LT | Temperature dependence (see Appendix F). | 0 |
|  | Specifies whether temperature-dependent data are given. | 3,4,5,6,7 |
|  | Number of pairs of numbers in the array {El,Fl}. | 31,33 |
| LTHR | Thermal data flag. | 7 |
| LTP | Specifies representation used for LAW=5. | 6 |
| LTT | Specifies whether Legendre or probability representation used. | 4,6,14 |
|  | Specifies whether Legendre coefficient covariance data start with a0 coefficient. | 34 |
| LTY | In "NC-type" sub-subsections, indicates the procedure used to obtain the covariance matrix. | 31,33 |
| LVT | Specifies whether a transformation matrix given for elastic scattering. | 4 |
| L1 | Integer to be used as a flag or a test. Number of Legendre coefficients. | 1 34 |
| L2 | Integer to be used as a flag or a test. | 1 |
| Mn | Number of atoms of the nth type in the molecule. | 7 |
| MAT | Material number. | 0 |
| MAT1 | Referenced material for covariance data. | 33 |
| MATF | MAT in which some data are sensitive to the same parameter. | 30 |
| MATP | Material number for the reaction product. | 8 |
| MATS | MAT in which a pertinent standard cross section (MTS) exists. | 31,33 |
| MF | File number. | 0 |
| MFn | MF of the nth section. | 1 |
| MFSEN,MTSEN | MF,MT of a section in which data are sensitive to the indicated parameter (MP). | 30 |
| MODn | Modification indicator for section MFn and MTn. | 1 |
| MP | Model parameter index. | 30 |
| MPAR | Number of parameters for which covariance data is given. | 32 |
| MPF | Model parameter index given the same parameter (MP) in another sublibrary/material | 30 |
| MT | Reaction type number, or, covariance file section identifier. | all |
| MTn | MT of the nth section. | 1 |
| MT1 | Referenced reaction type for covariance data. | 33 |
| MTL | Indicates MT that is a component of the lumped reaction. | 33 |
| MTS | Reaction type number for relevant standard cross section. | 31,33 |
| MUF | Number of degrees of freedom for fission widths. | 2 |
| MTRE1…MTRE4 | MT values for inelastic or charged particle reactions | 2 |
| N0 | Identifies reaction product that has radioactive ground state. | 8 |
| N1 | Number of items in a list to follow (except for MT 451). | 1 |
| N2 | Number of items in a second list to follow. | 1 |
| NA | Number of angles (cosines) at which secondary distributions given. | 6 |
| NAC | Number of channel radii | 2 |
| NAPS | Controls use of channel radius a and scattering radius AP. | 2,32 |
| NB | Total number of β value given. | 7 |
| NBC | Number of boundary-condition parameters. | 2 |
| NBK | Background-R-matrix parameter. | 2 |
| NBT(n) | Value of N separating the mth and (m+1)th interpolation rangers. | 0 |
| NC | Number of terms used in the polynomial expansion. | 1 |
|  | Total number of decay energies (eV) given (NC = 3 or 17). | 8 |
|  | Number of partial distributions used to represent f(Eγ  E). | 15 |
|  | Number of "NC-type" sub-subsections. | 31,33 |
| NCn | Number of physical records in the nth section. | 1 |
| NCH | Number of channels using particular background R-matrix element, phase shift, penetrability, channel radius, or boundary condition (LRU=1, LRF=5). | 2 |
| NCI | Number of reactions summed to obtain the reaction of interest. | 1 |
|  | For a "derived" cross section, number of reaction types for which cross sections are combined in the derivation. | 31,33 |
| NCP | Number of channels. | 2 |
| NCRE | Number of charged-particle reactions. | 2 |
| NCS | Number of channels in a particular spin group. | 2 |
| NCT | Total number of channels. | 2 |
| NCTAB | Number of CONT records in the corresponding table. | 30 |
| ND | Number of discrete energies (File 6); | 6 |
|  | Number of branches into which nuclide ZAP decays. | 8 |
| NDIR | Number of CONT records in the MF=30 directory. | 30 |
| NDK | Total number of decay modes given. | 8 |
| NE | Number of incident-energy points at which widths given. | 2 |
|  | Number of points at which tabulated distributions given. | 4 |
|  | Number of points at which θ(E) (file 5) given. | 5 |
|  | Number of energy points given in a TAB2 record. | 14,15 |
| NEI | Number of energy points in {EI,WEI} list. | 33 |
| NEP | Number of secondary energy points. | 6 |
| NER | Number of energy ranges given for this isotope. | 2,32 |
|  | Total number of discrete energies for given spectra type (STYP). | 8 |
|  | Number of energies corresponding to the rows of LB=6 covariance matrix. | 33 |
| NF | Number of channels not requiring a phase shift. | 2 |
|  | Number of secondary energy points in tabulation. | 5 |
| NFOR | Library format. | 1 |
| NFP | Number of fission-product nuclide states to be specified at each incident-energy point. | 8 |
| NFRE | Number of fission reactions. | 2 |
| NGRE | Number of capture reactions. | 2 |
| NHS | Number of channels that require hard-sphere phase shifts. | 2 |
| NI | Total number of items in the B(N) list; NL=6* (NS + 1). | 7 |
|  | Number of isotropic angular distributions given in section (MT) for which LI=0, i.e., with at least one anisotropic distribution). | 14 |
|  | Number of "NI-type" sub-subsections. | 31,33 |
| NIRE | Number of inelastic reactions. | 2 |
| NIS | Number of isotopes in this material. | 2,32 |
| NJS | Number of sets of resonance parameters (each having the same J state) for a specified l-state. | 2,32 |
| NK | Number of elements in transformation matrix; NK=(NM+1)2. | 4 |
|  | Number of partial energy distributions (one subsection for each partial distribution). | 5,6 |
|  | Number of partial energy distributions (LCON=5). | 8 |
|  | Number of discrete photons plus the photon continuum. | 12,13,14 |
|  | Number of subsections in this section (MT). | 26 |
|  | Number of incident-neutron energy ranges for covariance representation, each with a subsection. | 35 |
| NL | Highest order Legendre polynomial given at each energy. | 4,6,14 |
|  | Number of subsections within a section. | 33 |
| NLG | Number of logarithmically parameterized elements. | 2 |
| NL1 | Number of Legendre coefficients. | 34 |
| NLIB | Library identifier. | 1 |
| NLJ | Count of the number of levels for which parameters will be given. | 2 |
| NLRS | Number of subsections containing data on long-range resonance parameter covariance. | 32 |
| NLS | Number of l-values considered; a set of resonance parameters is given for each l-value. | 2,32 |
| NLSC | Number of l-value for convergence. | 2 |
| NLSJ | Number of resonances specified by l, s, and J. | 2 |
| NM | Maximum order Legendre polynomial required to describe the angular distributions. | 4 |
| NML | Number of entries in MT list. | 2 |
| NMOD | Modification number. | 1 |
| NMT1 | Number of subsections, for MT1  MT. | 34 |
| NMU | Number of emission cosine values for LAW=7. | 6 |
| NN | Number of elements in the LIST record | 8 |
| NNF | Number of precursor families considered. | 1 |
| NO | Decay information flag. | 8 |
| NP | Number of points in a tabulation of y(x) that are contained on the same record. | all but ( |
|  | Number of Bragg edges. | 7 |
|  | Total number of distinct model parameters. | 30 |
|  | Total number of pairs of numbers in the arrays {Ek,Fk}{El,Fl}. | 31,33 |
| NPE | Number of charged-particle penentrabilities. | 2 |
| NPP | Number of pairs of numbers in the {Ek,Fk} array. | 8 |
| NPS | Number of non-hard-sphere phase shifts. | 2 |
| NPSX | Number of particles distributed by LAW=6. | 6 |
| NR | Number of different interpolation intervals in a tabulation of y(x) that are contained in the same record. | all |
| NRB | Number of resonances in block. | 32 |
| NRM | Number of interpolation intervals for emission cosine for LAW=7. | 6 |
| NRO | Energy dependence of the scattering radius. | 2,32 |
| NRP | Number of interpolation intervals for emission energy (LAW=7). | 6 |
| NRS | Number of resolved resonances for a given l-state. | 2,32 |
| NRT | Total number of resonances. | 2 |
| NS | Number of non-principle scattering atom types. | 7 |
|  | Number of states of the radioactive reaction product. | 8,9,10 |
|  | Number of levels below the present one, including ground state. | 12 |
| NSG | Number of spin groups. | 2 |
| NSP | Total number of spectra radiation types (STYP) given. | 8 |
| NSRS | Number of subsections for covariances among parameters of specific resonances. | 32 |
| NSS | Number of different s-values. | 2 |
|  | Number of subshells. | 28 |
| NST | Number of statistically parameterized background R-matrix elements. | 2 |
| NSUB | Sub-library number. | 1 |
| NT | Number of transitions for which data given. | 2 |
|  | Number of entries for each discrete energy ER. | 8 |
|  | Total number of items in LIST. | 33,34,35 |
| NTP | Control flag for background-R-matrix or penetrability list. | 2 |
| NTR | Number of transitions. | 28 |
| NVER | Library version number. | 1 |
| NVS | Number of covariance elements for a block of resonances. | 32 |
| NW | Number of words in LIST record. | 6 |
| NWD | Number of elements in the text section. | 1 |
| NX | Number of sets of background constants to be given. | 2 |
| NXC | Number of the sections to be found in the dictionary | 1 |
| Pj(E) | Probability or weight given to jth partial distribution, gj(EγE). | 15 |
| Pk(EN) | Fractional part of cross section that can be described by the kth partial distribution of the nth incident-energy point. | 5 |
| p(μ,E) |  | 4 |
| PAR | Parity π of target nuclide. | 8 |
| PCP(E) | Charged-particle penetrability. | 2 |
| PMT | Floating point value for PMT. | 2 |
| PS(E) | Complex phase shift. | 2 |
| Q | Reaction Q-value (eV); Q=(rest mass of initial state - rest mass of final state). | 3,9,10 |
|  | Total decay energy (eV) available in corresponding decay process, not necessarily the same as maximum energy of emitted radiation). | 8 |
| QI | Reaction Q-value. | 3,9,10 |
| QM | Mass-difference Q-value. | 3,9,10 |
| QRE1…QRE4 | Q-values. | 2 |
| QX | Effective Q-value for the competitive width. | 2,32 |
| Rmjα | Probability of de-excitation. | 11 |
| R0,R1,R2 | Logarithmic parameters for a R-matrix element. | 2 |
| R0(E) | Complex background R-function. | 2 |
| RCOV | Relative covariance of model parameters. | 30 |
| RDATE | Date and number of last revision. | 1 |
| REF | Reference to evaluation. | 1 |
| RFS | Isomeric state flag for daughter nuclide. | 8 |
| RI | Resonance index. | 2 |
|  | Intensity of radiation produced (relative units). | 8 |
| RICC | Total internal conversion coefficient. | 8 |
| RICK | K-shell internal conversion coefficient. | 8 |
| RICL | L-shell internal conversion coefficient. | 8 |
| RIN | Statistical R-matrix parameters. | 2 |
| RIS | Internal pair formation coefficient (STYP=0.0); positron intensity (STYP=2.0). | 8 |
| RNPM | Number of particular sections (MT's). | 2 |
| RNSM | Number of summed sections (MT's). | 2 |
| RP | Spectrum of the continuum component of the radiation  RP(E)dE=1. | 8 |
| RPB | Real part of background R-matrix element. | 2 |
| RPS | Real part of a non-hard-sphere phase shift. | 2 |
| RPS(E) | Real part of PS(E). | 2 |
| RR0(E) | Real part of R0(E). | 2 |
| RTYP | Mode of decay of the nuclide in its LISO state. | 8 |
| RVij | Relative covariance quantities among average unresolved parameters. | 32 |
| S(α,β,T) | Defined (for a moderating molecule) by the relation. | 7 |
| S0, S1 | Logarithmic parameters for an R-matrix element. | 2 |
| SF | Statistical R-matrix parameter. | 2 |
| SMT | Floating-point value for MT. | 2 |
| SPD | Spin and parity for the daughter nucleus. | 2 |
| SPI | Nuclear spin of the target nucleus, I (positive number). | 2,8,32 |
| SPP | Spin and parity. | 2 |
| STA | Target stability flag. | 1 |
| STYP | Decay radiation type (defined in 8.3). | 8 |
| SUBI | Subshell designator. | 28 |
| SUBJ | Secondary subshell designator | 28 |
| SUBK | Tertiary subshell designator. | 28 |
| T | Temperature (K) at which temperature dependent data given. | 4,5,6,7 |
| T1/2 | Half-life of the original nuclide (seconds). | 8 |
| TAB1 | Control record for one-dimensional tabulated functions. | all |
| TAB2 | Control record for two-dimensional tabulated functions. | all |
| TEMP | Target temperature. | 1 |
| TM | Maximum temperature parameters. | 5 |
| TPi | Probability of a direct transition from level NS to level I, I = 0, 1, 2, …(NS-1). | 12 |
| TYPE | Indicates the type of transition for beta and electron capture. | 8 |
| U | Defines the upper energy limit for the secondary neutron, so that 0 EE-U (given in the Lab system). | 5 |
| Vk | Matrix elements of the transformation matrices. | 4 |
| Vmn | Variance-covariance matrix element among resonance parameters. | 32 |
| WEI | Weight of the standard cross section at a given EI relative to the next given energy. | 31,33 |
| x | E/θ(E). | 5 |
| x(n) | nth value of x. | 0 |
| XLFS1 | Floating-point form of final excited state number references for covariance data. | 33,40 |
| XLFSS | Floating-point form of LFSS, final excited state number of a reaction with a standard cross section | 31,33 |
| XMF1 | Floating-point form of file number reference for covariance data. | 33,40 |
| XMFS | Floating-point form of MFS, file number in which pertinent standard cross section (MTS) may be found. | 31,33 |
| XMTI | Floating-point equivalent of MT number of the reaction for which the cross section contributes to a "derived" cross section. | 31,33 |
| y(E) | Yield for particle described. | 26 |
| y(n) | nth value of y. | 0 |
| yi(E) | Product yield or multiplicity. | 6 |
| Y(E) | Total multiplicity at energy E(eV); given as energy-multiplicity pairs. | 9,12 |
|  | Partial multiplicity at energy E(eV). | 12 |
| YC | Cumulative yield for a particular fission product. | 8 |
| YI | Fractional independent yield for a particular fission product. | 8 |
| ZA | Designation of the original nuclide.** | all |
| ZAI | (Z,A) designation for an isotope.** | 2,32 |
| ZAFP | (Z,A) identifier for a particular fission product.** | 8 |
| ZAN | (Z,A) designation of the next nuclide in the chain.** | 8 |
| ZAP | (Z,A) designation of the product nuclide.** | 8 |
| ZSYMA | Test representation of material: Z-chemical symbol-A | 8 |
| ZSYMAM | Text representation of material Z-chemical symbol-A-state. | 1 |
| α | Momentum transfer,. | 7 |
| β | Energy transfer, β = (E - E)/kT. | 7 |
| δ(Eγ - εj + εi) | Delta function, with εj, εi being energy levels of the residual nucleus. | 11 |
| Δ | Uncertainty in quantity. | 1,8 |
| λi | Decay constant (sec-1) for the ith precursor. | 1 |
| θ | Parameter describing secondary energy distribution; definition of θ depends on the energy distribution law (LF). | 5 |
| (E) | Total average number of neutrons formed per fission event. | 1 |
| σ(E) | Cross section (barns) for a particular reaction type at incident energy point, E, in (eV). | 3,10,23 |
| σbn | Bound atom scattering cross section of nth type atom, | 7 |
| σfn | Free atom scattering cross section of nth type atom. | 7 |
| σkγ(E) | Photon production cross section for a discrete photon or photon continuum specified by k. | 13 |
| σm0(E) | Neutron cross section for exciting moth level with neutron energy E. | 11 |
| σs(E) | Scattering cross sections, e.g., elastic scattering at energy E as given in File 3 for the particular reaction type (MT). | 4 |
| σT (background) |  | 2 |
| σW | Wick's limit cross section in units of barns/steradian. | 4 |
|  | Differential scattering cross section in units of barns/steradian. | 4 |
|  | Differential photon production cross section in barns/steradian. | 14 |
| µ | Cosine of scattered angle in either laboratory or center-of-mass system. | 4,6,14 |

# Footnotes

*	The subscript r denotes the rth resonance.

**	(ZA=(1000.0*Z) + A).