Required Specifications

(1). One (1) Job: Design, furnish, deliver, and install a 42” plasma display, side mount speakers and Smart Technology overlay interactive whiteboard in room B135; remove existing CRT monitor and white board; install new plasma on the front wall; mount wall plate for interconnection of plasma and existing government furnished computer and DVD/VHS players - existing equipment to be relocated next to new wall plate.

Installation to include:

Labor

Installation and testing

Wall mount of new plasma screen

Mounting of existing speakers

Wall plate for interconnection of devices

VGAM-VGAM w/ audio to suit

Composite video cable to suit

S video cable to suit

Stereo audio cables to suit

Minimum one (1) - year warranty on parts and labor for installation

Specifications: Suggested - NEC 42” PX42XM4A or equal.

Technical Information

- Screen Size: 42"

- Viewing Angle: 160º

- Aspect Ratio: 16:9

- Sleep/Wakeup Timer: Sleep

- Features: Closed CaptionPicture on Picture

Video

- Video System: PALSECAMNTSC 3.58NTSC 4.43ATSC

- Scanning Frequencies: 15.5 kHz to 110 kHz Horizontal51 Hz to 120 Hz Vertical

- Resolution: 1024 x 768 - XGA

- Pixel Pitch: 0.9mm x 0.67mm

- Color Depth: 68.7 Billion Colors (4096 Steps)

Audio

- Speakers: 2 x 8W Speaker(s) Integrated

- Audio Decoding: Stereo

Interfaces/Ports

- Ports: 15-pin D-Sub (HD-15)5-BNC24-pin DVI-D-HDCP4-pin DIN

- S-VideoRS-232Infrared

Power Description

- Input Voltage: 110V AC220V AC

- Input Voltage Range: 120 V AC to 240 V AC

- Frequency: 50Hz60Hz

- Power Consumption: 285W Typical 0.9W Stand By

Environmental Conditions

- Temperature: 32 F (0 C) to 104 F (40 C) Operating14 F (-10 C) to 122 F (50 C) Storage

- Humidity: 20 to 80% Operating10 to 90% Storage

- Altitude: 0 ft to 9180 ft Operating0 ft to 9840 ft Storage

- Sound Emission: 22 dB

Physical Characteristics

- Dimensions: 24" Height x 40.2" Width x 3.9" Depth

- Weight: 61.1 lb

Miscellaneous

User Manual Remote Control Warranty

- Standard Warranty: 1 Year(s)

- Parts Warranty/Labor: 1 Year(s)

- Wall-mountable

- Attachable Multimedia Speakers

(2). One (1) Job: Design, furnish, deliver, and install a 61” plasma display, side mount speakers and Smart Technology overlay interactive whiteboard and install in room A244; remove existing 61” plasma display; install new plasma on the front wall. Mount wall plate for interconnection of plasma and existing government furnished computer and DVD/VHS players - existing equipment to be relocated next to new wall plate.

Installation to include:

Labor

Installation and testing

Wall mount of new plasma screen

Tilt wall mount for display

Mounting of existing speakers

Wall plate for interconnection of devices

VGAM-VGAM w/ audio to suit

Composite video cable to suit

S video cable to suit

Stereo audio cables to suit

Minimum one (1) - year warranty on parts and labor for installation

Specifications: Suggested - NEC PlasmaSync 61XM3 or equal.

Product type:  Plasma panel 
Technology:  Plasma (PDP) 
Diagonal size:  61 in 
Image aspect ratio:  16:9 
HDTV compatible:  Yes 
Digital TV Type:  High Definition monitor 
Width:  57.9 in 
Depth:  4.7 in 
Height:  34.6 in 
Weight:  134.5 lbs (maximum) 
Service & support:  Parts and labor - 1 year 
Resolution:  1365 x 768 
Pixel Pitch:  0.99 mm 
Viewing angle:  160 degrees 
Sound output mode:  Stereo 
Audio controls:  Bass, Treble, Balance, Sound mode 
External speakers amplifier power:  18 Watt 
Closed captioning:  Yes 
Freeze memo:  Yes 
Color temperature control:  Yes 
Compliant standards:  DDC-1, DDC-2B, UL 1950, CSA 22.2 No. 950, FCC Class A certified 
Additional features:  Split screen, On-screen menu, Anti-reflective filter 
Remote control 
Input/Output connections:  1 x VGA input / output (15 pin HD D-Sub (HD-15)), 1 x HD component video / RGB input (BNC x 5), 1 x DVI-HDCP (24 pin digital DVI), 1 x Composite video input/output (BNC), 1 x Composite video input (RCA phono), 1 x S-Video input (4 pin mini-DIN), 1 x Component video input (RCA phono x 3), 3 x Audio line-in (RCA phono x 2), 2 x Speakers output (9 pin D-Sub), 1 x Serial 
Power device:  Power supply - Internal 
Voltage requirement:  50/60 Hz 
Operational power consumption:  540 Watt 
Operational power consumption (standby):  0.9 Watt

(3). One (1) Job: Install an existing 42” NEC plasma display in the hallway of Wing B outside of the Admissions Office; a government owned-computer will provide the input to the plasma display; a wall plate for connectivity of plasma screen and computer to be installed on the wall; this wall plate to be able to connect other devices such as DVD and VCR recorders - connectivity to include audio capability.

Installation to include:

Labor

Installation and testing

Wall mount of existing plasma screen

Mounting of existing speakers

Wall plate for interconnection of devices

VGAM-VGAM w/ audio to suit

Composite video cable to suit

S video cable to suit

Stereo audio cables to suit