Example #5 - Nini Cement Plant

Data for a Plant in China with a Carbon Dioxide Emissions Reduction Target

Your target is a CO2 reduction of 50,000 tonnes CO2 per year. After you benchmark your plant, construct an energy management plan to achieve your savings goal using the energy efficiency measures section of the tool.

Raw Materials used at your plant (tonnes/year):

Limestone: 	1,500,000

Gypsum: 	50,000

Clay minerals: 	0

Iron ore: 	0

Blast furnace slag: 	100,000

Other slags: 	50,000

Fly ash: 	0

Natural pozzolans: 	100,000

Limestone powder: 	0

Municipal wastes: 	0

Other 1: 	0

Other 2: 	0

You preblend and crush all of your raw materials.

You only dry the slags you add to your raw material mix, but you grind all slags and pozzolans.

Both of your kilns are NSP kilns, one produces 250,000 tonnes/year of clinker and one produces 750,000 tonnes/year of clinker.

You produce the following cement types:

500,000 tonnes/year of pure Portland cement of the lowest quality (42.5/42.5R)

250,000 tonnes/year of 32.5 slag cement

250,000 tonnes/year of 42.5 slag cement

250,000 tonnes/year of 52.5R Pozzolana cement

All mills at your plant are ball mills. You grind 155,555 tonnes of coal. A quarry is not located at your site and you do not generate any electricity on site.

You purchase and use electricity for the following processes (kWh/year):

Preblending: 	3,500,000

Crushing: 	1,500,000

Grinding: 	42,400,000

Additive crushing and grinding: 	20,000,000

Fuel grinding: 	5,500,000

Homogenization: 	4,000,000

Kiln preheaters: 	140,000,000

Clinker cooler: 	4,500,000

Cement grinding: 	75,500,000

Other conveying and auxiliaries: 	14,250,000

Other electricity: 	2,000,000

You use coal for the following processes:

Additive drying: 5,000,000 kg of cleaned coal

Precalciners: 5,555,500 kg of cleaned coal

Kiln: 145,000,000 kg of cleaned coal

You pay 0.5RMB/kWh for electricity and 0.7 RMB/kgce for coal