UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON D.C., 20460

OFFICE  OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

PC Code: 031301

DP Barcodes: D294452

Date: 24 January 2006

MEMORANDUM

SUBJECT:	DCNA (Dicloran): Revised Tier I Drinking Water EDWC’s for Use in the Human Health Risk Assessment.

TO:		Christine Olinger, Chemist

RRBI/HED (7509C)

FROM:	Cheryl A. Sutton, Ph.D., Environmental Scientist

Environmental Risk Branch IV

Environmental Fate and Effects Division (7507C)

APPROVED

BY:		Elizabeth Behl, Branch Chief

ERB IV/EFED (7507C)

This memo summarizes the revised Tier I estimated drinking water concentrations (EDWC) for DCNA in surface water for use in the human health risk assessment.  The revision is due to the submission of new aerobic aquatic metabolism data by the registrant.  The EDWC’s are summarized in Table 1.  EFED used the screening model FIRST (FQPA Index Reservoir Screening Tool) to calculate the surface water EDWC.  The groundwater EDWC (1.3 ug/L ppb) reported in the initial DWA has not changed.  Both surface water (acute and chronic) and groundwater EDWC’s are based on DCNA use on apricots at 4.0 lb a.i./A/application applied in a single application.

Table 1.  Tier I surface water EDWCs for DCNA for the drinking water assessment.

| Surface water drinking water sources | 1-in-10-year acute: 172.8 ug/L (ppb) 1-in-10-year chronic: 1.8 ug/L (ppb) |
| --- | --- |

An additional degradate, 2,6-dicholorbenzoic acid (DCBA), was identified in the newly submitted aerobic aquatic metabolism study at maximum concentrations of 9.2-9.3% of the applied in the water phase (7 days) and 3.3-5.8% of the applied in the sediment phase (14 days).  By study termination, DCBA had decreased to 1.0-1.7% of the applied in the water phase.  There were no major degradates of DCNA detected in the previously reviewed laboratory studies (i.e. none accounted for as much as 10% of radioactivity measured at any point in the studies), with the exception of the transformed chemical present as nonextractable residues. The minor degradates of DCNA expected in the environment are:  2,6-dichloro-p-phenylenediamine (DCPD); 4-amino-3,5-dichloroacetanilide (DCAA); and 2,6-dichloro-4-hydroxyaniline (DCHA); and 3,5-dichloro-4-hydroxyacetanilide (3,5HA).

Estimated Drinking Water Concentrations

To estimate the surface water concentrations, the application rates for apricots (a single application of 4.0 lb a.i./A/application) was used, which represents the maximum label rate across all crops.  While there are several different types of applications to apricots listed on the labels at that rate, an aerial application was modeled, as it yields the highest EDWC’s due to the higher levels of spray drift associated with that application type.  Because the Tier I model is not dependent on crop type (other than for a percentage crop area factor), the EDWC’s determined for apricots are also applicable to other crops receiving 4 lb a.i./A by aerial application.

A summary of the model input parameter values used in FIRST is presented in Table 2.  The FIRST output file is located in Attachment 1.  The modeling input value for the aerobic aquatic metabolism half-life was decreased to 3.7 days from the initially used value of 1828 days based on the newly submitted data.  A table of the source data used to determine input parameter values is located in Attachment 2.

FIRST (v1.0) is a screening-level model designed to estimate the pesticide concentrations found in surface water for use in drinking water assessments.  The model provides upper bound estimates of environmental concentrations (acute and chronic) in surface water drinking water sources (untreated) that might occur following the use of a pesticide.  FIRST uses basic environmental fate data and pesticide label use and application information to estimate the EDWCs following the treatment of a 10-hectare field with subsequent runoff into a reservoir (an Index Reservoir, based on Shipman City Lake in Illinois, a 13-acre lake 9-feet deep with a watershed area of 427 acres or 172.8 hectares) that undergoes two full turnovers annually.  FIRST also uses a Percent Cropped Area (PCA) factor to adjust for the area within the watershed that is planted to the modeled crop.  In the model, a single runoff event occurs two days after the last application and can move a maximum of 8% of the applied pesticide into the reservoir, with the amount dependent on the degradation and adsorption of the pesticide which occurs in the field prior to the event, any incorporation of the pesticide at the time of application, and the PCA.  The model also accounts for degradation and binding to sediment which may occur in the reservoir following the runoff event.  Spray drift (resulting in direct deposition of the pesticide into the reservoir or indirect loading from spray drift landing on the feeding stream) in the model is equivalent to 16% of the applied for aerial application, 6.3% for orchard air blast application, and 6.4% for other ground spray application.

For use in the human health risk assessment, EFED recommends a revised 1-in-10-year acute surface water EDWC of 172.8 ppb (decreased from 182 ppb) and a revised 1-in-10-year chronic EDWC of 1.8 ppb (decreased from 35 ppb), both based on the use of DCNA on apricots at a rate of a single application of 4 lb a.i./A.  The recommended EWDC for groundwater, also based on the use of apricots at the previously stated rate, remains at 1.3 ppb.

Table 2. FIRST (v1.0) input parameter values for DCNA applied to apricots by aerial application.

| Parameter | Value | Source/Comments |
| --- | --- | --- |
| Application Rate (lb a.i./A) | 4 | EPA Reg. No. 10163-188 |
| Number of Applications | 1 | EPA Reg. No. 10163-188 |
| Interval between Applications (days) | Not Applicable | – |
| Organic Carbon Partitioning Coefficient (Koc; mL/g) | 660 | MRID 40538202; lowest non-sand value of four values, per input parameter guidance |
| Aerobic Soil Metabolism Half-life (days) | 914 | MRID 40894801; input value represents the 90th percentile of the upper confidence bound on the average of two half-life values, per input parameter guidance |
| Wetted in? | No | Input parameter guidance |
| Depth of Incorporation (inches) | 0 | Input parameter guidance |
| Method of Application | aerial spray | EPA Reg. No. 10163-188 |
| Percent Cropped Area | 0.87 (default value) | Input parameter guidance |
| Solubility in Water (mg/L or ppm) | 7 @ 20 oC | Product chemistry data |
| Aerobic Aquatic Metabolism Half-life (days) | 3.7 | MRID 46657101; input value represents the 90th percentile of the upper confidence bound on the average of two half-life values, per input parameter guidance |
| Hydrolysis Half-life @ pH 7 (days) | stable | ACC No. 253963 |
| Aquatic Photolysis Half-life @ pH7 (days) | 1.97 | MRID’s 43891901, 45575001 |

ATTACHMENT 1:   FIRST File

RUN No.   1 FOR dcna             ON   apricotr      * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

4.000(  4.000)   1   1     660.0    7.0   AERIAL(16.0)  87.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

914.00        2          N/A      1.97-  244.28     3.70      3.64

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))    Ver 1.0 AUG 1, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

172.801                      1.839

ATTACHMENT 2: General fate and physical-chemical property source data used for DCNA aquatic exposure modeling.

| PARAMETER | VALUE | SOURCE OF INFO./COMMENTS |
| --- | --- | --- |
| Chemical Name | 2,6-dichloro-4-nitroaniline (IUPAC) 2,6-dichloro-4-nitrobenzenamine (CAS) | – |
| Molecular Weight | 207.06 g/mole | -- |
| Solubility (20 oC) | 7 mg/L (ppm) @ 20 oC | Registrant |
| Dissociation Constant (pKa) | 3.31 | Registrant |
| Vapor Pressure | 1.96 x 10-6 mmHg @ 25 oC 1.2 x 10-6 mmHg @ 20 oC | Registrant |
| Hydrolysis Half-life (pH 5, 7, 9; 25 oC) | stable at pH 5, 7, 9 | Accession No. 253963 |
| Aqueous Photolysis Half-life (pH 7) | 47.2 hours (1.97 days) | MRID’s 43891901, 45575001 |
| Soil Photolysis Half-life | 263.2 hours | MRID 43893601 |
| Aerobic Soil Metabolism Half-life | 18 months (approx. 540 days) in sandy loam soil, 6 months (approx. 180 days) in sand soil | MRID 40894801 |
| Anaerobic Soil Metabolism Half-life | 38 days in sandy loam soil, 24 days in sand soil | MRID 40894801 |
| Anaerobic Aquatic Metabolism Half-life | 0.45 days1 | MRID 43866501 |
| Aerobic Aquatic Metabolism Half-life | 3.4, 3.5 days | MRID 46657101 |
| Organic Carbon Partition Coefficient (Koc) | 660, 735, 760, 1062 | MRID 40538202 |
| Soil Partition Coefficient (Kd, mL/g) | 3.7, 9.7, 13.6, 15.4 mL/g | MRID 40538202 |
| Log Kow | 2.76 | MRID 41176202 |
| Henry’s Law Constant (atm*m3/mol) | 7.78 x 10-8 | Registrant |
| Bioconcentration Factors (BCF) in Fish | 136X whole fish tissue 49X edible tissue 264X nonedible tissue | MRID 43782001 |

1The half-life was determined in a high organic matter (13.4%) sediment which may not be respresentative of the soils on which DCNA will be used.  In sandy loam (3.1% o.m.) and sand (1.6% o.m.) soils treated and flooded simultaneously, and then anaerobically incubated as part of another study (MRID 40894801), respective anaerobic aquatic metabolism half-lives of 10.1 and 5.6 days were determined.  In an aged soil column leaching study (MRID 43809001) where the soil was treated and aged anaerobically prior to placement on the columns, the half-lives of DCNA in sandy loam (2.8% o.m.), sand (0.59% o.m.), silt loam (0.54% o.m.) and clay (1.41% o.m.) soils, respectively, were 0.8, 8.5, 9.2 and 5.9 days.