UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C. 20460

OFFICE OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

June 13, 2006

MEMORANDUM

SUBJECT:	DCNA (Dicloran): 2nd Revised Occupational and Residential Exposure Assessment for the Reregistration Eligibility Decision.

FROM:	Matthew Lloyd, Industrial Hygienist and

Timothy Dole, CIH, Industrial Hygienist

Reregistration Branch 1

Health Effects Division

THRU:	Whang Phang, Ph. D., Branch Senior Scientist

Reregistration Branch 1

Health Effects Division

TO:		James Parker, Chemical Review Manager

Special Review and Reregistration Division

DP Barcode:	D313892

PC Code: 	031301

Attached is the 2nd Revised Occupational and Residential Exposure Assessment for the DCNA (Dicloran) Registration Elegibility Decision.  This assessment has been revised as follows: (1) Inhalation risk calculations for two handler scenario have been added, (2) The aerial application scenario for the dust formulation has been deleted, (3)The hand harvesting risk for lettuce and celery has been refined, (4)The application rate for potatoes has been increased, and (5) the applications rates for grapes, deciduous tree fruits, Christmas trees and snap beans has been reduced.

Reviewer:	Science Advisory Council on Exposure (7/21/05)

Table of Contents

Executive Summary	3

1.	Occupational and Residential Exposure/Risk Assessment	6

1.1.	Criteria for Conducting Exposure Assessments	6

1.2.	Summary of Hazard Concerns	6

1.2.1.	DCNA Hazard Concerns	6

1.3.	Incident Reports	8

1.4.	Summary of Use Patterns and Formulations	8

1.4.1.	End-Use Products	9

1.4.2.	Mode of Action and Targets Controlled	9

1.4.3.	Registered Use Categories and Sites	9

1.4.4.	Application Parameters	9

2.	Occupational Exposures and Risks	11

2.1.	Occupational Handler Exposures and Risks	11

2.1.1.	Handler Exposure Scenarios and Calculation Methods	11

2.1.2.	DCNA Occupational Handler Exposure Risk Estimates	15

2.1.3.	Overall Summary of Risk Concerns and  Data Gaps for Handlers	18

2.1.4.	Recommendations For Refining Occupational Handler Risk Assessment	18

2.2.	Occupational Handler Characterization	18

2.3.	Occupational Postapplication Exposures and Risks	20

2.3.1.	Occupational Postapplication Exposure Scenarios and Calculation Methods	20

2.3.2.	Data Used for Occupational Postapplication Exposure Scenarios	22

2.3.3.	Exposure Assumptions, Factors and Transfer Coefficients	23

2.3.4.	Occupational Postapplication Exposure and Risk Estimates	25

2.3.5.	Summary of Occupational Postapplication Risk Concerns and Data Gaps	26

2.3.6.	Occupational Postapplication Risk Characterization	26

List of Tables

Table 1 - Acute Toxicity Study Results for DCNA	6

Table 2- Endpoints for Assessing DCNA Non-Dietary Risks	8

Table 3 - DCNA Product Formulations	9

Table 4 - DCNA Application Rates	10

Table 5 - DCNA Dermal MOEs for Agricultural Handlers	16

Table 6 - DCNA Inhalation MOEs for Agricultural Handlers	17

Table 7 - Summary of Handler Input Values and Their Uncertainty	19

Table 8 - Postapplication Exposure Scenarios and Transfer Coefficients	24

Table 9 – DCNA Occupational Postapplication Risks	25

Table 10 – Summary of DCNA Postapplication Risks of Concern	26

###### List of Appendices

Appendix A – DCNA Occupational Handler Risk Calculations

Appendix B – DCNA DFR Study Information

Appendix C – DCNA Occupational Post Application Risk Calculations

# Executive Summary

## Use Information

Dicloran (DCNA) formulations include wettable powders, liquid flowables and dusts.  Agricultural uses include tree and vine crops (e.g.,apricots, grapes, nectarines, sweet cherries), row crops (e.g., lettuce, celery, potatoes and snap beans), and some greenhouse and hothouse crops (e.g., cucumbers, tomatoes). Horticultural uses include ornamental plants in nurseries and greenhouses for a variety of cut flowers. There are no residential labels current for DCNA.

There are currently 15 active DCNA labels and 10 section 24C registrations.  The application rate per application generally ranges from 0.75 lb ai/acre to 4.5 lb ai/acre for most crops. The application rate per year is 4.0 to 7.5 lb ai/acre for most crops.  The application rates in horticulture are 1 lb ai/acre for most ornamentals.  Horticulture applications are allowed as much as once weekly up to a maximum of 4 lb ai/acre per season.

The application methods were derived from the labels and/or Agency knowledge of typical use practices and include aerial, airblast, groundboom, chemigation, and hand application methods such as handwand and backpack sprayers.  The daily acres treated are those typically used by the Agency for risk assessment (e.g. 80 acres/day for groundboom, 350 acres/day for aerial and 40 acres/day for airblast).

## Toxicology Endpoints

DCNA is not acutely toxic, but it is a dermal sensitizer.  The following endpoints were used for assessing DCNA risks:

Exposure Route and Duration	Dose in mg/kg/day (Effects Observed)

Dermal - short/intermediate	Dermal NOAEL of 120 (adrenal weight changes/histopathological effects)

Dermal - long term		Oral NOAEL of 2.5 (clinical chemistry/liver weight effects)

Inhalation - short/intermediate	Oral NOAEL of 2.5 (hematological and clinical chemistry effects)

Inhalation - long term		Oral NOAEL of 2.5 (clinical chemistry/liver weight effects)

A dermal absorption factor of 100% was used for long term dermal exposures because the endpoint was based on an oral toxicity study for long term postapplication scenarios.  Risk calculations have been completed for short/intermediate term exposures for all occupational scenarios. Long term risks have not been calculated as long term exposures are not expected because the labels limit the amount that can be applied each year.

Occupational dermal or inhalation exposures that yield MOEs of 100 or greater are not of concern for DCNA.

## Occupational Handler Risks

Data Used for Occupational Handler Risk Assessments

No handler exposure studies were submitted in support of the re-registration of DCNA, therefore, PHED was used to assess the occupational handler exposures associated with DCNA applications to crops and ornamentals.  Seed piece treatment scenarios were not assessed and remain as a data gap.

Dermal Handler Risks

The dermal risks for loading dust are of concern at baseline and require single layer PPE (i.e. chemical resistant gloves) to achieve MOEs of 100 or greater.  The dermal risks for mixing/loading wettable powder to support aerial application and chemigation are of concern at all PPE levels and require engineering controls (i.e. water soluble bags) achieve acceptable MOEs.   The dermal risks for mixing/loading wettable powder for ground application are less of a concern and can be addressed with single layer PPE.  The risks for the remaining scenarios (applicators, flagger and mixer/loader/applicator) are not of concern with baseline or single layer PPE.

Inhalation Handler Risks

The inhalation risks for loading dust are of concern at baseline and require PF10 respiratory protection to achieve MOEs of 100 or greater.  The inhalation risks for mixing/loading wettable powder to support aerial application and chemigation are of concern at all PPE levels and require engineering controls (i.e. water soluble bags) achieve acceptable MOEs.   The inhalation risks for mixing/loading wettable powder for ground application are less of a concern and can be addressed with PF5 or PF10 respiratory protection.  The risks for the remaining scenarios are not of concern with baseline or single layer PPE.

## Occupational Postapplication Risks

## Data Used for Postapplication Exposure Assessment

One recent dislodgeable foliar residue (DFR) study (completed in 2000) (MRID 450620-01) was submitted by Gowan Company. The study involved the application of Botran® 75WP wettable powder to snap beans, DFR samples were collected using the standard methodology and were analyzed for DCNA the using electron gas chromatography analysis. Complete descriptions of the analytical methods and method validation data were included in the study reports. This study was reviewed by the Agency (Lloyd, D279651), it was found to comply with the series 875 guidelines. The study was adequate for exposure and risk assessment purposes.

Occupational Post Application Risk Summary

Post application dermal exposures occur when workers enter treated fields to perform tasks such as irrigation, thinning and hand harvesting.  These exposures were assessed using the DFR data described above and standard transfer coefficients from ExpoSAC Policy 3.1.  Some of the MOEs for post application exposures are less than 100 at the currently labeled REI of 12 hours and the time needed to achieve MOEs of 100 ranges from 2 for hand harvesting snap beans, cut flowers, greenhouse lettuce and endive to 32 days for cane turning and girdling grapes.   In some cases, the MOEs for hand harvesting are acceptable at the Pre Harvest Intervals (PHIs) which are longer than the REI.  The MOE for the high hand harvesting celery, florence and fennel is 100 on day 7 which is the same as the PHI.  This means that hand harvesting exposures are not of concern because they will not occur until 7 days after application at which time the MOE will have risen to 100 due to DFR decline.  The hand harvesting exposures for snap beans, greenhouse grown lettuce and endive are also not of concern because the MOEs exceed 100 at the PHIs of 2 days for snap beans, 14 days for greenhouse grown lettuce and 14 days for endive.

## Data Gaps and Recommendations for Refinement

The risks of dipping sweet potato seed pieces were not assessed because dipping is no longer used. According to sweet potato researchers at Sweet Potato Research Station (LSU), sweet potato seed pieces are treated in the plant bed using a sprayer.

The risks of post-harvest dip treatment of sweet potatoes were not assessed due to a lack of exposure data. This treatment is accomplished by using automated equipment; however, exposures can be minimized with the use of gloves.

The risk of loading the dust formulation was assessed with surrogate unit exposure values from mixing and loading wettable powders. The risk of applying dust formulations was not assessed due to lack of exposure data and remains as a data gap.

It was reported that aerial application was not usually used for applying fungicides to orchards and vineyards; however, this method was assessed for these crops because it was included on the labels and might be necessary during wet seasons. Information regarding the types of formulations, if any, used for aerial application could be used to refine the risk.

DCNA products are packaged as wettable powders, dusts, and liquid flowables. The labels indicate that only the wettable powder formulations can be used on all of the crops; however, it is suspected that liquid formulations can be used.  This information is critical because the dust and wettable powder formulations create the highest exposures particularly when it is used at high rates. These exposures can be greatly reduced by using the liquid formulations or by using the wettable powder in water soluble bags.

There are no data available to evaluate the mix/load/apply scenarios for backpack sprayer application of wettable powders. The PHED data for both high and low pressure handwand application of liquids (mix/load/apply and apply only) is also of low quality.  These data gaps make it difficult to accurately assess the risks of the handwand method of application which is commonly used in horticulture.

# Occupational and Residential Exposure/Risk Assessment

This document is the occupational and residential non-dietary exposure and risk assessment for DCNA (Dicloran) to be used in the re-registration process.

## Criteria for Conducting Exposure Assessments

An occupational and/or residential exposure assessment is required for an active ingredient if (1) certain toxicological criteria are triggered and (2) there is a potential for exposure to handlers (mixers, loaders, applicators, flaggers, etc.) during use or to persons entering treated sites after application is complete. Toxicological endpoints have been selected for short-, intermediate-, and long-term exposures to DCNA. There is a significant potential for exposure in a substantial number of agricultural and commercial settings. Therefore, risk assessments are required for occupational handlers and occupational postapplication exposures that can occur as a result of DCNA use.

## Summary of Hazard Concerns

## DCNA Hazard Concerns

The acute toxicity data indicate that DCNA has low acute toxicity by the oral, dermal and inhalation routes. Dicloran is a mild ocular irritant but not a dermal irritant, and it is a dermal sensitizer. Table 1 summarizes the acute toxicity data for DCNA.

| Table 1 - Acute Toxicity Study Results for DCNA |
| --- |
| Guideline No. | Study Type | MRID | Results | Toxicity Category |
| 870.1100/§81-1 | Acute Oral – rat | 0006879 | LD50 = 1000 mg/kg | IV |
| 870.1200/§81-2 | Acute Dermal – rabbit | 00086894 | LD50 = >2000 mg/kg | III |
| 870.1300/§81-3 | Acute Inhalation | Not Available | LC50 = N/A | N/A |
| 870.2400/§81-4 | Primary Eye Irritation | 00086892 | Mild ocular irritant | III |
| 870.2500/§81-5 | Primary Skin Irritation | 00086893 | Not a dermal irritant | IV |
| 870.2600/§81-6 | Dermal Sensitization | 00082721 | Potential dermal sensitizer | N/A |

The toxicological endpoints that were used to complete the occupational risk assessments for DCNA are listed in Table 2.  Effects were identified at different durations of exposure ranging from short-term (up to 30 days) to intermediate-term (up to 180 days) and including long term (more than 180 days).

The incidental oral endpoints for DCNA were based on a 90-day oral study in dogs (MRID 00029056, 00026810).  The effects that were observed and selected as the basis for the endpoint were hematological and clinical biochemistry and included reduced body weight gain, increased liver, spleen, and kidney weights, and histopathological changes in the liver. A No Observed Adverse Effect Level (NOAEL) of 2.5 mg/kg/day was identified in the study.  The results of this study were applied to short and intermediate term exposure durations.  No endpoints were selected for long term incidental oral exposures because these exposures were not anticipated to occur based upon DCNA use patterns in the residential environment.

The endpoint for short and intermediate term dermal exposure was based upon a 21 day dermal toxicity study on rabbits (MRID 40555101) during which increased adrenal weights in males and other effects were observed with a NOAEL of 120 mg/kg/day. The endpoint for long term dermal exposure is based upon two chronic toxicity study in dogs (MRID 45610801 (new study), 00029056,  00082718 (old study) during which a number of clinical chemistry changes were observed (increased alkaline phosphatase in both sexes, increased liver weights, hepatocyte hypertrophy, vacuolar alterations of the brain and spinal cord, etc.). A NOAEL of 2.5 mg/kg/day was identified in the study.

The endpoint for short and intermediate inhalation exposures is based on the same 90 day oral toxicity study in dogs that was used to determine the incidental oral endpoints. The NOAEL for the study was 2.5 mg/kg/day. The endpoint for long term inhalation exposure is based upon a two year chronic toxicity study in dogs (MRID 45610801 (new study), 00029056,  00082718 (old study)) during which a number of clinical chemistry changes were observed (increased alkaline phosphatase in both sexes, increased liver weights, hepatocyte hypertrophy, vacuolar alterations of the brain and spinal cord, etc.) A NOAEL of 2.5 mg/kg/day was identified in the study.

As indicated in Table 2, all of the long term endpoints for dermal and inhalation exposures are based upon hematological and clinical biochemistry effects. Since the revised product labels include maximum seasonal rates, chronic exposures scenarios are no longer applicable to the risk assessment and are not included in this chapter.

No dermal absorption studies are available on DCNA. Dermal absorption of structurally related compounds varied. Therefore, according to OPP policy, a default dermal absorption rate of 100% should be assumed, due to lack of appropriate data. Because the DCNA short/intermediate dermal endpoint is based upon a dermal toxicity study, the dermal absorption factor is not needed when assessing short/intermediate dermal exposures to DCNA. The dermal absorption factor is only needed when assessing long term dermal exposures.

The Agency’s level of concern for the handler risks is defined by the uncertainty factors that are applied to the assessment. The level of concern for the DCNA occupational dermal and inhalation exposures is an MOE of less than 100 which includes the factors of 10 to account for interspecies extrapolation to humans from the animal test species and the factor of 10 to account for intraspecies sensitivity variation.

| Table 2- Endpoints for Assessing DCNA Non-Dietary Risks |
| --- |
| Exposure Scenario | Dose (mg/kg/day) | Endpoint | Study |
| Incidental Oral Exposures (Postapplication) |
| [ST and IT] | NOAEL = 2.5 | Hematological and clinical biochemistry – reduced body weight gain, increased liver, spleen, and kidney weights, histopathological changes in the liver | 90 day Feeding, dog |
| Dermal Exposures |
| Short-Term [1-30 days] | NOAEL = 120 | Increased adrenal weights in males | 21-day Dermal, rabbit |
| Intermediate-Term [>30 days to 6 mos.] | NOAEL = 120 | Increased adrenal weights in males | 21-day Dermal, rabbit |
| Long-Term [> 6 months] | NOAEL = 2.5 | Clinical Chemistry changes, increased liver weights, hepatocyte hypertrophy, vacuolar alterations of the brain and spinal cord, prostate atrophy, degeneration of the seminiferous tubules, hypospermia in the epididymides | 2-year Chronic, dog |
| Inhalation Exposures |
| Short-Term [1-30 days] | NOAEL = 2.5 | Hematological and clinical biochemistry – reduced body weight gain, increased liver, spleen, and kidney weights, histopathological changes in the liver | 90 day Feeding, dog |
| Intermediate-Term [>30 days to 6 mos.] | NOAEL = 2.5 | Hematological and clinical biochemistry – reduced body weight gain, increased liver, spleen, and kidney weights, histopathological changes in the liver | 90 day Feeding, dog |
| Long-Term [>6 months] | NOAEL = 2.5 | Clinical Chemistry changes, increased liver weights, hepatocyte hypertrophy, vacuolar alterations of the brain and spinal cord, prostate atrophy, degeneration of the seminiferous tubules, hypospermia in the epididymides | 2-year Chronic, dog |

The committee members of CARC evaluated the available carcinogenicity toxicity data of DCNA and classified DCNA as having “Suggestive Evidence of Carcinogenic Potential” and recommended no quantification of cancer risk.

## Incident Reports

The incident report was prepared under a separate memo (D294468 of April 14, 2005) by Jerome Blondell, Ph.D. There were no incidents reported in the OPP Incident Data System from 1992 to 2002.   There were 7 exposures reported to the Poison Control Centers (1993-2001) and 1 case has medical outcome determined with dermal symptoms characterized as minor.  Two involved children under age six, one was occupational, and the other four were adults exposed in a non-occupational setting. There were no reports of DCNA poisoning in the California Pesticide Illness Surveillance Program (1982-2002).

## Summary of Use Patterns and Formulations

DCNA products are described in this section. Additionally, available information that describes the manner in which registered DCNA end-use products are used is provided in this section (e.g. use categories/sites, application methods and application rates).

## End-Use Products

Dicloran (2,6-dicloro-4-nitroaniline), also called DCNA, belongs to the substituted aromatics class of pesticides and is marketed in a variety of end-use products for occupational use. End-use product names include Botran® 6 Dust, Diclor Fungicide, Botran® 75-W, Botran® 5F, Botran® Sulfur 6-25.

DCNA formulations include dusts, flowables (liquid); and wettable powders. The active products (per result of an OPPIN search on 2/03/05) are listed in Table 3. Miscellaneous SLN’s are not included below in Table 3 as they are derived from the parent labels and represent the same crop usage in all cases.

| Table 3 - DCNA Product Formulations |
| --- |
| Formulation Type | EPA Registration Number (% Active Ingredient) |
| Technical/Formulation | 10163-195 (95), 10163-239 (65) |
| Liquid Flowable | 10163-221 (43.1), 10163-226 (46.7) |
| Wettable Powders | 10163-189 (75.0), 10163-207 [WSB] (75.0), |
| Dusts | 10163-187 (8.0), 10163-188 (6.0), 10163-190 (12.0), 10163-191 (15.0), 10163-192 (10.0), 10163-193 (4.0), 10951-13 (6.0), 10951-14 (6.0), 2935-529 (6.0). |

[WSB]= water soluble bag

## Mode of Action and Targets Controlled

DCNA is used as a contact fungicide.  It is considered highly useful against grey mold (Botrytis cinerea), and white mold (Sclerotinia sclerotiorum). It is also effective on the post-harvest fungi Botrytis, Rhizopus, and Monolinia spp.  DCNA prevents or inhibits normal spore germination and it suppresses the growth of fungus mycelium once infections are established.

## Registered Use Categories and Sites

Occupational Use Sites

Occupational populations are potentially exposed while making DCNA applications to the following targets or from contact with the treated targets. Use categories include tree and vine crops; vegetable crops; grapes; conifers/christmas trees; greenhouse grown flowers; greenhouse grown vegetables.

## Application Parameters

Application Rates

The application rates are provided in Table 4.  The current label application rates were derived from the product labels and/or the Use Closure Memo of August 14, 2003.   The revised label rates are based upon risk mitigation negotiations between SRRD and the Registrant and will be incorporated into the RED.

| Table 4 - DCNA Application Rates |
| --- |
| Crop Group | Crop or Target | Current Label Rates (lb ai/acre)1 | Revised Label Rates (lb ai/acre)2 | SLUA Max. % Crop Treated3 |
|  |  | Max. Per Application | Max. Per Season | Max. Per Application | Max. Per Year |  |
| Field/Row Crops, Low/Medium | Snap Beans | 3.75 | NS | 2.0 | 4 | NS |
| Cut Flowers | Chrysanthemums Roses, Hydrangeas | 0.75 1 | weekly NS | 0.75 1 | 4 | <50 lbs. Nationally* |
| Ornamentals, Potted Plants | Geraniums | 0.75 | NS | 0.75 | 4 | <50 lbs. Nationally* |
| Vegetable, Cucurbit | Cucumbers, Rhubarb | 1 | NS | 1 2 | 4 | NS NS |
| Vegetable, Fruiting | Tomatoes | 1 | 4 | 0.75 | 4 | <2.5 |
| Tree, Fruit, Deciduous | Apricots, Peaches, Nectarines, Plums, Prunes, Cherries | 4 | NS | 1.5 | 4 | <2.5-peaches NS-all others |
| Tree, Fruit, Evergreen | Conifers, Christmas Trees | 2 | NS | 1.5 | 4 | NS |
| Vegetable, Leafy, Greenhouse | Lettuce | 4 | 4 lb/cc | 2 | 4 | 15 |
| Vegetable, Root | Potatoes | 4.5 | 7.5 | 4.5 | 7.5 | <2.5 |
| Vegetable, Leafy, Outdoors | Celery, florence, fennel Lettuce Endive | 1 | 4 lb/cc | 4 4 2 | 5 4 4 | 60-celery 15-lettuce NS-endive |
| Vegetable, Root | (onions, garlic shallots) (sweet potatoes) | 4 120 | 4 lb/cc NS | 4 120 | 4 120 | <2.5-onions, garlic NS-all others |
| Vine/Trellis | Grapes (various types) | 3.5 | 3.5 lb/cc | 1.5 | 4 | 15 |

1 - Current label rates are taken from currently registered products.

2 – Revised label rates are from RED mitigation negotiations between SRRD and the Registrant (June 2006)

Rates for ornamentals/greenhouse are given in lbs ai/100 gallons and were converted to lb ai/acre by assuming that 100 gallons of spray would be applied per acre.

NS – Not Specified

cc – Crop Cycle

3 - SLUA Maximum Percentage Crop Treated – from SLUA report June 29, 2005

<2.5 indicates that less than 2.5% of the crop is treated

<50 pounds Nationally – indicates that less than 50 lbs. is applied via foliar application (from NASS Floriculture Survey – 2003)

Application Equipment

A summary of the application equipment used is given below:

- Conifers and Christmas Trees: aerial and airblast.

- Tree and Vine Crops: aerial and airblast.

- Field/Row Crops: groundboom, aerial, and chemigation.

- Vegetables: groundboom, aerial, and chemigation.

- Ornamentals: low-pressure (LP) handwand, backpack, high-pressure (HP) handwand, and groundboom.

- Greenhouse: low-pressure (LP) handwand, backpack, high-pressure (HP) handwand, and groundboom.

# Occupational Exposures and Risks

It has been determined there is the potential for exposure in occupational scenarios from handling DCNA products during the application process and from entering areas previously treated with DCNA. As a result, risk assessments have been completed for both handler and postapplication scenarios.

## Occupational Handler Exposures and Risks

The Agency uses the term “Handlers” to describe those individuals who are involved in the pesticide application process.  The agency believes that there are distinct job functions or tasks related to applications and that exposures can vary depending on the specifics of each task. Job requirements (e.g., amount of chemical to be used in an application), the kinds of equipment used, the crop or target being treated, and the circumstances of the user (e.g., the level of protection used by an applicator) can cause exposure levels to differ in a manner specific to each application event. Handler tasks can generally be categorized using one of the following terms:

- Mixer/loaders

- Applicators

- Mixer/loader/applicators

- Flaggers

## Handler Exposure Scenarios and Calculation Methods

Handler Exposure Scenarios

The use patterns and labels indicate several major occupational exposure scenarios based on the types of equipment and techniques that can potentially be used to make DCNA applications. The quantitative exposure/risk assessment developed for occupational handlers is based on the following scenarios:

Agricultural Crop Treatment Scenarios:

Mix/Load wettable powder, dusts or liquids

Apply using Aerial, Groundboom, Airblast or HP Handwand application methods

Mix/Load/Apply wettable powder with a LP handwand and  backpack sprayer;

Mix/Load/Apply liquids with a LP handwand and backpack sprayer;

Mix/Load/Apply dusts with a Handheld Power Duster;

Flag aerial application of liquids

Calculation Methods:

The Agency uses a concept known as unit exposure as the basis for assessing handler exposures.  The unit exposure is amount of exposure that occurs while handling a pound of active ingredient.  Daily exposures are calculated by considering application parameters (i.e., rate and area treated) along with unit exposure levels. Exposures are then normalized by body weight to calculate dose levels and the Margin of Exposure (MOE).

Daily Exposure:  The daily exposures to handlers are calculated as described below.  The first step is to calculate daily exposure (dermal or inhalation) using the following formula:

Daily Exposure = Unit Exposure x Application Rate x Amount Treated

Where:

Daily Exposure		=	Amount deposited on the surface of the skin or amount that is inhaled

(mg ai/day);

Unit Exposure 		=	Normalized exposure value, derived from August 1998 PHED Surrogate

Exposure Table and various referenced exposure studies (mg ai/lb ai);

Application Rate	=	Amount of a.i.  applied per unit treated such as acres or pounds of seed

Amount Treated 	=	Typically expressed as acres/day for crops and pounds/day for seed.

Inhalation exposure values are calculated in a similar manner. The only difference is that unit exposure values representing the inhalation route are calculated using PHED and standard human breathing rates (29 liters/minute and an 8 hour exposure).

Daily Dose:  Daily dose (inhalation or dermal) are then calculated by normalizing the daily dermal exposure value by body weight.  It should also be noted that a dermal absorption factor is not needed for DCNA, because the dermal endpoint was based upon a dermal study. The inhalation absorption factor is assumed to be 100 percent because the inhalation endpoint was based upon an oral study.  Daily dose is calculated using the following formula:

Average Daily Dose  = Daily Exposure  x

Where:

Average Daily Dose 	=	The amount as absorbed dose received from exposure to a pesticide in a given scenario (mg pesticide active ingredient/kg body weight/day);

Daily Exposure 		= 	Amount deposited on the surface of the skin that is available for dermal absorption or amount that is inhaled (mg ai/day);

Absorption Factor 	=	N/A for dermal exposures

100 percent for inhalation exposures

Body Weight 		= 	70 kg for DCNA because the endpoints are not gender specific.

The handler exposure assessment does not include any dietary or drinking water inputs.

Margins of Exposure:  Finally, the daily dermal dose and daily inhalation dose received by handlers are compared to the appropriate endpoint (i.e., NOAEL or LOAEL) to obtain a Margin of Exposure (MOE).  All MOE values were calculated separately for dermal and inhalation exposures using the formula below:

MOE = NOAEL/ADD

Where:

MOE 	=	Margin of exposure

ADD 	= 	Average Daily Dose (mg ai/kg/day) or the amount as absorbed dose received from exposure to a pesticide in a given scenario

NOAEL  = 	No Observed Adverse Effects Level (mg ai/kg/day).

The level of concern for all assessments is established by the uncertainty factor.  The uncertainty factor is 100 for both dermal and inhalation occupational exposures.

Data and Assumptions for Occupational Handler Exposure Scenarios

A series of assumptions and exposure factors served as the basis for completing the occupational handler risk assessments.  Each assumption and factor is detailed below.

- It is anticipated that the occupational handler DCNA exposures will generally occur in a short- and intermediate-term pattern because the labels limit the amount that can be applied per year.

- No PHED data were available for loading dusts.  The PHED baseline unit exposure data for mixing and loading wettable powders (3.7 mg/lb ai for dermal and 43 g/lb for inhalation) were used to calculate dermal and inhalation exposures for loading dusts.

- No PHED data were available for applying dusts with ground equipment. Applicator exposures from these scenarios remain as a data gap.

- No PHED data were available for the loading and applying dust with a handheld power duster. This scenario remains as a data gap.

- Several generic protection factors were used to calculate handler exposures. The values used for respiratory protection (i.e., PF 5 or PF 10) are based on the NIOSH Respirator Decision Logic.

- It is understood that human flagging is an uncommon because Global Positioning Satellite (GPS) technology is now predominantly used as indicated by the 2003 National Agricultural Aviation Association (NAAA) survey of their membership.  This survey did indicate, however, that human flaggers are still used in approximately 4 percent of aerial application operations.  The Agency strongly encourages the use of GPS, but will continue to evaluate risks for human flaggers until the potential for exposure is eliminated.

- The revised application rates were used as listed in Table 4.

- The acres treated per day values were taken from Health Effects Division Science Advisory Committee on Exposure Policy 9.1: Standard Values for Daily Acres Treated in Agriculture of September 25, 2001.  These factors are listed below:

- Aerial applications: 350 acres;

- Chemigation: 350 acres for most crops

- Groundboom: 80 acres treated

- Groundboom (sweet potatoes): 3 acres/day for plant bed spray based on the assumption that one acre of bedded seed will produce enough transplants for 100 acres of potatoes (USDA Crop Profile for Sweet Potatoes in Texas, June 2003).

- Airblast: 40 acres treated

- High Pressure Handwand: 10 acres for ornamental applications based on the assumption that at least 100 gallons are applied per acre and 1000 gallons are applied per day;

- Backpack Sprayer: 0.40 acres per day based on the assumption that at 100 gallons are applied per acre and 40 gallons are applied per day;

- Baseline PPE: includes typical work clothing (i.e., a long-sleeved shirt, long pants, shoes, socks, and no respiratory protection).  It does not include chemical-resistant gloves.

- Single Layer PPE: includes chemical-resistant gloves in addition to baseline clothing.

- Double Layer PPE:  adds coveralls to single layer PPE.

- PF5 Respirator: is a respirator with a protection factor of 5 (i.e., it provides 80 percent inhalation protection).  A PF5 respirator is a filtering facepiece respirator (i.e. a dustmask) that provides dust/mist filtering only.

- PF10 Respirator: is a respirator with a protection factor of 10 (i.e., it provides 90 percent inhalation protection).  A PF10 respirator is a half-face elastomeric facepiece with appropriate cartridges for dust/mists and/or organic vapors.

- Engineering Controls (EC): includes enclosed tractor cab, enclosed cockpit, water soluble bags and closed loading systems.

Unit Exposure Data Sources

All of the unit exposure values used in this assessment were based upon the Pesticide Handler Exposure Database (PHED) Version 1.1 (August 1998).   PHED was designed by a task force of representatives from the U.S. EPA, Health Canada, the California Department of Pesticide regulation, and member companies of the American Crop Protection Association.  Currently, the database contains values for over 1,700 monitored individuals (i.e., replicates) and HED has developed a series of tables of standard unit exposure values for many occupational scenarios that can be utilized to ensure consistency in exposure assessments.  These values are included in the “PHED Surrogate Exposure Guide” of August 1998.

Exposure Data Used for Agricultural Handlers and Applicators

No additional chemical-specific data that had not been previously considered in the development of PHED were submitted to the Agency for the reregistration of DCNA.    Therefore all of the handler assessments were performed using PHED data. These data are listed in Appendix A. There are no exposure data in PHED that are relevant to the application of dusts; therefore, dust application scenarios were not evaluated.

Exposure Data Used for Seed Piece Treatment:

No chemical specific data are available for assessing exposures during seed piece treatments.

No data are available to assess post-harvest dipping operations and because this operation is less hazardous than other scenarios assessed here, protective gloves should be adequate for PPE. This scenario is a “data gap.”

## DCNA Occupational Handler Exposure Risk Estimates

The MOEs were calculated for short/intermediate term exposures of DCNA handlers and a complete listing of these MOEs is included in Appendix A.  The MOEs for dermal exposures are summarized in Table 5 and the MOEs for inhalation exposures are summarized in Table 6. Several scenarios have been excluded from Tables 5 and 6 and they remain as data gaps. These include an applicator scenario for application of dust using ground equipment and a mix/load/apply scenario for handheld power dusting.

Dermal Handler Risks

The dermal risks for loading dust are of concern at baseline and require single layer PPE (i.e. chemical resistant gloves) to achieve MOEs of 100 or greater.  The dermal risks for mixing/loading wettable powder to support aerial application and chemigation are of concern at all PPE levels and require engineering controls (i.e. water soluble bags) achieve acceptable MOEs.   The dermal risks for mixing/loading wettable powder for ground application are less of a concern and can be addressed with single layer PPE.  The risks for the remaining scenarios (applicators, flagger and mixer/loader/applicator) are not of concern with baseline or single layer PPE.

Inhalation Handler Risks

The inhalation risks for loading dust are of concern at baseline and require PF10 respiratory protection to achieve MOEs of 100 or greater.  The inhalation risks for mixing/loading wettable powder to support aerial application and chemigation are of concern at all PPE levels and require engineering controls (i.e. water soluble bags) achieve acceptable MOEs.   The inhalation risks for mixing/loading wettable powder for ground application are less of a concern and can be addressed with PF5 or PF10 respiratory protection.  The risks for the remaining scenarios are not of concern with baseline or single layer PPE.

| Table 5 - DCNA Dermal MOEs for Agricultural Handlers (Note - The labels typically require single layer PPE) |
| --- |
| Exposure Scenario | Crop Groups | lb ai/acre | Acres per Day | Baseline PPE | SL PPE | DL PPE | EC |
| Mixer/Loader (M/L) |
| M/L Dust for Ground Equipment | tree/vine crops, field/row crops | 1.5 2.0-4.5 | 40 | 38 >13 | 820 >270 | 1100 >360 | N/A |
| M/L Wettable Powder (WP) for Aerial Application or Chemigation | field/row crops, tree/vine crops | 2.0-4.5 1.5 | 350 | >1 4 | >31 94 | >41 120 | > 540 >1000 |
| M/L WP for Ground-boom | sweet potatoes field/row crops | 120 2.0-4.5 | 3 80 | 6 >6 | 140 >140 | 180 >180 | >1000 >1000 |
| M/L WP for Airblast | tree/vine crops | 1.5 | 40 | 38 | 820 | >1000 | >1000 |
| M/L WP for HP Handwand | greenhouse crops | 0.75-2.5 | 10 | >94 | >1000 | >1000 | >1000 |
| M/L Liquids for Aerial Application or Chemigation | field/row crops tree/vine crops | 2.0-4.5 1.5 | 350 | >2 6 | >230 690 | >310 930 | >620 >1000 |
| M/L Liquids for Groundboom | field/row crops | 2.0-4.5 | 80 | >8 | >1000 | >1000 | >1000 |
| M/L Liquids for Airblast | tree/vine crops | 1.5 | 40 | 48 | >1000 | >1000 | >1000 |
| Applicator (APP) |
| Aerial Application (Closed Cockpit) | All crops above | 1.5-4.5 | 350 | N/A - only closed cockpit aircraft are used | >1000 |
| Groundboom Application | All crops above | 1.5 -120 | 3-80 | >1000 | >1000 | >1000 | >1000 |
| Airblast Application | tree/vine crops | 1.5 | 40 | 390 | 580 | 640 | >1000 |
| HP Handwand Application | greenhouse crops | 0.75-2.5 | 10 | >260 | >1000 | >1000 | ND |
| Mixer/Loader/Applicator (M/L/A) |
| M/L/A WP with LP Handwand | greenhouse crops | 0.75-2.5 | 0.4 | No Data | >490 | >680 | N/A |
| M/L/A WP with Backpack Sprayer |  |  |  | No Data |
| M/L/A Liquids with LP Handwand |  |  |  | >84 | >1000 | >1000 | N/A |
| M/L/A Liquids with Backpack Sprayer |  |  |  | No Data | >1000 | >1000 | N/A |
| Flagger |
| Flag Aerial Applications | All crops above | 1.5-4.5 | 350 | 480 | No Data | 530 | >1000 |
| *MOEs in bold are less than 100 and are of concern. ND - No Data N/A – Not applicable. Crop Groups Field/Row crops - includes celery, florence, fennel, endive, lettuce, onion, shallots, garlic, potatoes, snap beans, etc. Tree/Vine crops – includes apricots, grapes, peaches, nectarines, plums, prunes, sweet cherries, Christmas trees and other conifers Greenhouse Crops – includes ornamentals, certain vegetables and potato transplant seedlings PPE Levels Baseline - includes long pants and long sleeve shirts without gloves. Single Layer (SL) - includes baseline PPE with chemical resistant gloves Double Layer (DL) - includes coveralls over baseline PPE and chemical resistant gloves - typically required by the labels EC - Engineering control - includes water soluble bags, closed loading systems and enclosed cabs. |

| Table 6 - DCNA Inhalation MOEs for Agricultural Handlers (Note - The labels do not require respiratory protection) |
| --- |
| Exposure Scenario | Crop Groups ( See Notes) | lb ai/acre | Acres per Day | Base- line | PF5 | PF10 | EC |
| Mixer/Loader (M/L) |
| M/L Dust with Ground Equipment | tree/vine crops, field/row crops | 1.5 2.0-4.5 | 40 | 68 >23 | 340 >110 | 680 >230 | N/A |
| M/L Wettable Powder (WP) for Aerial Application or Chemigation | field/row crops, tree/vine crops | 2.0-4.5 1.5 | 350 | >3 >8 | >13 >39 | >26 >78 | >460 >1000 |
| M/L WP for Groundboom | sweet potatoes Field/row crops | 120 2.0-4.5 | 3 80 | 11 >11 | 57 >57 | 110 >110 | >1000 >1000 |
| M/L WP for Airblast | Tree/vine crops | 1.5 | 40 | 68 | 340 | 680 | >1000 |
| M/L WP for HP Handwand | greenhouse crops | 0.75-2.5 | 10 | >160 | >1000 | >1000 | >1000 |
| M/L Liquids for Aerial Application or Chemigation | potatoes field/row crops Tree/vine crops | 4.5 2.0-4.0 1.5 | 350 | 93 100 270 | 460 520 >1000 | 930 1000 >1000 | >1000 >1000 >1000 |
| M/L Liquids for Groundboom | Field/row crops | 2.0-4.5 | 80 | >410 | >1000 | >1000 | >1000 |
| M/L Liquids for Airblast | tree/vine crops | 1.5 | 40 | >1000 | >1000 | >1000 | >1000 |
| Applicator (APP) |
| Aerial Application | All crops above | 1.5-4.5 | 350 | N/A –Closed Cockpit Aircraft Are used | >1000 |
| Groundboom Application | All crops above | 2.0-120 | 3-80 | >660 | >1000 | >1000 | >1000 |
| Airblast Application | tree/ vine crops | 1.5 | 40 | 650 | >1000 | >1000 | >1000 |
| HP Handwand Application | greenhouse crops | 0.8-2.5 | 10 | >1000 | >1000 | >1000 | ND |
| Mixer/Loader/Applicator (M/L/A) |
| M/L/A WP with LP Handwand | greenhouse crops | 0.75-2.5 | 0.4 | >160 | >1000 | >1000 | ND |
| M/L/A WP with Backpack Sprayer |  |  |  | No Data |
| M/L/A Liquids with LP Handwand |  |  |  | >1000 | >1000 | >1000 | ND |
| M/L/A Liquids with Backpack Sprayer | Field/row crops | 4.0 | 0.4 | >1000 | >1000 | >1000 | ND |
| Flagger |
| Flag Aerial Applications | All crops above | 1.5-4.5 | 350 | >320 | >1000 | >1000 | >1000 |
| *MOEs in bold are less than 100 and are of concern. ND - No Data N/A – Not Applicable Crop Groups field/row crops - includes celery, florence, fennel, endive, lettuce, onion, shallots, garlic, potatoes, snap beans, etc. tree and vine crops – includes apricots, grapes, peaches, nectarines, plums, prunes, sweet cherries, Christmas trees and other conifers Greenhouse crops - includes ornamentals, certain vegetables and potato transplant seedlings PPE Levels Baseline - no respirator is worn PF5 - Filtering facepiece respirator (i.e. a dustmask) with a protection factor of 5 PF10 - Half face cartridge respirator with a protection factor of 10 EC - Engineering control - includes water soluble bags, closed loading systems and enclosed cabs. |

## Overall Summary of Risk Concerns and  Data Gaps for Handlers

Many of the scenarios that involve the mixing/loading of wettable powder for agricultural applications have risks of concern with label required PPE (coveralls and gloves over long sleeve clothing) and require engineering controls to be below Agency levels of concern.  These risks are often still of concern at baseline for liquid formulations, but greatly reduced by single layer PPE for dermal scenarios and the PF5 respirator for inhalation exposure scenarios.

Data gaps were identified for the following handler scenarios (GDL 875.1100 & 875.1200):

- Mix/Load/Apply wettable powders with low-pressure handwand or backpack sprayers

- Post harvest seed dip applications

- Application of dust formulations

- Mix/Load dusts for aerial application & ground equipment (data for mixing and loading wettable powders was used as a surrogate)

- Mix/Load/Apply dust with handheld power duster

- Flagger exposure to aerial application of dust

## Recommendations For Refining Occupational Handler Risk Assessment

It was understood that aerial application was not routinely used for applying fungicides to orchards and vineyards; however, this method was assessed for these crops because it was included on the labels and could be used during wet growing seasons.  Information regarding the types of formulations applied with aircraft could be used to refine the risk.

DCNA products are packaged as wettable powders, dusts, and liquid flowables. The labels indicate that all of the formulations can be used on all of the crops; however, it is suspected that some application scenarios require certain formulations.  This information is critical because the dust formulation and wettable powder formulation create significant exposures particularly when used at high rates. These exposures can be greatly reduced by using the other formulations or by using the wettable powder in water soluble bags. Information on the use of the dust formulations is also critical because the dust application scenario is a data gap and can result in excessive exposures.

## Occupational Handler Characterization

Product labels have been revised to include maximum seasonal application rates eliminating chronic exposures for the handler scenarios. The available NASS data indicate that very little (<50 lbs.) dichloran is used in floriculture.

Along with the unit exposure values used in the assessment, other inputs include application rates and daily acres treated values.  A summary of the input values and their uncertainty is given in Table 7.

In addition to the sources of information considered above, there are some underlying factors that may impact the overall results of a risk assessment. For example, in many cases the data included in PHED are based on the use of cotton gloves for hand exposure monitoring which are thought by many to overestimate exposure because they potentially retain residues more than human skin would over time (i.e., they act like a sponge compared to the hand).

| Table 7 - Summary of Handler Input Values and Their Uncertainty |
| --- |
| Input Value | Source | Comments |
| Daily Amt. Treated (based on 8 hour work day) | Taken from ExpoSAC Policy #9.1 of July 5, 2000 | Believed to represent typical values. |
| Application Rates | Maximum product label rates | N/A |
| Unit Exposure Data | PHED | Most values are geometric mean, not upper percentile. |
| Respiratory Protection Factors (5x & 10x) | NIOSH | The values were generated from studies using subjects that were fit tested and trained. The fit factors that are achieved by untested and untrained personnel are much lower. Respirator fit testing and training are currently not required by WPS. |

## Occupational Postapplication Exposures and Risks

The Agency uses the term “postapplication” to describe exposures to individuals that occur as a result of working in an environment that has been previously treated with a pesticide (also referred to as reentry exposure).  The Agency believes that there are distinct job functions or tasks related to the kinds of activities that occur in previously treated areas such as harvesting vegetables in a treated field.  Job requirements (e.g., the kinds of jobs to cultivate a crop), the nature of the crop or target that was treated, and the how chemical residues degrade in the environment can cause exposure levels to differ over time.  Each factor has been considered in this assessment.

## Occupational Postapplication Exposure Scenarios and Calculation Methods

Exposure Scenarios

DCNA use sites include field/row crops, tree crops, vineyards, greenhouse crops and ornamentals. Applications are typically begun in the spring or when disease conditions occur and can typically be repeated at 5 to 14 day intervals for the seasonal applications. In some instances, such as ornamental crops, it can be used more frequently.

The agency uses a concept known as the transfer coefficient to numerically represent the postapplication exposures one would receive (i.e., generally presented as cm2/hour).  These transfer coefficients are listed in Policy 003.1 Science Advisory Council for Exposure Policy Regarding Agricultural Transfer Coefficients.  In this policy, transfer coefficients were selected to represent the activities associated with 18 distinct crop/agronomic groupings based on different types of vegetables, trees, berries, vine/trellis crops, turf, field crops, and bunch/bundle crops (e.g., tobacco). DCNA uses were identified in most of the crop groups in the policy.

These crop groups include:

- Field/row crops, low/medium (e.g., snap beans);

- Cut flowers (e.g., floriculture crops);

- Ornamentals, potted plants,  (e.g., ornamental plants);

- Tree/fruit, deciduous (e.g., apples);

- Tree/fruit, evergreen (e.g., conifers);

- Vegetable, cucurbit (e.g., cucumber, endive);

- Vegetable, fruiting (e.g., tomato);

- Vegetable/leafy (e.g., lettuce, celery, florence, fennel);

- Vegetable, root (e.g., onions, garlic, shallots, potatoes, sweet potatoes);

- Vine/trellis (e.g., grapes – various types).

Within each agronomic group, a variety of cultural practices are required to maintain the included crops. These practices are varied and typically involve light contact with immature plants and heavy contact with more mature plants.

Calculation Methods

Post application exposures are calculated by considering transferable residue levels in areas where people work and the kinds of jobs or tasks that are required to produce agricultural commodities. These factors are represented by DFR concentrations and by transfer coefficients. Exposures are calculated by multiplying these factors by an 8 hour work day.  Exposures are then normalized by body weight to calculate absorbed doses. MOEs were then calculated.  Postapplication risks diminish over time because DCNA residues dissipate in the environment.  As a result, risk values were calculated over time based on changing residue levels.

Estimation of Residue Levels Using Dissipation Kinetics

The first step in the postapplication risk assessment was to complete an analysis of the available dislodgeable foliar residue (DFR) data. Best fit DFR levels were calculated based on empirical data using the equation D2-16 from Series 875-Occupational and Residential Test Guidelines: Group B-Postapplication Exposure Monitoring Test Guidelines. Half-lives were calculated using the algorithm (T1/2 = -Ln 2/slope). The results of those statistical analyses were used to calculate best fit concentrations over time using the following pseudo-first order equation:

Cenvir(t) = Cenvir(0)e(PAI(t) * M)

Where:

Cenvir(t) = dislodgeable foliar residue (μg/cm2) at time (t);

Cenvir(0) = same as above at time (0);

e =natural logarithms base function;

PAI(t)  = postapplication interval or dissipation time (e.g., days after treatment or DAT); and

M = slope of line generated during linear regression of data [ln(Cenvir) versus PAI].

Daily Exposure:  The next step in the risk assessment process was to calculate dermal exposure values on each postapplication day after application using the following equation (see equation D2-20 from Series 875-Occupational and Residential Test Guidelines: Group B-Post-application Exposure Monitoring Test Guidelines and Residential SOP 3.2: Postapplication Dermal Potential Doses from Pesticide Residues on Gardens):

DE(t) (mg/day) = (DFR(t) (ug/cm2) x TC (cm2/hr) x Hr/Day)/1000 (ug/mg)

Where:

DE(t)	=	Daily exposure or amount deposited on the surface of the skin at time (t) attributable for activity in a previously treated area, also referred to as potential dose (mg ai/day);

DFR(t)	=	Dislodgeable foliar residue at time (t) where the longest duration is dictated by the decay time observed in the studies (ug/cm2);

TC	= 	Transfer Coefficient (cm2/hour); and

Hr/day	=	Exposure duration meant to represent a typical workday (hours).

Daily Dose and Margins of Exposure:   Once daily exposure values are calculated, the calculation of daily absorbed dose and the resulting MOEs use the same algorithms that are described for the handler exposures.  These calculations are completed for each day after application.

The level of concern for all assessments is the same as for handlers (i.e. the target MOE is 100) as discussed in Section 2.1.3.

## Data Used for Occupational Postapplication Exposure Scenarios

One DFR study (MRID 450620-01) was submitted by BASF in support of the re-registration of DCNA. A brief description follows and additional information is provided in Appendix B. The DFR study was conducted on snap beans using groundboom application of a DCNA wettable powder formulation. The formulation used was Botran® 75W, a soluble powder that containing 75% by weight of active ingredient. This study was conducted at one site located on a Madera County, California (CA) research farm. A wetting agent was not used during application, and is not recommended in the product label.  Five weekly applications were made at the site, representing 100% of the proposed maximum use rate per season. The target rates for each application were 1.688 lb ai/acre to yield a total application of 8.4 lb ai/acre.  The finish spray was applied to the test site using a tractor mounted boom sprayer.  Two plots were established at the test area, one treated and one untreated.  The treated plot was divided into three subplots and the untreated into one subplot.  Each subplot was divided into 8, 40 inch beds for sampling. The treated crop was planted on August 9, 1999 and the untreated plot was planted on August 10, 1999. The 5th (and final) application took place on October 6th, 1999.

One sample from the untreated control plot and three samples were collected from the treated plot before and after each application then approximately 1,2,3,5,7,10,14,21,28 and 35 days after the fifth application. Forty snap bean leaf disks were collected using 2.5 cm Birkestrand leaf punches per sample for a total surface area of 405 cm2. Residues were dislodged in 100 ml of a 0.01% Aerosol OT using a reciprocal shaker at approximately 200 rpm for ten minutes. Field spikes were prepared by collecting and dislodging leaf disks from the untreated plots in the same manner as the samples collected from the treated plots.  Separate Birkestrand punches were used for the treated and untreated samples at each site. Dislodgeable foliar samples were analyzed using a specific method that involves Gas Chromatography using electron capture detection.The method was included in the study report.   The LOQ in terms of leaf area is 0.001 ug/cm2 and is supported by method validation.

No DCNA residue was detected in the pre-application or control plot samples except for the control samples taken pre- and postapplication number 2.  The average DCNA DFR (n=3) on Day After Treatment (DAT) zero after the fifth application was 3.72 ug/cm2. The DFR declined to 0.85 ug/cm2 (the LOQ is 0.001 ug/cm2) on day 35. Regression analysis of the natural logarithms of the 33 data points from DAT 0 to DAT 35 yielded an R2 value of 0.73 and a half life of 19 days.

This study appears to be of sufficient quality to be used for exposure and risk assessment purposes.   The product was applied to snap beans in a manner consistent with the label.

Application of the Study Data to the Exposure Scenarios

DCNA is used on several crop groups but dislodgeable foliar residue studies were submitted for only one crop. It is relevant to note that the DFR study took place at a California-based site, in dry conditions. Based upon this information, the data were extrapolated from the DFR studies to the labeled crops.

## Exposure Assumptions, Factors and Transfer Coefficients

The following assumptions, factors and transfer coefficients were used for assessing the occupational postapplication risks:

- The body weights, dermal absorption factors and toxicological endpoints are the same as those used for the occupational handler assessments.

- The revised application rates were used as listed in Table 4.

- The “multiple applications” rate of 2.0 lbs ai/acre was used for celery, florence and fennel because post application exposures do not occur when the “single application” rate of 4.0 lb ai/acre is applied.  According to the labels, the single application rate is applied 4 to 8 weeks before harvest with "a drop nozzle boom to direct spray to the base of plants and adjacent soil" which minimizes post application exposure.   Conversations with BEAD have also indicated that DCNA is applied to plant stems and soil to control soil borne organisms which is different than most fungicides which are applied to leaves to control airborne organisms.

- The “prethinning” rate of 2.25 lbs ai/acre was used for lettuce because post application exposures do not occur when the “post thinning” rate of 4.0 lb ai/acre is applied.  According to the labels, the post thinning rate is applied as a basal drench immediately after thinning and that "the soil surrounding the plants should not be disturbed" after the application.  These two factors preclude post application exposure when the post thinning rate is applied.

- When the Agency extrapolated the available DFR data to other crops, it adjusted the data for differences in application rate using a simple proportional approach

- Risks were calculated using generic transfer coefficients that represent many different types of cultural practices.  A listing of the transfer coefficients used in this assessment is given in Table 8.  Most of these transfer coefficients were taken from the Agency’s revised Policy 003.1 Science Advisory Council for Exposure Policy Regarding Agricultural Transfer Coefficients (August 7, 2000).  The transfer coefficients for ornamentals excluding cut flowers was taken from studies (ARTF-039 and ARTF-043) recently submitted by the ARTF. The transfer coefficients for ornamentals including cut flowers was taken from the ARTF-055 study.

- The use of personal protective equipment or other types of equipment to reduce exposures for postapplication workers is not considered a viable alternative for the regulatory process except in specialized situations (e.g., a rice scout will wear rubber boots in flooded paddies).  This is described in some detail in the Agency’s Worker Protection Standard (40 CFR 170).

| Table 8 - Postapplication Exposure Scenarios and Transfer Coefficients |
| --- |
| Crop Type (Specific Crops) | Postapplication Exposure Scenarios | Transfer Coefficient (cm2/hr) |
| Field/Row Crops, Low/Medium (Snap Beans) | Low - Irrigation, handweeding, scouting immature/low foliage plants Medium - Irrigation and scouting mature/high foliage plants High - Hand harvesting | 100 1500 2500 |
| Cut Flowers (gladiolas, roses, hydrangeas) | Hand harvesting – short term exposures Hand harvesting – Intermediate term/long term exposures | 51001 27002 |
| Ornamentals, Potted Plants | Low - Irrigation, scouting, thinning weeding immature low foliage plants Medium - Irrigation, scouting mature/high foliage plants High - Hand harvesting, pruning, thinning, pinching | 110 175 400 |
| Vegetable, Curcurbit (cucumber and rhubarb) | Low - Irrigation, scouting, thinning weeding immature plants Medium - Irrigation, scouting, weeding mature plants High - Hand harvesting, pulling, leaf thinning, thinning, turning | 500 1500 2500 |
| Vegetable, Fruiting (tomato) | Low - Irrigation, scouting, thinning weeding immature plants Medium - Irrigation, scouting, weeding mature plants High - Hand harvesting, pruning, staking, tying | 500 700 1000 |
| Tree, Fruit, Deciduous (apricots, peaches, nectarines, plums, prunes, and sweet cherries) | Low - Irrigation, scouting, weeding High – Pruning, training, tying, harvesting Very High – Thinning | 100 1500 3000 |
| Tree, Fruit, Evergreen (Christmas trees/conifers) | Low - Irrigation, scouting, hand weeding Medium – Shearing, harvesting | 1000 3000 |
| Vegetable, Leafy, Outdoors (celery, endive, florence, fennel) | Low - Irrigation, scouting, thinning weeding immature plants Medium - Irrigation, scouting, weeding mature plants High - Hand harvesting | 500 1500 2500 |
| Vegetable, Leafy, Outdoors (lettuce) | Low - Irrigation, scouting, thinning weeding immature plants Medium - N/A (applications are made prior to thinning seedlings) High – N/A (applications are made prior to thinning seedlings) | 500 N/A N/A |
| Vegetable, Leafy, Greenhouse (lettuce) | Low - Irrigation, scouting, thinning weeding immature plants Medium - Irrigation, scouting, weeding mature plants High - Hand harvesting | 500 1500 2500 |
| Vegetable, Root (onions, garlic, shallots) | Low - Irrigation, scouting, thinning, weeding immature plants Medium – Irrigation and scouting mature plants | 300 1500 |
| Vegetable, Root (potatoes) | Low - Irrigation, scouting, thinning, weeding immature plants Medium – Irrigation and scouting mature plants | 300 1500 |
| Vine/Trellis (Grape) | Low - Hedging, irrigation, scouting, hand weeding Medium - Scouting, training, tying High – Leaf pulling, thinning, pruning, training/tying Very High – Cane Turning and Tabling Grapes | 500 1000 5000 10000 |

1. Maximum mean value from ARTF-055

2. Mean of means from ARTF-055

## Occupational Postapplication Exposure and Risk Estimates

DCNA Risk Summary:

The post application risks for DCNA are summarized in Table 9 and details are presented in Appendix C.  Within each crop group, differing transfer coefficients were used to represent different types of cultural practices which were applicable to each crop group. Some of the MOEs for DCNA are of concern (i.e. are less than 100) at the currently labeled REI of 12 hours.  The time needed to achieve MOEs of 100 ranges from 2 for some high exposure tasks (hand harvesting) snap beans, cut flowers, greenhouse lettuce and endive to 32 days for very high exposure tasks (cane turning and girdling) grapes.

In the case of snap beans and leafy vegetables the high exposure task is hand harvesting which cannot occur until the Pre Harvest Interval (PHI) has expired.   These MOEs are acceptable at the PHIs which are longer than the REI.   The MOE for the high hand harvesting celery, florence and fennel is 100 on day 7 which is the same as the PHI.    The MOEs for the hand harvesting of snap beans, greenhouse grown lettuce and endive are also not of concern because the MOEs exceed 100 at the PHIs of 2 days for snap beans, 14 days for greenhouse grown lettuce and 14 days for endive.

| Table 9 – DCNA Occupational Postapplication Risks |
| --- |
| Crop Group | Application Rate (lb a.i/acre) | PHI (days) | MOE on Day 0 (Days when MOE > 100) |
|  |  |  | Low | Medium | High | Very High |
| Field/Row Crops, Low/Medium (snap beans) | 2 | 2 | 2400 | 160 | 95 (2)1 | N/A |
| Cut Flowers | 0.75 1 | None | N/A N/A | N/A N/A | 130 94 (2) | N/A N/A |
| Ornamentals, Potted Plants | 0.75 | None | 5800 | 3600 | 1600 | N/A |
| Vegetable, Curcurbit | 1 | 1 and 3 | 950 | 320 | 190 | N/A |
| Vegetable, Fruiting | 0.75 | 10 | 1300 | 910 | 640 | N/A |
| Tree, Fruit, Deciduous | 1.5 | 10 | 320 | N/A | 210 | 110 |
| Tree, Fruit, Evergreen | 1.5 | None | 320 | 110 | N/A | N/A |
| Vegetable, Leafy, Greenhouse | 2 | 14 | 480 | 160 | 95 (2)1 | N/A |
| Vegetable, Leafy, Outdoors (celery, florence, fennel) (lettuce) (endive) | 2.5 2.25 2 | 7 14 14 | 380 420 480 | 130 N/A 160 | 76 (7)1 N/A 95 (2)1 | N/A N/A N/A |
| Vegetable, Root (onions, garlic shallots) (potatoes) | 4 4.5 | 14 20 | 400 350 | 80 (7) 71 (10) | N/A N/A | N/A N/A |
| Vine/Trellis (grapes) | 1.5 | 1 | 640 | 320 | 64 (13) | 32 (32) |

1 – The MOE is 100 on the PHI, therefore the risks are not of concern for the high exposure tasks (hand harvesting)

MOEs in bold font are less than 100 and indicate risks of concern.

## Summary of Occupational Postapplication Risk Concerns and Data Gaps

A summary of all the occupational postapplication risks of concern for DCNA is included in Table 10, below.  Current label requirements specify 12 hour REI’s for all crops and PHIs of 2 to 14 days for food crops.  In some of the scenarios, the MOEs for DCNA do not exceed 100 at the REI for non-harvesting tasks or relevant PHI for harvesting tasks; and are therefore of concern to HED.

| Table 10 – Summary of DCNA Postapplication Risks of Concern |
| --- |
| Crop Group | Risks of Concern on Day 0 (12 hr REI) or the PHIs |
| Field/Row Crops, Low/Medium | None (MOE is 100 for hand harvesting after the 2 day PHI) |
| Cut Flowers | High exposure tasks |
| Ornamentals, Potted Plants | None |
| Vegetable, Curcurbit | None |
| Vegetable, Fruiting | None |
| Tree, Fruit, Deciduous | None |
| Tree, Fruit, Evergreen | None |
| Vegetable, Leafy, Greenhouse (Lettuce) | None (MOE is 100 for hand harvesting after the 14 day PHI) |
| Vegetable, Leafy, Outdoors (lettuce, celery, florence, fennel, endive) | None (MOEs are 100 for hand harvesting after the 7 and 14 day PHIs) |
| Vegetable, Root (onions, garlic, shallots, potatoes) | Medium exposure tasks - irrigating and scouting mature plants |
| Vine/Trellis (grapes) | High exposure tasks - hand harvest, leaf pulling, thinning, pruning, Very high exposure tasks - cane turning and girdling table grapes |

## Occupational Postapplication Risk Characterization

Since the DFR data was extrapolated from dry California test conditions, dissipation of DCNA may be faster in greenhouse settings.

The 2003 NASS Floriculture Survey indicates very low usage of DCNA on greenhouse grown plants and flowers.