Hydrology Lab's Research Modeling System (HL-RMS) User Manual

(Last Modified 10/25/04) _

Modified (11/1/04) by Fekadu Moreda – added features SNOW-17 & CONT-API

1.  INTRODUCTION

To facilitate research into the use of distributed modeling for hydrologic simulation and forecasting, HL has developed the Research Modeling System (HL-RMS).  Koren et al. (2003) provides a complete description of the model and its scientific basis.  Simulation results presented by Koren et al. (2003) and results from the Distributed Model Inter-comparison Project (DMIP) (http://www.nws.noaa.gov/oh/hrl/dmip/index.html) have demonstrated the benefits of using HL-RMS or similar modeling techniques for streamflow simulation.

This document provides all of the information required to setup and run the model.  The remainder of this user manual is organized into seven sections:

- Hydrologic system structure and hydrologic models

- Input data requirements

- System configuration

- Running the model

  - How to run

  - Input Deck Cards

  - Program output

  - Notes for running in forecast mode

  - Known limitations and bugs

- Parameter estimation and customization

6.1  The connectivity file

6.1.1  Adding outlets to the connectivity file

6.1.2  Adjusting cell areas in the connectivity file to reflect USGS defined drainage areas

6.3  Analyze flow measurement data to determine routing parameters

6.4  Generate customized routing parameter grids

- References

Appendices:

- Free format rules for the input deck

2.  HYDROLOGIC SYSTEM STRUCTURE AND HYDROLOGIC MODELS

A brief overview of the system structure and hydrologic models is provided here.  A more detailed description is provided by Koren et al. (2003).  The basic computational elements in the HL-RMS are HRAP (Hydrologic Rainfall Analysis Project) grid cells (or pixels).  Unique snowmelt, rainfall-runoff and routing parameters may be defined for each pixel.  There are also options within the system that allow spatial averaging of inputs or model parameters over areas larger than a single pixel (e.g. a forecast basin), but the HRAP pixel is the finest spatial resolution at which outputs can be generated and an hourly time step is the finest temporal resolution for time-series outputs in version 1.0.  Each model element consists of a SNOW-17, rainfall-runoff component (e.g. SAC-SMA or CONT-API model) and a routing component (hillslope and channel kinematic wave model in HL-RMS, a unit hydrograph option is also available).

The SNOW-17 model generates a rain-plus-melt which will be passed to a rainfall-runoff model. The rainfall-runoff component generates fast (surface) and slow (subsurface/ground) runoff.  Within each element, fast runoff is routed over a conceptual hillslope to a channel, and then channel inflow, combined with a slow runoff component and upstream pixel outflows, is routed through a pixel conceptual channel.  A conceptual hillslope consists of a number of uniform hillslopes (the number of uniform hillslopes depends on the stream channel density specified for the pixel).  A conceptual channel usually represents the highest order stream in a selected pixel.  A topographically defined cell-to-cell connectivity sequence is used to move water from upstream to downstream cells and to basin outlets.  Initially, complete HRAP cell-to-cell connectivity files are provided to each RFC by HL.  Algorithms used to define cell flow directions used to generate the cell-to-cell connectivity files are described by Reed (2003).  An implicit numerical scheme is used for the kinematic wave equation solution.

HL-RMS can currently be run in calibration mode and forecast mode.  In calibration mode, a likely use case is that simulations will be run for a relatively small area (e.g. a single basin or forecast group) but for many time steps (years).  In forecast mode, the anticipated use case is to run simulations for many basins/grid cells but for a shorter duration (e.g. 30 days). (The forecast option is not implemented in the version of HL-RMS delivered to MARFC. There will be future effort to include the forecasting option by providing additional function to output to the time series into infomix database.

3.  INPUT DATA

A simplified data flow diagram for the HL-RMS/ programs is provided in Figure 1.  Figure 1 shows that the main inputs required by the model are:

- Input variables, “XMRG grid files” (precipitation, air temperature and PE if available)

- Parameter grids

- Model states from a previous run (optional)

- Cell connectivity file

- Input deck

Figure 1.  HL-RMS Generalized Flow Chart

Grid formats:  HL-RMS reads precipitation and air temperature data in the XMRG format (http://www.nws.noaa.gov/oh/hrl/pps/pps.htm).  The data format for all other input grids (e.g. model parameters or saved model states from a previous run) is similar to XMRG binary grids with a minor difference in the header.  These XMRG-like grids are binary files with two header records. The first record is the same as the XMRG record and consists of four integers:  X- and Y-origins of HRAP, and numbers of columns and rows in the file.  The second record differs from XMRG records.  It includes two variables: an integer scale factor to convert integer*2 values into real values (to get the true values, divide the value stored in the file by this factor), and number of bytes per value (2 for integer*2 format and 4 for real*4 format). This allows keeping all grids in either integer*2 or real*4 formats.  As with the XMRG format, data values are written to the file in row-column format, with the southernmost row written to the file first and the northernmost row written last.

In calibration mode, during the first run for a set of basins, the model will read archived hourly XMRG precipitation files directly.  Reading many hourly XMRG files for long time periods (i.e. several years) is computationally slow; therefore, during the first run for an area separate 1-dimensional binary files are created which contain precipitation data for only the pixels being modeled.  Use of the 1-dimensional binary files as model input in subsequent runs greatly reduces run times.  Use of these 1-D binary files has been a useful strategy for calibration scenarios when the model is run many different times for the same model domain.  More details about the 1-D binary file format and the file naming conventions are provided in Section 5.

(1) Input variables.  These include hourly precipitation grids in XMRG format and climatological monthly potential evaporation (PE) and PE adjustment factor grids in an XMRG-like format.  A priori PE and PE adjustment factor grids are provided by HL for the conterminous United States.  NOTE: Hourly/daily potential evaporation grids can be also used as input if available.

(2) Parameters.

Up to 25 SNOW-17 parameters: Right now there are no a-priori SNOW-17 parameter grids. In our initial application of the distributed SNOW-17 model, all parameters are defined as a basin-specific. One exception is that the depletion curve can be set to a straight line with SI value greater than zero. Another alternative is to set SI=0. In the latter case the model assumes a snow or no snow for each pixel.

Up to 16 SAC-SMA parameters:  Right now, 11 a-priori SAC-SMA parameter grids are provided by HL for the conterminous United States.  In our initial applications, the other 5 SAC-SMA parameters (PCTIM, ADIMP, RIVA, SIDE, RSERV) have been defined as basin-specific constants in the input deck.  The program can accept grids for these 5 parameters if available, but the current HL-RMS pre-processing programs don’t produce spatially variable grids for these parameters.

Up to 37 CONT-API parameters: Right now, 10 a-priori CONT-API parameter grids are provided by the HL for Susquehanna River Basin. Other remaining parameters have been defined as basin-specific constants in the input deck.

Routing parameter grids:  As described by Koren et. al. (2003), there are two distinct routing regimes, hillslope and channel routing.  The hillslope routing method requires three input grids:  (1) slope, Sh, (2) roughness coefficient, nh, and (3) stream channel density, D.

The program converts hillslope parameter grids into one basic hillslope parameter grid, a specific hillslope discharge (q0,h) per a unit depth, based on Chezy-Manning’s equation:

where kq = 105 is a unit transformation coefficient.  A unit of hillslope specific discharge is

mm-2/3.s-1 if D is in km-1.

There are currently two options available for defining the channel routing parameter grids, a channel shape method and a rating curve method.  For the channel shape method, there are four channel input grids (4) slope, Sc, (5) roughness coefficient, nc, (6) shape parameter, b, and (7) top width parameter, a.  Shape and top width parameters are defined based on the assumed relationship between channel top width (B) and depth (H), B=a*H**b.  In this method, the four channel grids are converted into two basic channel parameter grids within the program, a specific channel discharge, q0,c, per unit channel cross-section, and a power value, mc, in the relationship between discharge and cross-section (Q = q0,cAmc) using the following relationships:

A unit of channel specific discharge is m3-mc.s-1 if a is in meters.

When the rating curve method is used, grids of q0,c and mc are defined explicitly by the user.  Section 7 of this manual describes methods to populate channel routing parameter grids with reasonable values using either method.

(3)  Initial state variables.  There are 8 initial state conditions for SNOW-17 model. For CONT-API there are 8 initial conditions.  SAC-SMA upper and lower zone states (UZTWC, UZFWC, LZTWC, LZFSC, LZFPC, ADIMPC), a hillslope routing state (water depth of each pixel), and channel routing states (channel cross-sectional flow area – states are stored at three locations along the conceptual channel of each pixel).  In calibration mode, the program will automatically save all the states for the last time step in each run.  In forecast mode, the program will automatically save all the states at 12z for each day up to the current time.  Only the states for selected basins are saved and all values outside the selected basin region are set to -1.0.  When starting simulations in a new basin or basins, it is often the case that no state variable grids are initially available, therefore, there is an option to start the model with spatially constant state variables for basins, specified in the input deck.  There is also an option in to output and display states for user specified times.

(4)  Connectivity file.  The connectivity file stores an ordered list of all cells in the model domain.  The cells are ordered so that each time the next cell in the list is reached, computations for all upstream cells have already been completed.  In the header of the connectivity file, the user specifies basin outlet cells and IDs of interest for a region.  The same outlet IDs used in the connectivity file are also used in the input deck to choose where hydrographs will be generated.  Figure 2 shows a screenshot of the top of a connectivity file.  More details about the contents of connectivity files are provided in Section 7.

(5) Input deck.  The input deck defines the model run period, parameter values and/or parameter scale factor adjustments for each basin, system paths to inputs and outputs, and other options.  All input deck options are described in Section 5.  Using input deck specifications, all parameter grids can be replaced by some uniform values for each selected basin/subbasin or the grids can be adjusted by some ratio for each selected basin/subbasin.

4.  SYSTEM CONFIGURATION

SYSTEM Configuration for ORMS ((See installation documents of ORMS. These documents are provided with the program source codes.)

5.  RUNNING THE MODEL

5.1. How to run (From the command line):

To run HLRMS, issue the command ‘orms -option <input.deck name>’ where orms is the executable program, and <input.deck name> is a file that defines the model run period, parameter values and/or parameter scale factor adjustments for each basin, file paths to inputs and output, and other options.

Run-time Options:

-c       By default HLRMS runs in forecast mode.  When the –c option is given, HLRMS executes in calibration mode.

-x       HLRMS can read binary XMRG files created on HP machines or Linux machines. Without the –x option, the program assumes that files were created on Linux.  With the –x option, the program assumes the files were created on an HP machine.

5.2.  Input Deck Cards:

Each card in the input deck begins with the @ symbol followed by a specific letter based on the type of input.  The entries on each card use free format, and the cards do not have to be defined in any particular order.  A description of the free format input rules is provided in Appendix I.  The only rule for placing input deck entries is that all basin specific information entries preceded by a “+”, have to be placed after each basin’s @I card.

Any line in the input deck that begins with “#” is considered a comment line.

@A (16 entries)

- start and end time (mmddyyy hh) – Z is the default time zone code.  In forecast mode, the start date represents the last day of observed data (LSTCMPDY).  In calibration mode this is the start and end of the simulation period.

Relative Dating – start and end dates can be specified using the “*”, which denotes the current date and time, followed by a “+” or “-“ sign and the number of days relative to the current date.

For example: If the current date and time is April 2 2003 06Z

- A start date of *-1, means the start date is April 1 2003 06Z

- time step in hours

- precipitation mode (1 = distributed (default), 0 =lumped precipitation)

- index telling whether to conduct a runoff simulation (1= run simulation, 0 = only process parameters)

- precipitation averaging scale (based on HRAP grid scale, e.g. if the input is 3, then the precipitation will be spatially averaged over 3x3 HRAP pixels)

- create XDHMS grids (1=yes, 0=no) for:

  - SAC parameters (sac_pname_xDHMS, where pname is one of 16 sac parameters)

  - routing parameters (rutpix_QSH_xdms, rutpix_Q0CHN_xdms, and rutpix_QMCHN_xdms)

  - monthly PE (sac_pe_mname_xdms, where mname is three letter abbreviation for month)

  - monthly PE adjustment (sac_peadj_mname_xdms, where mname is three letter abbreviation for month)

  - initial SAC states [fraction] (sac_name_xdms, where name is  uzfwc, uztwc, lztwc, lzfpc, lzfsc, and adimpc)

  - initial routing states (rutpix_areac1_xdms, rutpix_areac2_xdms, rutpix_areac3_xdms, rutpix_depth_xdms)

These grids show data relevant to the current run and reflect any adjustments specified on the @I card.  XDMS grids only show values for the basins modeled.  Other areas are filled with missing values (-9999).

- (Forecast Mode Only) number of days before the start time to start the simulation

- (Forecast Mode Only) number of hours of QPF (6,12,18, or 24)

e.g. @A  06011993   0   07312000   23   1   1   1   2   0  0   0   0   0   0   2 12

@O, Path to output files

- hydrograph (*.hyd)

- MAPX time series (*.pcp and *.mapx)

- model states (SAC-SMA and Routing – time stamped mmddyyyyhhz),

- requested XDMS format grids  - time stamped (see @V)

- This directory contains the “carry save” content grids(adimpc, lzfpc, uzfwc, lzfsc, lztwc, and uztwc- with the time stamp mmddyyyyhhz used in subsequent model runs.)

e.g. @O /bulk/1/SAC_dst_data

@P, Path to parameter grid files.

e.g. @P /fs/home/vkoren/devl/parameters/hrap

@Q, Path to sequence file.

e.g. @Q /fs/home/vkoren/SEQ_FILES/abrfc.seq

@X, Path to xmrg files and the number of characters denoting

the year.

e.g. @X /fs/hydro/Hydro_Data/ABRFC/PRECIPITATION/RADAR/STAGE3/RAD_97-99 4

@S, Path to QPF grid files and number of characters denoting year.  While this can be the same as the one defined for the @X card, it is not recommended. Placing the QPF and Precipitation XMRG files in the same directory greatly increases the display time of QPF files in XDHMS.

e.g. @S /fs/home/vkoren/devl/MPE   4

@V, Input for creating grids viewable in xdms (1 = yes, 0 = no, default is 0)

- start and end time for gridded output (format is ‘mmddyyy hhz’ where hh (hour) should be between 0 - 23)

NOTE: Dates can specified using the “*” as described for the @A card

- time interval for gridded output (e.g. 6 means output every 6 hours between the start and end date)

- precipitation grid  (xmrg_xdms_mmddyyyyhhz)

- ET grid (sac_et_xdms_mmddyyyyhhz)

- surface runoff grid (sac_surf_xdms_mmddyyyyhhz)

- subsurface runoff grid (sac_subf_xdms_mmddyyyyhhz)

- routed flow grid (sac_rutf_xdms_mmddyyyyhhz)

- SAC states grids [mm] (sac_name_xdms_mmddyyyyhhz, where name = uzfwc, uztwc, lztwc, lzfpc, lzfsc,adimpc)

- routing states grids (rutpix_depth_xdms_mmddyyyyhhz, rutpix_areac_xdms_mmddyyyyhhz)

These grids show data for the dates and interval specified.   XDMS grids only show values for the basins modeled.  Other areas are filled with missing values (-9999).  WARNING!!:  Using the @V card option can output a lot of interesting spatial information, but it can also potentially create a large number of output grids and fill up your disk, particularly if you choose a long duration and a short time interval.  In DHMS 1.0 the grids are not compressed and although output values are only written for the modeled area, the grids are padded with NODATA values for XDMS display.  Just one uncompressed file can be close to 1 MB.  Although XDMS cannot display compressed grids directly, if you want to output grids and save them for later use, a compression utility like gzip will reduce file sizes by a factor of several hundred.

e.g. @V  06081993 15 06081993 23    1   1   0   0    0    0   0  0

@D, SNOW model input

- ID

- number of parameter grids

- number of model parameters

- number of model states

e.g. @F snow 25 25 19

@F, runoff model input

- ID

- number of parameter grids

- number of model parameters

- number of model states

e.g. @F sac  17  17  6

e.g. @F api 37 37 8

@G, routing model input

- ID

- number of parameter grids

- number of model parameters

- number of states.

e.g. @G rutpix 7  3  2    Or @G rutpix 9 3 2

@I, Basin Inputs

- basin ID (maximum of 7 characters)

- indicator telling whether basin is nested (0 or 1if nested ;otherwise non-nested where the number denotes the number of nested basins, including itself).   Basins defined with an indicator greater than 0 will have a 1D xmrg file created.

e.g. @I  BLU18 0       Means nested basin

e.g. @I  BLUO2 2      Non-nested basin, the 2 indicates one sub-basin plus the parent basin (BLUO2)

Each @I card may contain entries specifying model parameter and state information.  There are three ways to define states and parameters:

(1) Specify a constant value for all cells in a basin.  This is done by entering a positive value for the parameter or state on the entry lines described below.  If positive, the specified value is used instead of a grid file, even if an input grid file exists.

(2)  Use values from an existing grid.  To do this, a value of -1 is entered for the state or parameter of interest.

(3)  Use values from an existing grid and scale them by a multiplier.  To do this, a negative value is entered for the parameter or state of interest.  The absolute value of this number is used as the grid multiplier.

If any parameter value entries are missing, the entries default to -1.  If either option 2 or 3 is used, the program will exit if no grid exists for the parameter or state of interest.

+ISRT, initial routing states:

- AREAC, Channel cross-sectional area of flow

- DEPTH, Hillslope water depth

e.g. +ISRT  5.0    0.

+ISRF, initial SAC-SMA states [fraction]

- uztwc, upper zone tension water contents

- uzfwc, upper zone free water contents

- lztwc, lower zone tension water contents

- lzfsc, lower zone free supplementary water contents

- lzfpc, lower zone free primary water contents

- adimpc, additional impervious area water contents

- +ISRF, initial CONT-API states

- API, Antecedent Precipitation Index

- SMI, Surface  Moisture Index

- BFI, Base Flow Index

- BFSC, Base flow

- AEI, Antecedent Evaporation Index

- ATI, Antecedent Temperature Index

- FI, Frost Index

- FEI, Frost Efficiency Index

e.g. +ISRF    0.25  0.25  0.25  0.25  0.25  0.25

Or   +ISRF   -1    -1    -1    -1    -1    -1   (use existing initial gridded states from a previous model run)

+ISSN, initial SNOW-17 states

- we, snow water equivalent (mm)

- neghs Initial heat deficit ( mm),

- liqw, liquid water equivalent

- tindex,  temperature index (DEGC)

- accmax, maximum water-equivalent that has occurred since snow began (mm)

- sndpt, snow depth (cm)

- sntmp, snow cover temperature (DEGC)

- sb, the last highest snow water equivalent before any snow fall (mm).

- e.g. +ISSN  0  0   0  0  0  0

Or   +ISSN  -1    -1    -1    -1    -1    -1   (use existing initial gridded states from a previous model run)

+IPSN Snow parameters

- ALAT, Altitude

- SCF, Snow fall correction factor

- MFMAX, Maximum melt factor /* input as mm/hr, but 'do_snow' converts to mm/dthr */z

- MFMIN, Minimum melt factor /* input as mm/hr, but 'do_snow' converts to mm/dthr */

- NMF, maximum negative melt factor mm/DEG/dtHR

- UADJ, The average wind function during rain-on-snow periods (mm * mb-1 * 6hr-1)

- SI,  areal water-equivalent above which 100 percent areal snow cover (mm)

- MBASE,  base temperature for non-rain melt factor  units -DEGC

- PXTMP, temperature that separates rain from snow  units -DEGC

- PLWHC, maximum amount of liquid-water held against gravity drainage – decimal fraction

- TIPM, antecedent snow temperature index parameter –range is 0.1 to 1.0

- PGM,   daily ground melt /* input as mm/day, but 'do_snow' converts to mm/dthr */

- ELEV, mean elevation

- LAEC  Snow –rain split Temperature, usually assumed to be Zero

- Depletion Curve (11 values)

+IPRF, API parameters (see table …)

Table11.  API parameters.

|  | Symbol | Description |  |
| --- | --- | --- | --- |
|  |  | Basic API parameters |  |
| 1 | AIXW | Intercept of wet curve (1st quadrant) | map |
| 2 | AIXD | Intercept of dry curve (1st quadrant) | map |
| 3 | CW | curvature of wet curve | map |
| 4 | CD | Curvature of dry curve | map |
| 5 | SMIX | Maximum value of SMIX | map |
| 6 | PEX | Potential evaporation that occurs on July 15th max for week number option) | unique |
| 7 | PEN | Potential evaporation that occurs on Jan 15th min for week number option) | unique |
| 8 | FRSX | Maximum percent runoff | 0.80 |
| 9 | EFC | Effective forest fraction |  |
| 10 | PIMPV | Fraction of watershed that acts as an impervious area | unique |
| 11 | RIVA | Fraction of watershed covered by riparian area | unique |
| 12 | RVAI | Antecedent Index, AI value above which riparian vegetation losses can occur | unique |
| 13 | APIKS | Daily API recession when snow exists | 0.93 |
| 14 | BFPK | Daily primary base flow recession rate | map |
| 15 | BFIK | Daily Base flow Index recession | map |
| 16 | BFIM | Weighing factor for BFI | map |
| 17 | AICR | Critical AIF value AIF value below which Fg=1.0 | map |
| 18 | CG | Curvature constant for groundwater inflow | unique |
|  |  | Commonly used option 1 for ET |  |
| 19 | AEIX | Maximum allowed Antecedent Index of Evaporation value | unique |
| 20 | AEIN | Minimum allowed Antecedent Index of Evaporation value | unique |
| 21 | APIX | Maximum value that API contains | 10 in |
| 22 | AEIK | Daily recession rate of AEI | unique |
| 23 | APIK | Daily recession of API | unique |
|  |  | Option 0 for week number |  |
| 24 | CS | Seasonal curvature Exponent (used only for week number option) | unique |
| 25 | WKW | Week number when the wettest condition exhibits | unique |
| 26 | WKD | Week number when the driest condition exhibits | unique |
|  |  | Option 2, for temperature | unique |
| 27 | ATIR | Temperature weight factor | unique |
| 28 | ATIX | Maximum allowed ATI | unique |
| 29 | ATIN | Minimum allowed ATI | unique |
|  |  | Option for frozen ground |  |
| 30 | CSOIL | Forest coefficient for bare ground | unique |
| 31 | CSNOW | Accounts for insulating effect of a snow cover | unique |
| 32 | GHC | Effect of heat transfer from below the forest layer | unique |
| 33 | FICR | Value of forest index above which soil frost has no effect | unique |
| 34 | CF | The EFI freezing coefficient controls the increase in FEI during cold periods | unique |
| 35 | CP | The amount of rain that must freeze to fill soil pores FEI during cold periods | unique |
| 36 | CT | The FEI thaw coeff.controls the decrease in FEI when thaws of the soil occurs | unique |
| 37 | EFA | Effective forest area controls the portion of watershed affected by frozen ground | unique |

+IPRF, SAC parameters

- UZTWM, maximum upper zone tension water

- UZFWM, maximum upper zone free water

- UZK, fractional daily upper zone free water withdrawal rate

- PCTIM, percent impervious area

- ADIMP, additional impervious area in percent

- RIVA, riparian vegetation area in percent

- ZPERC, maximum percolation rate

- REXP, exponent for the percolation equation

- LZTWM, maximum lower zone tension water

- LZFSM, maximum lower zone supplemental free water

- LZFPM, maximum lower zone primary free water

- LZSK, fractional daily supplemental withdrawal rate

- LZPK, fractional daily primary withdrawal rate

- PFREE, percent of percolated water which always goes directly to lower zone free water storages

- SIDE, ratio of non-channel baseflow (deep recharge) to channel (visible) baseflow

- RSERV, percent of lower zone free water which cannot be transferred to lower zone tension water

- PXADJ, an mapx adjustment factor (only accepts positive numbers) – not required

e.g. +IPRF -0.442  -0.99  -1.09 0.004  0.  0.028  -0.812  -1.05  -1.04 -0.87  -1.04  -1.302  -1.  -1.11  0.  0.3  1.5

+IPRT, routing parameters

- SLOPC, channel slope

- ROUGC, channel roughness coefficient,

- BETAC, channel shape parameter (exponent)

- ALPHC, channel shape parameter (top width at depth = 1)

- SLOPH, hillslope slope

- DS, channel density  (1/km)

- ROUGH , hillslope roughness coefficient

- Q0CHN, channel specific discharge for the rating curve method

- QMCHN, exponent in discharge-cross sectional area relationship for rating curve method

The following line specifies spatially constant values:

e.g., +IPRT  0.0005  0.05  1.2  2.0  0.002  1.5  0.35  0.2  1.25

+IPE, monthly PE entry (mm/day) (from Jan to Dec)

e.g. +IPE  1.19 1.33 1.84 2.63 3.70 4.91 5.21 4.33 3.49 2.52 1.67 1.25

+IPEA, monthly PE adjustment entry (from Jan to Dec)

e.g. +IPEA  1.0  1.0  1.0  1.0  1.0  1.0  1.0  1.0  1.0  1.0  1.0  1.0

+IUH, unit hydrograph entry: number of UHG ordinates followed by UHG values

e.g. +IUH   7   1.5    4.5    9.5   15.5   12.0   6.5   2.0

Note: If there is no IUH entry for a basin, then distributed channel routing is used as default

The @I card and all its entries are repeated for each modeled basin.

@STOP, End of input deck entries

5.3  Program Output: Text & Grid-Based

Several types of outputs are created by running HL-RMS.

Text

basin.info,  contains basin information, parameters and states:

Basin ID, AREA, number of PIXELS

Average API Parameters

Average API Initial States

Average monthly PE

Average PE Adjustment

Average Routing Parameters

Average Routing Hill States

Average snow Parameters

Average snow States

2)  Time series:

(* = five letter basin ID, all files are in OH datacard format)

*.hyd, simulated hydrograph

*.pcp, MAPX for local area

*.mapx, MAPX time series for a parent basin that contains nested basins; for basins that do not contain nested subbasins, no *.mapx file is created.  The data is in the *.pcp file.

Grid-Based

3)  XMRG-like Binary Grids:   These grids (parameters and states) are used as input to HL-RMS.  The parameter grids are read from the directory specified by the @P card.  State grids are either read from or written to the directory specified by the @O card.  In forecast mode state grids are automatically created at 12Z for each day of the modeled period.  In calibration mode state grids are created for the last time step.

* = runoff or routing model state name

*.mmddyyyyhh

4)  Binary Grids (Optional):

These grids, also in XMRG-like binary format, are created by executing HL-RMS.  They are meant for viewing in XDMS.  XDMS grids are requested on the @A and @V cards of the input deck  Grids requested on the @V card have names in the format name_xdms.mmddyyyyhhz.

Grids requested on the @A card are not date and time stamped and have the format name_xdms.

The output files described in items 1-4 are created by executing HL-RMS and saved in the directory specified on the @O card.

5)  Other:

*.xmrg (calibration mode only), a binary file containing rainfall data only for those grids within the selected basin. * represents a basin’s ID.  The new xmrg data is only created for basins with a non-zero entry for the @I card (non-nested).  The file is created to speed up calibration runs and thus is not used in forecast mode.  It duplicates data in the hourly XMRG files produced by StageIII/MPE.  For lack of a better term, we've been calling this a '1d XMRG' file even though it has a totally different file format from the hourly XMRG files.

Two WARNINGS when using 1D XMRG files:  (1)  Do not run multiple basins with a positive value on the @I card in the same deck and create multiple 1D XMRG files in the same run.  This creates the potential for erroneous reading and writing of data to the ‘1D XMRG files.  (2) Only reuse a 1D XMRG file as input to a subsequent run if you are simulating the exact same basin or set of nested basins used to create the file.  In calibration mode, the program automatically looks for a 1D XMRG file based on the name of the outlet defined with a non-zero entry for the @I card.

New data will automatically be appended to the file if the end time of simulation is later than the end time defined in an existing 1d xmrg file.  For other periods, the original xmrg data is read.  If any of the modeled basins does not have a 1d xmrg data, the program will read the original xmrg data.  The program does not read mixed xmrg data; it either reads original xmrg files or 1d-xmrg files.  Since the program may append new data to the 1d xmrg files, users need to make sure the file and directory permissions to the *.xrmg files are set as writable for all model users.  You can use use the executable chk_1dxmrg to get a summary of information related to the 1d xmrg data file.  Chk_1dxrmg is executed using the following syntax:

chk_1dxmrg ATIT2.xmrg

In this example, ATIT2.xrmg is located in the same directory as the executable.  Alternatively, the program will accept a full file path name

The following is an example of the information chk_1dxrmg returns.

This 1D xmrg binary file contains data

between 841512 (1/1/1996 0:00) to 902879 (12/31/2002 23:00) for 60 grids.

It contains total 61367 hours of data.

XMRGTOASCLX

xmrgtoasclx is a stand-alone utility used to convert binary xmrg-like grids to their ascii representation.  This utility is useful for viewing parameter, state and xmrg data created by executing HL-RMS.  Executing xmrgtoasclx with the -merge option creates an ascii and binary version of two merged xmrg-like binary grids.  Executing xmrgtoasclx without the –merge option requires 3 arguments, with the merge option it needs 4 in addition to the flag –merge.

Creating an ascii version of a xmrg-like binary grid

The syntax for executing xmrgtoasclx to create an ascii version of the xmrg-like grid is:

xmrgtoasclx grid.file1 output.file  [hrap/ster],

where grid.file1 is the name of a binary grid output from HL-RMS, output.file (with the extension .asc) is the name of the ascii file representing the xmrg-like grid.  This ascii file has a header defining the portion of the grid represented in the file.  The coordinates used to define x and y coordinates are determined by choosing hrap (HRAP) or ster (Polar Sterographic).

Merging xmrg-like binary grids

The syntax for executing xmrgtoasclx to merge xmrg-like grids is:

xmrgtoasclx –merge grid.file1 grid.file2 output.file  [hrap/ster]

where grid.file1 and grid.file2are the names of two binary grids output from hlrms, output.file is the name of the binary and ascii files containing the merged grids, and hrap or ster are used to define the coordinate system.  Running xmrgtoasclx with the –merge option creates an ascii text file named output.file. with the extension .asc.  In addition to the ascii file, the –merge option creates an xmrg-like binary file named output.file with the extension .bin.  This binary file is in a format HL-RMS can recognize as input.  When merging grids grid.file2 is superimposed onto grid1 (grid2 has precedence).

The following example takes the upper zone tension water binary state grids for wtto2  (sac_uztwc.0630200323z.wtto2) and knso2 (sac_uztwc.0630200323z.knso2) and creates the ascii file merge.output.asc and a binary version named merge.output.bin.

xmrgtoasclx –merge sac_uztwc.0630200323z.wtto2 sac_uztwc.0630200323z.knso2 merge.output  hrap

Future runs of xmrgtoasclx for the purpose of merging uztwc grids can use the merge.output.bin file as one of the input grids and join it with the sac_uztwc.0630200323z for another basin (e.g. sac_uztwc.0630200323z.eldo2).

5.5  Known limitations and bugs

1). Length of each line in input deck should not exceed 128 characters

2). Basin name in input deck should not exceed 8 characters

3). Maximum number of selected pixels for all basins should not exceed 50000

4). Maximum number of columns in modeling domain should not exceed 7000

5). Maximum number of basins/subbasins should not exceed 500

6). Default maximum length of channel routing subreach is 2000m, and maximum number of subreaches in one pixel should not exceed 4.

7). Cumulative flow comparison after the simulation incorrect for parent basins of nested basins.

8) New data can be appended to 1D xmrg files, they cannot be inserted.

6.  PARAMETER ESTIMATION AND CUSTOMIZATION

6.1 The connectivity file

6.1.1. Adding outlets to the connectivity file

The connectivity file contains 9 lines of general header information, followed by a list of basin outlets defined for the model, followed by an ordered list of pixels covering the entire modeling domain. The top portion of an RMS connectivity file is shown here.

TEXT_SEQ

NUM_HEADER_REC   13 24467

COL  1060

ROW   821

LLX     1

LLY     1

URX  1060

URY   821

DATA_HRAP

TEST1      1      5    5.0000  375  419

TEST2      1      9    5.0000  375  418

7099970    1   2232    5.6344  409  390

7124000    1   4879    6.4376  439  386

7130500    1   5370    6.6532  445  386

7139500    1  10177    6.7819  507  381

7146500    1  16856    6.6443  572  369

7164500    1  21425    6.5671  599  348

ELDO2      1  22439    6.1420  626  347

7249455    1  23316    6.4687  637  334

7263450    1  24466    6.4589  686  327

BLKO2      1  17407    6.2633  568  362

CBNK1      1  16559    6.2633  560  370

0     1 Rv    1 376 402  6.4589 377 419

1     5 Rv    1 375 401  6.4589 376 420

2     5 Rv    1 375 402  6.4589 376 419

3     5 Rv    1 374 401  6.4589 375 420

4     9 Rv    1 375 403  6.4589 376 418

5     9 Rv    1 374 402  6.4589 375 419

6    12 Rv    1 369 408  6.4589 370 413

7    12 Rv    1 369 406  6.4589 370 415

8    13 Rv    1 375 404  6.4589 376 417

.		.		.

.		.		.

.		.		.

Line 2:  Lists the number of outlets identified in this file (13) and the total number of cells listed in the file (24467)

Lines 3, 4:  Number of columns and rows in the input grids.

Lines 5, 6:  Lower-left X and Y coordinates.

Lines 7, 8:  Upper-right X and Y coordinates.

Lines 10-22:  Basin outlet specifications.  Information included in each line:

Col. 1:  ASCII identifier.  Must be the same as identifier used in HL-RMS Input Deck on the @I card (See HL-RMS User’s Manual).

Col. 2:  ignore

Col. 3:  Cell line number of this outlet

Col. 4:  Representative area (mi2) of cells in this basin.  Computed as the USGS area divided by the number of HRAP cells in the basin.  (program does not currently use this value)

Col. 5:  hrapx coordinate of outlet cell

Col. 6:  hrapy coordinate of outlet cell

Lines 23-24489:  Cell List

Col. 1:  Cell line number

Col. 2:  Cell line number of the next downstream cell

Col. 3:  ignore

Col. 4:  ignore

Cols. 5-6:  Local reference coordinates used internally by the program (ignore)

Col. 7:  Area represented by the cell in mi2

Cols. 8-9:  Globally referenced Hrapx and Hrapy (the true hrapx, hrapy coordinates)

To add a new outlet point, a new basin outlet specification line must be added (e.g. lines 10 – 22 in the example) and the value defining the number of outlets in line 2 (13 in this example) must be incremented by 1.  As defined above, the information required for the added line includes 6 values:  a basin identifier of eight characters or less, a dummy value of 1, the cell line number in the connectivity file corresponding to the basin outlet, a representative cell area, and the HRAP x and y coordinates of the outlet cell for this point.  These values should all be entered on one line in free format, separated by at least one space.

To determine the cell line number corresponding to a new outlet point, do a text string search on the connectivity file for the true hrapx and hrapy coordinates of the point you are adding (separated by a single space).  For example, search for “568 362” to identify the outlet line number for BLKO2 in the above example.  The search should find “568 362” in Columns 8-9 somewhere in the Cell List (lines 23-24489).  The value in Column 1 of the cell line number is the third number in your basin specification line (e.g. 17407 for BLKO2 in the example).  The fourth number, a representative cell area, can be taken from column 7 of the cell line number found in your search.

6.1.2 Adjusting cell areas in the connectivity file to reflect USGS defined drainage areas

The HL-RMS algorithms use the drainage areas defined for each cell in the connectivity file (cell list lines, Column 7) to convert rainfall-runoff depths to volumes.  The program sums the individual cell areas to get basin area estimates.  When the basic connectivity files are first generated, the drainage areas for each cell are computed based on the definition of the HRAP coordinate system.  Cell area estimates vary depending on the latitude of the cell center point.  Because of the coarse resolution of the HRAP cell network, it is sometimes possible that the total area estimate for basins from the raw connectivity file can be significantly different from the USGS estimate of the drainage area (on the order of 10% or more in some cases, particularly for basins smaller than 1000 km2) (see Reed (2003) for more details).  The reason for this is not just that curves in the basin boundaries cannot be precisely captured by a fixed origin, coarse resolution grid, but also that a single HRAP cell may contain the confluence of multiple stream tributaries.  If one of these tributaries is downstream of the gage and another upstream, then it is not possible to select an HRAP cell in the cell connectivity network that includes one tributary but not the other.

For situations when significant discrepancies between the USGS drainage area and the drainage area derived from the raw connectivity file exist, a separate utility program called cellareas is provided with DHMS 1.0 that will create adjust the cell areas in the connectivity file.  In this initial release, the cellareas utility is a rather inflexible program and uses an input file with strict formatting requirements; however, it serves its purpose.  Hopefully, the basin area adjustment functionality can be more smoothly incorporated into the main HL-RMS program in future releases.  The syntax for running the program is simply:

cellareas <control_file_name>

The control file must contain the following lines with no extra characters or comments:

Line 1:  Number of basins for which area adjustment is to be made (n)

Line 2:  Existing control file name

Line 3:  New control file name (the program adjusts areas for selected basins and copies the rest of the information from the original control file into the new control file)

Lines 4 through n+3:  A basin identifier (must be from 5 to 8 characters in length in this initial version) and the USGS area for the basin in km2.

Example control file contents:

2

wgrfc_var.con

wgrfc_var.con.adjust

ATIT2 831.34

KNLT2 896.1

** This example assumes cellareas is executed from the directory with the existing connectivity file.  Alternatively, lines 2 and 3 can be the entire file path, so cellareas can be executed from any directory **

IMPORTANT NOTE:  For basins containing subbasins, only the local area should be entered into the control file if the subbasins are also included in the same control file.  In other words, rather than entering the total area (km2) reported by the USGS for a large basin with nested/interior forecast points, the sum of all nested subbasins should be subtracted from the total basin area and that value should be entered in the cellareas control file.  (Yes, cellareas should be able to figure this out automatically, but it doesn’t yet.)  If your control file includes a parent basin but not the subbasin, then the areas for cells in the subbasin will be overwritten.  If you want the subbasin area to be overwritten, you should enter the total area for the parent basin.  If you add a new basin to the control file that is a subbasin of an existing parent basin, the area of the existing parent basin in the control file should be changed to reflect only the local area.  It is a good idea to keep all defined basins in one control file.

6.2  Analyze flow measurement data to determine routing parameters

6.2.1  Overview

The steps to estimate at-a-station routing parameters from flow measurement data could be done manually with a spreadsheet or similar tools.  However, because the procedure involves many steps, we offer an Excel Spreadsheet Add-in written with Visual Basic for Applications (VBA) to simplify this analysis process.  The Macros have not been tested on all versions of Excel.  They were originally developed using Excel 2000 and most recently used on Excel 2002.  Using the most recent version of Excel is recommended.

In this section, text describing required user actions is labeled with the word “Step” to distinguish it from additional explanatory text.  Some of the steps are optional as indicated in the explanation.

# 6.2.2  Download Flow Measurement Data

Step 1:  Go to http://water.usgs.gov/nwis

Step 2:  From the main page:  Click Surface Water.  Click Measurements.  At this point there are many search options to identify the stations you are interested in.  Choose whichever option you prefer.  The final product that you need to download is a Text file in Tab-Separated format.  Also, the date format is YYYY-MM-DD. The top of the file that you obtain should look something like the following (Note:  Data lines are cut-off on this example.  Actual data lines contain many more columns.).  Although it is possible to download data for multiple stations to a single file, the VBA Macros will only work if a separate data file is downloaded for each station.

#

# Surface water measurements

#

# Further descriptions of the columns and codes used can be found at:

# http://waterdata.usgs.gov/nwis/help?output_formats_help#streamflow

#

# Stations in this file include:

#  USGS 07337000 Red River at Index, AR

#

#

site_no	agency_cd	measurement_nu	measurement_dt	party_nm

15s	5s	5s	19d	12s	12s	12s	12s	12s	12s	12s

07337000	USGS	62	1952-07-11	k/m	5.40	1.03	0.43	1.68

07337000	USGS	63	1952-07-23	w	5.80	1.33	0.72	1.70

07337000	USGS	64	1952-08-06	w	35.0	38.5	0.79	2.07

07337000	USGS	65	1952-08-19	w	9.50	2.96	0.39	1.70

07337000	USGS	66	1952-09-03	g	7.60	2.14	0.34	1.69

6.2.3  SpreadSheet Instructions

As currently written, the VBA macros rely on a specific Workbook organization.  Sheets (Worksheets or Charts) with specific names are created.  A user may add his or her own  Worksheets or Charts and the order of the Sheets may be changed, but do not change any of the Chart or Worksheet names that are used by the programs!

A significant amount of introductory material describing the Worksheets created by the rmsmaster.xla Add-in is included here.  You may want to skip to instruction Step 3 and refer back to the Worksheet descriptions provided here as needed.

Default Worksheet Names and Explanation:

S_SelectData:  Selected columns of data are copied to this Sheet from the raw data file and sorted by Cross-section area (Area (m2)).  Columns with data in metric units are added to this sheet by the “Process Data” routines described below.

S_AvgdQAData:  Typically, there are many more observations at low flows than at high flows.  The “Process Data” routines average of observations with similar magnitudes to prevent excessive weighting at the low end of the Q vs. A curve in regression calculations.  These averaged values are stored in this Sheet.  This Sheet also contains numerous columns of predicted Q (“pred_Q”) as a function of A for different parameter sets (Defined in Columns A and B), and columns containing the differences between predicted and observed values.  Each of the predicted Q columns is computed based on intercept and slope parameters specified in Column B.  For Q = aA^b,  a = exp(intercept) and b = slope.  Several different types of regression fits are computed by default for consideration.

In the two ln[Q]cases, parameters (a, b(“slope”)) are derived by minimizing either the “squared error” differences or the “absolute error” differences between predicted and observed ln[Q].  Both intercept (int) and slope are optimized in these cases.  The labels for these cases are ln[Q] (squared error) and ln[Q] (absolute error).  A non-linear optimization fit is also done in arithmetic space.  Here residuals are computed based directly on the difference between predicted and observed Q values (rather than the log of the values).  These two cases (one minimizing the squared error and one minimizing the absolute error) are labeled “Q (squared error)” and “Q (absolute error)”.  In these four cases, parameter optimization is done automatically using the Excel solver (see steps below).  There are also two slots set up to allow for manual optimization (labeled “Manual Q Squared Error” and “Manual Q Absolute Error”)

The macros compute several different types of regression fits for the user because it is difficult to say with our current experience which fitting procedure is the best one to use.  In fact, so far, we have found that a manual option for specifying one parameter (say slope in log space) and then using the Excel Solver manually (explained more below) to optimize the other parameter produces the most satisfactory results based on our desired emphasis on high flow modeling in flood forecasting.

S_AvgdABData:  Same setup as the AvgdQAData Sheet except the variable relationship considered is cross-section area (A) as a function of width (B) as opposed to Q vs. A.  In this case, the parameters of interest ( and ) are both computed in Column D for various scenarios.   and  in B=H^are computed as a function of the intercept and slope terms in Column B.  Column B terms are optimized using the Solver.

S_Control:  Contains user input describing the basin or derived from other Sheets.

S_PredictedQA:  Contains Q and A data computed using the channel shape method.

Default Chart Names and Explanations :

C_QfA:  Observed data of Q vs A plus additional fitted lines; Data from S_AvgdQAData are displayed.  Notation stands for “Q as a function of A.”

C_Ln(QfA):  Plots of Ln(Q) vs. Ln(A) (observed data and fitted lines); Data from S_AvgdQAData

C_Ln(AfB):  Plots of Ln(A) vs. Ln(B) (observed data and fitted lines) using data from S_AvgdABData

C_AfB:  Plots of A vs B (observed data and fitted lines) using data from S_AvgdABData

C_n Graph:  Estimated Manning’s n vs. Q

Processing Steps:

Step 3:  You will need to load the “Rmsmaster” (provided by HL) and the “Solver” Add-ins.  To do this, put the file “rmsmaster.xla” anywhere on your PC.  With a blank Worksheet active, Select Tools – Add-ins and then click the “Browse. . .” button to locate the “Rmsmaster” Add-in.  Place a check mark next to this Add-in.  For the Solver, if the “Solver Add-in” is not listed as an option in your setup, you probably need to do a custom installation of Microsoft Excel to get the correct file off from your original CD-ROM.  Although you can benefit from rmsmaster.xla without the Solver, use of the Solver is recommended.

Step 4:  The first step is to load the USGS measurements file into Excel.  This can be done using standard Excel functions.  Select File --> Open (list all files *.*) and select your measurements file.  The “Text Import Wizard” should come up (Figure 3).

- Modify the “Start Import Row” to be the first non-comment row (comment rows start with #).  This is the row starting with the word “site_no”.

- Pick the “Delimited” option and click Next.  Use of the default “Tab” delimiters is correct.  Click Next again and then Finish.

Step 5:  With the data sheet that you just opened active, click Ctl-Shift-L and a new menu called “RMS Parameters” will appear.  (Ctl-Shift-U will unload this menu.)

Step 6:  Making sure that your raw data sheet is the active Sheet, Select the menu item:  RMS Parameters --> Process Data.  You will be prompted to enter a representative slope value for the basin outlet.  If you plan to use the rating curve routing parameter method you will not need a slope estimate.  If you don’t know the slope, you can always guess and enter the value later.  If you click Cancel, the value will default to 0.002.  The slope is used for calculating Manning’s n estimates.  This step creates the Charts and Worksheets described above and populates them with data.

### Figure 3.  Text Import Wizard

Step 7:  Populate the Charts with observed data by selecting any chart (e.g. C_QfA) and choosing the menu item Add/Subtract Series -->  Plot Observed

Step 8:  Compute default regression fits.  Make the Worksheet S_AvgdQAData active and select RMS Parameters --> Run Solver All

This should only take a few seconds; however, if the program appears to finish instantaneously there might be something wrong.  Some messages like “Trial Solution” should flash by at the bottom of the Excel Window.  The macro runs the Solver many times to get the optimal fits for parameters for the different regression cases on Sheets S_AvgdQAData and S_AvgdABData.

##### Estimate outlet Parameters for the “Channel Shape Method” or “Rating Curve Method”

At this point you can examine results and identify model parameters.  There are two methods currently available in RMS for defining channel parameters.  One method is referred to as the “Channel Shape Method” for which estimates of  and  in the relationship B=H^are required.  H is depth and B is width.  The second method is the “Rating Curve Method” for which estimates of a and b in the relationship Q = aA^b are required.  In general, it is easier to infer parameters for the Rating Curve Method than the Channel Shape Method from the flow measurement data.  For the DMIP basins our simulation results have shown little difference in the hydrographs simulated with the two different methods.  The expected advantage of the Channel Shape Method is in basins where there is significant variability in channel slopes because this method accounts for channel slope.  For more description of these two methods see Koren et al. (2003) or Reed et al. (2002).  We have not really worked enough with basins of this type to prove or disprove this advantage.

The menu “Add/Subtract Series” is available when a Chart Sheet is active.  Items under this menu will add a specified series to the graph if it is not there or remove the graph if it is there.  The item “Remove All Series” will remove all series from the graphs except the observed data.  Selecting an item under the “Add/Subtract Series” menu simultaneously updates all charts except C_n Graph, which is only affected by the “Plot Observed” option.

Channel Shape Method:

Step 9:  Look at "n Graph" Chart and pick a representative Manning's n value for high flows. Enter the Manning's n value you select in the "S_Control" Sheet B8.  You may want to adjust the y-axis scale when looking at this Chart (e.g. set the y-max value to 0.1).  Manning’s n values tend to approach a constant value as flows get bigger although the scatter in the data tends to be large.  There is much more scatter in these estimates at low flows but we are interested in values for higher flows so this is not a major concern.  Don’t worry too much about getting an exact value as this parameter can be adjusted later.

Step 10:  Examine the "C_Ln(AfB)" (area as a function of width) and "C_AfB” Charts.  Look at the default regression line fits.  For example, selecting the Add/Subtract Series --> ln[Q] (squared error) {Note that the series and menu item labels here are all ln[Q] or Q when they should be ln[A] or A.  The data are correct, just mislabeled – this can be fixed in a later version.} item will add the regression fit that minimizes the squared error differences between predicted and observed ln[A].  Predicted values are based on the intercept (B3) and line slope (B4) in the worksheet S_AvgdABData.  The corresponding  and  values are in cells D3 and D4 for this case.

The simple channel shape model cannot fit Area-Width data for all flow ranges, particularly since the flow characteristics are often markedly different when the flow exceeds bankfull conditions.  When fitting values of  and  parameters in the single parabola channel shape model to data, locations where a single large flow has been measured can significantly affect the values of these parameters.  We are currently planning to research a model with separate relationships for in-channel and out of channel flow but this has not yet been implemented.

Since we are more concerned with the flow velocity at high flows, we have tended to put more weight on the fit of regression lines at higher width and area values for initial HL-RMS testing.  To meet this criterion, we have been using a fairly subjective approach and we sometimes find it beneficial to using the automatically fitted lines for reference while also attempting semi-manual fits.

Step 11:  A semi-manual approach:  For example, looking at the optimized fits to the Ln(AfB) Chart, it is sometimes true that the fits in log space give much weight to low flow values while the fits in arithmetic space may ignore the low flow values a bit too much.  One thing that can be done is to compare the fitted slopes from the log and arithmetic cases in cells (S_AvgdABData) B8 and B16 (for example), and pick a slope somewhere in between these values, enter this value into cell B24, and then manually run the Excel solver to find the optimal intercept corresponding to that slope.  This type of fit may provide a reasonable representation of high flows while not completely ignoring middle and low flows.  Figure 4 shows an example of a subjectively fit line.  To manually run the Excel solver, run Tools --> Solver to optimize the intercept corresponding to a manually selected slope.  Figure 5 shows an example Solver dialog.  In this example the solver is used to minimize the residual values by changing the intercept value (S_AvgdABData!B18 by changing Cell B19).

The results from manual optimizations can also be plotted easily in the Charts using the option Add/Subtract Series -->  Q (manual, absolute error) (for example).

NOTE again that the values of  and  needed for HL-RMS are computed in column D of S_AvgdABData:  DO NOT CHANGE THE FORMULAS IN COLUMN D.

Figure 4.  Example of a subjective fit to ln[A] vs. ln[Width(m)] for TALO2 in ABRFC ( = 6.46 and  = 1.66)

#### Figure 5.  Example Solver Dialog

Step 12:  Choose your best set of  and  parameters and enter the values in S_Control!B9 and S_Control!B10.  Keep in mind that this is a very subjective procedure.  I wouldn’t agonize much over the choice of these values at this point since they can always be changed and may need adjustment when the simulation model is run.

Step 13:  Now you can plot the Q-A relationship predicted by your selected shape parameters and Manning’s n value.  Make the C_QfA Chart active and select Add/Subtract Series --> Plot Channel Shape Method QA.  The result is a dashed line on the Q vs. A plot.  You can now adjust your choice of Manning’s n in cell B8 on the control sheet to try to get a better match to the Q-A curve.

Step 14:  The genpar.exe program used to generate gridded parameter values (described in Section 2.3) requires one more piece of information: a representative cross section area at the outlet.  We usually select a value corresponding to relatively high flows that also corresponds to the selected Manning’s n value.  To get this value, go to the “S_SelectData” Worksheet and pick a value from Column G.  Manning’s n values are in Column n.  Don’t agonize too much over the choice of this value.

You now have all of the information you need to generate custom parameter grids using the Channel Shape Method:  , , n, slope, and Ao (representative x-section area at the outlet).

IF YOU HAVEN’T DONE SO, IT IS A GOOD IDEA TO SAVE YOUR WORK USING THE File --> Save As Microsoft Excel Workbook option.

Rating Curve Method:

Step 15:  Examine the "C_Ln(QfA)" and "C_QfA" Charts.  Look at the default regression line fits.  For example, selecting the Add/Subtract Series --> ln[Q] (squared error) item will add the regression fit that minimizes the squared error differences between predicted and observed ln[Q].  Predicted values are based on the intercept (B3) and line slope (B4) in the worksheet S_AvgdQAData.  The corresponding “a” value in the Q = aA^b relationship is in cell D3 for this case and the “b” value is equal to the line slope (cell B4).

The automatic regression fits tend to be more satisfactory for Q-A relationships than for A-B relationships; however, taking the semi-manual approach described in S11  seems reasonable for the Q-A fit also.  As with the A-B fits, the optimized fits in log space give more weight to lower flows and the optimized fits in arithmetic space give much less weight to lower flows.  An intermediate weighting can be achieved with the semi-manual fit: (1) compare the fitted slopes from the log and arithmetic cases in cells (S_AvgdQAData) B4 and B12 (for example), (2) pick a slope somewhere in between these values, (3) enter this value into cell B20, and (4) then manually run the Excel solver to find the optimal intercept corresponding to that slope.  To manually run the Excel solver, run Tools --> Solver to optimize the intercept corresponding to a manually selected slope.  Figure 5 shows an example Solver dialog.  In the Figure 5 example the solver is used to minimize the residual values by changing the intercept value (S_AvgdABData!B18 by changing Cell B19).

The results from manual optimizations can also be plotted easily in the Charts using the option Add/Subtract Series -->  Q (manual, squared error) (for example).

Figure 6 shows example results for a Q-A fitted relationship.  In this case, date information is also displayed for selected points.  Looking at dates in the raw data file may be useful if there has been a distinct change in the hydraulic behavior at a station.  Seeing distinct groupings of points.  At this point no tools have yet been developed to assist with this step.

Figure 6.  Example of a subjective fit to Q vs. A for TALO2 in ABRFC (a = 0.16, b = 1.283)

You can now use your a and b estimates to generate routing parameter grids as described in the next section.  Again, values of a are shown in S_AvgdQAData Column D and b values are the “slopes” in Column B.

6.3.  Generate customized routing parameter grids

Overview

The genpar program is used to update values in existing HL-RMS parameter grids.  The program assumes that all required parameter grid files already exist; however, the values in these grids may all be negative or NODATA.

Genpar can be used to update only one type of parameter at a time.  Multiple runs of genpar are required to update multiple parameters.  However, values in multiple basins can be updated in one run.  The input deck that specifies the basins for which parameters will be updated is very similar to that used for the main HL-RMS program.  The file genpar.card provided is an example input deck used to generate routing parameter grids.

Inputs

Values in the following parameter grids can be updated using genpar:

Table 2.  Routing parameter grids.

| No. | Grid Name | Description |
| --- | --- | --- |
| 1 | rutpix_SLOPC | channel slope |
| 2 | rutpix_ROUGC | channel roughness (Manning’s n) |
| 3 | rutpix_BETAC | channel shape parameter (b in B = aHb) |
| 4 | rutpix_ALPHC | channel width parameter (a in B = aHb) |
| 5 | rutpix_SLOPH | hillslope slope |
| 6 | rutpix_DS | drainage density |
| 7 | rutpix_ROUGH | hillslope roughness |
| 8 | rutpix_Q0CHN | q0,c in Q = q0,cAmc |
| 9 | rutpix_QMCHN | mc in Q = q0,cAmc |

The first seven grids are required to run HL-RMS using the channel shape method.  Only the last two grids are required for the rating curve method.

The genpar functionality for populating grids with parameter values depends on the type of parameter selected for a given run.  Currently there are 5 different parameter assignment algorithms implemented in genpar.  These algorithms are discussed briefly here with more explanation available in Koren et al. (2003).

- Constant value assignment.  This method assigns a constant value to all cells in a basin.  Different constants can be assigned for different basins.  Constant value assignment is possible for rutpix_BETAC, rutpix_SLOPH, rutpix_DS, rutpix_ROUGH, and rutpix_QMCHN.  In our applications, we have used constant values for all of these parameters except rutpix_SLOPH for which values can easily be computed from the DEM.  A pre-computed grid of rutpix_SLOPH is delivered with the HL-RMS software.  Rutpix_DS and rutpix_ROUGH grids are initially assigned default values of 2.5 and 0.15.  Default values for BETAC and QMCHN in the grids provided are 1 and 1.333 respectively; however, these values should be overwritten using locally derived values.

- Rutpix_SLOPC.  Default grids of channel slope are pre-computed at HL and provided to each RFC.  In the grids delivered, there are inaccuracies in computing channel slopes, particularly for low order channel cells.  Two reasons for inaccuracies are (1) the coarse resolution of the input DEM (400-m resolution in this case) and (2) the difficulty in precisely defining where lower order channels initiate.  Genpar can be used to make adjustments to slopes for low order channels based on an empirical relationship (Strahler, 1964) between hillslope slopes and channel slopes.  In the genpar routine, the relationship is only applied if the value predicted by the relationship is significantly different from the value computed from the DEM.

- Rutpix_ROUGC.  Spatially distributed values of channel roughness are estimated using an empirical relationship that is a function of drainage area, slope, and a representative channel roughness (no) at the outlet:

(Tokar and Johnson, 1995)

no and the two constants 0.272 and -0.00011 are specified on the +IPRG card described below.

- Rutpix_ALPHC values are estimated as a function of drainage area, slope, and ROUGC.

- Rutpix_Q0CHN values are estimated as a function of drainage area.

How to run

Execution syntax is simply:

genpar <input_deck_file>

Alternatively, instead of the genpar program, use HL-RMS to generate the routing parameters. In the HL-RMS case, modify the input card: the @G option and the @IPRG option as described below. Then, run HL-RMS (orms) with the modified input.

orms <input_deck_file>

If parameter generation is specified, HL-RMS will skip all other calculation and perform parameter generation. The generated parameter map will be saved in to a temp.gz file. The output file is placed in the output directory specified by @O. Note that parameters of multiple basins including nested are handled. However, as in the case of genapr, only one parameter map is generated per one run.

Input Deck Specifications

As shown in the example genpar.card file, the input deck cards that must be specified to run genpar include @O, @P, @Q, @G, and @I.  These cards are described in Section 5.2.  The output file specified on the @O card is not actually used by the program but a valid directory must be specified in order for the program to run properly.

The first entry on @G card must be 7 (channel shape method) to generate any of the grids 1-7 in Table 2.  The first entry should be 9 to generate either parameters 8 or 9, i.e.

@G rutpix  7  3  2   {for parameters 1 – 7, channel shape method}

@G rutpix  9  3  2    {for parameter 8 or 9, for the rating curve method}

Genpar will support the use of multiple @I cards (multiple basins) for a given run.  Only one +IPRG card should be specified for each @I card.

The +IPRG card:  The +IPRG line is used to specify parameter information.  The contents of the +IPRG card are:

+IPRG <n_values> <parameter #> <variable_1, variable_2,..., variable_(n_value-2)>

<n_values> is a number of entries in the input line including the <n_values> item.

<parameter #> is the number used to refer to a parameter (see Table 2)

<variable_i> input variables required to generate selected grid type

Example +IPRG cards:

+IPRG   3   3  <value>

Generates a constant value for rutpix_BETAC where <value> is the BETAC value

+IPRG  5  2  no 0.272 -0.00011

Generates distributed ROUGC parameters using the user defined no value (a representative roughness coefficient at outlet) and two constants in an empirical relationship.  Note that these constants are not counted in the <n_values> entry which is 2 for this case.

+IPRG   5   4   Qo   Ao   o

Generates distributed ALPHC grid.  Inputs are a ‘representative’ discharge (Qo) (This value is no longer used so really any value is o.k., but some value must be present), cross-section (Ao), and the  parameter at the outlet (deriving these values is discussed in Section 7.2).

+IPRG   3  9  <value>

Generates a constant value for rutpix_QMCHN

+IPRG   4  8  <q0chn_value>  <qmchn_value>

Generates rutpix_Q0CHN

Example steps for “Rating Curve Method” (numbers are only for this example)

Specify the @G card appropriately

@G rutpix  9  3  2

Specify a rutpix_QMCHN value

+IPRG   3  9 1.2333

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_QMCHN

Comment the rutpix_QMCHN line and specify the rutpix_Q0CHN line:

+IPRG   4  8 0.382  1.2333

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_Q0CHN

Example steps for “Channel Shape Method”

Specify the @G card appropriately

@G rutpix  7  3  2

#  Correct slope of small channels (SLOPC)

#  Parameters 0.178 & 1.25 are default values and could be excluded

Specify to correct rutpix_SLOPC

+IPRG  4  1  0.178  1.25

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_SLOPC

Comment the rutpix_SLOPC line and specify a rutpix_BETAC value

+IPRG   3  3 2.12

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_BETAC

Comment the rutpix_BETAC line and specify the rutpix_ROUGC line:

+IPRG   5  2  0.051  0.272  -0.00011

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_ROUGC

Comment the rutpix_ROUGC line and specify the rutpix_ALPHC line:

+IPRG   5  4  665.  614.  0.43

Run genpar

$genpar genpar.card

Copy TEMP

$ cp TEMP rutpix_ALPHC

Output

Genpar reads existing parameter grid files, computes new values for specified cells, and copies any unchanged values and the new values to a new file named ‘TEMP’ in the directory where the program is run.  This output file overwrites any existing file named ‘TEMP.’  TEMP is a binary parameter grid file.  After running genpar, the UNIX ‘cp’ command must be used to replace the corresponding binary grid in the HL-RMS parameter directory in order for HL-RMS to access the parameter updates, e.g.

cp TEMP rutpix_ALPHC

Note, again, that the TEMP file will be overwritten if genpar is executed again, so it is good idea to copy or rename the TEMP file after each ‘genpar’ run.

Rules and limitations

- The order in which parameter grids are generated is important!  The rutpix_ROUGC grid and rutpix_BETAC grids must be generated before the rutpix_ALPHC grid because the rutpix_ALPHC grid depends on ROUGC and BETAC.  For the same reason, the rutpix_QMCHN grid should be created before the rutpix_Q0CHN grid.

- Each time ‘genpar’ is executed for a basin, values for all cells upstream of basin outlets specified in the input deck are modified.  If a downstream outlet and a nested basin outlet are specified in the same input deck, the inter-basin area between the two gages will be assigned values depending on the downstream outlet parameters and cells upstream of the nested outlet will depend only on parameters specified for the nested outlet.  If in a subsequent run, only parameters for a downstream outlet are specified, values for cells inside the nested basin will be overwritten in the TEMP file.

- Genpar only updates parameter grid files.  Basic template files must exist in order for the program to work.  These template grids are provided by HL.

7.  REFERENCES

Koren, V., Reed, S., Smith, M., Zhang, Z., Seo, D.J., 2003, in press, Hydrology Laboratory Research Modeling System (HL-RMS) of the National Weather Service, Journal of Hydrology..

Reed, S., 2003, in press, Deriving Flow Directions for Coarse Resolution (1 - 4 km) Gridded Hydrologic Modeling, Water Resources Research.

Strahler, A.N., 1964.  Part II. Quantitative Geomorphology of Drainage Basins and Channel Networks, Handbook of Applied Hydrology, Section 4-II, V.T. Chow Editor, McGraw-Hill.

Appendix I:  Free format rules for the input deck

The program uses free format input for all cards.  Free format input rules are: The @ in the first position of the line denotes a card label.  Card labels can be on the same line or the line above the fields of the card.  For example:

@A 05021999 05311999 2

can be specified as

@A

05021999 05311999 2

- If a card is not needed for particular run, its label and all fields must be omitted.

- Only columns 1-128 can be used for input.  All columns beyond 128 are ignored.

- One comma or at least one blank can be used as a delimiter between fields.

- Blanks or commas are not allowed in character fields.

- All fields are required.  A null field (double commas) must be used to denote single fields for which default values are to be used.  If N consecutive fields use default values, N+1 commas must be used.  The following input implies that defaults are to be used for the first two fields on card C:

@C , , ,

- Not all fields have valid defaults.  If the documentation does not specify a default, the input must be specified.

- Consecutive commas at the end of a card can be omitted.  For example,

@E 1, , ,

Can be specified as

@E 1

- Any number of comment lines can be used in input card order.  Each comment line should have the # character in the first position of the comment line.

# Text boxes

A a BASIC TEST PROCEDURES  RESowered with DMS 1.0 and the suggested directory structure is provided in Table 1.  DMS 1.0.  Test