System Specification Changes for the WSR-88D Data Resolution and Coverage Enhancements

Prepared by OST/SEC

WSR-88D Data Resolution and Coverage Enhancements System Specification Changes

GENERAL NOTES:

This is a compilation of efforts completed to date by OST. ROC, and NSSL, and others suggesting changes to the WSR-88D System Specification for the Data Resolution and Coverage Enhancements. The purpose of this document is to describe System Specification level changes.  The changes described reflect the current understanding of requirements.

These are the proposed changes to revision F of the WSR-88D System Specification dated 28 April 2006.

The focus of this document is to identify the changes required in the system specification.

- Language in the FROM: sections are the requirements before the modification for Data Resolution and Coverage Enhancements.  Text in Bold Font are proposed changes since the last published System Specification.

FROM:

3.1.1.2.1  Base Data

Base data consist of the Doppler moments at the highest resolution available from the signal processor (at least reflectivity, mean radial velocity and spectrum width). The base products consist of reflectivity, mean radial velocity, and radial velocity spectrum width (standard deviation) estimates presented in a format suitable for display on a color graphic display. The derived products provide processed radar data, concentrated to provide large volumes and varieties of data in a form suitable for display on color graphic displays and, to the extent possible, requiring minimum interpretive effort. The alphanumeric products provide processed radar data for users without a graphic display capability. The derived data array products provide data in a non-displayable format for transmission to systems external to the WSR-88D System for further processing.

TO:

3.1.1.2.1  Base Data

Base data consist of the Doppler moments at the configured resolution available from the signal processor (at least reflectivity, mean radial velocity and spectrum width).

FROM:

3.1.1.2.2 Radar Products

Product generation will be automated to the extent feasible. However, at selected sites, an interactive display and data entry capability will be available for human analysis of radar data and assistance in the generation of certain radar products.

TO:

        - Radar Products

The base products consist of reflectivity, mean radial velocity, and radial velocity spectrum width (standard deviation) estimates presented in a format suitable for display on a color graphic display. The derived products provide processed radar data, concentrated to provide large volumes and varieties of data in a form suitable for display on color graphic displays and, to the extent possible, requiring minimum interpretive effort.  The alphanumeric products provide processed radar data for users without a graphic display capability.  The derived data array products provide data in a non-displayable format for transmission to systems external to the WSR-88D System for further processing.

Product generation will be automated to the extent feasible.  However, at selected sites, an interactive display and data entry capability will be available for human analysis of radar data and assistance in the generation of certain radar products.

FROM:

3.2.1.6   Data Processing Reserve

The equipment performing the RPG functions shall (1) have a processing reserve such that when processing the full load requirements (defined in Section 3.2.1.1) the utilization of each of the processing, addressable memory (available to software not including the operating system), and direct access mass storage functions, and removable storage functions averaged over a volume scan time period, does not exceed the following:

| RESOURCE | UTILIZATION |
| --- | --- |
| Processing | 30% |
| Addressable memory | 30% |
| Mass Storage | 30% |
| Removable Storage | N/A (Note1) |

Note 1: The utilization averaged over a volume scan time period is not reasonable when referring to removable storage since the functions described in 3.2.1.8 typically do not occur in that time frame.

This reserve is based upon the anticipated increase, over the first several years of operation, of resource requirements as indicated in the Radar Product Generation Algorithm Survey and Analysis Report, June 1996.

TO:

3.2.1.6   Data Processing Reserve

The equipment performing the RPG functions when the hardware is refreshed shall (1) have a processing reserve such that when processing the full load requirements (defined in Section 3.2.1.1) the utilization of each of the processing, addressable memory (available to software not including the operating system), and direct access mass storage functions, and removable storage functions averaged over a volume scan time period, does not exceed the following:

| RESOURCE | UTILIZATION |
| --- | --- |
| Processing | 30% |
| Addressable memory | 30% |
| Mass Storage | 30% |
| Removable Storage | N/A (Note1) |

Note 1: The utilization averaged over a volume scan time period is not reasonable when referring to removable storage since the functions described in 3.2.1.8 typically do not occur in that time frame.

This reserve is based upon the anticipated increase, over the first several years of operation after the hardware refresh, of resource requirements as indicated in the Radar Product Generation Algorithm Survey and Analysis Report, June 1996.

The equipment performing the RDA functions when the hardware is refreshed shall (2) have a processing reserve such that when processing the full load requirements (defined in Section 3.2.1.1) the utilization of each of the processing, addressable memory (available to software not including the operating system), and direct access mass storage functions, averaged over a volume scan time period, does not exceed the following:

| RESOURCE | UTILIZATION |
| --- | --- |
| Processing | 30% |
| Addressable memory | 30% |
| Mass Storage | 30% |

This reserve is based upon the anticipated increase, over the first several years of operation after the hardware refresh.

FROM:

3.7.1.1.1   Range Unfolding

The WSR-88D shall (1) provide mean radial velocity and spectrum width data processing with the accuracies specified in Section 3.7.2.2.3.1 over the unambiguous range interval of at least 115 km as defined by the following equation:

R (Unambiguous Range) = cTs
                                                        2

where: Ts = Doppler Pulse Repetition Time (PRT)
                           c = Speed of Light

##### A technique shall (2) be provided to present the mean radial velocity and spectrum width data at the correct range (range unfolding) to a minimum range of 230 km.  See Section 3.7.2.2.1.1 for unambiguous range coverage. Data significantly contaminated due to overlaid weather echoes or ground clutter shall (3) be identified.

TO:

3.7.1.1.1   Range Unfolding

The WSR-88D shall (1) provide mean radial velocity and spectrum width data processing with the accuracies specified in Section 3.7.2.2.3.1 over the unambiguous range interval of at least 115 km as defined by the following equation:

R (Unambiguous Range) = cTs

2

where: Ts = Doppler Pulse Repetition Time (PRT)

c = Speed of Light

A technique shall (2) be provided to present the mean radial velocity and spectrum width data at the correct range (range unfolding).  This range shall (2a) be configurable to a minimum range of 230 km or a minimum range of 300 km.  See Section 3.7.2.2.1.1 for unambiguous range coverage.  Data significantly contaminated due to overlaid echoes shall (3) be identified.

FROM:

3.7.1.6.4.18  Clutter Suppression Control

Through the MSCF, the capability shall (1) be provided, at a minimum, to:

a.	Define clutter suppression regions;

b.	Modify the bypass clutter filter map;

- Select the operational bypass map.

- Initiate generation of the bypass map

The definition of clutter suppression regions shall (2) include the capability to select the elevation angle(s), minimum and maximum ranges and azimuths, notch width selection, and type of suppression. The notch width selection shall (3) be one of the three levels of Doppler clutter suppression capability from Table 3-17. The capability shall (4) be provided to modify, through adaptation data, the selections in a, b, and c above.

The bypass clutter filter map shall (5) consist of a site-specific elevation angle independent clutter suppression map which specifies the ranges and azimuths to be used for clutter suppression.  This map applies to both Doppler and reflectivity clutter suppression.

TO:

3.7.1.6.4.18  Clutter Suppression Control

Through the MSCF, the capability shall (1) be provided, at a minimum, to:

- Define clutter suppression regions;

- Initiate generation of the bypass map

The definition of clutter suppression regions shall (2) include the capability to select the elevation angle(s), minimum and maximum ranges and azimuths, notch width selection, and type of suppression. The notch width selection shall (3) be one of the three levels of Doppler clutter suppression capability from Table 3-17. The capability shall (4) be provided to modify, through adaptation data, the selections in a, above.

The bypass clutter filter map shall (5) consist of a site-specific elevation angle independent clutter suppression map which specifies the ranges and azimuths to be used for clutter suppression.  This map applies to both Doppler and reflectivity clutter suppression.

FROM:

3.7.2.2.1.1.1 Base Reflectivity

The RDA shall (1) provide quantitative reflectivity estimates over an unambiguous range of 1 km to a minimum of 460 km (or up to a height of 70,000 ft MSL if this height occurs prior to reaching 460 km in horizontal range). The quantitative reflectivity estimates from 2 km to a minimum of 230 km shall (2) meet the accuracies specified in Section 3.7.2.2.3.2. The same signal processing scheme shall (3) be used to provide all reflectivity estimates.

TO:

3.7.2.2.1.1.1 Base Reflectivity

The RDA shall (1) provide quantitative reflectivity estimates over an unambiguous range of 1 km to a minimum of 460 km (or up to a height of 70,000 ft MSL if this height occurs prior to reaching 460 km in horizontal range). The quantitative reflectivity estimates from 2 km to a minimum of 230 km shall (2) meet the accuracies specified in Section 3.7.2.2.3.2.

FROM:

3.7.2.2.2.1 Azimuth Sample Interval

The RDA shall (1) provide an azimuth sample interval of greater than 0.953 degrees and less than 1.0555 degrees.

TO:

3.7.2.2.2.1 Azimuth Sample Interval

The RDA shall (1) provide a configurable azimuth sample interval.  The azimuth sample interval shall (2) be configurable to of greater than 0.953 degrees and less than 1.0555 degrees centered at the half degree or greater than 0.477 degrees and less than 0.528 degrees centered on the quarter and three-quarter degree.

FROM:

3.7.2.2.2.2 Range Sample Interval

The RDA shall (1) provide a range sample interval of not greater than 1 km, from 1 km to 460 km, including the effects of range averaging, for reflectivity measurements. The RDA shall (2) provide a range sample interval of not greater than 250 meters for mean radial velocity and spectrum width measurements from a range of 1 km to 230 km.

TO:

3.7.2.2.2.2 Range Sample Interval

The RDA shall (1) provide a configurable range sample interval of not greater than 250 m or 1 km, from 1 km to 460 km,  including the effects of range averaging, for reflectivity measurements. The RDA shall (2) provide a range sample interval of not greater than 250 meters for mean radial velocity and spectrum width measurements from a configurable range of 1 km to 300 km.

ADD:

###### 3.7.2.2.2.3 Effective Beam Width

For half-degree azimuth sample (3.7.2.2.2.1) mode of operation , the effective beam width shall (1) be no larger than 1.10 degrees (half power point).  For one degree azimuth sample (3.7.2.2.2.1) mode of operation , the effective beam width shall (2) be no larger than 1.50 degrees (half power point).

FROM:

3.7.2.2.3.1   Mean Radial Velocity and Spectrum Width

For the range of possible dwell times (TD), the RDA shall (1) provide estimates of mean radial velocity (V) and spectrum width (W) with the following accuracy and precision:

TABLE 3-14 MEAN RADIAL VELOCITY AND SPECTRUM WIDTH

|  | Accuracy | Precision (Note 2) |
| --- | --- | --- |
| Mean Radial Velocity | For a true spectrum width (Note 1) of 4 ms-1 the standard deviation in the estimate of the mean radial velocity will be less than or equal to 1.0 ms-1 including quantization errors, for signal-to-noise ratio (SNR) greater than 8 dB. | 0.50 ms-1 |
| Spectrum Width | For a true spectrum width (Note 1) of 4 ms-1 the standard deviation in the estimate of the spectrum width will be less than or equal to 1.0 ms-1 including quantization errors, for SNR greater than 10 dB. | 0.50 ms-1 |
| Note 1: True spectrum width is defined as one standard deviation of the meteorological phenomenon spectrum width within a sampled volume for which the indicated accuracy applies. Stated accuracy values apply for Nyquist velocities of the system. (Gaussian spectrum assumed.) Note 2: Precision is defined as the quantization, the smallest resolvable increment. Note 3. Significant biases introduced by the computational technique should be minimized. |

TO:

3.7.2.2.3.1   Mean Radial Velocity and Spectrum Width

For the range of possible dwell times (TD), the RDA shall (1) provide estimates of mean radial velocity (V) and spectrum width (W) with the following accuracy and precision for all Azimuth Sample Intervals specified in 3.7.2.2.2.1:

TABLE 3-14 MEAN RADIAL VELOCITY AND SPECTRUM WIDTH

|  | Accuracy | Precision (Note 2) |
| --- | --- | --- |
| Mean Radial Velocity | For a true spectrum width (Note 1) of 4 ms-1 the standard deviation in the estimate of the mean radial velocity will be less than or equal to 1.0 ms-1 including quantization errors, for signal-to-noise ratio (SNR) greater than 8 dB. | 0.50 ms-1 |
| Spectrum Width | For a true spectrum width (Note 1) of 4 ms-1 the standard deviation in the estimate of the spectrum width will be less than or equal to 1.0 ms-1 including quantization errors, for SNR greater than 10 dB. | 0.50 ms-1 |
| Note 1: True spectrum width is defined as one standard deviation of the meteorological phenomenon spectrum width within a sampled volume for which the indicated accuracy applies. Stated accuracy values apply for Nyquist velocities of the system. (Gaussian spectrum assumed.) Note 2: Precision is defined as the quantization, the smallest resolvable increment. Note 3. Significant biases introduced by the computational technique should be minimized. |

FROM:

3.7.2.2.3.2 Reflectivity (Z)

For the reflectivity provided by the RDA, from 2 to 230km, the estimates shall (1) be averaged over 1 km range bins. These reflectivity estimates shall (2) meet the following accuracy and precision requirements:

TABLE 3-15 REFLECTIVITY (Z)

|  | Accuracy | Precision (Note 2) |
| --- | --- | --- |
| Reflectivity(Z) | For a true spectrum width of 4 ms-1 the standard deviation in the estimate of the reflectivity will be less than or equal to 1 dB at SNR > 10 dB (including only the error due to meteorological signal fluctuations). | 1 dB |
| Note 1: Accuracy is defined as one standard deviation (SD) of the estimate, including effects of precision. Note 2: Precision is defined as the quantization, the smallest resolvable increment. |

Automatic calibration shall (3) reduce system hardware drift errors to less than 1 dB.

TO:

3.7.2.2.3.2 Reflectivity (Z)

For the reflectivity provided by the RDA, from 2 to 230km, all estimates shall (1) meet the following accuracy and precision requirements when averaged over 1 km for all Azimuth Sample Interval as specified in 3.7.2.2.1:

TABLE 3-15 REFLECTIVITY (Z)

|  | Accuracy | Precision (Note 2) |
| --- | --- | --- |
| Reflectivity(Z) | For a true spectrum width of 4 ms-1 the standard deviation in the estimate of the reflectivity will be less than or equal to 1 dB at SNR > 10 dB (including only the error due to meteorological signal fluctuations). | 1 dB |
| Note 1: Accuracy is defined as one standard deviation (SD) of the estimate, including effects of precision. Note 2: Precision is defined as the quantization, the smallest resolvable increment. |

Automatic calibration shall (3) reduce system hardware drift errors to less than 1 dB.

FROM:

        - Volume Coverage Pattern (VCP) Control

The capability to select the operational VCP from the set of defined local and remote (adaptation data) VCP suites shall (1) be provided (Note: “Local” scan strategies are stored in the RDA. “Remote” scan strategies are stored in the RPG). The capability shall (2) be provided to modify VCP parameters by elevation scan where appropriate. The parameters shall (3) include, but are not limited to Doppler PRF selection, SNR, sector definition, and velocity measurement increment.

TO:

3.7.3.4.15  Volume Coverage Pattern (VCP) Control

The capability to select the operational VCP from the set of defined local and remote (adaptation data) VCP suites shall (1) be provided (Note: “Local” scan strategies are stored in the RDA. “Remote” scan strategies are stored in the RPG). The capability shall (2) be provided to modify VCP parameters by elevation scan where appropriate. The parameters shall (3) include, but are not limited to Doppler PRF selection, SNR, sector definition, and velocity measurement increment.   The capability to display the current operational VCP shall (4) be provided.  The display shall (5) include but not limited to Doppler PRF selection, SNR, sector definition, base data resolution and velocity measurement increment.

ADD:

Appendix B Definitions

1.xx  Effective Beam Width

Effective Beam Width is the azimuthal resolution of a combination of the one-way antenna pattern, the azimuthal extent of the processed receiver samples, and any applied data windowing.  The Effective Beam is computed by the convolution of the one-way antenna pattern with the square of the data window as defined over the azimuthal extent of the sample.

FROM:

TABLE E-1a.  PRODUCT GENERATION & ARCHIVE PERFORMANCE LOAD

| Product Name | Coverage | Resolution | Products | Archive |
| --- | --- | --- | --- | --- |
| 1. Reflectivity Graphic | 0-230 | 1 x 1  | lowest 4 + 6.2, 10.0, 14.0 | lowest 1 |
| Graphic | 0-460 | 2 x 1  | lowest 3 | lowest 1 |
| Graphic | 0-460 | 4 x 1  | None |  |
| Digital | 0-460 | 1 x 1  | All elevations | None |
| 2. Mean Radial Velocity Graphic | 0-60 | 0.25 x 1  | lowest 1 | lowest 1 |
| Graphic | 0-115 | 0.5 x 1  | lowest 4 + 6.2, 10.0 | lowest 1 |
| Graphic | 0-230 | 1 x 1  | 14 elevations | lowest 1 |
| Digital | 0-230 | 0.25 x 1  | All elevations | None |
| 3. Spectrum Width | 0-60 | 0.25 x 1  | lowest 1 | lowest 1 |
|  | 0-115 | 0.5 x 1  | None |  |
|  | 0-230 | 1 x 1 | lowest 4 | lowest 1 |
| 4. Combined Shear | 230 x 230 | 1 x 1 | lowest 1 | None |
| 5. Combined Shear Contour | 230 x230 | 1 x 1 | No longer available |  |
| 6. Composite Reflectivity | 0-230 | 1 x 1 | 1 (16 lvl) 1 (8 lvl) | None None |
|  | 0-460 | 4 x 4 | 1 (16 lvl) 1 (8 lvl) | yes yes |
| AP removed | 0-230 | 1 x 1 | None | None |
| AP removed | 0-460 | 4 x 4 | None | None |
| 7. Composite Reflectivity Contour | 0-230 | 1 x 1 | No longer available |  |
|  | 0-460 | 4 x 4 | No longer available |  |
| 8. Echo Tops | 0-230 | 4 x 4 | 1 | yes |
| 9. Echo Tops Contour | 0-230 | 4 x 4 | No longer available | None |
| 10. Severe Weather Analysis (4 Products): | 50 x 50 | see product description | None |  |
| 11. Severe Weather Probability | 0-230 | 4 x 4 | 1 (with VIL) | yes |
| 12. Velocity Azimuth Display VAD |  | 1000 ft alt | None |  |
| Wind Profile |  | 1000 ft alt | 1 | None |
| 13. Combined Moment | 25 x 25 |  | No longer available |  |
| 14. Cross Section (230km X 70k') |  | 1 x 0.5 | 3 | None |
| 15. Weak Echo Region | 50 x 50 | 1 x 1 | No longer available |  |
| 16. Storm Rel Mean Radial Vel Region | 50 x 50 | 0.5 x 1 | 1 |  |
| Map | 0-230 | 1 x 1 | lowest 4 + 6.2, 10.0, 14.0 | lowest 1 |
| 17. Vertically Integrated Liquid | 0-230 | 4 x 4 | 1 | yes |
| 18. Storm Tracking | 0-460 | N/A | 1 | yes |
| 19. Hail Detection (Enhanced) | 0-230 | N/A | 1 | yes |
| 20. Mesocyclone | 0-230 | N/A | 1 | yes |
| Mesocyclone Rapid Update | 360 degrees x 124 nm | N/A | All Elevations | None |
| Mesocyclone Detection | 0-230 km | N/A | 1 | None |
| Mesocyclone Detection Data Array Product | 0-230 | N/A | All Elevations | None |
| Digital Mesocyclone Detection | 0-230 km | N/A | All Elevations | None |
| 21. Tornado Vortex Signature | 0-230 | N/A | 1 | yes |
| Tornado Vortex Signature Rapid Update | 0-230 km | N/A | 1 | None |
| 22. Storm Structure | 0-460 | N/A | 1 | None |
| 23. Layer Composite Reflec |  |  |  |  |
| 33M-60M | 460 x 460 | 4 x 4 | 1 | None |
| 24M-33M | 460 x 460 | 4 x 4 | 1 | None |
| Sfc-24M | 460 x 460 | 4 x 4 | 1 | None |
| AP removed Sfc-24M | 460 x 460 | 4 x 4 | 1 | None |
| 24. Layer Composite Turb |  |  |  |  |
| 33M-60M | 300 x 300 | 4 x 4 | No longer available |  |
| 24M-33M | 300 x 300 | 4 x 4 | No longer available |  |
| 25. User Alert Message | N/A | N/A | 1 | yes |
| 26. Radar Coded Message | N/A | N/A | 1 | yes |
| 27. Free Text Message | N/A | N/A | 1 | None |
| 28. Sfc Rainfall Accumulation 1 hr | 0-230 | 2 x 1 | 1 | yes |
| 3 hr | 0-230 | 2 x 1 | 1 | None |
| 29. Storm Total Rainfall Accum | 0-230 | 2 x 1 | 1 | yes |
| 30. Hourly Digital Precip Array | 0-230 | 1/40 LFM | 1 | yes |
| 31. Supplemental Precipitation Data | N/A | N/A | 1 | yes |
| 32. User Selectable Precip Accum | 0-230 | 2 x 1 | 1 | None |
| 33. Hybrid Reflectivity - Digital - Image | 0-230 0-230 | 1 x 1 2 x 1 | 1 | None |
| 34. Clutter filter control | 0-230 | 1 km x 1.4º (Legacy RDA) 1 km x 1.0º (Open RDA) | 1 | Yes |
| 35. ITWS Digital Base Velocity | 0-115 | 1 km x 1 º | None | None |
| 36. Clutter Likelihood Reflectivity | 0-230 | 1 x 1 | Lowest | None |
| 37. Clutter Likelihood Doppler | 0-230 | 1 x 1 | Lowest | None |
| 38. SuperOb | 0-230 (adaptable, default=100km) | Default = 5 x 6 (adaptable) | Default = 1 per hour (adaptable between 6 per hour and one every 3 hours) | None |
| 39. High Resolution VIL | 0-460 | 1 x 1 | 1 | Yes |
| 40. User Selectable Layer Composite Reflectivity | 360 degrees x 124 nm | 1 degree x 0.54 nm | None | None |
| 41. Digital High Resolution Enhanced Echo Tops | 0-345 | 1 x 1 ° | 1 | None |
| 42 One Hour Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| 43. Storm Total Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| 44. User Selectable Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| Note: Total product generation is depicted (both routine and one time requests). |

TO:

TABLE E-1a.  PRODUCT GENERATION & ARCHIVE PERFORMANCE LOAD

| Product Name | Coverage | Resolution | Products | Archive |
| --- | --- | --- | --- | --- |
| 1. Reflectivity Graphic | 0-230 | 1 x 1  | lowest 4 + 6.2, 10.0, 14.0 | lowest 1 |
| Graphic | 0-460 | 2 x 1  | lowest 3 | lowest 1 |
| Graphic | 0-460 | 4 x 1  | None |  |
| Digital | 0-460 | 1 x 1  | All elevations | None |
| Super Resolution Reflectivity | 0-460 | 0.25 x 0.5  | TBD | TBD |
| 2. Mean Radial Velocity Graphic | 0-60 | 0.25 x 1  | lowest 1 | lowest 1 |
| Graphic | 0-115 | 0.5 x 1  | lowest 4 + 6.2, 10.0 | lowest 1 |
| Graphic | 0-230 | 1 x 1  | 14 elevations | lowest 1 |
| Digital | 0-230 | 0.25 x 1  | All elevations | None |
| Super Resolution Mean Radial Velocity | 0-300 | 0.25 x 0.5  | TBD | TBD |
| 3. Spectrum Width | 0-60 | 0.25 x 1  | lowest 1 | lowest 1 |
|  | 0-115 | 0.5 x 1  | None |  |
|  | 0-230 | 1 x 1 | lowest 4 | lowest 1 |
| Super Resolution Spectrum Width | 0-300 | 0.25 x 0.5  | TBD | TBD |
| 4. Combined Shear | 230 x 230 | 1 x 1 | lowest 1 | None |
| 5. Deleted |  |  |  |  |
| 6. Composite Reflectivity | 0-230 | 1 x 1 | 1 (16 lvl) 1 (8 lvl) | None None |
|  | 0-460 | 4 x 4 | 1 (16 lvl) 1 (8 lvl) | yes yes |
| -AP removed | 0-230 | 1 x 1 | None | None |
| -AP removed | 0-460 | 4 x 4 | None | None |
| 7. Deleted |  |  |  |  |
| 8. Echo Tops | 0-230 | 4 x 4 | 1 | yes |
| 9. Deleted |  |  |  |  |
| 10. Severe Weather Analysis (4 Products): | 50 x 50 | see product description | None |  |
| 11. Severe Weather Probability | 0-230 | 4 x 4 | 1 (with VIL) | yes |
| 12. Velocity Azimuth Display VAD |  | 1000 ft alt | None |  |
| -Wind Profile |  | 1000 ft alt | 1 | None |
| 13. Deleted |  |  |  |  |
| 14. Cross Section (230km X 70k') |  | 1 x 0.5 | 3 | None |
| 15. Deleted |  |  |  |  |
| 16. Storm Rel Mean Radial Vel Region | 50 x 50 | 0.5 x 1 | 1 |  |
| Map | 0-230 | 1 x 1 | lowest 4 + 6.2, 10.0, 14.0 | lowest 1 |
| 17. Vertically Integrated Liquid | 0-230 | 4 x 4 | 1 | yes |
| 18. Storm Tracking | 0-460 | N/A | 1 | yes |
| 19. Hail Detection (Enhanced) | 0-230 | N/A | 1 | yes |
| 20. Mesocyclone | 0-230 | N/A | 1 | yes |
| Mesocyclone Rapid Update | 360 degrees x 124 nm | N/A | All Elevations | None |
| Mesocyclone Detection | 0-230 km | N/A | 1 | None |
| Mesocyclone Detection Data Array Product | 0-230 | N/A | All Elevations | None |
| Digital Mesocyclone Detection | 0-230 km | N/A | All Elevations | None |
| 21. Tornado Vortex Signature | 0-230 | N/A | 1 | yes |
| Tornado Vortex Signature Rapid Update | 0-230 km | N/A | 1 | None |
| 22. Storm Structure | 0-460 | N/A | 1 | None |
| 23. Layer Composite Reflec |  |  |  |  |
| 33M-60M | 460 x 460 | 4 x 4 | 1 | None |
| 24M-33M | 460 x 460 | 4 x 4 | 1 | None |
| Sfc-24M | 460 x 460 | 4 x 4 | 1 | None |
| AP removed Sfc-24M | 460 x 460 | 4 x 4 | 1 | None |
| 24.Deleted |  |  |  |  |
| 25. User Alert Message | N/A | N/A | 1 | yes |
| 26. Radar Coded Message | N/A | N/A | 1 | yes |
| 27. Free Text Message | N/A | N/A | 1 | None |
| 28. Sfc Rainfall Accumulation - 1 hr | 0-230 | 2 x 1 | 1 | yes |
| -3 hr | 0-230 | 2 x 1 | 1 | None |
| 29. Storm Total Rainfall Accum | 0-230 | 2 x 1 | 1 | yes |
| 30. Hourly Digital Precip Array | 0-230 | 1/40 LFM | 1 | yes |
| 31. Supplemental Precipitation Data | N/A | N/A | 1 | yes |
| 32. User Selectable Precip Accum | 0-230 | 2 x 1 | 1 | None |
| 33. Hybrid Reflectivity - Digital - Image | 0-230 0-230 | 1 x 1 2 x 1 | 1 | None |
| 34. Clutter filter control | 0-230 | 1 km x 1.4º (Legacy RDA) 1 km x 1.0º (Open RDA) | 1 | Yes |
| 35. ITWS Digital Base Velocity | 0-115 | 1 km x 1 º | None | None |
| 36. Clutter Likelihood Reflectivity | 0-230 | 1 x 1 | Lowest | None |
| 37. Clutter Likelihood Doppler | 0-230 | 1 x 1 | Lowest | None |
| 38. SuperOb | 0-230 (adaptable, default=100km) | Default = 5 x 6 (adaptable) | Default = 1 per hour (adaptable between 6 per hour and one every 3 hours) | None |
| 39. High Resolution VIL | 0-460 | 1 x 1 | 1 | Yes |
| 40. User Selectable Layer Composite Reflectivity | 360 degrees x 124 nm | 1 degree x 0.54 nm | None | None |
| 41. Digital High Resolution Enhanced Echo Tops | 0-345 | 1 x 1 ° | 1 | None |
| 42 One Hour Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| 43. Storm Total Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| 44. User Selectable Snow Accumulation | 0-230 | 1 x 1 | 1 | None |
| Note: Total product generation is depicted (both routine and one time requests). |