(SQ – 12) Wind Erosion Management Considerations (Assessment Guide)

| E = f (IKCLV): E = estimated avg. annual soil loss in tons/ac/yr; f = relationships are not straight-line mathematical calculations; I = soil erodibility index; K = soil surface roughness factor; C = climatic factor; L = unsheltered distance; V = vegetative cover |
| --- |
|  | I |  | K |  | C | Mo. %EWE |  | L | The smaller the unsheltered distance, the lower the soil erosion |  | V |  |
|  | WEG | SEI T/ac/yr |  | Krd | Krr |  | NM C factors | Jan Feb Mar Apr May Jun Jul Aug Sep Oct Nov Dec | 4.1 23.7 26.8 17.6 11.0 1.6 .4 .2 .9 1.3 5.0 7.6 |  | WED Factor | Multiply the WED factor times the Width of the Field to determine the Unsheltered Distance (L) in feet. |  |  | Lbs/acre of residues or growing crops |  |
|  |  |  |  | K = Krd x Krr |  |  |  |  |  |  |  |  |  |  |  |
|  | 1 | 220 |  | 1 .9 .8 .7 .6 .5 .4 | Lower Krd factor = lower soil erosion | 1 .9 .8 .7 .6 .5 .4 | Lower Krr factor = lower soil erosion |  | 30 50 80 100 120 150 | Lower C factor = lower soil erosion |  |  |  | 1.00 3.00 5.00 7.00 9.00 11.00 13.00 |  |  |  | Refer to the Small Grain equivalents (SGe) curves found in the NRCS National Agronomy Manual (NAM), Part 502, Figures a-1 through d-8. | Higher residue = lower soil erosion | The SGe expresses the effectiveness of residue or growing crops in resisting wind erosion. |  |
|  | 2 | 104 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3 | 56 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 4 | 56 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 4L | 56 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 5 | 38 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 6 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 7 | 21 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 8 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| WEG = Wind Erodibility Group SEI = Soil Erodibility Index (I) for irrigated soils Krd = Soil Ridge Roughness factor (is a function of Ridge height & Spacing, Angle of deviation & SEI) Krr = Random Roughness (rr) factor (Krr is a function of Cloddiness, as created by tillage & SEI) C is a function of windspeed & surface soil moisture % EWE = % Erosive Wind Energy (values are for Las Cruces, NM) | WED = Wind Erosion Direction factor (Reference: Tables 502-8A thru 502-8E of the NRCS NAM). WED factors are a function of field length/width ratio, wind preponderance and angle of deviation. V factor relates the kind, amount & orientation of vegetative material to its equivalent in lbs/ac of small grain residue in reference condition Small Grain Equivalent (SGe) | e.g. calculation: A fine textured soil was irrigated 3x during 45 days. 12% of the annual EWE occurs during this period. Therefore: Texture Wetness Factor (TWF) = 3; No. of irrigations during period = 3; Nonerodible Wet Days = 3 x 3 = 9; Irrigation Factor (IF) = (45 – 9) ÷ 45 = .80; Adjusted EWE = (.80) (12%) = 9.6% Note: angle of deviation is 00, when wind is perpendicular to the row Rudy Garcia 2008 |

NOTE: NRCS will be using WEPS (Wind Erosion Prediction System) to make wind erosion assessments