Summary Report

Workshop on Energetic Particle Measurements for the GOES R+ Satellites

Held at the

NOAA Space Environment Center

Boulder, CO

October 28-29, 2002

Workshop reporter: Dr. J. E. Mazur

The Aerospace Corporation

Space Sciences Department

January 2003

1. Summary	3

1. Synthesis of workshop recommendations	6

1.1 Electrons 100 eV-30 keV: surface charging	6

1.2 Protons	7

1.2.1 Protons <30 keV: surface dose and damage	7

1.2.2 Protons >300 MeV: total dose in SEP events	8

1.3 Z≥2	9

1.3.1 Z≥2, 1-100 keV: surface damage	9

1.3.2 Z≥2 above 10 MeV/nucleon: single-event effects	9

2. Measurement priorities	12

3. Instrument options	14

3.1 Electrons and protons 100 eV - 30 keV	14

3.2 Z≥2 above 10 MeV/nucleon	15

4. References	15

5. Acronym list	16

Appendix 1. Questionnaire results	17

Appendix 2. Summary of workshop presentations	20

Appendix 3. Attendance list distributed on October 28, 2002.	23

Appendix 4. Workshop schedule.	25

# 1. Summary

On October 28-29, 2002, the NOAA Space Environment Center hosted a workshop to solicit views on energetic particle measurements for the future GOES R+ spacecraft.  Terry Onsager of NOAA/SEC and Joe Mazur of The Aerospace Corporation invited workshop speakers, other attendees, and distributed a workshop questionnaire.  Attendees included representatives from NOAA, the US military, academic institutions, and other government agencies.  This document is a synthesis of the recommendations for particle measurements for the GOES R+ vehicles based on the workshop presentations and the responses to a workshop questionnaire.

Table 1 lists the main recommendations of the workshop.  The fiducial for the workshop was the capability of the GOES N-Q energetic particle instrumentation [Onsager].  In the case of electrons and protons, these recommendations extend the GOES N-Q capabilities to energies below 30 keV.  The major justifications were the improved specification of the electron spectrum in surface charging events and the extension of radiation belt models to cover energies important for surface dose and damage of spacecraft surfaces.  Surface charging is a significant hazard for spacecraft in GEO and the question of surface dose and damage is important for applications of new spacecraft materials.  There is also the science interest in the acceleration and drift of substorm electrons because, for example, of their possible role as seed particles for further acceleration up to MeV energies.

The case of Z≥2 ions is a new capability for GOES N-Q which measure only Z=2 above 4 MeV.  The major justification for the heavy ion measurements was the improved specification of heavy ion spectra in solar particle events that cause single-event effects in electronics.  The required instrumentation is more complex than the GOES-9 "Dome" detectors.  There was also a recommendation to include Z=8 at plasma energies for its role in surface damage to satellites.

Measurements of protons and electrons below 30 keV would be achievable with a single electrostatic analyzer.  The energetic heavy ions would require a more complex solid-state detector telescope.  See section 3 for more details on the instrument options.

In all cases, the workshop attendees agreed that GOES data are valuable for near-real time situational awareness.  Several presenters also stressed the value of the easily accessible and long-term archive of GOES data for development of future models and for input to science analysis.

| Species | Energy range | Target phenomenon | Spectral resolution | Pitch angle resolution | Instrument Type 1 | Page # |
| --- | --- | --- | --- | --- | --- | --- |
| Electrons | 100 eV- 30 keV | Surface charging | 10 to 40 channels | 5 to 36 bins; if not possible, restrict to equatorial pitch angles | ESA 2 | 6 |
| Protons | 100 eV- 30 keV | Surface damage | 10 to 40 channels | 5 to 36 bins; if not possible, restrict to equatorial pitch angles | ESA | 7 |
| Protons 3 | >300 MeV | Total dose in SEP events | 5 channels ; channel widths chosen to optimize statistics in typical MeV-2 spectra | 2 look directions | Same as GOES-9 | 8 |
| Z≥2 (Z=8) | 1- 100 keV | Surface damage | 10 to 40 channels | One equatorial look direction | ESA or magnetic-specrom-eter | 9 |
| Z≥2 Option: coarse Z resolution 4 | 10-500 MeV/nucleon | Single-event effects in SEP events | 10 differential for coarse mass resolution instrument | One look direction (west) | Multiple solid-state detector telescope | 9 |
| Z≥2 Option: LET monitor | LET from 0.1- 100 MeV/mg-cm2 | Single-event effects in SEP events | >36 channels in LET | One look direction (west) | Solid-state detector behind shielding | 10 |

Table 1.  Summary of GOES R+ energetic particles workshop recommendations.

Notes:  1 See section 3.

2 Electrostatic analyzer.

3 Modification of current capability of GOES N-Q: higher spectral resolution &

optimized channel widths.

4 Coarse resolution in Z corresponding to the mass groups He, CNO, Ne-S, and Fe.

Section 1 of this document contains a summary and synthesis of the major recommendations in the context of the GOES I-M and N-Q capabilities.  Section 2 discusses the priority of the recommendations, keeping in mind that the priorities for space environment data change as spacecraft technologies evolve.  Section 3 discusses some instrument options for making the recommended measurements.

# 1. Synthesis of workshop recommendations

The recommendations discussed in this section originate from the presentations at the workshop as well as the discussions and the workshop questionnaire.  We present them in a format that NOAA/SEC might use to develop requirements for the GOES R+ particles instrumentation.  They break down into three main areas: electrons (section 1.1), protons (section 1.2), and Z≥2 ions (section 1.3).

## 1.1 Electrons 100 eV-30 keV: surface charging

The workshop recommended extending the energy range for electrons to below the lower energy limit of the GOES N-Q satellites of 30 keV.  The main phenomenon driving this recommendation was differential charging of satellite surfaces (Fennell; Mandell; Carey). Fennell presented an overview of surface charging, pointing out the general conditions that lead to surface charging, but also noting that the phenomenon cannot yet be predicted in detail for a given vehicle in spite of significant modeling efforts.  Bodeau [1] pointed out an additional value of having monitors of the surface charging environment at the GOES satellites: GOES vehicles are closer to other satellites that orbit over the continental United States (CONUS) than the well-instrumented Los Alamos National Laboratory (LANL) vehicles [Baker et al. 1985].

Figure 1 shows an electron spectrum measured at geostationary orbit (GEO) during a charging event on a LANL vehicle [Mandell] along with fits to the spectrum.  In this case the data down to ~100 eV constrained the model of the environment.

Figure 1.  Measured electron spectrum (data points) and model fits (curves) to the electron environment during a surface-charging event on a LANL vehicle [Mandell].

Figure 2 shows the energy coverage electrons for GOES I-M and N-Q.  The figure also shows the workshop recommendation of a lower-energy limit of ~ 100 eV for GOES R+.

Figure 2.  Electron energy coverage of GOES I-M, N-Q, and workshop recommendation for R+.  Energies above 4 MeV are integral.

## 1.2 Protons

### 1.2.1 Protons <30 keV: surface dose and damage

The workshop recommended extending the energy range for protons to below the lower energy limit of the GOES N-Q satellites of 30 keV.  The phenomena driving this recommendation were radiation dose to surfaces, surface damage [Bodeau; Fennell] and source populations for the ring current [Carey; Sibeck].

Fennell [1] presented one example of ground-based tests of solar array cover glass samples after exposure to 10 years of the low-energy proton environment (Figure 3).  Discolorations in the figure indicated changes to the light transmittance of cover glass samples made with different compositions.  The changes from a visibly clear glass would have decreased the power output of the underlying arrays significantly.  The value of GOES measurements of protons down to ~100 eV would be the construction of an environment specification for use in spacecraft design [Bodeau; Fennell].

Figure 3.  Laboratory exposures of samples of solar array cover glass to low-energy protons [Fennell].

### 1.2.2 Protons >300 MeV: total dose in SEP events

There were two recommendations for the high-energy (>300 MeV) GOES proton measurements.  They both referred to the specification of the most extreme solar energetic particle events where the spectral forms are important inputs to total dose calculations for spacecraft design.  The first was to increase the spectral resolution above 300 MeV (GOES I-M, N-Q HEPAD has 3 differential channels and one integral above 700 MeV) in order to better measure the solar energetic spectrum of total ions at extremely high energies [Carey; Chenette].  The second recommendation was to adjust these high-energy range channel widths according to a typical energy-2 spectral slope to insure adequate statistics in the higher-energy channels [Kahler].

Figure 4 shows the energy coverage of protons for GOES I-M and N-Q and the workshop recommendation of a lower-energy limit of ~ 100 eV.  This lower energy limit would be the same as the electron limit if the measurements were made with a switching electrostatic analyzer (see section 3).

Figure 4.  Proton energy coverage of GOES I-M, N-Q, and workshop recommendation for R+.

## 1.3 Z≥2

For ions more massive than protons, the workshop presentations, questionnaire, and discussions focused on both surface-damage from low-energy plasma and single-event effects from high-energy ions.  The GOES I-M and N-Q cover helium from ~1-850 MeV/nucleon but do not identify heavier ions in any energy range.  Most workshop attendees suggested the addition of Z>2 ion measurements to GOES R+ in order to address the phenomena summarized in the following two sections.

### 1.3.1 Z≥2, 1-100 keV: surface damage

The workshop recommended measurements of ~1-100 keV O+, in addition to the H+ discussed in section 1.2.1, to address the most abundant species in the Earth's ring current for their effects on satellite surfaces (e.g. Fennell; Carey; Sibeck).  Specifically, these ions cause high radiation doses in surfaces as well as sputtering of materials whose by-products might contaminate systems using optical coatings, even solar arrays.  Since the surface effects are accumulated over long exposures to the environment, the value of making these measurements on the GOES satellites would be the ultimate specification of the environment for the design of future GEO spacecraft.

### 1.3.2 Z≥2 above 10 MeV/nucleon: single-event effects

The workshop discussed single-event effects from high energy (>10 MeV/nucleon) heavy ions and the uncertain specification of the energy spectra of these ions in intense solar energetic particle events [Barth; Golightly; Miller; Chenette].  The workshop recommended that coarse mass resolution from ~10-500 MeV/nucleon would be sufficient (He, CNO, Ne-S, & Fe), and offered an alternative approach based on particle energy deposit.

Chenette presented examples of the worst-case solar energetic particle (SEP) environment for ions, pointing out that the composition and variability of the galactic cosmic rays above ~10 MeV/nucleon are well defined and not necessary to measure with GOES.  The uses of these data include spacecraft anomaly investigations, decisions for launches of vehicles with single-event effect (SEE) susceptibilities, and archival data for the generation of environmental models.  Figure 5 compares the helium spectrum from the recent 14 July 2000 event with the worst-case "1-day in a thousand" measured on the IMP-8 satellite, highlighting their differences and the need to better specify these large-event spectra [Chenette].

Figure 5.  10-100 MeV/nucleon helium spectra in intense SEP events [Chenette].

Barth, Fennell, and Miller discussed the high-Z solar particle environment from the LET (linear energy transfer) perspective.  They also pointed out the need for improved specification of the high-energy and high-Z SEP environment, but expressed in units of LET (MeV/mg-cm2) most useful to the spacecraft design and testing communities (Figure 6).  Section 3 discusses this measurement approach in more detail.  Note that the LET measurement does not resolve mass, but includes all the species that are relevant to the energy deposit behind a known amount of spacecraft shielding.

Figure 6.  LET fluence spectrum integrated over a sequence of intense solar particle events [Barth].

Figure 7 summarizes the coverage in particle energy and atomic number for Z≥2 ions on GOES I-M, N-Q, and the workshop recommendations for R+.

Figure 7.  Energy coverage versus atomic number for GOES I-M, N-Q, and workshop recommendations for R+.

# 2. Measurement priorities

The workshop discussions did not significantly address measurement priorities.  For the purposes of this report, one way to infer the priorities implied at the workshop is to survey the presentations and questionnaires for the frequency with which the various phenomena and measurements were mentioned.  This approach has unknown uncertainty, as does any ranking of priorities based on the design needs for future spacecraft.  It is especially uncertain given the relatively low number of participants.

Table 2 lists the number of presentations that explicitly mentioned the need to make the following measurements.  Based on the 11 presentations, there was no phenomenon discussed at the workshop that had more interest than any other.  This suggests an equal priority for the recommended GOES R+ measurements.

| Phenomena/measurement | Number of presentations that mentioned the need for the measurement |
| --- | --- |
| Surface charging from 100 eV - 100 keV electrons | 5 |
| Surface damage from 1-100 keV ions | 3 |
| Single-event effects from >10 MeV/nucleon Z≥2 | 4 |

Table 2. Number of references in 11 workshop presentations to various recommended GOES R+ measurements.

For another approach to determining priorities, Fennell presented the results of a survey of the effects of the space environment on space systems [Koons et al. 1999]. Figure 8 is a histogram of the number of spacecraft anomaly reports versus environmental cause from the Koons et al. survey.  Figure 8 suggests that the specification of the surface-charging environment is most important since most of the surface charging anomalies occurred in GEO.  However, as noted above, if surface charging is highly localized and unpredictable, then the long-term specification of other surface effects and the LET environment may be a more important contribution for GOES.

Figure 8.  Histogram of the number of spacecraft anomalies versus environmental cause from the survey of Koons et al.  [Fennell & Mazur].

# 3. Instrument options

There were few discussions on instrument options at the workshop, so not every recommendation had an accompanying discussion about the details of how to make the measurement.  The following sections list the details that were mentioned in the presentations.  Table 3 lists the instrument options ordered by their complexity relative to the simplest instruments discussed at the meeting (surface charge monitor and LET monitor).

| Instrument | Product | Relative complexity |
| --- | --- | --- |
| Surface charge monitor | Surface-charging environment | Simple |
| LET monitor | LET behind known shielding | Simple |
| ESA | Spectrum of electrons responsible for surface-charging; low-energy protons responsible for surface dose/damage In principle, Z≥2 using foil technique | Moderate, but technologically mature |
| Z≥2 telescope | SEP spectra above 10 MeV/n | Moderate/high given coarse resolution requirement |
| Magnetic spectrometer | Plasma composition | High |

Table 3. Approximate relative complexity of several instrument options for the recommended GOES R+ measurements.

## 3.1 Electrons and protons 100 eV - 30 keV

The same instrument that would provide the spectral measurements of electrons below ~30 keV for surface charging effects could also provide the low-energy proton measurements important for surface dose and other surface effects.  An electrostatic analyzer with a cycling power supply fulfills these requirements with resources on the order of a few kg and a few watts [Carey].  In principle this same instrument could also provide the plasma O+ measurement in Table 1 by using a thin foil to stop the heavy ions, where the heavy ion intensity would be inferred by subtraction.

Fennell noted another example of a dual electron and ion capability in a single instrument.  An ion detector in back of a small magnetic spectrometer designed for electrons could provide clean proton measurements in the range of ~10-100 keV.  In this case, the clean proton measurement results from the deflection of the lower-rigidity electrons, and a threshold on a solid-state detector determines the low-energy limit.  The limit is not as low as achievable with an electrostatic analyzer [Carey].

Fennell also noted the usefulness of a simple charging-plate design as implemented on Intelsat satellites for monitoring the surface-charging environment.  In this case, the instrument returns the potential of the monitor relative to the spacecraft with a simple and robust technique but does not return the detailed spectra of the plasma environment that were responsible for charging events.  A charging plate is thus a simpler and lower-cost alternative to an electrostatic analyzer.

## 3.2 Z≥2 above 10 MeV/nucleon

Measurements of 10-500 MeV/nucleon Z≥2 ions with resolution of the major groups of He, CNO, Ne-S, and Fe, fulfills the need to specify the poorly characterized variability of the heavy-ion components in intense SEP events.  The coarse resolution lightens the requirements for knowledge of particle trajectories through an instrument with a stack of multiple solid state detectors.  It would still be necessary to have sufficient detector material to stop high energy Fe (e.g. the range of 170 MeV/n Fe is ~8.2 mm in silicon).

Barth noted that the energy spectra of individual ion species could be transformed into units of LET behind various thicknesses of spacecraft shielding for spacecraft engineering.  However, Barth, as well as Miller and Fennell, also pointed out the advantages of a direct measurement of LET behind shielding.  These advantages included the direct measurement of the parameter used in the engineering community (LET), the ability to measure LET behind several choices of shielding on the same vehicle, the inclusion of all relevant particle masses, and the relative simplicity of the instrument compared to a mass spectrometer.

In either case (mass spectrometer with coarse mass resolution or LET monitor), the workshop discussions noted that these measurements are not required on every GOES vehicle since the phenomenon is not as localized in local time as, for example, surface charging.  Mazur pointed out the SEP anisotropy of > 10 MeV protons at GEO due to particle access from the East versus the West, but noted the Western-looking direction would be sufficient for specifying the heavy-ion environment.  It was also noted that these Z≥2 ions could also be measured at an L1 monitor and still have significant application to satellites in GEO, although the time delay for propagating shocks from L1 to Earth can introduce uncertainty in specifying the SEP environment for the space station [Golightly].

# 4. References

D. N. Baker, W. Aiello, J. R. Asbridge, R. D. Belian, P. R. Higbie, R. W. Klebesadel, J. G. Laros and E. R. Tech, "Los Alamos Energetic Particle Sensor Systems at Geostationary Orbit," AIAA 85-0243. 1985.

J. Barth & M. Xapsos, "SEP measurements required for environment models and system design and testing", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

M. Bodeau, "What do satellite manufacturers want from GOES?", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

T. Carey, "LANL perspectives on space environment monitoring", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

D. Chenette, "On-orbit space systems users requirements for GOES energetic particle data: a perspective from Lockheed Martin", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

J. Fennell & J. Mazur, "Overview of the impact of the space environment on space systems", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

J. Fennell, "Let's not forget surface charging", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

M. Golightly, "3rd generation GOES spacecraft program: billions of dollars…GOES energetic particle measurements for support of manned spaceflight: priceless", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

S. Kahler, "Air Force Research Laboratory perspective on energetic particle measurements", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

H. Koons, J. E. Mazur, R. S. Selesnick, J. B. Blake, J. F. Fennell, J. L. Roeder, & P. C. Anderson, The impact of the space environment on space systems, Aerospace Technical Report TR-99(1670)-1, 1999.

M. Mandell, "The case for low-energy electrons", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

K. Miller, "The charged particle environment from a spacecraft designer's perspective", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

T. Onsager, "GOES I-M and N-Q EPS Overview", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

D. Sibeck, "Geospace and NASA's Living With a Star program", GOES R+ EP Workshop, Boulder, CO, 28-29 October 2002.

# 5. Acronym list

CONUS	continental United States

HEPAD	high-energy proton and alpha detector

GEO		geostationary orbit

LANL		Los Alamos National Laboratory

LET		linear energy transfer

SEE		single-event effect

SEP		solar energetic particle

# Appendix 1. Questionnaire results

On the GOES R+ workshop web site, NOAA/SEC provided the following questionnaire to survey the uses, limitations, and needs of users of GOES energetic particle data.  The total number of responses to the survey was 12; 8 of the people who responded also attended the workshop.

GOES R+ Energetic Particle Workshop Questionnaire

1. Select the category that best describes you as a current user of GOES energetic particle (EP) data.

_Government

_Military

_University/educational institution

_Commercial/business

_Other

2. For what purpose do you use the GOES EP data?

_Science research

_Situational awareness of the space environment

_As input to space weather models

_Other

3. Do you know of a need to measure the following on the GOES R+ platforms?

Energetic heavy nuclei - indicate mass resolution and desired energy range of measurements

| No |  |  |
| --- | --- | --- |
| If Yes, specify: | Mass resolution | Energy coverage (MeV/n) |
|  | Coarse element groups (CNO, Ne-S, Fe) | Minimum |
|  | Resolve all even-Z elements | Maximum |

Pitch angle resolution - indicate species, energy range, and angular resolution

| No |  |  |
| --- | --- | --- |
| If Yes, specify: | species | Energy coverage (MeV/n) |
|  | ions | Minimum |
|  | electrons | Maximum |

Particles at energies below ~30 keV:

| No |  |
| --- | --- |
| If Yes, specify: | species |
|  | ions |
|  | electrons |

4. Which best describes the bulk of your access to the current suite of GOES EP measurements?

_Near-real time

_Archival

5. What do you think are the significant limitations of GOES EP data? Indicate all that apply.

_Energy range

_Time resolution

_Energy resolution

_Ion composition

_Pitch angle coverage

6. Rate your satisfaction with current GOES EP measurements.

_Highly satisfied

_Satisfied

_Indifferent

_Dissatisfied

_Highly dissatisfied

7. Other comments or suggestions.

The responses to the questionnaires mostly reflected the opinions in the workshop presentations and discussions because of the significant number of respondents who also attended the workshop.  The following tables compile the answers to the questionnaire, each followed by a summary finding.  Note the percentages refer to the fraction out of 12.  Not all questions were answered fully.

| Question | Number of respondents who saw a need for this measurement | Coarse mass resolution (CNO, Ne-S, Fe) | Resolve all even-Z ions | Typical energy ranges (MeV/n) |
| --- | --- | --- | --- | --- |
| Need for measurements of energetic heavy nuclei | 9 (75%) | 7 (58%) | 2 (17%) | 30-400 0.02-0.6 20-1000 10-200+ |

Summary finding: Most respondents (75%) saw a need for Z≥2 measurements.  Most were also satisfied with coarse mass resolution of the heavy ions in the energy range from ~ 10 to a few hundred MeV/nucleon.

| Question | Number of respondents who saw a need for this measurement | Ions | Electrons | Typical energy ranges (MeV) | Typical pitch angle resolution (degrees) |
| --- | --- | --- | --- | --- | --- |
| Pitch angle resolution | 10 (83%) | 7 (58%) | 8 (67%) | 0.01-1 ions 0.01-10 e- | 5-36 |

Summary finding: Most respondents (83%) wanted pitch angle resolution for both ions and electrons.  The requested resolution varied from 5-degree bins to 36-degree bins.  One respondent suggested an energy-dependent resolution, with only 2 bins for electrons above a few hundred keV where there are fewer particles.

| Question | Number of respondents who saw a need for this measurement | Ions | Electrons | Typical energy range (from one respondent) (keV) |
| --- | --- | --- | --- | --- |
| Particles below 30 keV | 7 (58%) | 5 (42%) | 6 (50%) | 0.03-30 |

Summary finding: Most respondents (58%) wanted to extend the GOES capability below 30 keV for both electrons and ions.

| Question | Energy range | Time resolution | Energy resolution | Ion comp-osition | Pitch angle coverage |
| --- | --- | --- | --- | --- | --- |
| Significant limitations of current GOES EP measurements | 6 (50%) | 3 (25%) | 9 (75%) | 6 (50%) | 7 (58%) |

Summary finding: Over 50% of the respondents thought there are limitations in GOES energy range & resolution, ion composition, and pitch angle coverage.  The time resolution of the GOES data was not a significant limitation.

| Question | Highly satisfied | Satisfied | Indifferent | Dissatisfied | Highly dissatisfied | No comment |
| --- | --- | --- | --- | --- | --- | --- |
| Rate your satisfaction with current GOES EP measurements | 0 (0%) | 4 (33%) | 4 (33%) | 3 (25%) | 0 (0%) | 1 (8%) |

Summary finding: There was roughly an equal mix of respondents who were satisfied, indifferent, or dissatisfied with the current GOES particle measurements.

# Appendix 2. Summary of workshop presentations

Sources: presentations as forwarded to the workshop reporter, reporter's notes during the presentations and during the workshop discussions

Criterion for listing in the table: specific recommendations for GOES R+ above and beyond the requirements for GOES I-M and N-Q

| Presenter(s)/source | Electrons | Protons | Z≥2 | Comments on availability of GOES data and environment models |
| --- | --- | --- | --- | --- |
| Joe Fennell | Extend measurements down to 1 keV for surface charging environment Option: separate surface charging monitor | 1-100 keV H for surface damage environment | 1-100 keV O+ for surface damage environment Simple LET sensor to monitor energy deposit from high energy solar and galactic particles | GOES spacecraft are "gateway" to the magnetosphere Near real-time data from GOES are critical for space situational awareness |
| Mike Golightly |  | Protons from10 to 500 MeV most significant for human bio damage | Heavy-ions relevant for single-event effects on some ISS subsystems | Near-real-time data availability critical to ISS support |
| Kyle Miller |  |  | Measurement of LET in range of ~10-100 MeV/mg-cm2 rather than individual species Z≥2 not used in total dose calculations at present | Need validated models of worst-case, typical, and total solar particle fluence focused on effects on space systems (e.g. energy deposit, or LET) |

| Mike Bodeau | Spectra over ~10 -100 keV for analysis of surface charging environment in GEO longitudes over CONUS | 1- 100 keV for spacecraft design (e.g. solar arrays) |  | Need long-term data archive & models of plasma environment at GEO Not many data on GEO surface charging environment for satellites over CONUS |
| --- | --- | --- | --- | --- |
| Dave Chenette |  |  | High-Z solar particle composition poorly specified in models (e.g. worst-case flux of heavy-ions probably uncertain by factor of 10) Desire Z≥2 composition and spectra, 10-100's MeV/nucleon | GOES data valuable because of easy access to near real-time data and long-term, consistent archive |
| Janet Barth & Mike Xapsos |  |  | Recommended new instrument to monitor LET up to ~100 MeV/mg-cm2 (includes Z≥2 ions) Advantage of direct measurement of energy deposit behind spacecraft shielding |  |
| Tom Carey | Few eV to ~50 keV with 10 to 40 energy channels 0.3-10 MeV: biggest need is improved spectral resolution (4 or more differential channels) | 0.3 to ->500 MeV biggest need is improved spectral resolution (5 or more differential channels) | 1-100 keV O+ ring-current composition for surface effects |  |
| Steve Kahler |  | Optimize energy channels for a typical E-2 solar particle spectrum ( to ensure sufficient statistics in each channel at high energy) |  | GOES solar particle measurements essential for research |
| Stephan Quigley | 30 eV to 100 keV for surface charging specification |  |  |  |
| Myron Mandell | 1 eV to 100 keV with 10's of channels (capability similar to LANL magnetospheric particle analyzer instrument) |  |  | GOES low-energy electron data would be used to develop asset-specific models of spacecraft charging for design and in-fight analysis |
| Dave Sibeck | 20 keV to 10 MeV with full pitch angle resolution if complete pitch angle resolution not possible, restrict FOV to equatorial pitch angles | 20 - 600 keV H+ with full pitch angle resolution if complete pitch angle resolution not possible, restrict FOV to equatorial pitch angles | 20 - 600 keV O+ with full pitch angle resolution if complete pitch angle resolution not possible, restrict FOV to equatorial pitch angles | Improve availability of high-time resolution magnetometer data |

# Appendix 3. Attendance list distributed on October 28, 2002.

Total attendance = 27.

| Name |  | Institution | Phone | Email address |
| --- | --- | --- | --- | --- |
| Michael | Bodeau | Boeing Satellite Systems | 310-416-6928 | Michael.bodeau@boeing.com |
| Pat | Bornmann | Ball Aerospace | 303-939-5833 | Pbornmann@ball.com |
| Tom | Carey | Los Alamos National Lab | 505-667-1239 | Tcarey@lanl.gov |
| Thomas | Cayton | Los Alamos National Lab | 505-665-2582 | Tcayton@lanl.gov |
| David | Chenette | Lockheed Martin ATC | 650-424-3449 | Dave.chenette@lmco.com |
| Stephen W. | Dandt | Ball Aerospace | 303-939-5023 | Sdandt@ball.com |
| Gerald | Dittberner | NOAA/NESDIS | 301-457-5125 x113 | Gerald.dittberner@noaa.gov |
| Jim | Eraker | Ball Aerospace BATC | 303-939-5655 | Jeraker@ball.com |
| Joe | Fennell | The Aerospace Corporation | 310-336-7075 | Joseph.fennell@aero.org |
| Howard | Garcia | NOAA/SEC | 303-497-3916 | Howard.a.garcia@noaa.gov |
| Michael | Golightly | NASA/JSC | 281-483-6190 | Mgolight@ema.jsc.nasa.gov |
| George | Ho | JHU/APL | 240-228-7083 | George.ho@jhuapl.edu |
| Stephen W. | Kahler | AFRL/VSBXS | 781-377-9665 | Stephen.kahler@hanscom.af.mil |
| Xinlin | Li | University of Colorado/LASP | 303-492-3514 | Lix@lasp.colorado.edu |
| Myron | Mandell | SAIC | 858-826-1622 | Myron.mandell@saic.com |
| Joe | Mazur | The Aerospace Corporation | 310-336-2389 | Joseph.mazur@aero.org |
| Kyle | Miller | Mission Research Corporation | 719-237-4703 | Kimller@mrcll.com |
| Joe | Mobilia | Lockheed Martin ATC | 650-424-3292 | Joseph.mobilia@lmco.com |
| Bill | Murtagh | OL-P/AFWA USAF | 303-497-7492 | William.murtagh@noaa.gov |
| Neal | Nickles | Ball Aerospace | 303-939-4783 | Nnickles@ball.com |
| Terry | Onsager | NOAA/SEC | 303-497-5713 | Terry.onsager@noaa.sec |
| Ahmet | Ozkul | INTELSAT | 202-944-7334 | Ahmet.ozkul@intelsat.com |
| Bob | Prochaska | Raytheon | 719-637-7089 | Robert_d_prochaska@raytheon.com |
| Stephen | Quigley | AFRL/VSBX | 719-556-2889 | Stephen.quigley@cisf.af.mil |
| David | Sibeck | NASA/GSFC | 301-286-5998 | David.sibeck@gsfc.nasa.gov |
| Howard | Singer | NOAA/SEC | 303-497-6959 | Howard.singer@noaa.gov |
| Zdenka | Smith | NOAA/SEC | 303-497-3473 | Zdenka.smith@noaa.gov |
| Ron | Zwickl | NOAA/SEC | 303-497-3029 | Ron.d.zwickl@noaa.gov |

Figure A1.  Representation of different institutions at the workshop: gov = US government, mil = US military, edu = educational, com = commercial.

# Appendix 4. Workshop schedule.

GOES R+ Energetic Particles Workshop

Monday-Tuesday, October 28 - 29 2002

NOAA

David Skaggs Research Center

325 Broadway

Boulder, CO

Room 2A305

Phone: 303-497-3113

Schedule summary:

Monday, October 28, 2002

| 09:00 - 10:30 | Session 1 |
| --- | --- |
| 10:30 - 11:00 | Coffee break |
| 11:00 - 12:00 | Session 2 |
| 12:00 - 13:00 | Lunch break |
| 13:00 - 15:00 | Session 3 |
| 15:00 - 15:30 | Coffee break |
| 15:30 - 17:00 | Session 4 |

Tuesday, October 29, 2002

| 09:00 - 12:00 | Session 1 |
| --- | --- |

Breakfast:

A light breakfast will be served every morning from 08:00-09:00 outside room GC402, one floor down from the entrance area to the David Skaggs Research Center.

Presentations:

The times and order of the presentations are flexible.  We have allocated 20-30 minutes per talk, including at least 5 minutes of discussion.

NOAA will provide overhead projectors and computer projectors.  There will also be a laptop for running Powerpoint charts (bring presentations on a CD-ROM if you choose to use this method).

Joe Mazur and Terry Onsager will ask for copies of the presentations.  Either hardcopy at the meeting or electronic files sent via email after the meeting are acceptable.

| Monday, October 28, 2002 |
| --- |
| Welcome & workshop overview |
| 09:00 | Welcome & local arrangements | Terry Onsager/NOAA |
| 09:10 | Workshop goals | Terry Onsager/NOAA Joe Mazur/The Aerospace Corporation |
| 09:20 | Energetic particle sensors on the current GOES spacecraft | Terry Onsager/NOAA |
| 09:30 | Overview of the impact of the space environment on space systems | Joe Mazur/The Aerospace Corporation |
| Energetic particle measurement requirements |
| 10:00 | 3rd generation GOES spacecraft program: billions of dollars…GOES energetic particle measurements for support of manned spaceflight: priceless | Mike Golightly/NASA Johnson Space Center |
| 10:30 | Break |  |
| 11:00 | The charged particle environment from a spacecraft designer's perspective | Kyle Miller/Mission Research Corporation |
| 11:20 | What do satellite manufacturers want from GOES? | Mike Bodeau/Boeing |
| 11:40 | On-orbit space systems users requirements for GOES energetic particle data: a perspective from Lockheed Martin | Dave Chenette/Lockheed Martin Advanced Technology Center |
| 12:00 | Lunch |  |
| 13:00 | SEP measurements required for environment models and system design and testing | Mike Xapsos/Mike Jones/NASA Goddard Space Flight Center |
| 13:20 | European Space Agency interests in GOES energetic particle measurements | Eammon Daly/European Space Agency |
| 13:40 | LANL perspectives on space environment monitoring | Tom Carey/Los Alamos National Laboratory |
| 14:00 | Air Force requirements for energetic particle measurements | Maj. Pete Engelman/USAF |
| 14:20 | Air Force Research Laboratory perspective on energetic particle measurements | Steve Kahler/Air Force Research Laboratory |
| 14:40 | Proposed space environmental effects on satellite operations (SEESO) product | Stephan Quigley/Air Force Research Laboratory |
| 15:00 | Break |  |
| 15:30 | Let's not forget surface charging | Joe Fennell/ The Aerospace Corporation |
| 15:50 | The case for low-energy electrons | Myron Mandell/ Science Applications International Corporation |
| 16:10 | General discussion | All |
| 17:00 | Adjourn |  |
| Tuesday, October 29, 2002 |
| Interagency coordination and research perspective |
| 09:00 | Geospace and NASA's Living With a Star program | Dave Sibeck/ NASA Goddard Space Flight Center |
| 09:20 | Space Environment Sensor Suite for NPOESS | Pat Bornmann/ Ball Aerospace and Technologies Corporation |
| 09:40 | Measurements needed to improve forecast and specification of energetic electrons | Xinlin Li/ University of Colorado Laboratory for Atmospheric and Space Physics |
| 10:00 | General discussion of priorities for energetic particle measurements including: 1. Needs and requirements for heavy ion measurements (species, energy ranges, mass resolution, etc.) 2. Needs and requirements for low-energy electron measurements. 3. Additional modifications that could enhance the value of the energetic particle data. 4. Existing technologies that can make these measurements at reasonable cost. | All |
| 12:00 | Adjourn |  |