# Appendix 3

# (Supplemental Materials to Chapter 3)

## Non-EGU and Area Source Controls applied in the baseline and control scenarios

3.1.1 Non-EGU and Area Source Control Strategies for Ozone NAAQS Proposal

In the Non-EGU and Area Sources portion of the control strategy, maximum control scenarios were used from the existing control measure dataset from AirControlNET 4.1 for 2020 (for Geographic Areas defined for each level of the standard being analyzed).  This existing control measure dataset reflects changes and updates made as a result of the reviews performed for the final PM2.5 RIA.  Following this, an internal review was performed by the OAQPS engineers in the Sector Policies and Programs Division (SPPD) to examine the controls applied by AirControlNET and decide if these controls were sufficient or could be more aggressive in their application, given the 2020 analysis year.  This review was performed for non-EGU NOx control measures.  The result of this review was an increase in control efficiencies applied for many control measures, and more aggressive control measures for over 80 SCC’s.   For example, SPPD recommended that we apply SCR to cement kilns to reduce NOx emissions in 2020.  Currently, there are no SCRs in operation at cement kilns in the U.S, but there are several SCRs in operation at cement kilns in France now.  Based on the SCR experience at cement kilns in France, SPPD believes SCR could be applied at U.S. cement kilns by 2020.  Following this, it was recommended that supplemental controls could be applied to 8 additional SCC’s from non-EGU NOx sources.  We also looked into sources of controls for highly reactive VOC non-EGU sources.  Four additional controls were applied for highly reactive VOC non-EGU sources not in AirControlNET.

3.1.2 NOx Control Measures for Non-EGU Point Sources.

Several types of NOx control technologies exist for non-EGU sources: SCR, selective noncatalytic reduction (SNCR), natural gas reburn (NGR), coal reburn, and low-NOx burners. In some cases, LNB accompanied by flue gas recirculation (FGR) is applicable, such as when fuel-borne NOx emissions are expected to be of greater importance than thermal NOx emissions. When circumstances suggest that combustion controls do not make sense as a control technology (e.g., sintering processes, coke oven batteries, sulfur recovery plants), SNCR or SCR may be an appropriate choice. Finally, SCR can be applied along with a combustion control such as LNB with overfire air (OFA) to further reduce NOx emissions. All of these control measures are available for application on industrial boilers.

Besides industrial boilers, other non-EGU source categories covered in this RIA include petroleum refineries, kraft pulp mills, cement kilns, stationary internal combustion engines, glass manufacturing, combustion turbines, and incinerators. NOx control measures available for petroleum refineries, particularly process heaters at these plants, include LNB, SNCR, FGR, and SCR along with combinations of these technologies. NOx control measures available for kraft pulp mills include those available to industrial boilers, namely LNB, SCR, SNCR, along with water injection (WI). NOx control measures available for cement kilns include those available to industrial boilers, namely LNB, SCR, and SNCR. Non-selective catalytic reduction (NSCR) can be used on stationary internal combustion engines. OXY-firing, a technique to modify combustion at glass manufacturing plants, can be used to reduce NOx at such plants. LNB, SCR, and SCR + steam injection (SI) are available measures for combustion turbines. Finally, SNCR is an available control technology at incinerators. For more information on these measures, please refer to the AirControlNET 4.1 control measures documentation report.

3.1.3 VOC Control Measures for Non-EGU Point Sources.

VOC controls were applied to a variety of non-EGU point sources as defined in the emissions inventory in this RIA.  These controls are:  permanent total enclosure (PTE) applied to paper and web coating operations and fabric operations, and incinerators or thermal oxidizers applied to wood products and marine surface coating operations.  A PTE confines VOC emissions to a particular area where can be destroyed or used in a way that limits emissions to the outside atmosphere, and an incinerator or thermal oxidizer destroys VOC emissions through exposure to high temperatures (2,000 degrees Fahrenheit or higher).  For more information on these measures, refer to the AirControlNET 4.1 control measures documentation report.

3.1.4  NOx Control Measures for Area Sources.

There were two controls applied for NOx emissions from area sources.  The first is RACT (reasonably available control technology) to 25 tpy (LNB).  This control is the addition of a low NOx burner to reduce NOx emissions.  This control is applied to industrial oil, natural gas, and coal combustion sources.  The second control is water heaters plus LNB space heaters.  This control is based on the installation of low-NOx space heaters and water heaters in commercial and institutional sources for the reduction of NOx emissions.  For additional information regarding these controls please refer to the AirControlNET 4.1 control measures documentation report.

3.1.5 VOC Control Measures for Area Sources.

The most frequently applied control to reduce VOC emissions from area sources was CARB Long-Term Limits.  This control, which represents controls available in VOC rules promulgated by the California Air Resources Board, applies to commercial solvents and commercial adhesives, and depends on future technological innovation and market incentive methods to achieve emission reductions.  The next most frequently applied controls was the use of low or no VOC materials for graphic art source categories.  The South Coast Air District’s SCAQMD Rule 1168 control applies to wood furniture and solvent source categories sets limits for adhesive and sealant VOC content.  The OTC solvent cleaning rule control establishes hardware and operating requirements for specified vapor cleaning machines, as well as solvent volatility limits and operating practices for cold cleaners.  The Low Pressure/Vacuum Relief Valve control measure is the addition of low pressure/vacuum (LP/V) relief valves to gasoline storage tanks at service stations with Stage II control systems. LP/V relief valves prevent breathing emissions from gasoline storage tank vent pipes.  SCAQMD Limits control establishes VOC content limits for metal coatings along with application procedures and equipment requirements. Switch to Emulsified Asphalts control is a generic control measure replacing VOC-containing cutback asphalt with VOC-free emulsified asphalt.   The equipment and maintenance control measure applies to oil and natural gas production.  The Reformulation - FIP Rule control measure intends to reach the VOC limits by switching to and/or encouraging the use of low-VOC pesticides and better Integrated Pest Management (IPM) practices.  For additional information regarding these controls please refer to the AirControlNET 4.1 control measures documentation report.

3.1.6  Supplemental Controls

The table below summarizes the supplemental control measures added to our control measures database by providing the pollutant it controls and its control efficiency.  These controls were applied in the baseline scenario to Houston and Chicago, and the Northeast as well as in the incremental control strategy applied to the Eastern U.S..  However, these controls are not located in AirControlNET.

Supplemental Emission Control Measures Applied in Modeled Attainment Strategies for the Ozone NAAQS RIA – New Control Technologies Added to the Control Measures Database

| Pollutant | SCC | SCC Description | Control Technology | Percent Reduction (%) |
| --- | --- | --- | --- | --- |
| NOx | 20200252 | Internal Comb. Engines/Industrial/Natural Gas/2-cycle Lean Burn | LEC (Low Emission Combustion) | 87 |
|  | 20200254 | Internal Comb. Engines/Industrial/Natural Gas/4-cycle Lean Burn | LEC (Low Emission Combustion) | 87 |
| VOC* | 3018001- 30600701 and 30600999 - | Fugitive Leaks Flares | Enhanced LDAR | 50 98 |
|  | 3018001 - | Fugitive Leaks | LDAR | 80 |
|  | 30600702- | Cooling towers | Monitoring Program | No one general estimate |
|  | 30600503- | Wastewater Drains and Separators | Inspection and Maintenance Program (Separators) Water Seals (Drains) | 65 |

*Note:  the cost of these measures are not included in our incremental annualized cost estimates since these controls are found in the Harris-Galveston-Brazoria Cos. SIP (Texas), and they will be incurred by 2020 in any event.  We do quantify the emission reductions since these controls are not accounted for in our baseline inventory for 2020, however.

Low Emission Combustion (LEC)

Overview:  LEC technology is defined as the modification of a natural gas fueled, spark ignited, reciprocating internal combustion engine to reduce emissions of NOx by utilizing ultra-lean air-fuel ratios, high energy ignition systems and/or pre-combustion chambers, increased turbocharging or adding a turbocharger, and increased cooling and/or adding an intercooler or aftercooler, resulting in an engine that is designed to achieve a consistent NOx emission rate of not more than 1.5-3.0 g/bhp-hr at full capacity (usually 100 percent speed and 100 percent load). This type of retrofit technology is fairly widely available for stationary internal combustion engines.

For control efficiency, EPA estimates that it ranges from 82 to 91 percent for LEC technology applications.  The EPA believes application of LEC would achieve average NOx emission levels in the range of 1.5-3.0 g/bhp-hr.  This is an 82-91 percent reduction from the average uncontrolled emission levels reported in the ACT document.  An EPA memorandum summarizing 269 tests shows that 96 percent of IC engines with installed LEC technology achieved emission rates of less than 2.0 g/bhp-hr.  The 2000 EC/R report on IC engines summarizes 476 tests and shows that 97% of the IC engines with installed LEC technology achieve emission rates of 2.0 g/bhp-hr or less.

Major Uncertainties:  The EPA acknowledges that specific values will vary from engine to engine.  The amount of control desired and number of operating hours will make a difference in terms of the impact had from a LEC retrofit.  Also, the use of LEC may yield improved fuel economy and power output, both of which may affect the emissions generated by the device.

Leak Detection and Repair (LDAR) for Fugitive Leaks

Overview:  This control measure is a program to reduce leaks of fugitive VOC emissions from chemical plants and refineries.  The program includes special “sniffer” equipment to detect leaks, and maintenance schedules that affected facilities are to adhere to. This program is one that is contained within the Houston-Galveston-Brazoria 8-hour Ozone SIP.

Major Uncertainties:  The degree of leakage from pipes and processes at chemical plants is always difficult to quantify given the large number of such leaks at a typical chemical manufacturing plant.  There are also growing indications based on tests conducted by TCEQ and others in Harris County, Texas that fugitive leaks have been underestimated from chemical plants by a factor of 6 to 20 or greater.

Enhanced LDAR for Fugitive Leaks

Overview:  This control measure is a more stringent program to reduce leaks of fugitive VOC emissions from chemical plants and refineries that presumes that an existing LDAR program already is in operation.

Major Uncertainties:  The calculations of control efficiency and cost presume use of LDAR at a chemical plant.  This should not be an unreasonable assumption, however, given that most chemical plants are under some type of requirement to have an LDAR program.  However, as mentioned earlier, there is growing evidence that fugitive leak emissions are underestimated from chemical plants by a factor of 6 to 20 or greater.

Flare Gas Recovery

Overview:  This control measure is a condenser that can recover 98 percent of the VOC emitted by flares that emit 20 tons per year or more of the pollutant.

Major Uncertainties: Flare gas recovery is just gaining commercial acceptance in the US and is only in use at a small number of refineries.

Cooling Towers

Overview:  The control measure is continuous monitoring of VOC from the cooling water return to a level of 10 ppb.  This monitoring is accomplished by using a continuous flow monitor at the inlet to each cooling tower.

There is not a general estimate of control efficiency for this measure; one is to apply a continuous flow monitor until VOC emissions have reached a level of 1.7 tons/year for a given cooling tower.

Major Uncertainties:  The amount of VOC leakage from each cooling tower can greatly affect the overall cost-effectiveness of this control measure.

Wastewater Drains and Separators

Overview:   This control measure includes an inspection and maintenance program to reduce VOC emissions from wastewater drains and water seals on drains.  This measure is a more stringent version of measures that underlie existing NESHAP requirements for such sources.

Major Uncertainties:  The reference for this control measures notes that the VOC emissions inventories for the five San Francisco Bay Area refineries whose data was a centerpiece of this report are incomplete.  In addition, not all VOC species from these sources were included in the VOC data that is a basis for these calculations.

In addition to the new supplemental controls presented above, there were a number of changes made to existing AirControlNET controls.  These changes were made based upon an internal review performed by EPA engineers to examine the controls applied by AirControlNET and determine if these controls were sufficient or could be more aggressive in their application, given the 2020 analysis year.  This review was performed for non-EGU NOx control measures.  The result of this review was an increase in control efficiencies applied for many control measures, and more aggressive control measures for over 70 SCCs.  The changes apply to the control strategies performed for the Eastern US only.  These changes are listed in the table below.

Supplemental Emission Control Measures Applied in Modeled Attainment Strategies for the Ozone NAAQS RIA – Changes to Control technologies currently in our Control Measures Database

| Pollutant | SCC | AirControlNET Source Description | AirControlNET Control Technology | New Control Technology | New Control Efficiency (%) |
| --- | --- | --- | --- | --- | --- |
| NOX | 10200104 10200204 10200205 10300207 10300209 10200217 10300216 | ICI Boilers - Coal-Stoker | SNCR | SCR | 90.0 |
| NOX | 10200901 10200902 10200903 10200907 10300902 10300903 | ICI Boilers - Wood/Bark/ Waste | SNCR | SCR | 90.0 |
| NOX | 10200401 10200402 10200404 10200405 10300401 | ICI Boilers - Residual Oil | SCR | SCR | 90.0 |
| NOX | 10200501 10200502 10200504 | ICI Boilers - Distillate Oil | SCR | SCR | 90.0 |
| NOX | 10200601 10200602 10200603 10200604 10300601 10300602 10300603 10500106 10500206 | ICI Boilers - Natural Gas | SCR | SCR | 90.0 |
| NOX | 30500606 | Cement Manufacturing - Dry | SCR | SCR | 90.0 |
| NOX | 30500706 | Cement Manufacturing - Wet | SCR | SCR | 90.0 |
| NOX | 30300934 | Iron & Steel Mills - Annealing | SCR | SCR | 90.0 |
| NOX | 10200701 10200704 10200707 10200710 10200799 10201402 10300701 10300799 | ICI Boilers - Process Gas | SCR | SCR | 90.0 |
| NOX | 10200802 10200804 | ICI Boilers - Coke | SCR | SCR | 90.0 |
| NOX | 10201002 | ICI Boilers - LPG | SCR | SCR | 90.0 |
| NOX | 10201301 10201302 | ICI Boilers - Liquid Waste | SCR | SCR | 90.0 |
| NOX | 30700110 | Sulfate Pulping - Recovery Furnaces | SCR | SCR | 90.0 |
| NOX | 30100306 | Ammonia Production – Pri. Reformer, Nat. Gas | SCR | SCR | 90.0 |
|  | 30500622 30500623 | Cement Kilns | Biosolid Injection | Biosolid Injection | 40.0 |
| NOX | 30590013 30190013 30190014 39990013 | Industrial and Manufacturing Incinerators | SNCR | SCR | 90.0 |
| NOX | 30101301 30101302 | Nitric Acid Manufacturing | SNCR | SCR | 90.0 |
| NOX | 30600201 | Fluid Cat. Cracking Units | LNB + FGR | SCR | 90.0 |
| NOX | 30590003 | Process Heaters - Process Gas | LNB + SCR | LNB + SCR | 90.0 |
| NOX | 30600101 30600103 30600111 | Process Heaters - Distillate Oil | LNB + SCR | LNB + SCR | 90.0 |
| NOX | 30600106 30600199 | Process Heaters - Residual Oil | LNB + SCR | LNB + SCR | 90.0 |
| NOX | 30600102 30600105 | Process Heaters - Natural Gas | LNB + SCR | LNB + SCR | 90.0 |
| NOX | 30700104 | Sulfate Pulping - Recovery Furnaces | SCR | SCR | 90.0 |
| NOX | 30790013 | Pulp and Paper - Natural Gas - Incinerators | SNCR | SCR | 90.0 |
| NOX | 39000201 | In-Process; Bituminous Coal; Cement Kiln | SNCR - urea based | SCR | 90.0 |
| NOX | 39000203 | In-Process; Bituminous Coal; Lime Kiln | SNCR - urea based | SCR | 90.0 |
| NOX | 39000289 | In-Process Fuel Use;Bituminous Coal; Gen | SNCR | SCR | 90.0 |
| NOX | 39000489 | In-Process Fuel Use; Residual Oil; Gen | LNB | SCR | 90.0 |
| NOX | 39000689 | In-Process Fuel Use; Natural Gas; Gen | LNB | SCR | 90.0 |
| NOX | 39000701 | In-Proc;Process Gas;Coke Oven/Blast Furn | LNB + FGR | SCR | 90.0 |
| NOX | 39000789 | In-Process; Process Gas; Coke Oven Gas | LNB | SCR | 90.0 |
| NOX | 50100101 50100506 50200506 50300101 50300102 50300104 50300506 50100102 | Solid Waste Disp;Gov;Other Incin;Sludge | SNCR | SCR | 90.0 |

The last category of supplemental controls are control technologies currently in our control measures database being applied to SCCs not controlled currently in AirControlNET.

Supplemental Emission Control Measures Applied in Modeled Attainment Strategies for the Ozone NAAQS RIA –Control technologies currently in our Control Measures Database Applied to New Source types

| Pollutant | SCC | SCC Description | Control Technology | Control Efficiency |
| --- | --- | --- | --- | --- |
| NOX | 39000602 | Cement Manufacturing - Dry | SCR | 90.0 |
| NOX | 30501401 | Glass Manufacturing - General | OXY-Firing | 85.0 |
| NOX | 30302351 30302352 30302359 | Taconite Iron Ore Processing - Induration - Coal or Gas | SCR | 90.0 |
| NOX | 10100101 | External Combustion Boilers;Electric Generation;Anthracite Coal;Pulverized Coal | SNCR | 40.0 |
| NOX | 10100202 | External Combustion Boilers;Electric Generation;Bituminous/Subbituminous Coal;Pulverized Coal: Dry Bottom (Bituminous Coal) | SNCR | 40.0 |
| NOX | 10100204 | External Combustion Boilers;Electric Generation;Bituminous/Subbituminous Coal;Spreader Stoker (Bituminous Coal) | SNCR | 40.0 |
| NOX | 10100212 | External Combustion Boilers;Electric Generation;Bituminous/Subbituminous Coal;Pulverized Coal: Dry Bottom (Tangential) (Bituminous Coal) | SNCR | 40.0 |
| NOX | 10100401 | External Combustion Boilers;Electric Generation;Residual Oil;Grade 6 Oil: Normal Firing | SNCR | 50.0 |
| NOX | 10100404 | External Combustion Boilers;Electric Generation;Residual Oil;Grade 6 Oil: Tangential Firing | SNCR | 50.0 |
| NOX | 10100501 | External Combustion Boilers;Electric Generation;Distillate Oil;Grades 1 and 2 Oil | SNCR | 50.0 |
| NOX | 10100601 | External Combustion Boilers;Electric Generation;Natural Gas;Boilers > 100 Million Btu/hr except Tangential | NGR | 50.0 |
| NOX | 10100602 | External Combustion Boilers;Electric Generation;Natural Gas;Boilers < 100 Million Btu/hr except Tangential | NGR | 50.0 |
| NOX | 10100604 | External Combustion Boilers;Electric Generation;Natural Gas;Tangentially Fired Units | NGR | 50.0 |
| NOX | 10101202 | External Combustion Boilers;Electric Generation;Solid Waste;Refuse Derived Fuel | SNCR | 50.0 |
| NOX | 20200253 | Internal Comb. Engines/Industrial/Natural Gas/4-cycle Rich Burn | NSCR | 90 |

## Mobile Controls/Rules used in baseline and control scenarios

3.2.1 Diesel Retrofits and Vehicle Replacement

Retrofitting heavy-duty diesel vehicles and equipment manufactured before stricter standards are in place – in 2007-2010 for highway engines and in 2011-2014 for most nonroad equipment – can provide NOX and HC benefits.  The retrofit strategies included in the RIA retrofit measure are:

- Installation of emissions after-treatment devices called selective catalytic reduction (“SCRs”)

- Rebuilding nonroad engines (“rebuild/upgrade kit”)

We chose to focus on these strategies due to their high NOx emissions reduction potential and widespread application.  Additional retrofit strategies include, but are not limited to, lean NOx catalyst systems – which are another type of after-treatment device – and alternative fuels.  Additionally, SCRs are currently the most likely type of control technology to be used to meet EPA’s NOx 2007-2010 requirements for HD diesel trucks and 2008-2011 requirements for nonroad equipment. We looked at options of applying this measure to 50% and 100% of the fleet that do not meet EPA’s more stringent standards and are still expected to be operating in 2020. Actual emissions reductions may vary significantly by strategy and by the type and age of the engine and its application.

To estimate the potential emissions reductions from this measure, we applied a mix of two retrofit strategies (SCRs and rebuild/upgrade kits) for the 2020 inventory of:

- Heavy-duty highway trucks class 6 & above, Model Year 1995-2009

- All diesel nonroad engines, Model Year 1991-2007, except for locomotive, marine, pleasure craft, & aircraft engines

Class 6 and above trucks comprise the bulk of the NOx emissions inventory from heavy-duty highway vehicles, so we did not include trucks below class 6. We chose not to include locomotive and marine engines in our analysis since EPA has proposed regulations to address these engines, which will significantly impact the emissions inventory and emission reduction potential from retrofits in 2020.  There was also not enough data available to assess retrofit strategies for existing aircraft and pleasure craft engines, so we did not include them in this analysis.  In addition, EPA is in the process of negotiating standards for new aircraft engines.

The lower bound in the model year range – 1995 for highway vehicles and 1991 for nonroad engines – reflects the first model year in which emissions after-treatment devices can be reliably applied to the engines.  Due to a variety of factors, devices are at a higher risk of failure for earlier model years.  We expect the engines manufactured before the lower bound year that are still in existence in 2020 to be retired quickly due to natural turnover, therefore, we have not included strategies for pre-1995/1991 engines because of the strategies’ relatively small impact on emissions. The upper bound in the model year range reflects the last year before more stringent emissions standards will be fully phased-in.

We chose the type of strategy to apply to each model year of highway vehicles and nonroad equipment based on our technical assessment of which strategies would achieve reliable results at the lowest cost.  After-treatment devices can be more cost-effective than rebuild and vice versa depending on the emissions rate, application, usage rates, and expected life of the engine.  The performance of after-treatment devices, for example, depends heavily upon the model year of the engine; some older engines may not be suitable for after-treatment devices and would be better candidates for rebuild/upgrade kit.  In certain cases, nonroad engines may not be suitable for either after-treatment devices or rebuild, which is why we estimate that retrofits are not suitable for 5% of the nonroad fleet.  The mix of strategies employed in this RIA for highway vehicles and nonroad engines are presented in Table 1 and Table 2, respectively.  The groupings of model years for highway vehicles reflect changes in EPA’s published emissions standards for new engines.

Table 1: Application of Retrofit Strategy for Highway Vehicles by Percentage of Fleet

| Model Year | SCR |
| --- | --- |
| <1995 | 0% |
| 1995-2006 | 100% |
| 2007-2009 | 50% |
| >2009 | 0% |

Table 2: Application of Retrofit Strategy for Nonroad Equipment by Percentage of Fleet

| Model Year | Rebuild/Upgrade kit | SCR |
| --- | --- | --- |
| 1991-2007 | 50% | 50% |

The expected emissions reductions from SCR’s are based on data derived from EPA regulations (Control of Emissions of Air Pollution from 2004 and Later Model Year Heavy-duty Highway Engines and Vehicles published October 2000), interviews with component manufacturers, and EPA’s Summary of Potential Retrofit Technologies available at www.epa.gov/otaq/retrofit/retropotentialtech.htm.  The estimates for highway vehicles and nonroad engines are presented in Table 3 and Table 4, respectively.

Table 3: Percentage Emissions Reduction by Highway Vehicle Retrofit Strategy

|  | PM | CO | HC | NOx |
| --- | --- | --- | --- | --- |
| SCR (+DPF) | 90% | 90% | 90% | 70% |

Table 4: Percentage Emissions Reduction by Nonroad Equipment Retrofit Strategy

| Strategy | PM | CO | HC | NOx |
| --- | --- | --- | --- | --- |
| SCR (+DPF) | 90% | 90% | 90% | 70% |
| Rebuild/Upgrade Kit | 30% | 15% | 70% | 40% |

It is important to note that there is a great deal of variability among types of engines (especially nonroad), the applicability of retrofit strategies, and the associated emissions reductions.  We applied the retrofit emissions reduction estimates to engines across the board (e.g. retrofits for bulldozers are estimated to produce the same percentage reduction in emissions as for agricultural mowers).  We did this in order to simplify model runs, and, in some cases, where we did not have enough data to differentiate emissions reductions for different types of highway vehicles and nonroad equipment.  We believe the estimates used in the RIA, however, reflect the best available estimates of emissions reductions that can be expected from retrofitting the heavy-duty diesel fleet.

Using the retrofit module in EPA’s National Mobile Inventory Model (NMIM) available at http://www.epa.gov/otaq/nmim.htm, we calculated the total percentage reduction in emissions (PM, NOx, HC, and CO) from the retrofit measure for each relevant engine category (source category code, or SCC) for each  county in 2020. To evaluate this change in the emissions inventory, we conducted both a baseline and control analysis.  Both analyses were based on NMIM 2005 (version NMIM20060310), NONROAD2005 (February 2006), and MOBILE6.2.03 which included the updated diesel PM file PMDZML.csv dated March 17, 2006.

For the control analysis, we applied the retrofit measure corresponding to the percent reductions of the specified pollutants in Tables 3 and 4 to the specified model years in Tables 1 and 2 of the relevant SCCs.  Fleet turnover rates are modeled in the NMIM, so we applied the retrofit measure to the 2007 fleet inventory, and then evaluated the resulting emissions inventory in 2020. The timing of the application of the retrofit measure is not a factor; retrofits only need to take place prior to the attainment date target (2020 for this RIA).  For example, if retrofit devices are installed on 1995 model year bulldozers in 2007, the only impact on emissions in 2020 will be from the expected inventory of 1995 model year bulldozer emissions in 2020.

We then compared the baseline and control analyses to determine the percent reduction in emissions we estimate from this measure for the relevant SCC codes in the targeted nonattainment areas.

Pollutants and Source Categories Affected by Measure (SCC)

NOx, and HC

###### 3.3.2 Implement Continuous Inspection and Maintenance Using Remote Onboard Diagnostics (OBD)

Continuous Inspection and Maintenance (I/M) is a new way to check the status of OBD systems on OBD-equipped vehicles.  It involves equipping subject vehicles with some type of transmitter that attaches to the OBD port.  The device transmits the status of the OBD system to receivers distributed around the I/M area.  Transmission may be through radio-frequency, cellular or wi-fi means.  Radio frequency and cellular technologies are currently being used in the states of Oregon, California and Maryland.

Current I/M programs test vehicles on a periodic basis – either annually or biennially.  Emission reduction credit is assigned based on test frequency.  Using Continuous I/M, vehicles are continuously monitored as they are operated throughout the non-attainment area.  When a vehicle experiences an OBD failure, the motorist is notified and is required to get repairs within the normal grace period – typically about a month.  Thus, Continuous I/M will result in repairs happening essentially whenever a malfunction occurs that would cause the check engine light to illuminate.  Currently, MOBILE6 provides an increment of benefit when going from a biennial program to an annual program.  The same increment of credit applies going from an annual program to a continuous program.

Pollutants and Source Categories Affected by Measure (SCC):

- All 1996 and newer light-duty gasoline vehicles and trucks:

- All 1996 and newer 2201001000 Light Duty Gasoline Vehicles (LDGV), Total: All Road Types

- All 1996 and newer 2201020000 Light Duty Gasoline Trucks 1 (LDGT1), Total: All Road Types

- All 1996 and newer 2201040000 Light Duty Gasoline Trucks 2 (LDGT2), Total: All Road Types

OBD systems on light duty vehicles are required to illuminate the malfunction indicator lamp whenever emissions of HC, CO or NOx would exceed 1.5 times the vehicle’s certification standard.  Thus, the benefits of this measure will affect all three criteria pollutants.  MOBILE6 was used to estimate the emission reduction benefits of Continuous I/M, using the methodology discussed above.

3.2.3 Eliminating Long Duration Truck Idling

Virtually all long duration truck idling – idling that lasts for longer than 15 minutes – from heavy-duty diesel class 8a and 8b trucks can be eliminated with two strategies:

- truck stop & terminal electrification (TSE)

- mobile idle reduction technologies (MIRTs) such as auxiliary power units, generator sets, and direct-fired heaters

TSE can eliminate idling when trucks are resting at truck stops or public rest areas and while trucks are waiting to perform a task at private distribution terminals.  When truck spaces are electrified, truck drivers can shut down their engines and use electricity to power equipment which supplies air conditioning, heat, and electrical power for on-board appliances.

MIRTs can eliminate long duration idling from trucks that are stopped away from these central sites.  For a more complete list of MIRTs see EPA’s Idle Reduction Technology page at http://www.epa.gov/otaq/smartway/idlingtechnologies.htm.

This measure demonstrates the potential emissions reductions if every class 8a and 8b truck is equipped with a MIRT or has dependable access to sites with TSE in 2020.

To estimate the potential emissions reduction from this measure, we applied a reduction equal to the full amount of the emissions attributed to long duration idling in the MOBILE model, which is estimated to be 3.4% of the total NOx emissions from class 8a and 8b heavy duty diesel trucks.  Since the MOBILE model does not distinguish between idling and operating emissions, EPA estimates idling emissions in the inventory based on fuel conversion factors.  The inventory in the MOBILE model, however, does not fully capture long duration idling emissions.  There is evidence that idling may represent a much greater share than 3.4% of the real world inventory, based on engine control module data from long haul trucking companies.  As such, we believe the emissions reductions demonstrated from this measure in the RIA represent ambitious but realistic targets. For more information on determining baseline idling activity see EPA’s "Guidance for Quantifying and Using Long-Duration Truck Idling Emission Reductions in State Implementation Plans and Transportation Conformity” available at http://www.epa.gov/smartway/idle-guid.htm.

Pollutants and Source Categories Affected by Measure (SCC) : NOx

All class 8a and 8b heavy duty diesel trucks (decrease NOx for all SCCs):

| SCC | Note: All SCC Descriptions below begin with "Mobile Sources; Highway Vehicles - Diesel;" |
| --- | --- |
| 2230074110 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Interstate: Total |
| 2230074130 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Other Principal Arterial: Total |
| 2230074150 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Minor Arterial: Total |
| 2230074170 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Major Collector: Total |
| 2230074190 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Minor Collector: Total |
| 2230074210 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Rural Local: Total |
| 2230074230 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Interstate: Total |
| 2230074250 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Other Freeways and Expressways: Total |
| 2230074270 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Other Principal Arterial: Total |
| 2230074290 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Minor Arterial: Total |
| 2230074310 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Collector: Total |
| 2230074330 | Heavy Duty Diesel Vehicles (HDDV) Class 8A & 8B;Urban Local: Total |

Estimated Emissions Reduction from Measure (%): 3.4 % decrease in NOx for all SCCs affected by measure

3.2.4 Commuter Programs

Commuter programs recognize and support employers who provide incentives to employees to reduce light-duty vehicle emissions.  Employers implement a wide range of incentives to affect change in employee commuting habits including transit subsidies, bike-friendly facilities, telecommuting policies, and preferred parking for vanpools and carpools.  The commuter measure in this RIA reflects a mixed package of incentives.

This measure demonstrates the potential emissions reductions from providing commuter incentives to 10% and 25% of the commuter population in 2020.

We used the findings from a recent Best Workplaces for Commuters survey, which was an EPA sponsored employee trip reduction program, to estimate the potential emissions reductions from this measure.  The BWC survey found that, on average, employees at workplaces with comprehensive commuter programs emit 15% fewer emissions than employees at workplaces that do not offer a comprehensive commuter program.

We believe that getting 10-25% of the workforce involved in commuter programs is realistic. For modeling purposes, we divided the commuter programs measure into two program penetration rates: 10% and 25%.  This was meant to provide flexibility to model a lower penetration rate for areas that need only low levels of emissions reductions to achieve attainment.

According to the 2001 National Household Transportation Survey (NHTS) published by DOT, commute VMT represents 27% of total VMT.  Based on this information, we calculated that BWC would reduce light-duty gasoline emissions by 0.4% and 1% with a 10% and 25% program penetration rate, respectively.

Pollutants and Source Categories Affected by Measure (SCC): NOx, and VOC

All light-duty gasoline vehicles and trucks:

| SCC | Note: All SCC Descriptions below begin with "Mobile Sources; Highway Vehicles - Gasoline;" |
| --- | --- |
| 2201001110 | Light Duty Gasoline Vehicles (LDGV);Rural Interstate: Total |
| 2201001130 | Light Duty Gasoline Vehicles (LDGV);Rural Other Principal Arterial: Total |
| 2201001150 | Light Duty Gasoline Vehicles (LDGV);Rural Minor Arterial: Total |
| 2201001170 | Light Duty Gasoline Vehicles (LDGV);Rural Major Collector: Total |
| 2201001190 | Light Duty Gasoline Vehicles (LDGV);Rural Minor Collector: Total |
| 2201001210 | Light Duty Gasoline Vehicles (LDGV);Rural Local: Total |
| 2201001230 | Light Duty Gasoline Vehicles (LDGV);Urban Interstate: Total |
| 2201001250 | Light Duty Gasoline Vehicles (LDGV);Urban Other Freeways and Expressways: Total |
| 2201001270 | Light Duty Gasoline Vehicles (LDGV);Urban Other Principal Arterial: Total |
| 2201001290 | Light Duty Gasoline Vehicles (LDGV);Urban Minor Arterial: Total |
| 2201001310 | Light Duty Gasoline Vehicles (LDGV);Urban Collector: Total |
| 2201001330 | Light Duty Gasoline Vehicles (LDGV);Urban Local: Total |
| 2201020110 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Interstate: Total |
| 2201020130 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Other Principal Arterial: Total |
| 2201020150 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Minor Arterial: Total |
| 2201020170 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Major Collector: Total |
| 2201020190 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Minor Collector: Total |
| 2201020210 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Rural Local: Total |
| 2201020230 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Interstate: Total |
| 2201020250 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Other Freeways and Expressways: Total |
| 2201020270 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Other Principal Arterial: Total |
| 2201020290 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Minor Arterial: Total |
| 2201020310 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Collector: Total |
| 2201020330 | Light Duty Gasoline Trucks 1 & 2 (M6) = LDGT1 (M5);Urban Local: Total |
| 2201040110 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Interstate: Total |
| 2201040130 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Other Principal Arterial: Total |
| 2201040150 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Minor Arterial: Total |
| 2201040170 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Major Collector: Total |
| 2201040190 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Minor Collector: Total |
| 2201040210 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Rural Local: Total |
| 2201040230 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Interstate: Total |
| 2201040250 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Other Freeways and Expressways: Total |
| 2201040270 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Other Principal Arterial: Total |
| 2201040290 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Minor Arterial: Total |
| 2201040310 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Collector: Total |
| 2201040330 | Light Duty Gasoline Trucks 3 & 4 (M6) = LDGT2 (M5);Urban Local: Total |

Estimated Emissions Reduction from Measure (%):

With a 10% program penetration rate:	0.4%

With a 25% program penetration rate:	1%

###### 3.2.5 Reduce Gasoline RVP from 7.8 to 7.0 in Remaining Nonattainment Areas

Volatility is the property of a liquid fuel that defines its evaporation characteristics.  RVP is an abbreviation for "Reid vapor pressure," a common measure of gasoline volatility, as well as a generic term for gasoline volatility.  EPA regulates the vapor pressure of all gasoline during the summer months (June 1 to September 15 at retail stations).  Lower RVP helps to reduce VOCs, which are a precursor to ozone formation. This control measure represents the use of gasoline with a RVP limit of 7.0 psi from May through September in counties with an ozone season RVP value greater than 7.0 psi.

Under section 211(c)(4)(C) of the CAA, EPA may approve a non-identical state fuel control as a SIP provision, if the state demonstrates that the measure is necessary to achieve the national primary or secondary ambient air quality standard (NAAQS) that the plan implements. EPA can approve a state fuel requirement as necessary only if no other measures would bring about timely attainment, or if other measures exist but are unreasonable or impracticable.

Pollutants and Source Categories Affected by Measure (SCC):

- All light-duty gasoline vehicles and trucks: Affected SCC:

- 2201001000 Light Duty Gasoline Vehicles (LDGV), Total: All Road Types

- 2201020000 Light Duty Gasoline Trucks 1 (LDGT1), Total: All Road Types

- 2201040000 Light Duty Gasoline Trucks 2 (LDGT2), Total: All Road Types

- 2201070000 Heavy Duty Gasoline Vehicles (HDGV), Total: All Road Types

- 2201080000 Motorcycles (MC), Total: All Road Types

3.2.6 Application order for Onroad and Nonroad Mobile Controls

Application order- 0.084 Mobile

- Eliminate Long Duration Idling

- ONRetrofit

- LOWRVP

- Best Workplaces for Commuters

Application order- 0.084 Nonroad

- Diesel C1&C2 Marine/Diesel C3 Marine - 90% Rule (adding controls for SCCs for residual fuel)

- ICAO Engine NOx Standards for Commercial Aircraft

- NRRetrofit

- LOWRVP

Application order- 0.070 Mobile

- Eliminate Long Duration Idling

- Inspection and Maintenance

- ONRetrofit

- LOWRVP

- Best Workplaces for Commuters

Application order – 0.070  Nonroad

- Diesel C1&C2 Marine/Diesel C3 Marine - 90% Rule (adding controls for SCCs for residual fuel)

- ICAO Engine NOx Standards for Commercial Aircraft

- NRRetrofit

- LOWRVP

## 3.3  EGU controls used in the control strategy

CAIR

The data and projections presented in Section 3.2.2 cover the electric power sector, an industry that will achieve significant emission reductions under the Clean Air Interstate Rule (CAIR) over the next 10 to 15 years. Based on an assessment of the emissions contributing to interstate transport of air pollution and available control measures, EPA determined that achieving required reductions in the identified States by controlling emissions from power plants is highly cost effective. CAIR will permanently cap emissions of sulfur dioxide (SO2) and nitrogen oxides (NOx) in the eastern United States. CAIR achieves large reductions of SO2 and/or NOx emissions across 28 eastern states and the District of Columbia.

Figure 3-3A: CAIR Affected Region

When fully implemented, CAIR will reduce SO2 emissions in these states by over 70% and NOx emissions by over 60% from 2003 levels (some of which are due to NOx SIP Call). This will result in significant environmental and health benefits and will substantially reduce premature mortality in the eastern United States. The benefits will continue to grow each year with further implementation. CAIR was designed with current air quality standard in mind, and requires significant emission reductions in the East, where they are needed most and where transport of pollution is a major concern. CAIR will bring most areas in the Eastern US into attainment with the current ozone and current PM2.5 standards. Some areas will need to adopt additional local control measures beyond CAIR. CAIR is a regional solution to address transport, not a solution to all local nonattainment issues. The large reductions anticipated with CAIR, in conjunction with reasonable additional local control measures for SO2, NOx, and direct PM, will move States towards attainment in a deliberate and logical matter.

Based on the final State rules that have been submitted and the proposed State rules that EPA has reviewed, EPA believes that all States intend to use the CAIR trading programs as their mechanism for meeting the emission reduction requirements of CAIR.

The analysis in this section reflects these realities and attempts to show, in an illustrative fashion, the costs and impacts of meeting a proposed 8-hr ozone standard of 0.070 for the power sector.

#### Model and Background

CAIR was designed to achieve significant emissions reductions in a highly cost-effective manner to reduce the transport of fine particles that have been found to contribute to nonattainment. EPA analysis has found that the most efficient method to achieve the emissions reduction targets is through a cap-and-trade system on the power sector that States have the option of adopting. The modeling done with IPM assumes a region-wide cap and trade system on the power sector for the States covered.

It is important to note that the analysis herein uses the Integrated Planning Model (IPM) v2.1.9 to ensure consistency with the analysis presented in 2006 PM NAAQS RIA and report incremental results.  EPA’s IPM v2.1.9 incorporates Federal and State rules and regulations adopted before March 2004 and various NSR settlements.  A detailed discussion of uncertainties associated with the EGU sector can be found in 2006 PM NAAQS RIA (pg. 3-50).  A newer version of the model (IPM v3.0) is available which includes input and model assumption updates in modeling power sector.  IPM v3.0 will be used in the Final Ozone NAAQS RIA as part of the updated modeling platform.  Additionally, other control strategies are being considered that may be applicable to the EGU sector, which would be presented in the final Ozone RIA.

The economic modeling using IPM presented in this and other chapters has been developed for specific analyses of the power sector. EPA’s modeling is based on its best judgment for various input assumptions that are uncertain, particularly assumptions for future fuel prices and electricity demand growth. To some degree, EPA addresses the uncertainty surrounding these two assumptions through sensitivity analyses. More detail on IPM can be found in the model documentation, which provides additional information on the assumptions discussed here as well as all other assumptions and inputs to the model (http://www.epa.gov/airmarkets/progsregs/epa-ipm/past-modeling.html).

EGU NOx Emission Control Technologies

The Integrated Planning Model v2.1.9 (IPM) includes SO2, NOx, and mercury (Hg) emission control technology options for meeting existing and future federal, regional, and state, SO2, NOx and Hg emission limits. The NOx control technology options include Selective Catalytic Reduction (SCR) system and Selective Non-Catalytic Reduction (SNCR) systems.  It is important to note that beyond these emission control options, IPM offers other compliance options for meeting emission limits.  These include fuel switching, re-powering, and adjustments in the dispatching of electric generating units.

Table 3-3B summarizes retrofit NOx emission control performance assumptions.

Table 3-3B.  Summary of Retrofit NOx Emission Control Performance Assumptions

|  | Selective Catalytic Reduction (SCR) | Selective Non-Catalytic Reduction (SNCR) |
| --- | --- | --- |
| Unit Type | Coal | Oil/Gas* | Coal | Oil/Gas* |
| Percent Removal | 90% down to 0.06 lb/mmBtu | 80% | 35% | 50% |
| Size Applicability | Units  100 MW | Units  25 MW | Units  25 MW and Units < 200 MW | Units  25 MW |

* Controls to oil- or gas-fired EGUs are not applied as part of the EGU control strategy included in this RIA.

Existing coal-fired units that are retrofit with SCR have a NOx removal efficiency of 90%, with a minimum controlled NOx emission rate of 0.06 lb/mmBtu in IPM v2.1.9..  Potential (new) coal-fired, combined cycle, and IGCC units are modeled to be constructed with SCR systems and designed to have emission rates ranging between 0.02 and 0.06 lb NOx/mmBtu.

Detailed cost and performance derivations for NOx controls are discussed in detail in the EPA’s documentation of IPM (http://www.epa.gov/airmarkets/progsregs/epa-ipm/past-modeling.html).

  - Change in ozone concentrations between Baseline and post 0.070 ppm Control Strategy Modeling

| State | County | Baseline 8-hour ozone DV (ppm) | Control Scenario 8-hour ozone DV (ppm) | Change (ppm) |
| --- | --- | --- | --- | --- |
| Alabama | Baldwin | 0.067 | 0.066 | 0.001 |
| Alabama | Clay | 0.060 | 0.056 | 0.004 |
| Alabama | Elmore | 0.062 | 0.060 | 0.002 |
| Alabama | Jefferson | 0.064 | 0.063 | 0.001 |
| Alabama | Madison | 0.063 | 0.061 | 0.002 |
| Alabama | Mobile | 0.068 | 0.068 | 0.000 |
| Alabama | Montgomery | 0.061 | 0.060 | 0.001 |
| Alabama | Morgan | 0.066 | 0.065 | 0.001 |
| Alabama | Shelby | 0.066 | 0.065 | 0.001 |
| Alabama | Tuscaloosa | 0.057 | 0.056 | 0.001 |
| Arizona | Maricopa | 0.078 | 0.077 | 0.001 |
| Arizona | Pinal | 0.072 | 0.071 | 0.001 |
| Arkansas | Crittenden | 0.075 | 0.072 | 0.003 |
| Arkansas | Pulaski | 0.069 | 0.068 | 0.001 |
| California | Alameda | 0.067 | 0.067 | 0.000 |
| California | Amador | 0.068 | 0.068 | 0.000 |
| California | Butte | 0.069 | 0.069 | 0.000 |
| California | Calaveras | 0.073 | 0.073 | 0.000 |
| California | Colusa | 0.059 | 0.059 | 0.000 |
| California | Contra Costa | 0.070 | 0.070 | 0.000 |
| California | El Dorado | 0.080 | 0.080 | 0.000 |
| California | Fresno | 0.092 | 0.092 | 0.000 |
| California | Glenn | 0.060 | 0.060 | 0.000 |
| California | Imperial | 0.072 | 0.072 | 0.000 |
| California | Kern | 0.096 | 0.096 | 0.000 |
| California | Kings | 0.079 | 0.079 | 0.000 |
| California | Lake | 0.053 | 0.053 | 0.000 |
| California | Los Angeles | 0.105 | 0.105 | 0.000 |
| California | Madera | 0.075 | 0.075 | 0.000 |
| California | Mariposa | 0.073 | 0.073 | 0.000 |
| California | Merced | 0.080 | 0.080 | 0.000 |
| California | Monterey | 0.054 | 0.054 | 0.000 |
| California | Napa | 0.051 | 0.051 | 0.000 |
| California | Nevada | 0.076 | 0.076 | 0.000 |
| California | Orange | 0.066 | 0.065 | 0.001 |
| California | Placer | 0.076 | 0.076 | 0.000 |
| California | Riverside | 0.102 | 0.102 | 0.000 |
| California | Sacramento | 0.076 | 0.076 | 0.000 |
| California | San Benito | 0.067 | 0.067 | 0.000 |
| California | San Bernardino | 0.129 | 0.129 | 0.000 |
| California | San Diego | 0.077 | 0.077 | 0.000 |
| California | San Joaquin | 0.067 | 0.067 | 0.000 |
| California | San Luis Obispo | 0.053 | 0.053 | 0.000 |
| California | Santa Barbara | 0.065 | 0.065 | 0.000 |
| California | Santa Clara | 0.065 | 0.065 | 0.000 |
| California | Santa Cruz | 0.054 | 0.055 | -0.001 |
| California | Shasta | 0.058 | 0.058 | 0.000 |
| California | Solano | 0.057 | 0.057 | 0.000 |
| California | Sonoma | 0.049 | 0.049 | 0.000 |
| California | Stanislaus | 0.076 | 0.076 | 0.000 |
| California | Sutter | 0.065 | 0.065 | 0.000 |
| California | Tehama | 0.066 | 0.066 | 0.000 |
| California | Tulare | 0.088 | 0.088 | 0.000 |
| California | Tuolumne | 0.073 | 0.073 | 0.000 |
| California | Ventura | 0.079 | 0.080 | -0.001 |
| California | Yolo | 0.064 | 0.064 | 0.000 |
| Colorado | Adams | 0.061 | 0.060 | 0.001 |
| Colorado | Arapahoe | 0.073 | 0.072 | 0.001 |
| Colorado | Boulder | 0.066 | 0.064 | 0.002 |
| Colorado | Denver | 0.068 | 0.067 | 0.001 |
| Colorado | Douglas | 0.076 | 0.076 | 0.000 |
| Colorado | El Paso | 0.064 | 0.063 | 0.001 |
| Colorado | Jefferson | 0.078 | 0.076 | 0.002 |
| Colorado | Larimer | 0.069 | 0.067 | 0.002 |
| Colorado | Weld | 0.067 | 0.065 | 0.002 |
| Connecticut | Fairfield | 0.088 | 0.087 | 0.001 |
| Connecticut | Hartford | 0.069 | 0.067 | 0.002 |
| Connecticut | Litchfield | 0.063 | 0.061 | 0.002 |
| Connecticut | Middlesex | 0.081 | 0.080 | 0.001 |
| Connecticut | New Haven | 0.084 | 0.083 | 0.001 |
| Connecticut | New London | 0.072 | 0.070 | 0.002 |
| Connecticut | Tolland | 0.071 | 0.069 | 0.002 |
| D.C. | Washington | 0.076 | 0.073 | 0.003 |
| Delaware | Kent | 0.072 | 0.070 | 0.002 |
| Delaware | New Castle | 0.075 | 0.073 | 0.002 |
| Delaware | Sussex | 0.070 | 0.068 | 0.002 |
| Florida | Bay | 0.067 | 0.066 | 0.001 |
| Florida | Brevard | 0.055 | 0.053 | 0.002 |
| Florida | Duval | 0.058 | 0.057 | 0.001 |
| Florida | Escambia | 0.069 | 0.069 | 0.000 |
| Florida | Hillsborough | 0.072 | 0.071 | 0.001 |
| Florida | Manatee | 0.067 | 0.065 | 0.002 |
| Florida | Pasco | 0.061 | 0.060 | 0.001 |
| Florida | Pinellas | 0.064 | 0.063 | 0.001 |
| Florida | Santa Rosa | 0.065 | 0.064 | 0.001 |
| Florida | Sarasota | 0.063 | 0.061 | 0.002 |
| Georgia | Bibb | 0.073 | 0.069 | 0.004 |
| Georgia | Chatham | 0.057 | 0.056 | 0.001 |
| Georgia | Cherokee | 0.055 | 0.052 | 0.003 |
| Georgia | Cobb | 0.072 | 0.068 | 0.004 |
| Georgia | Coweta | 0.072 | 0.064 | 0.008 |
| Georgia | Dawson | 0.058 | 0.055 | 0.003 |
| Georgia | De Kalb | 0.076 | 0.072 | 0.004 |
| Georgia | Douglas | 0.071 | 0.067 | 0.004 |
| Georgia | Fayette | 0.069 | 0.066 | 0.003 |
| Georgia | Fulton | 0.080 | 0.076 | 0.004 |
| Georgia | Glynn | 0.058 | 0.057 | 0.001 |
| Georgia | Gwinnett | 0.067 | 0.064 | 0.003 |
| Georgia | Henry | 0.072 | 0.068 | 0.004 |
| Georgia | Murray | 0.062 | 0.059 | 0.003 |
| Georgia | Muscogee | 0.065 | 0.061 | 0.004 |
| Georgia | Paulding | 0.068 | 0.065 | 0.003 |
| Georgia | Richmond | 0.067 | 0.063 | 0.004 |
| Georgia | Rockdale | 0.071 | 0.067 | 0.004 |
| Illinois | Adams | 0.062 | 0.057 | 0.005 |
| Illinois | Champaign | 0.064 | 0.062 | 0.002 |
| Illinois | Clark | 0.057 | 0.056 | 0.001 |
| Illinois | Cook | 0.083 | 0.083 | 0.000 |
| Illinois | Du Page | 0.065 | 0.064 | 0.001 |
| Illinois | Effingham | 0.062 | 0.061 | 0.001 |
| Illinois | Hamilton | 0.066 | 0.064 | 0.002 |
| Illinois | Jersey | 0.074 | 0.069 | 0.005 |
| Illinois | Kane | 0.067 | 0.066 | 0.001 |
| Illinois | Lake | 0.074 | 0.073 | 0.001 |
| Illinois | Macon | 0.060 | 0.059 | 0.001 |
| Illinois | Macoupin | 0.064 | 0.060 | 0.004 |
| Illinois | Madison | 0.071 | 0.066 | 0.005 |
| Illinois | McHenry | 0.070 | 0.068 | 0.002 |
| Illinois | McLean | 0.063 | 0.061 | 0.002 |
| Illinois | Peoria | 0.066 | 0.064 | 0.002 |
| Illinois | Randolph | 0.065 | 0.062 | 0.003 |
| Illinois | Rock Island | 0.058 | 0.057 | 0.001 |
| Illinois | Sangamon | 0.060 | 0.058 | 0.002 |
| Illinois | St Clair | 0.072 | 0.069 | 0.003 |
| Illinois | Will | 0.068 | 0.067 | 0.001 |
| Illinois | Winnebago | 0.061 | 0.060 | 0.001 |
| Indiana | Allen | 0.070 | 0.068 | 0.002 |
| Indiana | Boone | 0.072 | 0.069 | 0.003 |
| Indiana | Carroll | 0.066 | 0.064 | 0.002 |
| Indiana | Clark | 0.076 | 0.074 | 0.002 |
| Indiana | Delaware | 0.069 | 0.067 | 0.002 |
| Indiana | Floyd | 0.071 | 0.070 | 0.001 |
| Indiana | Gibson | 0.056 | 0.054 | 0.002 |
| Indiana | Greene | 0.069 | 0.067 | 0.002 |
| Indiana | Hamilton | 0.076 | 0.073 | 0.003 |
| Indiana | Hancock | 0.074 | 0.071 | 0.003 |
| Indiana | Hendricks | 0.071 | 0.069 | 0.002 |
| Indiana | Huntington | 0.067 | 0.065 | 0.002 |
| Indiana | Jackson | 0.068 | 0.065 | 0.003 |
| Indiana | Johnson | 0.070 | 0.068 | 0.002 |
| Indiana | La Porte | 0.075 | 0.073 | 0.002 |
| Indiana | Lake | 0.084 | 0.083 | 0.001 |
| Indiana | Madison | 0.071 | 0.068 | 0.003 |
| Indiana | Marion | 0.075 | 0.072 | 0.003 |
| Indiana | Morgan | 0.070 | 0.066 | 0.004 |
| Indiana | Perry | 0.071 | 0.071 | 0.000 |
| Indiana | Porter | 0.078 | 0.077 | 0.001 |
| Indiana | Posey | 0.071 | 0.070 | 0.001 |
| Indiana | Shelby | 0.077 | 0.074 | 0.003 |
| Indiana | St Joseph | 0.069 | 0.067 | 0.002 |
| Indiana | Vanderburgh | 0.068 | 0.066 | 0.002 |
| Indiana | Vigo | 0.070 | 0.065 | 0.005 |
| Indiana | Warrick | 0.068 | 0.067 | 0.001 |
| Iowa | Clinton | 0.063 | 0.062 | 0.001 |
| Iowa | Scott | 0.066 | 0.065 | 0.001 |
| Kansas | Wyandotte | 0.070 | 0.069 | 0.001 |
| Kentucky | Bell | 0.063 | 0.062 | 0.001 |
| Kentucky | Boone | 0.067 | 0.066 | 0.001 |
| Kentucky | Boyd | 0.072 | 0.067 | 0.005 |
| Kentucky | Bullitt | 0.067 | 0.064 | 0.003 |
| Kentucky | Campbell | 0.077 | 0.073 | 0.004 |
| Kentucky | Carter | 0.064 | 0.061 | 0.003 |
| Kentucky | Christian | 0.066 | 0.065 | 0.001 |
| Kentucky | Daviess | 0.062 | 0.062 | 0.000 |
| Kentucky | Edmonson | 0.067 | 0.066 | 0.001 |
| Kentucky | Fayette | 0.063 | 0.061 | 0.002 |
| Kentucky | Graves | 0.068 | 0.066 | 0.002 |
| Kentucky | Greenup | 0.068 | 0.064 | 0.004 |
| Kentucky | Hancock | 0.067 | 0.067 | 0.000 |
| Kentucky | Hardin | 0.068 | 0.065 | 0.003 |
| Kentucky | Henderson | 0.066 | 0.065 | 0.001 |
| Kentucky | Jefferson | 0.072 | 0.070 | 0.002 |
| Kentucky | Jessamine | 0.062 | 0.063 | -0.001 |
| Kentucky | Kenton | 0.073 | 0.069 | 0.004 |
| Kentucky | Livingston | 0.071 | 0.069 | 0.002 |
| Kentucky | McCracken | 0.069 | 0.067 | 0.002 |
| Kentucky | McLean | 0.065 | 0.064 | 0.001 |
| Kentucky | Oldham | 0.072 | 0.070 | 0.002 |
| Kentucky | Pulaski | 0.065 | 0.064 | 0.001 |
| Kentucky | Scott | 0.056 | 0.055 | 0.001 |
| Kentucky | Simpson | 0.066 | 0.065 | 0.001 |
| Kentucky | Trigg | 0.060 | 0.058 | 0.002 |
| Kentucky | Warren | 0.066 | 0.065 | 0.001 |
| Louisiana | Ascension | 0.071 | 0.066 | 0.005 |
| Louisiana | Bossier | 0.073 | 0.070 | 0.003 |
| Louisiana | Caddo | 0.068 | 0.065 | 0.003 |
| Louisiana | Calcasieu | 0.072 | 0.067 | 0.005 |
| Louisiana | East Baton Rouge | 0.077 | 0.074 | 0.003 |
| Louisiana | Grant | 0.063 | 0.059 | 0.004 |
| Louisiana | Iberville | 0.076 | 0.072 | 0.004 |
| Louisiana | Jefferson | 0.072 | 0.069 | 0.003 |
| Louisiana | Lafayette | 0.070 | 0.064 | 0.006 |
| Louisiana | Lafourche | 0.072 | 0.068 | 0.004 |
| Louisiana | Livingston | 0.072 | 0.068 | 0.004 |
| Louisiana | Orleans | 0.060 | 0.058 | 0.002 |
| Louisiana | Ouachita | 0.068 | 0.064 | 0.004 |
| Louisiana | Pointe Coupee | 0.064 | 0.060 | 0.004 |
| Louisiana | St Bernard | 0.067 | 0.065 | 0.002 |
| Louisiana | St Charles | 0.068 | 0.066 | 0.002 |
| Louisiana | St James | 0.069 | 0.065 | 0.004 |
| Louisiana | St John The Baptist | 0.072 | 0.069 | 0.003 |
| Louisiana | St Mary | 0.068 | 0.062 | 0.006 |
| Louisiana | West Baton Rouge | 0.074 | 0.071 | 0.003 |
| Maine | Cumberland | 0.065 | 0.063 | 0.002 |
| Maine | Hancock | 0.070 | 0.067 | 0.003 |
| Maine | Kennebec | 0.060 | 0.057 | 0.003 |
| Maine | Knox | 0.063 | 0.060 | 0.003 |
| Maine | Penobscot | 0.062 | 0.059 | 0.003 |
| Maine | York | 0.069 | 0.066 | 0.003 |
| Maryland | Anne Arundel | 0.076 | 0.074 | 0.002 |
| Maryland | Baltimore | 0.077 | 0.075 | 0.002 |
| Maryland | Calvert | 0.065 | 0.063 | 0.002 |
| Maryland | Carroll | 0.068 | 0.066 | 0.002 |
| Maryland | Cecil | 0.078 | 0.075 | 0.003 |
| Maryland | Charles | 0.070 | 0.068 | 0.002 |
| Maryland | Frederick | 0.067 | 0.065 | 0.002 |
| Maryland | Harford | 0.084 | 0.082 | 0.002 |
| Maryland | Kent | 0.075 | 0.072 | 0.003 |
| Maryland | Montgomery | 0.072 | 0.070 | 0.002 |
| Maryland | Prince Georges | 0.075 | 0.072 | 0.003 |
| Maryland | Washington | 0.067 | 0.063 | 0.004 |
| Massachusetts | Barnstable | 0.072 | 0.070 | 0.002 |
| Massachusetts | Berkshire | 0.067 | 0.066 | 0.001 |
| Massachusetts | Bristol | 0.072 | 0.069 | 0.003 |
| Massachusetts | Essex | 0.071 | 0.070 | 0.001 |
| Massachusetts | Hampden | 0.070 | 0.068 | 0.002 |
| Massachusetts | Hampshire | 0.068 | 0.066 | 0.002 |
| Massachusetts | Middlesex | 0.067 | 0.064 | 0.003 |
| Massachusetts | Suffolk | 0.067 | 0.065 | 0.002 |
| Massachusetts | Worcester | 0.064 | 0.062 | 0.002 |
| Michigan | Allegan | 0.075 | 0.072 | 0.003 |
| Michigan | Benzie | 0.070 | 0.068 | 0.002 |
| Michigan | Berrien | 0.072 | 0.070 | 0.002 |
| Michigan | Cass | 0.069 | 0.067 | 0.002 |
| Michigan | Clinton | 0.066 | 0.062 | 0.004 |
| Michigan | Genesee | 0.067 | 0.064 | 0.003 |
| Michigan | Huron | 0.070 | 0.067 | 0.003 |
| Michigan | Ingham | 0.066 | 0.062 | 0.004 |
| Michigan | Kalamazoo | 0.065 | 0.062 | 0.003 |
| Michigan | Kent | 0.067 | 0.064 | 0.003 |
| Michigan | Lenawee | 0.069 | 0.063 | 0.006 |
| Michigan | Macomb | 0.080 | 0.078 | 0.002 |
| Michigan | Mason | 0.072 | 0.070 | 0.002 |
| Michigan | Missaukee | 0.064 | 0.061 | 0.003 |
| Michigan | Muskegon | 0.074 | 0.071 | 0.003 |
| Michigan | Oakland | 0.077 | 0.075 | 0.002 |
| Michigan | Ottawa | 0.070 | 0.067 | 0.003 |
| Michigan | St Clair | 0.073 | 0.071 | 0.002 |
| Michigan | Washtenaw | 0.076 | 0.072 | 0.004 |
| Michigan | Wayne | 0.076 | 0.073 | 0.003 |
| Minnesota | Anoka | 0.058 | 0.057 | 0.001 |
| Minnesota | Washington | 0.059 | 0.059 | 0.000 |
| Mississippi | De Soto | 0.069 | 0.067 | 0.002 |
| Mississippi | Hancock | 0.070 | 0.068 | 0.002 |
| Mississippi | Harrison | 0.064 | 0.067 | -0.003 |
| Mississippi | Hinds | 0.055 | 0.053 | 0.002 |
| Mississippi | Jackson | 0.069 | 0.070 | -0.001 |
| Mississippi | Warren | 0.054 | 0.051 | 0.003 |
| Missouri | Clay | 0.070 | 0.068 | 0.002 |
| Missouri | Jefferson | 0.076 | 0.072 | 0.004 |
| Missouri | Platte | 0.069 | 0.068 | 0.001 |
| Missouri | St Charles | 0.076 | 0.072 | 0.004 |
| Missouri | St Louis | 0.079 | 0.075 | 0.004 |
| Missouri | St Louis City | 0.078 | 0.075 | 0.003 |
| Missouri | Ste Genevieve | 0.068 | 0.064 | 0.004 |
| Nevada | Clark | 0.072 | 0.072 | 0.000 |
| Nevada | Washoe | 0.063 | 0.063 | 0.000 |
| New Hampshire | Hillsborough | 0.063 | 0.060 | 0.003 |
| New Hampshire | Rockingham | 0.063 | 0.061 | 0.002 |
| New Jersey | Atlantic | 0.071 | 0.069 | 0.002 |
| New Jersey | Bergen | 0.077 | 0.075 | 0.002 |
| New Jersey | Camden | 0.082 | 0.080 | 0.002 |
| New Jersey | Cumberland | 0.073 | 0.071 | 0.002 |
| New Jersey | Essex | 0.056 | 0.055 | 0.001 |
| New Jersey | Gloucester | 0.080 | 0.078 | 0.002 |
| New Jersey | Hudson | 0.074 | 0.073 | 0.001 |
| New Jersey | Hunterdon | 0.078 | 0.077 | 0.001 |
| New Jersey | Mercer | 0.083 | 0.081 | 0.002 |
| New Jersey | Middlesex | 0.081 | 0.079 | 0.002 |
| New Jersey | Monmouth | 0.078 | 0.077 | 0.001 |
| New Jersey | Morris | 0.077 | 0.075 | 0.002 |
| New Jersey | Ocean | 0.084 | 0.081 | 0.003 |
| New Jersey | Passaic | 0.071 | 0.069 | 0.002 |
| New Mexico | Dona Ana | 0.071 | 0.070 | 0.001 |
| New Mexico | San Juan | 0.071 | 0.068 | 0.003 |
| New York | Albany | 0.064 | 0.063 | 0.001 |
| New York | Bronx | 0.069 | 0.068 | 0.001 |
| New York | Chautauqua | 0.074 | 0.070 | 0.004 |
| New York | Dutchess | 0.067 | 0.066 | 0.001 |
| New York | Erie | 0.079 | 0.075 | 0.004 |
| New York | Jefferson | 0.075 | 0.072 | 0.003 |
| New York | Monroe | 0.073 | 0.072 | 0.001 |
| New York | Niagara | 0.076 | 0.075 | 0.001 |
| New York | Orange | 0.063 | 0.061 | 0.002 |
| New York | Putnam | 0.070 | 0.068 | 0.002 |
| New York | Queens | 0.068 | 0.067 | 0.001 |
| New York | Richmond | 0.074 | 0.072 | 0.002 |
| New York | Saratoga | 0.066 | 0.065 | 0.001 |
| New York | Suffolk | 0.086 | 0.084 | 0.002 |
| New York | Ulster | 0.065 | 0.063 | 0.002 |
| New York | Wayne | 0.070 | 0.068 | 0.002 |
| New York | Westchester | 0.075 | 0.074 | 0.001 |
| North Carolina | Alexander | 0.066 | 0.064 | 0.002 |
| North Carolina | Buncombe | 0.065 | 0.065 | 0.000 |
| North Carolina | Camden | 0.063 | 0.062 | 0.001 |
| North Carolina | Caswell | 0.063 | 0.059 | 0.004 |
| North Carolina | Chatham | 0.063 | 0.061 | 0.002 |
| North Carolina | Cumberland | 0.065 | 0.063 | 0.002 |
| North Carolina | Davie | 0.067 | 0.065 | 0.002 |
| North Carolina | Durham | 0.063 | 0.060 | 0.003 |
| North Carolina | Edgecombe | 0.066 | 0.064 | 0.002 |
| North Carolina | Forsyth | 0.068 | 0.065 | 0.003 |
| North Carolina | Franklin | 0.063 | 0.060 | 0.003 |
| North Carolina | Granville | 0.067 | 0.065 | 0.002 |
| North Carolina | Guilford | 0.064 | 0.061 | 0.003 |
| North Carolina | Johnston | 0.062 | 0.059 | 0.003 |
| North Carolina | Lincoln | 0.069 | 0.067 | 0.002 |
| North Carolina | Mecklenburg | 0.074 | 0.072 | 0.002 |
| North Carolina | New Hanover | 0.062 | 0.061 | 0.001 |
| North Carolina | Northampton | 0.067 | 0.064 | 0.003 |
| North Carolina | Person | 0.071 | 0.068 | 0.003 |
| North Carolina | Randolph | 0.063 | 0.060 | 0.003 |
| North Carolina | Rockingham | 0.064 | 0.061 | 0.003 |
| North Carolina | Rowan | 0.073 | 0.071 | 0.002 |
| North Carolina | Union | 0.065 | 0.063 | 0.002 |
| North Carolina | Wake | 0.066 | 0.064 | 0.002 |
| Ohio | Allen | 0.071 | 0.067 | 0.004 |
| Ohio | Ashtabula | 0.077 | 0.073 | 0.004 |
| Ohio | Butler | 0.073 | 0.070 | 0.003 |
| Ohio | Clark | 0.068 | 0.063 | 0.005 |
| Ohio | Clermont | 0.071 | 0.068 | 0.003 |
| Ohio | Clinton | 0.074 | 0.070 | 0.004 |
| Ohio | Cuyahoga | 0.071 | 0.068 | 0.003 |
| Ohio | Delaware | 0.071 | 0.068 | 0.003 |
| Ohio | Franklin | 0.076 | 0.073 | 0.003 |
| Ohio | Geauga | 0.080 | 0.076 | 0.004 |
| Ohio | Greene | 0.068 | 0.062 | 0.006 |
| Ohio | Hamilton | 0.074 | 0.070 | 0.004 |
| Ohio | Jefferson | 0.067 | 0.064 | 0.003 |
| Ohio | Knox | 0.069 | 0.065 | 0.004 |
| Ohio | Lake | 0.076 | 0.073 | 0.003 |
| Ohio | Lawrence | 0.069 | 0.065 | 0.004 |
| Ohio | Licking | 0.069 | 0.066 | 0.003 |
| Ohio | Lorain | 0.071 | 0.068 | 0.003 |
| Ohio | Lucas | 0.072 | 0.069 | 0.003 |
| Ohio | Madison | 0.068 | 0.063 | 0.005 |
| Ohio | Mahoning | 0.071 | 0.068 | 0.003 |
| Ohio | Medina | 0.069 | 0.066 | 0.003 |
| Ohio | Miami | 0.065 | 0.061 | 0.004 |
| Ohio | Montgomery | 0.068 | 0.062 | 0.006 |
| Ohio | Portage | 0.074 | 0.070 | 0.004 |
| Ohio | Preble | 0.061 | 0.058 | 0.003 |
| Ohio | Stark | 0.071 | 0.068 | 0.003 |
| Ohio | Summit | 0.075 | 0.071 | 0.004 |
| Ohio | Trumbull | 0.073 | 0.070 | 0.003 |
| Ohio | Warren | 0.071 | 0.068 | 0.003 |
| Ohio | Washington | 0.064 | 0.061 | 0.003 |
| Ohio | Wood | 0.070 | 0.067 | 0.003 |
| Oklahoma | Cleveland | 0.065 | 0.064 | 0.001 |
| Oklahoma | Marshall | 0.069 | 0.067 | 0.002 |
| Oklahoma | Mc Clain | 0.067 | 0.065 | 0.002 |
| Oklahoma | Oklahoma | 0.067 | 0.065 | 0.002 |
| Oklahoma | Tulsa | 0.073 | 0.070 | 0.003 |
| Pennsylvania | Allegheny | 0.079 | 0.076 | 0.003 |
| Pennsylvania | Armstrong | 0.072 | 0.069 | 0.003 |
| Pennsylvania | Beaver | 0.076 | 0.073 | 0.003 |
| Pennsylvania | Berks | 0.071 | 0.068 | 0.003 |
| Pennsylvania | Blair | 0.065 | 0.063 | 0.002 |
| Pennsylvania | Bucks | 0.084 | 0.082 | 0.002 |
| Pennsylvania | Cambria | 0.071 | 0.068 | 0.003 |
| Pennsylvania | Centre | 0.066 | 0.064 | 0.002 |
| Pennsylvania | Chester | 0.075 | 0.073 | 0.002 |
| Pennsylvania | Clearfield | 0.068 | 0.065 | 0.003 |
| Pennsylvania | Dauphin | 0.070 | 0.068 | 0.002 |
| Pennsylvania | Delaware | 0.074 | 0.073 | 0.001 |
| Pennsylvania | Erie | 0.069 | 0.067 | 0.002 |
| Pennsylvania | Franklin | 0.070 | 0.068 | 0.002 |
| Pennsylvania | Greene | 0.069 | 0.066 | 0.003 |
| Pennsylvania | Lackawanna | 0.064 | 0.062 | 0.002 |
| Pennsylvania | Lancaster | 0.071 | 0.068 | 0.003 |
| Pennsylvania | Lawrence | 0.063 | 0.059 | 0.004 |
| Pennsylvania | Lehigh | 0.071 | 0.069 | 0.002 |
| Pennsylvania | Luzerne | 0.064 | 0.063 | 0.001 |
| Pennsylvania | Lycoming | 0.059 | 0.057 | 0.002 |
| Pennsylvania | Mercer | 0.073 | 0.069 | 0.004 |
| Pennsylvania | Montgomery | 0.078 | 0.076 | 0.002 |
| Pennsylvania | Northampton | 0.072 | 0.070 | 0.002 |
| Pennsylvania | Perry | 0.063 | 0.061 | 0.002 |
| Pennsylvania | Philadelphia | 0.080 | 0.078 | 0.002 |
| Pennsylvania | Washington | 0.070 | 0.067 | 0.003 |
| Pennsylvania | Westmoreland | 0.070 | 0.067 | 0.003 |
| Pennsylvania | York | 0.071 | 0.067 | 0.004 |
| Rhode Island | Kent | 0.074 | 0.072 | 0.002 |
| Rhode Island | Providence | 0.071 | 0.068 | 0.003 |
| Rhode Island | Washington | 0.075 | 0.072 | 0.003 |
| South Carolina | Anderson | 0.067 | 0.065 | 0.002 |
| South Carolina | Berkeley | 0.058 | 0.057 | 0.001 |
| South Carolina | Charleston | 0.057 | 0.055 | 0.002 |
| South Carolina | Cherokee | 0.063 | 0.061 | 0.002 |
| South Carolina | Chester | 0.064 | 0.061 | 0.003 |
| South Carolina | Edgefield | 0.063 | 0.058 | 0.005 |
| South Carolina | Pickens | 0.065 | 0.063 | 0.002 |
| South Carolina | Richland | 0.069 | 0.066 | 0.003 |
| South Carolina | Spartanburg | 0.066 | 0.063 | 0.003 |
| South Carolina | Union | 0.062 | 0.059 | 0.003 |
| South Carolina | York | 0.063 | 0.061 | 0.002 |
| Tennessee | Anderson | 0.064 | 0.061 | 0.003 |
| Tennessee | Blount | 0.071 | 0.067 | 0.004 |
| Tennessee | Davidson | 0.064 | 0.063 | 0.001 |
| Tennessee | Hamilton | 0.066 | 0.063 | 0.003 |
| Tennessee | Haywood | 0.067 | 0.063 | 0.004 |
| Tennessee | Jefferson | 0.068 | 0.065 | 0.003 |
| Tennessee | Knox | 0.071 | 0.066 | 0.005 |
| Tennessee | Meigs | 0.066 | 0.063 | 0.003 |
| Tennessee | Rutherford | 0.065 | 0.063 | 0.002 |
| Tennessee | Shelby | 0.072 | 0.069 | 0.003 |
| Tennessee | Sullivan | 0.072 | 0.062 | 0.010 |
| Tennessee | Sumner | 0.068 | 0.067 | 0.001 |
| Tennessee | Williamson | 0.068 | 0.066 | 0.002 |
| Tennessee | Wilson | 0.066 | 0.065 | 0.001 |
| Texas | Brazoria | 0.078 | 0.076 | 0.002 |
| Texas | Collin | 0.075 | 0.072 | 0.003 |
| Texas | Dallas | 0.079 | 0.077 | 0.002 |
| Texas | Denton | 0.078 | 0.075 | 0.003 |
| Texas | El Paso | 0.070 | 0.069 | 0.001 |
| Texas | Ellis | 0.074 | 0.069 | 0.005 |
| Texas | Galveston | 0.078 | 0.075 | 0.003 |
| Texas | Gregg | 0.079 | 0.073 | 0.006 |
| Texas | Harris | 0.092 | 0.090 | 0.002 |
| Texas | Harrison | 0.065 | 0.062 | 0.003 |
| Texas | Hood | 0.068 | 0.066 | 0.002 |
| Texas | Jefferson | 0.079 | 0.072 | 0.007 |
| Texas | Johnson | 0.073 | 0.069 | 0.004 |
| Texas | Marion | 0.069 | 0.065 | 0.004 |
| Texas | Montgomery | 0.072 | 0.070 | 0.002 |
| Texas | Orange | 0.068 | 0.064 | 0.004 |
| Texas | Parker | 0.068 | 0.066 | 0.002 |
| Texas | Rockwall | 0.067 | 0.063 | 0.004 |
| Texas | Smith | 0.071 | 0.068 | 0.003 |
| Texas | Tarrant | 0.079 | 0.076 | 0.003 |
| Utah | Box Elder | 0.066 | 0.065 | 0.001 |
| Utah | Cache | 0.055 | 0.054 | 0.001 |
| Utah | Davis | 0.071 | 0.070 | 0.001 |
| Utah | Salt Lake | 0.073 | 0.072 | 0.001 |
| Utah | Utah | 0.070 | 0.069 | 0.001 |
| Utah | Weber | 0.067 | 0.066 | 0.001 |
| Vermont | Bennington | 0.060 | 0.059 | 0.001 |
| Virginia | Alexandria City | 0.072 | 0.069 | 0.003 |
| Virginia | Arlington | 0.078 | 0.075 | 0.003 |
| Virginia | Caroline | 0.063 | 0.062 | 0.001 |
| Virginia | Charles City | 0.074 | 0.073 | 0.001 |
| Virginia | Chesterfield | 0.071 | 0.070 | 0.001 |
| Virginia | Fairfax | 0.077 | 0.074 | 0.003 |
| Virginia | Fauquier | 0.062 | 0.061 | 0.001 |
| Virginia | Frederick | 0.067 | 0.064 | 0.003 |
| Virginia | Hampton City | 0.077 | 0.076 | 0.001 |
| Virginia | Hanover | 0.074 | 0.072 | 0.002 |
| Virginia | Henrico | 0.074 | 0.073 | 0.001 |
| Virginia | Loudoun | 0.070 | 0.068 | 0.002 |
| Virginia | Madison | 0.067 | 0.065 | 0.002 |
| Virginia | Prince William | 0.066 | 0.064 | 0.002 |
| Virginia | Roanoke | 0.069 | 0.067 | 0.002 |
| Virginia | Stafford | 0.064 | 0.062 | 0.002 |
| Virginia | Suffolk City | 0.080 | 0.080 | 0.000 |
| West Virginia | Berkeley | 0.068 | 0.063 | 0.005 |
| West Virginia | Cabell | 0.073 | 0.069 | 0.004 |
| West Virginia | Hancock | 0.068 | 0.065 | 0.003 |
| West Virginia | Kanawha | 0.069 | 0.064 | 0.005 |
| West Virginia | Monongalia | 0.064 | 0.063 | 0.001 |
| West Virginia | Ohio | 0.067 | 0.064 | 0.003 |
| West Virginia | Wood | 0.065 | 0.062 | 0.003 |
| Wisconsin | Brown | 0.065 | 0.063 | 0.002 |
| Wisconsin | Columbia | 0.062 | 0.061 | 0.001 |
| Wisconsin | Dane | 0.062 | 0.060 | 0.002 |
| Wisconsin | Dodge | 0.063 | 0.062 | 0.001 |
| Wisconsin | Door | 0.074 | 0.072 | 0.002 |
| Wisconsin | Fond Du Lac | 0.061 | 0.060 | 0.001 |
| Wisconsin | Jefferson | 0.066 | 0.065 | 0.001 |
| Wisconsin | Kenosha | 0.086 | 0.085 | 0.001 |
| Wisconsin | Kewaunee | 0.074 | 0.072 | 0.002 |
| Wisconsin | Manitowoc | 0.074 | 0.072 | 0.002 |
| Wisconsin | Milwaukee | 0.075 | 0.073 | 0.002 |
| Wisconsin | Outagamie | 0.059 | 0.057 | 0.002 |
| Wisconsin | Ozaukee | 0.079 | 0.077 | 0.002 |
| Wisconsin | Racine | 0.079 | 0.077 | 0.002 |
| Wisconsin | Rock | 0.069 | 0.068 | 0.001 |
| Wisconsin | Sheboygan | 0.082 | 0.080 | 0.002 |
| Wisconsin | Walworth | 0.066 | 0.065 | 0.001 |
| Wisconsin | Washington | 0.065 | 0.063 | 0.002 |
| Wisconsin | Waukesha | 0.067 | 0.065 | 0.002 |
| Wisconsin | Winnebago | 0.063 | 0.062 | 0.001 |

# Footnotes

“Stationary Reciprocating Internal Combustion Engines Technical Support Document for NOx SIP Call Proposal,” U.S. Environmental Protection Agency.  September 5, 2000.  Available on the Internet at http://www.epa.gov/ttn/naaqs/ozone/rto/sip/data/tsd9-00.pdf.

“Stationary Internal Combustion Engines:  Updated Information on NOx Emissions and Control Techniques,” Ec/R Incorporated, Chapel Hill, NC.  September 1, 2000.  Available on the Internet at http://www.epa.gov/ttn/naaqs/ozone/ozonetech/ic_engine_nox_update_09012000.pdf.

VOC Fugitive Losses:  New Monitors, Emissions Losses, and Potential Policy Gaps.  2006 International Workshop.  U.S. Environmental Protection Agency, Office of Air Quality Planning and Standards and Office of Solid Waste and Emergency Response.  October 25-27, 2006.

VOC Fugitive Losses:  New Monitors, Emissions Losses, and Potential Policy Gaps.  2006 International Workshop.  U.S. Environmental Protection Agency, Office of Air Quality Planning and Standards and Office of Solid Waste and Emergency Response.  October 25-27, 2006.

Bay Area Air Quality Management District (BAAQMD).  Proposed Revision of Regulation 8, Rule 8: Wastewater Collection Systems.  Staff Report, March 17, 2004.

Bay Area Air Quality Management District (BAAQMD).  Proposed Revision of Regulation 8, Rule 8: Wastewater Collection Systems.  Staff Report, March 17, 2004.

Herzog, E., Bricka, S., Audette, L., and Rockwell, J., 2005. Do Employee Commuter Benefits Reduce Vehicle Emissions and Fuel Consumption?  Results of the Fall 2004 Best Workplaces for Commuters Survey, Transportation Research Record, Journal of the Transportation Research Board: Forthcoming.

# Comments

This is the only place where PM is listed in the mobile stuff.