ACE-470

PERFORMANCE WORK STATEMENT

- INTRODUCTION

This Performance Work Statement describes a requirement to modify eighteen FAA Central Region facilities that are necessary to remedy several OSHA citations and bring the facilities into compliance with current safety standards.

2.0 	PURPOSE

The modifications reflected in this work statement will resultantly bring the affected Central Region facilities into compliance with current OSHA and NEC standards, and thereby provide a safer work environment for personnel employed at these sites.

- BACKGROUND

During regular facility inspections, the Airway Facilities Operations Branch, ACE-470, identified occupational safety and electrical code compliance issues in need of abatement.

This work statement references each of the eighteen findings from these inspections. Each Finding is described in a uniquely numbered Safety Abatement Engineering Project document, hereafter referred to as a “Finding” that also contains a respective engineering recommendation for resolution. These eighteen documents are incorporated by reference into this work statement.

- SCOPE

Work defined in this work statement is confined to the eighteen sites listed herein and the work modifications defined by the associated Findings documents.

Pursuant to attaining the Desired Outcome (see 5.1) for the listed modifications at the listed sites, the scope shall extend to include any pertinent matters that may not be explicitly addressed in this Work Statement.

- DESCRIPTION OF WORK

  - Desired Outcome In descending order of precedence, the intent of this work statement is to specify

    - Attainment of safe working conditions for personnel while

    - Attaining compliance with the appropriate code standards and

    - Adhering to the site-specific engineering recommendations.

  - Required work The contractor shall provide materials, tools and labor for the completion of the following tasks:

    - modify locations of wall-mounted and ceiling-mounted electrical equipment to obtain proper clearances as established in current code by relocating various types of switches, distribution panels, control panels, light fixtures, etc. (Six places: Findings # 93730, 97328, 1207700, 120802, 137820, and 132338)

    - Modify battery backup systems to eliminate floor clearance obstacles by removing an obsolete battery box from the required clearance area in front of other electrical equipment.  The batteries are to be removed from the obsolete box and reinstalled on a new, lower profile steel rack. (Nine places: Findings # 123134, 123136, 123196, 123128, 123156, 123164, 123178, 123222, and 123110)

    - Modify wooden hand railings around work platforms supporting the MALS systems to satisfy OSHA requirements so that the connection of railing posts to the steel platforms will satisfy current OSHA side-load requirements. Connections are to be strengthened as necessary, and posts showing deterioration at the connection point are to be replaced. (One place: Finding # 137738)

    - Replace concrete walking surface of a stoop at the door of a Localizer facility that has sunken so that the slope of the surface is a hazard in inclement weather. (One place, Finding # 123206)

    - Relocate Engine/Generator set to obtain necessary clearance. (One place, Finding # 120820)

5.3	Constraints The contractor shall coordinate all work with the Systems Support Center (SSC), who will define the hours and protocols for access to each facility. The contractor should be prepared to work irregular or unpredictable hours, and during the evening or night.

5.3.1	SSC Contact Information

- SGF SSC – Contact: Gayle Shields  (417) 868-5611

  - JQX-LOC	Joplin, MO

  - PLK-RCO	Branson, MO

  - ILJ-NDB	Willard, MO

- MCI SSC – Contact:  Curtis Burton  (816) 329-2800

  - MCI-DOT	Kansas City, MO

  - MCI-ATCT	Kansas City, MO

  - MCIE-SX	Kansas City, MO

  - MCI-ATCT	Kansas City, MO

- QUU SSC – Contact:  Rick Stadler  (785) 862-9421

  - QUU-FOE	Topeka, KS

  - QUU-JZM	Lawrence, KS

  - JZM-MM	Lawrence, KS

  - JZM-OM	Lawrence, KS

  - MHK-GS	Manhattan, KS

  - MHK-OM	Manhattan, KS

  - OJC-OM	Olathe, KS

  - QTH-SX	Lawrence, KS

  - TOP-LOC	Topeka, KS

  - TOP-MM	Topeka, KS

- MKC SSC – Contact:  Renae Anderson  (816) 329-2828

  - MKC-MALS	Kansas City, MO

- QUALITY ASSURANCE SURVEILLANCE PLAN

  - Performance Standard The contractor‘s completed work shall comply with

    - U.S. Dept. of Labor 29 CFR 1910 Occupational Safety and Health Standards (“OSHA “ Rules);

    - The NFPA 2005 National Electrical Code; and

    - Site-specific FAA directives and Technical Orders.

  - Acceptable Quality Level The contractor shall comply with

    - Generally accepted commercial standards for workmanship; and

    - Site-specific requirements brought forth by the CO, the COTR, or their designated representatives.

  - Surveillance

    - Surveillance Method The surveillance method shall be a combination of planned and random in-progress inspections, followed by a post-completion Acceptance Inspection Report. The CO and/or the COTR, and/or their designated representative shall make inspections and Acceptance. Designated representatives may include local code enforcement officials or other established experts in the relevant code regulations.

    - Level of Surveillance When the contractor performance is unsatisfactory, or when the performance threshold has been exceeded, the CO or his designate may elect to go to tightened or reduced inspection levels as follows:

      - Normal to Tightened – When normal inspections are in effect, tightened inspection is instituted when work has been rejected on original inspection.

      - Tightened to Normal – When tightened inspections are in effect, normal inspections are instituted when work has been considered acceptable on original inspection.

      - Normal to Reduced – When normal inspections are in effect, reduced inspections are instituted when normal inspections have exceeded the threshold of performance.

    - Surveillance Sample Size Inspection sample size shall be as follows:

      - A ‘Normal Inspection’ will inspect 10% of the volume work completed up to the date of the post-completion inspection.

      - A ‘Reduced Inspection’ will inspect 5 % of work completed up to the date of the post-completion inspection.

      - A ‘Tightened Inspection’ will inspect 30% of work completed up to the date of the post-completion inspection.

    - Evaluation Procedure If an inspection indicates unsatisfactory performance that cannot be resolved verbally between the inspector and the contractor, the inspector may elect to write a Contract Discrepancy Report (CDR) for transmittal to the CO. The Contractor shall be given three working days after notification to correct the unacceptable performance. Following correction completion, a re-examination of any or all areas of non-conformance may be conducted at the discretion of the inspector or CO.

  - Service Delivery Summary (SDS)

| SDS Number and Performance Objective | SOW Paragraph for Standard | Method of Surveillance | Performance Standard |
| --- | --- | --- | --- |
| Finding 97328 | 6.1 | Planned/Random | 100% |
| Finding 97370, | 6.1 | Planned/Random | 100% |
| Finding 120770 | 6.1 | Planned/Random | 100% |
| Finding 120802 | 6.1 | Planned/Random | 100% |
| Finding 120820 | 6.1 | Planned/Random | 100% |
| Finding 123110 | 6.1 | Planned/Random | 100% |
| Finding 123128 | 6.1 | Planned/Random | 100% |
| Finding 123134 | 6.1 | Planned/Random | 100% |
| Finding 123134 | 6.1 | Planned/Random | 100% |
| Finding 123136 | 6.1 | Planned/Random | 100% |
| Finding 123156 | 6.1 | Planned/Random | 100% |
| Finding 123164 | 6.1 | Planned/Random | 100% |
| Finding 123178 | 6.1 | Planned/Random | 100% |
| Finding 123196 | 6.1 | Planned/Random | 100% |
| Finding 123206 | 6.1 | Planned/Random | 100% |
| Finding 123222 | 6.1 | Planned/Random | 100% |
| Finding 132338 | 6.1 | Planned/Random | 100% |
| Finding 137738 | 6.1 | Planned/Random | 100% |
| Finding 137820 | 6.1 | Planned/Random | 100% |

- Places of Performance

  - The work will be performed at FAA facilities in or near the following municipalities:

- Branson, MO (97370)

- Joplin, MO (97328)

- Kansas City, MO (120770, 120802, 120820, 137738, 137820)

- Lawrence, KS (123128, 123134, 123136, 123196)

- Manhattan, KS (123156, 123164)

- Olathe, KS (123178)

- Topeka, KS (123110, 123206,123222)

- Willard, MO (132338)

- Deliverables

After completion of work at each site, the contractor shall obtain a post-completion, signed, site-specific Acceptance Inspection Report from the COTR.

- Schedules and Progress Report

Approximately 10 days after award, the Contractor shall submit a progress schedule indicating how they intend to complete work specified in this SOW within three-months.  Bi-weekly progress reports shall also be submitted, to document work completed and outlining the work planned for completion.

10.0	COTR Designation

###### The Contracting Officer’s Technical Representative (COTR) is delegated this function by the Contracting Officer and will provide technical direction to the contractor supporting this effort.  In addition to the COTR requirements previously established in this SOW, the COTR will coordinate with the contractor to establish the additional level of effort required to support this task during the performance period.

###### 11.0	Invoicing Procedures

11.1	The requirements set forth at AMS Clause 3.3.1-17, Prompt Payment, for the submission of a proper invoice, the contractor shall also submit a separate invoice through the electronic Aeronautical Center Franchise Acquisition Service (ACFAS) website located at:  http://www.franchiseacquisition.faa.gov/ each month representing the percentage of contract completion and any material or supplies furnished.

NOTE:  All problems experienced using the electronic ACFAS website, should be addressed to the ACFAS office, AML-50, at 405-954-1440.

11.2	The contractor shall complete the ACFAS coversheet provided to include the contract number, and the applicable task/delivery order number.  In addition, the following level of information is to be attached in ACFAS:

(1)	Level 1:  A summary sheet that contains the following:

(i)	Contract number, and project title

(ii)	Current amount invoiced and the cumulative value of all invoices to date.

(iii)	A schedule of values listing each task, the monetary value, and materials for the current invoice and the cumulative value.

(2)	Level 2:  Details supporting the information shown on Level 1 is as follows:

(i)	Payrolls with labor listed by person, category, hours, rates, and amounts.

(ii)	Progress Reports

11.3	Payment Address:

FAA, Financial Operations Division (AMZ-100)

6500 South MacArthur Boulevard

P.O. Box 25082

Oklahoma City, OK  73125-4304

12.0	Reference

Safety Abatement Engineering Project document  (Findings) List:

- Finding 97328	2 Pages

- Finding 97370	2 Pages

- Finding 120770 	2 Pages

- Finding 120802	2 Pages

- Finding 120820	2 Pages

- Finding 123110	3 Pages

- Finding 123128	3 Pages

- Finding 123134	3 Pages

- Finding 123136	3 Pages

- Finding 123156	2 Pages

- Finding 123164	3 Pages

- Finding 123178	3 Pages

- Finding 123196	3 Pages

- Finding 123206	4 Pages

- Finding 123222	3 Pages

- Finding 132338	2 Pages

- Finding 137738	4 Pages

- Finding 137820	3 Pages