Tevatron Ionization Profile Monitor (IPM) Buffer Module

10 December 2007

Mark Bowden

Richard Kwarciany

# Introduction

The IPM Buffer module receives data from the IPM QIE front end modules over fast serial optical links.  The data is buffered and then read out through a standard 3.3 Volt PCI interface by a commercial PC.  The difference in maximum input and output rates is approximately 10:1, so at least 10 seconds of data readout time are required for each second of data acquisition, or the data must be compressed/filtered.  Additional time will be required for analysis, depending on the speed of the processor.

IPM Buffer Block Diagram

# Implementation

The IPM system will use 16 optical links to supply data.  Standard optical components are available in 12 channel increments, meaning that two IPM Buffer modules with one optical receiver each will be used.

IPM Buffer PCI Card

## PCI Interface

The IPM Buffer uses the PLX PCI9656 interface.  The PCI9656 runs at 64 bits/ 66MHz on the PCI side but is limited to 32 bit/ 66 MHz operation on the local bus.  The maximum transfer rate is approximately 20 MBytes/sec, although it may be possible to run faster using two cards and transferring bursts of data in a “ping-pong” fashion.

PLX PCI9656

Advantages of the standalone PCI interface are;

1) it is active at power-up, and can be used to program the FPGA through PCI.

2) it has been used in previous Fermilab designs, so the development software exists and has been exercised.

PCI registers will be provided for configuration of the trigger, readout of the data, and diagnostic functions.  In diagnostic mode, all of the main memory is accessible to the PCI host.

## Memory

The IPM Buffer will hold two DDR SODIMM modules for a total of 0.5 GBytes of buffer memory.  This represents approximately 0.4 seconds of continuous data.

The memory is arranged in two banks, with a total bandwidth of 2 GBytes/sec.  This should be sufficient to handle the peak input data rate (1.5 GBytes/sec for 8 channels).

## FPGA

The FPGA chosen for the IPM buffer is the Xilinx XC2VP20.  This device has substantial internal resources (20,000+ registers and 1.5 Mbits of memory), allowing formatting and filtering to be done on-board the Buffer module before data is transferred to the PC.  Each input link is decoupled by a 64 bit wide FIFO and the data is transferred to external memory in blocks of 32 64-bit words (2 KBytes).

## Deserializers

The deserializers are included in the FPGA and are capable of accepting data rates in the range of 600-3000 Mbps.   They require a local reference clock with a frequency very near  (+/- 100 ppm) the intended data rate for initial lock.  Following the initial frequency lock, the deserializers will relock to the actual frequency of the incoming data.

The local reference clock is provided by a crystal oscillator.

For reliable link operation, the data transmitter should run at a rate slightly faster than the required data transfer rate.  This will cause insertion of an occasional idle character in the data stream, which helps to maintain word alignment in the receiver.

On command, the transmitter should also have the capability of sending a specific sync word (8B/10B comma character) for a period of at least 20 usec to establish receiver word synchronization.

All transmitters connected to the same IPM Buffer should operate at the same data rate (+/- 100 ppm).

## Optical Links

The IPM data sources are assumed to use multimode (850 nm) optics.  The transmitter connector type is not specified, since fanout cables are available in most common types.

Optical Receiver(s)

The receive end of the optical link uses the MTP/MPO style 12 channel connector.  The receiver(s) are Infineon V23832R devices (second source Molex 86991).  These receivers use a BGA array connector and are removable.

MTP (12 channel) parallel fiber

At the source end of the optical cable the 12 parallel fibers are split into individual fibers using either a short fanout adapter cable, or a fiber cassette.

Parallel fiber fanout cable.

# Functional Description

Figure 1

Fiber Reciever

Referring to Figure 1, the Fiber Receivers are actually one discrete component which convert the optical input to a CML differential signal.  The Infineon V23832R device used is a 12 channel device.  Eight of the 12 channels are used in this implementation.  Channels 8 through 11 are not connected.

SERDES

Each CML input channel is deserialized by a SERDES device internal to the FPGA. The SERDES produces a 16-bit wide parallel data stream.

FIFO

A two-stage FIFO memory on each input channel allows decoupling of the link clocks from the FPGA’s clock, and also formatting of the incoming data into 64-bit wide data frames.  The FIFOs are large enough to allow the data from all 8 serial links to be synchronized to each other.  Since data on the links is organized into frames, synchronization of the eight links with each other is accomplished by comparing the frame header information on the links.

Trigger / Data Filter

Configured through registers in the PCI interface, the Trigger / Data Filter block allows for selective acquisition of data from the front end electronics.  Up to 318 samples per turn can be stored by populating the sample masks through PCI.  For each bit set true in the mask, data at that sample will be forwarded to the Memory Controller block for storage in memory.  Individual channels are enabled or disabled in the Channel Mask Register.  All data is stored if Data Filtering is disabled.

The Trigger / Data Filter block also controls triggering of data acquisition.  The trigger logic is configured through PCI registers, and allows for saving a preset number of turns after an injection marker, or after a software data acquisition start command is issued.  To acquire a preset number of turns, the number of turns is set in the N Turns register, then the N Turn Enable bit is set in the CSR register.

Counters

The Counters block contains the Proton sample counter, the Pbar sample counter, and the Turn counter.  The Proton sample counter is a modulo-318 counter that is reset by the proton marker bit in the data header, and incremented on each sample.  The Pbar sample counter is similar, but is reset by the pbar marker bit.  The Turn counter is a 16-bit counter that is reset by the injection marker bit, and increments when the proton counter wraps to zero.  The values of each of the three counters is added to the header information and stored with the data during data acquisition.

Memory Controller

The Memory Controller block provides for initialization and control of the DDR SDRAM memory that is external to the FPGA.  The memory controller itself is internal to the FPGA.  Write and Read requests are entertained from either the PCI interface, or from the Trigger / Data Filter blocks, depending on which mode the IPM Buffer is in.  The mode is controlled via a bit in the CSR register.  Two modes are defined.  Acquisition Mode, and Readout Mode.  When in Acquisition Mode, the Trigger / Data Filter block has exclusive access to the DDR SDRAM, and read attempts from PCI return DEADBEEF.  Write attempts are ignored.  When in Readout Mode, the PCI interface has exclusive access to the DDR SDRAM, and data from the input links is not stored.

Main Memory

The main memory is discrete from the FPGA, and consists of two 256 MByte DDR SDRAM SODIMM modules.  Each module is treated as a separate bank by the Memory Controller block, but is accessed as one large bank via PCI.  Main memory can be read or written via PCI when the IPM Buffer is in Readout Mode.  Placing the module into Acquisition Mode allows data from the input links to be stored in Main Memory.

PCI Interface

The PCI interface is a dedicated PCI interface device that is discrete from the FPGA chip on the board.  It supports 64-bit, 66 MHz PCI.

## Diagnostic Features

Loopback Data Generator.

Each input serial link is equipped with a pattern generator that can be configured to transmit a known data pattern into the serial input.  When enabled data frames of the required format are generated with an incrementing pattern to allow for confidence testing of the high speed serial links.  The data generator transmits the following pattern:

Force Error Registers

To facilitate error reporting software development, the IPM Buffer module can be programmed to generate false error conditions.  These error conditions are reported in the Link Error registers.  Each of the individual links can be programmed to generate one or all of the 10 link error conditions by setting the mask bits in the Link Force Error Register.

Front End Diagnostic Mode

To facilitate debugging of front end boards, the IPM Buffer can be put into Front End Diagnostic Mode.  When in this mode, raw footer data from the lowest four channel front end boards is copied into the IPM Buffer memory frame in place of the data for the highest four channel front end boards.  Front End Diagnostic Mode is enabled by setting the Front End Diagnostic Mode bit in CSR0.

## Input Data Optical Connector

The Input Data Optical Connector accepts a 12-fiber ribbon with an MTP connector.  Fibers are numbered 0 – 11 with fiber 0 being defined as the bottom fiber when facing the IPM Buffer card from the rear of the host PC.  Only fibers 0 through 7 are used in the IPM Buffer Module.  Fibers 8 through 11 are not used.

The FONetworks 12-fiber breakout adapter breaks the fiber ribbon out into 12 individual fibers with LC type connectors.  The individual fibers are color coded as follows.

| Fiber Color | Fiber Number |
| --- | --- |
| Dark Blue | Fiber 0 |
| Orange | Fiber 1 |
| Green | Fiber 2 |
| Brown | Fiber 3 |
| Gray | Fiber 4 |
| White | Fiber 5 |
| Red | Fiber 6 |
| Black | Fiber 7 |
| Yellow | Fiber 8 |
| Purple | Fiber 9 |
| Pink | Fiber 10 |
| Light Blue | Fiber 11 |

## Input Data Format

Link data received from the font-end boards adheres to the following encoding scheme:

IPM Buffer accepts data in the format above only.  Data frames consist of seven contiguous 32-bit data words.  Each frame contains data for three time slices, identified by the capID bits.  Data frames may have fill characters between them, but a frame error will be set if fill a character occurs within a frame.  Once each link’s SERDES is locked, at least one fill character is required for IPM Buffer to frame synchronize, but once synchronized, a string of data frames with no fill character separating them is allowed.  It is recommended that a fill character be added between data frames occasionally to allow IPM Buffer to check for synchronization errors.  A counter is implemented to flag an error if a fill character is not received for more than approximately 100 contiguous data words.

IPM Buffer deserializers accept any 32-bit k character sequence as a fill character, but for deserializer clock correction, the clock correction sequence should be transmitted approximately every 5000 bytes.  This allows the deserializer to add or remove clock correction characters as necessary to compensate for small clock rate differences between the transmitter and the receiver.  The defined clock correction sequence for IPM Buffer is:

k28.5 d16.2 k28.5 d5.6 .

Data in the frame is defined as follows:

QIEx		Front End QIE pseudo exponential data.

CAPID	Two bit CAPID number from QIE chip.

Mode		Two bit Mode identifier from the QIE chip.  Defined modes are as

follows:

- Calibration

- Normal

- Debug/Testing

- RESET Marker

Timing Bits	Four front end timing bits defined as follows:

- Proton Injection

- PBar Injection

- Proton Marker

- PBar Marker

Error Bits	The following front end error bits are defined:

- – 25  Unused.

- PLL Lock Fail in Timeslice 2

- PLL Lock Fail in Timeslice 1

- PLL Lock Fail in Timeslice 0

- CAPID error in Timeslice 2

- CAPID error in Timeslice 1

- CAPID error in Timeslice 0

- FIFO Full in Timeslice 2

- FIFO Full in Timeslice 1

16  FIFO Full in Timeslice 0

Counter Data	16-bit counter increments on each timeslice.  This results in a

count value incrementing by three for each data frame.

## Memory Data Format

Data from the eight input links is combined and stored in main memory in 80 byte frames.  Each frame contains data from one timeslice.

Memory Data Frame Format

63 0

Header Low

Header High

Link 0 Data

Link 1 Data

Link 2 Data

Link 3 Data

Link 4 Data

Link 5 Data

Link 6 Data

Link 7 Data

Header Low

| 63 – 56 | 55 – 54 | 53 – 52 | 51 | 50 | 49 - 41 | 40 - 32 |
| --- | --- | --- | --- | --- | --- | --- |
| PLL Lock Error | QIE Mode | Cap ID | Inter Board Sync Error | 0 | Proton Counter | PBar Counter |

| 31 – 24 | 23 – 16 | 15 – 0 |
| --- | --- | --- |
| FIFO Full Error | Cap ID Error | Turn Counter |

Header High

| 63 – 56 | 55 – 48 | 47 – 40 | 39 – 32 | 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Counter Sync Error | Frame Error | QIE Mode Sync Error | Cap ID Sync Error | Proton Injection Error | PBar Injection Error | Proton Marker Error | PBar Marker Error |

Header error bits in eight bit blocks contain one error bit for each link, with the lowest significant bit corresponding to the error occurring in link 0, the next lowest in link 1, etc.

Link x Data

QIE Data can be stored in Raw format (exactly as received from the front end board), or converted to an integer value using the conversion lookup table.  The conversion lookup table is loaded and enabled through PCI (see: PCI Interface), and when enabled, causes the IPM Buffer to store an eight bit integer value into memory, instead of seven bit pseudo exponential value for each QIE channel.

Link x Data (RAW)

| 63 – 60 | 59 – 58 | 57 – 56 | 55 - 47 | 48 - 42 | 41 - 35 | 34 - 32 |
| --- | --- | --- | --- | --- | --- | --- |
| Timing | QIE Mode | Cap ID | QIE 7 | QIE 6 | QIE 5 | QIE 4 (high) |

| 31 – 28 | 27 – 21 | 20 – 14 | 13 – 7 | 6 – 0 |
| --- | --- | --- | --- | --- |
| QIE 4 (high) | QIE 3 | QIE 2 | QIE 1 | QIE 0 |

Link x Data (Integer Conversion Enabled)

| 63 – 56 | 55 – 48 | 47 – 40 | 39 – 32 | 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| QIE 7 | QIE 6 | QIE 5 | QIE 4 | QIE 3 | QIE 2 | QIE 1 | QIE 0 |

Memory Data Frame Format when in Front End Diagnostic Mode

63 0

Header Low

Header High

Link 0 Data

Link 1 Data

Link 2 Data

Link 3 Data

Link 0 RAW Front End Footer Data

Link 1 RAW Front End Footer Data

Link 2 RAW Front End Footer Data

Link 3 RAW Front End Footer Data

Link x RAW Front End Footer Data

| 63 – 56 | 55 – 48 | 47 – 40 | 39 – 32 |
| --- | --- | --- | --- |
| Frame Error, Hard Trigger and FE Init | Time Slice 2 Timing Mode and CapID | Time Slice 1 Timing Mode and CapID | Time Slice 0 Timing Mode and CapID |

31 – 0

RAW Front End Footer

Frame Error,  Hard Trigger, and Front End Init

| 63 | 62 | 61 | 60 – 56 |
| --- | --- | --- | --- |
| Frame Error | Hard Trigger | Front End Init | Unused (0x00000) |

Time Slice x Timing Mode and CapID

| 7 | 6 | 5 | 4 | 3 – 2 | 1 – 0 |
| --- | --- | --- | --- | --- | --- |
| Proton Inj | PBar Inj | Proton Marker | PBar Marker | Mode | CapID |

## Interboard Synchronization

The IPM Buffer provides a mechanism for ensuring synchronization between two boards in the same host system.  Connector J2 (top of pc board) provides for this function.  A 20-pin ribbon cable jumper must be connected between the J2 connectors of the two boards.  Once connected, one of the boards is designated the slave in software by setting the Interboard Slave Enable bit in the CSR register.  The other board is designated the master by setting the Interboard Master Enable bit in the CSR register.  Once properly configured and connected, the master IPM Buffer compares its low Proton Counter bits with those of the slave board.  Any errors are flagged in bit 51 of the data frame header on the master board.  Note that due to the time needed to do the compare, the error flag may not show true until the time slice frame after it actually occurs.  The master also passes the acquisition enable signal to the slave.

## PCI Interface

CAUTION:  The IPM Buffer board supports 3.3-Volt PCI ONLY.  The board will physically fit into a 5-Volt PCI slot, but powering a system with an IPM Buffer module in a 5-Volt slot WOULD BE BAD.  Fatal damage to the IPM Buffer, the system motherboard, power supply, or all of the above will result if attempted.

Note that 3.3 Volt PCI slots can be identified by the location of the key in the slot.  3.3 Volt PCI slots have the key near the back panel of the system, whereas 5 Volt PCI slots have the key nearest the end of the connector that is farthest from the back panel of the system.  See figure above.

The following PCI registers are defined:

PCI Configuration Space:

| 00h | Device ID / Vendor ID (9656 10B5) |
| --- | --- |
| 04h | Status / Command |
| 08h | Class Code / Rev ID (068000AD) |
| 10h | Base Address of Memory access to PLX registers (PCIBAR0) |
| 14h | Base Address of I/O access to PLX registers (PCIBAR1) |
| 18h | Base Address of Memory access to Readout Data Window (PCIBAR2) |
| 1Ch | Base Address of I/O Space access to IPM CSR register block (PCIBAR3) |
| 20h | Reserved |
| 24h | Reserved |
| 28h | Reserved |
| 2Ch | PCI Subsystem ID / PCI Subsystem Vendor ID (24400003) |
| 30h – 53h | Reserved (do not write) |

I/O space (I/O Base = contents of PCIBAR1):

| I/O Base + 00h | Control-Status register |
| --- | --- |
| I/O Base + 04h | Memory window page register |
| I/O Base + 08h | Master Link Select Mask / Trigger Mask |
| I/O Base + 0Ch | Event Data Address Counter register |
| I/O Base + 10h | SERDES Control 0 |
| I/O Base + 14h | SERDES Control 1 |
| I/O Base + 18h | Link Status Register |
| I/O Base + 1Ch | N Turn Count |
| I/O Base + 20h | Link Error Register 0 |
| I/O Base + 24h | Link Error Register 1 |
| I/O Base + 28h | Link Error Register 2 |
| I/O Base + 2Ch | Link Error Register 3 |
| I/O Base + 30h | Link Diagnostic Register |
| I/O Base + 34h | Peak Select Register |
| I/O Base + 38h | Peak 31 to 0 |
| I/O Base + 3Ch | Peak 63 to 32 |
| I/O Base + 40h – I/O Base + ACh | Reserved (DEADBEEF) |
| I/O Base + B0h | Running Sum Select |
| I/O Base + B4h – I/O Base + BCh | Reserved (DEADBEEF) |
| I/O Base + C0h | Running Sum 0 |
| I/O Base + C4h | Running Sum 1 |
| I/O Base + C8h | Running Sum 2 |
| I/O Base + CCh | Running Sum 3 |
| I/O Base + D0h | State Machine Low |
| I/O Base + D4h | State Machine Mid |
| I/O Base + D8h | State Machine High |
| I/O Base + DCh – I/O Base + ECh | Reserved (DEADBEEF) |
| I/O Base + F0h | Firmware ID code (date in mmddyyyy format) |
| I/O Base + F4h | FPGA Firmware JTAG TDO bit |
| I/O Base + F8h | IPM Buffer FIFO Full Error Flags |
| I/O Base + FCh | Reserved (DEADBEEF) |
| I/O Base + 100h | Proton Mask Register 0 (proton mask bits 31 to 0) |
| I/O Base + 104h | Proton Mask Register 1 (proton mask bits 63 to 32) |
| I/O Base + 108h | Proton Mask Register 2 (proton mask bits 95 to 64) |
| I/O Base + 10Ch | Proton Mask Register 3 (proton mask bits 127 to 96) |
| I/O Base + 110h | Proton Mask Register 4 (proton mask bits 159 to 128) |
| I/O Base + 114h | Proton Mask Register 5 (proton mask bits 191 to 160) |
| I/O Base + 118h | Proton Mask Register 6 (proton mask bits 223 to 192) |
| I/O Base + 11Ch | Proton Mask Register 7 (proton mask bits 255 to 224) |
| I/O Base + 120h | Proton Mask Register 8 (proton mask bits 287 to 256) |
| I/O Base + 124h | Proton Mask Register 9 (proton mask bits 317 to 288) |
| I/O Base + 128h – 13Ch | Reserved |
| I/O Base + 140h | PBar Mask Register 0 (PBar mask bits 31 to 0) |
| I/O Base + 144h | PBar Mask Register 1 (PBar mask bits 63 to 32) |
| I/O Base + 148h | PBar Mask Register 2 (PBar mask bits 95 to 64) |
| I/O Base + 14Ch | PBar Mask Register 3 (PBar mask bits 127 to 96) |
| I/O Base + 150h | PBar Mask Register 4 (PBar mask bits 159 to 128) |
| I/O Base + 154h | PBar Mask Register 5 (PBar mask bits 191 to 160) |
| I/O Base + 158h | PBar Mask Register 6 (PBar mask bits 223 to 192) |
| I/O Base + 15Ch | PBar Mask Register 7 (PBar mask bits 255 to 224) |
| I/O Base + 160h | PBar Mask Register 8 (PBar mask bits 287 to 256) |
| I/O Base + 164h | PBar Mask Register 9 (PBar mask bits 317 to 288) |
| I/O Base + 168h – 1FCh | Reserved |
| I/O Base + 200h – I/O Base + 3FFh | QIE Conversion Lookup Table |

Status / CSR Register (offset x00)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Status (x0000) | Control |

Bit 31 – 28	RO   Module Status (currently undefined x0000).

Bit 27		RO   IRQ On

Bit 26 – 16	RO   Module Status (currently undefined 00000000000).

Bit 15		WO  Master Reset (Reset all of FPGA including SERDES and link FIFOs)

Bit 14		R/W   Clear Errors

Bit 13		R/W   Clear IRQ

IRQ Enabled when low.

Bit 12		R/W   Force IRQ

When Bit 13 is low and 12 is high, the PCI Interrupt output is driven true.

Bit 11		R/W   Clear latched IRQ Status bit.

Bit 10		WO   Soft Reset (Reset all of FPGA except SERDES and link FIFOs)

Bit 9 – 8	RO   Unused (00).

Bit 7		R/W   Inter-Board Master Enable.

When high, board is placed into master mode for interboad

Synchronization error checking.  In master mode, the board receives the inter-board data and strobe signals.  The Acquisition Enable signal is driven.  When low, The Acquisition Enable signal is tri-stated.

Bit 6		R/W   Front End diagnostic mode enabled.  When high, raw footer data

from the front end modules on links 0 - 3 is written into the memory frame

in the place of the data for links 4 – 7.  In diagnostic mode, data from links

4 – 7 is not available.

Bit 5		R/W   RAW Mode Enable.  When high, enables true RAW mode.  Data

from front end modules is stored in same format as received.  Note that

RAW mode is only available when Conversion Enable is not enabled.  If

Conversion Enable is true, the RAW Mode Enable bit has no affect.

Bit 4		R/W   Inter-Board Slave Enable.

When high, board is placed into slave mode for interboard

synchronization error checking.  In slave mode, the board drives the

inter-board outputs, and applies its proton counter to them.  In slave mode,

Data Acquisition begins when the Acquisition Enable input goes true.

When the Inter-Board Slave Enable bit is low, the inter-board data and

Strobe outputs are tri-stated.

Bit 3		R/W   NTurn Enable

When high, a trigger will cause the number of turns stored in the N Turn

Count Register to be stored.

Bit 2		R/W   Sparsification Enable.

When high, Sparsification mode is enabled.  Only samples indicated in the

Proton or PBar masks will be stored.

Bit 1		R/W   Conversion Enable.

When high, the QIE conversion lookup table is enabled.  Raw QIE data

is used as an index into the conversion table.  The output of the conversion

table is stored in memory.  When low, raw QIE data is stored.

Bit 0		R/W   Acquisition Enable.

When high, the DAQ state machine controls the DDR memory.  Data

from the input links is stored.  PCI access to the DDR memory is

blocked.  When low, PCI access of the DDR memory is enabled.

Data from the Input links is not stored.  Note that this bit is only functional when in master mode.  When in slave mode, Acquisition Enable is passed over the interboard link from the Master board.

DDR Memory Page Register (offset x04)

| 31 - 29 | 28 – 20 | 19 - 0 |
| --- | --- | --- |
| 000 | Page | 0000000000000000000 |

Master Link Select Mask / Trigger Mask (offset x08)

| 31 – 24 | 23 - 16 | 15 – 4 | 3 - 0 |
| --- | --- | --- | --- |
| x00 | Master Link Select Mask | x000 | Trigger Mask |

Bit 31 – 24	RO   Unused (x00)

Bit 23		R/W   Select Link 7 as Master Link

When high, IPM buffer’s front end counter synchronizes itself to the

front end counter of this link.  Only one link may be selected as master.

Bit 22		R/W   Select Link 6 as Master Link

Similar to bit 23 for Link 6.

Bit 21		R/W   Select Link 5 as Master Link

Similar to bit 23 for Link 5.

Bit 20		R/W   Select Link 4 as Master Link

Similar to bit 23 for Link 4.

Bit 19		R/W   Select Link 3 as Master Link

Similar to bit 23 for Link 3.

Bit 18		R/W   Select Link 2 as Master Link

Similar to bit 23 for Link 2.

Bit 17		R/W   Select Link 1 as Master Link

Similar to bit 23 for Link 1.

Bit 16		R/W   Select Link 0 as Master Link

Similar to bit 23 for Link 0.

Bit 3		R/W   Proton Injection Bit

When high, acquisition triggers on receipt of a Proton Injection flag from

the front end.

Bit 2		R/W   PBar Injection Bit

When High, acquisition triggers on receipt of a PBar Injection flag from

the front end.

Bit 1		R/W   Proton Marker Bit

When High, acquisition triggers on receipt of a Proton Marker flag from

the front end.

Bit 0		R/W   PBar Marker Bit

When High, acquisition triggers on receipt of a PBar Marker flag from

the front end.

DDR Address Counter Register (offset x0C)

| 31 – 29 | 19 - 0 |
| --- | --- |
| Unused | Address Counter |

Bit 31 – 29	RO   Unused (000).

Bit 19 – 0	R/W   Address Counter Register.

When written, causes DAQ to begin writing at this address when

acquisition is enabled.  When read, shows the next address to be

written by the DAQ state machine.  Note that since DAQ state machine

always writes 64-bit words, low three bits are always zero.

SERDES Control 0 (offset x10)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| PowerDown | TXInhibit | RXReset | TXReset |

Bit 31 – 24	R/W   Power Down.

When high, powers off corresponding SERDES.

Bit 23 – 16	R/W   TX Inhibit.

When high, corresponding SERDES transmit is disabled.

Bit 15 – 8	R/W   RX Reset.

When high, corresponding SERDES receiver is in reset.

Bit 7 – 0	R/W   TX Reset.

When high, corresponding SERDES transmitter is in reset.

SERDES Control 1 (offset x14)

| 31 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- |
| Loopback Control | TX Pattern Enable | Link Enable |

Bit 31 – 16	R/W   SERDES loopback control.

Note that each SERDES uses two bits for loopback control.  Bits 17 and

16 correspond to SERDES 0 and so on.  The truth table for loopback

control is;  00 = Normal non-loopback mode, 01 = Parallel loopback

mode, 10 = Serial loopback mode.  Mode 11 is undefinded.

Bit 15 – 8	R/W   TX Pattern Enable.

When high SERDES Transmit pattern generator is enabled for

corresponding link.

Bit 7 – 0	R/W   Link Enable.

When high, corresponding link is enabled.

Link Status Register (offset x18)

| 31 – 26 | 25 – 24 | 23 – 16 | 15 – 8 | 7 - 0 |
| --- | --- | --- | --- | --- |
| 000000 | Paroli | Link Data Activity | Frame Locked | SERDES Locked |

Bit 31 – 26	RO  Unused (000000).

Bit 25		RO  Paroli Power bad latched.

Set by Paroli optical power on link 0 falling below minimum required for

reliable data transmission.  Cleared by Clear Errors bit, Reset bit, or hard

Reset.

Bit 24		Paroli Power good.

Not latched.  High if Paroli link 0 optical power is above the minimum

threshold required for reliable data transmission.  Low if not.

Bit 23 – 16	Link Data Activity.

High if data is being received on corresponding input link.

Bit 15 – 8	Frame Locked.

When high, IPM data frames are being received and the IPM buffer input

state machine for the corresponding link recognizes the frame as a valid

IPM frame.

Bit 7 – 0	SERDES Locked.

When high the input SERDES for the corresponding link is locked onto

the 8b-10b data received from the front end.  Data does not have to be

valid IPM data for SERDES lock to be true.

N Turn Count Register (offset x1C)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Unused | N Turn Count |

Bit 31 – 16	RO  Unused (x0000).

Bit 15 – 0	R/W   N Turn Count Register.

Sets the number of turns stored after a trigger.

Link Error 0 Register (offset x20)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Illegal Character latched | Comma Error Latched | Frame Error Latched | SERDESLock Error Latched |

Bit 31 – 24	RO   Illegal Character Latched.

Set high for corresponding link when SERDES has received an illegal

character.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 23 – 16	RO   Comma Error Latched.

Set high for corresponding link when a comma character has not been received for more than 100 words.  Cleared by the Clear Errors Bit, Reset bit, or hard reset.

Bit 15 – 8	RO   Frame Error Latched.

Set high for corresponding link when the link control state machine

detects an IPM frame error.  IPM frames are defined as seven consecutive

32-bit data words.  One or more comma characters between frames is

optional as long as at least one comma is received at least every 100

words.

Bit 7 – 0	RO   SERDES Lock Error Latched.

Set high for corresponding link when the SERDES looses lock.  Cleared

by Clear Errors bit, Reset bit, or hard reset.

Link Error 1 Register (offset x24)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Proton Marker Error Latched | PBar Marker Error Latched | QIE Mode Error Latched | Link Frame Error |

Bit 31 – 24	RO   Proton Marker Error Latched.

Set high for corresponding link when the Proton Marker bit does not agree

with other links.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 23 – 16	RO   PBar Marker Error Latched.

Set high for corresponding link when PBar Marker bit does not agree with

other links.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 15 – 8	RO   QIE Mode Error Latched.

Set high for corresponding link when QIE Mode bit does not agree with

other links.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 7 – 0	RO   Link Frame Error.

High for corresponding link when the link control state machine has

detected an IPM frame error.

Link Error 2 Register (offset x28)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| FIFO Full Error Latched | Cap ID Error Latched | Proton Injection Error Latched | PBar Injection Error Latched |

Bit 31 – 24	RO   FIFO Full Error Latched.

Set when the data link FIFO for the corresponding link reaches the full

state.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 23 – 16	RO   Cap ID Error Latched.

Set for corresponding link when front end logic has detected a CAP ID

Error.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 15 – 8	RO   Proton Injection Error latched.

Set for corresponding link when Proton Injection bit does not agree with

other links.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Bit 7 – 0	RO   PBar Injection Error Latched.

Set for corresponding link when PBar bit does not agree with other links.

Cleared by Clear Errors bit, Reset bit, or hard reset.

Link Error 3 Register (offset x2C)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Cap ID Sync Error Latched | QIE Mode Error Latched | Counter Error Latched | PLL Lock Error Latched |

Bit 31 – 24	RO   Cap ID Sync Error Latched.

Set for corresponding link when Cap ID value does not match value in other links.  Note that the Cap ID values must match for at least four links for these values to be valid.  If the Cap ID values do not match for at least four links, then error bits will be set, but it is not possible to determine which are errors and which are not.  Latched errors are cleared by the Clear Errors bit, Reset bit, or a hard reset.

Bit 23 – 16	RO   QIE Mode Error Latched.

Set for corresponding link when the QIE Mode value does not match the QIE Mode value in other links.  Note that the QIE Mode values must match for at least four links for these values to be valid.  If the QIE Mode values do not match for at least four links, then error bits will be set, but it is not possible to determine which are errors, and which are not.  Latched errors are cleared by the Clear Errors bit, Reset bit or a hard reset.

Bit 15 – 8	RO   Counter Error.

Set for corresponding link when front end counter value does not match

IPM Buffer counter value.  Cleared by Clear Errors bit, Reset bit, or hard

reset.

Bit 7 – 0	RO   PLL Lock Error Latched.

Set for corresponding link when front end logic has detected a PLL Lock

Error.  Cleared by Clear Errors bit, Reset bit, or hard reset.

Link Diagnostic (Force Error) Register (offset x30)

| 31 – 24 | 23 – 16 | 15 – 11 | 10 - 0 |
| --- | --- | --- | --- |
| Unused | Link Select | Unused | Force Error Mask |

Bit 31 – 24	RO   Unused (x00).

Bit 23 – 16	R/W   Link Select.

When high, corresponding link will generate error selected in Force Error

Mask.

Bit 15 – 11	RO   Unused (00000).

Bit 10 – 0	R/W   Force Error Mask.

Bit 10		Force CAP ID Sync Error.

Bit 9		Force Counter Error.

Bit 8		Force PLL Lock Error.

Bit 7		Force FIFO Full Error.

Bit 6		Force CAP ID Error.

Bit 5		Force Proton Injection Error.

Bit 4		Force PBar Injection Error.

Bit 3		Force Proton Marker Error.

Bit 2		Force PBar Marker Error.

Bit 1		Force QIE Mode Error.

Bit 0		Force Frame Error.

Peak Select Register (offset x34)

| 31 - 24 | 23 - 21 | 20 - 18 | 17 - 15 | 14 - 12 | 11 - 9 | 8 - 6 | 5 - 3 | 2 - 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Unused (x00) | Link7 | Link6 | Link5 | Link4 | Link3 | Link2 | Link1 | Link0 |

Bit 31 – 24	RO Unused (x00)

Bit 23 – 21	R/W  Peak Select for Link 7.  Select one of the eight channels on

Link 7 for Peak Finder to connect to.  Setting Bits 23 – 21 to b000

results in Link 7 channel 0 connected to the Peak Finder for Link 7.

A binary value of 001 connects Link 7 channel 1 to the Link 7 Peak

Finder, and so on.

Bit 20 – 18	R/W  Peak Select for Link 6.  Functions similarly to the Peak Select

for Link 7.

Bit 17 – 15	R/W  Peak Select for Link 5.  Functions similarly to the Peak Select

for Link 7.

Bit 14 – 12	R/W  Peak Select for Link 4.  Functions similarly to the Peak Select

for Link 7.

Bit 11 – 9	R/W  Peak Select for Link 3.  Functions similarly to the Peak Select

for Link 7.

Bit 8 – 6	R/W  Peak Select for Link 2.  Functions similarly to the Peak Select

for Link 7.

Bit 5 – 3	R/W  Peak Select for Link 1.  Functions similarly to the Peak Select

for Link 7.

Bit 2 – 0	R/W  Peak Select for Link 0.  Functions similarly to the Peak Select

for Link 7.

Peak 31 – 0 (offset x38)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Peak Link 3 | Peak Link 2 | Peak Link 1 | Peak Link 0 |

Bit 31 – 24	RO  Peak value for the Link 3 Peak Finder.

Bit 23 - 16	RO  Peak value for the Link 2 Peak Finder.

Bit 15 - 8	RO  Peak value for the Link 1 Peak Finder.

Bit 7 - 0	RO  Peak value for the Link 0 Peak Finder.

The Peak Finder in each link returns the peak value of the last completed turn for the channel it is connected to.  This value for links 0 through 3 can be read in the above bit fields.

Peak 63 - 32 (offset x3C)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Peak Link 7 | Peak Link 6 | Peak Link 5 | Peak Link 4 |

Bit 31 – 24	RO  Peak value for the Link 7 Peak Finder.

Bit 23 - 16	RO  Peak value for the Link 6 Peak Finder.

Bit 15 - 8	RO  Peak value for the Link 5 Peak Finder.

Bit 7 - 0	RO  Peak value for the Link 4 Peak Finder.

The Peak Finder in each link returns the peak value of the last completed turn for the channel it is connected to.  This value for links 4 through 7 can be read in the above bit fields.

Running Sum Select (offset xB0)

| 31 – 28 | 27 – 24 | 23 – 20 | 19 – 16 | 15 – 12 | 11 – 8 | 7 – 4 | 3 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Link7 | Link6 | Link5 | Link4 | Link3 | Link2 | Link1 | Link0 |

Bit 31 – 28	R/W   Running Sum Select for Link 7.  Selects which of the eight QIE

channels on link 7 to connect to the Link 7 running sum counter.  Valid

codes are 0 – 7.  Codes 8 – 15 are reserved.

Bit 27 – 24	R/W   Running Sum Select for Link 6.

Bit 23 – 20	R/W   Running Sum Select for Link 5.

Bit 19 – 16	R/W   Running Sum Select for Link 4.

Bit 15 – 12	R/W   Running Sum Select for Link 3.

Bit 11 –  8	R/W   Running Sum Select for Link 2.

Bit  7  –  4	R/W   Running Sum Select for Link 1.

Bit  3  –  0	R/W   Running Sum Select for Link 0.

Running Sum 0 (offset xC0)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Link 1 | Link 0 |

Bit 31 – 16	RO   Running Sum value for Link 1.

Bit 15 – 0	RO   Running Sum value for Link 0.

Running Sum 1 (offset xC4)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Link 3 | Link 2 |

Bit 31 – 16	RO   Running Sum value for Link 3.

Bit 15 – 0	RO   Running Sum value for Link 2.

Running Sum 2 (offset xC8)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Link 5 | Link 4 |

Bit 31 – 16	RO   Running Sum value for Link 5.

Bit 15 – 0	RO   Running Sum value for Link 4.

Running Sum 3 (offset xCC)

| 31 – 16 | 15 – 0 |
| --- | --- |
| Link 7 | Link 6 |

Bit 31 – 16	RO   Running Sum value for Link 7.

Bit 15 – 0	RO   Running Sum value for Link 6.

State Machine Low (offset xD0)

| 31 – 24 | 23 – 16 | 15 – 8 | 7 – 0 |
| --- | --- | --- | --- |
| Event DDR Address | Event DDR Data | PCI DDR Cache | PCI DDR State |

Bit 31 – 24	RO   Instantaneous value of the Event DDR Address State Machine.

Bit 23 – 16	RO   Instantaneous value of the Event DDR Data State Machine.

Bit 15 – 8	RO   Instantaneous value of the PCI DDR Cache Controller State

Machine.

Bit 7 – 0	RO   Instantaneous value of the PCI DDR State Machine.

State Machine Mid (offset xD4)

| 31 – 10 | 9 – 8 | 7 – 4 | 3 – 0 |
| --- | --- | --- | --- |
| Unused (zeros) | DDR Controler Write State | DDR Controller Read State | DDR Controller State |

Bit 9 – 8	RO   Instantaneous value of the DDR Controller Write State Machine.

Bit 7 – 4	RO   Instantaneous value of the DDR Controller Read State Machine.

Bit 3 – 0	RO   Instantaneous value of the DDR Controller State Machine.

State Machine High (offset xD8)

| 31 – 28 | 27 – 24 | 23 – 20 | 19 – 16 | 15 – 12 | 11 – 8 | 7 – 4 | 3 – 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Link 7 | Link 6 | Link 5 | Link 4 | Link 3 | Link 2 | Link 1 | Link 0 |

Bit 31 – 28	RO   Instantaneous value of the Link 7 state machine.

Bit 27 – 24	RO   Instantaneous value of the Link 6 state machine.

Bit 23 – 20	RO   Instantaneous value of the Link 5 state machine.

Bit 19 – 16	RO   Instantaneous value of the Link 4 state machine.

Bit 15 – 12	RO   Instantaneous value of the Link 3 state machine.

Bit 11 –  8	RO   Instantaneous value of the Link 2 state machine.

Bit  7  –  4	RO   Instantaneous value of the Link 1 state machine.

Bit  3  –  0	RO   Instantaneous value of the Link 0 state machine.

Firmware ID (offset xF0)

| 31 – 24 | 23 – 16 | 15 – 0 |
| --- | --- | --- |
| Month | Day | Year |

Bit 31 – 24	RO   Firmware revision month in BCD.

Bit 23 – 16	RO   Firmware revision day in BCD.

Bit 15 – 0	RO   Firmware revision year in BCD.

FPGA Firmware JTAG TDO bit (offset xF4)

| 31 – 1 | 0 |
| --- | --- |
| Unused (all zeros) | TDO |

Bit 31 – 1	RO   Unused (all zeros)

Bit 0		RO   FPGA Firmware JTAG TDO bit

IPM Buffer FIFO Full Error Flags (offset xF8)

| 31 - 29 | 28 – 0 |
| --- | --- |
| 000 | FIFO Full Error Flags |

Bit 31 – 29	RO  Unused (zeros)

Bit 28		RO  DDR Output (to external memory) Data FIFO Full Error

Bit 27		RO  DDR Command FIFO Full Error

Bit 26		RO  DDR Input (from external memory) Data FIFO Full Error

Bit 25		RO  PCI to DDR Data FIFO Full Error

Bit 24		RO  PCI to DDR Address FIFO Full Error

Bit 23 – 16	RO  Link Formatted Data FIFO Full Error

Bit 15 – 8	RO  Link Formatted Footer FIFO Full Error

Bit 7 – 0	RO  Link RAW Data FIFO Full Error

FIFO Full Error flags should not set under normal running conditions and when true indicate a firmware flaw in the IPM Buffer.  Errors are set when the error condition occurs, and are cleared by setting the Clear Errors Bit in CSR0, or by Reset.

Proton Sparsification Mask Registers (offset x100 – x124)

31 – 0

Proton Sparsification Mask

Bit 31 – 0	R/W   Proton Sparsification Mask.

When high, corresponding sample will be stored in memory on each turn

if Sparsification Enable bit is set.  If Sparsification Enable bit is cleared,

then Proton Mask is not used.  Note: Register at offset x40 contains mask

bits for samples 0 through 31.  Register at offset x44 contains mask bits

for samples 63 through 32, etc.

PBar Sparsification Mask Registers (offset x140 – x164)

31 – 0

Proton Sparsification Mask

Bit 31 – 0	R/W   PBar Sparsification Mask.

When high, corresponding sample will be stored in memory on each turn

if Sparsification Enable bit is set.  If Sparsification Enable bit is cleared,

then PBar Mask is not used.  Note: Register at offset x80 contains mask

bits for samples 0 through 31.  Register at offset x84 contains mask bits

for samples 63 through 32, etc.

QIE Conversion Lookup Table (I/O Base + 200h – 3FFh)

| 31 - 9 | 8 - 2 | 1 – 0 |
| --- | --- | --- |
| Don’t care | Conversion Value | Don’t care |

Bit 31 – 9	RO   Unused (zeros).

Bit 8 – 2	R/W   Conversion table Value.

Value written will be stored in DDR memory QIE raw data of this table

entry offset from the table base address.  Table is read-only when

Acquisition Enable bit is high.

Bit 1 – 0	RO   Unused (00).

Memory Space:

| Mem Base + 00000000h -- Mem Base + 000FFFFFh | Event Memory Window (1 Mbyte) |
| --- | --- |

## In-System FPGA Programming

The Xilinx FPGA and its associated configuration PROMs can be programmed using the Xilinx software and a Xilinx JTAG device programming cable.  The PROMs can also be programmed through the PCI interface without removing the IPM Buffer board from the host system.  This is done by first using the Xilinx Impact software to generate a .svf formatted file.  This file is then converted into a .xsvf formatted file using the SVF2XSVF502.EXE program:

c:\> svf2xsvf02 –r 0 –i ipmfpga.svf –o ipmfpga.xsvf

The IPM Buffer control program can then be used to program the FPGA flash memory on the buffer board.  Once programmed, the buffer board host system must be power cycled for the changes to take affect.

In System FPGA Programming technical details

In system programming of the FPGA flash memories is done by accessing the JTAG signals on the board through the PCI interface.  When in-system programming is enabled, the external JTAG connector on the board is disabled.  Enabling in-system programming is done by driving the USERo pin on the PLX PCI interface chip low.  Once low, the JTAG pins can be accessed through the PCI interface.  Details of programming can be found in Xilinx XAPP058: http://www.xilinx.com.  Once programming is complete, the USERo output should be returned to a high state.

In-system pin mapping is as follows.  Refer to the PLXPCI9656BA user manual for register locations:

USERo output enable: 	PLX CNTRL(19)

USERo output: 		PLX CNTRL(16)

JTAG_TCLK: 		PLX CNTRL(24)

JTAG_TMS: 			PLX CNTRL(25)

JTAG_TDI: 			PLX CNTRL(26)

JTAG_TDO: 			CSRBase + xF4(0)

Programming sequence:

Set USERo output to a known state:

CNTRL(16) <= 0x1

Enable USERo output:

CNTRL(19) <= 0x1

Set USERo output to enable in-system programming:

CNTRL(16) <= 0x0

Once enabled, the JTAG signals on the board can be accessed via register bits.  By sequencing the JTAG signals as described in XAPP058, the two FPGA flash memories can be programmed.

Upon completion of the programming operation, disable in-system programming:

CNTRL(16) <= 0x1

After the flash memories have been programmed, the IPM Buffer board and its host system must be power cycled for the changes to take affect.  Simply rebooting the board will not cause the FPGA to reload its program.

If in-system programming is interrupted or fails for some reason, it is possible to leave the flash memories with corrupted or incomplete data in them.  If this happens, the IPM Buffer board will remain functional with the previous FPGA code running, but once the module is power cycled, it will go into an unusable state.  To reflash an IPM Buffer in this state, DIP Switch SW-1(3) must be set to diagnostic mode (off) and the flash memories programmed using the Xilinx cable.

Using the IPM BUF Control program to re-program the IPM Buffer FPGA

The IPMBUF Control program supports in-system programming of the IPM Buffer module.  To program a buffer board, select the JTAG tab, browse to the desired .xsvf data file, and press the “program” button.  Once programming is complete, power cycle the host system when prompted.

Creating an in-system programming FPGA data file

The data file required by the IPMBUF Control program is in the XSVF format.  To create this file, the Xilinx Impact software must first create .MCS files.

Once a successful Place and Route is complete, the MCS files can be created using Impact as follows.

1) Start Impact and select “Prepare Configuration File” from the “Operation Mode Selection” dialog.

2) Select “PROM File” from the “Prepare Configuration Files” dialog.

3) At the “Prepare PROM Files” dialog, select “Parallel PROM”, and enter “ipmfpga” (no quotes) in the “PROM File name” box.

4) Select “512K” for the “Parallel PROM Density”, and press the “Add” button twice to add two devices.

5) Press “Next” at the summary dialog, and press “Add File…” at the “Add Device File” dialog.

6) Browse to the “ipmfpga.bit” file and select it.

7) Select “No” to add another design file.

8) Press “finish”, and “Yes” to generate the file now.

9) Two new files will be created.  ipmfpga_0.mcs, and ipmfpga_1.mcs.  Close Impact.

To create the .XSVF file from the .MCS files, continue.

1) Start Impact.  Select “Mode” from the pull-down bar and select “File Mode”.

2) Select the “SVF-STAPL-XSVF” tab.

3) Right-click in the upper pane and select “add Xilinx device”.

4) When prompted, select “Create” and “XSVF”.

5) Enter the .xsvf file name: ipmfpga.xsvf, and press “Save”.  Press “OK” to start adding devices.

6) Browse to and add the ipmfpga_0.mcs file.  Select “xc18v04_vq44” for the part name and press “OK”.

7) Right-click in the upper pane and select: “Add Xilinx Device”.  Select “ipmfpga_1.mcs.  Select “xc18v04_vq44” for the part name and press “OK”.

8) Right-click on the first Xilinx chip shown (labeled: ipmfpga_0.mcs) and select “program”.

9) Make sure “Erase Before Programming”, “Verify” and “Parallel Mode” are checked.  Make sure “Load FPGA” is not checked.  Press “OK”.

10) Repeat Steps 8 and 9 for the second Xilinx chip (labeled: ipmfpga_1.mcs).

11) Select “Output” from the pull-down menu, and select “XSVF” file and “Stop Writing to XSVF File”.

12) Close Impact.

## DIP Switch Settings

The IPM Buffer module is equipped with an eight-switch DIP switch to allow enabling of diagnostic features.  These switches do not need to be changed for normal operation of the module.  Note the the switches are number 1 to 8 beginning at pin 1 of SW1.

DIP Switch SW-1 switches are defined as follows:

| SW1 | Reserved (off) |
| --- | --- |
| SW2 | Reserved (off) |
| SW3 | IPM Buffer diagnostic/recovery mode enable |
| SW4 | Reserved (off) |
| SW5 | Reserved (off) |
| SW6 | Reserved (off) |
| SW7 | Reserved (off) |
| SW8 | Diagnostic Boundary Scan Enable |

SW1 – 2	Reserved.  Must be set to the Off position.

SW3		When set to On, the Buffer module is in normal mode.  The J3 JTAG

port is connected to the two FPGA Flash memories only (U8 and U9).

When set to Off, the Buffer module is in diagnostic mode.  The J3

JTAG port daisy chains the two FPGA Flash memories, the FPGA,

and the PLX PCI Interface chip in the JTAG chain.  In-system access

to the JTAG port is disabled, and the J3 connector is forced enabled.

SW4 – 7	Reserved.  Must be set to the Off position.

SW8		Diagnostic Boundary Scan Enable.  When On, the IPM Buffer module

is in boundary scan diagnostic mode, and the module will not

respond to PCI accesses.  When Off, boundary scan testing of the

module is disabled, and normal operation is enabled.

## Indicator LEDs

The rear panel of the IPM Buffer contains five multi-color LEDs.  These LEDs are labeled D9, D10, D11, D15, and D16 with D9 being the top-most LED.  There are also five more multi-color LEDs on the board that are visible only when looking inside the host system.  These are labeled D1 through D5 with D1 nearest the rear panel of the host system.  The function of the LEDs is as follows:

| D1 | FPGA PCI access |
| --- | --- |
| D2 | DDR Memory Activity |
| D3 | Reserved |
| D4 | SERDES Channel 0 through 3 data activity |
| D5 | SERDES Channel 4 through 7 data activity |
| D9 | Paroli Channel 1 Power Good |
| D10 | SERDES Channel 0 through 3 locked status |
| D11 | SERDES Channel 4 through 7 locked status |
| D15 | Link Channel 0 through 3 data frame lock status |
| D16 | Link Channel 4 through 7 data frame lock status |

D1	FPGA PCI Access.  LED will light blue when the FPGA is being accessed

through the PCI interface.  Note that registers accessed on the PLX PCI

interface chip will not cause D1 to light.

D2	DDR Memory Activity.  D2 will light Green when the DDR memory is being

read or written.

D3	Reserved.  Always dark.

D4	SERDES Channel 0 through 3 data activity.  D4 lights blue when recognizable

data is seen on any of channels 0 through 3.  D4 lights red if data errors are

seen on any of channels 0 through 3.

D5	SERDES Channel 4 through 7 data activity.  D4 lights blue when recognizable

data is seen on any of channels 4 through 7.  D4 lights red if data errors are

seen on any of channels 4 through 7.

D9	Paroli Channel 1 Power Good.  Lights blue if the light power detected on channel

zero of the Paroli optical receiver is good.

D10	SERDES Channel 0 through 3 locked status.  Lights green if the SERDES

PLLs are locked on channels 0 through 3.  Lights red if none of the PLLs on

channels 0 through 3 are locked, and lights orange if at lease one, but not all

four channels are locked.

D11	SERDES Channel 4 through 7 locked status.  Lights green if the SERDES

PLLs are locked on channels 4 through 7.  Lights red if none of the PLLs on

channels 4 through 7 are locked, and lights orange if at lease one, but not all

four channels are locked.

D15	Link Channel 0 through 3 data frame lock status.  Lights green if the IPM

Buffer receive logic recognizes the data frames coming on all four of channels

0 through 3.  Lights red if none of these four channels have recognizable data,

and lights orange if at least one, but not all of these four channels have

recognizable data.

D16	Link Channel 4 through 7 data frame lock status.  Lights green if the IPM

Buffer receive logic recognizes the data frames coming on all four of channels

4 through 7.  Lights red if none of these four channels have recognizable data,

and lights orange if at least one, but not all of these four channels have

recognizable data.

## Initial Board Configuration

Upon first powering up a newly assembled IPM Buffer board, the following steps should be taken:

- With DDR memory not installed, set DIP switches to switch 3 on and all others off.

- Ohm all power supplies to ground to verify that no power planes are shorted to ground.

- Insert board into 3.3 Volt PCI slot and turn on power.

- Verify all voltages.  Note that VREF_1.25V will read high until Xilinx is programmed.

- Connect Xilinx programming cable to J4 and program the CPLD.

- Turn off power and set DIP switches to switch 8 on and all others off.

- Install boundary scan SODIMM and connect boundary scan JTAG connector to J3.

- Install boundary scan jumpers at J1 and J2.  Note that the empty pins on the J1 connector face the pin 1 end of the connector.

- Connect boundary scan controller to the network and turn it on.

- Turn on power to the IPM Buffer host system, and start “Scanplus Runner”.

- Load and run test: IPM_interconnect_withU5.tsp.  If test fails view log and debug problem.

- Turn off power and remove boundary scan connections.

- Set DIP switch 3 to on and all others off.

- Turn on power and connect Xilinx programming cable to J3.

- Using Impact, program the two Xilinx PROMs with the current FPGA microcode.

- Run PLXMon and program the PLX’s serial EPROM using the utility included in PLXMon.  Use file: eedata8.eep.

- Reboot system and verify that IPM Buffer board functions correctly.

## Power Requirements

Xilinx X2VP20  5.5 Watts

Infineon  V23832-R 1.3 Watts

Infineon HYS64D64020GDL-7-A,  5 Watts (x 2)

PLX PCI9656BA  830 mW

Total estimated maximum power requirements: 19 Watts.

# Text boxes

13

14

15

QIE0

0

1

2

3

4

5

6

7

12

11

10

9

8

23

22

21

20

19

18

17

16

31

30

29

28

27

26

25

24

QIE1

QIE2

QIE3

QIE5

QIE6

QIE7

QIE4

QIE4

CAPID0

Timing bits

TX_EN/RX_DV

QIE0

QIE1

QIE2

QIE3

QIE5

QIE6

QIE7

QIE4

QIE4

CAPID1

Timing bits

QIE0

QIE1

QIE2

QIE3

QIE5

QIE6

QIE7

QIE4

QIE4

CAPID2

Timing bits

Counter data

Error bits

modemode

modemode

modemode