# Standard Operating Procedures

# Downloading and Correcting GPS Data

10/17/02

**When returning from the field, always bring in GPS unit to return to office**

## Downloading Data

- Turn on Datalogger, set in cradle.

- Click on “GPS Pathfinder” icon on desktop to open program (or click on “Start” Button, Select “Programs”, and double click GPS Pathfinder on menu).

- When the window opens, a “Select Project” pop-up will ask you to select a project name, (or just click “X” to bypass).

- Along the top of the window, click “Utilities” and select “Data Transfer” from the pull-down menu.  The “Device” column should say “GIS Datalogger on COM1”.  On the “Receive” tab, click the “ADD” button and select either datafile or waypoints (whichever you are trying to download).

- Once the “Open” window pops up, click on the files you want to download (click on one, or to select multiple files hold down the “Ctrl” key and click), Click “Open”.  Make sure that the “Destination” window shows the correct folder you want your file in.  Click “Transfer All”.

- A pop-up window will appear, saying whether or not the file was successfully transferred and will tell you a corresponding text file with log information.  Click “Close”.

- In Windows Explorer, check destination folder to make sure files have transferred.

## Correcting Data

- Open GPS Pathfinder Office (see above).

- On the menu along the top of the window, click “Utilities” and select “Differential Correction”.

- The Differential Correction window will appear.  In the “Rover Files” box, select files to be corrected.  If you just downloaded, they may appear automatically (if not, click on “Browse”, select your files and click “Open”).

- In the “Base Files” box, select “Internet Search”, make sure the window says “USFS- Prescott, AZ” and click “OK”.  Make sure in the “Corrected Files” box the window displays the folder you want your files in (if not, use the “Browse” button to find the right one).  File extension should say “cor”.  Click “OK”.

- The program should automatically download the corrected base station files from the website.  (If this doesn’t work, see the next section- Manually Correcting Files).

- The program will then give you a series of pop-up windows describing the status of corrections and percentages… if they are less than 90%; check to make sure that accuracy is sufficient or try and redo the corrections.

## Manually Correcting Files

- Go to the website http://www.fs.fed.us/database/gps/prescott.html.  From the pull-down menus, select the date for which you want corrections.  Click “List CBS files for Download” button.

- Files are named with two characters and then the date (Example: P2090101 for September 1, 2001).  Click on the links for all the files with the appropriate dates.  The computer will ask you if you want to open it or save it to your computer- save these files in a folder.

- On the “Differential Correction” window, select files to correct (see above).  In the “Base Files” box, select “Local Search” button.  Use the “Browse” button to select the folder where correction files were saved, Click “OK” button.  Make sure the “Corrected Files,” “Output Folder” box shows where you want your corrected files saved.

- The program will then give you a series of pop-ups telling you the status of corrections and percentages… if they are less than 90%, check to make sure that accuracy is sufficient or try and redo the corrections.