# Aqua Teleconference November 1, 2007

On the phone:

Project science:  Claire Parkinson (telecon chair), Steve Platnick, Steve Graham

Instruments: Mous Chahine, Denis Elliott, Norman Loeb

ESMO: Angie Kelly

HQ: Cheryl Yuhas

## Mission Ops  (Kelly):  see distributed ppt file from B. Guit (on travel in CO) for details.

Major activities over last month:

- 10/1: Aura STM, Pasadena.

- 10/8: AIRS photometric cal.

- 10/18: Dual Thruster Module #2 (DTM-2) Anomaly Review Board kickoff.

- 10/29: AMSU-A channel 4 performance change reported by JPL.

- 10/31-11/1: DoD Surveillance Working Group mtg. in Colorado Springs (attended by B. Guit).

- Ongoing IT Security/GS meetings - daily and weekly.

Planned Activities for Next Month

- 11/7: DMUM #31

- Weekly Cabletron replacement WG and IT Security/GS meetings.

Long-Term Plans

- Aura Relocation. Plan is to re-locate Aura closer to Aqua (~7-8 vs. 15 min); would be achieved by atmospheric drag so would take about 10 mos. The original 15 min separation was for downlink reasons, but now have additional antennae in Norway and Alaska. Working on getting approvals before the next Aura DMUM in December.

CY: Also looking at other tweaks in A-Train configuration, e.g., PARASOL plans for exiting the A-Train as fuel decreases, and CALIPSO view change (3° pitch to avoid crystal facet reflection) with coordination by CloudSat.

- Single S/C Ops, Dump-N-Go, and Lights Dim ops: no changes.

## Spacecraft Anomalies

- New: STM-2 Heater Anomaly observed in September. Final Anomaly Review Board report due by 12/1. No effect on spacecraft or instruments. Similar to Aura DTM-3 heater anomaly in Aug 2005.

## Instrument Anomalies

- AMSU-A Channel 4. Gain decrease in ch 4 (and noise increase) over the last few weeks reported by JPL on 10/29. If noise increase continues, ch 4 could impact retrievals and might have to be declared non-operational. JPL and FOT monitoring the situation. See accompanying plots in ppt file provided by Denis Elliott, AIRS project instrument operations and calibration manager. See AIRS notes for further details.

- AMSR-E motor current/torque. No changes. Current torque threshold was raised to 4.5 Nm in July 2007. QuikSCAT experienced similar behavior with its scatterometer antenna bearing assembly – obtained a copy of the JPL anomaly investigation report from Honeywell. What we have seen on AMSR-E is apparently not indicative of impending failure but normal wear and tear. Continuing to monitor.

Debris Collision Avoidance:  No significant approaches for Aqua in October.

Spacecraft: status = green

Instruments: status = green

Data capture/L0 processing: green. No data losses in October.

### Project Science (Parkinson, Platnick:):

No particular items to discuss.

Data system/EOSDIS:

No report.

CERES (Loeb):

Instruments nominal. Next STM will be the week of Nov. 12 in British Columbia.

MODIS:

No report.

AMSR-E:

No report.

### AIRS/AMSU (Chahine, Elliott):

DE: Put out two alerts regarding channel 4 gain issue: the AIRS users and DB community. The decline had been very slow, but has accelerated over the last month (e.g., slide 15 in Guit distribution). The NEdT (slide 19) is increasing, up to about 0.75K currently (from 0.12K at launch). We don’t yet know what the cause is.

MC: We have been preparing for loss of AMSU channels; currently have an AIRS-only algorithm that has been validated vs. use of AMSU. There are conditions of cloudiness where AMSU is very helpful. We’d expect to get the same temperature/moisture accuracy but would have less yield in regions of high cloudiness. The loss of channel 4 (at ~800 mb) is not expected to have a significant impact but we will be checking further.

MC: A 50th anniversary celebration of the “Keeling curve” is coming up this month in Hawaii. I’m going to look into seeing if it’s possible to get an AIRS mention/slide.

### HQ (Yuhas):

See comments in Mission Ops “long term plans”.

Outreach, web site, etc. (Graham):  No report.

I was in Paris a couple of weeks ago for the 3-week UNESCO meeting. NASA was a key part of the conference. The Magic Planet was very well-received. King and Abdalati both spoke. John Marburger (OSTP) was there, along with two key NSF representatives.

Next Telecon: Thursday, December 6, 2007

Minutes are being placed on the following site: http://aqua.nasa.gov/minutes. Corrections/additions should be sent to Steve Platnick.