February 11, 2004

SUBJECT:	SOI – Interpretations - Minimum Data Set for Organic Horizons

TO:	All State Conservationists	File Code:  430-12-5

All Regional Conservationists

All Center and Institute Directors

Pacific Basin and Caribbean Directors

In response to State Soil Scientists' request, the National Soil Survey Center (NSSC) is providing guidance regarding populating National Soil Information System (NASIS) data elements for O horizons.  A draft list was circulated to states for comments in February 2003.  The attached list was completed after receiving input from State Soil Scientists and MLRA Office Leaders and conferring with scientists developing the Wind Erosion Prediction System (WEPS) model.  Effective today, the following list of data elements is the minimum data set for all O horizons, including Histosols, Folists, litter (duff) layers, etc.

Presently data may not exist for several of the listed data elements.  In the future, when sampling soils for characterization projects or reference samples, please sample associated O horizons and request appropriate laboratory data for items listed in the included table.  As data is collected and populated, Soil Survey Interpretations staff at NSSC will begin to develop modified soil survey interpretations for use by those who wish to use them.  For the near term, NSSC plans to have soil survey interpretations available for both scenarios - those with populated O horizon data and those without O horizon data populated.  In the future, NSSC will eliminate the option to generate soil survey interpretations without O horizon data populated.

If you have further questions, please contact Cathy Seybold at (402) 437-4132 or cathy.seybold@nssc.nrcs.usda.gov.

/S/

MICHEAL L. GOLDEN

Director, Soil Survey Division

Attachment

cc:

Maurice Mausbach, Deputy Chief, Soil Survey and Resource Assessment, NRCS, 
Washington, DC

Robert J. Ahrens, Director, National Soil Survey Center, MS 32, NRCS, Lincoln, NE

NCSS National-level Cooperators

State Soil Scientists/MLRA Office Leaders

| Horizon Level |
| --- |
| Data Element | NASIS Data Field |
| Horizon designation | horizon_designation |
| Horizon Depths | horizon_depth_top horizon_depth_bottom |
| Rock fragments volumes (or wood fragments) | fragment_volume (1,rv,h) fragment_size (1,rv,h) fragment_kind fragment_hardness (for any mineral material) |
| In-lieu of texture | terms_used_in_lieu_of_texture |
| Organic matter | organic_matter_percent (l,rv,h) |
| Bulk Density | bulk_density_one_third_bar (l,rv,h) |
| Particle density | particle_density |
| Ksat | sat_hydraulic_conductivity (l,rv,h) |
| Available water capacity (AWC) | available_water_capacity (l,rv,h) |
| 1/3 bar water | water_one_third_bar (l,rv,h) |
| 15 bar water | water_fifteen_bar (l,rv,h) |
| Calcium carbonate equivalent | calcium_carbonate_equivalent (l,rv,h) |
| Gypsum | gypsum (l,rv,h) |
| Sodium Absorption Ratio (SAR) | sodium_absorption_ratio (l,rv,h) |
| Electrical conductivity (ec) | electrical_conductivity (l,rv,h) |
| pH - Populate the CaCl2 pH | pH_.0lm_cac12 (l,rv,h) |
| pH in water - Populate if available | pH_1:1_water ((l,rv,h) |
| Cation Exchange Capacity (CEC-7) - populate if pH is ( 5.5 | cation_exchange_capcty_NH4OacpH7 (l,rv,h) |
| Effective Cation Exchange Capacity -(ECEC) Populate if pH is <5.5 | effective_cation_exch_capacity (l,rv,h) |

| Atterberg Limits (LL, PI) - Populate only if the soils classify as organic OH or OL according to the UNIFIED classification. Do not populate for soils that classify as Pt. When organic soils are suspected, a liquid limit test is performed on 2 samples of the soil. One liquid limit test is performed on air-dried sample. The second test is performed on oven-dried sample. If the ratio of the liquid limit performed on the oven-dried sample to the liquid limit value of the air-dried sample is less than 0.75, then the soil is an organic silt (OL) or an organic clay (OH). Populate only the oven-dried Atterbergs. | liquid_limit (l,rv,h) plasticity_index (l,rv,h) |
| --- | --- |
| AASHTO and Unified - If the AASHTO class A-8 and unified classes OH, OL, and Pt apply to the organic layer in question, then enter these classes. Otherwise, do not populate. | unified_soil_classification AASHTO_group_classification |
| Particle Size Separates - Populate if the organic matter content is < 35%. If the layer contains andic soil materials, then populate if the organic matter content is < 50%. Also, populate the sand fractions (total sand, vcos, cos, s, fs, and vfs) for soil layers that have => 35% organic matter (needed for wind erosion model). | clay_total_separate (l,rv,h) silt_total_separate (l,rv,h) sand_total_separate (l,rv,h) very_coarse_sand_separate (l,rv,h) coarse_sand_separate (l,rv,h) medium_sand_separate (l,rv,h) fine_sand_separate (l,rv,h) very_fine_sand_separate (l,rv,h) |
| Percent Passing Sieves - If particle size separates are populated, then populate the sieves. Otherwise do not populate. | sieve_number_4 (l,rv,h) sieve_number_10 (l,rv,h) sieve_number_40 (l,rv,h) sieve_number_200 (l,rv,h) rock_frag_3_to_10_in (l,rv,h) rock_frag_greater_than_10_in (l,rv,h) |
| K factor | DO NOT POPULATE |
| Linear Extensibility Percent - LEP | DO NOT POPULATE |
| Component Level |
| Identify and separate drained and undrained map unit components - Properties of organic horizons (AWC, bulk density, and exchange properties) in drained soils are significantly different than those in undrained soils. | local_phase (to record drained & undrained) |
| For organic soils and mineral soils with surface organic horizons - populate all standard component level data, including subsidence, dominant land cover, and soil water state. |  |