D0 Muon Scintillator Electronics

SRC-To-Remote Host Protocol

Kwame Bowie

Xinyi Chen

Carmen Rotolo

Marcus Larwill

Tom Fitzpatrick

May 5, 1999

Revised: June 28, 2000

INTRODUCTION:

During normal operation, the front-end crates need to be monitored, maintained, and updated. In order to accomplish this task, the crates must be remotely accessible to subsystem engineers and control boards not located within the crate. Parameters must be monitored and changed, memories must be updated, and devices must be reset. All of these functions as well as various others will need to be performed by remote link. However, it was decided that a high-speed network connection such as Ethernet should not be present in the front-end crates. Two systems provide the necessary support for the remote links: the 1553 military standard transceiver system, and the SCC serial port system.

The 1553 military standard transceiver system is composed of a 1553 remote terminal (RT) and a 1553 controller. The remote terminal (RT) is the portion of the 1553 system that resides on the SRC. The 1553 controller board is located in a different crate and communicates with the external host computer via Ethernet. The 1553 controller board then forwards this information to the SRC via coaxial cabling.

The SCC system consists of two boards with SCC chips and their cable drivers. The Muon Scintillator SCC system is used to establish communications between the SRC and the MRC boards. Information is transferred to the MRC via Ethernet and the MRC transfers this information to the SRC via strip cabling.

In order to communicate with the SRC, the 1553 transceiver and SCC serial port systems, store data in a four-port RAM on the SRC dedicated to remote communications. The four port RAM acts as a mailbox and accepts all types of data and commands from both the SCC serial port and the 1553 transceiver system, and arranges the data in a known format. This report describes the data format of the four-port RAM, the expected groupings of related commands, and the supported functions of the remote link. Although functionality is provided for some test procedures, it is decided that testing will be done through a different interface. The block diagram below shows the system level functionality.

Fig. 1 Block Diagram of SRC to Remote Host Communication

COMMUNICATION PROCEDURE:

The SRC-to-remote host communication system is a half-duplex system. This means that the data can be sent both ways, but not simultaneously. In order to maintain adequate functionality, there must be two types of transactions: a WRITE transaction, and a READ transaction. The WRITE transaction denotes the transaction between the SRC and the remote host in which the remote host is sending data to the SRC. The READ transaction is the transaction between the SRC and the remote host in which data is sent from the SRC to the remote host.

1553 TRANSACTION PROCEDURE:

Although data may be sent in both directions, only the 1553 controller may request a transaction. The 1553 controller sends a command word and depending on the value of the T/R bit, it sends data or prepares to accept data. In order for any transaction to occur, a valid RT Address must be received by the SRC. The communications PLD accepts two (2) RT addresses for each DIP-switch setting. The RT Address is a 5-bit field, but the DIP-switch is only mapped to the upper 4 bits. This mapping was necessary to enable the SLP board to be controlled using the 1553 system on the SRC. As a result, all even RT Addresses are mapped to SRC and SFE commands, and all odd RT-Addresses are mapped to SLP commands. To ensure that the data transaction occurred without failure, a status word is sent back to the 1553 controller. The position of the status word varies depending on the type of transmission: it comes before the data for a READ and after the data for a WRITE. The bit mapping of the command and status words are shown below.

| Command Word | RT Address | T/R | Subaddress | Word Count |
| --- | --- | --- | --- | --- |
| Status Word | RT Address | ME | INS | SR | RESERVED | BCR | BSY | SF | DBC | TF |

WRITE transaction:

The write transaction is accessed by lowering the transmit bit in the 1553 command word. The remote terminal on the SRC sees the T/R bit low. After issuing the WRITE command, the 1553 controller, immediately sends the data. After the last data word is sent, the communications PLD on the SRC issues a level 7 VME interrupt. The crate processor is then required to send back an interrupt acknowledge signal. The 1553 spec indicates that the Status Word must be received at the 1553 controller within the response time of 10 to 16 microseconds. The communications PLD on the SRC generates a valid status word as long as the IACK arrives on time (within 7.5 (s of the interrupt) from the crate processor. If the IACK is late, the subsystem flag bit within the status word is set. The status word signals the end of a transaction

Response time (10 – 16 us)

…

1553 Controller

1553 BUS

RT on SRC

Fig. 2: 1553 WRITE Transaction Diagram

READ transaction:

The read transaction is accessed by asserting the receive bit in the 1553 command word. The remote terminal on the SRC sees the T/R bit high. After receiving the READ command word, the RT issues a VME interrupt. To produce a valid status word, the crate processor should deliver an IACK signal within 7.5 (s of the interrupt. Otherwise the subsystem flag bit in the status word is set to signify a processor timeout. In the READ transaction, the last data word signals the end of the transaction.

Response time (10 – 16 us)

1553 Controller

1553 BUS

RT on SRC

…

Fig. 3: 1553 READ Transaction Diagram

1553 Multi-block Commands

In order to load (or read) RAM devices on the SRC, large blocks of data must be loaded into consecutive locations. These multi-block commands require the crate processor to remember the last address loaded and restart just after that position on the next transaction. The 1553 command word specifies the starting address by selecting a subaddress code corresponding to the RAM device to be loaded (or read). Once the memory device is finished being loaded (or read), the correct Reset RAM Pointer mode command is issued. There are two (2) Reset RAM pointer mode commands, one for writes and one for reads. This enables reads and writes to be interspersed so that one RAM device may be loaded while another is read.

SCC SERIAL PORT TRANSACTION PROCEDURE:

The transaction procedure when using the SCC serial port is substantially different from the 1553 procedure. The 1553 system is essentially a synchronous system where a data buffer is loaded and then data is streamed out at a constant word rate only after a transmit (or receive) command is sent. Also, in most cases the command word comes at regular intervals. Conversely, the SCC serial port is an asynchronous connection where data is sent out of the SCC device as soon as data enters the data register. There is not a set interval length between transmissions or even between the individual data words in a transmission. The system level procedure is software controlled from the MRC and is yet to be fully developed. The SCC serial port system on the SRC is a slave device just the same as the 1553 RT on the SRC. As a result, commands and data are simply loaded into the appropriate positions when the MRC requests the transactions.

The first major difference between the two systems is that the SCC serial port does not require a confirmation word in order to show that the connection is made; a valid connection is simply assumed. The 1553 system requires a confirmation of connection in the form of a status word for every transaction. For the SCC serial port, there is not connection confirmation in hardware since all transactions are single-byte on the hardware level. Confirmation of a single-byte transfer would add an unreasonable data overhead for larger transmissions. However, connection confirmation may be embedded within the data in the form of parity bits. Embedding parity bits or some other form of confirmation in the data would be a software issue and beyond the scope of this document.

The other major difference between the SCC serial port system and the 1553 system is the word spacing. The 1553 controller has a data buffer memory so that data words may be packed together with no delays between words. Due to the buffering, there is a maximum transaction length of 32 words. This is not the case for the SCC serial port. The SCC serial port is asynchronous and data is sent whenever it is provided by the MRC. As a result, word spacing may be variable and transaction time has no predefined limit based on hardware.

The final major difference between the 1553 system and the SCC system is the fact that the SCC system has only three preset functions: WRITE, READ, and SYSRESET. Whereas the 1553 system had each subaddress mapped to a different function or register, the SCC system has no preset function or register mapping. The SCC is to be used as a console port to the crate processor. Thus all information about functions or registers to be accessed is contained within the data.

WRITE Transaction:

The WRITE transaction for SCC system is initiated when the MRC sends the command word: (DXXX) hex, where the X’s represent the word count. It is important to remember that the command word just like all SCC data must be entered into the MRC 8 bits-at-a-time. The word count is 12 bits, which means that the entire 4-Port RAM may be filled starting at location 64. The SCC serial port controller PLD on the SRC keeps track of the number of words moved into the 4-Port RAM. As soon as the transaction word count is equivalent to the word count in the command word, the connection is closed and the VME interrupt is issued. It should be noted that the command word appears in the 4-Port RAM as a 16-bit word, but the data in the subsequent addresses is only saved as 8-bit words. Thus only the lower byte of each location contains valid data.

READ Transaction:

The READ transaction proceeds slightly differently than the WRITE transaction. First, the READ transaction does not use more than one location of the 4-Port RAM. The first step of the READ transaction is the MRC requesting data from the SRC. The command word (EXXX) hex is placed in the first location of the serial port section of the 4-Port RAM (location 64) and then an interrupt is issued. The crate processor then writes one byte at a time to the SCC data register itself, completely bypassing the 4-Port RAM.  The MRC must remember how many words it requested so that it knows which data is associated with which request. The SRC will continue sending data until the word count is reached. Once the word count is reached, the crate processor will issue the Terminate Transaction command. Care must be taken that the data is not overwritten within the MRC.

4-PORT RAM DATA FORMAT:

The 4-Port RAM data format was selected to enable access through all four ports while maintaining a known data structure. A major concern was enabling the 1553 system to fit seamlessly into the EPICS slow control system. To accomplish this goal, the 1553 controller must be able to access the registers on the SRC that it needs in a timely manner. As a result, one segment of the 4-Port RAM is dedicated to holding data related to the 1553 system. To simplify the mapping of the 4-Port RAM, the two sections: 1553 memory and SCC memory start on page boundaries. The 1553 memory starts at location zero (0) and the SCC memory starts at location 64. More specific information on the ordering of words, bytes, and bits are shown in the sections below.

.

1553 Data Format

The 1553 section is located in the first few (33) locations of the 4-Port RAM. This section provides enough buffering memory for one 1553-transaction block.  The specifics of the word and bit locations are shown in Fig. 4 below.

1553 Transactions:

WRITE Transaction:

| Location 1 | Command Word | RT Address | T/R | Subaddress | Word Count |
| --- | --- | --- | --- | --- | --- |
| Location 2 | 1st Data Word | 16-Bit Data |
| … | … | 16-Bit Data |
| Location 33 | Last Data Word (MAX. 32) | 16-Bit Data |

READ Transaction:

| Location 1 | Command Word | RT Address | T/R | Subaddress | Word Count |
| --- | --- | --- | --- | --- | --- |
| Location 2 | 1st Data Word | 16-Bit Data |
| … | … | 16-Bit Data |
| Location 33 | Last Data Word (MAX 32) | 16-Bit Data |

###### Fig. 4  1553 Transaction Block Format

###### SCC Serial Port Data Format

The SCC serial port RAM section has enough locations to enable reasonably large chunks of data to be processed (roughly 4Kbytes at a time). There is command word associated with all data transactions for the SCC system. The SRC parses the command word for function code and word count and then places it in the 4-Port RAM. The three function codes are as follows: READ, WRITE, and SYSRESET. The function codes are mapped to the most significant nibble of the first byte. The word count is composed of the remaining nibble in the first command byte along with the next command byte, totaling 12 bits. The SCC chips only have 8-bit data ports so all words are transmitted 8 bits at a time. For a WRITE transaction, up to 4031 8-bit data words may be sent following the 16-bit command word. For a READ transaction, the front-end crate processor sends one byte at a time directly to the SCC data register, bypassing the 4-Port RAM.  The specifics of bit and word locations are shown in Fig. 5 below.

SCC Serial Port Transactions:

WRITE Transaction:

| Location 64 | Command Word | Fcn Code = D (hex) | Word Count |
| --- | --- | --- | --- |
| Location 65 | 1st Data Word | 8-Bit Data |
| … | … | 8-Bit Data |
| Location 4096 | Last Data Word (Max. 512) | 8-Bit Data |

READ Transaction:

| Command Word | FCN Code = E (hex) | Word Count |
| --- | --- | --- |

# Fig. 5  SCC Serial Port Transaction Format

## INTERRUPTS:

One of the most important aspects of the SRC-to-Remote host communication system is the need to update parameters and read status via the 1553 system. The 1553 system has fairly strict timing requirements, so any 1553 transaction must be handled immediately. It was decided that the best way to handle both the 1553 and SCC systems using the same memory was to use two different interrupts. By using two interrupts, the crate processor’s interrupt handler can handle an interrupt while accepting other interrupts. By setting the interrupt level for 1553 transactions to level 7, 1553 transactions become the first priority of the crate processor. Interrupt level 6 was selected for the SCC system, so SCC transactions are handled only after the 1553 transaction is finished.

APPENDIX  A:

SAMPLE TRANSACTIONS:

##### 1553 WRITE

Subaddress = 0x10, RT Address = 2, Word count =0x20

Send Command and Data (1553 Controller)

- Load Controller with header word  (2)	0x0002 ( ControllerBase + Location

- Load Controller w/ command word		0x1020 ( ControllerBase + Location + 2

- Load Controller w/ data			0xXYZ ( ControllerBase + Location + 4

- Repeat 2 until you reach word count	0xXYZ ( ControllerBase + Location + 4 + 2*I

- Issue execute command instruction		Location / 2 ( ControllerBase + 0xfffc

- Check status: valid transaction  =0z1000	Controller Base (  0x1000?

Receive and Check Data: (SRC)

- Check command word on SRC:	SRC_BASE + 0x780000 ( 0x1020?

- Check data words			SRC_BASE + 0x780000 + 4 ( 0xXYZ

- Continue 3 until reach word count	SRC_BASE + 0x7800000 + 4*I ( 0xXYZ

##### 1553 READ

Subaddress = 0xC, RT Address = 2, Word count = 6

Send Command (1553 Controller)

- Load Controller w/ command word:	0x1586 ( ControllerBase + Location

- Issue execute command instruction:		Location / 2 ( ControllerBase + 0xfffc

Write Data to 4-Port (SRC)

- Read Command word (get function and word count)	SRC_BASE + 0x780000 ( 0x1586

- Read Data from location pointed by subaddress:	SRC_BASE + 0x880000  + 4*I ( 	0xXYZ

- Write Data Word to 4-Port(starting at location2 ):	0xXYZ(SRC_BASE + 0x780004 + 4*I

- Repeat 2 and 3 until word count is reached

###### Read Status and Data from 1553 Controller

- Read Command word			ControllerBase + Location + 2 ( 0x1586

- Read Data word				ControllerBase + Location + 4 ( 0xXYZ

- Read data words until reach word count	ControllerBase + Location + 4  + 2*I ( 0xXYZ

- Read Status Word			ControllerBase + Location  + 4 + 2*words ( 0x1000

SCC WRITE

Word count  = 0x456

Send Command and Data (MRC)

- Reset SCC chip on MRC				0 ( MRC_BASE + 0xC00C

- Write command word 1st byte to SCC on MRC	0xD4 ( MRC_BASE + 0xC00C

- Write command word 2nd byte to SCC on MRC	0x56 ( MRC_BASE + 0xC00C

- Write data byte to SCC on MRC			0xXYZ ( MRC_BASE + 0xC00C

- Continue 4 until word count is reached		0xXYZ ( MRC_BASE + 0xC00C

Read/Check Data (SRC)

- Read back data from 4-Port RAM			SRC_BASE + 0x780100 ( 0xXYZ?

##### SCC READ

Word count  = 0x234

Send Command Word (MRC)

- Initialize MRC for READ (read 2 nulls)		MRC_BASE + 0xC00C ( 0

MRC_BASE + 0xC00C ( 0

- Write command word 1st byte to SCC on MRC	0xE2 ( MRC_BASE + 0xC00C

- Write command word 2nd byte to SCC on MRC	0x34 ( MRC_BASE + 0xC00C

Send Back Data (SRC)

- Read 4-Port RAM for word count			SRC_BASE + 0x780100 ( 0x234?

- Write Data directly to SCC Data Register		0x00YZ ( SRC_BASE + 0x600008

Read Received Data (MRC)

- Read received data from upper byte			MRC_BASE + 0xC00C ( 0xYZ00

**After word count is reached

Terminate READ transaction (SRC)

- Write to terminate transaction register		0 ( SRC_BASE + 0x600014

APPENDIX B:

### 1553 Subaddress/Mode Code Map

SubAddress		Register/Function				R/W	   #words

| 0 | MODE Command | W | - |
| --- | --- | --- | --- |
| 1 | SRC VME CSR1 | R | 1 word |
|  | SRC Readout Controller CSR1 |  | 1 word |
|  | SFE0 VME CSR1 |  | 16 words |
|  | . . . |  |  |
|  | SFEF VME CSR1 |  |  |
| 2 | SFE Write-only: Reset SFE boards CSR | W | 1 word |
|  | Clear latched errors CSR |  | 1 word |
|  | Reset output FIFO read pointer CSR |  | 1 word |
|  | Reset output FIFO CSR |  | 1 word |
|  | Reset TMCs CSR |  | 1 word |
|  | Reset ADC FIFO CSR |  | 1 word |
| 3 | Group A Chan En./ Analog chan sel. | R/W | 32 words |
| 4 | Croup B Chan En./ Analog chan. sel. | R/W | 32 words |
| 5 | Group C Chan En./ Analog chan. sel. | R/W | 32 words |
| 6 | SFE Master Controller CSR0 | R/W | 16 words |
| 7 | Readout Controller CSR0-3 | R/W | 4 words |
| 8 | Trigger Manager CSR0-6 | R/W | 7 words |
| 9 | HOTLINK CSRs: L2 & L3 | R/W | 2 words |
| A | LAT_PRE | R/W | 16 words |
|  | ADC_DEL ** |  | 16 words |
| B | L1_DEL | R/W | 16 words |
|  | L1STRG_LAT |  | 16 words |
| C | Crate Analog Data: A_Crate0 (Voltage, temp, etc.) | R | 7 words |
|  | . . . |  |  |
|  | Crate Analog Data: A_Crate6 |  |  |
| D | SRC Board Main CSR0 | R/W | 1 word |
| E | All TMCs CSR0 | All TMCs CSR1 | R/W | 32 words |
|  | All TMCs CSR2 | All TMCs CSR3 |  |  |
| F | Interrupt Vectors | R/W | 1 word |
| 10 | SFE Thresholds 0 | SFE Thresholds 1 | R/W | 32 words |
|  | SFE Thresholds 2 | SFE Thresholds 3 |  |  |
| 11 | SFE Thresholds 4 | SFE Thresholds 5 | R/W | 32 words |
|  | SFE Thresholds 6 | SFE Thresholds 7 |  |  |
| 12 | SFE Thresholds 8 | SFE Thresholds 9 | R/W | 32 words |
|  | SFE Thresholds 10 | SFE Thresholds 11 |  |  |
| 13 | SFE Thresholds 12 | SFE Thresholds 13 | R/W | 32 words |
|  | SFE Thresholds 14 | SFE Thresholds 15 |  |  |
| 14 | SFE Thresholds 16 | SFE Thresholds 17 | R/W | 32 words |
|  | SFE Thresholds 18 | SFE Thresholds 19 |  |  |
| 15 | SFE Thresholds 20 | SFE Thresholds 21 | R/W | 32 words |
|  | SFE Thresholds 22 | SFE Thresholds 23 |  |  |
| 16 | SFE Thresholds 24 | SFE Thresholds 25 | R/W | 32 words |
|  | SFE Thresholds 26 | SFE Thresholds 27 |  |  |
| 17 | SFE Thresholds 28 | SFE Thresholds 29 | R/W | 32 words |
|  | SFE Thresholds 30 | SFE Thresholds 31 |  |  |
| 18 | SFE Thresholds 32 | SFE Thresholds 33 | R/W | 32 words |
|  | SFE Thresholds 34 | SFE Thresholds 35 |  |  |
| 19 | SFE Thresholds 36 | SFE Thresholds 37 | R/W | 32 words |
|  | SFE Thresholds 38 | SFE Thresholds 39 |  |  |
| 1A | SFE Thresholds 40 | SFE Thresholds 41 | R/W | 32 words |
|  | SFE Thresholds 42 | SFE Thresholds 43 |  |  |
| 1B | SFE Thresholds 44 | SFE Thresholds 45 | R/W | 32 words |
|  | SFE Thresholds 46 | SFE Thresholds 47 |  |  |
| 1C | Port D Four Port RAM | R/W | Multi-block |
| 1D | DSP Flash RAM | R/W | Multi-block |
| 1E | DSP Dual Port RAM | R/W | Multi-block |
| 1F | MODE command | W | - |

MODE COMMAND CODES:

MC							R/W

| 09 | Reset RAM WRITE pointer | (T/R = 0) | None |
| --- | --- | --- | --- |
| 0A | Reset SRC | (T/R = 0) | None |
| 0B | DSP Service Request | (T/R = 0) | None |
| 0C | L2 & L3 FIFO Reset | (T/R = 0) | None |
| 0D | SRC CLR_ERRS | (T/R = 0) | None |
| 0E | SYSRESET | (T/R = 0) | None |
| 0F | Reset RAM READ pointer | (T/R = 0) | None |

APPENDIX C:

TYPICAL PROCEDURES:

The following are groups of essential procedures to be performed by the SRC. The groups are divided into large procedures, which can later be subdivided and/or shortened. Several of these groups contain no specified procedures. This is because it is assumed that other I/O methods would be better suited for performing that group’s associated procedures. The address map is provided in the following section.

- Initialize after power fail: Initialization after power failure includes resetting all devices, setting all parameters, and setting modes on all devices. Basically everything except rewriting flash RAMs and FLEX devices.

- Reset output FIFO				Address write (no data necessary)

- Reset output FIFO pointer			Address write (no data necessary)

- Reset SFE boards				Address write (no data necessary)

- Reset TMCs					Address write (no data necessary)

- Reset ADC FIFO				Address write (no data necessary)

- Reset SRC board				Address write (no data necessary)

- Reset DSP					Address write (no data necessary)

- Reset L2 & L3 FIFOs				Address write (no data necessary)

- Clear latched errors				Address write (no data necessary)

- SFE: Set TMC(0-B) CSR (0-2)			36 registers of 8-bit data  OR

3 registers of 8-bits sets CSRs

for all 12 TMCs with same values

- SFE: Set Group A-C thresholds		48 registers of 8-bit data

- SFE: Load threshold and TP-DAC?		Address write (no data necessary)

- SFE: Set Group A-C trigger gate registers	3 registers of 13-bit data

- SFE: Set Group A-C analog gate registers	3 registers of 13-bit data

- SFE: Enable Group A-C channels		3 registers of 16-bit data

- SFE: Set Master Controller CSR0		1 register of 16-bit data

- SFE: Read Master Controller CSR1		1 register of 16-bit data

- SFE: Set L1 timing data preset			1 register of 8-bit data

- SFE: Set ADC data trigger latency		1 register of 6-bit data

- SFE: Select analog group select (A, B, or C)	3 registers of 4-bit data

- SRC: Set VME controller CSR0		1 register of 16-bit data

- SRC: Read VME Controller CSR1		1 register of 16-bit data

- SRC: Set readout controller CSRs		4 registers of 16-bit data

- SRC: Set trigger manager CSRs		7 registers of 8-bit data

- SRC: Set L2 and L3 HOTLINK CSRs		2 registers of 8-bit data

- Parameter setting: Parameter setting, simply sets all parameters not used for testing.

- Set CSRs 0-2 for TMCs 0-11			36 registers of 8-bit data  OR

3 registers of 8-bits sets CSRs

for all 12 TMCs with same values

- Set discriminator thresholds: Groups A-C	48 registers of 8-bit data

- Load threshold and TP_DAC?			Address write (no data necessary)

- SFE: Load Group A-C trigger gate registers	3 registers of 13-bit data

- SFE: Load Group A-C analog gate registers	3 registers of 13-bit data

- SFE: Enable Group A-C channels		3 registers of 16-bit data

- SFE: Load Master Controller CSR0		1 register of 16-bit data

- SFE: Load timing data latency preset		1 register of 8-bit data

- SFE: Load ADC data L1 trigger latency		1 register of 6-bit data

- SFE: Select analog Group A, B, or C channels	3 registers of 4-bit data

- SRC: Set VME CSR0				1 register of 16-bit data

- SRC: Set readout controller CSRs		4 registers of 16-bit data

- SRC: Set trigger manager CSRs		7 registers of 8-bit data

- SRC: Set L2 & L3 HOTLINK CSRs		2 registers of 8 bit data

- Online error and status monitoring: Checks a few CSRs periodically to ensure that no errors have occurred.

- Check SFE CSR1: Control status of Test Output FIFO and Error Status of Trigger and Analog gate timing

- Check SRC VME Controller CSR1: Error status information for VME communications

- Check SRC Readout controller’s second CSR to see SFE timeout information.

- Testing: Perform all procedures required by the desired test. Advisable to implement using a method other than 1553 or serial port for the sake of speed and real-time data acquisition.

- Reconfiguration: Rewrite all PLDs, FPGAs and flash RAMs.  Also advisable to use other I/O modality do to the very large memory arrays.

###### APPENDIX  D:

###### Address Map of All Available Functions:

This is a list of all functions that may be performed under VME control. These functions are all available to the Remote Host.  Many may not be ideally suited for transmission via 1553 or SCC serial port, but they may nonetheless be performed.

SFEs:

1) Configure FLEX 10Ks :				W(000000

2) Configure FLEX 10K flash RAM		R/W ( 100000 – 1FFFFC

3) Read FLEX 10K INIT DONE register  		R( 200000

4) Read FLEX 10K STATUS register 	 	R(  300000

5) Clear latched errors  				W(  400000

6) Start TMCs W/R pointers  			W(  500000

7) Stop TMCs W/R pointers 			W(  600000

8-19) Delay Buffer x(0:B) DP RAM 		R/W(  808x00 – 808xFC

- Master controller DP RAM  			R/W( 808C00 – 808CFC

  - TMC x(0:B) CSR0  			R/W(  809x00

33-44) TMC x(0:B) CSR1 			R/W(   809x04

  - TMC x(0:B) CSR2  			R/W(  809x08

  - TMC x(0:B) CSR3  			R/W(  809x0C

  - All TMCs CSRs  				W(  809C00-8090C

73) Group A threshold settings 			R/W(  80A000 – 80A03C

74) Group B threshold settings			R/W(  80A100 – 80A13C

75) Group C threshold settings			R/W(  80A200 – 80A23C

76) Analog Test Pulse amplitude			R/W( 80A300

77) Load threshold and TP-DAC settings		W(80A400

78-80) Group A timing gate registers (Ch. 0-47)	R/W( 80B000, 80B300, 80B600

81-83) Group B timing gate registers (Ch. 0-47)	R/W( 80B100, 80B400, 80B700

84-86) Group C timing gate registers (Ch. 0-47)	R/W( 80B200, 80B500, 80B800

87) Master controller CSR0			R/W( 80C000

88) Master controller CSR1 Error and Status readout	R( 80C100

89) Timing data L1 trigger latency preset		R/W(80C200

90) Test Pulse crossing preset			R/W( 80C204

91) Test Pulse L1 crossing preset			R/W( 80C208

92) ADC data L1 trigger latency 			R/W( 80C20C

93) Group A analog Ch. 0:15 select			R/W( 80C210

94) Group B analog Ch. 16:31 select		R/W( 80C214

95) Group C analog  Ch. 32-47 select		R/W( 80C218

96) Delay buffer page PG0/PG1			R( 80C21C

97) Delay buffer HIT_Or <0:7>			R( 80C220

98) Delay buffer HIT_OR<8:11> plus OUT_EN	R( 80C224

99) L1 self test trigger latency			R/W( 80C228

100) Read output FIFO				R( 80C300

101) Reset output FIFO				W(80C400

102) Reset output FIFO pointer			W(80C500

103) Reset board					W( 80D000

104) Reset TMCs					W( 80D100

105) Reset ADC FIFO				W( 80D200

106) Arm test pulse				W( 80E000

107) Test readout					W( 80E100

SRC:

108) FLEX 10K configure 			W( 000000

109) FLEX 10K flash RAM			R/W(

110) Interrupt vector register			R/W( 080000

111) SRC VME CSR0 				R/W(100000

112) SRC VME CSR1				R( 180000

113) Clear latched errors				W( 200000

114) Reset board					W( 280000

115) L2 & L3 FIFO reset				W( 300000

116) DSP reset					W( 380000

117) Test pulse arm				W(400000

Readout controller

118) SFE_MASK					R/W(480000

119) TO_SET, TO_ERR_ADDR,

SFE_TO_ERR, and FULL_ERR		R/W(480004

120) PG_FULL					R/W(480008

121) L1_COUNT, PAGE				R/W(48000C

Trigger Manager

122) TP_PRE, LAT_PRE				R/W( 500000

123) TP_PRE					R/W( 500004

124) L1TST_PRE				R/W( 500008

125) TP_DLY_PRE				R/W( 50000C

126) BEAM_DLY				R/W( 500010

127) TP_REP_PRE				R/W( 500014

128) LOC_L1_DLY				R/W( 500018

DMA Controller

129) L2 HOTLINK CSR				R/W( 580000

130) L3 HOTLINK CSR				R/W( 580004

Serial port

131) Write command to SCC 			W( 600004

132) Write data to SCC				W( 600008

133) Read command from SCC			R( 600014

134) Read data from SCC				R( 600018

VME commands for DSP access

135) DSP flash RAM address			R/W( 680000 – 69FFFF

136) DSP dual port RAM address			R/W(700000 – 703FFF

137) VME access to port D of the four-port RAM	R/W( 780000 – 780FFF

138) DSP service request-interrupt			W(800000

139) ADC data read address			R( 880000-880014

DSP (own commands)

140) Internal RAM				R/W( 000000 – 001FFF

141) Dual Port Ram				R/W( 400000 – 403FFF

142) ROM (Flash RAM)				R/W( 800000 – 81FFFF

143) Four-Port RAM				R/W( C00000 – C00FFF

I/O Space commands

144) L2 FIFO read				R( 00

145) L1 crossing number read			R( 01

146) Send L3 HOTLINK leading control

byte DSP_D(0:7)				W( 03

147) Send L3 HOTLINK trailing control

byte DSP_D(8:15)				W( 04

148) Send L3 HOTLINK data word DSP_D(0:15)	W( 05

149) L2 turn number read				R( 08

150) L2 crossing number read			R( 09

151) DMA word count and L2 data transfer		W( 1A

# Text boxes

VME

RS-232

For testing, and re-configuring devices

1553

Controller

4-Port RAM

SCC Serial Port Interface

1553 Transceiver

Interface

1553 VME

Interrupt

DSP

SRC

SFE

SLP

VME Processor

MRC

External

Host

Computer

1553

Bus

DATA WORD 1

COMMAND

WORD: T/R = 0

LAST DATA

WORD

STATUS WORD

COMMAND

WORD: T/R = 1

LAST DATA

WORD

FIRST DATA

WORD

STATUS WORD

1553 VME Interrupt Lvl 7

1553 VME Interrupt Lvl 7

SCC VME

Interrupt

Locations: 1 - 33

Locations: 1 - 33

Locations: 64 - 4096

IACK < 7.5(s

IACK < 7.5(s

15 Hz.

Analog

32 words

32 words

6 words x 16

1-bit fields

18 words

15 Hz.

Digital