Jun-97 Rev1.0

Applications Note: G-Link Design for Phenix

Melissa C. Smith, John Writt, Jim Walker, and Adam Ponchak

# Introduction

Efforts to assemble a test fixture to simulate the Timing and Control (T&C) and FEM to DCM links at ORNL have led to some interesting do’s and don’ts associated with G-Link design.  In this applications note, we will cover some of the potential pitfalls associated with the design of a G-Link transmitter (Tx) or receiver (Rx) unit.

# Using the Appropriate Chip Set

There are two components which make up one end of a G-Link: 1) the Hewlett Packard (HP) G-Link chip (Tx or Rx) and 2) the Methode or HP optical component (Tx, Rx, or TRx).  Each of the G-Link chips are available in ECL or TTL versions (see Table 1).  The optical components are available in separate Tx and Rx components from Methode or as a transceiver from HP (see Table 2).

Table 1 HP G-Link Chips

|  | Tx | Rx |
| --- | --- | --- |
| ECL (PECL) | HDMP-1012 | HDMP-1014 |
| TTL | HDMP-1024 | HDMP-1024 |

Table 2 Optical Components

|  | Methode | HP |
| --- | --- | --- |
| Tx | MTM-8510-1-SC-S-S |  |
| Rx | MRM-8510-1-SC-S-S |  |
| TRx |  | HFBR-5305 |

Within Phenix there are three basic types of G-Link connections: 1) T&C Link, 2) FEM to DCM Link, 3) Level 1 Trigger Link.  The T&C link operates at 40 MHz and either the PECL or TTL chip set is appropriate when jitter is not a concern. If the timing jitter specifications are of concern, at this time the PECL version is recommended. Either chip set is appropriate for the FEM to DCM link that operates at 20 MHz. The EmCal and Pad Chambers subsystems must transfer DCM data between FEMs on Day 1 and thus should consider using the PECL version to avoid noise problems.  Finally, the TTL chip set has not been tested for Trigger links operating at 60 MHz.

# Avoiding General G-Link Pitfalls

# Power Supply Filtering

Each of the optical components should be properly bypassed with capacitors and inductors as shown in Figure 1.  Those subsystems affected by a magnetic field and cannot use a ferrite bead inductor will find suitable phenolic core inductors from manufactures such as Delevan.

Figure 1 Power Supply Filtering

# G-Link to Optical Component Connections

The connection between the HP chips and the optical components are differential PECL drive.  In the testing here at ORNL and also at AMES, no termination was necessary if 1) the components were placed close together, 2) traces were of equal length, and 3) impedance was controlled at 50(.  It is critical the differential lines are connected correctly (i.e. optical Rx+ output to the Rx+ input of the HP chip and optical Rx- output to the Rx- input of the HP chip, etc.).

# HP Chip PLL settings

# The HP G-Link chips have two pins to set the locking frequency range of the internal PLL.  These pins are denoted DIV1 and DIV0 in the HP data sheets.  Table 3 shows the frequency ranges for the four possible settings.  The setting DIV1=0 DIV0=0 is suggested for operating frequencies of 60 MHz and 40 MHz.  DIV1=0 DIV0=1 is suggested for 20 MHz operating frequency.

Table 3 G-Link Chip PLL Settings

| Parallel Word Frequency (MHz) | DIV1 | DIV0 |
| --- | --- | --- |
| 35 – 62.5 | 0 | 0 |
| 18 – 42 | 0 | 1 |
| 9 –21 | 1 | 0 |
| 6.3 – 10.5 | 1 | 1 |

# STRBIN Duty Cycle

Input latches on G-Link are triggered only on the positive edges of STRBIN, so STRBIN doesn’t have to be tightly controlled around a 50% duty cycle.  A duty cycle of 50% + 10% is a conservative number. The setup time for data is 6ns.

Note: There is always a clock signal on STRBOUT Tx and Rx. The clock will drift up in frequency, but it will always be present.  Also, with no STRBIN, the Tx will transmit FF0 throught the high-speed DOUT/DOUT* lines.

# Designing a Tx Unit

Table 4 below describes the connections for a G-LINK transmitter chip.  In PECL designs, all lines should be properly terminated according to PECL design guidelines.  Figure 2 shows the Tx timing diagram under normal operations. The appendix includes the reference designs used in the ORNL G-LINK test fixture. Figure 3 shows the necessary circuit for the PLL bypass.

Figure 2 Tx Timing

Table 4 Transmitter Connections

| Pin Name (ECL) | Pin Type | Description |
| --- | --- | --- |
| STRBIN (STRBIN*) | Input | Parallel word strobe frequency clock; Data valid on rising edge |
| HCLKON | Input | GND |
| HCLK/HCLK* | Output | AC couple to a 50( resistor to GND |
| LOUT/LOUT* | Output | AC couple to a 50( resistor to GND |
| LOOPEN | Input | GND |
| DOUT/DOUT* | Output | Connect to optical driver |
| DIV[1:0] | Input | See Table 3 |
| INV |  | NC |
| TEMP/TEMP* |  | NC |
| RST* | Input | Transmitter active low reset |
| D[19:0] | Input | 20 bit parallel data |
| RFD | Output | Re-timed version of ED can use as input to Heap Manager |
| ED | Input | Active high after lock is achieved |
| FF | Input | Vcc |
| CAV* | Input | Active low only when sending control data |
| DAV* | Input | Active low only when sending data |
| FLAGSEL | Input | GND |
| M20SEL | Input | Vcc for 20-bit format; GND for 16-bit format |
| MDFSEL | Input | GND |
| LOCKED | Output | Active high indicates transmitter locked |
| STRBOUT | Output | Copy of STRBIN when transmitter locked |
| EHCLKSEL | Input | GND |
| CAP0A, CAP1A , CAP0B, CAP1B | Input | See Figure 3 |

Figure 3 PLL Bypass Circuit

# Designing a Rx Unit

Table 5 below describes the connections for a G-LINK receiver chip.  In PECL designs, all lines should be properly terminated according to PECL design guidelines. Figure 4 shows the Rx timing diagram under normal operations.  The appendix includes the reference designs used in the ORNL G-LINK test fixture. Figure 3 shows the necessary circuit for the PLL bypass.

Figure 4 Rx Timing

Table 5 Receiver Connections

| Pin Name (ECL) | Pin Type | Description |
| --- | --- | --- |
| TCLKSEL | Input | GND |
| TCLK | Input | NC |
| EQEN | Input | Vcc; Not required when using optical drivers |
| LIN/LIN* | Input | NC |
| LOOPEN | Input | GND |
| DIN/DIN* | Input | Connect to optical receiver |
| DIV[1:0] | Input | See Table 3 |
| FDIS, ACTIVE, STAT1 | Input/ Output | Connect together |
| STAT0 | Output | Active high indicates receiver locked |
| SMRST[1:0] | Input | Active low receiver reset |
| D[19:0] | Output | 20 bit parallel data |
| STRBOUT | Output | Parallel word strobe frequency clock; Data valid on rising edge |
| LINKRDY* | Output | Active low indicates receiver locked |
| FF | Output | NC |
| CAV* | Output | Active low only when receiving control data |
| DAV* | Output | Active low only when receiving data |
| FLAGSEL | Input | GND |
| M20SEL | Input | Vcc for 20-bit format; GND for 16-bit format |
| FLAG | Output | NC |
| ERROR | Output | Asserted when error in received frame |
| TEMP/TEMP* |  | NC |
| CAP0A, CAP1A , CAP0B, CAP1B | Input | See Figure 3 |

# Resetting the Link

The G-Links lock and maintain lock by sending fill frames.  There are two fill frame types available with the HP chips: ff0 and ff1.  In Phenix we will use ff1 which requires that the FF pin on the Tx be pulled high. Also, DAV* and CAV* should be inactive when data is not being transmitted.

The first step in resetting the link and thus establishing lock, is to reset the transmitter unit by activating the RST* pin while holding the ED pin low.  The RST* pin should be held in the active low state for a minimum of 5 clock cycles. Once this cycle is completed, the transmitter’s internal PLL should be locked to the incoming strobe (STRBIN) and the output signal, LOCKED, should be active (high).  Also, the STRBOUT should match STRBIN with a slight phase delay. The ED pin should remain low until the receiver has also been reset and locked.

Once the transmitter is locked, the next step is to reset the receiver and allow it to lock to the carrier frequency.  The SMRST1* and SMRST0* pins should be pulled to the active low state for a minimum of 5 clock cycles.  During this time the receiver’s internal state machine will lock the internal PLL to the carrier frequency.  Once the lock is complete the STAT0 will be active high and LINKRDY* will be active low.  Also, the STRBOUT of the receiver unit should match the STRBIN of the transmitter unit.

A complete timing diagram is shown in Figure 5 below.

Figure 5 Link Reset Timing

# Additional Information

Additional information may be found in the data sheets for each of the components.  The best information on the jitter of the recovered clock on the receiver is published in a technical article: “A Two-chip 1.5 GBd Serial Link Interface”, IEEE Journal of Solid State Circuits vol. 27, no. 12, Dec 1992 pp 1805-1811.

# References

Hewlett-Packard, “HDMP-102K Evaluation Board User’s Guide”, Rev 1.0, February 1997.

Hewlett-Packard, “Reference Guide for the HDMP-101K Evaluation Board”, Rev 1.1, November 1996.

Hewlett-Packard, “Answers to Common G-Link Design Questions”, Rev 2.1, January 1996.

R. C. Walker, et al., “A Two-chip 1.5 GBd Serial Link Interface”, IEEE Journal of Solid State Circuits vol. 27, no. 12, Dec 1992 pp 1805-1811.

# Appendix