ARGOS O/C 37, CLS

Prepared by: A. Goasguen

## Agenda Item D-3: Status of Argos instruments

- Argos 1 instruments :

The Argos instrument onboard NOAA-11 has only 3 DRUs working since a few days after launch (1988). The fourth DRU is in standby. This satellite, launched in September 1988 is very useful because of the situation of its orbital plane.

Argos instruments onboard NOAA-11 and 14 have no redundant receiver. They have an increased telemetry bit rate of respectively 960 and 1200 b/s from 720 b/s.

Argos instruments onboard NOAA-12 has spent 12 years in orbit. It is part of the initial series TN and NOAA-A to G and was manufactured a long time ago.

All three payloads are fully operational.

- Argos 2 instruments:

Argos instruments onboard NOAA-15, 16 and 17 are second generation instruments. They have an increased receiving bandwidth (80 kHz instead of 24 kHz) and an increased telemetry bit rate of 2560 b/s. This leads to an increase of the capacity to process PTT transmission of 3.5 when the entire bandwidth is used.

ADEOS II was launch in December 2002, and the Argos payload was switched on end of January this year. This payload is composed of an Argos 2 receiver, a processor and a downlink transceiver provided by NASDA. Since January, the payload has been fully tested and is operational. It is the first two-way Argos instrument on orbit.

We have now seven operational payloads on orbit. Three are Argos 1 and four are Argos 2.

- Orbital planes:

The figure below shows the repartition of the orbital planes of the seven satellites as of May 2003. As said during the 36th OPSCOMM, it obviously shows the interest of NOAA 12 data for Service Argos.