Appendix C - Comparative Safety Assessment

Introduction

Purpose and Scope

Since ADS-B technology is heavily dependent on a Global Navigation Satellite System, the Surveillance and Broadcast Services (SBS) program was required to identify a backup system or strategy in the event of a GNSS outage - local or global. This Comparative Safety Assessment (CSA) was performed to identify and assess the system safety hazards associated with the proposed alternatives for the backup strategy. The results of this assessment, coupled with the technical evaluations, will serve in selecting the appropriate backup strategy. The CSA provides a listing of system safety hazards associated with each backup strategy alternative, along with a risk assessment for each alternative-hazard combination.  The CSA will aid in identifying the lowest risk alternative(s), from a system safety perspective.

As stated in section 3.1.6 of the Final Program Requirements (FPR) for SBS, the scope of the backup strategy is to maintain ATC Surveillance in the event of a GNSS failure:

- ATC Surveillance application shall continue to operate in the event of GNSS failure.

b.	A backup system or strategy shall be provided with the ADS-B system to ensure that the ATC surveillance application can be provided in the event the navigation source is operating in a degraded state.

The CSA does not address the in-cockpit applications, since the backup strategy is not intended to enable the continued operation of these applications in the event of GNSS failure or navigation source degradation.

The strategies under consideration utilize various technologies to obtain an aircraft’s position. Strategy 1 (Secondary Radar) uses existing primary and secondary surveillance radar (SSR) sensors to determine the aircraft position. Strategy 2 (Passive Multilateration) is comprised of several ground stations that triangulate the location of the aircraft based on the time of arrival of the ADS-B message. Strategy 3 (Active Multilateration) uses ground stations to interrogate aircraft transponders to determine position. Strategy 4 (SSR, DME/DME/IRU for Air Transport (AT) and SSR, eLoran for General Aviation (GA)) uses Secondary Radar in high density airspace, and in medium density airspace, the position is obtained on the aircraft through Distance Measuring Equipment (DME) (Air Transport) or eLoran (General Aviation). Equipment on the aircraft communicates with ground-based facilities and uses the time of arrival to calculate position. Strategy 5 (SSR, DME/DME/IRU, SATNAV for AT and SSR, SATNAV for GA) uses the DME/DME/IRU technology as well as additional satellite positioning systems that are to be developed in the near future. Strategy 6 (SATNAV only) provides a more diverse and robust GNSS instead of an alternate technology system, backing up the current GPS L1 with GPS L5 and/or Galileo. Strategy 7 (Terminal SSR and SATNAV) uses SSR in terminal airspace and SATNAV in en route airspace.

Background

Automatic Dependent Surveillance-Broadcast (ADS-B) is an advanced surveillance technology that enables equipped aircraft or surface vehicles to broadcast their identification, position, altitude, velocity, and other information. Since the position information is normally derived from the Global Positioning System (GPS) and broadcast approximately once per second, it provides improved accuracy and more timely information updates than conventional surveillance. The improved positional accuracy and the ability to provide additional aircraft-derived flight parameters (flight objects or flight data message elements) will result in enhanced surveillance in the NAS. ADS-B is automatic because no external stimulus is required; it is dependent because it relies on on-board navigation sources and onboard broadcast transmission systems to provide surveillance information to other users. The aircraft or vehicle originating the broadcast may or may not have knowledge of which users, aircraft or ground-based, are receiving its broadcast.

ADS-B technology also enables the implementation of Traffic Information Service-Broadcast (TIS-B), ADS-B Rebroadcast (ADS-R), and Flight Information Service-Broadcast (FIS-B) to support enhanced situational awareness and other applications intended for air crews. TIS-B service provides traffic information to receiver-equipped aircraft and surface vehicles based on the conventional radar returns received for non-ADS-B equipped aircraft. ADS-R provides traffic information to equipped aircraft based on ADS-B transmission from aircraft on independent data links. FIS-B provides weather and NAS Status information to equipped aircraft.

Per the FAA’s ADS-B Link Decision, two data link technologies, the 1090 MHz extended squitter (1090ES) and the 978 MHz Universal Access Transceiver (UAT) have been approved for use in the NAS. It is anticipated that air transport category aircraft will equip with the 1090ES link and general aviation will equip with the UAT link. Both the UAT and 1090ES links support TIS-B and ADS-R services. Only UAT supports FIS-B service.

The Surveillance and Broadcast Services Safety Risk Management Panel prepared and conducted the Preliminary Hazard Analysis (PHA) for seven applications selected for the near-term NAS implementation:

- ATC Surveillance

- Weather and NAS Status Situational Awareness

- Enhanced Visual Acquisition

- Enhanced Visual Approaches

- Final Approach and Runway Occupancy Awareness

- Airport Surface Situational Awareness

- Conflict Detection

Rulemaking is planned to require aircraft equipage with ADS-B transmit capability to support the ATC Surveillance application. On the other hand, equipping with avionics necessary to support the remaining applications is voluntary.

SBS Description

System Description

ADS-B is an advanced surveillance technology that enables equipped aircraft, or surface vehicles, to broadcast their identification, position, altitude, velocity, and other information.  Since the position information is normally derived from the Global Positioning System (GPS) and broadcast approximately once per second, it provides improved accuracy and more timely information updates than conventional surveillance.  The superior positional accuracy and the ability to provide additional aircraft-derived flight parameters (flight objects or flight data message elements) will result in enhanced surveillance in the NAS.  ADS-B is automatic because no external stimulus is required; it is dependent because it relies on on-board navigation sources and onboard broadcast transmission systems to provide surveillance information to other users.  The aircraft or vehicle originating the broadcast may or may not have knowledge of which users, aircraft or ground-based, are receiving its broadcast.

ADS-B technology additionally facilitates the implementation of Traffic Information Service-Broadcast (TIS-B), ADS-B Rebroadcast (ADS-R), and Flight Information Service-Broadcast (FIS-B) to support enhanced situational awareness and other applications.  TIS-B service provides traffic information to equipped aircraft and surface vehicles based on the conventional radar returns received for non-equipped aircraft. ADS-R provides traffic information to equipped aircraft based on ADS-B transmission from aircraft on independent data links. FIS-B provides weather and NAS Status information to equipped aircraft.

Per the FAA’s ADS-B Link Decision, two data link technologies, the 1090 MHz extended squitter (1090ES) and the 978 MHz Universal Access Transceiver (UAT) have been approved for use in the NAS.  It is anticipated that air transport category aircraft will equip with the 1090ES link and general aviation will equip with the UAT link.

The introduction of ADS-B services into the NAS will enable some well established applications, currently supported by radar and other existing surveillance sources, and facilitate the introduction of new applications, that promise to improve safety and increase capacity.  See the FAA’s Surveillance and Broadcast Services Concept of Operations (CONOPS) for further details on ADS-B Services and Applications. Table C1-1 summarizes the relationship between ADS-B related applications, services, and SBS system operational system functions (described in Section 1.3.2).

Table C1-1: Applications, Services, and Functions

| ADS-B Enabled Applications | Services | Broadcast Services Function | Link-Specific Processing Function | ATC Automation Function | Aircraft / Vehicle Function |
| --- | --- | --- | --- | --- | --- |
| ATC Surveillance | ADS-B |  | X | X | X (Transmit) |
| Airport Surface Situational Awareness (ASSA) Final Approach Runway Occupancy (FAROA) Enhanced Visual Acquisition (EVAcq) Enhanced Visual Approach (EVApp) Conflict Detection (CD) | ADS-B (only Aircraft/ Vehicle Functionality Required) ADS-R TIS-B* | X | X |  | X (Receive) |
| Weather and NAS Status Situational Awareness | FIS-B | X | X |  | X (Receive) |

* TIS-B, as specified herein, supports the ASSA and EVAcq applications only

The Surveillance and Broadcast Services System’s functions (Aircraft/Vehicle, Link Specific Processing, Broadcast Services, and ATC Automation) provide the ADS-B services that support ADS-B applications.  Figure C1-1 shows the relationship between the principle and sub-system components:

- The Aircraft/Vehicle function is identified as the components located in the avionics section at the top of the illustration.

- The Link Specific function is identified as the air interfaces and 1090ES and UAT receive/transmit components located mid-illustration.

- The Broadcast Services function is identified as the ground interfaces and associated TIS-B and FIS-B processors.

- ATC Automation.

TIS-B and FIS-B services require all functions except ATC Automation.  The ADS-B Rebroadcast (ADS-R) Service is a subset of the fundamental TIS-B Service.

Figure C1-1:  SBS Architecture

Functional Description

The ADS-B System can be logically divided into five major functions (see Figure C1-2):

- Aircraft/Vehicle Function

- Link-Specific Processing (LSP) Function

- Broadcast Services (BCS) Function

- ATC Automation Function

- Maintenance Function

The first four functions are operational, while the Maintenance Function provides for the control and monitoring of the operational functions.  Note that only the operational functions are listed in Table C1-1, as the Maintenance Function supports the services and applications in an indirect manner.  The Aircraft/Vehicle Function resides in participant aircraft and surface vehicles.  The ATC Automation Function resides in participant automation systems.  The Link-Specific Processing, Broadcast Services, and Maintenance Functions form the ADS-B ground infrastructure.

Figure C1-2:  SBS System Functions

The ADS-B System receives surveillance reports, from various NAS systems, to support the TIS-B service and weather and NAS status information, from government and commercial sources, to support the FIS-B service.  The ADS-B system distributes ADS-B Reports to authorized user systems.  The status of the GNSS and other NAS systems is also an input to the ADS-B System to determine degraded operations or an outage of these systems.

Aircraft/Vehicle Function

The Aircraft/Vehicle includes a transmit capability that supports all applications and a receive capability for aircraft/vehicle based applications.

The Aircraft/Vehicle Function is the source of ADS-B information.  The Function derives state vector information, using GNSS or another navigation source, and determines the associated integrity and accuracy indicators.  The Aircraft/Vehicle function also ascertains altitude information from a qualified barometric altitude source.  Vehicles for surface use only could use a pre-programmed source for altitude information.  The Function collects other ownship data, potentially including weather related measurements, and provides a means for crew input of additional information, such as aircraft identification data.  The Aircraft/Vehicle Function encodes and broadcasts ADS-B Messages, conveying the collected information.

The Aircraft/Vehicle Function receives and decodes ADS-B Messages transmitted by other Aircraft/Vehicles equipped with the same data link and TIS-B and ADS-R Messages transmitted by the ADS-B LSP Function.  Aircraft/Vehicle Functions equipped with the UAT data link additionally receive and decode FIS-B Messages transmitted by the LSP Function. The Aircraft/Vehicle Function processes and displays the information conveyed in received messages.

Link-Specific Processing Function

The LSP Function provides the ADS-B System transmit/receive functionality on the ground.  The Function receives ADS-B Messages from equipped aircraft and surface vehicles, formats the associated ADS-B Reports, and distributes them to ATC Automation, the BCS Function, and other authorized users.  LSP transmits TIS-B, ADS-R, and FIS-B Messages as directed by the BCS Function.  This Function supports all services and applications.

Broadcast Services Function

The BCS Function processes, including tracking, filtering, and applying quality indicators, surveillance reports from external sources and ADS-B Messages from the LSP Function.  Broadcast Services generates TIS-B and ADS-R Reports for transmission as TIS-B and ADS-R Messages by LSP.  The BCS Function additionally processes weather and NAS status data from external sources and generates applicable FIS-B Reports for transmission as FIS-B Messages by LSP.  This Function supports TIS-B, ADS-R, and FIS-B Services, but is not required for ADS-B.  It supports all applications except ATC Surveillance.

ATC Automation Function

The ATC Automation Function uses ADS-B surveillance data similar to its use of radar system surveillance information.  The Function supports environments with only ADS-B Surveillance as well as those having both ADS-B and radar surveillance.  ATC Automation validates the position information provided in ADS-B Reports by comparing it with reports from other surveillance sources, as available.  The Function associates the ADS-B Report data with filed flight plans, creates and updates tracks, and displays target and emergency information to Air Traffic Specialists.  ATC Automation performs safety function processing, including Minimum Safe Altitude Warning, Conflict Alert, and Restricted Airspace Monitoring, using ADS-B and radar data, as available, and displays any associated alerts.

Maintenance Function

The Maintenance Function provides for the control and monitoring of the ADS-B ground infrastructure operational functions, Link-Specific Processing and Broadcast Services.  Control includes the setting of configuration items, the download of new software, the request for read back of monitored parameter values, and any other actions necessary to control the operation and support the maintenance of the system.  Monitoring includes the generation of alerts and alarms as well as the injection of Health Status Messages (test targets) into the LSP Function, and any other monitoring activities necessary to support the operation and maintenance of the system.  The Maintenance Function uses information gathered in monitoring the system to generate Status Reports, containing high-level alarm and alert information and system counts, such as number of ADS-B Messages received, number of TIS-B Reports generated, etc. and distributing them to the ATC Automation Function.

The Maintenance Function additionally monitors ADS-B reception and the GNSS to analyze coverage and identify potential quality issues with Aircraft/Vehicle performance.  The Function provides an interface to systems engineers and technicians for use in control and monitoring of the ADS-B System.

Backup Strategy Alternatives

Addressing the requirement from the fPR, the backup strategy alternatives listed below provide a means for obtaining aircraft position in order to enable the ATC Surveillance application.

Each alternative uses primary radar to mitigate single-aircraft avionics failures in the terminal domain but not in the en route domain. Therefore, primary radar functions shown in each block diagram only apply to terminal surveillance.  The primary radar transmits a radio frequency (RF) pulse. The radar system processes the reflected signal to determine azimuth and slant range. This information is supplied to automation and displayed to ATC.

Alternative 1: Secondary Radar

The secondary radar alternative involves using existing secondary radar sensors to interrogate aircraft equipped with ATCRBS and/or Mode S transponders. The aircraft responds with aircraft information, such as beacon code and altitude. The radar receives the reply and processes the antenna position and time of reply to determine the azimuth and slant range for the aircraft. The target report is generated for the aircraft and sent to automation for tracking and alerting.

This alternative employs a reduced version of the current secondary radar network to cover the required airspace and primary radars in terminal areas.

Alternative 2: Passive Multilateration

The passive multilateration alternative obtains the aircraft position by using three or more ground stations that receive the broadcast ADS-B message. The time-of-arrival (TOA) of the messages are measured for each of the ground stations. The ground stations are synchronized through a reference signal or clock, and this point of reference is used to calculate a time-difference-of-arrival (TDOA). A central processor uses this information to determine the aircraft position. Other target data, such as aircraft identity and barometric altitude, are obtained by decoding the ADS-B message.

Figure C2-1:  Functions of Secondary Radar Alternative

Figure C2-2:  Functions of Passive Multilateration Alternative

Alternative 3: Active Multilateration

Active multilateration relies on three or more geographically distributed ground stations successfully interrogating aircraft equipped with ATCRBS and/or Mode S transponders. The ground stations measure the TOA for the same transponder reply. As with passive multilateration, the aircraft position is determined by joint processing of the TDOA measurements, which are calculated with respect to the synchronized time source. Aircraft identity and barometric altitude are determined by decoding the information in the transponder replies.

Figure C2-3:  Functions of Active Multilateration Alternative

Alternative 4: SSR, DME/DME/IRU for AT and SSR, eLoran for GA

Distance Measuring Equipment (DME) and Enhanced LOng RAnge Navigation (eLoran) are both navigation systems, with DME common to Air Transport (AT) and eLoran common to General Aviation (GA). The position is obtained on the aircraft and provided to ATC Surveillance via the ADS-B broadcast message.

The DME/DME/IRU approach consists of equipment on the aircraft that interrogates DME ground facilities. The ground facilities respond with a fixed delay. The aircraft uses the TOAs from the responses from two or more DME facilities and the known locations of the DME facilities (from a database on the aircraft) to determine the aircraft position. Inertial Reference Unit (IRU) is used to augment DME by mitigating the impact of gaps in coverage. IRU determines the aircraft position by using inertial metrics and last-known positions.

DME/DME/IRU is not able to support five nautical mile separation in medium density airspace.

The present Loran system, Loran-C, is comprised of a series of ground station groups (chains). The chains are made up of three to six ground stations, with one station serving as the master. The other stations are synchronized to the master through a radio frequency (RF) pulse that is transmitted by the master station. Most of the 24 U.S. Loran stations have been modernized to support eLoran performance. When that process is complete, the stations will operate in an “all-in-view” mode, which provides better system availability and integrity. All stations will be synchronized to Coordinated Universal Time (UTC).

The ground stations transmit a periodic series of nine RF pulses in the 90-110 kHz frequency band. The aircraft uses the TOAs of the pulses from three or more ground stations and the known locations of the ground stations (from a database on the aircraft) to determine the two-dimensional position of the aircraft. The ninth pulse in each broadcast is modulated to capture differential accuracy corrections (for maritime applications), station identification, and integrity information.

Figure C2-4:  Functions of SSR, DME/DME/IRU for AT and SSR,

eLoran for GA Alternative

Alternative 5: SSR, DME/DME/IRU, SATNAV for AT and SSR, SATNAV for GA

This alternative uses SSR in high-density airspace. For AT in medium density airspace, DME/DME/IRU and Satellite Navigation (SATNAV, see Section C2.6) are used for backup. For GA in medium density airspace, SATNAV is used.

Figure C2-5:  Functions of SSR, DME/DME/IRU, and SATNAV for AT,

and SSR and SATNAV for GA

Alternative 6: SATNAV Only

The SATNAV alternative continues to use a form of GNSS as its source for position, however, the probability of loss compared to GPS alone decreases significantly by providing more backup satellite sources. Currently, Global Positioning System (GPS) L1 is the only GNSS source used by ADS-B. The L5 GPS signal and the European Galileo system provide additional signals that are to be implemented within the next ten years. In the event of a GPS L1 loss of service, the ADS-B would default to one of the other GNSS signals to obtain the aircraft position.

Although this approach mitigates the likelihood of a GNSS outage, it does not mitigate multi-frequency interference.

Figure C2-6:  Functions of SATNAV Only Alternative

Alternative 7: Terminal SSR and SATNAV

By using secondary radar in high-density terminal areas in addition to the SATNAV strategy, the multi-frequency interference is mitigated.

Figure C2-7:  Functions of Terminal SSR and SATNAV Alternative

Assessment Methodology

This CSA was developed by the SBS Program Office as a quick turn-around safety assessment using guidance contained in the NAS System Safety Handbook (SSH). This assessment, which has not yet been reviewed by the ATO-S System Safety Working Group (SSWG), will require an update to comply with the CSA content and format requirements outlined in the NAS Systems Safety Management Program (SSMP).

After determining and analyzing the pertinent system functions for providing ATC Surveillance, an initial set of hazards was identified. Only ATC Surveillance application hazards were evaluated in the CSA, since the purpose of the backup strategy is to maintain ATC Surveillance in the event of a GNSS failure.  No new hazards were evaluated for any strategy, though a hazard for loss of aircraft navigation should be considered in a future analysis.

The following ATC Surveillance hazards were evaluated in the CSA:

- H1 Loss of ATC Surveillance (All Aircraft)

- H2 Loss of Surveillance (Single Aircraft)

- H17 Loss of Surveillance (Multiple Aircraft)

Hazards associated with inaccurate position, altitude, and identification are addressed in the SBS Preliminary Hazard Analysis (PHA).  It was not necessary to address these hazards in the CSA for several reasons. First, the backup strategies were defined to ensure that accuracy requirements for terminal and en route ATC separation standards are met; therefore, hazards that dealt with inaccurate position would not function as a discriminator in comparing the alternatives.  Also, the source for altitude and identification data was not affected by any of the backup strategies, and the risk already identified in the SBS PHA does not change as a function of alternative.

While the hazards evaluated in this CSA are similar to those addressed in the SBS PHA, system states that affected the risk assessment varied.  For example, the hazards in the SBS PHA were analyzed for the terminal domain, whereas the CSA considered both en route and terminal domains.  Therefore, the assessed risk levels from the CSA should not be compared to those assessed in the SBS PHA, as it would not be an equivalent comparison.  The hazards identified in the SBS PHA will ultimately be re-evaluated based on the selected backup strategy.

A multi-step process was employed to determine the risk associated with each strategy – hazard combination.  First, functional flow block diagrams, provided in Section 5, were developed for each backup strategy alternative based on the draft technical descriptions.  These block diagrams were used to identify potential faults or failure modes for each backup strategy that could cause a hazard. Fault trees, provided in Section 8, were prepared using the functional flow block diagrams and technical descriptions of each strategy.  Each fault tree represents the SBS system and backup strategy faults that, if present in a certain combination, result in a hazard.  Individual faults were assigned a likelihood of occurrence derived from requirements documentation, technical description information, engineering judgment, or a combination thereof.  Fault tree analysis software was used to calculate the probability of the top-level fault occurring (i.e., the hazard).  Next, event trees, provided in Section 8, were developed for each hazard to represent the possible system state variables, actions subsequent to the hazard, and resultant range of hazard effects.  Probabilities associated with certain system state variables were also modified from the original event trees presented in the SBS PHA.  Effects and severities were assigned to each path (i.e., set of branches) in the event trees, and likelihoods for each path were calculated. For each event tree path, the combined likelihood of the hazard occurring and that particular path was calculated.  Worst case risk was determined by comparing the total likelihood and severity pairs, and selecting the maximum resultant risk.

Risk Definitions

Severity and likelihood definitions contained in the NAS SSMP are provided below. For more information regarding these definitions, refer to FAA Advisory Circular 25.1309-1A, “System Design Analysis”.

Table C3-1:  Severity Definitions

| Effect on | Hazard Severity Classification |
| --- | --- |
|  | No Safety Effect (5) | Minor (4) | Major (3) | Hazardous (2) | Catastrophic (1) |
| General |  | Does not significantly reduce system safety. Required actions are within operator's capabilities. Includes (see below): | Reduces the capability of the system or operators to cope with adverse operating condition to the extent that there would be a (see below): | Reduces the capability of the system or the operator's ability to cope with adverse conditions to the extent that there would be a (see below): | Total loss of systems control such that (see below): |
| Air Traffic Control | Slight increase in ATC workload | Slight reduction in ATC capability, or significant increase in ATC workload | Reduction in separation as defined by a low/moderate severity operational error (as defined in FAA Order 7210.56), or significant reduction in ATC capability | Reduction in separation as defined by a high severity operational error (as defined in FAA Order 7210.56), or a total loss of ATC (ATC Zero) | Collision with other aircraft, obstacles, or terrain |
| Flying Public | - No effect on flight crew - Has no effect on safety -Inconvenience | - Slight increase in workload - Slight reduction in safety margin or functional capabilities - Minor illness or damage - Some physical discomfort | - Significant increase in flight crew workload - Significant reduction in safety margin or functional capability - Major illness, injury, or damage - Physical distress | - Large reduction in safety margin or functional capability - Serious or fatal injury to small number - Physical distress/ excessive workload | Outcome would result in: - Hull loss - Multiple fatalities |

Table C3-2:  Likelihood Definitions

|  | NAS Systems | Flight Procedures | ATC Operational |
| --- | --- | --- | --- |
|  | Quantitative | Qualitative |  | Periodicity |
|  |  | Individual Item/System | ATC Service/ NAS Level System |  | Per Facility | NAS-wide |
| Frequent A | Probability of occurrence per operation/ operational hour is equal to or greater than 1x10-3 | Expected to occur about once every 3 months for an item | Experienced continuously in the system | P ≥ 1 x 10-5 | Expected to occur more than once per week | Expected to occur more than every 1-2 days |
| Probable B | Probability of occurrence per operation/ operational hour is less than 1x10-3, but equal to or greater than 1x10-5 | Expected to occur about once per year for an item | Expected to occur frequently in the system |  | Expected to occur about once every month | Expected to occur about several times per month |
| Remote C | Probability of occurrence per operation/ operational hour is less than or equal to 1x10-5 but equal to or greater than 1x10-7 | Expected to occur several times in life cycle of an item | Expected to occur numerous times in system life cycle | 10-5 > P ≥ 10-7 | Expected to occur about once every year | Expected to occur about once every few months |
| Extremely Remote D | Probability of occurrence per operation/ operational hour is less than or equal to 1x10-7 but equal to or greater than 1x10-9 | Unlikely to occur, but possible in an item’s life cycle | Expected to occur several times in the system’s life cycle | 10-7 > P ≥ 10-9 | Expected to occur about once every 10-100 years | Expected to occur about once every 3 years |
| Extremely Improbable E | Probability of occurrence per operation/ operational hour is less than 1x10-9 | So unlikely that it can be assumed that it will not occur in an item’s life cycle | Unlikely to occur, but possible in system life cycle | P < 10-9 | Expected to occur less than once every 100 years | Expected to occur less than once every 30 years |

Note: Table C3-2 includes corrections for errata contained in SSMP version 10 Table 4.2-2.  Likelihood definitions for “Probable” and “Frequent” (which are reversed in the SSMP) and mathematical inequality expressions are corrected in the table above.

|  | No Safety Effect 5 | Minor 4 | Major 3 | Hazardous 2 | Catastrophic 1 |
| --- | --- | --- | --- | --- | --- |
| Frequent A |  |  |  |  |  |
| Probable B |  |  |  |  |  |
| Remote C |  |  |  |  |  |
| Extremely Remote D |  |  |  |  |  |
| Extremely Improbable E |  |  |  |  |  |
|  |  | High |  | * Unacceptable with single point and common cause failures |
|  |  | Medium |  |  |
|  |  | Low |  |  |

Figure C3-3:  Risk Assessment Matrix

Assumptions

In identifying and assessing the hazards that apply to the SBS backup strategy, the following assumptions were made. The SBS FPR only explicitly called out the ATC Surveillance application to be supported by the backup strategy. Though some of the strategies presented may still have the capability to support the other applications, hazards specific to those applications were not addressed in this assessment, as they may not apply to all of the strategies. Accordingly, since these applications may not be available in the event of a switchover to backup, it is assumed the pilot and ATC would be notified.

Data Sources

Quantitative data was used whenever it was available. If quantitative data was not available, qualitative numbers were provided by subject matter experts (SMEs).  Probability of failure numbers for existing systems in the NAS were calculated from availability specifications for the most common systems currently in use (ASR-9, ATCBI-6, ASDE-X).  The availability of DME/DME/IRU and eLoran were each 99.9%, as indicated in the technical descriptions provided by the SMEs.  The SATNAV system was given a single-frequency availability of 99.9%, as a worst-case value.  Probabilities of detection for SSR, PSR and Multilateration were taken from the system specifications and used for hazards H2 and H17.  Transponder probability of failure was given as 10-5 for GA; the probability would only be lower for Air Transport (AT), so 10-5 was used for transponder failure in general.  This number was also applied for other avionics, such as DME and eLoran.

Results

Risk Assessment Ratings

Based on the CSA, each alternative had acceptable levels of risk (i.e., there were no high risks). The assessed risk for each alternative – hazard combination is plotted in the risk matrix and listed in the table below.  Different symbols are used to represent the alternative backup strategies.  Each symbol is annotated with the number of hazards.

Figure C4-1:  Risk Assessment Matrix for Backup Strategies

Table C4-1:  Risk per Alternative-Hazard Combination

| No. | Hazard | 1: SSR | 2: Passive ML | 3: Active ML | 4: SSR, DDI & eLoran | 5: SSR, DDI & SATNAV | 6: SATNAV Only | 7: SATNAV & SSR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| H1 | Loss of ATC Surveillance (All Aircraft) | 4B (Med) | 4B (Med) | 4B (Med) | 4B (Med) | 4B (Med) | 4B (Med) | 4B (Med) |
| H2 | Loss of Surveillance (Single Aircraft) | 4A (Med) | 4A (Med) | 4A (Med) | 4A (Med) | 4A (Med) | 4A (Med) | 4A (Med) |
| H17 | Loss of Surveillance (Multiple Aircraft) | 4C (Low) | 4B (Med) | 4B (Med) | 4A (Med) | 4A (Med) | 4A (Med) | 4C (Low) |

The worst, credible outcome for each of the hazards was a significant increase in ATC workload, which is classified as a “Minor” (4) severity.  While higher severity outcomes were evaluated, the likelihood of occurrence for those scenarios was often several orders of magnitude below “Extremely Improbable,” and therefore deemed not credible from an SMS perspective.  The likelihood for the loss of surveillance for all aircraft (H1) did not vary with the different strategies, as automation and power system failures were the primary drivers for the hazard (the alternative backup strategies are not intended to mitigate the probability of automation or power system failure). The likelihood for the loss of surveillance for a single aircraft (H2) is primarily influenced by avionics failures.  For the analysis, it was assumed that the probability of failures of ADS-B avionics, DME/DME/IRU avionics, and transponders were equivalent.  The likelihoods varied from “Remote” (C) to “Frequent” (A) for the risk of losing surveillance for multiple aircraft (H17).  The likelihood for hazard H17 was driven by the probability of detection for SSR (for alternative 1) and Multilateration (for alternatives 2 and 3).  The probability of ground station faults influence the likelihood for hazard H17 in the case of navigation based alternatives.  Because systems employed for each alternative depended on the type of airspace, hazards were evaluated separately for terminal and en route airspace.  Then the maximum resultant risk was assigned to that hazard.  For hazards H2 and H17, the en route airspace resulted in the maximum risk, primarily due to the lack of Primary Surveillance Radar.

The table below summarizes the results of the fault tree and event tree analyses used to determine the overall risk for each alternative-hazard combination.

Table C4-2:  Likelihood Components per Alternative-Hazard Combination

| Strategy | Hazard / Cause ID | Description | Fault Tree Top-Level Event Likelihood (A) | Worst Case, Credible Event Tree Path | Likelihood for Event Tree Path N (B) | Hazard Likelihood (A) x (B) | Hazard Severity | Risk |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Terminal | En Route |  |  |  |  |  |
| Alt 1 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 1 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 1 | H17 | Loss of surveillance (multiple aircraft) | 10-10 | 10-6 | vii | 0.999999 | 10-6 | 4 | 4C (Low) |
| Alt 2 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 2 | H2 | Loss of surveillance (single aircraft) | 10-4 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 2 | H17 | Loss of surveillance (multiple aircraft) | 10-9 | 10-5 | vii | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 3 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 3 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 3 | H17 | Loss of surveillance (multiple aircraft) | 10-9 | 10-5 | vii | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 4 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 4 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-3 | vii | 0.999999 | 10-3 | 4 | 4A (Med) |
| Alt 4 | H17 | Loss of surveillance (multiple aircraft) | 10-10 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 5 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 5 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-3 | vii | 0.999999 | 10-3 | 4 | 4A (Med) |
| Alt 5 | H17 | Loss of surveillance (multiple aircraft) | 10-10 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 6 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 6 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-3 | vii | 0.999999 | 10-3 | 4 | 4A (Med) |
| Alt 6 | H17 | Loss of surveillance (multiple aircraft) | 10-2 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |

Table C4-2 (ctd):  Likelihood Components per Alternative-Hazard Combination

| Strategy | Hazard / Cause ID | Description | Fault Tree Top-Level Event Likelihood (A) | Worst Case, Credible Event Tree Path | Likelihood for Event Tree Path N (B) | Hazard Likelihood (A) x (B) | Hazard Severity | Risk |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Terminal | En Route |  |  |  |  |  |
| Alt 7 | H1 | Loss of ATC surveillance (all aircraft) | 10-5 | 10-5 | vi | 0.999999 | 10-5 | 4 | 4B (Med) |
| Alt 7 | H2 | Loss of surveillance (single aircraft) | 10-3 | 10-2 | vii | 0.999999 | 10-2 | 4 | 4A (Med) |
| Alt 7 | H17 | Loss of surveillance (multiple aircraft) | 10-10 | 10-6 | vii | 0.999999 | 10-6 | 4 | 4C (Low) |

Analysis Backup

Fault Trees

Fault trees were used as to determine one component of the overall hazard likelihood.  One fault tree is shown for each alternative-hazard combination.  Some alternatives used a different system for terminal airspace and en route airspace.  In the alternatives where a Primary Surveillance Radar (PSR) was not present, the faults associated with the PSR were mathematically removed (though still shown in the fault tree) by assigning a probability of 0% if it was under an “OR” gate or assigning a probability of 100% if it was under an “AND” gate.  Shaded events in each tree denote backup strategy specific faults.

Table C5-1 indicates which fault trees were used to calculate the likelihood, based on the technical descriptions for the alternatives.

Event Trees

Event trees are used in combination with fault trees to aid in identifying the worst, credible outcome.  Since the severity of a hazard is greatly influenced by the circumstances under which it occurs, the event trees help identify the most severe outcome that can realistically happen.  While it is possible that a collision could occur with any of the hazards examined in this assessment, certain conditions would have to be present in a particular combination and several existing controls would have to fail.  Therefore, the likelihood of a collision occurring is not credible.

Table C5-1:  Fault Trees by Airspace

| Hazard | Airspace | Alt 1 | Alt 2 | Alt 3 | Alt 4 | Alt 5 | Alt 6 | Alt 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| H1 | Terminal | Fig. C5-1 | Fig. C5-4 | Fig. C5-7 | Fig. C5-1 | Fig. C5-1 | Fig. C5-16 | Fig. C5-19 |
|  | En Route | Fig. C5-1 | Fig. C5-4 | Fig. C5-7 | Fig. C5-10 | Fig. C5-13 | Fig. C5-16 | Fig. C5-16 |
| H2 | Terminal | Fig. C5-2 | Fig. C5-5 | Fig. C5-8 | Fig. C5-2 | Fig. C5-2 | Fig. C5-17 | Fig. C5-20 |
|  | En Route | Fig. C5-2 | Fig. C5-5 | Fig. C5-8 | Fig. C5-11 | Fig. C5-14 | Fig. C5-17 | Fig. C5-17 |
| H17 | Terminal | Fig. C5-3 | Fig. C5-6 | Fig. C5-9 | Fig. C5-3 | Fig. C5-3 | Fig. C5-18 | Fig. C5-21 |
|  | En Route | Fig. C5-3 | Fig. C5-6 | Fig. C5-9 | Fig. C5-12 | Fig. C5-15 | Fig. C5-18 | Fig. C5-18 |

Figure C5-1:  Strategy 1 - Hazard H1

Figure C5-2:  Strategy 1 - Hazard H2

Figure C5-3:  Strategy 1 - Hazard H17

Figure C5-4:  Strategy 2 - Hazard H1

Figure C5-5:  Strategy 2 - Hazard H2

Figure C5-6:  Strategy 2 - Hazard H17

Figure C5-7:  Strategy 3 - Hazard H1

Figure C5-8:  Strategy 3 - Hazard H2

Figure C5-9:  Strategy 3 - Hazard H17

Figure C5-10:  Strategy 4 - Hazard H1

Figure C5-11:  Strategy 4 - Hazard H2

Figure C5-12:  Strategy 4 - Hazard H17

Figure C5-13:  Strategy 5 - Hazard H1

Figure C5-14:  Strategy 5 - Hazard H2

Figure C5-15:  Strategy 5 - Hazard H17

Figure C5-16:  Strategy 6 - Hazard H1

Figure C5-17:  Strategy 6 - Hazard H2

Figure C5-18:  Strategy 6 - Hazard H17

Figure C5-19:  Strategy 7 - Hazard H1

Figure C5-20:  Strategy 7 - Hazard H2

Figure C5-21:  Strategy 7 - Hazard H17

This page intentionally blank

| H1 | Aircraft on collision course? | TCAS present? | TCAS success-fully resolves traffic conflict? | See and avoid / maneuver successful? | Consequence |
| --- | --- | --- | --- | --- | --- |
|  |  | Yes | Yes | Null | Major (3) – Signif. reduction in safety margin |
|  |  |  |  | Yes | Hazardous (2) – Large reduction in safety margin |
|  |  |  | No |  |  |
|  | Yes |  |  | No | Catastrophic (1) - Collision |
| Failure: Hazard occurs |  | No |  |  |  |
|  |  |  |  | Yes | Major (3) – Signif. reduction in safety margin |
|  |  |  | Null |  |  |
|  |  |  |  | No | Catastrophic (1) - Collision |
|  | No | Null | Null | Null | Minor (4) – Signif. ATC workload increase |

Figure C5-22:  Event Tree for Hazard H1

| H2, H17 | Aircraft on collision course? | ATC detects & resolves problem? | TCAS present? | TCAS success-fully resolves traffic conflict? | See and avoid / maneuver successful? | Consequence |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Yes | Null | Null | Null | Minor (4) – Signif. ATC workload increase |
|  |  |  |  | Yes | Null | Major (3) – Signif. reduction in safety margin |
|  |  |  | Yes |  | Yes | Hazardous (2) – Large reduction in safety margin |
|  | Yes |  |  | No |  |  |
| Failure: Hazard occurs |  | No |  |  | No | Catastrophic (1) - Collision |
|  |  |  |  |  | Yes | Major (3) – Signif. reduction in safety margin |
|  |  |  | No | Null |  |  |
|  |  |  |  |  | No | Catastrophic (1) - Collision |
|  |  | Yes | Null | Null | Null | Minor (4) – Signif. ATC workload increase |
|  | No |  |  |  |  |  |
|  |  | No | Null | Null | Null | Minor (4) – Signif. ATC workload increase |

Figure C5-23:  Event Tree for Hazards H2, H17

Table C5-2:  Event Tree Paths for Hazard H1

| Event Tree Path | On collision course? | Likelihood | TCAS equipped? | Likelihood | TCAS successful? | Likelihood | See & avoid successful? | Likelihood | Event Tree Calc. Likelihood | Severity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i | Y | 1.00000E-06 | Y | 0.6 | Y | 0.9 | Null | N/A | 5.40000E-07 | 3 |
| ii | Y | 1.00000E-06 | Y | 0.6 | N | 0.1 | Y | 0.001 | 6.00000E-11 | 2 |
| iii | Y | 1.00000E-06 | Y | 0.6 | N | 0.1 | N | 0.999 | 5.99400E-08 | 1 |
| iv | Y | 1.00000E-06 | N | 0.4 | Null | N/A | Y | 0.001 | 4.00000E-10 | 3 |
| v | Y | 1.00000E-06 | N | 0.4 | Null | N/A | N | 0.999 | 3.99600E-07 | 1 |
| vi | N | 9.99999E-01 | Null |  | Null |  | Null |  | 9.99999E-01 | 4 |

Note: Event tree path ii is considered “not credible” based on likelihood < = 10-11

Table C5-3:  Event Tree Paths for Hazard H2

| Event Tree Path | On collision course? | Likelihood | ATC detects & corrects? | Likelihood | TCAS equipped? | Likelihood | TCAS successful? | Likelihood | See & avoid successful? | Likelihood | Event Tree Calc. Likelihood | Severity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i | Y | 1.00000E-06 | Y | 0.9 | Null | N/A | Null | N/A | Null | N/A | 9.00000E-07 | 4 |
| ii | Y | 1.00000E-06 | N | 0.1 | Y | 0.6 | Y | 0.9 | Null | N/A | 5.40000E-08 | 3 |
| iii | Y | 1.00000E-06 | N | 0.1 | Y | 0.6 | N | 0.1 | Y | 0.001 | 6.00000E-12 | 2 |
| iv | Y | 1.00000E-06 | N | 0.1 | Y | 0.6 | N | 0.1 | N | 0.999 | 5.99400E-09 | 1 |
| v | Y | 1.00000E-06 | N | 0.1 | N | 0.4 | Null | N/A | Y | 0.001 | 4.00000E-11 | 3 |
| vi | Y | 1.00000E-06 | N | 0.1 | N | 0.4 | Null | N/A | N | 0.999 | 3.99600E-08 | 1 |
| vii | N | 9.99999E-01 | Null |  | Null |  | Null |  | Null |  | 9.99999E-01 | 4 |

Note: Event tree paths iii and v are considered “not credible” based on likelihood < = 10-11

Table C5-4:  Event Tree Paths for Hazard H17

| Event Tree Path | On collision course? | Likelihood | ATC detects & corrects? | Likelihood | TCAS equipped? | Likelihood | TCAS successful? | Likelihood | See & avoid successful? | Likelihood | Event Tree Calc. Likelihood | Severity |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i | Y | 1.00000E-06 | Y | 0.999 | Null | N/A | Null | N/A | Null | N/A | 9.99000E-07 | 4 |
| ii | Y | 1.00000E-06 | N | 0.001 | Y | 0.6 | Y | 0.9 | Null | N/A | 5.40000E-10 | 3 |
| iii | Y | 1.00000E-06 | N | 0.001 | Y | 0.6 | N | 0.1 | Y | 0.001 | 6.00000E-14 | 2 |
| iv | Y | 1.00000E-06 | N | 0.001 | Y | 0.6 | N | 0.1 | N | 0.999 | 5.99400E-11 | 1 |
| v | Y | 1.00000E-06 | N | 0.001 | N | 0.4 | Null | N/A | Y | 0.001 | 4.00000E-13 | 3 |
| vi | Y | 1.00000E-06 | N | 0.001 | N | 0.4 | Null | N/A | N | 0.999 | 3.99600E-10 | 1 |
| vii | N | 9.99999E-01 | Y | 0.999 | Null | N/A | Null | N/A | Null | N/A | 9.99999E-01 | 4 |
| viii | N | 9.99999E-01 | N | 0.001 | Null | N/A | Null | N/A | Null | N/A | 9.99999E-04 | 4 |

Note: Event tree paths iii, iv, and v are considered “not credible” based on likelihood < = 10-11

This page intentionally blank

# Text boxes

Path i

*

Path i