16 May 2002

U.S. NATIONAL IMPLEMENTATION TASK FORCE GMDSS INFORMATION BULLETIN

USE OF GMDSS EQUIPMENT FOR NON-SAFETY COMMUNICATIONS

The Problem

It has come to the attention of the Task Force that the Masters of some ships equipped for the Global Maritime Distress and Safety System (GMDSS) have instructed watchstanders not to use GMDSS radio transmitting equipment except for Distress and Safety communications. This is contrary to the philosophy adopted by the International Maritime Organization (IMO) while formulating GMDSS principles. The purpose of this Information Bulletin is to remind masters and others that GMDSS operators can and should use the GMDSS equipment suite for routine, non-safety ship's communications.

GMDSS Functional Requirements

GMDSS was designed to carry out nine separate functional requirements identified by the IMO as listed below. A properly chosen suite of GMDSS equipment can comply with all safety and distress requirements and also meet the ship's needs for routine operational  and business communications. The GMDSS functional requirements dictate that ships at sea be capable of:

1. Transmitting ship-to-shore distress alerts by at least two separate and independent

means, each using a different radiocommunication service;

2. Receiving shore-to-ship distress alerts;

3. Transmitting and receiving ship-to-ship distress alerts;

4. Transmitting and receiving search and rescue coordinating instructions;

5. Transmitting and receiving on-scene communications;

6. Transmitting and receiving signals for locating;

7. Transmitting and receiving marine safety information;

8. Transmitting and receiving general radiocommunications to and from shore-based

radio systems or networks; and

9. Transmitting and receiving bridge-to-bridge communications.

Regular Use of GMDSS Equipment Assures Operator Competence

When operators use the GMDSS equipment on a regular basis, they develop familiarity with its operation in order to become competent operators. Competency becomes especially important when distress and safety communications are required. Increased operator competency through regular use of GMDSS equipment will also help to reduce false alerts, which have often been transmitted inadvertently by inexperienced operators.

Regular Use of GMDSS Equipment Assures Availability

One of the principal reasons for making GMDSS equipment available for routine ship's business communications is to assure that the equipment is maintained in proper working order. There are relatively few occasions for a ship to utilize GMDSS transmitting equipment for safety and distress purposes and regular use for routine communications helps to ensure that it will be in proper working order when needed. This applies to Digital Selective Calling (DSC) on VHF, MF, and HF systems and to the Inmarsat A, B, C, Mini-C, and the new Fleet 77 systems. Participation in the NOAA/Coast Guard free reporting services for weather observations and Amver reports via Inmarsat-C is an excellent way to ensure proper operation of that system.

Duplicated Equipment Provided as a Maintenance Option

A ship operating on the high seas may elect "duplicated" equipment as one of the two required

means of maintaining GMDSS equipment (the others being shore based maintenance and use of an

on-board maintainer). The "duplicated" equipment concept requires an additional VHF-DSC

transceiver and an additional long-range system such as HF-DSC or one of the Inmarsat systems.

This duplicated equipment must be installed with it's own antennas and ready for use. This

duplicated equipment should also be exercised routinely for ship's normal communications or test

calls to assure that it is in proper working order.

Testing of GMDSS Equipment on Ships Having Other Systems

Many ships with a high volume of business communications carry alternative voluntary systems in

order to meet these specialized needs in the most efficient and cost effective manner. While these

special systems effectively meet business needs and in some cases can even be used to transmit

distress alerts, use of the GMDSS systems is the preferred method for reliable and timely alerting of

the rescue network and is essential for interaction with other GMDSS ships. It is therefore

recommended that these ships arrange to transmit selected regular messages or test messages via the

GMDSS systems for operator training and to assure equipment availability.

The GMDSS Task Force

This Information Bulletin was approved on 14 October 1997 and updated on 16 May 2002 by the National GMDSS Implementation Task Force, a U.S. Coast Guard sponsored group established to coordinate implementation problems, recommend their resolution, and disseminate GMDSS information. The Task Force is soliciting feedback on problems encountered and invites responses from all concerned. Address responses to Captain Jack Fuechsel, Task Force Executive Director, 1600 North Oak Street, #427, Arlington, VA 22209; phone 703-5270484; or email: gmdss@comcast.net. See also the GMDSS section of the Coast Guard website at www.navcen.uscg.gov/marcomms (click on GMDSS, then on GMDSS Task Force). Note that this information Bulletin prompted issuance by the IMO of COMSAR/Circ.17 of 9 May 1998. Reproduction and wide dissemination of this document is encouraged.

File: gmdssib-2.doc