# Bench Tests of shaped ABT clock pulse

## N. Stanton    7/22/99

What circuit does:

Applies adjustable  DC level shift (SVX guide says “0” should be ~ 2.2 V)

Passive shaping of  ABT pulse to compensate cable response and HDI reflection effects

Test setup:

Pulser-driven shaped ABT logic (min pulser period 24 ns)

Cable = 21’ NEEW twin coax + 8’ submini coax + empty HDI with optional cap. load

### Signal injected into TEMP, GND lines of HDI, probe at TEMP pad

Adjustment of shaping time constants could probably improve response for larger capacitive loads.

# Text boxes

ABT pulses (10, 25 ns)

with level shift

but no shaping.

Probe at cable input

Unshaped ABT pulses at open cable end (left) and at open HDI end (right).

Trailing edge is distorted by cable response and HDI reflection effects.

### Shaped ABT pulses

(10, 25 ns)

### at cable input

Shaped ABT pulses

(10, 25 ns)

at open HDI end

Trailing edge now

clean and sharp!

Shaped ABT pulses at open HDI end showing small reflections from source

### Shaped 10 ns  ABT pulses

### at open HDI end

### 24 ns period (pulser max)

Same, showing shaped

clock and clockbar

together

### Shaped 25 ns pulses

### at open HDI end

50% duty cycle

Effect of capacitive load  at HDI end

(simulates SVX load??)

37 pF   (top)

27 pF

10 pF

0 pF    (bottom)