| Company Name: | Equipment/Job Identification: Hydrate Helper Type of Equipment: Make: Model: Year: Use: |
| --- | --- |
| Mine Name: |  |
| Date of Analysis: 01/31/06 through 02/02/06 |  |

# Prerequisites

All MSHA Part 46 requirements must be met including Task Training

Company policy requirements and SOPs

Task training records must be on file prior to performing any job duty

# Duty 1: Beginning-of-Shift

Learner will explain the importance of the beginning-of-shift activities.  The learner will explain each job step, why it is conducted, any associated risk, and how to implement appropriate controls.  Beginning-of-shift activities include the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Conduct a Self Assessment |  | 1 |  |  |
| Clock In |  | 1 |  |  |
| Drive to the change/lunch room |  | 1 |  |  |
| Park car |  | 1 |  |  |
| Proceed to change room |  | 1 |  |  |
| Change clothes (if needed) |  |  |  |  |
| Collect and put on PPE | Failure to put on PPE may cause serious injury; company policy | 2 |  |  |
| Collect Hard Hat |  |  |  |  |
| Collect Safety Glasses |  |  |  |  |
| Collect Safety shoes |  |  |  |  |
| Collect Ear plugs |  |  |  |  |
| Collect Gloves |  |  |  |  |
| Proceed to the pump floor |  | 1 |  |  |
| Start visual inspection of the plant | Failure to catching a machinery defect or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  |  |
| Look at housekeeping |  |  |  | Accumulation of lime |
| Look for slip and trip hazards |  |  |  |  |
| Listen for unusual noises |  |  |  |  |
| Check for guards that are not in place |  |  |  |  |
| Ensure that machinery is properly operating |  |  |  |  |
| Check for unusual smells |  |  |  |  |
| Check trip hazards |  |  |  |  |
| Check hand rails |  |  |  |  |
| Check stairs |  |  |  |  |
| Check Walkways |  |  |  |  |
| Notify the maintenance supervisor immediately if any defective conditions are found. |  |  |  |  |
| Write up a work order on any other defective conditions that are found |  |  |  |  |
| Attend briefing with the hydrate helper leaving | Failure to may cause a loss of production because the oncoming helper would not know what is going on with the plant | 2 |  |  |
| Receive status of the trucks and railcars loaded |  |  |  |  |
| Discuss the ongoing maintenance |  |  |  |  |
| Talk to the operator | May reduce the quality control of the product shipment, and reduce efficiency | 2 |  |  |
| Discuss silo levels |  |  |  |  |
| Discuss moisture levels |  |  |  | <.7% moisture loads in trucks. >.7% moisture bagged |
| Ensure that he don’t need anything |  |  |  |  |

# Duty 2:  Load Bulk Trucks

Learner will demonstrate how to safely and efficiently load bulk trucks. Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of loading bulk trucks includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catching a machinery defect or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Coordinate the loading of the trucks with the bagging operation | If there is no coordination it may reduce production because the baggers need to be shut down to spot the truck | 2 |  |  |
| Assist the baggers with the crossover belt if needed |  |  |  |  |
| Communicate with truck driver to ensure that they know that you will be on the truck | Failure to do this may cause the helper to fall from the truck causing a disabling injury or death | 3 |  |  |
| Ensure that the truck driver has his brakes set and the pressure is released from inside trailer | Could cause burns from steam; the tank pressure could knock the helper off the truck; the truck could move causing injury or death | 3 |  |  |
| Obtain and put on PPE | Failure to wear the proper PPE could cause serious injury or death | 3 |  |  |
| Body harness |  |  |  |  |
| Dust Mask |  |  |  |  |
| Goggles |  |  |  |  |
| Inspect the ladder for slip, trip and fall hazards and/or broken rungs | Failure may cause a disabling injury or death because of falling from the ladder because of slipping from muddy or broken rung | 3 |  |  |
| Climb ladder to load out shack | Failure to climb the ladder would result in the truck not being loaded; loss of production; may cause the operator to shut down the pump because the silos are full | 3 |  |  |
| Attach the retractable lanyard to the harness | Failure could cause injury in case of a fall because truck movement; slips because of wet conditions | 3 |  |  |
| Position the truck where the spout is between the center loading holes |  | 1 |  | To ensure that all lids can be accessed without adjusting truck position |
| Lower the ramp | Failure to lower ramp would prevent the helper from accessing the truck for loading causing a loss of production | 3 |  |  |
| Walk out onto the truck | Failure prevents the helper from accessing the truck for loading causing a loss of production | 3 |  |  |
| Open the lids | Failure to open the lids would prevent the helper from loading the truck causing a loss of production; not opening the lids correctly may cause a disabling injury because the lids will fly up very quickly | 3 |  |  |
| Open latches starting near the hinge |  |  |  |  |
| Release the latch with the safety catch last |  |  |  | In case there is pressure inside the tank which may cause the lid to “fly up” |
| Return to the ramp | Failure to do this step would halt production because the loading process can’t begin | 3 |  |  |
| Proceed to load out shack | Failure to do this step would halt production because the loading process can’t begin | 3 |  |  |
| Reposition the truck | Failure to do this step would halt production because the loading process can’t begin | 3 |  | Use directional lights; if lights are not working use hand signals. |
| Lower the spout into the first loading hole | Failure would cause loss of production or cause severe clean up problems because of dumping lime on the ground | 3 |  | May have to return to the ramp to ensure that the spout goes in the loading hole |
| Remove the retractable lanyard from the harness |  | 1 |  |  |
| Turn on the vibrator on loading spout | Failure may cause the spout to plug causing loss of production and material | 3 |  |  |
| Turn on the load out screw | Failure would prevent the loading process | 3 |  |  |
| Turn on the load out elevator | Failure would prevent the loading process | 3 |  |  |
| Ensure that the elevator is operating | Failure may delay loading time, cause more cleanup, cause the system to plug and backup reducing production | 2 |  |  |
| Look for the turning shaft at the bottom of the elevator |  |  |  |  |
| Turn on the #2 silo discharge screw | Failure would prevent the loading process | 3 |  |  |
| Ensure that the screw is running | Failure may delay loading time, cause more cleanup reducing production | 2 |  |  |
| Look for the turning shaft at the end of the screw |  |  |  |  |
| Notify the operator if the screw is not turning |  |  |  |  |
| Fill hole to the proper level | Failure to properly load the truck may result in bring the truck back to add more material causing a reduction in production | 2 |  | Hole is full when a steady stream of dust is coming from the spout and the hole |
| Turn off the #2 silo discharge screw | Failure would cause the truck to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the elevator | Failure would cause the truck to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the load out screw | Failure would cause the truck to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the vibrator |  | 1 |  |  |
| Raise the load out spout | Failure would cause equipment damage to the spout and/or the truck | 3 |  |  |
| Reposition the truck | Failure to do this step would halt production because the loading process can’t continue | 3 |  | Use directional lights; if lights are not working use hand signals. |
| Listen for the air brakes on the truck to ensure that the brakes are set | Failure to ensure that the brakes are set may cause the helper to fall from the truck causing a disabling injury or death | 3 |  |  |
| Obtain the sample can |  | 1 |  | In load out shack |
| Re-attach the retractable lanyard to the harness | Failure may result in a fall causing a disabling injury or death | 3 |  |  |
| Return to the top of truck | Failure to do this step would halt production because the loading process can’t continue | 3 |  |  |
| Fill the sample can from the first load out hole | Failure to do this step would halt production because the samples would not be taken | 3 |  | Run the sample if needed for that truck Only run one sample from each truck |
| Close the first truck lid |  | 1 |  | Ensure that all the latches are properly secured |
| Follow the same loading process for the remaining holes | Failure to do this step would halt production because the loading process can’t be completed | 3 |  |  |
| Shut down loading operation after last hole | Failure would cause the truck to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Shut down the silo discharge screw |  |  |  |  |
| Allow system to run until cleared |  |  |  |  |
| Shut down elevator |  |  |  |  |
| Shut down the load-out screw |  |  |  |  |
| Turn off the vibrator |  |  |  |  |
| Raise the load out spout all the way up |  |  |  |  |
| Position the truck with the spout between the two center holes |  | 1 |  |  |
| Ensure all lids and latches are closed | Failure to do this step wouldn’t allow the truck to pressurize, could let moisture in contaminating the product | 3 |  |  |
| Blow off the top of the truck using air lance | Failure may cause the product to blow off during transport causing visibility issues to the public highways | 3 |  | Company policy, it’s required that the trucks are blown off after loading |
| Return to the load out shack | Failure to get off truck would cause the truck not be able to move severely reducing production | 3 |  |  |
| Remove the retractable lanyard | Failure would prevent continuing the process | 3 |  |  |
| Ensure that the ramp is raised up | Failure would cause equipment damage to the ramp and/or the truck | 3 |  |  |
| Climb down the ladder to the ground | Failure would prevent continuing the process | 3 |  |  |
| Remove the body harness and store in proper place |  | 1 |  |  |
| Notify the truck driver that the loading process is over | Failure would prevent continuing the process | 3 |  |  |
| Proceed to the rail scale check out shack | Failure would prevent continuing the process | 3 |  |  |
| Fill out bill of lading | Failure would prevent continuing the process | 3 |  |  |
| Give bill of lading to the truck driver | Failure would prevent continuing the process | 3 |  |  |

# Duty 3:  Load Train Cars

Learner will demonstrate how to safely and efficiently load train cars.  The learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of loading train cars includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catching a machinery defect or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Coordinate the loading of the rail cars with the bagging operation | If there is no coordination it may reduce production because the baggers need to be shut down to spot the truck | 2 |  |  |
| Assist the baggers with the crossover belt if needed |  |  |  |  |
| Check to ensure that the load out ramp and spout are in the fully raised position | Failure to do this step would cause damage to the ramp, spout, and rail car causing a halt in production | 3 |  |  |
| Obtain the loader | Must be done to start the loading process | 3 |  | CAT 966 |
| Conduct a pre-shift inspection of the loader | Failure to do this step may result in equipment damage and disciplinary action | 3 |  | Use the Pre-Op check sheet inside the loader. Company Policy |
| Climb inside loader | Must be done to start the loading process | 3 |  |  |
| Put on seat belt | Failure to use seat belt may result in a disabling injury or death in case of accidents | 3 |  | Company Policy |
| Start up loader | Must be done to start the loading process | 3 |  |  |
| Fill out the Pre-Op inspection check sheet | May result in disciplinary action if not done | 3 |  | Company Policy |
| Proceed to the rail cars | Must be done to start the loading process | 3 |  |  |
| Drop bucket to the ground | Will help prevent the loader from moving | 3 |  | Company Policy |
| Set the brakes on the loader | To prevent unexpected movement of the loader which may cause sever injury or death | 3 |  | Company Policy |
| Ensure that the loader is in neutral | In case the brakes fail it would help prevent unexpected movement of the loader | 3 |  | Company Policy |
| Dismount the loader | Must be done to start the loading process | 3 |  |  |
| Check for proper brake tension on the rail cars | Could cause rail car damage if the brakes are locked or cause the car to move unexpectedly causing injury or death | 3 |  | If more than one car, check the brake systems on all cars |
| Pull on brake chain system to ensure tightness |  |  |  |  |
| Check the knuckle of the car that you are going to hook to ensuring that it is open |  | 1 |  |  |
| Check the knuckle on the loader to ensure that it is open |  | 1 |  |  |
| Mount the loader | Must be done to start the loading process | 3 |  |  |
| Put on seat belt | Failure to use seat belt may result in a disabling injury or death in case of accidents | 3 |  | Company Policy |
| Raise the bucket | Failure to raise the bucket may cause turning problems reducing equipment efficiency or may cause an injury | 2 |  |  |
| Release park brake on the loader | May cause equipment damage | 3 |  |  |
| Set the lock on the knuckle in the loader | Must be done to start the loading process, can’t move the car unless the lock is engaged | 3 |  |  |
| Push the switch next to the seat forward |  |  |  |  |
| Back up to the train car until the knuckle is engaged | Must be done to start the loading process | 3 |  |  |
| Proceed to the load out station | Must be done to start the loading process | 3 |  |  |
| Spot the car on the center hole using the alignment marks on the wall | Must be done to start the loading process | 3 |  | Gray for seven hole cars Orange for six hole cars |
| Align your right shoulder with the painted marks on the wall |  |  |  |  |
| Unhook the rail car from the loader |  | 1 |  |  |
| Push switch next to seat to the rear of the loader |  |  |  |  |
| Park the loader in a safe location away from the dust |  | 1 |  | Use parking procedure |
| Obtain paperwork and seals | Necessary to accomplish the job, the paperwork needs to be obtained and filled out | 3 |  | Paperwork located in lock up |
| Start train car profile paperwork | Necessary to accomplish the job, the paperwork needs to be obtained and filled out | 3 |  |  |
| Record car number, seal numbers, and empty car weight on the profile |  |  |  | Car weight an number located on the car |
| Obtain and put on PPE | Failure may cause injury or death airborne dust or falling from rail car causing a disabling injury or death | 3 |  | Body harness, Dust Mask, Goggles |
| Inspect the ladder for slip, trip and fall hazards and/or broken rungs | Failure may cause a disabling injury or death because of falling from the ladder because of slipping from muddy or broken rung | 3 |  |  |
| Climb ladder to load out shack | Failure to climb the ladder would result in the rail car not being loaded; loss of production; may cause the operator to shut down the pump because the silos are full | 3 |  |  |
| Attach retractable lanyard to the harness | Failure could cause injury in case of a fall because rail car movement; slips because of wet conditions | 3 |  |  |
| Lower the ramp | Failure to lower ramp would prevent the helper from accessing the rail car for loading causing a loss of production | 3 |  |  |
| Walk out onto the rail car | Failure prevents the helper from accessing the rail car for loading causing a loss of production | 3 |  |  |
| Open lids 1-4 | Failure to open the lids would prevent the helper from loading the rail car causing a loss of production; not opening the lids correctly may cause a disabling injury because the lids will fly up very quickly | 3 |  |  |
| Open latches starting near the hinge |  |  |  |  |
| Release the latch with the safety catch last |  |  |  | In case there is pressure inside the tank which may cause the lid to “fly up” |
| Return to the ramp | Must be done to continue the loading process | 3 |  |  |
| Proceed to load out shack | Must be done to continue the loading process | 3 |  |  |
| Lower the spout into the first loading hole | Failure would cause loss of production or cause severe clean up problems because of dumping lime on the ground | 3 |  | May have to return to the ramp to ensure that the spout goes in the loading hole |
| Remove the lanyard from the harness |  | 1 |  |  |
| Turn on the vibrator on loading spout | Failure may cause the spout to plug causing loss of production and material | 3 |  | To ensure that the spout don’t plug |
| Turn on the load out screw | Failure would prevent the loading process | 3 |  |  |
| Turn on the load out elevator | Failure would prevent the loading process | 3 |  |  |
| Ensure that the elevator is operating | Failure may delay loading time, cause more cleanup, cause the system to plug and backup reducing production | 2 |  |  |
| Look for the turning shaft at the bottom of the elevator |  |  |  |  |
| Turn on the #2 silo discharge screw | Failure would prevent the loading process | 3 |  |  |
| Ensure that the screw is running | Failure may delay loading time, cause more cleanup reducing production | 2 |  |  |
| Look for the turning shaft at the end of the screw |  |  |  |  |
| Notify the operator if the screw is not turning |  |  |  |  |
| Fill hole to the proper level | Failure to properly load the rail car may result in bringing the rail car back to add more material causing a reduction in production | 2 |  | Hole is full when a steady stream of dust is coming from the spout and the hole |
| Turn off the #2 silo discharge screw | Failure would cause the rail car to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the elevator | Failure would cause the rail car to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the load out screw | Failure would cause the rail car to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Turn off the vibrator |  | 1 |  |  |
| Raise the load out spout | Failure would cause equipment damage to the spout and/or the rail car | 3 |  |  |
| Raise the ramp in the fully raised position | Failure would cause equipment damage to the ramp and/or the rail car | 3 |  |  |
| Climb down ladder to the ground | Failure would prevent continuing the process | 3 |  |  |
| Obtain the loader | Must be done to continue the loading process | 3 |  |  |
| Connect the loader to the rail cars using the connection procedures | Must be done to continue the loading process | 3 |  |  |
| Reposition rail cars to the next paint marks | Must be done to continue the loading process | 3 |  |  |
| Leave the loader attached to the rail cars and repeat loading process for holes 2-4 | Failure may reduce production spending time hooking and unhooking the loader from the rail cars | 2 |  | Leaving the loader attached speeds up the loading process |
| Obtain three sample cans | Must be done to continue the loading process | 3 |  | In load out shack |
| Re-attach the retractable lanyard to the harness | Failure could cause injury in case of a fall because rail car movement; slips because of wet conditions | 3 |  |  |
| Return to the top of the rail car | Must be done to continue the loading process | 3 |  |  |
| Fill the sample can from the first and fourth holes | This step must be done to complete the loading process | 3 |  | Use one can for each hole |
| Close lids and attach seals on holes 1-4 after hole #4 is filled | Failure to do this step wouldn’t allow the rail car to pressurize, could let moisture in contaminating the product; rail cars can’t be transported without the seals | 3 |  | Attaching seals are Company Policy |
| Clean off the top of the rail car using compressed air and air lance | Failure to do this step causes a loss of production because the car would have to be repositioned | 3 |  | Only clean the area around the loaded holes 1-4 |
| Follow the same loading process for the remaining holes | Must be done to continue the loading process | 3 |  |  |
| Shut down loading operation after last hole | Failure would cause the rail car to overload causing cleanup problems, loss of product severely reducing production | 3 |  |  |
| Shut down the silo discharge screw |  |  |  |  |
| Allow system to run until cleared |  |  |  |  |
| Shut down elevator |  |  |  |  |
| Shut down the load-out screw |  |  |  |  |
| Turn off the vibrator |  |  |  |  |
| Raise the load out spout up |  |  |  |  |
| Take a sample from the last load out hole | Must be done to complete the loading process | 3 |  | A total of three sample per car |
| Close and attach seals to the remaining lids | Must be done to complete the loading process | 3 |  |  |
| Ensure that all latches are secured | Failure to do this step wouldn’t allow the rail car to pressurize, could let moisture in contaminating the product; rail cars can’t be transported without the seals | 3 |  | Company Policy |
| Clean off the top of the car using air lance | Failure may cause the product to blow off during transport | 3 |  | Company Policy; failure may cause disciplinary action; railroad policy |
| Return to load out shack | Must be done to complete the loading process | 3 |  |  |
| Remove the retractable lanyard | Must be done to complete the loading process | 3 |  |  |
| Raise ramp all the way up | Failure to do this step would cause damage to the ramp and rail car causing a halt in production | 3 |  |  |
| Climb down the ladder to the ground | Must be done to complete the loading process | 3 |  |  |
| Remove the body harness and store in proper place |  | 1 |  |  |
| Check the position of the track switch | Failure may result in equipment damage and loss of production | 3 |  |  |
| Ensure that the rail switch flag is cross ways with the track |  |  |  |  |
| Return to the loader | Must be done to complete the loading process | 3 |  |  |
| Move the rail car through the switch | Must be done to complete the loading process | 3 |  | Use first gear |
| Stop and exit the loader | Must be done to complete the loading process | 3 |  | Ensure that proper parking procedures are followed |
| Turn the rail switch back to where the flag is parallel to the rails | Must be done to complete the loading process; loss of production | 3 |  |  |
| Return to loader | Must be done to complete the loading process | 3 |  |  |
| Unhook the loader from the rail car using switch inside loader | Must be done to complete the loading process | 3 |  |  |
| Move the loader to the other end of the car | Must be done to complete the loading process | 3 |  |  |
| Couple the loader to the car | Must be done to complete the loading process | 3 |  |  |
| Pull through the switch and onto the scale | Must be done to complete the loading process | 3 |  |  |
| Record the gross weight of the rail car on the profile report | Must be done to complete the loading process | 3 |  | Note the weight on the digital scale read out monitor |
| Exit the loader | Must be done to complete the loading process | 3 |  |  |
| Inspect the area around the rail cars and loader to ensure all persons are clear | Failure to inspect the area may cause severe injury or death to persons or property damage | 3 |  |  |
| Open any closed couplers on loaded train cars that may be present on the track | Failure could result in property damage | 3 |  | Couplers are opened by lifting the bar on the end of the rail car |
| Return to the loader | Must be done to complete the loading process | 3 |  |  |
| Sound the loader horn before moving | Failure could result in property damage or death due to collision | 3 |  |  |
| Back the car in the reverse direction off of the scale | Must be done to complete the loading process | 3 |  |  |
| Couple the car to any additional cars and move past the switch at least 2 car lengths to allow the next car to clear | Must be done to complete the loading process | 3 |  | If there is more than on car the brakes may have to be released enough to move the loaded cars forward |
| Stop and park the loader using the proper procedures | Failure to use proper procedures may cause serious injury, death and/or property damage | 3 |  |  |
| Exit the loader | Must be done to complete the loading process | 3 |  |  |
| Ensure that the brake is fully set on at least one rail car | Failure to use proper procedures may cause serious injury, death and/or property damage | 3 |  |  |
| Get in the loader | Must be done to complete the loading process | 3 |  |  |
| Unhook the car from the loader using the proper procedure | Must be done to complete the loading process | 3 |  |  |
| Park loader in designated area | Failure to park in a safe designated area may cause the train to hit loader causing equipment damage | 3 |  | Company Policy |
| Obtain the three full sample cans and proceed to the lab | Must be done to complete the loading process | 3 |  |  |
| Run all required tests | Failure could result in disciplinary action because the train car can’t be released until the samples are completed | 3 |  | Moisture %, Viscosity, Pack set. Company Policy |
| Record all results on the profile report and lab log | Failure could result in disciplinary action because the train car can’t be released until the samples are completed | 3 |  | Company Policy |
| Ensure that the profile is complete |  | 1 |  |  |
| Take profile report to the pump control room |  | 1 |  |  |

# Duty 4:  Fill Tanner Gas

Learner will demonstrate how to safely and efficiently perform the procedures to fill tanner gas. The learner will also explain each job step, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of the fill tanner gas activities includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catch machinery defects or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Obtain and put on PPE | Failure to wear face shield or goggles could allow the gas to splash up causing personal serious injury | 3 |  | Face shield or goggles Rubber Gloves |
| Ensure that the correct container is used | May cause damage to equipment or personal injury because of contamination | 2 |  | Blue 5 gallon bucket stored beneath the tank |
| Proceed to the oil house (if needed) | Failure to do this step could result in an air loss to the plant which would cause production to stop | 3 |  |  |
| Locate the 55 gallon drum of methanol | Failure to do this step could result in an air loss to the plant which would cause production to stop | 3 |  |  |
| Ensure that all caps are closed and tight | Failure may cause a loss of product, serious personal injury due to splashing of methanol | 3 |  |  |
| Place drum on the dolly | Failure to use dolly can result in serious personal injury due to strain | 3 |  |  |
| Lay drum on its side with the pour spout down | Failure to do this step would result in the loss of production because the methanol would not come out properly | 3 |  |  |
| Place the 5 gallon bucket under the spout | May cause the methanol to pour out on the ground | 3 |  |  |
| Open the small cap on the top of the drum | Failure would cause insufficient air inside the drum causing the methanol to burp which may splashing on persons causing serious personal injury; loss of product | 3 |  |  |
| Remove the lid from the 5 gallon bucket | Failure would cause loss of production, can’t fill bucket properly; loss of product | 3 |  |  |
| Open the spout on the drum slowly | Failure may cause the product to come out to fast causing splashing and loss of product; serious personal injury due to chemical exposure | 3 |  | Open to the correct flow rate to eliminate splashing |
| Close spout when the bucket is full | Failure may cause the product to continue to come out causing splashing and loss of product; serious personal injury due to chemical exposure | 3 |  |  |
| Put lid back on 5 gallon bucket | May splash when carrying the bucket causing serious personal injury due to chemical exposure | 3 |  |  |
| Put small lid back on air flow hole and hand tighten | Failure may cause the methanol to splash causing chemical exposure and serious personal injury | 3 |  |  |
| Stand the drum back to the vertical position | Failure may allow the methanol to leak out of the cap causing environmental problems; may cause chemical exposure | 3 |  |  |
| Proceed back to the tanner gas tank with the bucket | Failure would reduce production; needs to be done to complete the job | 3 |  |  |
| Open air lines to the main pipe | Failure wouldn’t allow the air to flow to the rest plant causing loss of production | 3 |  |  |
| Close both valves to the tanner gas tank | Failure to close valves would leave air in the tank which could be released under pressure causing personal injury | 3 |  | Up to 120 lbs. air pressure |
| Remove the plug on the fill pipe | Failure would not allow the product to be poured into the tank; loss of production | 3 |  |  |
| Open the valve on the fill pipe (slowly) | Failure could release to much air containing methanol to blow out in your face causing personal injury; chemical exposure | 3 |  |  |
| Dump the methanol into the fill pipe until full | Failure would reduce production; needs to be done to complete the job | 3 |  |  |
| Close valve on the fill pipe | Failure could release to much air containing methanol to blow out in your face causing personal injury; chemical exposure | 3 |  |  |
| Replace the plug in the end of the fill pipe | Failure may cause chemical exposure if fill pipe valve becomes defective | 3 |  |  |
| Open both valves on the bypass pipe | Failure to open both valves would prevent air from passing through the tank causing loss of production | 3 |  |  |
| Close the valve to the main line | Failure to open the valve would prevent air from passing through the tank causing loss of production | 3 |  |  |
| Repeat steps to refill 5 gallon bucket if needed |  | 1 |  | 5 gallon bucket should remain full to be used if needed |
| Replace 5 gallon bucket under tanner tank | Failure to leave bucket under the tank would cause loss of time which would affect production | 2 |  |  |

# Duty 5:  Run Samples

Learner will demonstrate how to safely and efficiently run samples.  The learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of running samples includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catch machinery defects or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Follow the written procedure for determining the moisture (%) content | Failure to follow the procedure may alter the sample results causing poor quality control | 3 |  | The written procedure is in the lab There will be one sample per truck and three samples per rail car |
| Follow the written procedure for determining the viscosity of the sample | Failure to follow the procedure may alter the sample results causing poor quality control | 3 |  | The written procedure is in the lab There will be one sample per truck and three samples per rail car |
| Notify operator if viscosity is less than 110,000 | Failure could result in a poor quality of the product; could be loss of production; impact on the plant | 3 |  |  |
| Communicate with operator on additive feed dial settings to be used | Failure could result in a poor quality of the product; could be loss of production; impact on the plant | 3 |  |  |
| Begin application of additive when notified by operator | Failure could result in a poor quality of the product; could be loss of production | 3 |  |  |
| Proceed to Devils Hole |  |  |  |  |
| Check feed pipe and clear if necessary |  |  |  |  |
| Set dial to appropriate settings |  |  |  |  |
| Turn toggle switch to on position |  |  |  |  |
| Proceed to additive hopper |  |  |  |  |
| Place a bag of additive on the grate above the hopper |  |  |  |  |
| Break the bag open and dump into hopper |  |  |  |  |
| Repeat adding additive as needed |  |  |  | Additional additive is in the warehouse |
| Place empty bags into the dumpster next to the bagger shack |  |  |  |  |
| Follow the written procedure for the Pack Set test | Failure to follow the procedure may alter the sample results causing poor quality control | 3 |  | The written procedure is on the bottom and back of the train car profile sheet There will be one sample per truck and three samples per rail car |
| Record all test results on the lab sheet report | Failure could result in poor quality control resulting in loss of production | 3 |  | Company Policy; May cause disciplinary action if not done |
| Combine all remaining samples from each rail car into one bucket and leave in the lab | Failure could result in further tests not being able to be completed which could cause a loss of production | 3 |  | Company Policy; May cause disciplinary action if not done |
| Tag samples with car number, date and initial |  |  |  |  |

# Duty 6: Dump the Reject Hopper

Learner will demonstrate how to safely and efficiently dump the reject hopper.  The learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance dumping the reject hopper includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catch machinery defects or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Close the air gate above the hopper | Failure would allow the product to dump on the ground causing severe cleanup issue; equipment damage; loss of production | 3 |  |  |
| Obtain the Forklift | Failure could cause a loss of production; forklift is used to complete the job; | 3 |  |  |
| Conduct a pre-operational inspection on the forklift | Failure could cause equipment damage or a safety hazard could go un-noticed causing serious personal injury | 3 |  | Company Policy; possible disciplinary action |
| Fill out the pre-op form | Failure could result in the mechanics not receiving the reports on a possible defect | 3 |  | Company Policy; possible disciplinary action |
| Get on the forklift | Failure would prevent the job from being completed | 3 |  |  |
| Put on seat belt | Failure may result in a disabling injury or death in case of an accident | 3 |  | Company Policy; possible disciplinary action |
| Start forklift | Failure would prevent the job from being completed | 3 |  |  |
| Raise forks | Failure would prevent the job from being completed | 3 |  | 4 to 6 inches |
| Release parking brake | Failure may cause equipment damage; loss of production | 3 |  |  |
| Proceed to hopper | Failure would prevent the job from being completed | 3 |  |  |
| Lift hopper onto forks | Failure would prevent the job from being completed | 3 |  |  |
| Carry hopper to dump site | Failure would prevent the job from being completed | 3 |  | Watch for screws, elevators, persons, beams, pipes, etc. |
| Stop forklift and set park brake at dump site | Failure may result in serious personal injury due to the unexpected movement of the forklift | 3 |  |  |
| Raise hopper about three feet from the ground | Failure could result in the hopper not properly dumping and/or cause serious personal injury if the hopper is raised too high | 3 |  |  |
| Tilt the mast forward | Failure could result in the hopper not dumping properly or cause serious personal injury because of trying to push hopper to dump | 3 |  |  |
| Dismount forklift | Failure would prevent the job from being completed | 3 |  |  |
| Raise the dump latch on the hopper | Failure could result in the hopper not dumping properly | 3 |  |  |
| Get back on the forklift | Failure would prevent the job from being completed | 3 |  |  |
| Raise the load to dump the hopper | Failure would prevent the job from being completed | 3 |  |  |
| Tilt the mast back to vertical | Failure would result in the hopper not returning to the closed position | 3 |  |  |
| Lower the hopper to the ground | Failure would prevent the job from being completed | 3 |  |  |
| Dismount forklift | Failure would prevent the job from being completed | 3 |  |  |
| Check latch to ensure hopper properly secured | Failure could result in property damage because the hopper might roll into the dump position unexpectedly | 3 |  |  |
| Remount the forklift | Failure would prevent the job from being completed | 3 |  |  |
| Raise load four to six inches off the ground | Failure could result in property damage during transport; if raised too high it would cause a reduction in visibility; serious personal injury to persons | 3 |  |  |
| Release the park brake | Failure would cause equipment damage | 3 |  |  |
| Drive hopper back to dirt devil | Failure would prevent the job from being completed | 3 |  |  |
| Set hopper in place | Failure would prevent the job from being completed | 3 |  |  |
| Return forklift to designated area | Failure could result in property damage because the forklift may be covered with lime | 3 |  | Company Policy |
| Set park brake and lower forks | Failure could result in unexpected movement causing serious personal injury or death; forks could cause a tripping hazard | 3 |  | Company Policy |
| Shut off forklift | Failure could cause the forklift to run out of fuel causing a loss of production because it would have to be refueled | 2 |  |  |
| Proceed to and open air gate | Failure could cause equipment damage and loss of production because it would cause the system to back up | 3 |  | Only open gate half way |

# Duty 7: General clean up

Learner will demonstrate how to safely and efficiently perform general clean up activities.  The learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of general clean up activities includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catch machinery defects or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Obtain and put on PPE | Failure to put on PPE may cause serious injury; company policy | 3 |  | Gloves, Glasses, Dust Mask |
| Inspect the condition of hand tools | Failure may cause personal injury because of a defective tool | 2 |  | Wheelbarrow, Shovel, Brooms. If defects are found turn them into a Supervisor for replacement |
| Obtain Bobcat if needed |  | 1 |  |  |
| Inspect before use |  |  |  |  |
| Fill out pre-operational check sheet |  |  |  |  |
| Tape off lower level before sweeping or blowing off upper level | Failure may cause personal injury to persons in or around the plant because of flying/falling debris | 3 |  |  |
| Clean up the Hydrate area | Failure could result in personal injury because of slip, trip and fall hazards | 2 |  | Part of the job description |
| Clean up main floor |  |  |  |  |
| Clean up Pump floor |  |  |  |  |
| Clean off Top of Silos |  |  |  |  |
| Clean off Top of Separators |  |  |  |  |
| Clean up Devils Hole |  |  |  | The pump must be shut off before cleanup is done in the Devils hole (Clean up with two persons) |
| Clean up Below the Hydrator |  |  |  |  |
| Clean up around the load out |  |  |  |  |
| Clean up around train tracks |  |  |  |  |
| Put away all tools in designated areas when finished | Failure could result in personal injury because of slip, trip and fall hazards; loss of production if the tools can’t be found | 2 |  |  |

# Duty 8: General Maintenance

Learner will demonstrate how to safely and efficiently perform general maintenance activities.  The learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of the general maintenance activities includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Continue Visual Inspection | Failure to catch machinery defects or a problem may reduce equipment efficiency; may not find slip and trip and other hazards which may cause injuries | 2 |  | This inspection is a continuation of the items listed in the “Beginning of Shift” duty |
| Obtain tools | Can’t complete the job without the proper tools | 3 |  |  |
| Get grease gun |  |  |  |  |
| Get rags |  |  |  |  |
| Get screw driver |  |  |  |  |
| Get extra tube of grease |  |  |  |  |
| Greasing | Failure could result in the equipment efficiency or operational life because of bearing failure | 3 |  |  |
| Follow lubrication schedule as posted in the control room |  |  |  |  |
| Check condition of the V-belts | Failure to detect worn or defective belts may result in additional equipment down time | 2 |  | If worn or in poor condition, write a work order |
| Replace broken or missing V-belts | Failure to replace the V-Belts could cause a loss of production. Failure to follow the proper procedure could cause serious personal injury or death | 3 |  |  |
| Notify the operator |  |  |  |  |
| Lock and tag out motor after the operator has shut down motor circuit | All persons working on equipment must lock and tag out |  |  | Follow company lock and tag out policy |
| Obtain tools |  |  |  | Crescent wrench, 9/16” wrench, screw driver, and hammer |
| Remove the guard |  |  |  |  |
| Check the V-belt for the size |  |  |  |  |
| Obtain the replacement V-belt |  |  |  | Belt room |
| Fill out inventory sheet in belt room (quantity, size, and what you put it on) |  |  |  |  |
| Install the new V-belt |  |  |  |  |
| Loosen the torque arm or adjust motor to shorten belt span |  |  |  |  |
| Remove any existing belts that may be on pulley |  |  |  |  |
| Install the new belts over the pulley |  |  |  |  |
| Adjust the torque arm or motor to the proper tension |  |  |  |  |
| Tighten the torque and /or motor locking nuts |  |  |  |  |
| Install guard |  |  |  | Company policy states that nothing is started without the guard properly in place |
| Remove lock an tag |  |  |  |  |
| Put tools away |  |  |  |  |
| Energize motor |  |  |  |  |
| Check top and bottom elevator bearings | Failure to detect defective bearing could result in extra down time and/or equipment damage | 2 |  | Ensure that the balls are in the bearing, shaft is centered within the two bearings, seals are in place, shaft is not spinning inside the bearing, and ensure that the bearing is getting grease (check on a daily basis) |
| Check Load out elevator |  |  |  |  |
| Check Silo feed elevator |  |  |  |  |
| Check reject elevator |  |  |  |  |
| Check collector elevator |  |  |  |  |
| Check Surge bin elevator |  |  |  |  |
| Check to ensure the operation of the screw conveyors (Tail Bearings) | Failure to detect defective bearing could result in extra down time and/or equipment damage | 2 |  | Ensure that the balls are in the bearing, seals are in place, ensure that the shaft is not spinning inside the bearing, ensure that the bearing is getting grease (should be check on a daily basis) |
| Check the surge bin feed screw |  |  |  |  |
| Check the surge bin discharge screw |  |  |  |  |
| Check the #1 and #2 clean out screws |  |  |  |  |
| Check the collector discharge screw |  |  |  |  |
| Check the #1 separator feed screw |  |  |  |  |
| Check the #1 separator product screw |  |  |  |  |
| Check the #1 separator reject screw |  |  |  |  |
| Check the #2 separator feed screw |  |  |  |  |
| Check the #2 separator product screw |  |  |  |  |
| Check the #2 separator reject screw |  |  |  |  |
| Check the micro pulverizing screw (dirt devil) |  |  |  |  |
| Check the silo feed screw |  |  |  |  |
| Check top separator Bearings | Failure to detect defective bearing could result in extra down time and/or equipment damage | 2 |  | Ensure that the balls are in the bearing, seals are in place, ensure that the shaft is not spinning inside the bearing, ensure that the bearing is getting grease, remove lime build-up if necessary (check on a daily basis) |
| Check #1 separator bearing |  |  |  |  |
| Check #2 separator bearing |  |  |  |  |

# Duty 9: End-0f-Shift

Learner will demonstrate how to safely and efficiently perform end-of shift activities.  The learner will also explain the job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient performance of the end-of-activities includes the following steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Ensure that the reject hopper is empty | Failure would result in down time because the system will plug up | 2 |  | Follow the dumping of reject hopper job steps. To be done within ½ hour of the end of the shift |
| Ensure that samples have been run | Failure would cause a problem with quality control, extra down time, loss of production. | 3 |  | If samples have not been run advise incoming hydrate helper. If not done it may be grounds for disciplinary action |
| Ensure that all reports and paperwork have been completed | Failure would cause a problem with quality control, extra down time, loss of production. | 3 |  |  |
| Railcar profile report |  |  |  |  |
| Pre-Op inspection report |  |  |  |  |
| Any work orders |  |  |  |  |
| Tool orders list |  |  |  |  |
| Parts orders |  |  |  |  |
| Wait for proper relief | Failure to wait for relief may cause a loss of production because your not allowed to work alone | 3 |  |  |
| Brief incoming hydrate helper | Failure may result in confusion in what needs to be or has been accomplished; loss of production | 2 |  |  |
| Discuss what train cars are done or half done |  |  |  |  |
| Advise of trucks loaded |  |  |  |  |
| Advise of any break downs or maintenance issues |  |  |  |  |
| Advise of the condition of the lime |  |  |  |  |
| Discuss any other potential problems |  |  |  |  |
| Return to lunchroom |  | 1 |  |  |
| Change clothes |  | 1 |  |  |
| Clock out |  | 1 |  |  |