Quality and Accuracy Report

for

National Park Service Alaska Support Office

##### In Partnership with

##### Earth Satellite Corporation

### Contract No.:	     1443CX991097004

Task Order No.:	 1443TO991098011

#### Title:  State Surficial Geology Map of Alaska

##### Date:  February 14, 1999

National Park Service Alaska Support Office

Quality and Accuracy Report

Data Layer Name:	Qcode

Data Layer Description:	Statewide Alaska Geology

Firm:	Greenhorne & O'Mara, Inc.

9800 4th Street, North Suite 202

St. Petersburg, FL 33702

(727)576-0402

(727)576-0305 (fax)

Project Manager:	Kathleen O'Keife

Prepared By:	Kimberly A. Ermann

Date:	January 14, 1999

A.  DATA

1.  Description of Source Material Provided by National Park Service

a.	US Geological Survey Maps

Name:	Miscellaneous Geologic Investigations (West)  I-357

Scale (ratio):	1:1,584,000

Datum:	Mean Sea Level

Map Projection:	Unknown

Condition of Media:	Good

Creator Organization:	USGS

Date of Source Material:	1955

Name:	Miscellaneous Geological Investigations (East) I-357

Scale (ratio):	1:1,584,000

Datum:	Mean Sea Level

Map Projection:	Unknown

Condition of Media:	Good

Creator Organization:	USGS

Date of Source Material:	1960

- Coverages:

- Alaska_c

- Alaska_cl

- Alaska_cb

- Glaciers

- Lakes

- Majriv

2.  Deliverable Format

Map Projection:	Albers

Zunits:	No

Units:	Meters

Spheroid:	Clarke 1866

Xshift:	0.000

Yshift:	0.000

Parameters:	55 0 0.000/* 1st standard parallel

65 0 0.000/* 2nd standard parallel

-154 0 0.000/* central  meridian

50 0 0.000/*latitude of projection’s origin

0.00000/* false easting (meters)

3.  Derivation of Data / Method of Derivation

The Geologic map  extents were collected through a series of procedures.

- Mylar sheets were overlain on the hard-copy geologic survey maps.

- Corner tics were etched on the mylar overlays with a rapidiograph pen.

- Utilizing a light table, the Qcode extents, indicated by the colored polygons on the hard-copy maps, were traced onto the mylar overlays with rapidiograph pens.

- Intersecting latitude/longitude tics were indicated and labeled for reference.

- The resultant inked mylar overlays were scanned and output into TIF format

- Utilizing the SRV software package, the linework was autovectorized.

- After vectorization, the linework was imported and the file was attributed.

- The coverages provided by NPS contained tics that represented real world coordinate values.  The new coverages were transformed into the provided coverages.

- The project specification dictated that the NPS provided coverages supercede the older data set in cases of conflict (e.g., differing coastline features.)

- "Qcode" attributes were assigned; utilizing the ARC/INFO software package

- QC Plots were created for each individual map.

- Visual quality assurance was conducted by overlaying each plot on the corresponding geologic maps.

- The separate coverages were edgematched and dissolved into one coverage.

- NPS received interim checkplots and digital data for internal QC.

- Final edit were performed at contractor facility.

- Final digital quality assurance was conducted., Report was finalized and product was produced on CDRom for final delivery to NPS.

4.  Equipment

- Sun Ultra 170 Workstations

- GTCO Digitizing Tablets

- HP750c Plotter

5.  Data Automation

- Data was compiled from October 8, 1998 to January 14, 1999.

6.  Software System and Version Used

- ESRI's ARC/INFO version 7.04 and 7.1.2

| Q code | Deposit Type | Deposit Name |
| --- | --- | --- |
| Qi | Glacier | Ice |
| Qm4 | Current moraine | Glacial moraines & drift |
| Qm3 | Lightly modified moraine | Glacial moraines & drift |
| Qm2 | Moderately modified moraine | Glacial moraines & drift |
| Qm1 | Highly modified moraine | Glacial moraines & drift |
| Qg | Proglacial lake | Glacio-lacustrine |
| Qgm/Qm3 Note: call all these Qgm. Disregard date denominator. | Proglacial lake over moraine | Glacio-lacustrine |
| Qw2 | Current glacial outwash | Glacio-fluvial |
| Qw1 | Old glacial outwash | Glacio-fluvial |
| Qfp | Floodplain | Fluvial |
| Qat | Alluvial Terrace | Fluvial |
| Qaf | Alluvial Fan | Fluvial |
| Qed | Sand Dune | Eolian |
| Qed | Upland Loess | Eolian |
| Qes | Valley Loess & alluvium | Eolian |
| Qcb | Beach | Coastal |
| Qcd | Coastal Delta | Coastal |
| Qcc | Old marine 7 alluvium | Coastal |
| Qu | Undifferentiated mosaic | Undifferentiated alluvium & colluvium |
| Qra | Bedrock & coarse rubble | Mountain alluvium & colluvium |
| Qrb | Coarse & fine rubble | Mountain alluvium & colluvium |
| Qrc | Fine rubble | Mountain alluvium & colluvium |
| Qrd | Volcanic | Mountain alluvium & colluvium |
| Qre | Alluvium over old alluvium | Mountain alluvium & colluvium |
| Ql | Lake | Water |

- EXPLANATION

Glacial Moraines and Associated Drift

- Qi – Existing glaciers

- Qm4 – Moraines and associated drift near existing glacier fronts

- Qm3- Prominent little modified moraines and associated drift lying

above or beyond boundaries of Qm4

- Qm2 – Modified moraines and associated drift lying above of beyond boundaries of Qm3.

- Qm1 – Remnants of highly modified moraines and associated drift lying above or

beyond boundaries of Qm2

Glacio-lacustrine Deposits

- Qg – Proglacial lake deposits

- Qgm – Proglacial lake deposits, discontinuously mantling glacial and

glacio-fluvial deposits but not completely obscuring glacial topography: age indicated by symbols

# Glacio-fluvial Deposits

- Qw2 – Outwash and valley train deposits graded to glacier fronts and recent moraines

- Qw1 – Outwash deposits bordering older moraines: fluvial deposits further downvalley

may be dissected distal parts of outwash aprons or valley trains and are included in Qat and Qaf

# Fluvial Deposits

- Qfp – Modern flood-plain and associated low-terrace and alluvial fan deposits

- Qat – Higher terrace deposits on valley margins and discontinuous terrace deposits in

valleys where flood plains are too small to map

- Qaf – Alluvial-fan deposits

## Eolian Deposits

- Qed – Sand dunes: dotted pattern indicates areas of active dunes

- Qe – Silt more than 5 feet thick, covering upland interfluve areas, predominantly eolian

- Qes – Thick valley bottom silt and sand, predominantly eolian but including much colluvium

and stratified water-laid deposits

## Coastal Deposits

- Qcb – Modern coastal beaches, spits, and bars

- Qcd – Coastal delta deposits

- Qcc-  Older coastal deposits of inter-stratified alluvial and marine sediments, including,

locally, glacial drift

Undifferentiated Upland Valley and Lowland Alluvium

- Qu - Alluvium in larger upland valleys and in lowlands of central Alaska including

undifferentiated eolian, colluvial, fluvial, marine, and glacial deposits

## Undifferentiated Alluvium and Slope Deposits in Mountainous and Hilly Regions

- Qra – dominantly coarse rubbly deposits associated with steep-sloped mountains

with high percentage of bedrock exposures

- Qrb- Course- and fine-grained deposits associated with moderate to sleep-sloped

mountains and hills with bedrock exposures largely restricted to upper slopes and crestlines

- Qrc -  Dominantly fine-grained deposits associated with gently sloping hills with rare bedrock

exposures

- Qrd – deposits with high percentages of volcanic rock particles, ash, and pumice flanking volcanic cones and peaks of Quarternary and Tertiary age

- Qre – Discontinuous alluvial deposits overlying dissected unconsolidated, semi-consolidated,

and locally consolidated silt, sand, and gravel of Tertiary and younger age

C.  LINEWORK ACCURACY

1.  Linework Completeness and Positional Accuracy

a.  Value

100% of all linework was captured.

b.  Date

Final Quality Control checks were made in February 1999.

c.  Methods Used to Derived Value

Overlay of Quality Control Plots with Geologic maps.

D.  ATTRIBUTE ACCURACY

1.  Attribute Completeness Check

a.  Value

100% of all attributes on the source material were captured.

b.  Data

Final Quality Control Checks were made in February 1999.

c.  Method Used to Derive Value

Visual comparisons occurred between the geologic maps.

and the Attributed Quality Control Plots.

E.  LOGICAL CONSISTENCY

1.  Topologic Tests

a.  Tests Performed

Cartographic Tests included the following ARC/INFO commands:

BUILD, CLEAN, DESCRIBE, LABEL ERRORS, NODE ERRORS.

b.  Date

Tests were performed in December 1998 and on final product in February 1999.

c.  Are all polygons closed?

Yes.

d.  Have dangles been eliminated?

Yes

e.  Have slivers been eliminated?

Yes.

f.  Do features (lines, polygons) have unique identifiers?

Yes.