About the THOR System Flight Patch and Logo

The THOR System flight patch conceptually illustrates key elements of the NASA/GSFC Earth Sciences cloud measurement instrument.  The acronym THOR stands for (Cloud) THickness from Offbeam Returns.  The Principle Investigator is Bob Cahalan, Code 913.

Inspiration for the THOR project name came from Norse mythology.  THOR was the powerful god of thunder who wielded a mighty hammer called Mjollnir.  Legends depict THOR as a powerful entity often surrounded by large storm clouds, so it was fitting to choose THOR and his hammer to symbolize the new cloud-measuring device.

The THOR instrument is symbolically depicted in the flight patch as a stylized version of THOR’s hammer (see below). Hammer design was based on photos of ancient Norse amulets.  In mythology, THOR’s hammer, Mjollnir, was often believed to be a source of lightning.  More on the relevance of that symbology follows later.

The THOR System uses a powerful, green laser to generate a cloud-measuring signal.  The system laser is depicted in the flight patch by the prominent end of the hammer; a green laser beam is shown emanating from it.

When a laser beam strikes cloud, a halo is created as depicted in the flight patch.

Scattered and reflected light rays (returns) from the halo are collected by the system’s telescope.  The telescope is represented symbolically in the flight patch by the head of the hammer; reflected light is shown being collected by it.

Cloud thickness can be determined from the halo diameter and timing information as the halo forms.  It is interesting to note that when lightning strikes a cloud, a halo of light is created in the cloud, similar to the halo created by a laser.  That fact ties together the mythology of THOR’s hammer as a source of lightning, instrument operation, and flight patch symbology.

The top of the flight patch is a banner that states the purpose of the instrument and defines the THOR acronym.

The bottom of the flight patch repeats the symbolic representation of the hammer head and encloses the organizations involved in the instrument development

The Flight Patch was designed by John Kolasinski, THOR Instrument Chief Engineer, Code 565, with direction from Bob Cahalan.  Special thanks go to Diwan Bhathal, Code 565, and Debbi McLean of GSFC Graphics Arts for design assistance and artistic guidance.

The THOR System Flight Patch may be produced in an embroidered cloth version or decal as opportunities present themselves.

The THOR Logo is a simple, stylized icon for the project.  The Logo was designed to have recognizable details when printed in very small sizes (~ 0.5 inches).  The THOR Logo may be used as a project icon for documentation, since flight patch details and lettering are lost when printed in small form (compare previous page small patch graphic to the small Logo below).

The THOR Logo uses symbols that are similar to those contained in the flight patch:  hammer, clouds, and project acronym (see below).

The Logo was designed by John Kolasinski with direction from Bob Cahalan.  Special thanks go to Diwan Bhathal, Code 565 and Debbi McLean of GSFC Graphics Arts for design assistance and artistic guidance.

The THOR Logo may be produced in an embroidered cloth version or decal as opportunities present themselves.