THOR

Weather Scenario Server

Interface Design Document and

Message Catalog

Version 1.3

May, 2003

Prepared by

Raytheon Technical Services Company

For

Human Information Processing Research Branch

NASA Ames Research Center

Moffet Field, CA

Table of Contents

Introduction	3

Start Up Configuration File	3

Message Catalog	4

Incoming Messages	4

Start Scenario Message	4

Stop Scenario Message	5

Subscribe Message	5

Unsubscribe Message	6

Data Request Message	7

System Time Request Message	8

Load Scenario Message	8

Outgoing Messages	9

System Time Response Message	9

Update Notice Message	10

Data Reply Message	10

Region Product Data Format	11

Grid Data Format	12

Gridded Product Data Format	12

Appendix A – Summary of Operational Concept	13

# Introduction

The Thor Weather Scenario Server is a server designed to provide weather data to cockpit and out-the-window display simulations. It is named Thor after the Norse god of thunder. The server runs as a Win32 application and takes its start up parameters from an XML configuration file. It receives its run-time controls and serves data through socket connections, using the message formats described in this document. For the operational concept description of this interface, see the Weather Models and Architecture Power Point briefing, 17-May-2002.

The Thor server reads the weather scenario from a set of scenario files in a defined directory hierarchy. The scenario is described in a top-level XML scenario description file. Weather data can be obtained from the Thor server by using the Data Request message described later, or by directly reading the scenario files. The format of the scenario files is described in a separate document.

# Start Up Configuration File

When the Thor server starts up, it reads start-up parameters from a file named thorConfig.xml that must reside in the directory from which the Thor executable is started. The fields includes in the file are listed in Table 1.0. An example configuration file is shown in Figure 1. The only tag for which there can be multiple entries is SCENARIO_FILE. Other duplicate entries will overwrite the previous entry. When the server first starts, it will load the scenario file in the first entry.

Table 1.0 – Thor Configuration File Parameters

| Field Name | XML Tag | Required | Field Description |
| --- | --- | --- | --- |
| Root | THOR_CONFIG | Y | The XML root for the configuration data. All other tags must be enclosed within this root tag. |
| Scenario File | SCENARIO_FILE | Y | The full path to a scenario descriptor file. |
| Start Time Step | START_TIMESTEP | N | The time-step within the scenario file at which the Thor server will start serving weather data. Default is time zero. |
| Log File | LOG_FILE | N | The full path name to a file to be written as the server log. Default: “Thor.log”. |
| Use Log Server | USE_LOG_SERVER | N | A TRUE/FALSE flag that indicates whether to write to a local log file or to send the log data to a remote server. The implementation of this feature is TBD. Default is False. |
| Log Server IP | LOG_SERVER_IP | N | Not used. |
| Log Server Port | LOG_SERVER_PORT | N | Not used. |
| Listen Port | LISTEN_PORT | Y | The server port at which the Thor server listens for connections. |

<?xml version="1.0"?>

<THOR_CONFIG>

<SCENARIO_FILE>c:\dev\wxserver\Scenario.xml</SCENARIO_FILE>

<START_TIMESTEP>10</START_TIMESTEP>

<LOG_FILE>c:\dev\wxserver\ScenarioServer.log</LOG_FILE>

<USE_LOG_SERVER>FALSE</USE_LOG_SERVER>

<LISTEN_PORT>4444</LISTEN_PORT>

</THOR_CONFIG>

Figure 1 – Example ThorConfig.xml File.

# Message Catalog

The Thor server complies with the HI Laboratory-standard CCI messaging format. While the server itself is written in C++, the message format is described in a language-neutral form, recognizing that some clients may be written in other languages.

## Incoming Messages

### Start Scenario Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | long | Total size in bytes of the message |
| 8-11 |  | Msg Type | long | Message type code: 17310 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |

### Stop Scenario Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | long | Total size in bytes of the message |
| 8-11 |  | Msg Type | long | Message type code: 17320 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |

### Subscribe Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | long | Total size in bytes of the message |
| 8-11 |  | Msg Type | long | Message type code: 19500 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Port Number | Unsigned long | Subscribers Port to receive notifications |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |
| 56-59 | Payload | Text Product bit map | Unsigned long | Bitmap identifying text products to include |
| 60-63 |  | Radar Prod. bit map | Unsigned long | Bitmap identifying Radar products to include |
| 64-67 |  | Current Wx Product bit map | Unsigned long | Bitmap identifying current weather products to include |
| 68-71 |  | Forecast Wx Product bit map | Unsigned long | Bitmap identifying forecast weather products to include |
| 72-75 |  | Actual Wx Product bit map | Unsigned long | Bitmap identifying actual weather products to include |
| 76-79 |  | Aux.Wx Product bit map | Unsigned long | Bitmap identifying auxiliary weather products to include |

For the Weather product bit maps, Table 2.0 lists the codes have been defined as of this draft of this document. The bit patterns can be logically Or-ed together to include multiple products.

Table 2.0 – Product Bit Settings

| Bit Map | Wx Product to Include | Bit Pattern |
| --- | --- | --- |
| Text Products | AIRMET | 0x00000001 |
|  | SIGMET | 0x00000004 |
|  | METAR | 0x00000010 |
| Radar Products | NEXRAD | 0x00000001 |
|  | RCM | 0x00000002 |
|  | NEXRADLOW | 0x00000004 |
|  | ECHOTOPS | 0x00000008 |
|  | STORMMODEL | 0x00000020 |
| Current, Forecast and Actual Products | CEILING | 0x00000001 |
|  | ICING | 0x00000004 |
|  | LIGHTNING | 0x00000008 |
|  | PRECIPITATION | 0x00000010 |
|  | TEMPERATURE | 0x00000040 |
|  | TURBULANCE | 0x00000080 |
|  | VISIBILITY | 0x00000100 |
|  | WIND | 0x00000400 |
| Auxiliary Products | WIND_GRID | 0x00000001 |
|  | OUT_THE_WINDOW | 0x00000004 |

### Unsubscribe Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 19510 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Port Number | Unsigned long | Subscribers Port – needed for identification |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |

### Data Request Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 19530 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |
| 56-59 | Payload | Text Product bit map | Unsigned long | Bitmap identifying text products requested |
| 60-63 |  | Radar Prod. bit map | Unsigned long | Bitmap identifying Radar products requested |
| 64-67 |  | Current Wx Product bit map | Unsigned long | Bitmap identifying current weather requested |
| 68-71 |  | Forecast Wx Product bit map | Unsigned long | Bitmap identifying forecast weather products requested |
| 72-75 |  | Actual Wx Product bit map | Unsigned long | Bitmap identifying actual weather products requested |
| 76-79 |  | Aux.Wx Product bit map | Unsigned long | Bitmap identifying auxiliary weather products (see Table 2.0 for bit map codes) |
| 80-87 |  | Latitude | Double float | Latitude of center of region of interest in degrees (-90.0 to 90.0N). |
| 88-95 |  | Longitude | Double float | Longitude of center of region of interest in degrees (-180 to 180E). |
| 96-103 |  | Altitude | Double float | Altitude of center of region of interest |
| 104-111 |  | Radius | Double float | Radius of region of interest in nautical miles. Data will be clipped to approximately this radius. |

### System Time Request Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 504 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |

The Load Scenario message requests that the Thor server load a new scenario file. The file name (including full path on the system hosting Thor) is specified in an ASCII string as the payload of the message. Upon receipt of the message, Thor will stop processing any existing scenario, load the new file and go into the idle state. Any current subscribers or connections will be maintained.

### Load Scenario Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 19515 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time – Not Used |
| 36-39 |  | Month | Long | Part of Date/Time – Not Used |
| 40-43 |  | Day | Long | Part of Date/Time – Not Used |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – not used |
| 48-55 |  | Time | Double Float | System Time – not used |
| 56-59 |  | String length | integer | Length in bytes of next field. |
| 60-(60 + Str. Len.) |  | Scenario File Path | Character | The full path to the scenario file, on the system hosting Thor. |

Outgoing Messages

The system Time Response message is sent in reply to a System Time Request message. As a payload, it provides the current system time of the system on which the Thor server is running.

### System Time Response Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 505 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Part of Date/Time |
| 36-39 |  | Month | Long | Part of Date/Time |
| 40-43 |  | Day | Long | Part of Date/Time |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field |
| 48-55 |  | Time | Double Float | System Time |
| 56-59 |  | Year | Long | Part of Date/Time |
| 60-63 |  | Month | Long | Part of Date/Time |
| 64-67 |  | Day | Long | Part of Date/Time |
| 68-71 |  | Time Type | Integer | Code for the meaning of next field |
| 72-79 |  | Time | Double Float | System Time |

The Update Notice message is sent to subscribers to indicate that the next time step for a product is available. The message includes a bit map which indicates which products are updated. If a single product is referenced in the message, then the final field contains the time-step number for that product. Otherwise, the final field is omitted. This field is intended to be used by subscribers with a local cache, who might use the time-step number as some kind of an index into the cache.

### Update Notice Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code: 19520 dec. |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Current year |
| 36-39 |  | Month | Long | Current month (1 – 12) |
| 40-43 |  | Day | Long | Current day in month ( 1 – 31) |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field – UTC |
| 48-55 |  | Time | Double Float | System Time |
| 56-59 | Payload | Text Product bit map | Unsigned long | Bitmap identifying text products updated |
| 60-63 |  | Radar Prod. bit map | Unsigned long | Bitmap identifying Radar products updated |
| 64-67 |  | Current Wx Product bit map | Unsigned long | Bitmap identifying current weather updated |
| 68-71 |  | Forecast Wx Product bit map | Unsigned long | Bitmap identifying forecast weather products updated |
| 72-75 |  | Actual Wx Product bit map | Unsigned long | Bitmap identifying actual weather products updated |
| 76-79 |  | Aux.Wx Product bit map | Unsigned long | Bitmap identifying auxiliary products updated (see Table 2.0 for bit map codes) |
| 80-83 |  | Time step number | Unsigned long | Only for notices that specify a single product, this field is the time-step counter for that product. |

The Data Reply Message can have different Message Type Codes, depending on the type of data in the reply. If more than one weather products are requested so that the reply contains multiple products, the Message Type will designate a General Reply. Otherwise, the Message Type will indicate the kind of data record for the single product in the reply: Region, Grid Map, Gridded, or Text.

### Data Reply Message

| Byte | Msg Part | Field | Data Type | Description |
| --- | --- | --- | --- | --- |
| 0-3 | Header | Marker | unsigned long | Bit pattern for start of message. Either 55a5aa5a hex for Win or 5aaaa555 hex for Unix. Helps identify whether bytes need to be swapped |
| 4-7 |  | Msg Size | Long | Total size in bytes of the message |
| 8-11 |  | Msg Type | Long | Message type code (decimal): 19540 General Reply 19550 Region Data Reply 19560 Grid Map Reply 19570 Gridded Data Reply 19580 Text Data Reply |
| 12-15 |  | Source Id | Unsigned long | Not Used |
| 16-19 |  | Destination Id | Unsigned long | Not Used |
| 20-23 |  | Transaction Id | Unsigned long | Not Used |
| 24-27 |  | Ref Id | Unsigned long | Not Used |
| 28-31 |  | Misc. one | Unsigned long | Not Used |
| 32-35 |  | Year | Long | Current year |
| 36-39 |  | Month | Long | Current month (1 – 12) |
| 40-43 |  | Day | Long | Current day in month ( 1- 31) |
| 44-47 |  | Time Type | Integer | Code for the meaning of next field |
| 48-55 |  | Time | Double Float | System Time |
| 56-59 | Payload | Text Product bit map | Unsigned long | Bitmap identifying text products included |
| 60-63 |  | Radar Prod. bit map | Unsigned long | Bitmap identifying Radar products included |
| 64-67 |  | Current Wx Product bit map | Unsigned long | Bitmap identifying current weather included |
| 68-71 |  | Forecast Wx Product bit map | Unsigned long | Bitmap identifying forecast weather products included |
| 72-75 |  | Actual Wx Product bit map | Unsigned long | Bitmap identifying actual weather products included |
| 76-79 |  | Aux.Wx Product bit map | Unsigned long | Bitmap identifying auxiliary products included (see Table 2.0 for bit map codes) |
| 80… | One or more Product Data Sets as Described in the following Tables |  |  |  |

The following tables describe the Product Data Set formats. The fields in the data set are aligned on four byte boundaries. This may require padding the character data with one or more null characters

### Region Product Data Format

| Field | Data Type | Description |
| --- | --- | --- |
| Product Type | Int | 0 = Text, 1 = Radar, 2 = Current, 3 = Forecast, 4 = Actual. |
| Product Code | unsigned long | Code for specific weather Product (see Table 2.0) |
| Count | Int | Number of regions to follow. |
| Repeats Count | Value | Int | A context–specific value associated with the region. Possibly level of intensity. |
| Times | Altitude † | Double | The altitude at which this region is defined. |
|  | Vertex Count | Int | Number of vertices (0, 1, or 3 or more) defining geo-spatial point or region affected by this product. |
|  | Latitude - 1 | Double | First vertex |
|  | Longitude - 1 | Double | First vertex |
|  | … |  |  |
|  | Latitude – N | Double | Last vertex |
|  | Longitude – N | Double | Last Vertex |
|  | Text Length | Long | Length in bytes of annotation. Zero if no text. |
|  | Text ‡ | Character | Descriptive text associated with the region. |

† For Echo Tops, the value of the region is the altitude, in kilo-feet. The Value field holds this value, and the Altitude field is always zero.

‡ For the Storm Model product only: the text region always begins with the eight character storm id of the form: AAAAXXDD where AAAA is the site Id, XX is the NEXRAD cell Id and DD is unique number for polygon (with leading zero).

The Region Product Data Format is used for the non-gridded weather products that can be represented by a region or a point: SIGMET, AIRMET, METAR, NEXRAD, NEXRAD LOW, STORM MODEL, ECHO TOPS, CEILING, LIGHTNING, ICING, TURBULENCE, PRECIPITATION and VISIBILITY.

### Grid Data Format

| Field | Data Type | Description |
| --- | --- | --- |
| Product Type | Int | 5 = Auxiliary. |
| Product Code | unsigned long | WIND_GRID (see Table 2.0) |
| Row Size | Int | Number of points in a row. |
| Row Count | Int | Number of Rows. |
| Row 1 | Latitude 1 | Double |  |
|  | Longitude 1 | Double |  |
|  | … |  |  |
|  | Latitude n | Double |  |
|  | Longitude n | Double |  |
| Row 2 | Latitude 1 | Double |  |
|  | Longitude 1 | Double |  |
|  | … |  |  |
|  | Latitude n | Double |  |
|  | Longitude n | double |  |
| … |  |  |  |
| Row n |  |  |  |

The Grid Data Format is used to send a grid that defines the Lat-Lon location of the points constituting the gridded weather products. The grid is the same for all altitude levels and is provided in row-major order.

### Gridded Product Data Format

| Field | Data Type | Description |
| --- | --- | --- |
| Product Type | Int | 2 = Current, 3 = Forecast, 4 = Actual. |
| Product Code | unsigned long | Code for specific weather Product (see Table 2.0) |
| Clipped Flag | Int | 0 = grid is not clipped, 1 = clipping info follows. |
| Optional, | NW Row | Int | Grid row number of NW corner of clipped area. |
| used if | NW Col. | Int | Grid column number NW corner of clipped area. |
| Clipped | Row Length | Long | Number of entries in each row. |
| Flag is set | Rows | Long | Number of rows in the clipped area. |
| Altitude 1 | Double | The altitude at which the points are defined. |
| Row 1 | Value 1 ‡ |  | A context–specific value associated with the point. |
|  | Value 2 |  |  |
|  | … |  |  |
|  | Value n |  |  |
| Row 2 | Value 1 |  |  |
|  | Value 2 |  |  |
|  | … |  |  |
|  | Value n |  |  |
| … |  |  |  |
| Row n | … |  |  |
| Altitude 2 | Double |  |
| … |  |  |
| Altitude n | Double |  |

‡ Value could be a single value, or a structure containing one or more items, depending on the product.

The Gridded Product Data Format is used for the gridded weather products that can be represented by a grid of points: WIND and TEMPERATURE. The points are organized into altitude levels, and by rows of points that correspond to the lat/lon positions in the matching WIND_GRID product. In practice, the WIND_GRID would be sent to all clients and those lat/lon positions would apply to all subsequent gridded products.

Table 2 – Gridded Product Value Types

| Product | Value | Description |
| --- | --- | --- |
| Temperature | float | Temperature in degrees Kelvin |
| Wind | (float, float) | UV components of wind vector |

# Appendix A – Summary of Operational Concept

When the server starts up, it is in a neutral state. It will read its configuration file and then send a message to the ADRS, asking to be notified when the scenario starts. In the neutral state, the server can accept Subscription messages from clients wishing to be notified of weather product updates.

The server will remain in a neutral state until it is transitioned to the “Started” state. This transition is affected by receipt of a “Start Scenario” message from the ADRS. For stand-alone test purposes, a pop-up menu at the server application dialog allows manual transition to the Started state.

Once in the Started state, the Thor server will use an internal timer and the update rates in weather scenario file to determine when a weather product should be updated. When a product needs to be updated, the Thor server will send a Notification message to any clients that have subscribed to update notifications for that product.

Upon receipt of an Update Notification message, a client may send the Thor server a Data Request message to obtain the updated product. The server will send the product data back over the socket connection upon which the Data Request message was received. Alternatively, the client may read the updated data directly from a local copy of the scenario file; in this case, the Thor server is used solely as a sequencer.

The Thor server will continue to operate in this manner until it receives a “Stop Scenario” message. Upon receipt of this message, the server will halt its internal timer, reset the weather scenario back to its beginning and return to a neutral state. All subscribers remain intact, and the scenario can be started again with a “Start Scenario” message. To change to a different weather scenario, the ThorConfig.xml file must be edited and the server shutdown and restarted.