Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Time Interpolation and Spatial Averaging (TISA)

(Subsystems 7.1, 8.0, & 10.0)

Test Plan

Release 4

Version 8

Primary Authors

Cathy Nguyen, Raja Raju

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  January 2008

Document Date:  January 2008

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/28/01 | R3V3 | 276 | Updated the SCCR number. Updated filenames and compilation commands. Corrected the PGE execution command and updated gif filenames. Added instructions for executing the cleanup script. Updated format to comply with standards. | 2.1 2.2 3.1.1.2 3.1.3 All |
| 04/01/02 | R3V4 | 334 | Updated the SCCR number. Added one tar file. Updated filenames and compilation commands. Added SRBAVG3 file. Took out two .gif files Changed the total run time, memory and required disk space. Updated format to comply with standards. | 2.1 2.2 3.1.1.2 3.1.1.4 All |
| 06/17/02 | R3V5 | 368 | Updated the SCCR number. Updated to mention the source environment file. Changed the total run time, memory and required disk space. Added the locations of the compared data files. Updated format to comply with standards. | 2.1 3.1.1.1 3.1.1.4 3.1.2.3 All |
| 09/03/02 | R3V6 | 386 | Updated the SCCR number. Changed the total run time, memory and required disk space. Updated format to comply with standards. | 2.1 3.1.1.4 All |
| 01/07/03 | R3V7 | 415 | Updated the SCCR number. Changed the instrument ID from 1 to 3 in the output file names since FM2 is used. Changed the total run time, memory and required disk space. Updated format to comply with standards. | 2.1 3.1.1.2 3.1.1.4 All |
| 01/22/03 | R3V8 | 418 | Updated Document Overview to add Subsystem 7.1. Updated Subsystem Overview to add Subsystem 7.1. Added Subsystem 7.1. Updated the SCCR number and added Subsystem 7.1. Added Subsystem 7.1 and updated Subsystem 10. Added Subsystem 7.1 Main Processor. Changed the instrument ID from 1 to 3 in the output file names since FM2 is used. Changed the total run time, memory and required disk space. Updated format to comply with standards. | 1.1 1.2 2.0 2.1 2.2 3.1 3.1.1.2 3.2.1.4 All |
| 04/08/03 | R3V9 | 433 | Updated to change the SCCR numbers to XXX. Updated to change the month. Changed the file range to the test case. Changed the main processor summary. Updated format to comply with standards. | 2.1 3.1.1.1 3.1.1.2 3.1.1.4 All |
| 05/29/03 | R3V10 | 440 | Updated to change the month. Changed the year and month to variables. Changed the main processor summary. Updated format to comply with standards. | 3.1.1.1 3.1.1.2 3.1.1.4 All |
| 08/25/03 | R3V11 | 462 | Updated to add subsystem overview for Subsystem 8. Added in the installation for Subsystem 8. Updated to add Subsystem 8 in the compilation. Added the main processor for Subsystem 8. Changed the compilation command for Subsystems 7.1, 8 and 10. Corrected the number of files delivered in out_exp and changed the “diff” command to “cmp” command. Updated format to comply with standards. | 1.2.2 & 1.2.3 2.1 2.2 3.2 2.2 3.1.2.3 All |
| 05/21/04 | R3V12 | 527 | Added the removal of the ancillary directory. Updated to change the month. Changed the year and month to variables. Changed the main processor summary. Updated format to comply with standards. | 2.1 3.1.1.1 3.1.1.2 3.1.1.4 All |
| 08/20/04 | R3V13 | 554 | Changed the name of the tar file. Updated to change the month and the file name. Changed run time and memory. Changed the month for Subsystem 10. Updated format to comply with standards. | 2.1 3.2.1.1 3.2.1.4 3.3.1.1 All |
| 09/15/04 | R4V1 | 516 | Added more commands to remove the old directories. Deleted one file. Changed the directory name. Updated to change the month and the file name. Changed run time and memory. Changed the script name. Added Test Procedures for Aqua. Updated format to comply with standards. | 2.1 2.2 3.3.1.1 3.3.1.4 3.3.2.3 3.3.4 All |
| 04/20/05 | R4V2 | 583 | Added phase one of SRBAVG run. Changed file name. Added to remover directories. Updated to change the file name and added one more compilation process for phase one. Changed year, month, file name, and changed the script name. Added one output file. Added one more file to compare. Changed the total run time. Added test case for Terra FM2. Added comparison for the output file for Aqua. Added test case for Aqua FM4. Added a new processor. Updated format to comply with standards. | 1.2.4 2.1 2.2 3.3.1.1 3.3.1.2 3.3.2.3 3.3.1.4 3.3.4 3.3.7.2 3.3.10 3.4 All |
| 04/24/06 | R4V3 | 624 | Updated to add descriptions of the daily means and the cloud in ISCCP format. Added more files. Added the PGE name for verification. Added the new PGE CER10.1P3. Updated format to comply with standards. | 1.2 2.1 2.2 3.5 All |
| 06/21/06 | R4V4 | 629 | Updated to delete the new installation part. Updated the clean-up scripts for Subsystem 10. Updated format to comply with standards. | 2.1 3.3, 3.4, & 3.5 All |
| 07/10/06 | R4V5 | 631 | Updated to delete the new installation part. Updated to add tests for Aqua and Terra. Updated format to comply with standards. | 2.1 3.1 All |
| 10/04/06 | R4V6 | 637 | Added more tar files. Added compilation for PGE CER10.1P4. Removed Aqua FM3 and FM4 Test Procedure for CER10.1P1. Removed Aqua FM3 and FM4 Test Procedure for CER10.1P2. Added CER10.1P4 Main Processor. Added CER10.1P5 Phase One Processor. | 2.1 2.2 3.3.7 & 3.3.8 3.4.7 & 3.4.8 3.6 3.7 |
| 11/15/06 | R4V7 | 639 | Updated to delete the new installation part. Added installation part for the new PGE. Updated stand alone test for Terra FM1 and Terra FM2. Added new PGE CER8.2P1. Deleted “SAIC” and added “SSAI” to Acronym List. | 2.1 3.2 3.3 App. A |
| 10/11/07 | R4V8 | 660 | Updated stand alone test for Terra FM2 and Aqua FM3 and FM4. Document was converted from FrameMaker to Word. | 3.1.4.1 3.1.7.1 3.1.10.1 All |

Document Revision Record	ii

1.0	Introduction	1

1.1.	Document Overview	1

1.2.	Subsystem Overview	1

1.2.1.	CERES Time Space Interpolation (TSI) Subsystem 7.1 Main Processor	1

1.2.2.	Compute Regional, Zonal, and Global Averages Subsystem 8.0
	Main Processor	2

1.2.3.	Compute Monthly and Regional TOA and SRB Averages Subsystem
	10.0 Main Processor	3

1.2.4.	Compute Monthly Hourly CERES Clear-sky Albedo, CERES Clear-sky
	map and Monthly Regional Snow/Ice Map	3

1.2.5.	Compute Daily and Regional TOA and SRB Averages and Produce
	ISCCP Format Cloud Types	4

2.0	Software and Data File Installation Procedures	5

2.1.	Installation	5

2.2.	Compilation	7

3.0	Test and Evaluation Procedures	10

3.1.	CER7.1.1P1 Main Processor for Subsystem 7.1	10

3.1.1.	Stand-alone Test Procedures for Terra FM1	10

3.1.1.1.	PCF Generator	10

3.1.1.2.	Execution	11

3.1.1.3.	Exit Codes	11

3.1.1.4.	Main Processor Test Summary	11

3.1.2.	Evaluation Procedures	12

3.1.2.1.	Log and Status File Results	12

3.1.2.2.	Metadata	12

3.1.2.3.	Execution of Comparison Software	12

3.1.3.	Solutions to Possible Problems	12

3.1.4.	Stand-alone Test Procedures for Terra FM2	13

3.1.4.1.	PCF Generator	13

3.1.4.2.	Execution	14

3.1.4.3.	Exit Codes	14

3.1.4.4.	Main Processor Test Summary	14

3.1.5.	Evaluation Procedures	14

3.1.5.1.	Log and Status File Results	14

3.1.5.2.	Metadata	15

3.1.5.3.	Execution of Comparison Software	15

3.1.6.	Solutions to Possible Problems	15

3.1.7.	Stand-alone Test Procedures for Aqua FM3	16

3.1.7.1.	PCF Generator	16

3.1.7.2.	Execution	16

3.1.7.3.	Exit Codes	17

3.1.7.4.	Main Processor Test Summary	17

3.1.8.	Evaluation Procedures	17

3.1.8.1.	Log and Status File Results	17

3.1.8.2.	Metadata	17

3.1.8.3.	Execution of Comparison Software	18

3.1.9.	Solutions to Possible Problems	18

3.1.10.	Stand-alone Test Procedures for Aqua FM4	19

3.1.10.1.	PCF Generator	19

3.1.10.2.	Execution	19

3.1.10.3.	Exit Codes	20

3.1.10.4.	Main Processor Test Summary	20

3.1.11.	Evaluation Procedures	20

3.1.11.1.	Log and Status File Results	20

3.1.11.2.	Metadata	20

3.1.11.3.	Execution of Comparison Software	21

3.1.12.	Solutions to Possible Problems	21

3.2.	CER8.1P1 Main Processor	22

3.2.1.	Stand Alone Test Procedures for Terra FM1	22

3.2.1.1.	PCF Generator	22

3.2.1.2.	Execution	22

3.2.1.3.	Exit Codes	23

3.2.1.4.	Main Processor Test Summary	23

3.2.2.	Evaluation Procedures	23

3.2.2.1.	Log and Status File Results	23

3.2.2.2.	Metadata	23

3.2.2.3.	Execution of Comparison Software	23

3.2.3.	Solutions to Possible Problems	24

3.2.4.	Stand Alone Test Procedures for Terra FM2	24

3.2.4.1.	PCF Generator	24

3.2.4.2.	Execution	25

3.2.4.3.	Exit Codes	25

3.2.4.4.	Main Processor Test Summary	25

3.2.5.	Evaluation Procedures	25

3.2.5.1.	Log and Status File Results	25

3.2.5.2.	Metadata	25

3.2.5.3.	Execution of Comparison Software	26

3.2.6.	Solutions to Possible Problems	26

3.3.	CER8.2P1 Post Processor	27

3.3.1.	Stand Alone Test Procedures for Terra FM1	27

3.3.1.1.	PCF Generator	27

3.3.1.2.	Execution	28

3.3.1.3.	Exit Codes	28

3.3.1.4.	Main Processor Test Summary	29

3.3.2.	Evaluation Procedures	29

3.3.2.1.	Log and Status File Results	29

3.3.2.2.	Execution of Comparison Software	29

3.3.3.	Solutions to Possible Problems	29

3.3.4.	Stand Alone Test Procedures for Terra FM2	29

3.3.4.1.	PCF Generator	29

3.3.4.2.	Execution	30

3.3.4.3.	Exit Codes	31

3.3.4.4.	Main Processor Test Summary	31

3.3.5.	Evaluation Procedures	31

3.3.5.1.	Log and Status File Results	32

3.3.5.2.	Execution of Comparison Software	32

3.3.6.	Solutions to Possible Problems	32

3.4.	CER10.1P1 Main Processor	33

3.4.1.	Stand-alone Test Procedures for Terra FM1	33

3.4.1.1.	PCF Generator	33

3.4.1.2.	Execution	34

3.4.1.3.	Exit Codes	36

3.4.1.4.	Main Processor Test Summary	36

3.4.2.	Evaluation Procedures	36

3.4.2.1.	Log and Status File Results	36

3.4.2.2.	Metadata	36

3.4.2.3.	Execution of Comparison Software	36

3.4.3.	Solutions to Possible Problems	37

3.4.4.	Stand-alone Test Procedures for Terra FM2	38

3.4.4.1.	PCF Generator	38

3.4.4.2.	Execution	39

3.4.4.3.	Exit Codes	41

3.4.4.4.	Main Processor Test Summary	41

3.4.5.	Evaluation Procedures	41

3.4.5.1.	Log and Status File Results	41

3.4.5.2.	Metadata	41

3.4.5.3.	Execution of Comparison Software	41

3.4.6.	Solutions to Possible Problems	42

3.5.	CER10.1P2 Main Processor	43

3.5.1.	Stand Alone Test Procedures for Terra FM1	43

3.5.1.1.	PCF Generator	43

3.5.1.2.	Execution	44

3.5.1.3.	Exit Codes	44

3.5.1.4.	Main Processor Test Summary	44

3.5.2.	Evaluation Procedures	44

3.5.2.1.	Log and Status File Results	44

3.5.2.2.	Metadata	44

3.5.2.3.	Execution of Comparison Software	44

3.5.3.	Solutions to Possible Problems	45

3.5.4.	Stand Alone Test Procedures for Terra FM2	46

3.5.4.1.	PCF Generator	46

3.5.4.2.	Execution	46

3.5.4.3.	Exit Codes	47

3.5.4.4.	Main Processor Test Summary	47

3.5.5.	Evaluation Procedures	47

3.5.5.1.	Log and Status File Results	47

3.5.5.2.	Metadata	47

3.5.5.3.	Execution of Comparison Software	47

3.5.6.	Solutions to Possible Problems	48

3.6.	CER10.1P3 Main Processor	49

3.6.1.	Stand-alone Test Procedures for Terra FM1	49

3.6.1.1.	PCF Generator and Execution	49

3.6.1.2.	Execution	50

3.6.1.3.	Exit Codes	50

3.6.1.4.	Main Processor Test Summary	50

3.6.2.	Evaluation Procedures	50

3.6.2.1.	Log and Status File Results	50

3.6.2.2.	Metadata	50

3.6.2.3.	Execution of Comparison Software	51

3.6.3.	Solutions to Possible Problems	51

3.6.4.	Stand-alone Test Procedures for Terra FM2	52

3.6.4.1.	PCF Generator and Execution	52

3.6.4.2.	Execution	52

3.6.4.3.	Exit Codes	53

3.6.4.4.	Main Processor Test Summary	53

3.6.5.	Evaluation Procedures	53

3.6.5.1.	Log and Status File Results	53

3.6.5.2.	Metadata	53

3.6.5.3.	Execution of Comparison Software	53

3.6.6.	Solutions to Possible Problems	54

3.6.7.	Stand-alone Test Procedures for Aqua FM3	55

3.6.7.1.	PCF Generator and Execution	55

3.6.7.2.	Execution	55

3.6.7.3.	Exit Codes	56

3.6.7.4.	Main Processor Test Summary	56

3.6.8.	Evaluation Procedures	56

3.6.8.1.	Log and Status File Results	56

3.6.8.2.	Metadata	56

3.6.8.3.	Execution of Comparison Software	56

3.6.9.	Solutions to Possible Problems	57

3.6.10.	Stand-alone Test Procedures for Aqua FM4	58

3.6.10.1.	PCF Generator	58

3.6.10.2.	Execution	58

3.6.10.3.	Exit Codes	59

3.6.10.4.	Main Processor Test Summary	59

3.6.11.	Evaluation Procedures	59

3.6.11.1.	Log and Status File Results	59

3.6.11.2.	Metadata	59

3.6.11.3.	Execution of Comparison Software	59

3.6.12.	Solutions to Possible Problems	60

3.7.	CER10.1P4 Main Processor	61

3.7.1.	Stand-alone Test Procedures for Aqua FM3	61

3.7.1.1.	PCF Generator	61

3.7.1.2.	Execution	62

3.7.1.3.	Exit Codes	64

3.7.1.4.	Main Processor Test Summary	64

3.7.2.	Evaluation Procedures	64

3.7.2.1.	Log and Status File Results	64

3.7.2.2.	Metadata	64

3.7.2.3.	Execution of Comparison Software	64

3.7.3.	Solutions to Possible Problems	64

3.7.4.	Stand-alone Test Procedures for Aqua FM4	66

3.7.4.1.	PCF Generator	66

3.7.4.2.	Execution	67

3.7.4.3.	Exit Codes	69

3.7.4.4.	Main Processor Test Summary	69

3.7.5.	Evaluation Procedures	69

3.7.5.1.	Log and Status File Results	69

3.7.5.2.	Metadata	69

3.7.5.3.	Execution of Comparison Software	69

3.7.6.	Solutions to Possible Problems	69

3.8.	CER10.1P5 Main Processor	71

3.8.1.	Stand Alone Test Procedures for Aqua FM3	71

3.8.1.1.	PCF Generator	71

3.8.1.2.	Execution	72

3.8.1.3.	Exit Codes	72

3.8.1.4.	Main Processor Test Summary	72

3.8.2.	Evaluation Procedures	72

3.8.2.1.	Log and Status File Results	72

3.8.2.2.	Metadata	72

3.8.2.3.	Execution of Comparison Software	72

3.8.3.	Solutions to Possible Problems	73

3.8.4.	Stand Alone Test Procedures for Aqua FM4	74

3.8.4.1.	PCF Generator	74

3.8.4.2.	Execution	74

3.8.4.3.	Exit Codes	75

3.8.4.4.	Main Processor Test Summary	75

3.8.5.	Evaluation Procedures	75

3.8.5.1.	Log and Status File Results	75

3.8.5.2.	Metadata	75

3.8.5.3.	Execution of Comparison Software	75

3.8.6.	Solutions to Possible Problems	76

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagrams	B-1

Appendix C - File Description Tables	C-1

C.1.	Production Script	C-1

C.2.	Executables	C-1

C.3.	Status Message Files	C-2

C.4.	Ancillary Input Data	C-2

C.5.	Processing Control Files (PCF), Metadata Control Files (MCF)	C-3

Figure B-1.  Directory Structure for the TISA Averaging (tisa_avg) Tar File	B-1

Table 3-1.  Test Summary for PGE 7.1.1P1	11

Table 3-2.  Test Summary for PGE 7.1.1P1	14

Table 3-3.  Test Summary for PGE 7.1.1P1	17

Table 3-4.  Test Summary for PGE 7.1.1P1	20

Table C.1-1.  Production Scripts @ ($CERESHOME/tisa_avg/bin)	C-1

Table C.2-1.  Executables	C-1

Table C.3-1.  Status Message Files @ ($CERESHOME/tisa_avg/smf)	C-2

Table C.4-1.  Ancillary Input Data @ ($CERESHOME/tisa_avg/data/ancillary/static)	C-2

Table C.5-1.  Process Control Files (PCF) @ (CERESHOME/tisa_avg/rcf)	C-3

Table C.5-2.  Metadata Control Files (MCF) for Subsystem 10.0 @ 	($CERESHOME/tisa_avg/rcf)	C-3

# Introduction

The Clouds and the Earth’s Radiant Energy System (CERES) is a key component of the Earth Observing System (EOS) program.  The CERES instrument provides radiometric measurements of the Earth's atmosphere from three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The CERES instruments are improved models of the Earth Radiation Budget Experiment (ERBE) scanner instruments, which operated from 1984 through 1990 on the National Aeronautics and Space Administration’s (NASA) Earth Radiation Budget Satellite (ERBS) and on the National Oceanic and Atmospheric Administration’s (NOAA) operational weather satellites NOAA-9 and NOAA-10.  The strategy of flying instruments on Sun-synchronous, polar orbiting satellites, such as NOAA-9 and NOAA-10, simultaneously with instruments on satellites that have precessing orbits in lower inclinations, such as ERBS, was successfully developed in ERBE to reduce time sampling errors.  CERES continues that strategy by flying instruments on the polar orbiting EOS platforms simultaneously with an instrument on the Tropical Rainfall Measuring Mission (TRMM) spacecraft, which has an orbital inclination of 35 degrees.  In addition, to reduce the uncertainty in data interpretation and to improve the consistency between the cloud parameters and the radiation fields, CERES includes cloud imager data and other atmospheric parameters.  The TRMM satellite carries one CERES instrument while the EOS satellites carry two CERES instruments, one operating in a fixed azimuth plane scanning mode (FAPS) for continuous Earth sampling and the other operating in a rotating azimuth plane scan mode (RAPS) for improved angular sampling.

## Document Overview

This document, the CERES Release 4 Test Plan for the Time Interpolation and Averaging Subsystems 7.1 and Subsystem 10.0, Version 1, provides a description of the CERES Time Interpolation and Spatial Averaging Release 3 software and supporting data files and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the results of executing the software.  A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B, and a description of the software and data files is contained in Appendix C.

The document is organized as follows.

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

Appendix B - Directory Structure Diagrams

Appendix C - File Description Tables

## Subsystem Overview

### CERES Time Space Interpolation (TSI) Subsystem 7.1 Main Processor

The time interpolation process (7.1), one of the two key parts of Subsystem 7.0, temporally interpolates CERES data and produces global synoptic maps of top-of-the-atmosphere (TOA) fluxes and cloud properties on a 1.0-degree equal-area grid.  Another key part of Subsystem 7.0, the Synoptic Surface and Atmospheric Radiation Budget (SARB), Subsystem 7.2, produces the Intermediate Synoptic Radiative Fluxes and Clouds (SYNI), which contains the vertical structure of atmospheric and surface flux using the interpolated data as input and boundary conditions.

The main input to the time interpolation process is the Hourly Gridded Single Satellite Fluxes and Clouds (FSW) product, produced by Atmospheric Gridding and Spatial Averaging, Subsystem 6.0.  The gridded shortwave (SW) and longwave (LW) TOA fluxes and cloud information are the key items to be interpolated.  The radiative profile will be recalculated in the SARB part of Subsystem 7.0 using the interpolated fluxes as constraints.  This process produces the internal product, Time Space Interpolate (TSI).  These files contain nested grid region data which is the input to Subsystem 7.2.

The time interpolation process produces global maps of TOA total-sky LW and SW flux, TOA clear-sky LW and SW flux, TOA window radiances, and cloud properties at Universal Time (UT) for every day of the month.  The process of producing synoptic maps involves:

Cloud properties from the CERES times of observation are interpolated for every hour of the month.

The CERES TOA LW and SW fluxes are interpolated for every hour using geostationary data to assist in modeling meteorological variations between times of observations.

### Compute Regional, Zonal, and Global Averages Subsystem 8.0 Main Processor

The Monthly Regional, Zonal, and Global Radiation Fluxes and Cloud Properties Subsystem 8.0 produces regional, zonal and global monthly and monthly-hourly means.  These means are calculated from one month of synoptic maps on a regional basis and then combined to produce zonal and global averages.

The main input to this Subsystem is the Surface and Atmospheric Radiation Budget (SARB) product, produced by Subsystem 7.2, SYNI.  This product contains one month of 3-hourly synoptic maps of top-of-atmosphere (TOA) LW and SW fluxes, TOA window fluxes, upwelling and downwelling SW and LW fluxes at each standard CERES pressure level, and numerous cloud parameters for each region of the CERES global 1.0-degree equal-area grid.  The flux parameters include both total-sky and clear-sky.

The three archival products output from this Subsystem are the Monthly Regional Radiative Fluxes and Clouds (AVG) product (HDF format) which contains regional monthly and monthly-hourly means of fluxes and cloud parameters, the Monthly Zonal and Global Radiative Fluxes,  Clouds (ZAVG) product (HDF format) which contains the zonal and global monthly and cloud parameters, and the Synoptic Radiative Fluxes and Clouds (SYN) product (HDF format) which contains regional synoptic hourly means of fluxes and cloud parameters.

The main steps involved in the averaging process are:

- Read the synoptically ordered data.

Average the flux data to produce regional synoptic hourly, monthly and monthly-hourly means.

Average the cloud properties using the specified weighting schemes to produce regional synoptic hourly, monthly and monthly-hourly means.

Average the regional means to produce zonal means.

Average the zonal means to produce global means.

### Compute Monthly and Regional TOA and SRB Averages Subsystem 10.0 Main Processor

The Monthly Regional TOA and SRB Averages Subsystem (10.0) computes averages of TOA longwave (LW) and shortwave (SW) fluxes, surface fluxes, and cloud properties on regional, zonal, and global spatial scales.  The main input to Subsystem 10.0 is the Hourly Gridded Single Satellite TOA and Surface Fluxes and Clouds (SFC) product produced by Surface Gridding and Spatial Averaging Subsystem (9).  SFC contains hourly single satellite flux and cloud properties averaged over 1.0-degree regions.  Subsystem 10.0 produces the Monthly Regional TOA and SRB Averages (SRBAVG) product (HDF-EOS format).  Two methods are used to compute the regional TOA total-sky flux averages.  TOA flux estimates from both of the two methods are used to produce estimates of surface flux at all temporal and spatial scales using the TOA-to-surface flux parameterization schemes for shortwave and longwave.

The process of producing the means stored in SRBAVG involves:

- The TOA clear-sky flux data, surface flux data, and the cloud property data are linearly interpolated.

Monthly and monthly-hourly means are calculated from the interpolated fluxes and cloud properties on regional, zonal, and global scales.

### Compute Monthly Hourly CERES Clear-sky Albedo, CERES Clear-sky map and Monthly Regional Snow/Ice Map

The Clear-sky Map, the Monthly Hourly CERES clear-sky Albedo and Monthly Regional Snow/Ice Map are required for inputs into Subsystem 10.0.  The main input are the Hourly Gridded Single Satellite TOA and Surface Fluxes and Clouds (SFC) product from Subsystem 9.

The process of producing the Monthly Hourly CERES clear-sky Albedo, the Clear-sky map and the Monthly Snow/Ice map involved:

- The TOA clear-sky flux data and the cloud property data are linearly interpolated.

Monthly and monthly-hourly means are calculated from the interpolated fluxes and cloud properties on regional.

The CERES clear-sky albedos were computed and the adjusted depending on the regional surface type to create the proper clear-sky map.

From the surface input data from gridding, the snow and ice data are averaged for each region.

### Compute Daily and Regional TOA and SRB Averages and Produce ISCCP Format Cloud Types

The regional daily averages of TOA fluxes, surface fluxes, aerosol data and cloud data are stored in additional SRBAVG_Daily1 and SRBAVG_Daily2.  The GGEO cloud data in ISCCP format are stored in SRBAVG-ISCCP-D2-like1, and the MODIS cloud data in ISCCP format are stored in SRBAVG-ISCCP-D2-like2.  A QC-ISCCP-D2-NITE is also produced for the nighttime MODIS cloud.

The process of computing daily and regional TOA and SRB averages and producing ISCCP format cloud types involved:

- GGEO TOA fluxes, surface fluxes and the merged GGEO and CERES cloud data are averaged daily for each region.

- CERES TOA fluxes, ocean and land aerosol data, snow/ice from the ten minutes snow map, the zonal solar incident and the MODIS cloud data are also averaged daily

- GGEO and MODIS cloud are averaged into 15 ISCCP cloud types and 9 GMT time slots for each region.

# Software and Data File Installation Procedures

This section describes how to install Time Interpolation and Space Averaging (TISA) Averaging Subsystems 7.1, 8.0, and 10.0 software in preparation for making the necessary test runs at the Langley Atmospheric Sciences Data Center (ASDC).  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables, and compiling the TISA Averaging source code.

## Installation

Software/Delta File Install Procedure:

- The scripts, Makefile, and Process Control Files in Subsystems 7.1 and Subsystem 10.0 expect the CERES environment variable, $CERESENV, to point to a file which sets the following environment variables:

PGSDIR	Directory for Toolkit libraries

F90	Pointer to the SGI F90 64-bit compiler

CERESHOME	Top Directory for CERES software

CERESLIB	Directory for CERESlib

F90COMP, FCOMP	SGI 64-bit Fortran 90 compile flags

F90LOAD	SGI 64-bit Fortran 90 load flags

PGSMSG	Directory which contains Toolkit and CERES

Status Message Files

PGSINC	Pointer to the PGS include file directory

HDFDIR	Pointer to the HDF home directory

HDFEOSDIR	Pointer to the HDF-EOS home directory

Change directory to the directory where you plan to install the TISA Averaging Subsystem.  The following instructions assume that the directory will be $CERESHOME.

For Subsystem 7.1, uncompress and untar the tar files by replacing XXX with the appropriate SCCR number and typing the following commands:

source $CERESENV

cd $CERESHOME/tisa_avg/data/data_7

rm -r out_comp

rm -r out_exp

rm -r input

cd $CERESHOME

uncompress TISAavg_anc_R4-XXX.tar.Z

tar xvf TISAavg_anc_R4-XXX.tar

uncompress TISAavg_src_1_R4-XXX.tar.Z

tar xvf TISAavg_src_1_R4-XXX.tar

On Warlock:

uncompress TISAavg_data7_1_warlock_R4-XXX.tar.Z

tar xvf TISAavg_data7_1_warlock_R4-XXX.tar

uncompress TISAavg_data7_2_warlock_R4-XXX.tar.Z

tar xvf TISAavg_data7_2_warlock_R4-XXX.tar

uncompress TISAavg_data7_3_warlock_R4-XXX.tar.Z

tar xvf TISAavg_data7_3_warlock_R4-XXX.tar

On Linux Cluster:

uncompress TISAavg_data7_1_cluster_R4-XXX.tar.Z

tar xvf TISAavg_data7_1_cluster_R4-XXX.tar

uncompress TISAavg_data7_2_cluster_R4-XXX.tar.Z

tar xvf TISAavg_data7_2_cluster_R4-XXX.tar

uncompress TISAavg_data7_3_cluster_R4-XXX.tar.Z

tar xvf TISAavg_data7_3_cluster_R4-XXX.tar

For Subsystem 8, uncompress and untar the tar files by replacing XXX with the appropriate SCCR number and typing the following commands:

uncompress TISAavg_anc_R4-XXX.tar.Z

tar xvf TISAavg_anc_R4-XXX.tar

uncompress TISAavg_src_R4-XXX.tar.Z

tar xvf TISAavg_src_R4-XXX.tar

uncompress TISAavg_src_8.2_R4-XXX.tar.Z

tar xvf TISAavg_src_8.2_R4-XXX.tar

uncompress TISAavg_data8_1_R4-XXX.tar.Z

tar xvf TISAavg_data8_1_R4-XXX.tar

uncompress TISAavg_data8_2_R4-XXX.tar.Z

tar xvf TISAavg_data8_2_R4-XXX.tar

uncompress TISAavg_data8_3_R4-XXX.tar.Z

tar xvf TISAavg_data8_3_R4-XXX.tar

uncompress TISAavg_data8_4_R4-XXX.tar.Z

tar xvf TISAavg_data8_4_R4-XXX.tar

For Subsystem 10, uncompress and untar the tar files by replacing XXX with the appropriate SCCR number and typing the following commands:

source $CERESENV

cd $CERESHOME

uncompress TISAavg_src1_R4-XXX.tar.Z

tar xvf TISAavg_src1_R4-XXX.tar

uncompress TISAavg_src2_R4-XXX.tar.Z

tar xvf TISAavg_src2_R4-XXX.tar

uncompress TISAavg_data10_1_R4-XXX.tar.Z

tar xvf TISAavg_data10_1_R4-XXX.tar

uncompress TISAavg_data10_2_R4-XXX.tar.Z

tar xvf TISAavg_data10_2_R4-XXX.tar

uncompress TISAavg_data10_3_R4-XXX.tar.Z

tar xvf TISAavg_data10_3_R4-XXX.tar

Directory - Files/Direction

NOTE:  If the PMOA files are not included in the delivery, then skip this step.

Since PMOA files are delivered, the above PMOA files are required to be moved to this
directory:

$CERESHOME/tisa_grid/data/out_comp/data/PMOA

## Compilation

- For Subsystem 7.1, Subsystem 8, and Subsystem 10 create the message files and message include files:

source $CERESENV

cd $CERESHOME/tisa_avg/smf

$CERESLIB/bin/smfcompile_all.csh

The smfcompile_all.csh will send a message to the screen at completion to indicate whether or not the compile was successful.  ASDC personnel may have an alternate procedure for compiling these message files.  Any alternate procedure should copy all message include files to the $PGSINC directory and all message files to the $PGSMSG directory.

For Subsystem 10 only for PGE CER10.1P1, webplot.exe, the executable for creating binary data files and converting to .gif files for web plotting for Subsystem 10, is not provided in the tar file.  To create the executable in directory $CERESHOME/tisa_avg/web/plot/dat, type the following commands:

source $CERESENV

cd $CERESHOME/tisa_avg/web/plot/dat

make -f makeplot

NOTE:  The executable, webplot.exe, is run during processing of Subsystem 10, so the above steps must be done before running Subsystem 10.

For the Subsystem 7.1 Main Processor, tisa7.exe, the executable for the Subsystem 7.1 Main Processor, is not provided in the tar file.  To create the executable in directory $CERESHOME/tisa_avg/bin, type the following commands:

source $CERESENV

cd $CERESHOME/tisa_avg/src

./compile_ss7.csh

For the Subsystem 8 Main Processor, tisa8.exe, the executable for the Subsystem 8 Main Processor is not provided in the tar file.  To create the executable in directory $CERESHOME/tisa_avg/bin, type the following commands:

source $CERESENV

cd $CERESHOME/tisa_avg/src

./compile_ss8.csh

For the Subsystem 8 SYN Plot Processor, syn_plots.exe, the executable for the Subsystem 8 SYN plot Processor is not provided in the tar file. To create the executable in directory $CERESHOME/tisa_avg/bin, type the following commands:

cd $CERESHOME/tisa_avg/bin

./compile_8.2P1.csh

For the Subsystem 10 CERES Clear-sky and Snow/Ice Maps Main Processor (PGE CER10.1P2 or CER10.1P5), the executable tisa10_phase1.exe or tisa10_aqua_phase1.exe is not provided in the tar file.  To create the executable in directory $CERESHOME/tisa_avg/bin, type the following commands:

cd $CERESHOME/tisa_avg/src

./compile_ss10_phase1.csh

For the Subsystem 10 Main Processors (PGEs CER10.1P1 or CER10.1P4), the executable tisa10.CER10.1P1.exe or tisa10.CER10.1P4.exe is not provided in the tar file.  To create the executable in directory $CERESHOME/tisa_avg/bin, type the following commands:

cd $CERESHOME/tisa_avg/src

./compile_ss10.csh

For Subsystem 8, comp8.exe is the executable generating ascii files for comparison purposes.  To create the executable in directory $CERESHOME/tisa_avg/test_suites/CER8.1P1, type the following commands:

cd $CERESHOME/tisa_avg/test_suites/CER8.1P1

make -f makecmp_8

For Subsystem 10 PGE CER10.1P1, comp10.exe is the executable generating binary files for comparison purposes.  To create the executable in directory $CERESHOME/tisa_avg/test_suites/CER10.1P1, type the following commands:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P1

make -f makecmp_10

For Subsystem 10 PGE CER10.1P4, comp10.exe is the executable generating binary files for comparison purposes.  To create the executable in directory $CERESHOME/tisa_avg/test_suites/CER10.1P4, type the following commands:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P4

make -f makecmp_10

For Subsystem 10 PGE CER10.1P3, comp10.exe is the executable generating binary files for comparison purposes.  To create the executable in directory $CERESHOME/tisa_avg/test_suites/CER10.1P3, type the following commands:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P3

make -f makecmp_10

# Test and Evaluation Procedures

This section provides general information on how to execute Subsystem 10.0 and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## CER7.1.1P1 Main Processor for Subsystem 7.1

### Stand-alone Test Procedures for Terra FM1

#### PCF Generator

The Main Processor production script, CER7.1.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_7.1.1P1_ascii_gen_ssit.csh, and then executing the PCF generator, tisavg_7.1.1P1_pcfgen.csh.

For production run, the ASCII file generator, tisavg_7.1.1P1_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments: 1-digit Subsystem Number(7); 4-digit Data Year(1998); 2-digit Data Month(01); and 1-character GGEO data file exist flag(Y), (Optional, default value = Y).  The PCF generator, tisavg_7.1.1P1_pcfgen.csh, then executes using the newly created ASCII input file name as a command-line argument.

NOTE: The PCF generator script, tisavg_7.1.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the $CERESHOME/tisa_avg/bin directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test-env.csh FM1

source $CERESHOME/tisa_avg/bin/ENV7.1.1P1-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_ascii_gen_ssit.csh 7 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER7.1.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER7.1.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER7.1.1P1 $year $month CER7.1.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER7.1.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_7/out_comp:

CER_TSIB_$INSTANCE\Zi*

CER_TSIB_$INSTANCE\Zi*.met

CER_JRGRP_$INSTANCE

CER_JRGRP_$INSTANCE.met

CER_JVREG_$INSTANCE

CER_JVREG_$INSTANCE.met

*i indicates multiple files which, for the test case, range from 052 - 054.

#### Exit Codes

The processor CER7.1.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Table 3-1.  Test Summary for PGE 7.1.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM1 | FM1 |
| Run Time | 10:47 minutes | 2:38 minutes |
| Memory | 84112 K | 1364 K |
| Required Disk Space | 2.5 GB | 2.5 GB |

### Evaluation Procedures

When running the production script, CER7.1.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER7.1.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_7/runlogs.

#### Metadata

Metadata files which end in extension, ’.met’, are located in the same directory as their corresponding output files after CER7.1.1P1 has been executed.

#### Execution of Comparison Software

Due to the size of the output of SS7.1 (307 megabytes), only three of the 180 files is being delivered in this package; however, the rest will be provided if requested.  The evaluation software for SS7.1 does a diff on the one file in out_exp and the first file created during processing:

cmp $CERESHOME/tisa_avg/data/data_7/out_exp/CER_TSIB_$INSTANCE’Zi*’ $CERESHOME/tisa_avg/data/data_7/out_comp/CER_TSIB_$INSTANCE’Zi*’

*i indicates multiple files which, for the test case, range from 052 -054.

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER7.1.1P1:

$CERESHOME/tisa_avg/bin/cleanup 7.1.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Terra FM2

#### PCF Generator

The Main Processor production script, CER7.1.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_7.1.1P1_ascii_gen_ssit.csh, and then executing the PCF generator, tisavg_7.1.1P1_pcfgen.csh.

For production run, the ASCII file generator, tisavg_7.1.1P1_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments: 1-digit Subsystem Number(7); 4-digit Data Year(1998); 2-digit Data Month(01); and 1-character GGEO data file exist flag(Y), (Optional, default value = Y).  The PCF generator, tisavg_7.1.1P1_pcfgen.csh, then executes using the newly created ASCII input file name as a command-line argument.

NOTE: The PCF generator script, tisavg_7.1.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the $CERESHOME/tisa_avg/bin directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test-env.csh FM2

source $CERESHOME/tisa_avg/bin/ENV7.1.1P1-env.csh

setenv year 2001

setenv month 10

setenv DATADATE 200110

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_ascii_gen_ssit.csh 7 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER7.1.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER7.1.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER7.1.1P1 $year $month CER7.1.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER7.1.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_7/out_comp:

CER_TSIB_$INSTANCE\Zi*

CER_TSIB_$INSTANCE\Zi*.met

CER_JRGRP_$INSTANCE

CER_JRGRP_$INSTANCE.met

CER_JVREG_$INSTANCE

CER_JVREG_$INSTANCE.met

*i indicates multiple files which, for the test case, range from 052 - 054.

#### Exit Codes

The processor CER7.1.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Table 3-2.  Test Summary for PGE 7.1.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM2 | FM2 |
| Run Time | 9:17 minutes | 2:25 minutes |
| Memory | 84112 K | 1364 K |
| Required Disk Space | 2.5 GB | 2.5 GB |

### Evaluation Procedures

When running the production script, CER7.1.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER7.1.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_7/runlogs.

#### Metadata

Metadata files which end in extension, ’.met’, are located in the same directory as their corresponding output files after CER7.1.1P1 has been executed.

#### Execution of Comparison Software

Due to the size of the output of SS7.1 (307 megabytes), only three of the 180 files is being delivered in this package; however, the rest will be provided if requested.  The evaluation software for SS7.1 does a diff on the one file in out_exp and the first file created during processing:

cmp $CERESHOME/tisa_avg/data/data_7/out_exp/CER_TSIB_$INSTANCE’Zi*’ $CERESHOME/tisa_avg/data/data_7/out_comp/CER_TSIB_$INSTANCE’Zi*’

*i indicates multiple files which, for the test case, range from 052 -054.

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER7.1.1P1:

$CERESHOME/tisa_avg/bin/cleanup 7.1.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Aqua FM3

#### PCF Generator

The Main Processor production script, CER7.1.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_7.1.1P1_ascii_gen_ssit.csh, and then executing the PCF generator, tisavg_7.1.1P1_pcfgen.csh.

For production run, the ASCII file generator, tisavg_7.1.1P1_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments: 1-digit Subsystem Number(7); 4-digit Data Year(1998); 2-digit Data Month(01); and 1-character GGEO data file exist flag(Y), (Optional, default value = Y).  The PCF generator, tisavg_7.1.1P1_pcfgen.csh, then executes using the newly created ASCII input file name as a command-line argument.

NOTE: The PCF generator script, tisavg_7.1.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the $CERESHOME/tisa_avg/bin directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test-env.csh FM3

source $CERESHOME/tisa_avg/bin/ENV7.1.1P1-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM3-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_ascii_gen_ssit.csh 7 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER7.1.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER7.1.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER7.1.1P1 $year $month CER7.1.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER7.1.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_7/out_comp:

CER_TSIB_$INSTANCE\Zi*

CER_TSIB_$INSTANCE\Zi*.met

CER_JRGRP_$INSTANCE

CER_JRGRP_$INSTANCE.met

CER_JVREG_$INSTANCE

CER_JVREG_$INSTANCE.met

*i indicates multiple files which, for the test case, range from 052 - 054.

#### Exit Codes

The processor CER7.1.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Table 3-3.  Test Summary for PGE 7.1.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM3 | FM3 |
| Run Time | 10:41 minutes | 2:27 minutes |
| Memory | 84112 K | 1364 K |
| Required Disk Space | 2.5 GB | 2.5 GB |

### Evaluation Procedures

When running the production script, CER7.1.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER7.1.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_7/runlogs.

#### Metadata

Metadata files which end in extension, ’.met’, are located in the same directory as their corresponding output files after CER7.1.1P1 has been executed.

#### Execution of Comparison Software

Due to the size of the output of SS7.1 (307 megabytes), only three of the 180 files is being delivered in this package; however, the rest will be provided if requested.  The evaluation software for SS7.1 does a diff on the one file in out_exp and the first file created during processing:

cmp $CERESHOME/tisa_avg/data/data_7/out_exp/CER_TSIB_$INSTANCE’Zi*’ $CERESHOME/tisa_avg/data/data_7/out_comp/CER_TSIB_$INSTANCE’Zi*’

*i indicates multiple files which, for the test case, range from 052 -054.

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER7.1.1P1:

$CERESHOME/tisa_avg/bin/cleanup 7.1.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Aqua FM4

#### PCF Generator

The Main Processor production script, CER7.1.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_7.1.1P1_ascii_gen_ssit.csh, and then executing the PCF generator, tisavg_7.1.1P1_pcfgen.csh.

For production run, the ASCII file generator, tisavg_7.1.1P1_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments: 1-digit Subsystem Number(7); 4-digit Data Year(1998); 2-digit Data Month(01); and 1-character GGEO data file exist flag(Y), (Optional, default value = Y).  The PCF generator, tisavg_7.1.1P1_pcfgen.csh, then executes using the newly created ASCII input file name as a command-line argument.

NOTE: The PCF generator script, tisavg_7.1.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the $CERESHOME/tisa_avg/bin directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test-env.csh FM4

source $CERESHOME/tisa_avg/bin/ENV7.1.1P1-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM4-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_ascii_gen_ssit.csh 7 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_7.1.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER7.1.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER7.1.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER7.1.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER7.1.1P1 $year $month CER7.1.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER7.1.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_7/out_comp:

CER_TSIB_$INSTANCE\Zi*

CER_TSIB_$INSTANCE\Zi*.met

CER_JRGRP_$INSTANCE

CER_JRGRP_$INSTANCE.met

CER_JVREG_$INSTANCE

CER_JVREG_$INSTANCE.met

*i indicates multiple files which, for the test case, range from 052 - 054.

#### Exit Codes

The processor CER7.1.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Table 3-4.  Test Summary for PGE 7.1.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM4 | FM4 |
| Run Time | 10:09 minutes | 2:29 minutes |
| Memory | 84112 K | 1364 K |
| Required Disk Space | 2.5 GB | 2.5 GB |

### Evaluation Procedures

When running the production script, CER7.1.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER7.1.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_7/runlogs.

#### Metadata

Metadata files which end in extension, ’.met’, are located in the same directory as their corresponding output files after CER7.1.1P1 has been executed.

#### Execution of Comparison Software

Due to the size of the output of SS7.1 (307 megabytes), only three of the 180 files is being delivered in this package; however, the rest will be provided if requested.  The evaluation software for SS7.1 does a diff on the one file in out_exp and the first file created during processing:

cmp $CERESHOME/tisa_avg/data/data_7/out_exp/CER_TSIB_$INSTANCE’Zi*’ $CERESHOME/tisa_avg/data/data_7/out_comp/CER_TSIB_$INSTANCE’Zi*’

*i indicates multiple files which, for the test case, range from 052 -054.

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER7.1.1P1:

$CERESHOME/tisa_avg/bin/cleanup 7.1.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

## CER8.1P1 Main Processor

### Stand Alone Test Procedures for Terra FM1

#### PCF Generator

The Main Processor production script, CER8.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_8.1P1_ascii_gen_test, and then executing the PCF generator, tisavg_8.1P1_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_8.1P1_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command line arguments, 1 or 2-digit subsystem number, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_8.1P1_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_8.1P1_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM1.csh

source $CERESHOME/tisa_avg/bin/ENV8.1P1-env.csh

setenv year 2001

setenv month 07

setenv DATADATE 200107

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_8.1P1_ascii_gen_test.csh 8 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_8.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER8.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER8.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER8.1P1 $year $month CER8.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_8.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_8/out_comp:

CER_AVG_$INSTANCE

CER_AVG_$INSTANCE.met

CER_ZAVG_$INSTANCE

CER_ZAVG_$INSTANCE.met

CER_SYN_$INSTANCE\i*

CER_SYN_$INSTANCE\i*.met

CER_LRGRP_$INSTANCE

CER_LRGRP_$INSTANCE.met

*i indicates multiple day files which, for the test case, range from 01-31.

#### Exit Codes

All CER8.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	1 hours 15 minutes and 45 seconds

Memory:	242224 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER8.1P1, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER8.1P1_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_8/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER8.1P1 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_8/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_8/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss8_output_Terra_FM1.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER8.1P1

eval_ss8_output_Terra_FM1.csh

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER8.1P1:

$CERESHOME/tisa_avg/bin/cleanup 8.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand Alone Test Procedures for Terra FM2

#### PCF Generator

The Main Processor production script, CER8.1P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_8.1P1_ascii_gen_test, and then executing the PCF generator, tisavg_8.1P1_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_8.1P1_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command line arguments, 1 or 2-digit subsystem number, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_8.1P1_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_8.1P1_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM2.csh

source $CERESHOME/tisa_avg/bin/ENV8.1P1-env.csh

setenv year 2001

setenv month 08

setenv DATADATE 200108

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_8.1P1_ascii_gen_test.csh 8 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_8.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER8.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.1P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER8.1P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER8.1P1 $year $month CER8.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_8.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_8/out_comp:

CER_AVG_$INSTANCE

CER_AVG_$INSTANCE.met

CER_ZAVG_$INSTANCE

CER_ZAVG_$INSTANCE.met

CER_SYN_$INSTANCE\i*

CER_SYN_$INSTANCE\i*.met

CER_LRGRP_$INSTANCE

CER_LRGRP_$INSTANCE.met

*i indicates multiple day files which, for the test case, range from 01-31.

#### Exit Codes

All CER8.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	1 hours 15 minutes and 45 seconds

Memory:	242224 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER8.1P1, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER8.1P1_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_8/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER8.1P1 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_8/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_8/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss8_output_Terra_FM2.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER8.1P1

eval_ss8_output_Terra_FM2.csh

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER8.1P1:

$CERESHOME/tisa_avg/bin/cleanup 8.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

## CER8.2P1 Post Processor

### Stand Alone Test Procedures for Terra FM1

#### PCF Generator

The Post Processor production script, CER8.2P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_8.2P1_ascii_gen_test, and then executing the PCF generator, tisavg_8.2P1_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_8.2P1_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires two command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_8.2P1_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_8.2P1_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

source $CERESENV

set RCFDIR = $CERESHOME/tisa_avg/rcf

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM1.csh

source $CERESHOME/tisa_avg/bin/ENV8.2P1-env.csh

setenv year 2001

setenv month 07

setenv DATADATE 200107

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/cleanup_8.2P1.csh $year$month

$CERESHOME/tisa_avg/bin/tisavg_8.2P1_ascii_gen_test.csh $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.2P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_8.2P1_pcfgen.csh $RCFDIR/CER8.2P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.2P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER8.2P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER8.2P1 $year $month $RCFDIR/CER8.2P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_8.2P1, will be executed and will create the following files in $CERESHOME/tisa_avg/web/plot/gif/SYN_200107 directory:

AER_OPT_*.gif

ALB_SFC_CLR_*.gif

CLD_EMISS_*.gif

CLD_FRAC_*.gif

CLD_ICE_DIAM_*.gif

CLD_LIQ_RAD_*.gif

CLD_OPT_*.gif

CLD_PBOT_*.gif

CLD_PHASE_*.gif

CLD_PTOP_*.gif

CLD_TEMP_*.gif

LW_DOWN_SFC_*.gif

LW_NET_SFC_*.gif

LW_TOA_CLDFORC_*.gif

LW_TOA_OBS_*.gif

LW_TOA_TUN_*.gif

LW_TOA_UNT-OBS_*.gif

NET_TOA_OBS_*.gif

SFC_UV_INDEX_*gif

SW_DOWN_SFC_*.gif

SW_NET_SFC_*.gif

SW_SFC_AERFORC_*.gif

SW_TOA_AERFORC_*.gif

SW_TOA_CLDFORC_*.gif

SW_TOA_OBS_*.gif

SW_TOA_TUN_*.gif

SW_TOA_UNT-OBS_*.gif

* files 01 - 248.

#### Exit Codes

All CER8.2P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	6141.997u 1004.770s 2:40:12.41

Memory:	30552 K

Required Disk Space:	1GB

### Evaluation Procedures

When running the production script, CER8.2P1, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER8.2P1_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_8/runlogs.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_8/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_8/int_prod.  These input files are accessed from those areas for the comparison.

eval_ss8_output_Terra_FM1.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER8.2P1

$CERESLIB/bin/setVariables.csh test

set PCFTest = 1

eval_ss8.2_output_Terra_FM1.csh $PCFTest

set LOGTest = 2

eval_ss8.2_output_Terra_FM1.csh $LOGTest

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup_8.2P1.csh, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER8.2P1:

$CERESHOME/tisa_avg/bin/cleanup_8.2P1.csh $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand Alone Test Procedures for Terra FM2

#### PCF Generator

The Main Processor production script, CER8.2P1, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_8.2P1_ascii_gen_test, and then executing the PCF generator, tisavg_8.2P1_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_8.2P1_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires two command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_8.2P1_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_8.2P1_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

set RCFDIR = $CERESHOME/tisa_avg/rcf

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM2.csh

source $CERESHOME/tisa_avg/bin/ENV8.2P1-env.csh

setenv year 2001

setenv month 08

$CERESHOME/tisa_avg/bin/cleanup_8.2P1.csh $year$month

setenv DATADATE 200108

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_8.2P1_ascii_gen_test.csh $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.2P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_8.2P1_pcfgen.csh $RCFDIR/CER8.2P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER8.2P1_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER8.2P1, followed by three command-line arguments: year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER8.2P1 $year $month $RCFDIR/CER8.2P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_8.2P1, will be executed and will create the following files in $CERESHOME/tisa_avg/web/plot/gif/SYN_200108 directory:

AER_OPT_*.gif

ALB_SFC_CLR_*.gif

CLD_EMISS_*.gif

CLD_FRAC_*.gif

CLD_ICE_DIAM_*.gif

CLD_LIQ_RAD_*.gif

CLD_OPT_*.gif

CLD_PBOT_*.gif

CLD_PHASE_*.gif

CLD_PTOP_*.gif

CLD_TEMP_*.gif

LW_DOWN_SFC_*.gif

LW_NET_SFC_*.gif

LW_TOA_CLDFORC_*.gif

LW_TOA_OBS_*.gif

LW_TOA_TUN_*.gif

LW_TOA_UNT-OBS_*.gif

NET_TOA_OBS_*.gif

SFC_UV_INDEX_*gif

SW_DOWN_SFC_*.gif

SW_NET_SFC_*.gif

SW_SFC_AERFORC_*.gif

SW_TOA_AERFORC_*.gif

SW_TOA_CLDFORC_*.gif

SW_TOA_OBS_*.gif

SW_TOA_TUN_*.gif

SW_TOA_UNT-OBS_*.gif

* files 01 - 248.

#### Exit Codes

All CER8.2P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	6141.997u 1004.770s 2:40:12.41

Memory:	30552 K

Required Disk Space:	1 GB

### Evaluation Procedures

When running the production script, CER8.2P1, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER8.1P1_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_8/runlogs.

cd $CERESHOME/ggeo/test_suites/CER8.2P1

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_8/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_8/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss8.2_output_Terra_FM2.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER8.2P1

$CERESLIB/bin/setVariables.csh test

set PCFTest = 1

eval_ss8.2_output_Terra_FM2.csh $PCFTest

set LOGTest = 2

eval_ss8.2_output_Terra_FM2.csh $LOGTest

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script, which removes PGE created files, cleanup_8.2P1.csh, is located in directory $CERESHOME/tisa_avg/bin.  To use the clean-up files for CER8.2P1:

$CERESHOME/tisa_avg/bin/cleanup_8.2P1.csh $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler

## CER10.1P1 Main Processor

### Stand-alone Test Procedures for Terra FM1

(NOTE:  CER10.1P2 has to be run before running this test procedure for Terra.)

#### PCF Generator

The Main Processor production script, CER10.1P1, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P1_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P1_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P1_env.csh and setup_test_env_Terra_FM1.csh.

For production runs, the ASCII file generator, tisavg_10.1P1_ascii_SSIT_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P1_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM1.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P1-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P1_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P1_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P1, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P1 $year $month CER10.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG1_$INSTANCE

CER_SRBAVG1_$INSTANCE.met

CER_SRBAVG2_$INSTANCE

CER_SRBAVG2_$INSTANCE.met

CER_SRBAVG3_$INSTANCE

CER_SRBAVG3_$INSTANCE.met

CER_NQCRP_$INSTANCE

CER_NQCRP_$INSTANCE.met

CER_NRGRP_$INSTANCE

CER_NRGRP_$INSTANCE.met

CER_NVREG_$INSTANCE

CER_NVREG_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic:

CER_xglb_$INSTANCE

CER_xglb_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/web/tsplot:

SURF_TSP_$DATADATE\_2.pdf

TOA_TSP_$DATADATE\_2.pdf

Create the following files in $CERESHOME/tisa_avg/web/plot/gif/TAVG_$DATADATE\_2:

CALB_A_$DATADATE\_2.gif

CALB_B_$DATADATE\_2.gif

CALB_D_$DATADATE\_2.gif

CLDO_HIGH_$DATADATE\_2.gif

CLDO_LMID_$DATADATE\_2.gif

CLDO_LOW_$DATADATE\_2.gif

CLDO_UMID_$DATADATE\_2.gif

CLDP_HIGH_$DATADATE\_2.gif

CLDP_LMID_$DATADATE\_2.gif

CLDP_LOW_$DATADATE\_2.gif

CLDP_UMID_$DATADATE\_2.gif

CLW_A_$DATADATE\_2.gif

CLW_B_$DATADATE\_2.gif

CLW_D_$DATADATE\_2.gif

CNF_A_$DATADATE\_2.gif

CNF_B_$DATADATE\_2.gif

CNF_D_$DATADATE\_2.gif

CSDLW_A_$DATADATE\_2.gif

CSDLW_B_$DATADATE\_2.gif

CSDLW_D_$DATADATE\_2.gif

CSDSW_A_$DATADATE\_2.gif

CSDSW_B_$DATADATE\_2.gif

CSDSW_D_$DATADATE\_2.gif

CSDWN_A_$DATADATE\_2.gif

CSNLW_A_$DATADATE\_2.gif

CSNLW_B_$DATADATE\_2.gif

CSNLW_D_$DATADATE\_2.gif

CSNSW_A_$DATADATE\_2.gif

CSNSW_B_$DATADATE\_2.gif

CSNSW_D_$DATADATE\_2.gif

CSN_B_$DATADATE\_2.gif

CSW_A_$DATADATE\_2.gif

CSW_B_$DATADATE\_2.gif

CSW_D_$DATADATE\_2.gif

CWN_A_$DATADATE\_2.gif

CWN_B_$DATADATE\_2.gif

CWN_D_$DATADATE\_2.gif

TALB_A_$DATADATE\_2.gif

TALB_B_$DATADATE\_2.gif

TALB_D_$DATADATE\_2.gif

TLW_A_$DATADATE\_2.gif

TLW_B_$DATADATE\_2.gif

TLW_D_$DATADATE\_2.gif

TNF_A_$DATADATE\_2.gif

TNF_B_$DATADATE\_2.gif

TNF_D_$DATADATE\_2.gif

TSDLW_B_$DATADATE\_2.gif

TSDSW_A_$DATADATE\_2.gif

TSDSW_B_$DATADATE\_2.gif

TSDSW_D_$DATADATE\_2.gif

TSDWN_A_$DATADATE\_2.gif

TSNLW_A_$DATADATE\_2.gif

TSNLW_B_$DATADATE\_2.gif

TSNLW_D_$DATADATE\_2.gif

TSNSW_A_$DATADATE\_2.gif

TSNSW_B_$DATADATE\_2.gif

TSNSW_D_$DATADATE\_2.gif

TSN_B_$DATADATE\_2.gif

TSW_A_$DATADATE\_2.gif

TSW_B_$DATADATE\_2.gif

TSW_D_$DATADATE\_2.gif

TWN_A_$DATADATE\_2.gif

TWN_B_$DATADATE\_2.gif

TWN_D_$DATADATE\_2.gif

#### Exit Codes

The processor CER10.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	15 minutes 47 seconds

Memory:	132752 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P1 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Terra.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P1

eval_ss10_output_Terra_FM1.csh $year $month

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_xglb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_xglb_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM1 CER10.1P1:

$CERESHOME/tisa_avg/bin/cleanup 10.1P1 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Terra FM2

(NOTE:  CER10.1P2 has to be run before running this test procedure for Terra.)

#### PCF Generator

The Main Processor production script, CER10.1P1, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P1_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P1_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P1_env.csh and setup_test_env_Terra_FM2.csh.

For production runs, the ASCII file generator, tisavg_10.1P1_ascii_ssit_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P1_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P1_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM2.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P1-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P1_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P1_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P1_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P1_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P1_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P1, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P1 $year $month CER10.1P1_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P1, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG1_$INSTANCE

CER_SRBAVG1_$INSTANCE.met

CER_SRBAVG2_$INSTANCE

CER_SRBAVG2_$INSTANCE.met

CER_SRBAVG3_$INSTANCE

CER_SRBAVG3_$INSTANCE.met

CER_NQCRP_$INSTANCE

CER_NQCRP_$INSTANCE.met

CER_NRGRP_$INSTANCE

CER_NRGRP_$INSTANCE.met

CER_NVREG_$INSTANCE

CER_NVREG_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic:

CER_xglb_$INSTANCE

CER_xglb_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/web/tsplot:

SURF_TSP_$DATADATE\_3.pdf

TOA_TSP_$DATADATE\_3.pdf

Create the following files in $CERESHOME/tisa_avg/web/plot/gif/TAVG_$DATADATE\_3:

CALB_A_$DATADATE\_3.gif

CALB_B_$DATADATE\_3.gif

CALB_D_$DATADATE\_3.gif

CLDO_HIGH_$DATADATE\_3.gif

CLDO_LMID_$DATADATE\_3.gif

CLDO_LOW_$DATADATE\_3.gif

CLDO_UMID_$DATADATE\_3.gif

CLDP_HIGH_$DATADATE\_3.gif

CLDP_LMID_$DATADATE\_3.gif

CLDP_LOW_$DATADATE\_3.gif

CLDP_UMID_$DATADATE\_3.gif

CLW_A_$DATADATE\_3.gif

CLW_B_$DATADATE\_3.gif

CLW_D_$DATADATE\_3.gif

CNF_A_$DATADATE\_3.gif

CNF_B_$DATADATE\_3.gif

CNF_D_$DATADATE\_3.gif

CSDLW_A_$DATADATE\_3.gif

CSDLW_B_$DATADATE\_3.gif

CSDLW_D_$DATADATE\_3.gif

CSDSW_A_$DATADATE\_3.gif

CSDSW_B_$DATADATE\_3.gif

CSDSW_D_$DATADATE\_3.gif

CSDWN_A_$DATADATE\_3.gif

CSNLW_A_$DATADATE\_3.gif

CSNLW_B_$DATADATE\_3.gif

CSNLW_D_$DATADATE\_3.gif

CSNSW_A_$DATADATE\_3.gif

CSNSW_B_$DATADATE\_3.gif

CSNSW_D_$DATADATE\_3.gif

CSN_B_$DATADATE\_3.gif

CSW_A_$DATADATE\_3.gif

CSW_B_$DATADATE\_3.gif

CSW_D_$DATADATE\_3.gif

CWN_A_$DATADATE\_3.gif

CWN_B_$DATADATE\_3.gif

CWN_D_$DATADATE\_3.gif

TALB_A_$DATADATE\_3.gif

TALB_B_$DATADATE\_3.gif

TALB_D_$DATADATE\_3.gif

TLW_A_$DATADATE\_3.gif

TLW_B_$DATADATE\_3.gif

TLW_D_$DATADATE\_3.gif

TNF_A_$DATADATE\_3.gif

TNF_B_$DATADATE\_3.gif

TNF_D_$DATADATE\_3.gif

TSDLW_B_$DATADATE\_3.gif

TSDSW_A_$DATADATE\_3.gif

TSDSW_B_$DATADATE\_3.gif

TSDSW_D_$DATADATE\_3.gif

TSDWN_A_$DATADATE\_3.gif

TSNLW_A_$DATADATE\_3.gif

TSNLW_B_$DATADATE\_3.gif

TSNLW_D_$DATADATE\_3.gif

TSNSW_A_$DATADATE\_3.gif

TSNSW_B_$DATADATE\_3.gif

TSNSW_D_$DATADATE\_3.gif

TSN_B_$DATADATE\_3.gif

TSW_A_$DATADATE\_3.gif

TSW_B_$DATADATE\_3.gif

TSW_D_$DATADATE\_3.gif

TWN_A_$DATADATE\_3.gif

TWN_B_$DATADATE\_3.gif

TWN_D_$DATADATE\_3.gif

#### Exit Codes

The processor CER10.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	15 minutes 47 seconds

Memory:	132752 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P1, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P1_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P1 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Terra_FM2.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P1

eval_ss10_output_Terra_FM2.csh $year $month

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_xglb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_xglb_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM2 CER10.1P1:

$CERESHOME/tisa_avg/bin/cleanup 10.1P1 $year$month

## CER10.1P2 Main Processor

(NOTE:  CER10.1P2 has to be run before running the test procedure for CER 10.1P1 Terra.)

### Stand Alone Test Procedures for Terra FM1

#### PCF Generator

The Main Processor production script, CER10.1P2, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_10.1P2_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P2_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_10.1P2_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires 2 command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_10.1P2_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_10.1P2_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM1.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P2-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P2_ascii_ssit_gen.csh  10 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P2_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P2_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P2_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P2_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER10.1P2, followed by one command-line argument:  PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P2  $year $month CER10.1P2_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_10.1P2, will be executed and will create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic/:

CER_SNOW-PCT_$INSTANCE

CER_SNOW-PCT_$INSTANCE.met

CER_mhr-csalb_$INSTANCE

CER_mhr-csalb_$INSTANCE.met

CER_csalb0-intrp2s_$INSTANCE

CER_csalb0-intrp2s_$INSTANCE.met

#### Exit Codes

All CER10.1P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	2 minute and 33 seconds

Memory:	55040 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER10.1P2, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P2_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P2 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new output files from the execution are in $CERESHOME/tisa_avg/data/ancillary/dynamic.  These output files are accessed from those areas for the comparison.

Since the output files are a binary and ascii files, the evaluation software for CER10.1P2 does a diff on the one ascii file in out_exp and the file created during processing and a cmp on the binary files:

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_SNOW-PCT_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_SNOW-PCT_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_mhr-csalb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_mhr-csalb_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_csalb0-intrp2s_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_csalb0-intrp2s_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM1 CER10.1P2:

$CERESHOME/tisa_avg/bin/cleanup 10.1P2 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand Alone Test Procedures for Terra FM2

(NOTE:  CER10.1P2 has to be run before running the test procedure for CER 10.1P1 Terra.)

#### PCF Generator

The Main Processor production script, CER10.1P2, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_10.1P2_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P2_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_10.1P2_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires 2 command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_10.1P2_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_10.1P2_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM2.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P2-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P2_ascii_ssit_gen.csh  10 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P2_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P2_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P2_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P2_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER10.1P2, followed by one command-line argument:  PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P2  $year $month CER10.1P2_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER_10.1P2, will be executed and will create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic/:

CER_SNOW-PCT_$INSTANCE

CER_SNOW-PCT_$INSTANCE.met

CER_mhr-csalb_$INSTANCE

CER_mhr-csalb_$INSTANCE.met

CER_csalb0-intrp2s_$INSTANCE

CER_csalb0-intrp2s_$INSTANCE.met

#### Exit Codes

All CER10.1P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	2 minute and 33 seconds

Memory:	55040 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER10.1P2, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P2_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P2 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new output files from the execution are in $CERESHOME/tisa_avg/data/ancillary/dynamic.  These output files are accessed from those areas for the comparison.

Since the output files are a binary and ascii files, the evaluation software for CER10.1P2 does a diff on the one ascii file in out_exp and the file created during processing and a cmp on the binary files:

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_SNOW-PCT_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_SNOW-PCT_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_mhr-csalb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_mhr-csalb_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_csalb0-intrp2s_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_csalb0-intrp2s_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM2 CER10.1P2:

$CERESHOME/tisa_avg/bin/cleanup 10.1P2 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

## CER10.1P3 Main Processor

### Stand-alone Test Procedures for Terra FM1

#### PCF Generator and Execution

The Main Processor production script, CER10.1P3, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P3_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P3_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P3-env_ssit.csh and setup_test_env_Terra_FM1.csh.

For production runs, the ASCII file generator, tisavg_10.1P3_ascii_ssit_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P3_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P3_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM1.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P3-env_ssit.csh

setenv year 2003

setenv month 01

setenv DATADATE 200301

setenv INSTANCE Terra-FM1-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P3_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P3, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P3 $year $month CER10.1P3_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P3, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG-Daily1_$INSTANCE

CER_SRBAVG-Daily1_$INSTANCE.met

CER_SRBAVG-Daily2_$INSTANCE

CER_SRBAVG-Daily2_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE.met

CER_QC-ISCCP-D2-NITE_$INSTANCE

CER_QC-ISCCP-D2-NITE_$INSTANCE.met

#### Exit Codes

The processor CER10.1P3 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	13 minutes 15 seconds

Memory:	190160K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P3, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P3_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P3 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Terra.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P3

eval_ss10_output_Terra_FM1.csh $year $month

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM1 CER10.1P3:

$CERESHOME/tisa_avg/bin/cleanup 10.1P3 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Terra FM2

#### PCF Generator and Execution

The Main Processor production script, CER10.1P3, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P3_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P3_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P3-env_ssit.csh and setup_test_env_Terra_FM2.csh.

For production runs, the ASCII file generator, tisavg_10.1P3_ascii_ssit_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P3_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P3_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Terra_FM2.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P3-env_ssit.csh

setenv year 2003

setenv month 01

setenv DATADATE 200301

setenv INSTANCE Terra-FM2-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P3_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P3, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P3 $year $month CER10.1P3_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P3, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG-Daily1_$INSTANCE

CER_SRBAVG-Daily1_$INSTANCE.met

CER_SRBAVG-Daily2_$INSTANCE

CER_SRBAVG-Daily2_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE.met

CER_QC-ISCCP-D2-NITE_$INSTANCE

CER_QC-ISCCP-D2-NITE_$INSTANCE.met

#### Exit Codes

The processor CER10.1P3 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	13 minutes 15 seconds

Memory:	190160 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P3, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P3_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P3 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Terra_FM2.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P3

eval_ss10_output_Terra_FM2.csh $year $month

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Terra FM2 CER10.1P3:

$CERESHOME/tisa_avg/bin/cleanup 10.1P3 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Aqua FM3

#### PCF Generator and Execution

The Main Processor production script, CER10.1P3, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P3_ascii_gen-test.csh, and then executing the PCF generator, tisavg_10.1P3_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P3-env_ssit.csh and setup_test_env_Aqua_FM3.csh.

For production runs, the ASCII file generator, tisavg_10.1P3_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P3_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P3_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM3.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P3-env_ssit.csh

setenv year 2003

setenv month 01

setenv DATADATE 200301

setenv INSTANCE Aqua-FM3-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P3_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P3, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P3 $year $month CER10.1P3_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P3, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG-Daily1_$INSTANCE

CER_SRBAVG-Daily1_$INSTANCE.met

CER_SRBAVG-Daily2_$INSTANCE

CER_SRBAVG-Daily2_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE.met

CER_QC-ISCCP-D2-NITE_$INSTANCE

CER_QC-ISCCP-D2-NITE_$INSTANCE.met

#### Exit Codes

The processor CER10.1P3 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	13 minutes 15 seconds

Memory:	190160K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P3, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P3_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P3 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Aqua_FM3.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P3

eval_ss10_output_Aqua_FM3.csh $year $month

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM3 CER10.1P3:

$CERESHOME/tisa_avg/bin/cleanup 10.1P3 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Aqua FM4

#### PCF Generator

The Main Processor production script, CER10.1P3, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P3_ascii_gen-test.csh, and then executing the PCF generator, tisavg_10.1P3_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P3-env_ssit.csh and setup_test_env_Aqua_FM4.csh.

For production runs, the ASCII file generator, tisavg_10.1P3_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P3_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P3_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM4.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P3-env_ssit.csh

setenv year 2003

setenv month 01

setenv DATADATE 200301

setenv INSTANCE Aqua-FM4-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P3_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P3_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P3_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P3, followed by three command-line arguments:  year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P3 $year $month CER10.1P3_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P3, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG-Daily1_$INSTANCE

CER_SRBAVG-Daily1_$INSTANCE.met

CER_SRBAVG-Daily2_$INSTANCE

CER_SRBAVG-Daily2_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE

CER_SRBAVG-ISCCP-D2-like1_$INSTANCE.met

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE

CER_SRBAVG-ISCCP-D2-like2_$INSTANCE.met

CER_QC-ISCCP-D2-NITE_$INSTANCE

CER_QC-ISCCP-D2-NITE_$INSTANCE.met

#### Exit Codes

The processor CER10.1P3 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	13 minutes 15 seconds

Memory:	190160 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P3, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P3_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P3 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Aqua_FM4.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P3

eval_ss10_output_Aqua_FM4.csh $year $month

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM4 CER10.1P3:

$CERESHOME/tisa_avg/bin/cleanup 10.1P3 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

## CER10.1P4 Main Processor

### Stand-alone Test Procedures for Aqua FM3

(NOTE:  CER10.1P5 has to be run before running this test procedure for Aqua.)

#### PCF Generator

The Main Processor production script, CER10.1P4, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P4_ascii_gen-test.csh, and then executing the PCF generator, tisavg_10.1P4_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P4_env.csh and setup_test_env_Aqua_FM3.csh.

For production runs, the ASCII file generator, tisavg_10.1P4_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P4_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P4_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM3.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P4-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM3-MODIS_SSIT_999999.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P4_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P4_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P4_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P4_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P4_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P4, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P4 $year $month CER10.1P4_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P4, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG1_$INSTANCE

CER_SRBAVG1_$INSTANCE.met

CER_SRBAVG2_$INSTANCE

CER_SRBAVG2_$INSTANCE.met

CER_SRBAVG3_$INSTANCE

CER_SRBAVG3_$INSTANCE.met

CER_NQCRP_$INSTANCE

CER_NQCRP_$INSTANCE.met

CER_NRGRP_$INSTANCE

CER_NRGRP_$INSTANCE.met

CER_NVREG_$INSTANCE

CER_NVREG_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/web/tsplot:

SURF_TSP_$DATADATE\_4.pdf

TOA_TSP_$DATADATE\_4.pdf

Create the following files in $CERESHOME/tisa_avg/web/plot/gif/TAVG_$DATADATE\_4:

CALB_A_$DATADATE\_4.gif

CALB_B_$DATADATE\_4.gif

CALB_D_$DATADATE\_4.gif

CLDO_HIGH_$DATADATE\_4.gif

CLDO_LMID_$DATADATE\_4.gif

CLDO_LOW_$DATADATE\_4.gif

CLDO_UMID_$DATADATE\_4.gif

CLDP_HIGH_$DATADATE\_4.gif

CLDP_LMID_$DATADATE\_4.gif

CLDP_LOW_$DATADATE\_4.gif

CLDP_UMID_$DATADATE\_4.gif

CLW_A_$DATADATE\_4.gif

CLW_B_$DATADATE\_4.gif

CLW_D_$DATADATE\_4.gif

CNF_A_$DATADATE\_4.gif

CNF_B_$DATADATE\_4.gif

CNF_D_$DATADATE\_4.gif

CSDLW_A_$DATADATE\_4.gif

CSDLW_B_$DATADATE\_4.gif

CSDLW_D_$DATADATE\_4.gif

CSDSW_A_$DATADATE\_4.gif

CSDSW_B_$DATADATE\_4.gif

CSDSW_D_$DATADATE\_4.gif

CSDWN_A_$DATADATE\_4.gif

CSNLW_A_$DATADATE\_4.gif

CSNLW_B_$DATADATE\_4.gif

CSNLW_D_$DATADATE\_4.gif

CSNSW_A_$DATADATE\_4.gif

CSNSW_B_$DATADATE\_4.gif

CSNSW_D_$DATADATE\_4.gif

CSN_B_$DATADATE\_4.gif

CSW_A_$DATADATE\_4.gif

CSW_B_$DATADATE\_4.gif

CSW_D_$DATADATE\_4.gif

CWN_A_$DATADATE\_4.gif

CWN_B_$DATADATE\_4.gif

CWN_D_$DATADATE\_4.gif

TALB_A_$DATADATE\_4.gif

TALB_B_$DATADATE\_4.gif

TALB_D_$DATADATE\_4.gif

TLW_A_$DATADATE\_4.gif

TLW_B_$DATADATE\_4.gif

TLW_D_$DATADATE\_4.gif

TNF_A_$DATADATE\_4.gif

TNF_B_$DATADATE\_4.gif

TNF_D_$DATADATE\_4.gif

TSDLW_B_$DATADATE\_4.gif

TSDSW_A_$DATADATE\_4.gif

TSDSW_B_$DATADATE\_4.gif

TSDSW_D_$DATADATE\_4.gif

TSDWN_A_$DATADATE\_4.gif

TSNLW_A_$DATADATE\_4.gif

TSNLW_B_$DATADATE\_4.gif

TSNLW_D_$DATADATE\_4.gif

TSNSW_A_$DATADATE\_4.gif

TSNSW_B_$DATADATE\_4.gif

TSNSW_D_$DATADATE\_4.gif

TSN_B_$DATADATE\_4.gif

TSW_A_$DATADATE\_4.gif

TSW_B_$DATADATE\_4.gif

TSW_D_$DATADATE\_4.gif

TWN_A_$DATADATE\_4.gif

TWN_B_$DATADATE\_4.gif

TWN_D_$DATADATE\_4.gif

#### Exit Codes

The processor CER10.1P4 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	26 minutes 13 seconds

Memory:	193520 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P4, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P4_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P4 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Aqua_FM3.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P4

eval_ss10_output_Aqua_FM3.csh $year $month

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_xglb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_xglb_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM3 CER10.1P4:

$CERESHOME/tisa_avg/bin/cleanup 10.1P4 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand-alone Test Procedures for Aqua FM4

(NOTE:  CER10.1P5 has to be run before running this test procedure for Aqua.)

#### PCF Generator

The Main Processor production script, CER10.1P4, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF file for the test case is created by first executing an ASCII file generator, tisavg_10.1P4_ascii_gen-test.csh, and then executing the PCF generator, tisavg_10.1P4_pcfgen.csh.  The ASCII file generators source Subsystem 10.0-specific environment script ENV10.1P4_env.csh and setup_test_env_Aqua_FM4.csh.

For production runs, the ASCII file generator, tisavg_10.1P4_ascii_gen.csh, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires four command-line arguments:  2-digit subsystem number(10); 4-digit Data Year(1998); 2-digit Data Month(02); and 1-character GGEO data file exist flag(Y), (optional, default value = Y).  The PCF generator, tisavg_10.1P4_pcfgen.csh, then must be executed using the newly created ASCII input file name as a command-line argument.

NOTE:  The PCF generator script, tisavg_10.1P4_pcfgen.csh, uses the file PCF.template.  Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM4.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P4-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM4-MODIS_SSIT_999999.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P4_ascii_ssit_gen.csh 10 $year $month Y

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P4_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P4_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P4_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P4_PCF_$INSTANCE

#### Execution

Execute the production script by typing the script name, CER10.1P4, followed by three command-line arguments:   year (YYYY), month (MM), and PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P4 $year $month CER10.1P4_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P4, will be executed and will create the following files in $CERESHOME/tisa_avg/data/data_10/out_comp:

CER_SRBAVG1_$INSTANCE

CER_SRBAVG1_$INSTANCE.met

CER_SRBAVG2_$INSTANCE

CER_SRBAVG2_$INSTANCE.met

CER_SRBAVG3_$INSTANCE

CER_SRBAVG3_$INSTANCE.met

CER_NQCRP_$INSTANCE

CER_NQCRP_$INSTANCE.met

CER_NRGRP_$INSTANCE

CER_NRGRP_$INSTANCE.met

CER_NVREG_$INSTANCE

CER_NVREG_$INSTANCE.met

Create the following files in $CERESHOME/tisa_avg/web/tsplot:

SURF_TSP_$DATADATE\_5.pdf

TOA_TSP_$DATADATE\_5.pdf

Create the following files in $CERESHOME/tisa_avg/web/plot/gif/TAVG_$DATADATE\_5:

CALB_A_$DATADATE\_5.gif

CALB_B_$DATADATE\_5.gif

CALB_D_$DATADATE\_5.gif

CLDO_HIGH_$DATADATE\_5.gif

CLDO_LMID_$DATADATE\_5.gif

CLDO_LOW_$DATADATE\_5.gif

CLDO_UMID_$DATADATE\_5.gif

CLDP_HIGH_$DATADATE\_5.gif

CLDP_LMID_$DATADATE\_5.gif

CLDP_LOW_$DATADATE\_5.gif

CLDP_UMID_$DATADATE\_5.gif

CLW_A_$DATADATE\_5.gif

CLW_B_$DATADATE\_5.gif

CLW_D_$DATADATE\_5.gif

CNF_A_$DATADATE\_5.gif

CNF_B_$DATADATE\_5.gif

CNF_D_$DATADATE\_5.gif

CSDLW_A_$DATADATE\_5.gif

CSDLW_B_$DATADATE\_5.gif

CSDLW_D_$DATADATE\_5.gif

CSDSW_A_$DATADATE\_5.gif

CSDSW_B_$DATADATE\_5.gif

CSDSW_D_$DATADATE\_5.gif

CSDWN_A_$DATADATE\_5.gif

CSNLW_A_$DATADATE\_5.gif

CSNLW_B_$DATADATE\_5.gif

CSNLW_D_$DATADATE\_5.gif

CSNSW_A_$DATADATE\_5.gif

CSNSW_B_$DATADATE\_5.gif

CSNSW_D_$DATADATE\_5.gif

CSN_B_$DATADATE\_5.gif

CSW_A_$DATADATE\_5.gif

CSW_B_$DATADATE\_5.gif

CSW_D_$DATADATE\_5.gif

CWN_A_$DATADATE\_5.gif

CWN_B_$DATADATE\_5.gif

CWN_D_$DATADATE\_5.gif

TALB_A_$DATADATE\_5.gif

TALB_B_$DATADATE\_5.gif

TALB_D_$DATADATE\_5.gif

TLW_A_$DATADATE\_5.gif

TLW_B_$DATADATE\_5.gif

TLW_D_$DATADATE\_5.gif

TNF_A_$DATADATE\_5.gif

TNF_B_$DATADATE\_5.gif

TNF_D_$DATADATE\_5.gif

TSDLW_B_$DATADATE\_5.gif

TSDSW_A_$DATADATE\_5.gif

TSDSW_B_$DATADATE\_5.gif

TSDSW_D_$DATADATE\_5.gif

TSDWN_A_$DATADATE\_5.gif

TSNLW_A_$DATADATE\_5.gif

TSNLW_B_$DATADATE\_5.gif

TSNLW_D_$DATADATE\_5.gif

TSNSW_A_$DATADATE\_5.gif

TSNSW_B_$DATADATE\_5.gif

TSNSW_D_$DATADATE\_5.gif

TSN_B_$DATADATE\_5.gif

TSW_A_$DATADATE\_5.gif

TSW_B_$DATADATE\_5.gif

TSW_D_$DATADATE\_5.gif

TWN_A_$DATADATE\_5.gif

TWN_B_$DATADATE\_5.gif

TWN_D_$DATADATE\_5.gif

#### Exit Codes

The processor CER10.1P4 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  Failure is indicated by an exit code 202.

#### Main Processor Test Summary

Total Run Time:	26 minutes 13 seconds

Memory:	193520 K

Required Disk Space:	3.4 GB

### Evaluation Procedures

When running the production script, CER10.1P4, the system message, ‘No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P4_LogReport_$INSTANCE, is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P4 has been executed.  Metadata files are written to directory, $CERESHOME/tisa_avg/data/data_10/out_comp.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new input files from the execution are in $CERESHOME/tisa_avg/data/data_10/out_comp.  These input files are accessed from those areas for the comparison.

eval_ss10_output_Aqua_FM4.csh is a script needed to execute the comparison program.  Type the following:

cd $CERESHOME/tisa_avg/test_suites/CER10.1P4

eval_ss10_output_Aqua_FM4.csh $year $month

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_xglb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_xglb_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM4 CER10.1P4:

$CERESHOME/tisa_avg/bin/cleanup 10.1P4 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

## CER10.1P5 Main Processor

### Stand Alone Test Procedures for Aqua FM3

(NOTE:  CER10.1P5 has to be run before running the test procedure for  CER10.1P4 Aqua.)

#### PCF Generator

The Main Processor production script, CER10.1P5, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_10.1P5_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P5_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_10.1P5_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires 2 command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_10.1P5_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_10.1P5_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM3.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P5-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM3-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P5_ascii_ssit_gen.csh 10 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P5_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P5_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P5_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P5_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER10.1P5, followed by one command-line argument:  PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P5 $year $month CER10.1P5_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P5, will be executed and will create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic/:

CER_SNOW-PCT_$INSTANCE

CER_SNOW-PCT_$INSTANCE.met

CER_mhr-csalb_$INSTANCE

CER_mhr-csalb_$INSTANCE.met

CER_csalb0-intrp2s_$INSTANCE

CER_csalb0-intrp2s_$INSTANCE.met

#### Exit Codes

All CER10.1P5 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	2 minute and 33 seconds

Memory:	55040 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER10.1P5, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P5_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P5 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new output files from the execution are in $CERESHOME/tisa_avg/data/ancillary/dynamic.  These output files are accessed from those areas for the comparison.

Since the output files are a binary and ascii files, the evaluation software for CER10.1P5 does a diff on the one ascii file in out_exp and the file created during processing and a cmp on the binary files:

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_SNOW-PCT_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_SNOW-PCT_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_mhr-csalb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_mhr-csalb_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_csalb0-intrp2s_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_csalb0-intrp2s_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM3 CER10.1P5:

$CERESHOME/tisa_avg/bin/cleanup 10.1P5 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

### Stand Alone Test Procedures for Aqua FM4

(NOTE:  CER10.1P5 has to be run before running the test procedure for CER10.1P4 Aqua.)

#### PCF Generator

The Main Processor production script, CER10.1P5, references a Process Control File (PCF) which contain the correct file names and paths for the test procedures.  The PCF for the test case is created by first executing an ASCII file generator, tisavg_10.1P5_ascii_ssit_gen.csh, and then executing the PCF generator, tisavg_10.1P5_pcfgen.csh.

For production runs, the ASCII file generator, tisavg_10.1P5_ascii_gen, must be executed to create the ASCII input file for a particular production run.  The ASCII file generator requires 2 command line arguments, 4-digit Data Year, 2-digit Data Month.  The PCF generator, tisavg_10.1P5_pcfgen.csh, is then executed using the newly created ASCII input file name as a command line argument.

NOTE:  The PCF generator script, tisavg_10.1P5_pcfgen.csh, uses the file PCF.template. Therefore, PCF.template must exist in the same directory.

- Generate the ASCII input file for the test case:

cd $CERESHOME/tisa_avg/bin

source $CERESENV

source $CERESHOME/tisa_avg/bin/setup_test_env_Aqua_FM4.csh

source $CERESHOME/tisa_avg/bin/ENV10.1P5-env.csh

setenv year 2002

setenv month 07

setenv DATADATE 200207

setenv INSTANCE Aqua-FM4-MODIS_SSIT_000000.$DATADATE

$CERESHOME/tisa_avg/bin/tisavg_10.1P5_ascii_ssit_gen.csh 10 $year $month

The following file will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P5_PCFin_$INSTANCE

Generate the PCF for the test case:

$CERESHOME/tisa_avg/bin/tisavg_10.1P5_pcfgen.csh $CERESHOME/tisa_avg/rcf/CER10.1P5_PCFin_$INSTANCE

The following PCF will be generated in $CERESHOME/tisa_avg/rcf/:

CER10.1P5_PCF_$INSTANCE

#### Execution

The production script is executed by typing the script name, CER10.1P5, followed by one command-line argument:  PCF file name.

$CERESHOME/tisa_avg/bin/CER10.1P5 $year $month CER10.1P5_PCF_$INSTANCE

The Main Processor, Product Generation Executive (PGE) CER10.1P5, will be executed and will create the following files in $CERESHOME/tisa_avg/data/ancillary/dynamic/:

CER_SNOW-PCT_$INSTANCE

CER_SNOW-PCT_$INSTANCE.met

CER_mhr-csalb_$INSTANCE

CER_mhr-csalb_$INSTANCE.met

CER_csalb0-intrp2s_$INSTANCE

CER_csalb0-intrp2s_$INSTANCE.met

#### Exit Codes

All CER10.1P5 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completions indicated by an exit code of 0.

#### Main Processor Test Summary

Total Run Time:	2 minute and 33 seconds

Memory:	55040 K

Required Disk Space:	19.08 GB

### Evaluation Procedures

When running the production script, CER10.1P5, the system message, ‘No match’, may be written to the screen. This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log File, CER10.1P5_LogReport_$INSTANCE is located in directory $CERESHOME/tisa_avg/data/data_10/runlogs.

#### Metadata

Metadata files which end in extension,’.met’, are located in the same directory as their corresponding output files after CER10.1P5 has been executed.

#### Execution of Comparison Software

The delivered input files are in $CERESHOME/tisa_avg/data/data_10/out_exp and new output files from the execution are in $CERESHOME/tisa_avg/data/ancillary/dynamic.  These output files are accessed from those areas for the comparison.

Since the output files are a binary and ascii files, the evaluation software for CER10.1P5 does a diff on the one ascii file in out_exp and the file created during processing and a cmp on the binary files:

cmp $CERESHOME/tisa_avg/data/data_10/out_exp/CER_SNOW-PCT_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_SNOW-PCT_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_mhr-csalb_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_mhr-csalb_$INSTANCE

and

diff $CERESHOME/tisa_avg/data/data_10/out_exp/CER_csalb0-intrp2s_$INSTANCE $CERESHOME/tisa_avg/data/ancillary/dynamic/CER_csalb0-intrp2s_$INSTANCE

### Solutions to Possible Problems

- All output files are opened with status=NEW.  These files must be removed before running test procedures.  A script which removes PGE-created files, cleanup, is located in directory $CERESHOME/tisa_avg/bin.  To clean up the files for Aqua FM4 CER10.1P5:

$CERESHOME/tisa_avg/bin/cleanup 10.1P5 $year$month

Environment variable F90 must be set to the 64-bit SGI F90 compiler.

Acronyms and Abbreviations

ADM	Angular Distribution Models

ASCII	American Standard Code Information Interchange

ASDC	Atmospheric Sciences Data Center

AVG	Monthly Regional Radiative Fluxes and Clouds

CERES	Clouds and the Earth’s Radiant Energy System

CERESLib	CERES Library

DAAC	Distributed Active Archive Center

ECS	EOSDIS Core System

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOSDIS	EOS Data Information System

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FSW	Gridded Single Satellite Fluxes and Clouds and Compute Spatial Averages

GB	Gigabytes

F90	Fortran 90

FOV 	Field-of-View

GGEO	Geostationary data file

GMT	Greenwich mean time

HDF	Hierarchical Data Format

HDF-EOS	Hierarchical Data Format - Earth Observing System

KB	Kilobytes

LaRC	Langley Research Center

LaTIS	Langley TRMM Information System

LW	Longwave

MB	Megabytes

MCF	Metadata Control Files

met	metadata file

MM	Two digit month

MOA	Meteorological, Ozone, and Aerosol

N/A	Not Applicable

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executive

PMOA	Post Meteorological, Ozone, and Aerosol

PSF	Point Spread Function

QC	Quality Control

SARB	Surface and Atmospheric Radiation Budget

SDP	Science Data Production

SFC	Hourly Gridded Single Satellite TOA and Surface Fluxes and Clouds

SMF	Status Message File

SRBAVG	Monthly TOA and SRB Averages

SRD	Software Requirements Document

SSAI	Science Systems and Applications, Inc.

SW	Shortwave

SYN	Synoptic Radiative Fluxes and Clouds

TISA	Time Interpolation and Spatial Averaging

TOA	Top-of-the-Atmosphere

TRMM	Tropical Rainfall Measuring Mission

TSI	Time Space Interpolate

UT	Universal Time

Directory Structure Diagrams

Figure B-1.  Directory Structure for the TISA Averaging (tisa_avg) Tar File

Figure B-1.  Directory Structure for the TISA Averaging (tisa_avg) Tar File

Figure B-1.  Directory Structure for the TISA Averaging (tisa_avg) Tar File

File Description Tables

Production Script

The following scripts must be moved to the production environment.

Table C.1-1.  Production Scripts @ ($CERESHOME/tisa_avg/bin)

| File Name | Format | Description |
| --- | --- | --- |
| tisavg_ascii_gen.csh | ASCII | C-Shell script which creates the PCF generator’s ASCII file needed Main Processor PCF file generator script |
| tisavg_ascii_gen_test.csh | ASCII | C-Shell script which creates the PCF generator’s ASCII file needed Main Processor PCF file generator script. Not a production script. |
| tisavg_pcfgen.csh | ASCII | C-Shell script which creates the PCF file for the main processor. |
| setupenv.csh | ASCII | C-Shell script which sets the sampling strategy, production strategy, configuration code, SCCR environment variables. |
| ENV10.1P1-env.csh | ASCII | C-Shell script which sets the sampling strategy and production strategy for SS10. |
| CER10.1P1 | ASCII | C-Shell Script which executes the SS10 Main Processor |

Executables

Table C.2-1.  Executables

| File Name | Format | Description |
| --- | --- | --- |
| tisa_710.exe1 | Binary | Main Processor executable |
| webplot.exe1 | Binary | Executable to create data files for web plots |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Status Message Files

Table C.3-1.  Status Message Files @ ($CERESHOME/tisa_avg/smf)

| File Name | Format | Description |
| --- | --- | --- |
| TISAVG_26300.t | ASCII | Status Message File for Subsystem 10.0 |

Ancillary Input Data

Table C.4-1.  Ancillary Input Data @ ($CERESHOME/tisa_avg/data/ancillary/static)

| File Name | Format | Description |
| --- | --- | --- |
| CERES_DIR_MODEL.19971212 | Binary | Directional Models, TOA |
| Refl_Coef.19971107 | ASCII | Directional Models, Surface |
| NIISW03.19971101 | Binary | SW Angular Distribution Models (ADM) |
| NIILWAT.19971101 | Binary | LW ERBE ADM for Sep., Oct., Nov. |
| NIILWSP.19971101 | Binary | LW ERBE ADM for Mar., Apr., May |
| NIILWSM.19971101 | Binary | LW ERBE ADM for Jun., Jul., Aug. |
| NIILWWN.19971101 | Binary | LW ERBE ADM for Dec., Jan., Feb |
| georc.19971212 | Binary | Coefficient file. |
| CER_GGEO_CERES_Composite_007002.199801 | Binary | GGEO product produced by Subsystem 11. |
| range_values.19980204 | ASCII | Contains valid range values for all TISA Averaging data product parameters |
| valid_regions.19980316 | ASCII | Contains the validation region numbers. |

Processing Control Files (PCF), Metadata Control Files (MCF)

Table C.5-1.  Process Control Files (PCF) @ (CERESHOME/tisa_avg/rcf)

| File Name. | Format | Description |
| --- | --- | --- |
| CER10.1P1_PCFin_TRMM-PFM-VIRS-ValidationR2_000000.1998011 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER10.1P1_PCF_TRMM-PFM-VIRS-ValidationR2_000000.1998011 | ASCII | Process control file for ss10 Main Processor |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Table C.5-2.  Metadata Control Files (MCF) for Subsystem 10.0 @ ($CERESHOME/tisa_avg/rcf)

| File Name | Format | Description |
| --- | --- | --- |
| SRBAVGB.MCF | ASCII | MCF for binary SRBAVG (SS10) Main Processor |
| SRBAVG1.MCF | ASCII | MCF for HDF-EOS SRBAVG1 (SS10) Main Processor |
| SRBAVG2.MCF | ASCII | MCF for HDF-EOS SRBAVG2 (SS10) Main Processor |
| NQCRP.MCF | ASCII | MCF for QC Report for SS10 |
| NVREG.MCF | ASCII | MCF for SS10 Validation File |

# Text boxes

test_10

test_8

test_7

include8

include7_10

web*

smf

rcf

test_suites

data*

bin

plot

diff

TAVG*

map

font

color

src

gif

csh

dat

anc

tsplot

plot

web

Breakdown of the tisa_avg/web Directory

bin

src

tisa_avg

CERES

* Breakdown of subdirectories shown on following pages.

Directory Structure for the TISA Averaging Tar File

* PMOA files are included in this delivery.

*

PMOA

test_input

runlogs

out_exp

out_comp

input

static

dynamic

scr

data_7

data_8

data_10

data

ancillary

Breakdown of the tisa_avg/data Directory