Intelligent Transportation Systems (ITS)

Commercial Vehicle Operations (CVO)

Commercial Vehicle Information Systems and
Networks (CVISN) Architecture

POR-02-7364 V2.0

March 2004

Prepared for:

US Department of Transportation

Federal Motor Carrier Safety Administration

400 Seventh Street, SW

Washington, DC  20590

Prepared by:

The Johns Hopkins University

Applied Physics Laboratory

11100 Johns Hopkins Road

Laurel, MD  20723-6099

The Motor Carrier Safety Improvement Act was signed into law on December 9, 1999.  This act established a new Federal Motor Carrier Safety Administration (FMCSA) within the US Department of Transportation (DOT), effective January 1, 2000.  Prior to that, the motor carrier and highway safety program was administered under the Federal Highway Administration (FHWA).

The mission of the FMCSA is to improve truck and commercial passenger carrier safety on our nation’s highways through information technology, targeted enforcement, research and technology, outreach, and partnerships. The FMCSA manages the Intelligent Transportation Systems (ITS)/Commercial Vehicle Operations (CVO) Program, a voluntary effort involving public and private partnerships that uses information systems, innovative technologies, and business practice reengineering to improve safety, simplify government administrative systems, and provide savings to states and motor carriers. The FMCSA works closely with the FHWA’s ITS Joint Program Office (JPO) to ensure the integration and interoperability of ITS/CVO systems with the national ITS program.

As part of the CVISN program, FMCSA defined an initial set of capabilities that could be deployed incrementally by a state and its motor carriers.  The capabilities focus on electronically exchanging safety and credentialing information, electronically processing interstate registration and fuel tax credentials, and implementing roadside electronic screening at one fixed or mobile site.  These capabilities were originally referred to as “CVISN Level 1” capabilities, but are now called “Core” CVISN capabilities.

This is Version 2 of a Baseline Issue

This document has completed internal and external reviews of previously published draft versions.  All comments received to date have been incorporated or addressed.

This document is disseminated in the interest of information exchange.  The Johns Hopkins University Applied Physics Laboratory (JHU/APL) assumes no liability for its contents or use thereof.  This report does not constitute a standard, specification, or regulation.  JHU/APL does not endorse products or manufacturers.  Trade and manufacturer’s names appear in this report only because they are considered essential to the object of this document.

Note:  This document and other CVISN-related documentation are available for review and downloading by the ITS/CVO community from the JHU/APL CVISN site on the World Wide Web. The URL for the CVISN site is: http://www.jhuapl.edu/cvisn/.

Review and comments to this document are welcome.  Please send comments to:

Ms. Valerie Barnes

JHU/APL

Phone:	717-261-0635

Fax:	717-261-0635

E-Mail:	Valerie.Barnes@jhuapl.edu

CVISN Architecture

Table of Contents

1.	CVISN ARCHITECTURE	1–1

1.1.	Background	1–1

1.2.	Scope	1–1

1.3.	Maintaining the CVISN Architecture	1–1

2.	CVISN ARCHITECTURE	2–1

2.1.	Architecture Conventions	2–1

2.2.	Architecture Flow Diagram	2–2

2.3.	Tables	2–5

3.	CHANGE REQUESTS	3–1

3.1.	Change Requests Incorporated	3–1

3.2.	Change Requests Pending	3–2

4.	REFERENCES	4–1

This Page Intentionally Blank

# CVISN ARCHITECTURE

## Background

This document establishes a new baseline for the CVISN Architecture.  The CVISN Architecture baseline was aligned with the National Intelligent Transportation Systems (ITS) and International Border Clearance (IBC) Architectures in 2001-2002 [References 1 – 3].  This version of the CVISN Architecture has been updated to align with Version 5.0 of the National ITS Architecture [Reference 4].  The CVISN Architecture uses terminology and components that the National ITS Architecture uses.

## Scope

CVISN represents a subset of the National ITS Architecture <http://www.iteris.com/itsarch/> [Reference 4].  CVISN comprises the information systems and networks that support commercial vehicle operations.

A diagram that depicts subsystems, equipment packages, architecture flows, and terminators represents the CVISN Architecture [Figure 2–1].  Tables in this document provide additional information about each item shown on the diagram.  The architecture reflects the vision for CVISN over the next few years.

## Maintaining the CVISN Architecture

The CVISN Architecture is under configuration management.  There is a three-tier process for proposing a change to the architecture.  First, the proposed change will be presented to and reviewed by the CVISN Architecture Configuration Control Board (ACCB).  The ACCB is made up of FMCSA and state representatives, and is staffed by JHU/APL.  Change Requests (CR) are reviewed in regular (monthly) meetings.  Once the ACCB has reached consensus about a proposed change that may also impact the National ITS Architecture, the CR recommended for approval will be discussed with the National ITS Architecture team.  If the National ITS Architecture team concurs, in the final stage of the process, the proposed change will be presented to FMCSA for consideration.  If FMCSA approves the proposed change, it will be implemented in CVISN.  At the next release, it will be implemented in the National ITS Architecture.

If a new user service requires that CVO-related functions be added to the National ITS Architecture, then existing components may need to be changed or other components added.  The CVISN Architecture team will work with the National ITS Architecture team to develop the proposed changes to the architecture, and then go through the CR process with the CVISN ACCB.

Chapter 3 explains the change requests that are incorporated in this version of the CVISN Architecture.  In Chapter 2, impacted rows are flagged with the change request number (CR #).

This Page Intentionally Blank

# CVISN ARCHITECTURE

The CVISN Architecture reflects alignment with the National ITS Architecture using these ground rules:

The elements of the physical architecture (subsystems, terminators and architecture flows) are aligned.  The logical architectures were not aligned as part of this process.

The scope is limited to CVISN Level 1 functions plus toll, international border crossing, other safety functions, and Commercial Vehicle Operations (CVO) security.  This particular version of the CVISN Architecture document reflects the alignment with Version 5.0 of the National ITS Architecture.  Major changes were made to include security functions.

Human terminators, except the Commercial Vehicle (CV) Driver, are not part of the alignment.

## Architecture Conventions

The CVISN Architecture follows these conventions for naming, styles, etc.:

- The National ITS Architecture naming conventions are used by CVISN for aligned architecture flows: flow names are lower case except for acronyms.

- The National ITS Architecture definitions for aligned subsystems, equipment packages, terminators, and architecture flows are used by CVISN.

- For the alignment process, basic vehicle (Vehicle Subsystem) functions were incorporated into the CV realm.  The CVISN Architecture aggregates the National ITS Architecture’s Commercial Vehicle and Vehicle Subsystems into a single subsystem named CVSAg.  In this document we indicate which data are related to the Vehicle Subsystem by labeling the aggregated subsystem as CVSAg (VS).  If a flow is related to the Commercial Vehicle Subsystem, the aggregated subsystem is labeled CVSAg (CVS).

- Architecture flows are characterized as to whether or not there are applicable standards.  The four line types used on the flow diagram are as follows:

  - Wireline (Fixed Point Communications) – shown as a solid line

  - Dedicated Short Range Communication (DSRC) – shown as a long dashed line

  - Wide Area Wireless – shown as a long-short-long dashed line

  - Other Transactions – shown as a dotted line

With the exception of (d), the architecture flow types used by CVISN match those defined by the National ITS Architecture.  These are designated as “architecture interconnects” by the National ITS Architecture.

- Some architecture flows between humans and subsystems remain in the National ITS Architecture but are not shown in the CVISN Architecture; the human operator is considered to be part of the subsystem in CVISN.  The one exception is the Commercial Vehicle Driver.

## Architecture Flow Diagram

Figure 2–1 is the CVISN Architecture Flow Diagram.  The CVISN Architecture Flow Diagram depicts the CVO data flow among subsystems and between CVO subsystems and external entities.  The subsystems and equipment packages shown relate to the processes defined in the National ITS Architecture’s Physical Architecture.  The shaded equipment packages are not part of CVISN Level 1.  In this version of this document, descriptions for all equipment packages shown on the diagram were added as a new table, Table 4.

Entities external to the ITS information systems are shown in ovals.  In National Architecture terminology, these are “terminators.”

Connections and data exchanges shown on the figures are marked with different line types to differentiate the means of communication used.  The definitions provided below are from the National ITS Architecture [Reference 4].

Wireline (Fixed Point Communications):  A communication link serving stationary entities. It may be implemented using a variety of public or private communication networks and technologies.  It can include, but is not limited to, twisted pair, coaxial cable, fiber optic, microwave relay networks, spread spectrum, etc.  In Fixed-Point to Fixed-Point (FP2FP) communication the important issue is that it serves stationary entities.  Both dedicated and shared communication resources may be used.

DSRC:  A wireless communications channel used for close-proximity communications between vehicles and the immediate infrastructure.  It supports location-specific communications for ITS capabilities such as toll collection, transit vehicle management, driver information, and automated commercial vehicle operations.

Wide Area Wireless:  A communications link that provides communications via a wireless device between a user and an infrastructure-based system. Both broadcast (one-way) and interactive (two-way) communications services are grouped into wide-area wireless communications in the National ITS Architecture. These links support a range of services in the National ITS Architecture including real-time traveler information and various forms of fleet communications.

Other Transactions:  Any of the following National ITS Architecture’s architecture interconnects – Physical Interface, Human, Internal Vehicle Interface, Contact or Proximity Interface, or Position Location Interface.

Symbols for the Emergency Management Subsystem and the Freight Equipment terminator contain the text string “(2)”, indicating that each symbol appears twice on the diagram.  This was done to maintain a semblance of readability and has nothing to do with functionality.

Replace this page with 11x17 foldout

Figure 2–1.  CVISN Architecture Flow Diagram

Replace this page with 11x17 foldout

## Tables

In the discussion of the tables, a “flow” is comprised of the source, destination and architecture flow name.  “Flow name” is a label for a set of data elements.  A list of the acronyms and abbreviations used in the tables is given just prior to Table 1.

The tables provided are:

Table 1.  CVISN Architecture Flows

Table 2.  CVISN Architecture Flow Names and Descriptions

Table 3.  Subsystem and Terminator Descriptions

Table 4.  Equipment Package Descriptions

ACRONYMS AND ABBREVIATIONS:

AAS:	Alerting and Advisory Systems

ADMS:	Archived Data Management Subsystem

BCV:	Basic Commercial Vehicle

CV:	Commercial Vehicle

CVAS:	Commercial Vehicle Administration Subsystem

CVCS:	Commercial Vehicle Check Subsystem

CV Driver:	Commercial Vehicle Driver

CVOIR:	Commercial Vehicle Operations Information Requestor

CVS:	Commercial Vehicle Subsystem

CVSAg:	Commercial Vehicle Subsystem Aggregated with the Vehicle Subsystem (this term is used only by CVISN)

CVSAg (CVS): 	Associated with the CVS part of CVSAg

CVSAg (VS): 	Associated with the VS part of CVSAg

EA:	(Law) Enforcement Agency

EM: 	Emergency Management Subsystem

EVS:	Emergency Vehicle Subsystem

FE:	Freight Equipment

FI:	Financial Institution

FMS:	Fleet and Freight Management Subsystem

IFD:	Intermodal Freight Depot

IFS:	Intermodal Freight Shipper

ISP:	Information Service Provider Subsystem

LDS:	Location Data Source

MCMS:	Maintenance and Construction Management Subsystem

MUP:	Map Update Provider

PMS:	Parking Management Subsystem

RS:	Roadway Subsystem

TAS:	Toll Administration Subsystem

TC:	Traveler Card

TCS:	Toll Collection Subsystem

TRA:	Trade Regulatory Agencies

VS:	Vehicle Subsystem

Table 1 presents a detailed look at each architecture flow contained in the CVISN Architecture Flow Diagram [Figure 2–1].

This table is ordered alphabetically by source and destination.  An “X” in the Std. column indicates that there are standards that apply to the architecture flow; refer to Version 5.0 of the National ITS Architecture for the applicable standards [Reference 4].  In Version 5.0 of the National ITS Architecture, many architecture flows are identified as candidates for future standardization; those are marked as “future” in the Std. column and CR 2390 applies.  The CR # column indicates any other applicable Change Requests for the flow.  If CR 2390 is listed, then the architecture flow was added via that change request.

Table 1.  CVISN Architecture Flows

| CVISN Architecture Flows |
| --- |
| Source | Destination | Flow Name | Std. | CR # |
| AAS | FMS | alerts and advisories | future | CR 2390 |
| ADMS | CVAS | archive requests | future |  |
| ADMS | CVAS | archive status | future |  |
| BCV | CVCS | CVO weight and presence |  |  |
| BCV | CVCS | identification information |  |  |
| BCV | CVSAg (CVS) | commercial vehicle measures | future |  |
| CVAS | ADMS | commercial vehicle archive data | X |  |
| CVAS | CVCS | border agency clearance results | future |  |
| CVAS | CVCS | credentials information | X |  |
| CVAS | CVCS | credentials status information | X |  |
| CVAS | CVCS | transportation border clearance assessment | future |  |
| CVAS | CVCS | trip declaration identifiers | future |  |
| CVAS | CVCS | safety inspection report | X |  |
| CVAS | CVCS | safety status information | X |  |
| CVAS | CVOIR | credentials information | X |  |
| CVAS | CVOIR | credentials status information | X |  |
| CVAS | CVOIR | safety status information | X |  |
| CVAS | EA | accident report | future |  |
| CVAS | EA | citation | future |  |
| CVAS | EA | violation notification | future |  |
| CVAS | FI | payment request |  |  |
| CVAS | FMS | accident report | future |  |
| CVAS | FMS | border clearance status | future |  |
| CVAS | FMS | citation | future |  |
| CVAS | FMS | compliance review report | future |  |
| CVAS | FMS | credentials information | X |  |
| CVAS | FMS | credentials status information | X |  |
| CVAS | FMS | route restrictions | future | CR 2390 |
| CVAS | FMS | safety inspection report | X |  |
| CVAS | FMS | safety status information | X |  |
| CVAS | IFS | border clearance status | future |  |
| CVAS | ISP | route restrictions | future | CR 2390 |
| CVAS | MUP | route restrictions | future | CR 2390 |
| CVAS | Other CVAS | border clearance status | future |  |
| CVAS | Other CVAS | credential fee coordination | future |  |
| CVAS | Other CVAS | credentials information | X |  |
| CVAS | Other CVAS | credentials status information | X |  |
| CVAS | Other CVAS | route restrictions | future | CR 2390 |
| CVAS | Other CVAS | safety inspection report | X |  |
| CVAS | Other CVAS | safety status information | X |  |
| CVAS | TRA | border clearance status | future |  |
| CVAS | TRA | domestic transportation information | future |  |
| CVAS | TRA | transportation border clearance assessment | future |  |
| CVCS | CVAS | accident report | future |  |
| CVCS | CVAS | citation | future |  |
| CVCS | CVAS | daily site activity data | future |  |
| CVCS | CVAS | border clearance event | future |  |
| CVCS | CVAS | safety inspection report | X |  |
| CVCS | CVAS | violation notification | future |  |
| CVCS | CV Driver | CVO pass/pull-in message |  |  |
| CVCS | CVSAg (CVS) | border clearance data request | X |  |
| CVCS | CVSAg (CVS) | border clearance event | X |  |
| CVCS | CVSAg (CVS) | driver log request | future |  |
| CVCS | CVSAg (CVS) | electronic lock data request | X |  |
| CVCS | CVSAg (CVS) | electronic screening request | X |  |
| CVCS | CVSAg (CVS) | on-board safety request | X |  |
| CVCS | CVSAg (CVS) | pass/pull-in | X |  |
| CVCS | CVSAg (CVS) | request tag data | future |  |
| CVCS | CVSAg (CVS) | safety inspection record | future |  |
| CVCS | CVSAg (CVS) | safety inspection request | future |  |
| CVCS | CVSAg (CVS) | screening event record | X |  |
| CVCS | EM | alarm | future | CR 2390 |
| CV Driver | CVSAg (CVS) | alert response |  | CR 2390 |
| CV Driver | CVSAg (CVS) | CVO driver initialization |  |  |
| CV Driver | CVSAg (CVS) | driver identity characteristics |  | CR 2390 |
| CV Driver | CVSAg (CVS) | trip identification number |  |  |
| CVSAg (CVS) | BCV | safe vehicle disable | future | CR 2390 |
| CVSAg (CVS) | CVCS | border clearance data | X |  |
| CVSAg (CVS) | CVCS | commercial vehicle breach | future | CR 2390 |
| CVSAg (CVS) | CVCS | driver log | future |  |
| CVSAg (CVS) | CVCS | electronic lock data | X |  |
| CVSAg (CVS) | CVCS | on-board safety data | X |  |
| CVSAg (CVS) | CVCS | safety inspection record | future |  |
| CVSAg (CVS) | CVCS | screening event record | X |  |
| CVSAg (CVS) | CVCS | tag data | future |  |
| CVSAg (CVS) | CV Driver | alerts |  |  |
| CVSAg (CVS) | CV Driver | CVO pass/pull-in message |  |  |
| CVSAg (CVS) | CV Driver | trip log information |  |  |
| CVSAg (CVS) | EM | hazmat spill notification | future |  |
| CVSAg (CVS) | FMS | commercial vehicle breach | future | CR 2390 |
| CVSAg (CVS) | FMS | driver alert response | future | CR 2390 |
| CVSAg (CVS) | FMS | driver to fleet request | future |  |
| CVSAg (CVS) | FMS | freight equipment information | future | CR 2390 |
| CVSAg (CVS) | FMS | identities | future | CR 2390 |
| CVSAg (CVS) | FMS | on-board safety data | X | CR 439 |
| CVSAg (CVS) | FMS | on-board vehicle data | future | CR 439 |
| CVSAg (CVS) | FMS | route deviation alert | future | CR 2390 |
| CVSAg (CVS) | FMS | trip log | future | CR 439 |
| CVSAg (VS) | EM | emergency notification | X |  |
| CVSAg (VS) | EVS | vehicle location |  | CR 2390 |
| CVSAg (VS) | ISP | vehicle probe data | future |  |
| CVSAg (VS) | PMS | tag data | X |  |
| CVSAg (VS) | RS | vehicle probe data | X |  |
| CVSAg (VS) | TC | request for payment |  |  |
| CVSAg (VS) | TCS | tag data | X |  |
| EA | CVAS | information on violators | future |  |
| EA | CVCS | information on violators | future |  |
| EM | CVSAg (VS) | emergency acknowledge | X |  |
| EM | CVSAg (VS) | emergency data request | X |  |
| EM | FMS | disable commercial vehicle | future | CR 2390 |
| EM | FMS | hazmat information request | X |  |
| FE | CVCS | freight breach | future | CR 2390 |
| FE | CVCS | freight equipment information | future | CR 2390 |
| FE | CVCS | hazmat environmental factors |  | CR 2390 |
| FE | CVSAg (CVS) | freight breach | future | CR 2390 |
| FE | CVSAg (CVS) | freight equipment information | future | CR 2390 |
| FE | FMS | freight breach | future | CR 2390 |
| FE | FMS | freight equipment information | future | CR 2390 |
| FI | CVAS | transaction status |  |  |
| FI | ISP | transaction status |  |  |
| FI | PMS | transaction status |  |  |
| FI | TAS | transaction status |  |  |
| FMS | AAS | fleet and freight threat information | future | CR 2390 |
| FMS | CVAS | audit data | future |  |
| FMS | CVAS | credential application | X |  |
| FMS | CVAS | tax filing | X | CR 654 |
| FMS | CVSAg (CVS) | commercial vehicle disable | future | CR 2390 |
| FMS | CVSAg (CVS) | expected driver identity characteristics | future | CR 2390 |
| FMS | CVSAg (CVS) | fleet to driver update | future |  |
| FMS | CVSAg (CVS) | on-board safety request | X | CR 439 |
| FMS | CVSAg (CVS) | on-board vehicle request | future | CR 439 |
| FMS | CVSAg (CVS) | trip identification number | future | CR 439 |
| FMS | CVSAg (CVS) | trip log request | future | CR 439 |
| FMS | EM | alarm | future | CR 2390 |
| FMS | EM | hazmat information | X |  |
| FMS | FE | freight monitoring parameters | future | CR 2390 |
| FMS | IFD | booking status | future | CR 2390 |
| FMS | IFD | intermod CVO coord | future |  |
| FMS | IFS | booking status | future | CR 2390 |
| FMS | IFS | freight breach | future | CR 2390 |
| FMS | IFS | intermod CVO coord | future |  |
| FMS | ISP | route request | X |  |
| FMS | ISP | toll data request | future |  |
| FMS | MUP | map update request |  | CR 2390 |
| FMS | TAS | toll data request | future |  |
| IFD | FMS | intermod CVO coord | future |  |
| IFS | CVSAg (CVS) | trip identification number | future |  |
| IFS | FMS | breach response | future | CR 2390 |
| IFS | FMS | freight transport booking | future | CR 2390 |
| IFS | FMS | intermod CVO coord | future |  |
| ISP | FI | payment request |  |  |
| ISP | FMS | road network conditions | X |  |
| ISP | FMS | route plan | X |  |
| ISP | FMS | toll data | future |  |
| ISP | TAS | toll data request | future |  |
| LDS | CVSAg (VS) | position fix |  |  |
| MCMS | CVAS | current asset restrictions | future |  |
| MUP | FMS | map updates |  | CR 2390 |
| Other CVAS | CVAS | border clearance status | future |  |
| Other CVAS | CVAS | credential fee coordination | future |  |
| Other CVAS | CVAS | credentials information | X |  |
| Other CVAS | CVAS | credentials status information | X |  |
| Other CVAS | CVAS | route restrictions | future | CR 2390 |
| Other CVAS | CVAS | safety inspection report | X |  |
| Other CVAS | CVAS | safety status information | X |  |
| PMS | CVSAg (VS) | request tag data | X |  |
| PMS | CVSAg (VS) | tag update | X |  |
| PMS | FI | payment request |  |  |
| RS | CVSAg (VS) | request tag data | X |  |
| RS | CVSAg (VS) | vehicle signage data | X |  |
| TAS | FI | payment request |  |  |
| TAS | FMS | toll data | future |  |
| TAS | ISP | toll data | future |  |
| TC | CVSAg (VS) | payment |  |  |
| TCS | CVSAg (VS) | request tag data | X |  |
| TCS | CVSAg (VS) | tag update | X |  |
| TRA | CVAS | declaration information | future |  |
| TRA | CVAS | domestic transportation information | future |  |

Table 2 defines the architecture flow names.  Unless otherwise indicated, all flow definitions are from the National ITS Architecture Version 5.0 [Reference 4].

Table 2.  CVISN Architecture Flow Names and Descriptions

| CVISN Architecture Flow Names and Descriptions |
| --- |
| Flow Name | Flow Description | CR # |
| accident report | Report of commercial vehicle safety accident. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. |  |
| alarm | Information about a Commercial Vehicle or Freight Equipment breach, non-permitted security sensitive hazmat detected at the roadside, route deviation, or Commercial Vehicle Driver / Commercial Vehicle / Freight Equipment assignment mismatches which includes the location of the Commercial Vehicle and appropriate identities. | CR 2390 |
| alert response | This flow represents the tactile or auditory interface with ITS equipment containing the response by a Commercial Vehicle Driver or Fleet-Freight Manager that confirms or cancels an alert. | CR 2390 |
| alerts | This flow represents the visual or auditory interface with ITS equipment containing specific alerts and messages related to commercial vehicles (e.g. trucks not advised, trucks over 10 tons not allowed on bridge, route details). This also includes detected route deviations and warning indications detected by on-board sensors (e.g., safety) and freight equipment sensors (e.g., breach, cargo). | CR 2390 |
| alerts and advisories | Assessments (general incident and vulnerability awareness information), advisories (identification of threats or recommendations to increase preparedness levels), and alerts (information on imminent or in-progress emergencies). This flow also provides supporting descriptive detail on incidents, threats, and vulnerabilities to increase preparedness and support effective response to threats against the surface transportation system. | CR 2390 |
| archive requests | A request to a data source for information on available data (i.e., "catalog") or a request that defines the data to be archived. The request can be a general subscription intended to initiate a continuous or regular data stream or a specific request intended to initiate a one-time response from the recipient. |  |
| archive status | Notification that data provided to an archive contains erroneous, missing, or suspicious data or verification that the data provided appears valid. If an error has been detected, the offending data and the nature of the potential problem are identified. |  |
| audit data | Information to support a tax audit. |  |
| booking status | Status of the freight transport booking that includes the identities of the Commercial Vehicle and driver who will pick-up the freight or a request for more information from the originator. | CR 2390 |
| border agency clearance results | Notification regarding the granting of permission for commercial freight shipment to enter the U.S. |  |
| border clearance data | Trip specific data regarding the movement of goods across international borders. Includes trip identification number. May also include results from recent border crossing screening events. |  |
| border clearance data request | Request for trip specific data regarding the movement of goods across international borders. Includes trip identification number. May also include results from recent border crossing screening events. |  |
| border clearance event | Reports clearance event data regarding action taken at border, including acceptance or override of system decision, and date/time stamp. |  |
| border clearance status | Notification regarding the crossing status of commercial freight shipment scheduled to enter the U.S. Includes portions of border agency and transportation agency clearance results, as they become available. Recipients may include trade regulatory agencies that do not receive status information directly from U.S. Customs (e.g., other transportation agencies with trade related responsibilities, such as NHTSA, MARAD, etc.). |  |
| breach response | This is an Intermodal Freight Shipper's response to a breach or tamper event of their freight equipment. There may be instructions for handling of the shipment, possible re-routing or pickup. | CR 2390 |
| citation | Report of commercial vehicle citation. The citation includes references to the statute(s) that was (were) violated. It includes information on the violator and the officer issuing the citation. A citation differs from a violation because it is adjudicated by the courts. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. |  |
| commercial vehicle archive data | Information describing commercial vehicle travel and commodity flow characteristics. Content may include a catalog of available information, the actual information to be archived, and associated meta data that describes the archived information. |  |
| commercial vehicle breach | Information about a breach or tamper event on a Commercial Vehicle or its attached freight equipment which includes identity, type of breach, location, and time. | CR 2390 |
| commercial vehicle disable | This flow safely disables a specific commercial vehicle. | CR 2390 |
| commercial vehicle measures | Commercial vehicle and driver status measured by on-board ITS equipment. | CR 2390 |
| compliance review report | Report containing results of carrier compliance review, including concomitant out-of-service notifications, carrier warnings/notifications. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. |  |
| credential application | Application for commercial vehicle credentials. Authorization for payment is included. |  |
| credential fee coordination | Jurisdiction's rates for various credentials (IRP, IFTA, etc.) that are exchanged between agencies. |  |
| credentials information | Response containing full credentials information. "Response" may be provided in reaction to a real-time query or a standing request for updated information. The query flow is not explicitly shown. |  |
| credentials status information | Credentials information such as registration, licensing, insurance, check flags, and electronic screening enrollment data. A unique identifier is included. Corresponds to the credentials portion of CVISN "snapshots." The status information may be provided as a response to a real-time query or as a result of a standing request for updated information (subscription). This may also include information about non-U.S. fleets for use by U.S. authorities, and information regarding U.S. fleets made available to Mexican and Canadian authorities. The query flow is not explicitly shown. |  |
| current asset restrictions | Restrictions levied on transportation asset usage based on infrastructure design, surveys, tests, or analyses. This includes standard facility design height, width, and weight restrictions, special restrictions such as spring weight restrictions, and temporary facility restrictions that are imposed during maintenance and construction. |  |
| CVO driver initialization | This flow represents the tactile or auditory interface with ITS equipment containing the commercial vehicle driver and vehicle information. This flow contains inquiries to the commercial vehicle managing system. | CR 2390 |
| CVO pass/pull-in message | This flow represents the visual or auditory interface with ITS equipment containing a message sent to commercial vehicle driver indicating whether to bypass or requesting pull in to inspection/verification stop along with inspection results (e.g., LED indicator on transponder or variable message sign). | CR 2390 |
| CVO weight and presence | Physical attribute of commercial vehicle that can be measured (for example, weight, number of axles, axle spacing, etc.). |  |
| daily site activity data | Record of daily activities at commercial vehicle check stations including summaries of screening events and inspections. |  |
| declaration information | Notification containing information regarding pending commercial freight shipment into the U.S. |  |
| disable commercial vehicle | A request that a specific commercial vehicle should be safely disabled. | CR 2390 |
| domestic transportation information | Real-time or near real-time data regarding trade transportation activity. Potentially categorized by shipper classification, carrier, commodity, etc. Intended for use as a transportation decision tool. |  |
| driver alert response | Commercial Vehicle Driver response to a breach alert for a Freight Equipment breach or tamper event. | CR 2390 |
| driver identity characteristics | The physical or visible characteristics of a commercial vehicle driver that can be measured to uniquely identify a driver. Could be an Identification Card with a Personal Identification Number, biometrics, or visual verification by an operator. | CR 2390 |
| driver log | A daily log showing hours in service for the current driver. |  |
| driver log request | Request for driver log data. |  |
| driver to fleet request | Requests from the driver and vehicle for routing, payment, and enrollment information. |  |
| electronic lock data | Notification to roadside (via transponder) of the presence and status of electronic cargo locks. |  |
| electronic lock data request | Request from roadside for data regarding presence and status of electronic cargo locks. |  |
| electronic screening request | Request for identification data to support electronic screening. |  |
| emergency acknowledge | Acknowledge request for emergency assistance and provide additional details regarding actions and verification requirements. |  |
| emergency data request | A request for additional information or a control command issued by the emergency response agency in response to an emergency request for assistance from a traveler. |  |
| emergency notification | An emergency request for assistance originated by a traveler using an in-vehicle, public access, or personal device or originated by a transit vehicle operator using an on-board device. | CR 2390 |
| expected driver identity characteristics | Driver identification information, e.g., encrypted PIN codes issued to drivers, encrypted driver biometric parameters. | CR 2390 |
| fleet and freight threat information | Information about threats detected by commercial vehicle fleet and freight operators. The threats include incidents involving commercial vehicles (i.e., hijacking), unusual activities observed by commercial vehicle operators (i.e., truck parked under a bridge), and incidents involving freight equipment (i.e., freight equipment tampering). | CR 2390 |
| fleet to driver update | Updated instructions to the driver including dispatch, routing, and special instructions. |  |
| freight breach | Information about a breach or tamper event on Freight Equipment which includes identity, type of breach, location, and time. | CR 2390 |
| freight equipment information | Container, trailer, or chassis information regarding identity, type, location, brake wear data, mileage, seal #, seal type, door open/close status, chassis bare/covered status, tethered / untethered status, Bill of Lading, and sensor status. | CR 2390 |
| freight monitoring parameters | Parameters to configure the Freight Equipment for event reporting and keep alive functions. | CR 2390 |
| freight transport booking | Booking information for the transport of freight that includes company, contact information, point of origin, pick-up location, drop-off location, and freight equipment identifier. | CR 2390 |
| hazmat environmental factors | Sensed characteristics of a vehicle that are analyzed to indicate if the vehicle is carrying a security sensitive substance, e.g., detection of radiation or ammonia compounds. | CR 2390 |
| hazmat information | Information about a particular hazmat load including nature of the load and unloading instructions. May also include hazmat vehicle route and route update information. |  |
| hazmat information request | Request for information about a particular hazmat load. |  |
| hazmat spill notification | This data flow is used by the on-board cargo monitoring equipment package to contact emergency response organizations when the cargo sensors detect a release of hazardous material. This information will include the vehicle location discussed above as well as identifying the carrier. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. |  |
| identification information | The physical characteristics of a commercial vehicle that can be used to determine a vehicle's identity, such as a license plate number, USDOT number, ICC number, bar code, etc. | CR 2390 |
| identities | Identification information for the Commercial Vehicle (e.g., license plate number or USDOT number), Freight Equipment (e.g., container, chassis, or trailer identification), and Driver. | CR 2390 |
| information on violators | Information on violators provided by a law enforcement agency. May include information about commercial vehicle violations or other kinds of violations associated with the particular entity. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. | CR 2390 |
| intermod CVO coord | Cargo movement logs, routing information, and cargo ID’s. |  |
| map update request | Request for a map update which could include a new underlying map or map layer updates. | CR 2390 |
| map updates | Map update which could include a new underlying static or real-time map or map layer(s) update. | CR 2390 |
| on-board safety data | Safety data measured by on-board sensors. Includes information about the vehicle, vehicle components, cargo, and driver. |  |
| on-board safety request | Request for on-board vehicle safety data by the roadside equipment. |  |
| on-board vehicle data | Information about the commercial vehicle stored on-board (for maintenance purposes, gate access, cargo status, lock status, etc.). |  |
| on-board vehicle request | Request for on-board vehicle data. |  |
| pass/pull-in | Command to commercial vehicle to pull into or bypass inspection station. |  |
| payment | Payment of some kind (e.g., toll, parking, fare) by traveler, which, in most cases, can be related to a credit account. |  |
| payment request | Request for payment from financial institution. |  |
| position fix | Information, which provides a traveler's or vehicles geographical position. |  |
| request for payment | Request to deduct cost of service from user's payment account. |  |
| request tag data | Request for tag information including credit identity, stored value card cash, etc. |  |
| road network conditions | Current and forecasted traffic information, road and weather conditions, traffic incident information, and other road network status. Either raw data, processed data, or some combination of both may be provided by this architecture flow. Information on diversions and alternate routes, closures, and special traffic restrictions (lane/shoulder use, weight restrictions, width restrictions, HOV requirements) in effect is also included. | CR 2390 |
| route deviation alert | An alert that indicates a deviation from a planned route has been detected. The alert will contain the current Commercial Vehicle location and identity. | CR 2390 |
| route plan | Tailored route provided by ISP in response to a specific request. |  |
| route request | Request for a tailored route based on given constraints. |  |
| route restrictions | Information about routes, road segments, and areas that do not allow the transport of security sensitive hazmat cargoes or include other restrictions (such as height or weight limits). | CR 2390 |
| safe vehicle disable | Control signal disabling or enabling commercial vehicle. | CR 2390 |
| safety inspection record | Record containing results of commercial vehicle safety inspection. |  |
| safety inspection report | Report containing results of commercial vehicle safety inspection. The information may be provided as a response to a real-time query or proactively by the source. The query flow is not explicitly shown. |  |
| safety inspection request | Request for safety inspection record. |  |
| safety status information | Safety information such as safety ratings, inspection summaries, and violation summaries. A unique identifier is included. Corresponds to the safety portion of CVISN "snapshots." The status information may be provided as a response to a real-time query or as a result of a standing request for updated information (subscription). This may also include information about non-U.S. fleets for use by U.S. authorities, and information regarding U.S. fleets made available to Mexican and Canadian authorities. The query flow is not explicitly shown. |  |
| screening event record | Results of CVO electronic screening activity. |  |
| tag data | Unique tag ID and related vehicle information. |  |
| tag update | Update data held in tag which can be read by another roadside device (Commercial Vehicle Check Subsystem, Toll Collection Subsystem, etc.). |  |
| tax filing | Commercial vehicle tax filing data. Authorization for payment is included. |  |
| toll data | Current toll schedules for different types of vehicles as well as advanced toll payment information. |  |
| toll data request | Request made to obtain toll schedule information or pay a toll in advance. The request can be a subscription that initiates as-needed information updates as well as a one-time request for information. |  |
| transaction status | Response to transaction request. Normally dealing with a request for payment. |  |
| transportation border clearance assessment | Notification regarding the granting of permission for commercial freight shipment to enter the U.S. Includes directions for commercial driver to proceed to nearest vehicle weigh and inspection station for further review if required. |  |
| trip declaration identifiers | Specific identifiers extracted from notification containing information regarding pending commercial freight shipment into the U.S. Includes carrier, vehicle, and driver identification data. |  |
| trip identification number | The unique trip load number for a specific cross-border shipment. |  |
| trip log | Driver's daily log, vehicle location, mileage, and trip activity (includes screening, inspection and border clearance event data as well as fare payments). |  |
| trip log information | This flow represents the tactile or auditory interface with ITS equipment containing the information entered into the trip log, or request for update. | CR 2390 |
| trip log request | Request for trip log. |  |
| vehicle location | Location of a vehicle calculated on-board the vehicle. | CR 2390 |
| vehicle probe data | Vehicle probe data indicating identity, route segment identity, link time and location. |  |
| vehicle signage data | In-vehicle signage data generated by the roadway infrastructure indicating either road conditions, street names, or special information. |  |
| violation notification | Notification to enforcement agency of a violation. The violation notification flow describes the statute or regulation that was violated and how it was violated (e.g., overweight on specific axle by xxx pounds or which brake was out of adjustment and how far out of adjustment it was). A violation differs from a citation because it is not adjudicated by the courts. |  |

Table 3 presents the definitions for subsystems and terminators.  Unless otherwise indicated, all definitions are from National ITS Architecture Version 5.0 [Reference 4].

Table 3.  Subsystem and Terminator Descriptions.

| Subsystem and Terminator Descriptions |
| --- |
| Subsystem/Terminator | Updated Description | CR # |
| Alerting and Advisory Systems | This terminator represents the federal, state, and local alerting and advisory systems that provide alerts, advisories, and other potential threat information that is relevant to surface transportation systems. This includes systems such as the Information Sharing and Analysis Centers (ISACs), the National Infrastructure Protection Center (NIPC), the Homeland Security Advisory System (HSAS), and other systems that provide intelligence about potential, imminent, or actual attacks on the transportation infrastructure or its supporting information systems. This terminator also represents the early warning and emergency alert systems operated by federal, state, county, and local agencies that provide advisories and alerts regarding all types of emergencies including natural hazards (floods, hurricanes, tornados, earthquakes), accidents (chemical spills, nuclear power plant emergencies) and other civil emergencies such as child abduction alerts that impact transportation system operation and/or require immediate public notification. Note that weather related watches and warnings, such as those issued by the National Hurricane Center, are provided by both this terminator and the Weather Service terminator since many alerting and advisory systems and the National Weather Service both provide severe weather and related hazards information. The alerts and advisories that are provided by the systems represented by this terminator are based on analysis of potential threat information that is collected from a variety of sources, including information collected by ITS systems. The bidirectional interface with this terminator allows potential threat information that is collected by ITS systems to be provided to the alerting and advisory systems to improve their ability to identify threats and provide useful and timely information. The types of information provided by this terminator include general assessments and incident awareness information, advisories that identify potential threats or recommendations to increase preparedness levels, alerts regarding imminent or in-progress emergencies, and specific threat information such as visual imagery used for biometric image processing. | CR2390 |
| Archived Data Management (ADMS) | The Archived Data Management Subsystem collects, archives, manages, and distributes data generated from ITS sources for use in transportation administration, policy evaluation, safety, planning, performance monitoring, program assessment, operations, and research applications. The data received is formatted and tagged with attributes that define the data source, conditions under which it was collected, data transformations, and other information (i.e., meta data) necessary to interpret the data. The subsystem can fuse ITS generated data with data from non-ITS sources and other archives to generate information products utilizing data from multiple functional areas, modes, and jurisdictions. The subsystem prepares data products that can serve as inputs to federal, state, and local data reporting systems. This subsystem may be implemented in many different ways. It may reside within an operational center and provide focused access to a particular agency's data archives. Alternatively, it may operate as a distinct center that collects data from multiple agencies and sources and provides a general data warehouse service for a region. | CR2390 |
| Basic Commercial Vehicle | This terminator represents the motorized commercial vehicle platform that interfaces with and hosts ITS electronics. This terminator represents a vehicle that is used to transport goods which are operated by professional drivers, typically administered as part of a larger fleet, and regulated by a Fleet-Freight Manager. This classification applies to all such vehicles ranging from small panel vans used in local pick-up and delivery services to large, multi-axle tractor-trailer rigs operating on long haul routes. | CR2390 |
| Commercial Vehicle Administration (CVAS) | The Commercial Vehicle Administration Subsystem will operate at one or more fixed locations within a region. This subsystem performs administrative functions supporting credentials, tax, and safety regulations. It issues credentials, collects fees and taxes, and supports enforcement of credential requirements. This subsystem communicates with the Fleet Management Subsystems associated with the motor carriers to process credentials applications and collect fuel taxes, weight/distance taxes, and other taxes and fees associated with commercial vehicle operations. The subsystem also receives applications for, and issues special Oversize/Overweight and HAZMAT permits in coordination with other cognizant authorities. The subsystem coordinates with other Commercial Vehicle Administration Subsystems (in other states/regions) to support nationwide access to credentials and safety information for administration and enforcement functions. This subsystem supports communications with Commercial Vehicle Check Subsystems operating at the roadside to enable credential checking and safety information collection. The collected safety information is processed, stored, and made available to qualified stakeholders to identify carriers and drivers that operate unsafely. |  |
| Commercial Vehicle Check (CVCS) | The Commercial Vehicle Check Subsystem supports automated vehicle identification at mainline speeds for credential checking, roadside safety inspections, and weigh-in-motion using two-way data exchange. These capabilities include providing warnings to the commercial vehicle drivers, their fleet managers, and proper authorities of any safety problems that have been identified, accessing and examining historical safety data, and automatically deciding whether to allow the vehicle to pass or require it to stop with operator manual override. The Commercial Vehicle Check Subsystem also provides supplemental inspection services to current capabilities by supporting expedited brake inspections, the use of operator hand-held devices, on-board safety database access, and the enrollment of vehicles and carriers in the electronic clearance program. |  |
| Commercial Vehicle Driver | This terminator represents the human entity that operates vehicles transporting goods including both long haul trucks and local pick up and delivery vans. This terminator is complementary to the Driver terminator in that it represents those interactions which are unique to Commercial Vehicle Operations. Data flowing from the Commercial Vehicle Driver terminator will include those system inputs specific to Commercial Vehicle Operations, such as information back to the Fleet-Freight Manager. Data flowing to the Commercial Vehicle Driver may include system outputs such as commands to pull into a roadside safety inspection facility. Showing the Driver as a terminator includes the user interface devices within the ITS architecture boundary. The Commercial Vehicle Driver will be expected to interact with the ITS interface devices designed to provide support for their usage. | CR2390 |
| Commercial Vehicle Subsystem Aggregate (CVSAg) [The Commercial Vehicle Subsystem Aggregate combines the National ITS Architecture Commercial Vehicle and Vehicle Subsystems; it is not a standalone subsystem within the National ITS Architecture.] | The Commercial Vehicle Subsystem part resides in a commercial vehicle and provides the sensory, processing, storage, and communications functions necessary to support safe and efficient commercial vehicle operations. The Commercial Vehicle Subsystem provides two-way communications between the commercial vehicle drivers, their fleet managers, attached freight equipment, and roadside officials, and provides HAZMAT response teams with timely and accurate cargo contents information after a vehicle incident. This subsystem provides the capability to collect and process vehicle, cargo information from the attached freight equipment, and driver safety data and status and alert the driver whenever there is a potential safety or security problem. Basic identification, security and safety status data are supplied to inspection facilities at mainline speeds. In addition, the subsystem will automatically collect and record mileage, fuel usage, and border crossings. The Vehicle Subsystem part provides the sensory, processing, storage, and communications functions necessary to support efficient, safe, and convenient travel. These functions reside in general vehicles including personal automobiles, commercial vehicles, emergency vehicles, transit vehicles, or other vehicle types. Information services provide the driver with current travel conditions and the availability of services along the route and at the destination. Both one-way and two-way communications options support a spectrum of information services from low-cost broadcast services to advanced, pay for use personalized information services. Route guidance capabilities assist in formulation of an optimal route and step-by-step guidance along the travel route. Advanced sensors, processors, enhanced driver interfaces, and actuators complement the driver information services so that, in addition to making informed mode and route selections, the driver travels these routes in a safer and more consistent manner. Initial collision avoidance functions provide “vigilant co-pilot” driver-warning capabilities. More advanced functions assume limited control of the vehicle to maintain safe headway. Ultimately, this subsystem supports completely automated vehicle operation through advanced communications with other vehicles in the vicinity and in coordination with supporting infrastructure subsystems. Pre-crash safety systems are deployed and emergency notification messages are issued when unavoidable collisions do occur. | CR2390 |
| CVO Information Requestor | This terminator represents any organization requesting information from the CVO Information Exchange network. It typically represents insurance companies requesting safety information on carriers, etc. |  |
| Emergency Management (EM) | The Emergency Management Subsystem represents public safety, emergency management, and other allied agency systems that support incident management, disaster response and evacuation, security monitoring, and other security and public safety-oriented ITS applications. The subsystem includes the functions associated with fixed and mobile public safety communications centers including public safety call taker and dispatch centers operated by police (including transit police), fire, and emergency medical services. It includes the functions associated with Emergency Operations Centers that are activated at local, regional, state, and federal levels for emergencies and the portable and transportable systems that support Incident Command System operations at an incident. This subsystem also represents other allied systems including centers associated with towing and recovery, freeway service patrols, HAZMAT response teams, and mayday service providers. The subsystem manages sensor and surveillance equipment used to enhance transportation security of the roadway infrastructure (including bridges, tunnels, interchanges, and other key roadway segments) and the public transportation system (including transit vehicles, public areas such as transit stops and stations, facilities such as transit yards, and transit infrastructure such as rail, bridges, tunnels, or bus guideways). The subsystem provides security/surveillance services to improve traveler security in public areas not a part of the public transportation system. This subsystem monitors alerts, advisories, and other threat information and prepares for and responds to identified emergencies. It interfaces with other Emergency Management Subsystems to support coordinated emergency response involving multiple agencies. The subsystem stores, coordinates, and utilizes emergency response and evacuation plans to facilitate this coordinated response. As the response progresses, situation information including damage assessments, response status, evacuation information, and resource information are shared to keep all allied agencies appraised of the response. Interface with the Transit Management Subsystem allows coordinated use of transit vehicles to facilitate response to major emergencies and to support evacuation efforts. The Emergency Management Subsystem also provides a focal point for coordination of the emergency and evacuation information that is provided to the traveling public, including wide-area alerts when immediate public notification is warranted. The subsystem tracks and manages emergency vehicle fleets using real-time road network status and routing information from the other center subsystems to aide in selecting the emergency vehicle(s) and routes that will provide the most timely response. Interface with the Traffic Management Subsystem allows strategic coordination in tailoring traffic control to support emergency vehicle ingress and egress, implementation of special traffic restrictions and closures, evacuation traffic control plans, and other special strategies that adapt the transportation system to better meet the unique demands of an emergency. | CR2390 |
| Emergency Vehicle (EVS) | This subsystem resides in an emergency vehicle and provides the sensory, processing, storage, and communications functions necessary to support safe and efficient incident response. The subsystem represents a range of vehicles including those operated by police, fire, and emergency medical services. In addition, this subsystem represents other incident response vehicles including towing and recovery vehicles and freeway service patrols. The Emergency Vehicle Subsystem includes two-way communications to support coordinated response to emergencies in accordance with an associated Emergency Management Subsystem. Emergency vehicles are equipped with automated vehicle location capability for monitoring by vehicle tracking and fleet management functions in the Emergency Management Subsystem. Using these capabilities, the appropriate emergency vehicle to respond to each emergency is determined. Route guidance capabilities within the vehicle enable safe and efficient routing to the emergency. In addition, the emergency vehicle may be equipped to support signal preemption through communications with the Roadway Subsystem. | CR2390 |
| Enforcement Agency | This terminator represents the systems that receive reports of violations detected by various ITS facilities including individual vehicle emissions, toll violations, CVO violations, excessive speed in work zones, etc. |  |
| Financial Institution | This terminator represents the organization that handles all electronic fund transfer requests to enable the transfer of funds from the user of the service to the provider of the service. The functions and activities of financial clearinghouses are subsumed by this entity. |  |
| Fleet and Freight Management (FMS) | The Fleet and Freight Management Subsystem provides the capability for commercial drivers and fleet or freight managers to receive real-time routing information and access databases containing vehicle and/or freight equipment locations as well as carrier, vehicle, freight equipment and driver information. In addition, the capability to purchase credentials electronically shall also be provided, with automated and efficient connections to financial institutions and regulatory agencies, along with post-trip automated mileage and fuel usage reporting. The Fleet and Freight Management Subsystem also provides the capability for fleet managers to monitor the safety and security of their commercial vehicle drivers and fleet. The subsystem also supports application for hazmat credentials and makes information about hazmat cargo available to agencies as required. Within this subsystem lies all the functionality associated with subsystems and components necessary to enroll and participate in international goods movement programs aimed at enhancing trade and transportation safety and security. | CR2390 |
| Freight Equipment | This terminator represents a freight container, intermodal chassis or trailer and provides information to support safe, secure and efficient freight operations. This terminator provides equipment safety data and status and can alert the appropriate systems of an incident, breach, or tamper event. This terminator provides accurate position information to support in-transit visibility of freight equipment. | CR2390 |
| Information Service Provider (ISP) | This subsystem collects, processes, stores, and disseminates transportation information to system operators and the traveling public. The subsystem can play several different roles in an integrated ITS. In one role, the ISP provides a general data warehousing function, collecting information from transportation system operators and redistributing this information to other system operators in the region and other ISPs. In this information redistribution role, the ISP provides a bridge between the various transportation systems that produce the information and the other ISPs and their subscribers that use the information. The second role of an ISP is focused on delivery of traveler information to subscribers and the public at large. Information provided includes basic advisories, traffic and road conditions, transit schedule information, yellow pages information, ridematching information, and parking information. The subsystem also provides the capability to provide specific directions to travelers by receiving origin and destination requests from travelers, generating route plans, and returning the calculated plans to the users. In addition to general route planning for travelers, the ISP also supports specialized route planning for vehicle fleets. In this third role, the ISP function may be dedicated to, or even embedded within, the dispatch system. Reservation services are also provided in advanced implementations. The information is provided to the traveler through the Personal Information Access Subsystem, Remote Traveler Support Subsystem, and various Vehicle Subsystems through available communications links. Both basic one-way (broadcast) and personalized two-way information provision is supported. The subsystem provides the capability for an informational infrastructure to connect providers and consumers, and gather that market information needed to assist in the planning of service improvements and in maintenance of operations. |  |
| Intermodal Freight Depot | A depot operated either by a depot manager or an alternate mode freight shipper which represents the point of exchange where freight is moved from one mode to another. The depot has knowledge about activities that may impact travel on roadways such as large groups of trucks entering the highway after unloading a ship or freight train. The depot interfaces to the ITS to coordinate freight movement with Fleet-Freight Managers, gather information on traffic conditions affecting the depot, and to provide information on intermodal freight activities that is pertinent to traffic movement in the surrounding area. | CR2390 |
| Intermodal Freight Shipper | This terminator represents organizations that engage in the shipment of freight by multiple means, in addition to road-going trucks. They enable ITS to move goods on routes that require the use of other modes of transportation such as heavy rail, air, sea, etc. This terminator includes third party logistics providers (i.e., brokers, freight forwarders, etc) that interface with Fleet-Freight Managers to transfer cargo from one mode to another. This definition includes those responsible for the movement of freight across international borders. These entities are responsible for filing required declarations, and have an acute interest in the status of international shipments. | CR2390 |
| Location Data Source | This terminator provides accurate position information. Systems, which use GPS, terrestrial trilateration, or driver inputs, are all potential examples of Location Data Sources. This terminator contains sensors such as radio position receivers (e.g., GPS) and/or dead reckoning sensors (e.g., odometer, differential odometer, magnetic compass, gyro, etc.). This terminator implies that some additional functionality associated with developing an absolute position is outside the system and will not be directly modeled by the logical or physical architecture representations of the system. |  |
| Maintenance and Construction Management | The Maintenance and Construction Management Subsystem monitors and manages roadway infrastructure construction and maintenance activities. Representing both public agencies and private contractors that provide these functions, this subsystem manages fleets of maintenance, construction, or special service vehicles (e.g., snow and ice control equipment). The subsystem receives a wide range of status information from these vehicles and performs vehicle dispatch, routing, and resource management for the vehicle fleets and associated equipment. The subsystem participates in incident response by deploying maintenance and construction resources to an incident scene, in coordination with other center subsystems. The subsystem manages equipment at the roadside, including environmental sensors and automated systems that monitor and mitigate adverse road and surface weather conditions. The subsystem manages the repair and maintenance of both non-ITS and ITS equipment including the traffic controllers, detectors, dynamic message signs, signals, and other equipment associated with the roadway infrastructure. Additional interfaces to weather information providers (the weather service and surface transportation weather service providers) provide current and forecast weather information that can be fused with other data sources and used to support advanced decision support systems that increase the efficiency and effectiveness of maintenance and construction operations. The subsystem remotely monitors and manages ITS capabilities in work zones, gathering, storing, and disseminating work zone information to other systems. It manages traffic in the vicinity of the work zone and advises drivers of work zone status (either directly at the roadside or through an interface with the Information Service Provider or Traffic Management subsystems.) It schedules and manages the location and usage of maintenance assets (such as portable dynamic message signs). Construction and maintenance activities are tracked and coordinated with other systems, improving the quality and accuracy of information available regarding closures and other roadway construction and maintenance activities. |  |
| Map Update Provider | This terminator represents a third-party developer and provider of digitized map databases used to support ITS services. It supports the provision of the databases that are required exclusively for route guidance (navigable maps) as well as those that are used exclusively for display by operators, e.g., Fleet-Freight Managers (restricted routes) and at traveler information points, e.g., kiosks (display maps). | CR2390 |
| Other CVAS | This terminator is intended to provide a source and destination for ITS data flows between peer (e.g., inter-regional) commercial vehicle administration functions. It enables commercial vehicle administration activities to be coordinated across different jurisdictional areas. In the Physical Architecture, this terminator is a reciprocal Commercial Vehicle Administration Subsystem (CVAS). This terminator encompasses all functions associated with commercial vehicle safety, registration, and operating authority for non-U.S. based commercial motor vehicle carriers. The agencies represented herein may include Federal, state, provincial, and local regulatory entities outside the U.S. |  |
| Parking Management (PMS) | The Parking Management Subsystem provides electronic monitoring and management of parking facilities. It supports a dedicated short-range communications (DSRC) communications link to the Vehicle Subsystem that allows electronic collection of parking fees. It also includes the instrumentation, signs, and other infrastructure that monitors parking lot usage and provides local information about parking availability and other general parking information. This portion of the subsystem functionality must be located in the parking facility where it can monitor, classify, and share information with customers and their vehicles. The subsystem also interfaces with the financial infrastructure and broadly disseminates parking information to other operational centers in the region. Note that the latter functionality may be located in a back office, remote from the parking facility. |  |
| Roadway (RS) | This subsystem includes the equipment distributed on and along the roadway that monitors and controls traffic and monitors and manages the roadway itself. Equipment includes traffic detectors, environmental sensors, traffic signals, highway advisory radios, dynamic message signs, CCTV cameras and video image processing systems, grade crossing warning systems, and freeway ramp metering systems. HOV lane management, reversible lane management functions, and barrier systems that control access to transportation infrastructure such as roadways, bridges and tunnels are also supported. This subsystem also provides the capability for environmental monitoring including sensors that measure road conditions, surface weather, and vehicle emissions. In adverse conditions, automated systems can be used to apply anti-icing materials, disperse fog, etc. Work zone systems including work zone surveillance, traffic control, driver warning, and work crew safety systems are also included. To enhance security, safeguard systems such as blast shields, exhaust systems and other automated and remotely controlled systems to protect transportation infrastructure is also provided. In advanced implementations, this subsystem supports automated vehicle safety systems by safely controlling access to and egress from an Automated Highway System through monitoring of, and communications with, AHS vehicles. Intersection collision avoidance functions are provided by determining the probability of a collision in the intersection and sending appropriate warnings and/or control actions to the approaching vehicles. | CR2390 |
| Toll Administration (TAS) | The Toll Administration Subsystem provides general payment administration capabilities and supports the electronic transfer of authenticated funds from the customer to the transportation system operator. This subsystem supports traveler enrollment and collection of both pre-payment and post-payment transportation fees in coordination with the existing, and evolving financial infrastructure supporting electronic payment transactions. The system may establish and administer escrow accounts depending on the clearinghouse scheme and the type of payments involved. This subsystem posts a transaction to the customer account and generates a bill (for post-payment accounts), debits an escrow account, or interfaces to the financial infrastructure to debit a customer designated account. It supports communications with the Toll Collection Subsystem to support fee collection operations. The subsystem also sets and administers the pricing structures and includes the capability to implement road-pricing policies in coordination with the Traffic Management Subsystem. The electronic financial transactions in which this subsystem is an intermediary between the customer and the financial infrastructure shall be cryptographically protected and authenticated to preserve privacy and ensure authenticity and auditability. |  |
| Toll Collection (TCS) | The Toll Collection Subsystem provides the capability for vehicle operators to pay tolls without stopping their vehicles using locally determined pricing structures and includes the capability to implement various variable road pricing policies. Each transaction is accompanied by feedback to the customer indicating the general status of the customer account. A record of the transactions is provided to the Toll Administration Subsystem for reconciliation and so that the customer can periodically receive a detailed record of the transactions. | CR2390 |
| Trade Regulatory Agencies | These agencies include U.S. domestic and foreign governmental agencies responsible for the regulation of trade, and the enforcement of customs and immigration laws. These agencies include U.S. Customs, the U.S. Immigration and Naturalization Service (INS), and their counterparts in Canada and Mexico. They may also include secondary trade agencies (e.g., U.S. Food and Drug Administration, U.S. Department of Agriculture, other USDOT departments, etc.), and agencies from other trading nations. |  |
| Traveler Card | This terminator represents the entity that enables the actual transfer of electronic information from the user of a service (i.e., a traveler) to the provider of the service. This may include the transfer of funds through means of an electronic payment instrument. The device, like a smart card, may also hold and update the traveler's information such as personal profiles or trip histories. |  |

Table 4 presents the definitions for equipment packages.  Unless otherwise indicated, all definitions are from National ITS Architecture Version 5.0 [Reference 4].  Italics indicate that the equipment package currently falls outside the scope of CVISN Level 1 but is part of systems that support commercial vehicle operations; if the equipment package name is also underlined, it is a candidate for inclusion in future enhancements of CVISN.  This table was added to this document via CR 2535.

Table 4.  Equipment Package Descriptions.

| Equipment Package Descriptions |
| --- |
| SUBSYSTEM Equipment Package | Updated Description | CR # |
| CVAS |  |  |
| Credentials and Taxes Administration | This equipment package provides administrative capabilities for commercial vehicle operations including database management and administrator-to-roadside and administrator-to-administrator interfaces. For example, this equipment package would manage the electronic credentials database for a state, perform reconciliation of mileage and fuel taxes (possibly post trip), and interface with roadsides performing credential checks. This equipment package communicates with similar packages in other CVAS locations to exchange credentials database information. Example locations would be state agency or regional offices that are involved with commercial vehicle operations. This equipment package also exchanges hazmat route restrictions information, and provides a clearinghouse for this information that then can share the information with Map Update Providers, Fleet and Freight Management subsystems and Information Service Providers. | CR2390 |
| CV Data Collection | This equipment package collects and stores commercial vehicle information that is collected in the course of Commercial Vehicle Administration Subsystem operations. This data can be used directly by operations personnel or it can be made available to other data users and archives in the region. |  |
| CV Information Exchange | This equipment package supports the exchange of safety and credentials data among jurisdiction. The package also supports the exchange of safety and credentials data between agencies (for example, an administrative center and the roadside check facilities) within a single jurisdiction. Data are collected from multiple authoritative sources and packaged into snapshots (top-level summary and critical status information) and profiles (detailed and historical data). |  |
| CV Safety Administration | This equipment package augments the Credentials and Taxes Administration equipment package with safety data. This package ensures that safety criteria are available for automated roadside safety checks. It supports the collection and review of carrier safety data and determines the carrier safety rating. |  |
| International CV Administration | This equipment package is used by government agencies such as customs and immigration, carriers, and service providers (e.g., brokers) to generate and process the entry documentation necessary to obtain release of vehicle, cargo, and driver across and international border, report the results of the crossing event, and handle duty fee processing. |  |
| CVCS |  |  |
| Citation and Accident Electronic Recording | The equipment package documents violations and forwards the information to the Commercial Vehicle Administration Subsystem for processing as part of the normal credentials processing package. |  |
| International Border Crossing | This equipment package is used by government agencies such as customs and immigration to check compliance with import/export and immigration regulations to allow release of cargo, vehicle, and driver across an international border. |  |
| Roadside Electronic Screening | This equipment package provides the Commercial Vehicle Check Subsystem the capabilities for two-way communication with approaching properly equipped commercial vehicles at mainline speeds, reading tags for automated vehicle identification and credential checking. There will be a capability to appropriately screen all vehicles, not just those that are equipped. This equipment package shall be able to process the data from the commercial vehicles along with accessed database information to determine whether a pull-in message is needed or to generate random pull-in messages with provisions for facility operators and enforcement officials to have manual override capabilities. Support shall be provided to both interstate and intrastate carriers. |  |
| Roadside HAZMAT Detection | This equipment package monitors roadside remote sensing sensor data deployed to collect physical characteristics of security sensitive materials. It assesses the likelihood of the presence of security sensitive HAZMAT materials based on remote sensed data as well as other physical information acquired about the CV. It then determines if any detected HAZMAT is authorized. If unauthorized HAZMAT material is detected then it messages the Commercial Vehicle Driver to pull-in. The equipment package may also issue a message to the Emergency Management (Police Dispatch) function with jurisdiction over the location of the incident that the event has occurred including: the location of the incident, and current location of the commercial vehicle and a timestamp, Vehicle ID, Carrier ID, Driver ID, CV Credentials information, HAZMAT material or category detected and expected cargo manifest (if known). The CVCS may issue a similar message to the TMS agency(ies) with jurisdiction over the region of the incident, as well as to the CVAS and then to the FMS which manages the vehicle (does not need to be real-time). This might be used to disable the vehicle. | CR2390 |
| Roadside Safety and Security Inspection | This equipment package provides the Commercial Vehicle Check Subsystem the capabilities for operators to automate the roadside safety inspection process including the support of use of hand held devices to rapidly inspect the vehicle and driver. In addition this equipment package provides the Roadside Check Subsystem the capabilities for operators to automate the roadside safety inspection process including the support of automated mainline speed reading of on-board safety data to rapidly screen the vehicle and driver. This equipment package shall also provide the capabilities to collect, store, maintain, and provide safety data and access historical safety data after receiving identification from vehicles at mainline speeds or while stopped at the roadside. Results of screening and summary safety inspection can be written back onto the tag. The capabilities to process safety data and issue pull-in messages or provide warnings to the driver, carrier, and enforcement agencies shall be provided. These capabilities have a prerequisite of the Roadside Electronic Screening equipment package and shall be provided primarily through the utilization of an additional safety database. Since a vehicle may cross jurisdiction boundaries during a trip, this equipment package supports the concept of a last clearance event record (aka trip ticket) carried on the vehicle s tag. The last clearance event record reflects the results of the roadside verification action. For example, if the vehicle is pulled over in State A and undergoes credential, weight, and safety checks, the results of the clearance process are written to the vehicle s tag. If the vehicle continues the trip and passes a roadside station in State B, the State B station has access to the results of the previous pull-in because it can read the last clearance event record written by the State A roadside station. |  |
| Roadside WIM | This equipment package allows for roadside high speed weigh in motion. This package can be fixed to a location or mobile. It can include an interface to the credential check package and augment electronic credentials check with electronic weight check or it can be a stand alone package with display. |  |
| CVSAg (CVS) |  |  |
| On-board Cargo Monitoring | This equipment package provides the Commercial Vehicle Subsystem the capability to monitor both interstate and intrastate cargo safety and security such that enforcement and HAZMAT response teams can be provided with timely and accurate information. In addition, this package provides security alerts in the case of tampering or other cargo security breaches. This includes only the equipment on board the cargo container such as a communication device, possibly the addition of a cell-based radio, and equipment for the processing and storage of cargo material. This can also include optional sensors for temperature, pressure, load leveling, or acceleration depending upon the items monitored. It is already expected that the cargo location devices such as GPS equipment and an integration processor already exist. These items are presented as part of the On-board Trip Monitoring equipment package. | CR2390 |
| On-board CV Electronic Data | This equipment package provides the Commercial Vehicle Subsystem the capability for two-way data exchange between the vehicle and the roadside facility with the transmission of information such as status of driver, vehicle, and carrier IDs and cargo information. The driver, vehicle and carrier are identified via the tag so that actual weight from roadside mainline weigh-in-motion may be checked. This includes only the equipment on the commercial vehicle including a processor/tag for identification, especially a HAZMAT identification. The actual reading and processing required for the credential checking and weigh-in-motion will be performed by the roadside. | CR2390 |
| On-board CV Safety and Security | This equipment package provides the Commercial Vehicle Subsystem the capability to collect and process on board vehicle and driver safety and security information to monitor the safety and security status. This equipment package also supplies this information to the roadside facilities both at mainline speeds and while stopped for inspections. The capability to alert the commercial vehicle driver whenever there is a critical safety or security problem or potential emergency shall also be provided. These capabilities include only the equipment on the commercial vehicle including the sensors and processors to monitor the vehicle and driver with the information stored on the vehicle. When the information is transmitted to the roadside facility or after the trip, it will utilize the communication devices already in place. The package will also support onboard driver safety log maintenance and checking. | CR2390 |
| On-board Driver Authentication | This equipment package monitors the identity of the commercial vehicle driver and compares it with the planned drivers for the commercial vehicle. Any change in driver is sent to the Fleet and Freight Management Subsystem. Notification of any unexpected drivers will also be send to the Fleet and Freight Management Subsystem which, in turn may send a disable vehicle command back to this equipment package to cause the vehicle to stop. On receipt of a disable vehicle message from the Fleet and Freight Management Subsystem or on detection of an unauthorized driver, the equipment package will safety disable the CV. | CR2390 |
| On-board Trip Monitoring | This equipment package provides the capabilities to support fleet management with automatic vehicle location and automated mileage and fuel reporting and auditing. In addition, this equipment is used to monitor the planned route and notify the Fleet and Freight Management Subsystem of any deviations. This package may also record other special events resulting from communication with roadside equipment. This includes only the equipment on board the vehicle to support this function including the vehicle location devices such as GPS equipment, communication interfaces, a processor to record trip length, and the sensors/actuators/interfaces necessary to record mileage and fuel usage. | CR2390 |
| CVSAg (VS) |  |  |
| Vehicle Location Determination | This equipment package determines current location information and provides this information to other equipment packages that use the location information to provide various ITS services. |  |
| Vehicle Mayday Interface | This equipment package shall provide the capability for an in-vehicle manually initiated distress signal with cancel a prior issued manual request for help feature. This capability shall include automatically identifying that a collision had occurred using equipment such as collision detection sensors with interface to mayday type equipment that would automatically detect vehicle problems and for some cases, automatically send appropriate distress signals to the Emergency Management Subsystem. |  |
| Vehicle Probe Support | This equipment package includes capabilities for the probe vehicle to identify its location, measure traffic conditions such as link travel time and speed and possibly environmental hazards such as icy road conditions, and transmit these data to either the ISP or TMC (Traffic Management Center). |  |
| Vehicle Toll/Parking Interface | This equipment package shall provide the capability for vehicle operators to pay toll without stopping their vehicles and pay for parking without the use of cash. These capabilities shall be provided through the use of equipment such as an active tag interface and debit/credit card interface. |  |
| FMS |  |  |
| Commercial Vehicle and Freight Security | This equipment package provides for the security of the commercial vehicle and the freight that it carries by detecting breaches such as seals or locks being broken into by unauthorized personnel and/or any other unauthorized tampering. In addition, this equipment package monitors the commercial vehicle driver and compares it with the planned driver for the vehicle. In a similar manner, the driver and vehicle that have been assigned to move freight are monitored and compared with the planned assignment for that freight. In all cases, any deviations to the planned assignments and any breach or tamper events are reported to the Emergency Management Subsystem. | CR2390 |
| Fleet Administration | This equipment package provides vehicle tracking, dispatch, and reporting capabilities to fleet management center personnel. It gathers current road conditions and traffic information, prepares vehicle routes, and provides a fleet interface for toll collection. It also provides route plan information for network performance evaluation. As part of the tracking function, this equipment package monitors commercial vehicle location, compares it against the known route and notifies the Emergency Management Subsystem and Fleet-Freight Manager of any deviations, including HAZMAT route restriction violations. | CR2390 |
| Fleet Credentials and Taxes Management and Reporting | This equipment package provides the Fleet and Freight Management Subsystem the capabilities to purchase credentials and file trip reports electronically by the fleet managers, to perform automated enrollment at the roadside facilities, and electronically manage the credentials checking by the roadside commercial vehicle inspectors. The electronic purchase shall be performed in accordance with developing standards such that a single integrated system for electronic payments might develop ensuring that deployment across multiple agency political boundaries is performed without degradation. Inherent to credential management shall be the management of the vehicles, with a prerequisite of the vehicle tracking software from the Fleet Administration equipment package. |  |
| Fleet HAZMAT Management | This equipment package provides the Fleet and Freight Management Subsystem the capabilities to enhance the Fleet Administration equipment package functions by adding HAZMAT tracking. The additional requirements to perform this function include enhanced processing and enhanced fleet management software. In order to effectively track HAZMAT cargo, communication interfaces to Information Service Providers, and Emergency Management Subsystems shall be provided, including additional communication software. | CR2390 |
| Fleet Maintenance Management | This equipment package provides the capability to use vehicle mileage data to automatically generate preventative maintenance schedules for each specific vehicle by utilizing vehicle tracking data from the prerequisite tracking equipment package (Fleet and Freight Management). In addition, capability to automatically ensure that proper service personnel are provided information for maintenance activities and to record and verify that maintenance work was performed shall be provided. | CR2390 |
| Freight Administration and Management | This equipment package provides the communication necessary to track cargo/freight from source to destination via links to intermodal freight shippers and depots. There are also communication links to cargo routing services. As part of the tracking function, this equipment package monitors cargo/freight location and compares it against the known route and notifies the Emergency Management Subsystem of any deviations. | CR2390 |
| Manage CV Driver Identification | This equipment package collects and stores driver identification records including driver issued PINS and/or individual driver biometric measurements. The equipment package can also manage the storage on individual CVs of driver PINs and/or biometric measurements for drivers authorized to operate the CV. Based on information reported by the commercial vehicle, the equipment package will determine if driver is authorized based on the local driver inventory store, and notify the Commercial Vehicle Manager when an unauthorized driver is detected. The Commercial Vehicle Manager may override the disable vehicle action. When an unauthorized driver is detected and the system is not overridden, then the equipment package will issue a message to the CVS to safely disable the vehicle. If an unauthorized CV driver is detected then the equipment package will issue a message to the Emergency Management Police Dispatch function with jurisdiction over the location of the incident that the event has occurred. This message will include: the location of the incident, current location of the CV, Vehicle ID, Carrier ID, Driver ID, CV Credentials information, and expected cargo manifest (if known). Also, the equipment package will issue a message to the TMS agency(ies) with jurisdiction over the region of the incident. | CR2390 |

This Page Intentionally Blank

# CHANGE REQUESTS

## Change Requests Incorporated

This section summarizes the changes incorporated into the CVISN Architecture since it was aligned with the National ITS and IBC Architectures as documented in References 1, 2 and 3 prior to the release of Version 5.0 of the National ITS Architecture [Reference 4].

CR 439 – Discrepancy between CVISN and V4 National ITS Architecture.
In the following request/response pairs, the National ITS Architecture dropped the possibility of a DSRC connection between FMS and CVSAg in ITS Architecture Version 4.0.  In Baseline V1.0 of the CVISN Architecture document, the DSRC connection option was retained.  This was shown as “X?” in the Std column of Table 1 for these flows:

  - on-board safety request/on-board safety data

  - trip log request/trip log

  - on-board vehicle request/on-board vehicle data

In Version 5.0 of the National ITS Architecture, the discrepancy was eliminated. Allowance was made for future standardization of the “trip log request”, “trip log”, “on-board vehicle request”, and “on-board vehicle data” flows.  The flow “trip identification number” was also added to the set that may be transmitted via either DSRC or wide area wireless, with an option for future standardization.  Figure 2–1 and Table 1 of the CVISN Architecture Baseline Version 2.0 document have been updated to align with Version 5.0 of the National ITS Architecture.

CR 654 – National ITS Architecture 4.0 showed no standard for "tax filing".
In the National ITS Architecture Version 4.0, the architecture flow named "tax filing" was not mapped to any standard.  EDI TS 813, Electronic Filing of Tax Return Data, is available to carry fuel tax return information and should be shown.  In Version 5.0 of the National ITS Architecture, “tax filing” is mapped to EDI TS 813, so Table 1 in the CVISN Architecture has been updated.

CR 2390 – Update CVISN Architecture to keep pace with changes to the National ITS Architecture (Version 5).
The most significant Version 5.0 enhancement is the improvement of the coverage of transportation security in the National ITS Architecture.  These improvements include updates to the physical architecture, market packages, logical architecture, and supporting documentation.  Using ITS to Enhance Transportation Security is addressed in the following CVO-related areas: Freight and Commercial Vehicle, HAZMAT, Wide Area Alerts, and Transportation Infrastructure.  In addition, guidance is now offered on ways in which ITS can be made more secure.

The diagram and tables in the CVISN architecture have been updated to include National ITS Architecture changes to the items listed below.  Note that only a few of the items include components that are typically associated with any state or federal government systems.  This could minimize the CVISN impact beyond the architecture level, at least for now.

Changes made include adding equipment packages, flows, and terminators; updating definitions for subsystems, equipment packages, flows, and terminators; updating standards indications; and updating interconnection types.

See Reference 4 for details about what is new in Version 5.0 of the National ITS Architecture.

CR 2535 – Add equipment package descriptions to CVISN Architecture document.
Baseline V1.0 of the CVISN Architecture document does not include descriptions of the equipment packages shown on the CVISN Architecture Flow Diagram.  To make the document more complete, descriptions were added as Table 4.

## Change Requests Pending

None.

# REFERENCES

- JHU/APL, ITS/CVO CVISN and National ITS Architecture Alignment, D.1, August 2001.  (Delivered via SSD-PL-01-0358, 3 August 2001.)

- JHU/APL, Commercial Vehicle Information Systems and Networks (CVISN), International Border Clearance (IBC) and National ITS Architecture Alignment, SSD-POR-02-7349 D.2, December 2001.  (Delivered via SSD-PL-01-0650, 25 March 2002.)

- JHU/APL, Commercial Vehicle Information Systems and Networks (CVISN) Architecture, SSD-POR-02-7364 V1.0, May 2002.  (Delivered via SSD-PL-02-0307, 22 August 2002.)

- The US DOT Joint Program Office, The National ITS Architecture:  a Framework for Integrated Transportation into the 21st Century, V 5.0, 2003, maintained by Iteris.  Available in CD format or on the WWW at http://www.iteris.com/itsarch/.

This Page Intentionally Blank