Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Synoptic SARB

(Subsystem 7.2)

Release 4 Test Plan

TRMM Launch

Version 1

Primary Authors

Lisa Coleman, Tom Caldwell

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA 23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  December 2007

Document Date:  December 2007

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/19/03 | R3V1 | 445 | Initial version of document. Updated format to comply with standards. | All All |
| 08/13/04 | R3V2 | 550 | Updated tar filenames. Updated environment variable filename and generalized filename variables. Updated runtime information. Added new section for Terra test case. Updated filenames and added new ones. Updated format to comply with standards. | 2.1 3.1.1.1 through 3.1.1.4, 3.1.2 3.1.1.1.2 3.2 Appendix C (Table C3-1) All |
| 08/11/06 | R3V3 | 634 | Updated tar filenames. Updated section to reflect use of new compilation script. Changed names of scripts to reflect conversion to Perl. Added use of input data file move script. Updated sections to reflect use of new Perl scripts. Updated test summary information tables. Updated filenames and added new ones. Updated format to comply with standards. | 2.1 2.2 3.1, 3.2, App. C (Table C1-1) 3.1.1.1, 3.2.1.1 3.1.1.1, 3.2.1.1 Table 3-1, Table 3-2 App. C (Table C3-1) All |
| 12/12/07 | R4V1 | 663 | Added description of new SYNs output. Updated SCCR number in filenames. Updated test case information. Updated test case summary. Added new section for Aqua test case. Updated filenames and added surface albedo history and site list filenames. | 1.2.1 2.1 3.2.1.1 3.2.1.1.2 3.3 Table C-3 |

Document Revision Record	ii

1.0	Introduction	1

1.1.	Document Overview	1

1.2.	Subsystem Overview	2

1.2.1.	CER7.2.1P1:  CERES Synoptic SARB Subsystem Main-Processor	2

2.0	Software and Data File Installation Procedures	3

2.1.	Installation	3

2.2.	Compilation	4

2.2.1.	Compiling PGE 7.2.1P1	4

3.0	Test and Evaluation Procedures	6

3.1.	PGE CER7.2.1P1--Main-Processor TRMM Test Case	6

3.1.1.	Stand Alone Test Procedures	6

3.1.1.1.	PCF Generation and Execution	6

3.1.1.1.1.	Exit Codes	7

3.1.1.1.2.	Test Summary	7

3.1.1.2.	Metadata Evaluation	8

3.1.1.3.	Execution of Comparison Software for the Main-Processor	8

3.1.1.4.	Evaluation of Main-Processor Comparison Software Output	9

3.1.2.	Solutions to Possible Problems	9

3.2.	PGE CER7.2.1P1--Main-Processor Terra Test Case	9

3.2.1.	Stand Alone Test Procedures	9

3.2.1.1.	PCF Generation and Execution	10

3.2.1.1.1.	Exit Codes	11

3.2.1.1.2.	Test Summary	11

3.2.1.2.	Metadata Evaluation	11

3.2.1.3.	Execution of Comparison Software for the Main-Processor	12

3.2.1.4.	Evaluation of Main-Processor Comparison Software Output	12

3.2.2.	Solutions to Possible Problems	13

3.3.	PGE CER7.2.1P1--Main-Processor Aqua Test Case	13

3.3.1.	Stand Alone Test Procedures	13

3.3.1.1.	PCF Generation and Execution	13

3.3.1.1.1.	Exit Codes	15

3.3.1.1.2.	Test Summary	15

3.3.1.2.	Metadata Evaluation	15

3.3.1.3.	Execution of Comparison Software for the Main-Processor	15

3.3.1.4.	Evaluation of Main-Processor Comparison Software Output	16

3.3.2.	Solutions to Possible Problems	16

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagrams	B-1

Appendix C - File Description Tables	C-1

C.1.	Production Scripts and Executables	C-1

C.2.	Processing Control Files (PCF), Metadata Control Files (MCF) and Status
	Message Files (SMF)	C-1

C.3.	Ancillary Input Data	C-4

C.4.	Output Temporary Data Files (Production Results)	C-5

Figure B-1.  Synoptic SARB Directory Structure	B-1

Table 3-1.  Test Summary for PGE 7.2.1P1	7

Table 3-2.  Test Summary for PGE 7.2.1P1	11

Table 3-3.  Test Summary for PGE 7.2.1P1	15

Table C.1-1.  Production Scripts	C-1

Table C.1-2.  Executables	C-1

Table C.2-1.  Metadata Control Files	C-1

Table C.2-2.  Process Control Files	C-2

Table C.2-3.  Status Message Files (SMF)	C-2

Table C.3-1.  Ancillary Input Data	C-4

Table C.4-1.  Output Temporary Data Files	C-5

# Introduction

The Clouds and the Earth’s Radiant Energy System (CERES) is a key component of the Earth Observing System (EOS).  The CERES instrument provides radiometric measurements of the Earth’s atmosphere from three broadband channels: a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The CERES instruments are improved models of the Earth Radiation Budget Experiment (ERBE) scanner instruments, which operated from 1984 through 1990 on the National Aeronautics and Space Administration’s (NASA) Earth Radiation Budget Satellite (ERBS) and on the National Oceanic and Atmospheric Administration’s (NOAA) operational weather satellites NOAA-9 and NOAA-10.  The strategy of flying instruments on Sun-synchronous, polar orbiting satellites, such as NOAA-9 and NOAA-10, simultaneously with instruments on satellites that have precessing orbits in lower inclinations, such as ERBS, was successfully developed in ERBE to reduce time sampling errors.  CERES continues that strategy by flying instruments on the polar orbiting EOS platforms simultaneously with an instrument on the Tropical Rainfall Measuring Mission (TRMM) spacecraft, which has an orbital inclination of 35 degrees.  In addition, to reduce the uncertainty in data interpretation and to improve the consistency between the cloud parameters and the radiation fields, CERES includes cloud imager data and other atmospheric parameters.  The CERES instruments fly on the TRMM spacecraft, on the EOS-AM platforms and on the EOS-PM platforms.  The TRMM satellite carries one CERES instrument while the EOS satellites carry two CERES instruments, one operating in a fixed azimuth scanning mode and the other operating in a rotating azimuth scanning mode.

## Document Overview

This document, the CERES Release 3 Delivery Test Plan for the CERES Synoptic Surface and Atmospheric Radiation Budget (SARB) Subsystem (Subsystem 7.2), is part of the CERES Subsystem 7.2 Release 3 delivery package provided to the Langley Atmospheric Sciences Data Center (ASDC).  It provides a description of the CERES Synoptic SARB Subsystem Release 3 software, and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the results of executing the software.  A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B, and a description of the software and data files is contained in Appendix C.

The document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

Appendix B - Directory Structure Diagrams

Appendix C - File Description Tables

## Subsystem Overview

### CER7.2.1P1:  CERES Synoptic SARB Subsystem Main-Processor

The Product Generation Executive (PGE) CER7.2.1P1 processes the CERES Synoptic SARB Subsystem.  This PGE consists of a Main-Processor only.  The Synoptic SARB Subsystem Main-Processor computes vertical longwave, shortwave, and window channel flux profiles that span from the surface to the top of the Earth’s atmosphere for each CERES region within a 1-degree latitudinal zone for each hour of the month.  The primary output is the Synoptic Intermediate (SYNI) product, which contains vertical flux profile data for all CERES regions.  A secondary output is the Synoptic Subset (SYNS) product, which contains the TSIB and SYNI data for regions selected by Science Team members.  An ASCII Quality Control (QC) report is also produced with each run of the Subsystem.

The SYNI serves as input for CERES Subsystem 8.0, PGE CER8.1P1.

# Software and Data File Installation Procedures

This section describes how to install both the SARB library and the Subsystem 7.2 Synoptic SARB software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered files, properly defining environmental variables, and compiling the Synoptic SARB programs.

## Installation

Software/Data File Install Procedure:

The scripts, makefiles, and Process Control Files (PCF) in the Subsystem 7.2 delivery package expect the following environment variables, found in the $CERESENV script, to be defined:

PGSDIR	-	Directory for Toolkit libraries

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib

PGSINC	-	Pointer to the PGS Include file directory

PGSLIB	-	Directory which contains the SGI 64-bit Toolkit library file

PGSMSG	-	Directory which contains Toolkit and CERES

Status Message Files

HDFDIR	-	Pointer to the HDF home directory

The included makefiles for the Main-Processor (SARBlib and Synoptic SARB-only code) redefine the following environment variables:

FCOMP	-	Fortran 77 compilation flags (-O2 -c -64)

F90COMP	-	SGI Fortran 90 compilation flags (use the following options: -w -O2 -c -64)

Change directory to the directory where you plan to install the SARB Subsystems.  (The following instructions assume that the directory will be $CERESHOME.)

Uncompress and untar the SARB library and Synoptic SARB Subsystem files:

uncompress SynSARB_anc_R4-663.tar.Z

tar xf SynSARB_anc_R4-663.tar

uncompress SynSARB_src_R4-663.tar.Z

tar xf SynSARB_src_R4-663.tar

For testing on warlock:

uncompress SynSARB_dataexp_warlock_R4-663.tar.Z

tar xf SynSARB_dataexp_warlock_R4-663.tar

For testing on cluster:

uncompress SynSARB_dataexp_cluster_R4-663.tar.Z

tar xf SynSARB_dataexp_cluster_R4-663.tar

If the delivery is a full subsystem delivery then the files from previous deliveries should be removed using the $CERESHOME/SynSARB_OldFileRemove.csh script before the newly untarred files are copied into the /SSIT/CERES directory.  This script removes all of the old Synoptic SARB files except the ones in the $CERESHOME/sarb/data/
ancillary/static/sarbsyn directory and the source code files in the $CERESHOME/sarb/lib/src directory.

## Compilation

Software modules common to more than one SARB PGE are contained in the SARB library.  Since many modules and their associated error messages are shared between SARB subsystems, all error message files are stored in one directory.  The instructions for compiling these portions of the subsystem follow.  Instructions for generating the executable for PGE CER 7.2.1P1 are contained in Section 2.2.1.

NOTE: For full subsystem deliveries, use the following commands to compile all the software:

cd $CERESHOME/sarb/bin/sarbsyn

./compile_7.2.1.pl all

- The Status Message Files can be made by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./compile_7.2.1.pl smf

The SARB Library can be made by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./compile_7.2.1.pl lib

As this is a software library, no executable is generated.  The message “Warning: creating SARBlib_SYN.a” appears at the end of successful compilation.  The file, SARBlib_SYN.a, remains in the $CERESHOME/sarb/lib/src directory.

### Compiling PGE 7.2.1P1

- The Subsystem 7.2 Main-Processor executable can be made by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./compile_7.2.1.pl 7.2.1

The resulting executable, SynSARB_Drv.exe, is stored in the directory $CERESHOME/sarb/bin/sarbsyn.

Execute the following to compile the comparison software for the Main-Processor output:

cd $CERESHOME/sarb/bin/sarbsyn

./compile_7.2.1.pl test

The resulting executable, synicomp.exe, remains in the directory $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2.

# Test and Evaluation Procedures

This section provides general information on how to execute the Subsystem 7.2 PGE and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## PGE CER7.2.1P1--Main-Processor TRMM Test Case

### Stand Alone Test Procedures

The Main-Processor production script, runsarb, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF is created by first executing an ASCII file generator, ascii_gen_7.2.1P1.pl, and then executing the PCF generator, pcfgen_7.2.1P1.pl.

In the production environment, ascii_gen_7.2.1P1.pl and pcfgen_7.2.1P1.pl must be executed to create the PCF for each production run.  The ASCII file generator, ascii_gen_7.2.1P1.pl, requires one command line argument--the date/zone parameter, formatted as YYYYMMZxxx, where YYYY is the 4-digit year, MM is the 2-digit month, Z is a constant and xxx is the 3-digit latitudinal zone index.  The PCF generator, pcfgen_7.2.1P1.pl, is then executed using the newly created ASCII input file name as a command line argument.  Execute the production script by typing the script name, run_7.2.1.pl, followed by the name of the PCF generated by pcfgen_7.2.1P1.pl.

#### PCF Generation and Execution

- Copy the TSIB input file provided with this delivery, and link to the to the directories to which the PCF is pointing by typing:

cd $CERESHOME/sarb/data/input/sarbsyn

./CER7.2P1_InputFileMover.csh copyfiles

Generate the PCF for the TRMM test case:

Set the test case environment variables:

cd $CERESHOME/sarb/bin/sarbsyn

cp $CERESHOME/sarb/bin/sarb/ssit-main-env-TRMM.pl

$CERESHOME/sarb/bin/sarb/ssit-main-env.pl

setenv DATE 199807Z090

setenv INSTANCE TRMM-PFM-VIRS_SSIT_999999.199807Z090

Execute the ASCII file and PCF generators:

$CERESHOME/sarb/bin/sarbsyn/setup7.2.1.pl $DATE

The following PCF will be generated in $CERESHOME/sarb/rcf/pcf/sarbsyn:

CER7.2.1P1_PCF_$INSTANCE

Compare the PCF for the test case with the PCF provided in this delivery, using the diff command:

diff $CERESHOME/sarb/rcf/pcf/sarbsyn/CER7.2.1P1_PCF_$INSTANCE  $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_PCF_$INSTANCE

The only differences between the files should be in the directory paths where the tests were run.

Execute the test case by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./run_7.2.1.pl CER7.2.1P1_PCF_$INSTANCE

Four files will be created by the Main-Processor:

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met

##### Exit Codes

All CER7.2.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

##### Test Summary

Table 3-1.  Test Summary for PGE 7.2.1P1

|  | Warlock |
| --- | --- |
|  | PFM |
| Run Time | 8:10 hours |
| Memory | 69200 K |
| Required Disk Space | 6615 MB |

#### Metadata Evaluation

Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER7.2.1P1 has been executed.  Compare the metadata contained in these files with the expected contents of the files with the same names found in directory $CERESHOME/sarb/data/out_exp/data/sarbsyn, using the diff command.

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

diff $CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_SYNI_$INSTANCE.met

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE.met

#### Execution of Comparison Software for the Main-Processor

This section provides information on how to execute the comparison software for the Synoptic SARB Subsystem PGE CER7.2.1P1.

- Execute the following to compare the binary output from the Main-Processor Full-Hour Mode test case.  Note that this software does not compare the HDF version of the CRS.

cd $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2

./run_syni_compare.pl CER_SYNI_$INSTANCE

One file will be created:

$CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/CER_SYNI_$INSTANCE\_test_suites_results

NOTE:  The script run_syni_compare.pl removes any output files leftover from previous executions if they exist.  If a file the script is attempting to remove does not exist, a message is written to the screen.

Compare the Quality Control Report for the Mode against the expected output:

First, try to remove old output files IF they exist:

cd $CERESHOME/sarb/data/out_exp/data/sarbsyn

rm CER7.2.1P1_MainQC_diff

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE > $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_MainQC_diff

The only differences should be in the Processing Date information in the Quality Control Report Header.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.

#### Evaluation of Main-Processor Comparison Software Output

This section provides the procedure for evaluating the output from the Synoptic SARB Subsystem 7.2.

- Examine the comparison report files for the Main-Processor:

more $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/CER_SYNI_$INSTANCE\_test_suites_results

If all goes well, there will be a line indicating that no mismatches were found when comparing the results produced by the Langley ASDC with those produced by the CERES team.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.  Just perform Step 2.

E-mail the files $CERESHOME/sarb/test_suites/sarbsyn/mainss7_2/
CER_SYNI_$INSTANCE\_test_suites_results and $CERESHOME/sarb/ data/out_exp/sarbsyn/CER7.2.1P1_MainQC_diff to ceresdmt+sarb@larc.nasa.gov.

### Solutions to Possible Problems

- All output files must be deleted or renamed in order to run the production software properly again.  To use the provided script, type the following:

cd $CERESHOME/sarb/bin/sarbsyn

./rm_script_7.2.1P1.pl CER7.2.1P1_PCF_$INSTANCE

Environment variables, FCOMP and F90COMP, must be set to the following SGI compiler options for the Main-Processor:

setenv F90COMP ‘-w -O2 -c -64’

setenv FCOMP ‘-O2 -c -64’

A “No match” indicates there were no files to delete during execution of a script.  This message does not indicate a problem.

## PGE CER7.2.1P1--Main-Processor Terra Test Case

### Stand Alone Test Procedures

The Main-Processor production script, runsarb, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF is created by first executing an ASCII file generator, ascii_gen_7.2.1P1.pl, and then executing the PCF generator, pcfgen_7.2.1P1.pl.

In the production environment, ascii_gen_7.2.1P1.pl and pcfgen_7.2.1P1.pl must be executed to create the PCF for each production run.  The ASCII file generator, ascii_gen_7.2.1P1.pl, requires one command line argument--the date/zone parameter, formatted as YYYYMMZxxx, where YYYY is the 4-digit year, MM is the 2-digit month, Z is a constant and xxx is the 3-digit latitudinal zone index.  The PCF generator, pcfgen_7.2.1P1.pl, is then executed using the newly created ASCII input file name as a command line argument.  Execute the production script by typing the script name, run_7.2.1.pl, followed by the name of the PCF generated by pcfgen_7.2.1P1.pl.

#### PCF Generation and Execution

- Copy the TSIB input file provided with this delivery, and link to the to the directories to which the PCF is pointing by typing:

cd $CERESHOME/sarb/data/input/sarbsyn

./CER7.2P1_InputFileMover.csh copyfiles

Generate the PCF for the Terra test cases:

Set the test case environment variables:

For FM1:

cd $CERESHOME/sarb/bin/sarbsyn

cp $CERESHOME/sarb/bin/sarbsyn/ssit-main-env-Terra-FM1.pl $CERESHOME/sarb/bin/sarbsyn/ssit-main-env.pl

setenv DATE 200207Z054

setenv INSTANCE Terra-FM1-MODIS_SSIT_999999.200207Z054

For FM2:

cd $CERESHOME/sarb/bin/sarbsyn

cp $CERESHOME/sarb/bin/sarbsyn/ssit-main-env-Terra-FM2.pl $CERESHOME/sarb/bin/sarbsyn/ssit-main-env.pl

setenv DATE 200110Z054

setenv INSTANCE Terra-FM2-MODIS_SSIT_999999.200110Z054

Execute the ASCII file and PCF generators:

$CERESHOME/sarb/bin/sarbsyn/setup7.2.1.pl $DATE

The following PCF will be generated in $CERESHOME/sarb/rcf/pcf/sarbsyn:

CER7.2.1P1_PCF_$INSTANCE

Compare the PCF for the test case with the PCF provided in this delivery, using the diff command:

diff $CERESHOME/sarb/rcf/pcf/sarbsyn/CER7.2.1P1_PCF_$INSTANCE $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_PCF_$INSTANCE

The only differences between the files should be in the directory paths where the tests were run.

Execute the test case by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./run_7.2.1.pl CER7.2.1P1_PCF_$INSTANCE

Four files will be created by the Main-Processor:

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met

##### Exit Codes

All CER7.2.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

##### Test Summary

Table 3-2.  Test Summary for PGE 7.2.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM1 | FM2 | FM1 | FM2 |
| Run Time | 15:03 hours | 14:10 hours | 9:54 hours | 9:16 hours |
| Memory | 73256 K | 73088 K | 73088 K | 73088 K |
| Required Disk Space | 8603 MB | 8603 MB | 8603 MB | 8603 MB |

#### Metadata Evaluation

Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER7.2.1P1 has been executed.  Compare the metadata contained in these files with the expected contents of the files with the same names found in directory $CERESHOME/sarb/data/out_exp/data/sarbsyn, using the diff command.

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

diff $CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_SYNI_$INSTANCE.met

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE.met

#### Execution of Comparison Software for the Main-Processor

This section provides information on how to execute the comparison software for the Synoptic SARB Subsystem PGE CER7.2.1P1.

- Execute the following to compare the binary output from the Main-Processor Full-Hour Mode test case.  Note that this software does not compare the HDF version of the CRS.

cd $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2

./run_syni_compare.pl CER_SYNI_$INSTANCE

One file will be created:

$CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/CER_SYNI_$INSTANCE\_test_suites_results

NOTE:  The script run_syni_compare.pl removes any output files leftover from previous executions if they exist.  If a file the script is attempting to remove does not exist, a message is written to the screen.

Compare the Quality Control Report for the Mode against the expected output:

First, try to remove old output files IF they exist:

cd $CERESHOME/sarb/data/out_exp/data/sarbsyn

rm CER7.2.1P1_MainQC_diff

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE > $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_MainQC_diff

The only differences should be in the Processing Date information in the Quality Control Report Header.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.

#### Evaluation of Main-Processor Comparison Software Output

This section provides the procedure for evaluating the output from the Synoptic SARB Subsystem 7.2.

- Examine the comparison report files for the Main-Processor:

more $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/CER_SYNI_$INSTANCE\_test_suites_results

If all goes well, there will be a line indicating that no mismatches were found when comparing the results produced by the Langley ASDC with those produced by the CERES team.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.  Just perform Step 2.

E-mail the files $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/
CER_SYNI_$INSTANCE\_test_suites_results and $CERESHOME/sarb/data/
out_exp/data/sarbsyn/CER7.2.1P1_MainQC_diff to ceresdmt+sarb@larc.nasa.gov.

### Solutions to Possible Problems

- All output files must be deleted or renamed in order to run the production software properly again.  To use the provided script, type the following:

cd $CERESHOME/sarb/bin/sarbsyn

./rm_script_7.2.1P1.pl CER7.2.1P1_PCF_$INSTANCE

Environment variables, FCOMP and F90COMP, must be set to the following SGI compiler options for the Main-Processor:

setenv F90COMP ‘-w -O2 -c -64’

setenv FCOMP ‘-O2 -c -64’

A “No match” indicates there were no files to delete during execution of a script.  This message does not indicate a problem.

## PGE CER7.2.1P1--Main-Processor Aqua Test Case

### Stand Alone Test Procedures

The Main-Processor production script, runsarb, references a Process Control File (PCF) which contains the correct file names and paths for the test procedures.  The PCF is created by first executing an ASCII file generator, ascii_gen_7.2.1P1.pl, and then executing the PCF generator, pcfgen_7.2.1P1.pl.

In the production environment, ascii_gen_7.2.1P1.pl and pcfgen_7.2.1P1.pl must be executed to create the PCF for each production run.  The ASCII file generator, ascii_gen_7.2.1P1.pl, requires one command line argument--the date/zone parameter, formatted as YYYYMMZxxx, where YYYY is the 4-digit year, MM is the 2-digit month, Z is a constant and xxx is the 3-digit latitudinal zone index.  The PCF generator, pcfgen_7.2.1P1.pl, is then executed using the newly created ASCII input file name as a command line argument.  Execute the production script by typing the script name, run_7.2.1.pl, followed by the name of the PCF generated by pcfgen_7.2.1P1.pl.

#### PCF Generation and Execution

- Copy the TSIB input file provided with this delivery, and link to the to the directories to which the PCF is pointing by typing:

cd $CERESHOME/sarb/data/input/sarbsyn

./CER7.2P1_InputFileMover.csh copyfiles

Generate the PCF for the Aqua test cases:

Set the test case environment variables:

For FM3:

cd $CERESHOME/sarb/bin/sarbsyn

cp $CERESHOME/sarb/bin/sarbsyn/ssit-main-env-Aqua-FM3.pl $CERESHOME/sarb/bin/sarbsyn/ssit-main-env.pl

setenv DATE 200207Z054

setenv INSTANCE Aqua-FM3-MODIS_SSIT_999999.200207Z054

For FM4:

cd $CERESHOME/sarb/bin/sarbsyn

cp $CERESHOME/sarb/bin/sarbsyn/ssit-main-env-Aqua-FM4.pl $CERESHOME/sarb/bin/sarbsyn/ssit-main-env.pl

setenv DATE 200207Z054

setenv INSTANCE Aqua-FM4-MODIS_SSIT_999999.200207Z054

Execute the ASCII file and PCF generators:

$CERESHOME/sarb/bin/sarbsyn/setup7.2.1.pl $DATE

NOTE: The scripts may state that certain optional input files are missing.  If this happens, 	enter a y to tell the scripts to finish generating the PCF.

The following PCF will be generated in $CERESHOME/sarb/rcf/pcf/sarbsyn:

CER7.2.1P1_PCF_$INSTANCE

Compare the PCF for the test case with the PCF provided in this delivery, using the diff command:

diff $CERESHOME/sarb/rcf/pcf/sarbsyn/CER7.2.1P1_PCF_$INSTANCE $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_PCF_$INSTANCE

The only differences between the files should be in the directory paths where the tests were run.

Execute the test case by typing:

cd $CERESHOME/sarb/bin/sarbsyn

./run_7.2.1.pl CER7.2.1P1_PCF_$INSTANCE

Four files will be created by the Main-Processor:

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE

$CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE

$CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met

##### Exit Codes

All CER7.2.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

##### Test Summary

Table 3-3.  Test Summary for PGE 7.2.1P1

|  | Warlock | Linux Cluster |
| --- | --- | --- |
|  | FM3 | FM4 | FM3 | FM4 |
| Run Time | 10:08 hours | 15:10 hours | 9:57 hours | 10:10 hours |
| Memory | 73256 K | 73088 K | 73088 K | 73088 K |
| Required Disk Space | 8603 MB | 8603 MB | 8603 MB | 8603 MB |

#### Metadata Evaluation

Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER7.2.1P1 has been executed.  Compare the metadata contained in these files with the expected contents of the files with the same names found in directory $CERESHOME/sarb/data/out_exp/data/sarbsyn, using the diff command.

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

diff $CERESHOME/sarb/data/out_comp/data/sarbsyn/CER_SYNI_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_SYNI_$INSTANCE.met

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE.met $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE.met

#### Execution of Comparison Software for the Main-Processor

This section provides information on how to execute the comparison software for the Synoptic SARB Subsystem PGE CER7.2.1P1.

- Execute the following to compare the binary output from the Main-Processor Full-Hour Mode test case.  Note that this software does not compare the HDF version of the CRS.

cd $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2

./run_syni_compare.pl CER_SYNI_$INSTANCE

One file will be created:

$CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/CER_SYNI_$INSTANCE\_test_suites_results

NOTE:  The script run_syni_compare.pl removes any output files leftover from previous executions if they exist.  If a file the script is attempting to remove does not exist, a message is written to the screen.

Compare the Quality Control Report for the Mode against the expected output:

First, try to remove old output files IF they exist:

cd $CERESHOME/sarb/data/out_exp/data/sarbsyn

rm CER7.2.1P1_MainQC_diff

diff $CERESHOME/sarb/data/out_comp/qa_reports/sarbsyn/CER_KQCR_$INSTANCE $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER_KQCR_$INSTANCE > $CERESHOME/sarb/data/out_exp/data/sarbsyn/CER7.2.1P1_MainQC_diff

The only differences should be in the Processing Date information in the Quality Control Report Header.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.

#### Evaluation of Main-Processor Comparison Software Output

This section provides the procedure for evaluating the output from the Synoptic SARB Subsystem 7.2.

- Examine the comparison report files for the Main-Processor:

more $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/
CER_SYNI_$INSTANCE\_test_suites_results

If all goes well, there will be a line indicating that no mismatches were found when comparing the results produced by the Langley ASDC with those produced by the CERES team.  Some mismatches might occur due to computer precision, thus, there is no need for immediate alarm.  Just perform Step 2.

E-mail the files $CERESHOME/sarb/test_suites/sarbsyn/src/mainss7_2/
CER_SYNI_$INSTANCE\_test_suites_results and $CERESHOME/sarb/data/
out_exp/data/sarbsyn/CER7.2.1P1_MainQC_diff to ceresdmt+sarb@larc.nasa.gov.

### Solutions to Possible Problems

- All output files must be deleted or renamed in order to run the production software properly again.  To use the provided script, type the following:

cd $CERESHOME/sarb/bin/sarbsyn

./rm_script_7.2.1P1.pl CER7.2.1P1_PCF_$INSTANCE

Environment variables, FCOMP and F90COMP, must be set to the following SGI compiler options for the Main-Processor:

setenv F90COMP ‘-w -O2 -c -64’

setenv FCOMP ‘-O2 -c -64’

A “No match” indicates there were no files to delete during execution of a script.  This message does not indicate a problem.

Acronyms and Abbreviations

ASDC	Atmospheric Sciences Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

CRS	Clouds and Radiation Swath

CRSB	Clouds and Radiation Swath Binary

DAAC	Distributed Active Archive Center

DRIVTAB	Derivative Table

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FOV	Field-of-View

HDF	Hierarchical Data Format

LaTIS	Langley TRMM Information System

MCF	Metadata Control Files

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executive

QC	Quality Control

SARB	Surface and Atmospheric Radiation Budget

SCF	Science Computing Facility

SMF	Status Message Facility

SYNI	Synoptic Intermediate Product

TRMM	Tropical Rainfall Measuring Mission

TSIB	Time Space Interpolate Binary Product

Directory Structure Diagrams

Figure B-1.  Synoptic SARB Directory Structure

Figure B-1.  Synoptic SARB Directory Structure

Figure B-1.  Synoptic SARB Directory Structure

File Description Tables

Production Scripts and Executables

The following scripts must be moved to the production environment.

Table C.1-1.  Production Scripts

| File Name | Format | Description |
| --- | --- | --- |
| ascii_gen_7.2.1P1.pl | ASCII | Perl script which creates the PCF generator’s ASCII file needed by the Main-Processor |
| pcfgen_7.2.1P1.pl | ASCII | Perl script which creates the PCF for the Main-Processor |
| run_7.2.1.pl | ASCII | Perl script which executes the Main-Processor |

Table C.1-2.  Executables

| File Name | Format | Description |
| --- | --- | --- |
| SynSARB_Drv.exe1 | Binary | Main-Processor executable |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Processing Control Files (PCF), Metadata Control Files (MCF) and Status Message Files (SMF)

The Process Control Files are not included in the Software Delivery Package.  They will be created by the PCF generator scripts.

Table C.2-1.  Metadata Control Files

| File Name | Format | Description |
| --- | --- | --- |
| mcf_sarbsynqc | ODL | MCF for Binary QC Report for Main-Processor |
| mcf_sarbsyn | ODL | MCF for Binary CRS file for Main-Processor |

Table C.2-2.  Process Control Files

| File Name | Format | Description |
| --- | --- | --- |
| CER7.2.1P1_PCF_TRMM-PFM-VIRS_SSIT_000000.199807Z0901 | ASCII | Process Control File for Main-Processor |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

| Table C.2-3. Status Message Files (SMF) |
| --- |
| File Name | Format | Directory | Description |
| ANCINIT_25725.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257251 | ASCII | PGS_message/sarb | Toolkit Message File |
| FLSALUT_25724.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257241 | ASCII | PGS_message/sarb | Toolkit Message File |
| GFDLAER_25716.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257161 | ASCII | PGS_message/sarb | Toolkit Message File |
| HCMOCNALB_225723.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_2257231 | ASCII | PGS_message/sarb | Toolkit Message File |
| IGBPUTIL_25721.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257211 | ASCII | PGS_message/sarb | Toolkit Message File |
| INITSARB_25701.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257011 | ASCII | PGS_message/sarb | Toolkit Message File |
| MSFCALBIO_25722.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257221 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_INGEST_25702.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257021 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SIGMALOAD_25703.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257031 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_TUNEDRV_25704.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257041 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_FLXRANGE_25705.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257051 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_FLMODEL_25706.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257061 | ASCII | PGS_message/sarb | Toolkit Message File |
| SARBMETA_25726.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257261 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_MODISAERRD_25751.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_25751 | ASCII | PGS_message/sarb | Toolkit Message File |
| SARBIOUTIL_25750.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_25750 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SFCALBCALC_25707.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257071 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SFCALBINGEST_25708.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257081 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_DERIVLOAD_25709.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257091 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_WRAPSARB_25710.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257101 | ASCII | PGS_message/sarb | Toolkit Message File |
| INITSYN_26003.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26003 | ASCII | PGS_message/sarb | Toolkit Message File |
| REGDRV_26005.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26005 | ASCII | PGS_message/sarb | Toolkit Message File |
| TSIRET_26004.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26004 | ASCII | PGS_message/sarb | Toolkit Message File |
| WRAPSYN_26006.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26006 | ASCII | PGS_message/sarb | Toolkit Message File |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Ancillary Input Data

The Synoptic SARB Subsystem accesses several ancillary input data files.  Many of these files are shared with the Instantaneous SARB Subsystem PGE CER5.1P1, and are thus located in either the $CERESHOME/sarb/data/ancillary/static/sarb or the $CERESHOME/sarb/data/ancillary/dynamic/sarb directory.  Ancillary input data files only accessed by the Synoptic SARB Subsystem PGE CER7.2.1P1 are located in the $CERESHOME/sarb/data/ancillary/static/sarbsyn directory.

| Table C.3-1. Ancillary Input Data |
| --- |
| File Name | Format | Description | Static/Dynamic |
| SS5_DrivTab_19990315 | Binary | Derivative tables | Static |
| IGBP_Ver3.0 | Binary | IGBP map | Static |
| SigTab_Synoptic_20040730 | ASCII | Sigma tables | Static |
| CollinsAer_1998TRMM_Ver3.0 | Binary | Collins-based assimilated aerosol climatology | Static |
| ControFile_20070920 | ASCII | Drives selection of data sources based on specified record conditions | Static |
| SS5_ZJin_OcnAlb_20011218 | Binary | Coefficients for Zhonghai Jin surface albedo over ocean retrieval | Static |
| SS5_GFDLAerClim_200006 | Binary | Geophysical Fluid Dynamics Laboratory (GFDL) Aerosol climatology | Static |
| flsa0404_lut.2s.coef | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa3_lut.4s.coef_19991215 | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa4_lut.2s.coef_19991215 | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa200508c.fubin.tab | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| SAH.v5.yyyymm (in sahmaps) | Binary | Surface albedo history look up tables | Static |
| MATCH_TERRA_AOTS_CLIM_ MODIS.mm (in match_aot) | Binary | Match climatology data for Terra processing | Static |
| MATCH_TERRA_AOTS_MODIS.yyyymmdd (in match_aot/match_aots_yyyymm/) | Binary | Match aerosol data for Terra processing | Static |
| MATCH_TERRA_VERTICAL_MODIS. yyyymmdd (in match_vert/match_verts_yyyymm/) | Binary | Match aerosol profile data for Terra processing | Static |
| chlor_clim.mm (in data/ancillary/static/ sarbsyn/chlor_clim) | Binary | Seasonal climatology of chlorophyll used as an input to the Z. Jin Ocean spectral surface albedo | Static |
| indxs_nesds.dat (in data/ancillary/ static/sarbsyn/iceage) | Binary | Monthly chlorophyll based on seawifs data | Static |
| seawifs_chlor.yyyymm (in data/ ancillary/static/sarbsyn/seawifs) | Binary | Monthly chlorophyll based on seawifs data | Static |
| zjin.ice.bin.1 (in data/ancillary/static/ sarbsyn/zjin) | Binary | Ice look up tables of Zhonhai Jin's spectral surface albedo | Static |
| zjin.snow.bin.1 (in data/ancillary/static/ sarbsyn/zjin) | Binary | Snow look up tables of Zhonhai Jin's spectral surface albedo | Static |
| zjin_ocean_feb04.bin (in data/ancillary/ static/sarbsyn/zjin) | Binary | Ocean look up tables of Zhonhai Jin's spectral surface albedo | Static |
| Sitelist.txt | ASCII | List of sites included in Subset SYN product | Static |

Output Temporary Data Files (Production Results)

Table C.4-1.  Output Temporary Data Files

| File Name | Format | Description |
| --- | --- | --- |
| CER7.2.1P1_PCFin_TRMM-PFM-VIRS_SSIT_000000.199807Z0901 | ASCII | ASCII file created by the ASCII file generator to be used to produce PCF generator used by both the Main-Processor and the HDF Post-Processor for the Full-Hour Mode. |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

# Text boxes

browse

QA Reports

metadata

data

out_exp

(Expected test results)

qa_reports

out_comp

(Runtime test results)

ancillary

errlogs

scr

input

sarbsyn

Directory

data

src

sarbsyn

test_suites

sarbsyn

PCFgen

sarb-

sarbsyn

mcf

sarb-

sarbsyn

Italicized names are dependent on delivered software

Directory

BREAKDOWN OF THE SYNOPTIC SARB DIRECTORY STRUCTURE

pcf

rcf

data

runlogs

browse

src

mainss7_2

mainss7_2

BREAKDOWN OF A DATA DIRECTORY

src

sarbsyn

smf

[include]

(Global)

rcf*

test_suites*

Names in brackets [ ] are optional files or directories

Italicized names are dependent on delivered software

*Breakdown of subdirectories shown on following pages

sarbsyn

sarbsyn*

[lib]

(Working Group)

bin

data*

src

Directory

sarb

BREAKDOWN OF THE SYNOPTIC SARB DIRECTORY STRUCTURE

metadata

sarbsyn

sarbsyn

sarbsyn

sarbsyn

sarbsyn

dynamic

static

Italicized names are dependent on delivered software

sarbsyn