NATURAL RESOURCES CONSERVATION SERVICE

Idaho

CONSTRUCTION SPECIFICATIONS

FOR

SUSPENSION FENCE

_________________________________		_____________________________________

(Owner/Operator)					(Project Title)

GENERAL

Installation shall be in accordance with an approved plan.  Details of construction shown on the drawings but not include herein are considered as part of these specifications.  Construction activities shall be in accordance with applicable OSHA regulations.

When planning fences in know sage grouse habitat, consult with biologists from Idaho Department of Fish and Game regarding fence placement and lek location. Consultation is required under the Memorandum of Understanding between NRCS and Idaho F&G dated 1990.

Prior to construction the fence lines shall be cleared of any possible obstruction that would hinder the fence placement and operation.

The soil surface along the fence line shall be relatively smooth such that placement of the bottom fencing member does not exceed the maximum fence member to soil surface spacing specified.

The fence materials shall have an expected life of 10 years with routine maintenance.  All wood materials except Orange Osage, Western Red Cedar, Juniper and Black Locust that have contact with the soil shall be treated with an EPA-registered wood preservative.  Wood posts shall be treated from the butt end of the post to distance of at least 30 inches for line posts and 36 inches for all corner, gate and brace posts.  Refer to Table 1 for the life expectancy of treated versus untreated wood posts.

MATERIALS

Wood Posts.  Line posts shall have a minimum top diameter of 3 inches and shall be a minimum of 6 feet in length.  Corner, gate and brace posts shall have a minimum top diameter of 6 inches and shall be a minimum of 8 feet in length.  Braces shall have a minimum top diameter of 4 inches and shall be a minimum of 6 feet in length.

Table 1.  Life Expectancy of Untreated and Treated Fence Posts (Years)

| Kind of Wood | Un-treated | Pressure Treated | Hot and Cold Bath | Cold Soak |
| --- | --- | --- | --- | --- |
| Western Red Cedar | 12-15 | 20-25 | 20-25 | - |
| Lodgepole & Ponderosa Pine | 2-4 | 20-25 | 15-20 | 10-20 |
| Aspen or Cottonwood | 1-3 | 15-20 | 10-15 | 5-10 |
| Douglas Fir & Western Hemlock | 3-6 | 20-35 | 15-25 | 10-20 |

Steel Posts.  Steel line posts shall be the “T”, “U” or “Y” type with a welded or riveted anchor plate near the bottom (minimum 18 inches square area) and have suitable corrugations, knobs, studs or grooves for fastening the wire.  Line posts shall weigh at least 1.33 pounds per linear foot of length and shall be a minimum of 5.5 feet long.

Steel Pipe Posts.  Steel pipe corner, gate or brace posts shall be a minimum diameter of 2 inches, Schedule 40 (2.375-inch O.D.) and at least 7 feet long.  Bracing shall be a minimum of 1-1/2 inch nominal diameter, Schedule 40 pipe.  Brace fittings and clamps shall be galvanized.

Angle Section Posts.  Angle section posts shall have nominal sectional dimensions of 2.5 by 2.5 by 0.25 inches thick and at least 7 feet in length.  Braces shall be of the same size dimensions as corner and gate posts and shall be a minimum of 6 feet in length.

Barbed Wire.  Barbed wire shall be composed of two strands of 12.5 gauge zinc coated wire wrapped around each other, with 2-point 14 gauge barbs spaced no more than 5 inches apart conforming to ASTM A 121.

Smooth Wire.  Smooth wire shall be a single steel wire of 9 gauge or heavier, two wrapped strands of 12.5 gauge or heavier wire.  Wire shall have a minimum tensile strength of 45,000 psi.

Wire Panel Fasteners.  Staples shall be 9 gauge or heavier and have a minimum length of 1.5 inches, except 1.0 inch staples are allowed n very hard woods.  Fasteners for use with steel posts shall be 12 gauge or heavier zinc coated wire.

Stays.  Wire stays shall be 9.5 gauge or heavier, zinc coated, twisted wire.  The length shall be at least two inches longer than the distance between the top and the bottom strands of the fence.  Wood stays shall be sound, straight pieces at least 2 inches in diameter.

INSTALLATION

The fence shall be reasonably straight and shall not deviate more than 12 inches between any corner and gate or line brace assembly.

Post Depth.  Line steel posts shall be set a minimum depth of 1.5 feet and wood line posts shall be set to a minimum depth of 2 feet, unless otherwise specified.  Gate, corner and brace posts shall be set to a minimum depth of 3 feet, unless otherwise specified.  Steel pipe and angle section posts shall be embedded in a 12-inch circular or square concrete pier, except when set in firm rock.

Suspension fences should be constructed with approximately a 3-inch sag in the wires between posts to permit maximum sway of the fence.

Post Spacing.  The maximum post spacing interval shall not exceed 100 feet.

Line Bracing.  Line brace assemblies shall be located at all corners, gates and abrupt changes in vertical topography (generally considered as 15 degrees).  On straight reaches of fencing line braces shall be installed at a spacing of no more than 1300 feet.

Wire Spacing.  Wire spacings are as follows, unless otherwise specified:

Table 2. Barbed Wire Fence

| Fence Type | Spacing Measured from Groundline (inches) |
| --- | --- |
| 3-wire | 16 | 28 | 40 |  |  |
| 4-wire | 14 | 22 | 30 | 42 |  |
| 5-wire | 5 | 12 | 20 | 30 | 42 |

Note: Where the movement of antelope is a concern, the minimum height of the bottom wire shall be 16 inches from the groundline and the wire may be smooth.  Antelope crossings shall be provided if sheep-tight fences are built.

Wire Fasteners.  Staples shall be driven diagonally into the wood grain of the post.  Space shall be left between the post and the staple to allow movement of the wire.  Fasteners on steel posts shall be snug enough to prevent vertical movement of the wire on the post.

Stays.  The maximum distance between stays and/or line, corner, gate or brace posts shall not exceed 15 feet.

Drainageways.  In crossing drainageways or depressions a weight or deadman anchor shall be fastened to the fence to maintain the required spacing interval or additional wires shall be added to maintain the required minimum wire height from the groundline.

WILDLIFE FENCES

In areas commonly used by wildlife, fencing should be designed to facilitate passage of wildlife species without injury. The bottom wire will be smooth and a minimum of 16” from the ground to allow for the passage of antelope and fawn deer. Spacing between the top two wires will be 12” to reduce instances of entanglement (see Table 4).  If practical use a top wood rail instead of barbed wire where elk are a concern. Replace woven wire with barbed or smooth wire when possible, otherwise refer to Table 5.

When fencing in areas where sage grouse are present do not install fences closer than 0.6 miles to a lek location. In areas where leks are present improve visibility of wires by using reflective tagging.

Table 4 - Wildlife Barbed Wire

| Wire Description | Spacing Measured From Groundline (inches) |
| --- | --- |
| 3 -wire | 16 | 26 | 38 |  |
| 4 -wire | 16 | 21 | 26 | 38 |

Table 5 – Wildlife Woven wire

| Wire Description | Spacing Measured From Groundline (inches) |
| --- | --- |
| 26-inch woven | Ground | 26 | 26 wire | 38 wire |
| 32-inch woven | Ground | no wire |  |  |

ADDITIONAL SPECIFICATIONS