| Project Number: |  |  | Project Manager: |  |
| --- | --- | --- | --- | --- |
| Project Name: |  |  | Lead Designer: |  |
| Design Speed: |  | ADT: |  | Date: |  |
| Posted Speed: |  | Location: |  |

Please place a mark in the box next to all the Roadside Design “Features” appropriate for the project.

|  | Feature | Guideline | Remarks/Justifications |
| --- | --- | --- | --- |
|  | CLEAR ZONE *See Table 3.1 and 3.2 and Section 3.3 of the RDG. **See Table 2.1 in the FLH Barrier Guide for Low Volume and Low Speed Roads for barrier warrants. The FLH Barrier Guide is applicable for FL projects with existing traffic volumes below 2000 and/or speeds 45 mph or lower. | Clear Zone Range: Preferred: Used: |  |
|  | ROADSIDE OBSTACLES including: Signs Roadway lighting Traffic signals Railroad warning devices Motorist-aid call boxes Mailboxes Utility poles Trees and other vegetation Bollards | Remove obstacle. Redesign the obstacle so it can safely traversed. Relocate the obstacle to the point where it is less likely to be struck. Reduce impact severity by using an appropriate breakaway device. Shield the obstacle with a longitudinal traffic barrier designed for redirection and/or using a crash cushion. Delineate the obstacle if the above alternatives are not appropriate. |  |
|  | EMBANKMENT SLOPES Recoverable Parallel Slope Non-recoverable Parallel Slope *See example C of Section 3.3.4 of the RDG to calculate Clear Runout Area. | Typical Slope: Any Locations w/ Steeper Slopes: Slopes of 4:1 (Horizontal:Vertical) or flatter are desirable. Slopes from 3:1 to 4:1 are considered non-recoverable. Clear Runout Area: Required: Used: |  |
|  | ROADSIDE CHANNEL *See Table 3.5 and 3.6 of the RDG for preferred foreslopes and backslopes. | Channel Front Slope: Required: Used: Channel Back Slope: Required: Used: |  |
|  | CURB *See Section 3.4.1 of the RDG. | Mountable Curb height: Non-Mountable Curb height: |  |
|  | DRAINAGE INLETS including: Curb and Grate Curb opening (including entry to waterway) Grate inlet Slotted Drain | Curb opening length: Grate inlet style: Is the grate bicycle safe: |  |
|  | PIPE CULVERT END TREATMENTS; Headwalls and End Sections *See Section 3.4.2 of the RDG for more details. | Are Headwalls and/or End Sections within the Clear Zone? (If “Yes”, then explain how it was mitigated.) Possibly extend pipes so that Headwalls and End Sections are past the Clear Zone. Single structures and end treatments wider than 3 ft (1 m) can be made traversable by using using bar grates. |  |
|  | ROADSIDE BARRIERS *Chapter 5 of the RDG *See web site: for approved barriers and end treatments. | Roadside Barrier warranted (Section 5.2)? Barrier type used: End Treatment: Shy Line Offset (Table 5.4): Required: Used: Slope in front of barrier: Required: Used: Slope behind barrier (Section 5.6.2.2): Required: Used: Flare Rate (Table 5.6): Required: Used: Length of Need: *See Figures 5.19 thru 5.27 and Table 5.7 Required: Used: |  |
|  | MEDIAN BARRIERS *Chapter 6 of the RDG *See web site: for approved barriers and end treatments. Also Refer to Section 6.4.1 and 6.5 of the RDG for Standard Sections. | Roadside Barrier warranted (Figure 6.1)? Barrier type used: End Treatment: Shy Line Offset (Table 5.4): Required: Used: Slope in front of barrier: Required: Used: Slope behind barrier (Section 5.6.2.2): Required: Used: Flare Rate (Table 5.6): Required: Used: Length of Need: *See Figures 5.19 thru 5.27 and Table 5.7 Required: Used: |  |
|  | BRIDGE RAILINGS & TRANSITIONS *Chapter 7 of the RDG *Virtually all structures require some type of railing. See web site: for approved bridge railings and end treatments. | Railing type used: End Treatment: Slope in front of barrier: Required: Used: Slope behind barrier (Section 5.6.2.2): Required: Used: Flare Rate (Table 5.6): Required: Used: Length of Need: *See Figures 5.19 thru 5.27 and Table 5.7 Required: Used: |  |

*Please note that RDG refers to the AASHTO Roadside Design Guide