October 25, 2007

The Honorable Nicole R. Nason

Administrator

National Highway Traffic Safety Administration

1200 New Jersey Ave., SE

West Building, 4th Floor

Washington, DC 20590

Attn: Docket No. NHTSA-29134

Petition for Reconsideration

The National Truck Equipment Association submits this Petition for Reconsideration on the Final Rule issued in the September 11, 2007 Federal Register by the National Highway Traffic Safety Administration (NHTSA) on federal motor vehicle safety standard – Occupant Protection in Interior Impact; Side Impact Protection; Fuel System Integrity; Electric-Powered Vehicles: Electrolyte Spillage and Electrical Shock Protection; Side Impact Phase-In Reporting Requirements.

The NTEA requests that NHTSA reconsider the scope of this amended regulation and exempt multi-stage produced vehicles such as specialized work trucks from the new requirements of this regulation. It will not be possible for the chassis manufacturers to develop compliance strategies for this regulation that would allow multi-stage manufacturers to continue producing the range of diversified work trucks demanded by the marketplace.

In the event this amended regulation continues to apply to multi-stage produced vehicles, the NTEA requests that NHTSA consider amending the phased-in effective dates such that the effective date for multi-stage produced vehicles with a gross vehicle weight rating greater than 8,500 is September 1, 2014 (one year later than the effective date for single stage produced vehicles).

Work Trucks

The NTEA requests that NHTSA exempt vehicles built in two or more stages from these new requirements. The end users of multi-stage produced vehicles such as work trucks require an extensive variety of completions and alterations in order that the vehicle efficiently performs its intended task (including bulkheads and partitions to protect the driver from loose cargo in the back of the vehicle).  The design of a vehicle produced by a

multi-stage manufacturer or alterer will almost certainly affect the performance of original equipment manufacturers' (OEMs) side airbags systems (side airbags, curtains, sensing systems, and interior and structural components).

NHTSA's traditional view has been that multi-stage manufactures will be able to pass through the certification of the chassis manufacturers. The more complex the chassis manufacturers’ compliance strategies for their own products become, however, the less likely it becomes that multi-stage manufacturers will be able to pass-through their certification.  In the case of this final rule, the chassis manufacturers will typically be installing side airbag systems. As NHTSA is aware, these systems are highly complex.

The side airbag system is just that, a system consisting of airbags, curtains, sensors, and interior and structural components. Each variation from that system as developed by the chassis manufacturer would require individual compliance certification. While we are not privy to the precise compliance plans of the chassis manufacturers, it is clear that it will not be possible for the chassis manufacturers to provide a generic compliance envelope covering any significant portion of the vehicle configurations produced by today’s work truck industry. If NHTSA wishes to confirm our assumptions the Agency could directly query the chassis manufacturers as to how they expect this final rule will affect their pass-through certification plans for vehicles built in more than one stage or altered prior to the first retail sale of the vehicle.

In order to preserve the specialized vehicles required by today’s commercial and vocational users, the NTEA requests that NHTSA exempt from these new requirements vehicles produced in more than one stage such as specialized work trucks.

Effective Dates

In the Final Rule NHTSA allows an additional year of lead-time for alterers, manufacturers of vehicles produced in more than one stage, and manufacturers of vehicles with a gross vehicle weight rating greater than 8,500 pounds - until September 1, 2013 to meet the upgraded pole and barrier test requirements.

NHTSA has recognized that it is appropriate to allow additional lead-time for multi-stage manufacturers as these manufacturers cannot begin planning their compliance strategies until the chassis manufacturers have validated the single stage version of the chassis. The Final Rule provides multi-stage vehicle manufacturers an additional year for compliance beyond that for single stage manufacturers with regard to vehicles 8,500 pounds GVWR and less. It appears that NHTSA then also granted the same additional year of lead-time to all manufacturers of vehicles over 8,500 pounds GVWR.

According to NHTSA, “…this final rule provides more lead time to meet the pole test requirements to manufacturers of vehicles with a GVWR greater than 3,855 kg (8,500 lb) than proposed in the NPRM. These vehicles need more lead time because they have never been regulated under FMVSS No. 214's dynamic requirements and are not subject to the industry's voluntary commitment to install side air bags. Because these vehicles may need more redesign of the vehicle side structure, interior trim, and/or optimization of dynamically deploying head/side protection systems than light vehicles, this final rule does not subject these vehicles to the pole test requirements until September 1, 2013.”

We understand and support NHTSA’s decisions to allow additional lead-time for vehicles above 8,500 pounds GVWR – they have not been previously subject to the dynamic testing requirements of FMVSS 214 and therefore may require more significant redesigns. For the same reason and those reasons NHTSA has recognized many times in the past, the NTEA requests that if they remain subject to this rule, vehicles in that same weight category (above 8,500 pounds GVWR) produced by multi-stage manufacturers not be required to comply with the amended regulations until September 1, 2014. It would not be possible for multi-stage manufacturers of these larger vehicles to comply on the same date as the chassis manufacturers of those vehicles.

Sincerely,

Michael Kastner

Director of Government Relations

NTEA Washington, DC Office