# MEMORANDUM

# To:           The Record

Subject:  Characterization of Petroleum Refining Waste and Possible Gasification Scenarios

In support of the final rule:  Regulation of Oil-Bearing Hazardous Secondary Materials From the Petroleum Refining Industry Processed in a Gasification System to Produce Synthesis Gas Fuel (Tier 3, RIN#2050-AE78) additional analysis was conducted on a proposed condition requiring gasification residuals to meet the Universal Treatment Standards for six selected metals (antimony, arsenic, chromium, lead, nickel, and vanadium).

Background

In the proposed rule, we requested comment on a condition to the exclusion that would establish leachate limits (i.e., Universal Treatment Standards (UTS)) for six toxic metals in the gasification co-products and residuals prior to any placement on the land.  We originally considered this condition to ensure that co-products and residues generated by the gasification process that were to be placed on the land did not contain toxic metals with a potential for leaching greater than allowed by the requirements of the Land Disposal Restrictions (LDR) program.  (See 67 FR at 13691, March 25, 2002.)  In developing this possible condition, we were influenced by the condition established for hazardous waste derived products that are used in a manner constituting disposal (see 40 CFR 266.20).  These materials are required to meet the appropriate LDR treatment standards prior to use as products applied to the land (e.g., fertilizers).  We reasoned, in the proposal, that requiring this same condition for co-products and residuals would ensure legitimate fuel manufacturing by applying the same land disposal provisions to the co-products and residuals that would have existed had the material (i.e., the listed waste) not been excluded from the definition of solid waste.  Further, we reasoned that this proposed condition would be needed to assure that the gasification system is operated for the purpose claimed – conversion of organic matter in the oil-bearing hazardous secondary material into fuels (or intermediates), while removing metals from raw synthesis gas and trapping those metals in an inert matrix.  It was reasoned that the levels in the proposed condition (UTS levels) would provide a means of quantifying this premise.

We received comments that both supported and opposed this condition (See the Response to Comment Document for a complete presentation and discussion of all the comments on this condition).  Commenters opposed to the condition stated that there was no need to impose the UTS requirements beyond what the regulations (e.g., 40 CFR 261.4(a)(12)(i)) already required for residues generated from the petroleum refining process (i.e., the characteristic test).  Commenters argued that EPA had provided no rationale basis for imposing the additional UTS requirements.

In response to these comments, the Agency set about reexamining the merits of this condition.  This began with a more detailed analysis of the characterization data for petroleum refining wastes collected as part of the LDR program.

Characterization Data for Listed Wastes Identified as Oil-Bearing Hazardous Secondary Materials

We reviewed data presented in several Best Demonstrated Available Technology (BDAT) Background Documents for petroleum refining wastes to get a better understanding of the total concentration levels of these metals in different petroleum refining wastes.   Concentration data were analyzed for nine listed petroleum refining wastes identified as coming under the category of “oil-bearing hazardous secondary materials” (Tables 1 and 2).  Next, we look at whether these six metals constituents were part of the LDR treatment standards for the listed oil-bearing secondary materials that would be affected by the rule (Table 3).

Table 1 – ANALYSIS OF WASTE CHARACTERISTIC DATA

| Constituents | K048 | K049 | K050 | K051 | K052 | K169 | K170 | K171 | K172 | F037 K051* | F038 K048* |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Water % | 81 | 50 | 44 | 70-91.4 | 18 | 19.2 | 11.4 | 1.3 | 3.6 | --- | --- |
| Oil and grease% | 12 | 39 | 8 | 4.5-13 | 13 | 34.3 | 29.5 | 3.6 | 22 | --- | --- |
| TOC % | --- | --- | --- | --- | --- | 23 | 29 | 4.0 | 7.0 | --- | --- |
| Organic liquid % | --- | --- | --- | --- | --- | 31.8 | 25.7 | 0.5 | 1.0 | --- | --- |
| Solids, dirt, sand % | 86 | 10 | 47 | 16 | 68 | 54.5 | 69.7 | 98.8 | 97 | --- | --- |
| BTU content | --- | 150 | 1500 | --- | --- | 7281 | 5935 | 1244 | 1684 | --- | --- |
| BDAT constituent % | <1 | <1 | <1 | <1 | <1 | <1 | <1 | <1 | <1 | --- | --- |
| Nickel (ppm) Total concentration | 0.025-16 | 9.2-86 | 61-170 | 0.25-150.4 | 97.2-392 | 15-380 | 62-300 | 66-25,000 | 8-14,000 | 12-240 | <0.16-95 |
| Nickel (TCLP) | --- | --- | --- | --- | --- | --- | 0.2-0.52 | 0.91-310 | 0.73-67 | --- | --- |
| Vanadium (ppm) Total concentration | 0.05-460 | 2.5-60 | 0.7-50 | 1-350 | 1.0-9.8 | 5-1,400 | 91-430 | 10-33,000 | 25-31,000 | 50-<90 | 50-<90 |
| Vanadium (TCLP) | --- | --- | --- | --- | --- | --- | --- | 0.25-6.6 | 0.25-3.3 | --- | --- |

## Table 2 – CONCENTRATION RANGES OF SELECTED METALS IN PETROLEUM REFINERY LISTED WASTE (mg/kg) (1.)

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| K048 | 4.4 - 7 | 0.05 - 10.5 | 0.04 - 3435 | 0.05 - 1250 | 0.025 – 16 | 0.05 – 460 |
| K049 | BDL – 19** | <2.2 – 30*** | 28.9 - 1400 | 21.95 - 3900 | 9.2 – 86 | 2.5 – 60 |
| K050 | --- | 10.2 -11 | 11 – 1600 | 0.5 – 1100 | 61 – 170 | 0.7 – 50 |
| K051 | 9 - 18 | 0.1 – 32 | 0.1 - 6790 | 0.25 - 2480 | 0.25 - 150.4 | 1 – 350 |
| K052 | 111 | 63 – 525 | 1.0 - 504 | 11 - 5800 | 97.2 – 392 | 1.0 - 9.8 |
| K169 | <6 - 15 | 5.7 – 32 | 9.7 - 310 | 44 - 870 | 15 – 380 | 5 – 1400 |
| K170 | <6 - 940 | <1 - 4.7 | 8.4 - 34 | 17 - 47 | 62 – 300 | 91 – 430 |
| F037 | Not Reported | ND – 61 | 12 - 2020 | 22 - 4570 | 12.4 – 740 | Not Reported |
| F038 | Not Reported | 0.34 - 109.4 | 2.5 - 2990 | <1 - 3900 | <0.16 – 95 | Not Reported |
| Composite Range | 4.4 - 940 | 0.05 – 525 | 0.04 - 6790 | 0.05 - 5800 | 0.025 – 740 | 0.05 – 1400 |
| Petroleum Coke **** | --- | 3.53 | 1.3 | 1.5 | 370 | 1500 |

1.  USEPA.  Best Demonstrated Available Technology Background Document for K048, K049, K051, K052.  August 1988; USEPA.  Best demonstrated Available Technology Background Document for F037 and F038. 1992.  USEPA.  Best Demonstrated Available Technology Background Document for K169-K171.  1998.

2.  If ND or BDL was reported, the next largest value was used in determining the range.

## 3.  If the concentration was reported as a “less than” , the reported value was used without the “less than” designation.

4.  Nickel and Vanadium concentration values are from: Gasification of Petcoke Using E-Gas Technology at Wabash River, 2000.  Three concentration values for petroleum coke were presented, the highest value was selected for these calculations.

Table 3 – REGULATED BDAT CONSITUTENTS

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| TC Levels (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | (not a UHC) |
| UTS(mg/L TCLP) | 1.15 | 5.0 | 0.60 | 0.75 | 11 | 1.6 |
| K048 - Dissolved air flotation (DAF) float |  |  | X |  | X |  |
| K049 - Slop oil emulsion solids |  |  | X |  | X |  |
| K050 - Heat exchange bundle cleaning sludge |  |  | X |  | X |  |
| K051 - API separator sludge |  |  | X |  | X |  |
| K052 - Tank bottoms (leaded) |  |  | X |  | X |  |
| K169 - Crude oil tank sediment |  |  |  |  |  |  |
| K170 - Clarified slurry oil sediment |  |  |  |  |  |  |
| K171 - Spent hydrotreating catalyst |  | X |  |  | X | X |
| K172 - Spent hydrorefining catalyst | X | X |  |  | X | X |
| F037 - Primary oil/water/solids separator sludge |  |  | X |  | X |  |
| F038 - Secondary oil/water/solids separator sludge |  |  | X |  | X |  |

1)  Original treatment standard for Nickel (K048-K052) was calculated at 0.048 mg/L TCLP based on one data point;

2)  Arsenic treatment standard is the same as TC level; and

3)  Antimony, Arsenic and Vanadium are regulated in catalysts only (catalysts may not be suitable gasification feed).

Analysis of Petroleum Coke and Other Gasification Feedstock

We also reviewed chemical characterization data on petroleum coke as well as other petroleum refining materials that could be used as feedstock for gasification units (Tables 4, 5, and 6).  Refinery feedstock suitable for gasification are often off-gas streams and residual oils such as vacuum resid, visbreaker tar, and deasphalter pitch.  These residuals are often referred to generically as “heavy oils”.

The ultimate analysis of petroleum coke showed: 1) Water content ranges from 7.0% to 12.0%; 2) Carbon content ranges from 77.7% to 81.1%; 3) BTU value ranges from 13,360 to 14,282; 4) The concentrations of Nickel and Vanadium (BDAT constituents) in petroleum coke are often in higher concentrations that in the hazardous waste, except for catalysts K171 and K172.

Table 4 – PETROLEUM COKE CHARACTERIZATION DATA

|  | 1997 | 1999 | 2000 |
| --- | --- | --- | --- |
| Moisture % | 7.0 | 12.0 | 7.8 |
| Ash % | 0.3 | 0.4 | 0.6 |
| Volatiles % | 12.4 | 11.2 | 10.5 |
| Fixed Carbon% | 80.4 | 77.7 | 81.1 |
| Sulfur % | 5.2 | 5.6 | 5.7 |
| Metals in Fuel |  |  |  |
| Nickel, ppm | 210 | 290 | 370 |
| Vanadium, ppm | 430 | 1500 | 890 |
| Heating value (BTU/lb) | 14,282 | 13,360 | 14,026 |

Petroleum Coke Analysis:  (Gasification of Petcoke Using E-Gas Technology at Wabash River 2000)

Table 5 – CHARACTERIZATION DATA FOR VARIOUS FEEDSTOCK INTENDED FOR PETROLEUM REFINING GASIFICATION

|  | Units | Vacuum Resid | Visbreaker Tar | Asphalt | Petcoke |
| --- | --- | --- | --- | --- | --- |
| Ultimate Analysis |  |  |  |  |  |
| C | wt/wt | 84.9% | 86.1% | 85.1% | 88.6% |
| H |  | 10.4% | 10.4% | 9.1% | 2.8% |
| N |  | 0.5% | 0.6% | 0.7% | 1.1% |
| S |  | 4.2% | 2.4% | 5.1% | 7.3% |
| O |  |  | 0.5% |  | 0.0% |
| Ash |  | 0.0% |  | 0.1% | 0.2% |
| Total | wt/wt | 100.0% | 100.0% | 100.0% | 100.0% |
| H2/C ratio | mol/mol | 0.727 | 0.720 | 0.640 | 0.188 |
| Density |  |  |  |  |  |
| Specific Gravity | 60/60 | 1.028 | 1.008 | 1.070 | 0.863 |
| API Gravity | API | 6.2 | 8.88 | 0.8 | --- |
| Heating Values |  |  |  |  |  |
| HHV(dry) | M BTU/lb | 17.72 | 18.6 | 17.28 | 14.85 |
| LHV(dry) | M BTU/lb | 16.77 | 17.6 | 16.45 | 14.48 |

Reference:  Refinery Technology Profiles:  Gasification and Supporting Technologies, U.S. Department of Energy, National Energy Technology Laboratory, Energy Information Administration, June 2003

Table 6 – ANALYSIS OF EL DORADO GASIFIER FEEDSTOCK

|  | Petroleum Coke | Recycled Filter Cake (1.) | Fluxing Additive | Acid Soluble Oil | API Separator Bottoms | Primary Sludge | Phenolic Residue |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | D001,D018 | K051 (2.) | F037, F038 (3.) | K022 (4.) |
| Moisture (as received),wt% | 5-10 | 50 | 5 | 1.4 | 20-75 | 20 | 0.8 |
| Heating Value (dry), BTU/lb | 15,400 | 13,000 | 0 | 18,900 | 6,300 | <1,000 | 15,700 |
| Ultimate Analysis (dry) Wt% |  |  |  |  |  |  |  |
| Carbon | 89.5 | 88.9 | --- | 86.4 | 32.8 | 0-5 | 82.7 |
| Hydrogen | 3.9 | 0.1 | --- | 12.0 | 4.3 | --- | 7.4 |
| Nitrogen | 1.3 | 0.7 | --- | 0.02 | 0.5 | --- | 0.1 |
| Sulfur | 4.7 | 2.4 | --- | 0.3 | 2.7 | --- | 0.01 |
| Ash | 0.4 | 7.9 | 100 | 0.4 | 57.6 | 95-100 | 0.2 |

1.  This is the unconverted carbon from the gasifier recovered in a gravity settler and dewatered by rotary vacuum filtration.  It’s non-hazardous and non-leachable through testing.  Although it has a high BTU value no buyer has been found, it’s another low value item for the refinery and recycled back into gasifier.

2.  The refinery’s delayed coker is also capable of processing API separator bottoms.

3.  The gasifier was not designed to handle the entire refinery production of primary sludge.  The design intent was to gasify all the available API separator bottoms and then gasify as much sludge as possible.  The refinery’s delayed coker is also capable of processing primary sludge.

4.  Distillation bottom tars from the production of phenol/acetone from cumene.

Experience with Low Value Feed Gasification at the El Dorado, Kansas Refinery by Gary DelGrego, Texaco Power and Gasification.  Presented at the 1999 Gasification Technologies Conference.

Results of Biennial Report Analysis

Generation Rates

Potential generation rates of oil-bearing hazardous secondary materials were derived from the 2003 Biennial Report, using the following waste codes: K048-K052, K169-K172, F037 and F038 representing oil-bearing hazardous secondary materials.  The BRS reported 324,371 tons of oil-bearing hazardous secondary materials generated by 153 sites (SIC 2811).  The average generation rate was calculated at 2,314 tons/year, with a maximum generation rate of 76,582 tons/year and a minimum of less than 1 ton/year.  Over 82 facilities generate over 10,000 tons/year

Management

144,012 tons of oil-bearing hazardous material was managed by material recovery (primarily metal catalysts); 25,457 tons went to energy recovery (cement kilns, BTU >5000); 92,658 tons to incineration; 17,495 tons to other treatment (sludge treatment, stabilization, macro-encapsulation); 23,352 tons to disposal (land treatment, landfill, and deepwell injection); and 21,396 tons went to other management (unknown management, fuel blending, storage/bulking/transfer).

Possible Gasification Scenarios Utilizing Oil-bearing Hazardous Secondary Material With Petroleum Coke

Based on all this information, the following possible refining scenarios utilizing gasification were developed, demonstrating that oil-bearing hazardous secondary materials (low-value fuels) could supplement the petroleum coke feed on a very limited basis.  It should be noted however, that to date, no information has been discovered that would suggest that this type of activity is being pursued.

As an example, consider a 1000 TPD gasification unit being employed at a petroleum refinery producing 1000 TPD petroleum coke.  The facility also produces 2000 TPY of oil-bearing hazardous secondary material.  If the gasification system is fed the oil-bearing hazardous secondary material at 10% of the total feed (900 TPD petroleum coke, 100 TPD supplemental feed).  The supplemental feed will be depleted in 20 days.  If you reduce the feed to 5%, the supplemental feed is depleted in 40 days, and 1%, the supplemental feed is depleted in 200 days.

As a second example, consider a 2000 TPD gasification unit.  The petroleum refinery produces 1800 TPD of petroleum coke, and 10,000 TPY of oil-bearing hazardous secondary material.  If the gasification system is fed the oil-bearing hazardous secondary material at a rate of 10% of the total feed (1800 TPD petcoke; 200 TPD supplemental) the supplemental feed will be depleted in 50 days.  Reduce the feed to 5%, it is depleted in 100 days; and reduce to 1%, the feed is depleted in 500 days.

These examples suggest that oil-bearing hazardous secondary material can be introduced, on a limited basis, into a gasification system with petroleum coke.

The following table is derived from the Gasification Technology Council’s website and presents information on various gasification units operating in the United States.   The information presented on the future gasifier planned for the BP facility in Carson City, California was found on the BP website.

Table 6 – GASIFICATION SYSTEMS USING PETROLEUM COKE AND/OR REFINERY WASTE AS FEED

| Facility | Feed | Status(2004) |
| --- | --- | --- |
| Frontier El Dorado, Kansas | 150.60 mt/d petcoke 13.6 mt/d refinery waste 7,000 mm BTU/d | Operating |
| ExxonMobil Chemical Baytown, Texas | 1,000 mt/d deasphalter pitch | Operating |
| Coffeyville Resources Refining and Marketing Coffeyville, Kansas | 1,100 mt/d petcoke | Operating |
| Eastman Chemical Kingsport, Tennessee | 1,225 t/d coal | Operating |
| Wabash West Terre Haute, Indiana | 2,000 mt/d petcoke | Operating |
| Premcor Wilmington, Delaware | 2,100 mt/d petcoke | Operating |
| Vanguard Louisiana | 2,700 mt/d petcoke | Startup 2008 |
| BP Carson, California | 4,500 TPD petcoke | Startup 2011 Cost $1 billion |
| CITGO Lake Charles, Louisiana | 7,000 mt/d petcoke | Startup 2009 |
| Great Plains Beulah, North Dakota | 14,000 t/d coal 50.00 t/d refinery waste | Operating |

From:  www.gasification.org and www.bp.com

Future Trends in Petroleum Refining Gasification

Information from the DOE report, Refinery Technology Profiles: Gasification and Supporting Technologies. US DOE, National Energy Technology Laboratory.  June 2003, suggests that growth in petroleum refinery gasification will most likely be driven by future supply and demand of petroleum coke.  (Coking capacity has grown by 60% over last decade, trend is expected to continue but at a slower rate.).  There are 40 refineries (out of 153) within the U.S. (located in California, Texas, and Louisiana) that produce sufficient quantities of petroleum coke(>1000 TPD) to be considered candidates for the addition of petroleum coke gasification at the petroleum refinery.  These 40 facilities account for 98% of total volume of petroleum coke generated in the U.S.  Simple economic payback estimated at 4-5 years. Market penetration rate of possibly one plant every two years would not seem unreasonable.  This would result in 7 to 9 plants by 2010 and as many as 17 plants by 2025.  Gasification plant capacities of 1,000 to 2,000 TPD typical, however the two planned facilities are over 5,000 TPD (Louisiana and Texas).  This coincides with the amount of petroleum coke currently generated at the facilities.

Both waste characterization data and data on waste generation rates suggest that industry would probably not build a gasification unit dedicated to the gasification of oil-bearing hazardous secondary materials.  However, smaller gasification units are still being explored for possible application at petroleum refineries, and as part of this analysis have been evaluated.  Given, existing information and current gasification patterns, that the most probable gasification scenario, however, is that a petroleum refinery will build a gasification unit for petroleum coke gasification with oil-bearing hazardous secondary material possibly used as a supplemental feed.  As suggested in the DOE report, gasifiers will most likely be built at petroleum refineries that generate >1000 TPD of petroleum coke.  There are approximately 40 refineries located in California, Texas, and Louisiana that generate that quantity of petroleum coke.  Available information on existing gasification units suggest that if oil-bearing hazardous secondary material is used as a supplemental feedstock, it could make-up between 0.1 to 10% of the total feed (This range is derived by using the lowest (Dakota Gasification) input, on a percentage basis of oil-bearing hazardous secondary material and highest (El Dorado) input of oil-bearing hazardous secondary material in combination with petroleum coke or coal to a gasification unit.)  Total BDAT constituents (metals and organics) in listed refinery wastes account for less than 1% total composition of the waste. Petroleum coke will dominate residual composition.

The DOE report indicates that no new gasification systems will come on-line until 2008 and possibly only 3 by 2011, and that these gasification systems will be designed for processing petroleum coke.  Oil-bearing secondary materials (low value fuels) could supplement the petroleum coke feed on a very limited basis. However, no information has been presented to suggest this is what will occur.   (Note:  These predictions appear to be optimistic based on current information available to the Agency).

We developed various scenarios for feeding petroleum coke to a gasification system to estimate TCLP concentrations of selected metals in the gasification bottoms.  As part of this analysis we made several assumptions:  1) The concentration of selected metals in the secondary feed is given as a “composite range” of the listed petroleum refining wastes K048-K052, K169-K170 and F037-F038;  2)  171 and K172 wastes are catalysts from petroleum refining operations and are not used as part of the “composite range” because of its low carbon and high metal content; and 3) 100% of the metals will partition to the gasification bottoms.  With these assumptions we developed several gasification scenarios.

Scenario 1:  A 2000 MTD gasification system feeding 100% petroleum coke.

Scenario 2:  A 2000 MTD gasification system feeding 90% petroleum coke and 10% of a refining waste composite using a lower bound and upper bound analysis for selected metal concentrations in the composite petroleum refining waste.  This represents a gasification scenario with a maximum input of oil-bearing hazardous secondary material in combination with petroleum coke.

Scenario 3:  A 20 MTD gasification system feeding 100% of a refining waste composite using a lower bound, mean of the composite range and upper bound analysis for selected metal concentrations.

Scenarios 4 and 5:  A 20 MTD gasification system feeding 100% of a refining waste composite using a lower bound, mean of the composite range  and upper bound analysis for selected metal concentrations, where 50% and 80% of the feed partitions to the gasifier bottoms.

## Selected Gasification Scenarios:

Scenario 1:

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 2000 MTD Gasifier Feeding 100% Petroleum Coke

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.60 | 0.75 | 11 | 1.6 |
| Concentration in Petroleum Coke (mg/kg) | --- | 3.53 | 1.3 | 1.5 | 370 | 1500 |
| Total Concentration of Metal in Bottoms (mg/kg) | --- | 35.3 | 13 | 15 | 3700 | 15000 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | --- | 1.76 | 0.65 | 0.75 | 185 | 750 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | --- | 0.0353 | 0.013 | 0.015 | 3.7 | 15 |

## Sample Calculation – Method 1 (Arsenic):

2000 MT (3.53/10E6) = 0.00706 MT of Arsenic

0.00706 MT of Arsenic/200 MT of bottoms = 0.0000353 x 10E6 = 35.3 mg/kg Arsenic in bottoms

(35.3)(.05) = 1.76 mg/L TCLP

(35.3)(.001) = 0.0353 mg/L TCLP

Sample Calculation – Method 2 (Arsenic):

(2000 MT)(1000 kg/MT) = 2,000,000 kg of petroleum coke

(2,000,000 kg)(3.53mg Arsenic/kg) = 7,060,000 mg Arsenic

7,060,000 mg Arsenic/(200 MT)(1000kg/MT) = 35.3 mg/kg Arsenic in gasifier bottoms

(35.3)(.05) = 1.76 mg/L TCLP

(35.3)(.001) = 0.0353 mg/L TCLP

## Scenario 2:

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 2000 MTD Gasifier Feeding 90% Petroleum Coke/10% Petroleum Waste Composite

LOWER BOUND

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.60 | 0.75 | 11 | 1.6 |
| Lower Bound Petroleum Waste Composite (mg/kg) | 4.4 | 0.05 | 0.04 | 0.05 | 0.025 | 0.05 |
| Concentration in Petroleum Coke (mg/kg) | --- | 3.53 | 1.3 | 1.5 | 370 | 1500 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | --- | 31.8 | 11.54 | 13.55 | 3330.025 | 13500 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | --- | 1.59 | 0.577 | 0.6775 | 166.50 | 675.0 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | --- | 0.0318 | 0.01154 | 0.01355 | 3.33 | 13.5 |

UPPER BOUND

| Upper Bound Petroleum Waste Composite(mg/kg) | 940 | 525 | 6790 | 5800 | 740 | 1400 |
| --- | --- | --- | --- | --- | --- | --- |
| Concentration in Petroleum Coke (mg/kg) | --- | 3.53 | 1.3 | 1.5 | 370 | 1500 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | --- | 556.77 | 6801.7 | 5813.5 | 4070 | 14900 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | --- | 27.84 | 340.1 | 290.7 | 203.5 | 745 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | --- | 0.557 | 6.8 | 5.81 | 4.1 | 14.9 |

Sample Calculation – Method 1 (Arsenic):

(1800 MT of petcoke)(3.53/10E6) + (200 MT of secondary material) (0.05/10E6) = 0.006354 + .00000005 = .00635405/200tons x 10E6 = 31.77 = 31.8 mg/kg Arsenic in bottoms

Application of 20:1 ratio from TCLP (multiply by 0.05):  31.77 x .05 = 31.8 x 0.05 = 1.59 mg/L TCLP

Application of 1000:1 ratio from TCLP (multiply by 0.001):  31.77 x .001 = 31.8 x 0.001 = 0.0318 mg/L TCLP

Sample Calculation – Method 2 (Arsenic)

(1800 MT of petroleum coke)(1000kg/MT) = 1.8 x 10E6 kg petroleum coke     (200 MT of secondary material)(1000kg/MT) = 2.0 x 10E5 kg secondary material.

(1.8 x 10E6 kg petroleum coke)(3.53 mg Arsenic in petroleum coke/kg) = 6.3 54x 10E6 mg Arsenic

(2.0 x 10E5 kg secondary material)(0.05 mg Arsenic/kg secondary material) = 1 x 10E4 mg Arsenic

6.354 x 10E6 mg Arsenic +.01 x 10 E6 mg Arsenic = 6.364 x 10E6 mg Arsenic

200 MT of gasifier bottoms

6.364 x 10E6/(200MT)(1000 kg/MT) = 31.8 mg/kg Arsenic in bottoms.

Application of 20:1 ratio from TCLP (multiply by 0.05):  31.8 x .05 = 1.59 mg/L TCLP

Application of 1000:1 ratio from TCLP (multiply by 0.001):  31.8 x 0.001 = 0.0318 mg/L TCLP

## Scenario 3:

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 20 MTD Gasifier Feeding 100% Petroleum Waste With 10% of Mass to Gasifier Bottoms

LOWER BOUND

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.6 | 0.75 | 11 | 1.6 |
| Lower Bound Waste Composite (mg/kg) | 4.4 | 0.05 | 0.04 | 0.05 | 0.025 | 0.05 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 44 | 0.5 | 0.4 | 0.5 | 0.25 | 0.5 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 2.2 | 0.025 | 0.02 | 0.025 | 0.0125 | 0.025 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.044 | 0.0005 | 0.0004 | 0.0005 | 0.00025 | 0.0005 |

UPPER BOUND

| Upper Bound Waste Composite (mg/kg) | 940 | 525 | 6790 | 5800 | 740 | 1400 |
| --- | --- | --- | --- | --- | --- | --- |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 9400 | 5250 | 67900 | 58000 | 7400 | 14000 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 470 | 262.5 | 3395 | 2900 | 370 | 700 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 9.4 | 5.25 | 67.9 | 58 | 7.4 | 14 |

Sample Calculation (Antimony):

(20 MT)(1000kg/MT) = 20,000 kg waste

(20,000 kg waste)(4.4 mg/kg) =88000 mg Antimony

In 20 MTD gasifiers 90% mass goes to syngas; 10% to bottoms with 100% of metals

Therefore; 2 MTD of bottoms generated.

88000 mg Antimony/(2 MT)(1000kg/MT) = 44 mg/kg of Antimony

Apply 20:1 TCLP ratio (multiply by 0.05) = 2.2 mg/L TCLP

Apply 1000:1 (multiply by 0.001) = 0.044 mg/L TCLP

## Scenario 4

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 20 MTD Gasifier Feeding 100% Petroleum Waste With 50% of Mass to Gasifier Bottoms

LOWER BOUND

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.6 | 0.75 | 11 | 1.6 |
| Lower Bound Waste Composite (mg/kg) | 4.4 | 0.05 | 0.04 | 0.05 | 0.025 | 0.05 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 8.8 | 0.1 | 0.08 | 0.1 | 0.05 | 0.1 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 0.44 | 0.005 | 0.004 | 0.005 | 0.0025 | 0.005 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.0088 | 0.0001 | 0.00008 | 0.0001 | 0.00005 | 0.0001 |

MEAN OF THE COMPOSITE RANGE

| Mean of the Composite Range (mg/kg) | 472.2 | 262.5 | 3395 | 290 | 370 | 700 |
| --- | --- | --- | --- | --- | --- | --- |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 944 | 525 | 6790 | 580 | 740 | 1400 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 47.22 | 26.25 | 339.5 | 29 | 37 | 70 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.944 | 0.525 | 6.79 | 0.58 | 0.74 | 1.4 |

UPPER BOUND

| Upper Bound Waste Composite (mg/kg) | 940 | 525 | 6790 | 5800 | 740 | 1400 |
| --- | --- | --- | --- | --- | --- | --- |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 1880 | 1050 | 13580 | 11600 | 1480 | 2800 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 94 | 52.5 | 679 | 580 | 74 | 140 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 1.88 | 1.05 | 13.58 | 11.6 | 1.48 | 2.8 |

Sample Calculation (Antimony):

(20 MT)(1000kg/MT) = 20,000 kg waste

(20,000 kg waste)(940 mg/kg) =18,800,000 mg Antimony

In 20 MTD gasifiers 50% mass goes to syngas; 50% to bottoms with 100% of metals

Therefore; 10 MTD of bottoms generated.

18,800,000 mg Antimony/(10 MT)(1000kg/MT) = 1880 mg/kg of Antimony

Apply 20:1 TCLP ratio (multiply by 0.05) = 94 mg/L TCLP;   Apply 1000:1 (multiply by 0.001) =  1.88 mg/L TCLP

Scenario 5

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 20 MTD Gasifier Feeding 100% Petroleum Waste With 80% of Mass to Gasifier Bottoms

LOWER BOUND

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.6 | 0.75 | 11 | 1.6 |
| Lower Bound Waste Composite (mg/kg) | 4.4 | 0.05 | 0.04 | 0.05 | 0.025 | 0.05 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 5.5 | 0.0625 | 0.05 | 0.0625 | 0.03125 | 0.0625 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 0.275 | 0.0031 | 0.0025 | 0.0031 | 0.0016 | 0.0031 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.0055 | 0.0000625 | 0.00005 | 0.0000625 | 0.000031 | 0.000625 |

MEAN OF THE COMPOSITE RANGE

| Mean of the Composite Range (mg/kg) | 472.2 | 262.5 | 3395 | 290 | 370 | 700 |
| --- | --- | --- | --- | --- | --- | --- |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 590.25 | 328.125 | 4243.75 | 362.5 | 462.5 | 875 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 29.5 | 16.4 | 212.2 | 18.12 | 23.12 | 43.75 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.59 | 0.328 | 4.24 | 0.3625 | 0.462 | 0.875 |

UPPER BOUND

| Upper Bound Waste Composite (mg/kg) | 940 | 525 | 6790 | 5800 | 740 | 1400 |
| --- | --- | --- | --- | --- | --- | --- |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 1175 | 656.25 | 8487.5 | 7250 | 925 | 1750 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 58.75 | 32.81 | 424.37 | 362.5 | 46.25 | 87.5 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 1.175 | 0.656 | 8.48 | 7.25 | 0.925 | 1.750 |

Sample Calculation (Antimony):

(20 MT)(1000kg/MT) = 20,000 kg waste

(20,000 kg waste)(940 mg/kg) =18,800,000 mg Antimony

In 20 MTD gasifiers 20% mass goes to syngas; 80% to bottoms with 100% of metals

Therefore; 16 MTD of bottoms generated.

18,800,000 mg Antimony/(16 MT)(1000kg/MT) = 1175 mg/kg of Antimony

Apply 20:1 TCLP ratio (multiply by 0.05) = 58.75 mg/L TCLP; Apply 1000:1 (multiply by 0.001) =  1.175 mg/L TCLP

Analysis of Gasification Scenarios

Nickel (370 mg/kg) and Vanadium (1500mg/kg) concentrations found in petroleum coke will dominate TCLP results in 2000 MTD gasification scenarios.  The upper bound scenarios for Chromium and Lead are based on characterization data not reflective of overall reduction in the use of these metals throughout the refinery industry.   Under LDRs, only Chromium and Nickel would be regulated as “constituents of concern” in these wastes.

Two gasification scenarios were developed that represented “extremes” for gasification activities that could be conducted at petroleum refineries.  The first scenario was a large gasification system ( i.e., 2000 MT/day) utilizing  a feedstock comprised of 90% petroleum coke and 10% oil-bearing hazardous secondary material (this is consistent with the largest feedrate for oil-bearing hazardous secondary material gasified at a petroleum refinery) and a small gasifer dedicated to processing 100% of oil-bearing hazardous secondary material.  As a result of this analysis, we concluded, that gasification residuals would achieve the UTS levels for all metals, except for vanadium in one scenario (2000 MT/day) and chromium(20 MT/day) in the other.  With regard to chromium the concentration level was below the characteristic level, but above the UTS level.  As for vanadium, it was determined that petroleum coke (a product) contributed most of the vanadium to the gasifier, and that vanadium concentrations in the gasification residuals would not be affected when feeding petroleum coke alone or in combination with oil-bearing hazardous secondary materials.

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 2000 MTD Gasifier Feeding 90% Petroleum Coke/10% Petroleum Waste Composite

LOWER BOUND

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.60 | 0.75 | 11 | 1.6 |
| Lower Bound Petroleum Waste Composite (mg/kg) | 4.4 | 0.05 | 0.04 | 0.05 | 0.025 | 0.05 |
| Concentration in Petroleum Coke (mg/kg) | --- | 3.53 | 1.3 | 1.5 | 370 | 1500 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | --- | 31.8 | 11.54 | 13.55 | 3330.025 | 13500 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | --- | 1.59 | 0.577 | 0.6775 | 166.50 | 675.0 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by 0.001) | --- | 0.0318 | 0.01154 | 0.01355 | 3.33 | 13.5 |

As generated, the gasifier bottoms will not be characteristic and will meet the UTS for all metals except vanadium.

## TCLP Concentration Estimates for Selected Metals in Gasifier Bottoms

## 20 MTD Gasifier Feeding 100% Petroleum Waste With 80% of Mass to Gasifier Bottoms

MEAN OF THE COMPOSITE RANGE

|  | Antimony | Arsenic | Chromium | Lead | Nickel | Vanadium |
| --- | --- | --- | --- | --- | --- | --- |
| Characteristic Level (mg/L TCLP) | --- | 5.0 | 5.0 | 5.0 | --- | --- |
| UTS (mg/L TCLP) | 1.15 | 5.0 | 0.6 | 0.75 | 11 | 1.6 |
| Mean of the Composite Range (mg/kg) | 472.2 | 262.5 | 3395 | 290 | 370 | 700 |
| Total Concentration of Metal in Gasifier Bottoms (mg/kg) | 590.25 | 328.125 | 4243.75 | 362.5 | 462.5 | 875 |
| TCLP Concentration in Gasifier Bottoms Using 20:1 Ratio (mg/L) (multiply by 0.05) | 29.5 | 16.4 | 212.2 | 18.12 | 23.12 | 43.75 |
| TCLP Concentration in Gasifier Bottoms Using 1000:1 Ratio (mg/L) (multiply by .001) | 0.59 | 0.328 | 4.24 | 0.3625 | 0.462 | 0.875 |

As generated, the gasifier bottoms will not be characteristic and will meet the UTS for all metals except chromium.

Although this analysis showed chromium levels above the UTS in one scenario, the Agency is convinced that chromium concentrations in oil-bearing hazardous secondary materials have decreased from the levels found in our characterization studies, which were written in 1988, 1992, and 1998, and therefore will be lower than what we used in our analysis (i. e., the gasification residuals will have concentration levels below the UTS.)  This is based on information in the preamble for the August 1998 listing rule promulgating the exclusion at 40 CFR 261.4(a)(12)(i) that indicates that chromium levels in these hazardous secondary materials will decrease due to a prohibition on chromium-based water treatment chemicals in industrial cooling towers as a result of Clean Air Act requirements, see 450 CFR Part Subpart Q (On September 8, 1994 (59 FR 46339), EPA issued a final MACT rule that eliminated the use of chromium-based treatment chemicals and subsequently chromium compound emissions from industrial cooling towers.)

# Footnotes

USEPA.  Best Demonstrated Available Technology Background Document for K048, K049, K051, K052.  August 1988; USEPA.  Best demonstrated Available Technology Background Document for F037 and F038. 1992.  USEPA.  Best Demonstrated Available Technology Background Document for K169-K171.  1998.

Petroleum Listing (1998):  “EPA also believes that the lead and chromium in the secondary materials should decline with time.  This is due to overall reduction in the use of these metals throughout the refinery (e.g., leaded gasoline is no longer produced on a wide-scale and chromium-based water treatment chemicals are no longer used in industrial cooling towers, as a result of Clean Air Act requirements, see 40 CFR Part 63, Subpart Q).”