Organic Geochemistry Data of Alaska

Data Base Structure Documentation

11/1/99

By Charles N. Threlkeld and J. David King

U. S. Geological Survey

Office of Energy and Marine Geology

Branch of Petroleum Geology

Box 25046 MS 977 DFC

Denver, Colorado 80225

Any use of trade, product or firm names in this publication is for descriptive purposes only and does not imply endorsement by the U. S. Government.

CONTENTS

Abstract	3

Introduction	4

Relational Data Base Tables, Structures and Definitions	6

Data Table Structures and Definitions	8

Encoding Schemes	31

Appendix A - Definitions of Some Commonly Used Terms	40

Appendix B - Manufacturers of Products and Services Mentioned	41

Abstract

The U. S. Geological Survey Energy Resources Team’s Organic Geochemistry Laboratory is a research laboratory devoted to the investigation of the origin and occurrence of organic fossil fuels. Although it is not a service laboratory, many of the analytical results from the laboratory could prove useful in future petroleum geological and geochemical studies. In order to archive these results, the USGS developed an Alaskan Organic Geochemical Data Base (AOGDB) in 1978 to house the data from not only the USGS’ involvement in the project, but also the data accumulated from a host of sub-contracting laboratories.  The accumulated data resided in a flat text file entitled “PGS” and was maintained by Petroleum Information Corporation.  The information herein is a breakout of tables from the master flat file to form the AOGDB in a relational data base format.  Additional information can be obtained in Geology and Exploration of the National Petroleum Reserve in Alaska, 1974-1982, USGS Professional Paper 1399, pgs 478-481 and 545-549.

Introduction

The data base management software used throughout this circular is MicroRim Corporation's RBase for DOS, a data base package designed for use on IBM XT or AT or equivalent computers with MS-DOS or equivalent disk operating systems.	The AOGDB consists of RBase TABLES which have subsequently been converted to Microsoft Access tables. Each TABLE is organized into vertical columns and horizontal rows of information. Each row represents one sample; the columns within each row represents specific information about the sample. There is only one driving TABLE:

HEADER_PGS	Contains generic sample information

There can be any number of DATA tables, one for each analytical technique that produces data in some numeric format. The USGS AOGDB has 19 DATA tables + one legend table that attempts to correlate tabular information back to the original PGS notations.  Additionally, 5 other tables exist from which a number of attributes were transferred to form portions of the Header_PGS table.  The tables below are the break-out product of the PGS flat file.

HDSP_13c_40_PGS Stable Carbon, Hydrogen,& Sulfur Isotopes of Headspace gas

WHLOIL_13C_65_PGS	Stable Carbon Isotopes of Whole Oils

# SAT_ARO_13C_39_PGS	Stable Carbon Isotopes of Saturate and Aromatic Fractions

COMMENTS_PGS	Sample/Analytical Comments

ELEM_36_PGS	Weight %Carbon, Nitrogen, Hydrogen and Ash

ELEM_37_PGS		Weight % Oxygen, Sulfur, and Ash

FRAC_2930_PGS	% Saturates, Aromatics, and Non-Hydrocarbon Fractions

CANGAS_8081_PGS	Standard Chemical Analyses of Gas

GASRNG_23_PGS	C5–C8 Gasoline Range Components by Gas Chromatography

GC_3162_PGS	C7–C35 Paraffin Range Components by Gas Chromatography

HEADER_PGS	Location, Lithology, Age, and Rock Unit information

ISOT_38_PGS	34S and 15N Stable isotopes of Saturates and Ashpaltines

Legend_PGS	Correlation to PGS analytical tables (Contained Herein)

MASTER_PGS	Every code in the datafile + the Comments_pgs comments field

RKEV_41_PGS	Standard Rock-Eval data

SPGR_60_PGS		Specific Gravity of Oils

TAI_35_PGS		Thermal Alteration Index of Macerals

TC_TOC_2728_PGS	Total Carbon and Total Organic Carbon Values

TEAFID_26_PGS  	%Volatiles, TMAX, and Hydrocarbon Yield

VISKER_34_PGS	Standard Visual Kerogen Analysis

VITREF_33_PGS	Standard Vitrinite Analysis

Note that throughout this circular UNDERLINED words are actual table names and BOLD words are table elements (column titles).

The DATA tables are structured such that any number of tables may be combined to form a large data base. The first 4 columns of each DATA table are identical in structure and provide a "key" to the HEADER	 and subsequent data tables. Please note that the column entitled RC_* is not present in the Header_PGS table but exists in all the Data tables.  The internal "key" for the AOGDB is the WMO number.

The WMO number is a concatenation of four basic fields: WSC UNIQ HCST and SEQ. 	 The following explains the formation of the WMO number:

1 WSC A text field formed by the World State County combined codes of the WMO number. Samples collected within the USA (including Alaska, Hawaii, and its Exclusive Economic Zones (EEZ)) are identified by the world quadrant number of “9” then a two digit state code followed by a three digit county code. In instances of samples received outside the USA or the EEZ, the state and county codes become pseudo state and county codes by substituting 2 digits of latitude for the state code and three digits of longitude for the county code. The 6 digits in the WSC are the first 6 digits in the WMO number

2 UNIQ The unique portion of an API well number.  In the case of outcrops, the Uniq value becomes a serial 5 digit number greater than 94999.  The UNIQ portion of the WMO number is 5 digits beginning at the 7th position of the WMO number.

3 HCST Side Track and Hole Change.  The HCST field consists of 4 digits and begins at the 12th position of the WMO number.  It is normally “0000”.

4 Seq The last 4 digits of the WMO number.  Provides for multiple (9999) samples from one location.  This portion begins at the 16th position of the WMO number.

The WMO global "key" (in table Header_PGS) is provided for use by other data bases via a unique American Petroleum Institute (API) or World Meterological Organization (WMO) number which is merely a modified form of the API number.

No provision has been made for archiving digitized raw data (chromatograms, pyrograms, etc.)and hence, this file contains no raw data.

Relational Data base tables, structures and definitions

(Refer to Encoding Schemes for detailed element encoding)

Table HEADER_PGS contains information from sample log-in. Sample location (in three dimensions: longitude, latitude, elevation and depth); other location information; sample identification; sample type(s); lithologies (4 ea); formation names and ages; well and outcrop (surface) samples and any additional information, are all addressed in the HEADER_PGS table as well as other information that may be of use in data retreival for specialized reports, charts and maps.

Table HEADER_PGS Column definitions

# HEADER_PGS

Record Count: 	30175

1	WMO		Text	20

2	API		Text	14

3	LABNO		Text	8

4	DI_B001	Text	6

5	M1			Text	1

6	TOP		Number (Double)	8

7	BOT		Number (Double)	8

8	STY		Text	2

9	OTHR		Text	6

10	ADDNL		Text	17

11	SAMPID	Text	40

12	ELEV		Text	10

13	TLD		Text	7

14	WELCLAS	Text	2

15	SRT		Text	10

16	LAT		Number (Double)	8

17	LONG		Number (Double)	8

18	FAGE		Text	4

19	FUNIT		Text	4

20	LC_R020	Text	4

21	LITHO1	Text	20

22	P1			Text	4

23	LITHO2	Text	20

24	P2			Text	4

25	LITHO3	Text	20

26	P3			Text	4

27	LITHO4	Text	20

28	P4			Text	4

29	CONTAM1	Text	20

30	CP1		Text	4

31	CONTAM2	Text	20

32	CP2		Text	4

33	POR		Text	1

34	SHO		Text	1

35	SWT		Text	4

Description of elements:

## 1	WMO   	Modified form of the api number.

## 2	API		Unique Well identifier.

3	LABNO 	Prime Contractor’s (USGS) Lab number.

4	DI_B001 	Date of Sample entered into system.  A login date.

5	M1  		"M" for metric or "F" for english units (depths, etc.)

6	TOP 		Top depth of sampled interval (if from a well)

7	BOT 		Bottom depth of sampled interval (or blank if spot sample)

8	STY 		Sample source or type

9	OTHR 		Other sample information

10	ADDNL 	Additional comments, fieldnames, special ID’s

11	SAMPID 	Sample identification: either a well number and name (if from a well data base), or the submitter's field sample name (if an outcrop [surface] sample.)

12	ELEV 		Elevation of well or outcrop (units as in M1)

13	TLD 		Total depth (if from a well)

14	WELCLAS 	Well Class

15	SRT 		For samples within the U.S., the Township direction (D), Township number (NNN etc.), Range direction, Range number and section number in the following format: DNNNDNNNNN

16	LAT 		Latitude, 5 decimals

17	LONG 		Longitude, 5 decimals

18	FAGE 		Formation age code

19	FUNIT 	Formation name code

20	LC_R020 	Lab Code Notation in PGS

21	LITHO1 	Gross lithology #1 (CODED)

22	P1 		percent of lithology #1

23	LITHO2 	Gross lithology #2 (CODED)

24	P2 		percent of lithology #2

25	LITHO3 	Gross lithology #3 (CODED)

26	P3 		percent of lithology #3

27	LITHO4 	Gross lithology #4 (CODED)

28	P4 		percent of lithology #4

29	CONTAM1 	Contaminant  #1 (CODED)

30	CP1 		percent of contaminant #1

31	CONTAM2 	Contaminant  #2 (CODED)

32	CP2 		percent of contaminant #2

33	POR 		Gross porosity code

34	SHO 		Gross SHOW code

35	SWT 		Sample Weight

The HEADER_PGS table contains one row per sample, each row comprised of all 34 columns as defined above.

###### Data Table Structures and Definitions

The table HDSP_13C_40_PGS contains data on the Stable Carbon Isotopic signature of Headspace gas.  The Number “40” in the table links to the old PGS code of 040 for this analysis. The leading 7 characters of the HDSP_13C_40_PGStable attempt to convey that this table consists of Stable Carbon   isotopic values on headspace (HDSP) gas.

The table exists with the following fields of information:

Table: HDSP_13C_40_PGS       No lock(s)

Read Password: No

Modify Password: No

Column definitions

# Name     Type     Length         Key   Expression

1 WMO	  TEXT	20 characters

2 rc_r040  TEXT       7 characters

3 lc_r040  TEXT       4 characters

4 do_r040  TEXT       6 characters

5 c13_hdsp TEXT       8 characters

Current number of rows: 548

Description of the Attributes:

## 1	  WMO   		Modified form of the api number.

2  RC_r040  	The old PGS record code for this analysis.  Note that the lower casr “r” implies the original sample fraction received into the lab was a rock sample.  In this instance, even though a gas sample was analyzed, it originated from the desorption of a canned core (rock)sample.

3  LC_r040 	A code depicting the subcontracting laboratory in which the sample was analyzed.

4  DO_r040  	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5  C13_HDSP  Parts per thousand delta from the international standard PDB.  Note: Several isotope values were reported with out the

negative (“-“) notation.  These values were, in all likelyhood, imporperly keypunched into the system.  This observer feels that in fact, no positive values exist in this data set.  No attempt has been made here to remedy this oversight.

The Table WHLOIL_13C_65_PGS contains information on the Stable Carbon Isotopes of Whole Oils.  The last six digits of the table name relate to the old PGS analytical code of 065 for this analysis.

The table exists with the following fields of information:

Table: WHLOIL_13C_65_PGS        No lock(s)

Read Password: No

Column definitions

# Name     Type     Length         Key   Expression

1 WMO	  TEXT	20 characters

2 rc_o065  TEXT       7 characters

3 lc_o065  TEXT       4 characters

4 do_o065  TEXT       6 characters

5 13cwhoil TEXT       8 characters

Current number of rows: 112

Description of the Attributes:

- WMO   		Modified form of the api number.

- RC_o065  	The old PGS record code for this analysis.  Note that the lower case “o” implies the original sample fraction received into the lab was an oil sample.

3  LC_o065  	A code depicting the subcontracting laboratory in which the sample was analyzed.

4   DO_o065 	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5 13CWHLOIL 	The delta stable Carbon isotopic value in parts per thousand variance from that of the international standard: PDB.

The table SAT_ARO_13C_39_PGS contains information on the Stable Carbon Isotopes of the C15+ saturate and C15+ aromatic hydrocarbon fractions of oils and rock extracts. This table is a combination or the old PGS r039 and o039 data tables.

The table exists with the following fields of information:

Table: SAT_ARO_13C_39_PGS         No lock(s)

Column definitions

# Name     Type     Length         Key   Expression

1 WMO	  TEXT	20 characters

2 RC_039   TEXT       7 characters

3 LC_039   TEXT       4 characters

4 DO_039   TEXT       6 characters

5 c13_s15  TEXT       8 characters

6 c13_a15  TEXT       8 characters

Current number of rows: 805

Description of the Attributes:

1 WMO  		 Modified form of the api number.

2  RC_039  	The old PGS record code for this analysis.  Note that there exists no lower case designation for (r)ock samples or (o)il samples as in other tables.

3  LC_039  	A code depicting the subcontracting laboratory in which the sample was analyzed.

4   DO_039  	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5  C13_s15 	The delta stable Carbon isotopic value in parts per thousand variance from that of the international standard: PDB of the C15+ saturate fraction.

6   C13_a15 	The delta stable Carbon isotopic value in parts per thousand variance from that of the international standard: PDB of the C15+ saromatic fraction.

The table COMMENTS_PGS is a forum for the contracting lab to make statements regarding the sample condition, analytical technique, or to list problems encountered with the sample. Preserved in the table are the original API values before they were modified to WMO numbers. NOTE: The comment field of this table has been transferred to the MASTER_PGS table to facilitate the creation of views encompassing comments re the sample integrity.

Table: COMMENTS_PGS        No lock(s)

Read Password: No

Modify Password: No

Column definitions

# Name     Type     Length

1 WMO	  TEXT     	20

2 API      TEXT      19

3 SQ       TEXT       4

4 RECNO    TEXT       7

5 COMMENT  TEXT      40

6 FILDTE   TEXT       6

Current number of rows: 2698

Description of the Attributes:

1 WMO 		Modified form of the api number.

2 API  		The original API designation of the sample in PGS

3 SQ  		The Original sequence number in PGS

4 RECNO		The original record number in PGS

## 5 COMMENT  	Any Comment regarding the sample

6 FILDTE	  	Filing date of the comment

The table ELEM_36_PGS contains information on the elemental composition of a sample.

ELEM_36_PGS

Record Count: 	1813

1	WMO		     Text	20

2	RC_R036		Text	7

3	LC_R036		Text	4

4	DO_R036		Text	6

##### 5	WPCT_C		Number (Double)	8

6	WPCT_H		Number (Double)	8

7	WPCT_N		Number (Double)	8

8	WPCT_ASH		Number (Double)	8

Description of the Attributes:

1 WMO  		 Modified form of the api number.

2 RC_r036 		 The old PGS record code for this analysis.

3 LC_r036		 A code depicting the subcontracting laboratory in which the sample was analyzed.

4 DO_r036		 Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5 WPCT_C  		Weight Percent Carbon

6 WPCT_H  		Weight Percent Hydrogen

7 WPCT_N  		Weight Percent Nitrogen

8 WPCT_Ash 	Weight Percent Ash

The table: ELEM_37_PGS contains information on the elemental composition of the sample.

ELEM_37_PGS

RecordCount: 	910

1	WMO		     Text	20

2	RC_R037		Text	7

3	LC_R037		Text	4

4	DO_R037		Text	6

5	WPCT_O		Number (Double)	8

6	WPCT_S		Number (Double)	8

7	ASH_WPCT		Number (Double)	8

Description of the Attributes:

1			WMO		Modified form of the api number.

2			RC_r036	The old PGS record code for this analysis.

3			LC_r036	A code depicting the subcontracting laboratory in which the sample was analyzed.

4		DO_r036	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5		WPCT_O	Weight Percent Oxygen

6		WPCT_S	Weight Percent Sulfur

7		Ash_WPCT 	Weight Percent Ash

The table FRAC_2930_PGS is a combination of two PGS tables and includes data on the fractional composition of rock extracts or oils.

# FRAC_2930_PGS

Record Count: 	1536

1	WMO		     Text	20

##### 2	RC_R029		Text	7

3	LC_R029		Text	4

4	DO_R029		Text	6

5	GM_RK_WT		Number (Double)	8

6	PPM_BIT		Number (Double)	8

7	RC_030		Text	7

8	LC_R030		Text	4

9	DO_R030		Text	6

10	PCT_SATS		Number (Double)	8

11	PCT_AROM		Number (Double)	8

12	PCT_N_HC		Number (Double)	8

13	PCT_RECV		Number (Double)	8

Description of the Attributes:

1 		WMO   	Modified form of the api number.

#### 2 		RC_029	The old PGS record code for this analysis

3 		LC_r029  	A code depicting the subcontracting laboratory in which the sample was analyzed.

4		DO_r029  	Assumed to be the date of completion of the  analysis or the date the data was encoded into the file.

5			GM_RK_WT 	Weight in Grams of rock.

6			PPM_BIT  	Parts per Million of bitumen

#### 7			RC_030	The old PGS record code for this analysis

8			LC_R030 	A code depicting the subcontracting laboratory in which the sample was analyzed.

#### 9			DO_R030 	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

#### 10		PCT_SATS  	Percentage of Saturated components in the sample

11	PCT_AROM  	Percentage of Aromatic components in the sample

#### 12	PCT_N_HC 	Percentage of non-hydrocarbon components in the sample.

13	PCT_RECV   Percent of sample recovered

The CANGAS_8081_PGS table is again a combination of two PGS tables. This table contains chemical composition data as well as stable carbon isotopic data for the methane and CO2 compounds in the headspace portion of canned samples.

# CANGAS_8081_PGS

##### Record Count: 	75

1	WMO		     Text	20

2	RC_G080		Text	7

3	LC_G080		Text	4

4	DO_G080		Text	6

5	AIR		     Number (Double)	8

6	METHANE		Number (Double)	8

7	CO2		     Number (Double)	8

8	ETHANE		Number (Double)	8

9	H2S		     Number (Double)	8

10	PROPANE		Number (Double)	8

11	IBUTANE		Number (Double)	8

12	NBUTANE		Number (Double)	8

13	IPENTANE		Number (Double)	8

14	NPENTANE		Number (Double)	8

15	HEXANES		Number (Double)	8

16	RC_G081		Text	7

17	LC_G081		Text	4

18	DO_R081		Text	6

19	13C_C1		Text	8

20	13C_CO2		Text	8

21	COMMENT		Text	40

Description of the Attributes:

1 			WMO 		Modified form of the api number.

2 			RC_g080  	The old PGS record code for this analysis.

3 			LC_g080  	A code depicting the subcontracting laboratory in which the sample was analyzed.

4 		DO_g080  	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5			AIR	  	Mole percentage of both Air and Nitrogen in the sample

6			METHANE  	Mole percentage of Methane in the sample

## 7			CO2	  	Mole Percentage of Carbon Dioxide in the sample

## 8			ETHANE   	Mole Percentage of Ethane in the sample

9			H2S     	Mole Percentage of Hydrogen Sulfide in the sample

## 10		PROPANE  	Mole Percentage of Propane in the sample

11		IBUTANE  	Mole Percentage of Iso-butane in the sample

12		NBUTANE  	Mole Percentage of Normal Butane in the sample

13		IPENTANE 	Mole Percentage of Iso-pentane in the sample

## 14		NPENTANE 	Mole Percentage of Normal Pentane in the sample

15		HEXANES  	Estimated mole percentage of Hexanes+ in the sample

16		RC_G081  	The old record code from PGS for this analysis

17		LC_G081  	A code depicting the subcontracting laboratory in which the sample was analyzed

18		DO_R081  	Assumed to be the date of completion of analysis or the date the data was encoded into the file

19		13C_C1   	Stable carbon (13) isotope of the Methane homolog as compared to the international standard, PDB

20	13C_CO2  	Stable carbon (13) isotope of the Carbon Dioxide peak as compared to the international standard, PDB

21	COMMENT  	Analytical comments regarding the sample. NOTE:  this comment field is not the same as the comment field in the  COMMENTS_PGS or MASTER_PGS tables

The GASRNG_23_PGS table summarizes the content of most of the more commonly found peaks in the C5-C8 chromatogram.

# GASRNG_23_PGS

Record Count: 	1296

1	WMO		    	Text	20

2	RC_023		Text	7

3	LC_RO23		Text	4

4	DO_R023		Text	6

5	IC4		    	Number (Double)	8

6	NC4		    	Number (Double)	8

7	NEO_C5		Number (Double)	8

8	IC5		    	Number (Double)	8

9	NC5		    	Number (Double)	8

10	22DM_C4		Number (Double)	8

11	CYC_C5		Number (Double)	8

12	23DM_C4		Number (Double)	8

13	2M_C5		    	Number (Double)	8

14	3M_C5		    	Number (Double)	8

15	N_HEX		    	Number (Double)	8

16	M_CYC_C5		Number (Double)	8

17	22_DM_C5		Number (Double)	8

18	BENZENE		Number (Double)	8

19	24_DM_C5		Number (Double)	8

20	223_TMC4		Number (Double)	8

21	CYC_HEX		Number (Double)	8

22	33_DM_C5		Number (Double)	8

23	11DMCYC5		Number (Double)	8

24	2_M_HEX		Number (Double)	8

25	23_DM_C5		Number (Double)	8

26	1C3DMCC5		Number (Double)	8

27	3_M_HEX		Number (Double)	8

28	1T3DMCC5		Number (Double)	8

29	1T2DMCC5		Number (Double)	8

30	3_ETH_C5		Number (Double)	8

31	224TM_C5		Number (Double)	8

32	N_HEP		     Number (Double)	8

33	1C2DMCC5		Number (Double)	8

34	M_CYC_C6		Number (Double)	8

35	113TMCC5		Number (Double)	8

36	22DM_C6		Number (Double)	8

37	E_CYC_C5		Number (Double)	8

38	TOLUENE		Number (Double)	8

39	C4_C8PPM		Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_023	The old PGS record code for this analysis.

3	LC_RO23	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R023	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	IC4		Weight Pct Iso-Butane

6	NC4		Weight Pct Normal Butane

7	NEO_C5	Weight Pct Neo-pentane

8	IC5		Weight Pct Iso-Pentane

9	NC5		Weight Pct Normal Pentane

10	22DM_C4	Weight Pct 2,2,Dimethyl Butane

11	CYC_C5	Weight Pct Cyclo Pentane

12	23DM_C4	Weight Pct 2,3, Dimethyl butane

13	2M_C5		Weight Pct 2 Methyl pentane

14	3M_C5		Weight Pct 3 Methyl Pentane

15	N_HEX		Weight Pct Normal Hexane

16	M_CYC_C5	Weight Pct Methyl Cyclo Pentane

17	22_DM_C5	Weight Pct 2,2,Dimethyl Pentane

18	BENZENE	Weight Pct Benzene

19	24_DM_C5	Weight Pct 2,4, Dimethyl Pentane

20	223_TMC4	Weight Pct 2,2,3 Tri Methyl Butane

21	CYC_HEX	Weight Pct Cyclo Hexane

22	33_DM_C5	Weight Pct 3,3 Dimethyl  Pentane

23	11DMCYC5	Weight Pct 1,1 Dimethyl Cyclo Pentane

24	2_M_HEX	Weight Pct 2 Methyl Hexane

25	23_DM_C5	Weight Pct  2,3 Dimethyl Pentane

26	1C3DMCC5	Weight Pct 1-cis-3 Dimethyl Cyclo Pentane

27	3_M_HEX	Weight Pct 3 Methyl Hexane

28	1T3DMCC5	Weight Pct 1-trans-3 Dimethyl Cyclo Pentane

29	1T2DMCC5	Weight Pct 1-trans-2 Dimethyl Cyclo Pentane

30	3_ETH_C5	Weight Pct 3 Ethyl Pentane

31	224TM_C5	Weight Pct 2,2,4 Trimethyl Pentane

32	N_HEP		Weight Pct Normal Heptane

33	1C2DMCC5	Weight Pct 1-cis-2 Dimethyl Cyclo Pentane

34	M_CYC_C6	Weight Pct Methyl Cyclo Hexane

35	113TMCC5	Weight Pct 1,1,3 Trimethyl Cyclo Pentane

36	22DM_C6	Weight Pct 2,2, Dimethyl Hexane

37	E_CYC_C5	Weight Pct Ethyl Cyclo Pentane

38	TOLUENE	Weight Pct Toluene

39	C4_C8PPM	Parts Per Million all c4 - c8 compounds

The GC31_62_PGS table contains information on the C7-C35 normal alkanes within the saturate fraction of the sample.

GC31_62_PGS

Record Count: 	1061

1	WMO		Text	20

2	RC_031	Text	7

3	LC_031	Text	4

4	DO_031	Text	6

5	N_C7		Number (Double)	8

6	N_C8		Number (Double)	8

7	N_C9		Number (Double)	8

8	N_C10		Number (Double)	8

9	N_C11		Number (Double)	8

10	N_C12		Number (Double)	8

11	N_C13		Number (Double)	8

12	N_C14		Number (Double)	8

13	N_C15		Number (Double)	8

14	N_C16		Number (Double)	8

15	N_C17		Number (Double)	8

16	PRIST		Number (Double)	8

17	N_C18		Number (Double)	8

18	PHYT		Number (Double)	8

19	N_C19		Number (Double)	8

20	N_C20		Number (Double)	8

21	N_C21		Number (Double)	8

22	N_C22		Number (Double)	8

23	N_C23		Number (Double)	8

24	N_C24		Number (Double)	8

25	N_C25		Number (Double)	8

26	N_C26		Number (Double)	8

27	N_C27		Number (Double)	8

28	N_C28		Number (Double)	8

29	N_C29		Number (Double)	8

30	N_C30		Number (Double)	8

31	N_C31		Number (Double)	8

32	N_C32		Number (Double)	8

33	N_C33		Number (Double)	8

34	N_C34		Number (Double)	8

35	N_C35		Number (Double)	8

36	PCT_RESL	Number (Double)	8

37	CPI		Number (Double)	8

38	PR_PH		Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_031	The old PGS record code for this analysis.

3	LC_031	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_031	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	N_C7		Weight Pct Normal  C7

6	N_C8		Weight Pct Normal  C8

7	N_C9		Weight Pct Normal  C9

8	N_C10		Weight Pct Normal  C10

9	N_C11		Weight Pct Normal  C11

10	N_C12		Weight Pct Normal  C12

11	N_C13		Weight Pct Normal  C13

12	N_C14		Weight Pct Normal  C14

##### 13	N_C15		Weight Pct Normal  C15

14	N_C16		Weight Pct Normal  C16

15	N_C17		Weight Pct Normal  C17

16	PRIST		Weight Pct Pristane

17	N_C18		Weight Pct Normal  C18

18	PHYT		Weight Pct Phytane

19	N_C19		Weight Pct Normal  C19

20	N_C20		Weight Pct Normal  C20

21	N_C21		Weight Pct Normal  C21

22	N_C22		Weight Pct Normal  C22

23	N_C23		Weight Pct Normal  C23

24	N_C24		Weight Pct Normal  C24

25	N_C25		Weight Pct Normal  C25

26	N_C26		Weight Pct Normal  C26

27	N_C27		Weight Pct Normal  C27

28	N_C28		Weight Pct Normal  C28

29	N_C29		Weight Pct Normal  C29

30	N_C30		Weight Pct Normal  C30

31	N_C31		Weight Pct Normal  C31

32	N_C32		Weight Pct Normal  C32

33	N_C33		Weight Pct Normal  C33

##### 34	N_C34		Weight Pct Normal  C34

35	N_C35		Weight Pct Normal  C35

36	PCT_RESL	Percent Resolved Peaks

37	CPI		Carbon Preference Index

38	PR_PH		Ratio Pristane/Phytane

The ISOT_38_PGS table contains information on the asphaltene fraction of the sample.

ISOT_38_PGS

##### Record Count: 	103

1	WMO			Text	20

2	RC_O038		Text	7

3	LC_O038		Text	4

4	DO_O038		Text	6

5	WPCT_S		Number (Double)	8

6	34S_ASPH		Text	8

7	WPCT_N		Number (Double)	8

8	15N_ASPH		Text	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_O038	The old PGS record code for this analysis.

3	LC_O038	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_O038	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	WPCT_S	Weight % Sulfur

6	34S_ASPH	del 34S of Asphaltenes

7	WPCT_N	Weight % Nitrogen

8	15N_ASPH	del 15N of Asphaltenes

The Legend_PGS table is a tool to try and explain the makeup and combination of the old PGS tables into the present day scheme.

# Legend_PGS

Record Count: 	25

1	TABN			Text	8

2	NUMCOLS		Number (Double)	8

3	NUMROWS		Number (Double)	8

4	ORIGPGS1		Text	8

5	ORIGPGS2		Text	8

##### 6	ORIGPGS3		Text	8

7	ORIGPGS4		Text	8

8	COMMENT		Text	40

Description of the Attributes:

1	TABN		Table ID

2	NUMCOLS	Number of colums

3	NUMROWS	Number of rows

4	ORIGPGS1	Original PGS table ID of 1st table

5	ORIGPGS2	Original PGS ID of 2nd table

6	ORIGPGS3	Original PGS ID of 3rd Table

7	ORIGPGS4	Original PGS ID of 4th Table

8	COMMENT	Comments on naming conventions

The RKEV_41_PGS table contains information on Rock-Eval samples.

# RKEV_41_PGS

Record Count: 15384

1	WMO			Text	20

2	RC_R041		Text	8

3	LC_R041 		Text	8

4	DO_R041		Text	8

5	TMAX			Number (Double)	8

6	S1				Number (Double)	8

7	S2				Number (Double)	8

8	S3				Number (Double)	8

9	PI				Number (Double)	8

10	S2S3			Number (Double)	8

11	PC				Number (Double)	8

12	OC				Number (Double)	8

13	HI				Number (Double)	8

14	OI				Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_R041	The old PGS record code for this analysis.

3	LC_R041	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R041	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	TMAX		Tmax of S2 peak (°C)

6	S1			Amount of volatile hydrocarbons (S1 , milligrams)

7	S2			Amount of pyrolyzable hydrocarbons (S2 , milligrams)

8	S3			Amount of released CO2 , milligrams

9	PI			Rock-Eval Production Index (Transformation Ratio)

10	S2S3		S2/S3 Ratio of pyrolyzable hydrocarbons to CO2

11	PC			Total pyrolyzable Carbon (as percent of whole sample)

12	TOC		Total organic Carbon (as percent of whole sample)

13	HI			Rock-Eval Hydrogen Index

14	OI			Rock-Eval Oxygen Index

The SPGR_60_PGS table contains information on the Specific Gravity of crude oils.

# SPGR_60_PGS

Record Count: 	84

1	WMO		    	Text	20

2	RC_O060		Text	7

3	LC_O060		Text	4

4	DO_O060		Text	6

5	SPGR			Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_O060	The old PGS record code for this analysis.

3	LC_O060	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_O060	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	SPGR		API gravity (crude oils only)

The TAI_35_PGS table contains information on the Thermal Alteration Index of the sample

TAI_35_PGS

Record Count: 	3849

1	WMO			Text	20

2	RC_R035		Text	7

3	LC_R035		Text	4

4	DO_R035		Text	6

5	TAI			Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_R035	The old PGS record code for this analysis.

3	LC_R035	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R035	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	TAI		Thermal Alteration Index

The TC_TOC_2728 combined table contains information on the Total Carbon and Total Organic Carbon concentrations of rock samples.

# TC_TOC_2728

Record Count: 	18499

1	WMO			Text	20

2	LC_R027		Text	4

3	DO_R027		Text	6

4	TOC_WTPC		Number (Double)	8

5	LC_R028		Text	4

6	DO_R028		Text	6

7	TC_WTPCT		Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	LC_R027	A code depicting the subcontracting laboratory in which the sample was analyzed.

3	DO_R027	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

4	TOC_WTPC	Weight PCT Total Organic Carbon

5	LC_R028	A code depicting the subcontracting laboratory in which the sample was analyzed.

6	DO_R028	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

7	TC_WTPCT	Weight PCT Total Carbon

The TEAFID_26_PGS table contains information on the pyrolysis of rock samples.

# TEAFID_26_PGS

Record Count: 	6344

1	WMO		 	Text	20

2	RC_R026	 	Text	7

3	LC_R026	 	Text	4

4	DO_R026	 	Text	6

5	HC_YIELD	 	Number (Double)	8

6	VOLATILE	 	Number (Double)	8

7	TEA_MAX	 	Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_R026	The old PGS record code for this analysis.

3	LC_R026	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R026	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	HC_YIELD	Weight PCT Hydrocarbon Yield

6	VOLATILE	Parts per million volatile Hydrocarbons <300 C

7	TEA_MAX	Maximum temp of Hydrocarbon yield

The VISKER_34_PGS table contains information on the visual kerogen types.

# VISKER_34_PGS

Record Count: 	4541

1	WMO		Text	20

2	RC_R034	Text	7

3	LC_R034	Text	4

4	DO_R034	Text	6

5	AMORP		Number (Double)	8

6	HERBA		Number (Double)	8

7	WOODY		Number (Double)	8

8	INERT		Number (Double)	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_R034	The old PGS record code for this analysis.

3	LC_R034	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R034	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	AMORP		PCT Amorphous

6	HERBA		Pct Herbaceous

7	WOODY		PCT Woody

8	INERT		PCT Inert

The VITREF_33_PGS table contains information on the Vitrinite Reflectance of samples.

# VITREF_33_PGS

##### Record Count: 	4833

1	WMO	 		Text	20

2	RC_R033	 	Text	7

3	LC_R033	 	Text	4

4	DO_R033	 	Text	6

5	P_QUAL	 	Text	8

6	EASE_CY1	 	Text	8

7	RO_MEAN	 	Number (Double)	8

8	MODAL	 		Number (Double)	8

9	PYRITE	 	Text	8

Description of the Attributes:

1	WMO		Modified form of the api number.

2	RC_R033	The old PGS record code for this analysis.

3	LC_R033	A code depicting the subcontracting laboratory in which the sample was analyzed.

4	DO_R033	Assumed to be the date of completion of the analysis or the date the data was encoded into the file.

5	P_QUAL	Quality of the Polish

6	EASE_CY1	Ease of selecting the first cycle

7	RO_MEAN	Mean value of all reflectance measurements

8	MODAL		Median Reflectance Value

9	PYRITE	Abundance of Pyrite

10	ROS		Individual reflectance measurements

Other (original PGS) Tables in the Alaskan data base that were used to generate some of the previous tables are included here but are not intended to be used as stand-alone data tables (see Legend_PGS table for explanations) are as follows:

The R_Unit_PGS table contains data that is included in the Header table.

R_Unit_PGS

Record Count: 	742

1	FAGE		Text	4

2	FUNIT		Text	4

3	FM			Text	43

4	Era		Text	40

Description of the Attributes:

1	FAGE		Formation Age Code

2	FUNIT		Formation Unit Code

3	FM			English Formation Name

4	Era		Major Geologic Era

The Points_PGS table contains information included in the Header table.

# POINTS_PGS

Record Count: 	2968

1	WMO		Text	19

2	ID			Text	20

3	UNKN1		Text	20

4	LATTIT	Number (Double)	8

5	LO			Number (Double)	8

6	ELE		Text	10

7	FAGE		Text	4

8	FUNIT		Text	4

Description of the Attributes:

1	WMO		Modified form of the api number.

2	ID			Sample Identification

3	UNKN1		unknown field

4	LATTIT	Latitude

5	LO			Longitude

6	ELE		Elevation

7	FAGE		Formation Age Code

8	FUNIT		Formation Unit Code

The MASTER	_PGS table contains information on the correlation between WMO numbers and their associated records. It also includes the comment field from COMMENTS_PGS

# MASTER	_PGS

Record Count: 	147213

##### 1	WMO		Text	20

2	CODES		Text	7

3	COMMENT	TEXT 40

Description of the Attributes:

1	WMO	Modified form of the api number.

2	CODES	Record Codes

3	COMMENT Analytical comments re the analysis from the contracting lab

The A001_Wells_PGS table contains information on the wells sampled. This information is contained in the Header table.

# A001_WELLS_PGS

Record Count: 	26926

1	WMO		Text	20

2	API		Text	19

3	X				Text	4

4	RC_A001	Text	7

5	WELLN		Text	40

6	ELEV		Text	10

7	TLD		Text	7

8	WELCLAS	Text	2

9	SRT		Text	10

10	FD_A001	Text	6

Description of the Attributes:

1	WMO		Modified form of the api number.

2	API		API number

3	X				Unknown Field

4	RC_A001	The old PGS record code for this analysis.

5	WELLN		Well Name

6	ELEV		Elevation

7	TLD		Total Depth

8	WELCLAS	Well Class

9	SRT		Location of Well Tns-Rng-Sec

10	FD_A001	File Date

The B001_Outcrops_PGS table contains data on the outcrops sampled in the study.  This information resides in the Header_PGS table.

# B001_Outcrops_PGS

##### Record Count: 	29798

1	WMO		Text	20

2	API		Text	19

3	SQ			Text	4

4	RC_B001	Text	7

5	LC_B001	Text	4

6	LABNO		Text	8

7	DI_B001	Text	6

8	M1			Text	1

9	TOP		Number (Double)	8

10	BOT		Number (Double)	8

11	STY		Text	2

12	OTHR		Text	6

13	ADDNL		Text	17

14	FD_B001	Text	6

Description of the Attributes:

1	WMO		Modified form of the api number.

2	API		API number

3	SQ			Sequence number

4	RC_B001	The old PGS record code for this analysis.

5	LC_B001	A code depicting the subcontracting laboratory in which the sample was analyzed.

6	LABNO		Laboratory ID number

7	DI_B001	Date sample entered into Laboratory

8	M1			Measurement in (F)eet or (M)eters

9	TOP		Top Depth

10	BOT		Bottom Depth

11	STY		Sample Type

12	OTHR		Coded Info Unknown

13	ADDNL		Additional comments

14	FD_B001	File Date

Encoding Schemes

AD		Included for compatibility with PI PGS, but used by USGS

to exclude certain types of samples from user data base.

a two byte sample type code:

CL		Control sample

CO		Coal

CS		Composite

DT		Drill stem test

OS		Oil-stained rock

##### UK		Unknown

RS		Research sample (not applicable directly to mapping, etc.)

ADDNL	Submitter's Additional Description (free format ASCII)

API		Modified American Petroleum Institute number (assigned for

all samples from within the United States and the U.S. Exclusive Economic Zone [USA/EEZ]), or (see WMO)

BD		Bottom Depth sampled in units specified by M1

(8 bytes, integer or floating point number)

CONTAM	(Possible or probable) Contaminant codes, usually provided

by submitter or sample prep lab technician. Modeled after PI PGS "Catalog of contaminants"

6 byte code, first 3 bytes = contaminant code

last 3 bytes = % abundance

Code:	Contaminant:

-0-		(null) = no observable contaminants (default)

B01		Unknown contaminant

B02		Varied organic contaminants

B03		Varied inorganic contaminants

B04		Carvings (from borehole)

B05		Casing cement

B06		Drilling mud

B07		Mud additives

B08		Walnut shells

B09		Straw

B10		Mica

B11		Rubber

B12		Oil base drilling mud

B13		Pipe dope

B14		Gilsonite

B15		Asphalt

B19		No contaminants

B21		Diesel oil

B22		Crude oil

B23		Lignosulfonate

B25		Sample package contaminant (i.e., core box wax)

% Abundance = 000 through 100 % ; 001 implies 1% or less estimated

abundance of suspect contaminant; default 000 implies no

contaminants or not applicable.

CT		Container code (3 bytes maximum):

Code:	Container type:

B		Pressure cylinder (bomb)

C		Can

E		Paper or plastic envelope or bag

G		Glass bottle

P		Plastic bottle

U		None (or unknown)

CTY		API county code (3 decimal digits)

EC		Container external condition code (3 bytes maximum):

Code:	External condition:

AT		Tightly sealed, no holes or tears

NT		Not tightly sealed, damaged

UK		Unknown

ELEV		Elevation of well or surface sample in units

specified by M1

(8 bytes, integer or floating point number)

FAGE		Formation age code (3 decimal digits):

first 2 digits for encoding the geologic time table SYSTEM,   last digit for encoding the geologic time table EPOCH:

Code, SYSTEM:			Code, EPOCH:

00 Unknown			0 Unknown

70 Quaternary			9 Undifferentiated

2 Recent

1 Pleistocene

66 Quaternary			9 -Tertiary (boundary)

65 Tertiary			9 Undifferentiated

5 Pliocene

4 Miocene

3 Oligocene

2 Eocene

1 Paleocene

61 Tertiary			9 Cretaceous (boundary)

60 Cretaceous			9 Undifferentiated

5 Gulfian

4 Montanan

3 Coloradoan

2 Comanchean

1 Coahuilan

56 Jurassic			9 -Cretaceous (boundary)

55 Jurassic			9 Undifferentiated

3 Upper

2 Middle

1 Lower

51 Triassic			9 -Jurassic (boundary)

50 Triassic			9 Undifferentiated

3 Upper

2 Middle

1 Lower

46 Permo				9 -Triassic (boundary)

45 Permian			9 Undifferentiated

4 Ochoan

3 Guadalupian

2 Leonardian

1 Wolfcampian

41 Permo				9 -Pennsylvanian (boundary)

40 Pennsylvanian		9 Undifferentiated

6 Virgilian or Cisco or Monogahelan

5 Missourian or Canyon or Conemaughan

4 Desmoinesian or Strawn or Alleghenian

3 Atokan or Bend or Pottsvillian

2 Morrowan

1 Springeran

36 Mississippian		9 -Pennsylvanian (boundary)

35 Mississippian		9 Undifferentiated

4 Chesterian

3 Meramecian

2 Osagian

1 Kinderhookian

31 Mississippian		9 -Devonian (boundary)

30 Devonian			9 Undifferentiated

6 Upper

5 Bradfordian

4 Chatauquan

3 Senecan

2 Erian or Middle

1 Ulsterian or Lower

26 Silurian			9 -Devonian (boundary)

25 Silurian			9 Undifferentiated

3 Cayugan

2 Niagaran

1 Albion or Alexandrian

21 Silurian			9 -Ordovician (boundary)

20 Ordovician			9 Undifferentiated

3 Cincinnatian

2 Champlainian

1 Canadian

16 Cambro			9 -Ordivician (boundary)

15 Cambrian			9 Undifferentiated

3 Croixian

2 Albertian

1 Waucoban

11 Precambrian		9 -Cambrian (boundary)

10 Precambrian		9 Undifferentiated

FUNIT	Formation name code (up to 5 bytes, alphabetic)

These codes are assigned by Petroleum Information Corporation (PI) and are proprietary to PI; they are identical to the formation codes used in PI's Well History Control System (WHCS). Formation name codes for formations outside US/EEZ are assigned by the USGS on a sample by sample basis and are public domain. An example:

PNDQ = the Pindiquan formation (Junggar Basin, China)

HCST		Side track / hole change portion of API number

(4 numeric digits)

IC		Container internal condition code (3 bytes maximum)

Code:	Internal condition:

-0-		(null) not applicable

A		Sample absent

D		Dry

M		Wet

U		Unwashed

Q		Unknown

LAT		Sampling location latitude (7 decimal digits, 5 implied

decimals). The actual latitude for mapping purposes may be calculated from LAT and the first digit of WSC (or API):

Latitude = (LAT)X10-5 if first digit of WSC = 1, 7 or 9

Latitude = - (LAT)X10-5 if first digit of WSC = 3 or 5

LC_* A code depicting the subcontracting laboratory in which the sample was analyzed. The first 2 alpha characters of the 4 character code is the contractor code (CC):

AK		Alaska Div of Oil & Gas

CL		Core Labs, Inc.

CS		Canadian Geological Survey

GC		Geochem Research

GS		USGS Organic Geochem Lab, Denver, CO

MO		Mobil Oil Co.

NA		Not Available/unknown

SH		Shell Oil Co.

TE		Tenneco Oil Co.

UN		Unical Oil Co.

WH		Woods Hole

The next two characters in the LC_* code are the laboratory codes for the analytical lab performing the analyses (LC):

BR		Brown & Ruth Labs

CL		Core Labs, Inc.

CS		Canadian Geological Survey

##### GC		Geochem Research

GG		Global Geochemistry Corp.

GS		USGS Organic Geochem Lab, Denver, CO

NA	 	Not Available/unknown

SH		Shell Oil Co.

TE		Tenneco Oil Co.

UN		Union Oil Co.

WH		Woods Hole

LITHO	Lithology codes Up to 4 alphabetic characters for the

actual lithology, then 3 decimal digits expressing the approximate percentage of the lithology, as determined by the submitter or laboratory technician. (The sum of all LITHO and CONTAM percentages should be 100.)

Code:	Lithology:

XXXX		Not available or not determined

ANHY		Anhydrite

CCRN		Concretion

CHRT		Chert

COAL		Coal

DOLL		Limey dolomite

DOLO		Dolomite

FLMD		Mudstone

FLSH		Shale

FMCY		Claystone

LSAR		Argillaceous limestone

LSCH		Cherty limestone

LSDL		Limey dolomite

LSFL		Laminated limestone

LSND		Limestone

MICR		Micrite

SALT		Salt

SHBT		Bituminous Shale

SILT		Siltstone

SSBT		Tar or solid bitumens

SSLS		Limey sandstone

SSND		Sandstone

TUFF		Volcanic tuff

LONG		Sampling location longitude (8 decimal digits, 5 implied

decimals). The actual longitude for mapping purposes may be calculated from LONG and the first digit of WSC (or API):

Longitude = (LONG)X10-5 if first digit of WSC = 1 or 3

Longitude = - (LONG)X10-5 if first digit of WSC = 5, 7, or 9

M1		English or Metric units indicator (one character - either

F for depths and elevations in feet, or

M for depths and elevations in meters).

POR		(defunct) Included for compatibility with PI PGS

Porosity code (one numeric digit), supplied by the submitter, estimated (not measured).

Code:	Porosity:

0		Unknown (default)

1		Tight

2		Very poor

3		Poor

4		Fair

5		Good

6		Excellent

SQ		(up to 4 ASCII characters, but usually integer numbers)

SHO 	(defunct) Included for compatibility with PI PGS

(Oil) "SHOW" code supplied by the submitter.

Code:	Quality of oil show:

0		Unknown (default)

1		No show

2		Very poor

3		Poor

4		Fair

5		Good

6		Excellent

SRT		For samples within US/EEZ, Township, Range and Section:

10 alphanumeric characters

Character

Position:	Definition:

1		Township direction (N or S)

2- 4		Township number (right justified, leading blanks)

5		Range direction (E or W)

6- 8		Range number (right justified, leading blanks)

9-10		Section number (right justified, leading blanks)

ST		For samples within US/EEZ, State postal code

(two alphabetic characters)

STY		Sample source code, 2 alphanumeric characters:

Code:	Sample source:

CO		Core

CT		Cuttings

EN		Emulsion

GC		Suspected contaminant

GS		Natural gas

IG		Inorganic

LO		Generic liquid

MD		Drilling mud

OL		Crude oil or natural gas condensates

OT		Outcrop

SO		Generic solid

SW		Side wall core

UK		Unknown

WT		Water

SW		(defunct) Included for compatibility with PI PGS

Sample weight in grams (0 to 9999, right justified)

TD		Top Depth sampled in units specified by M1

(8 bytes, integer or floating point number)

TLD		Total depth of well in units specified by M1

(8 bytes, integer or floating point number)

UNIQ		Unique well code portion of API (digits 7-11 of the API

number) cf. API encoding scheme.

WMO a modified World Meteorological Organization number (assigned for all samples outside the USA/EEZ. The total number of digits in the modified API (or WMO) number is 19, defined thus:

Digit

Position:	Definition:

1		World code based on 4 quadrants relative to the

Equator and the Greenwich Meridian:

1 = northeast quadrant

3 = southeast quadrant

5 = southwest quadrant

7 = northwest quadrant

9 = USA/EEZ

2- 3	two digit state or latitude code:

(a) state code as defined by API for USA/EEZ (World = 9)

(b) latitude of location truncated to the nearest degree

(World = 1, 3, 5 or 7)

4- 6	three digit county or longitude code:

(a) county code as defined by API for USA/EEZ (World = 9)

(b) longitude of location truncated to the nearest degree

(World = 1, 3, 5 or 7)

7-11	five digit unique well code:

(a) 0000 - 64999 assigned by API for USA/EEZ (World = 9)

(b) 10000 - 94999 assigned by USGS WAPI for wells outside

the USA/EEZ (World = 1, 3, 5, or 7)

(c) 65000 - 94999 used for wells for which API has

not assigned a number (World = 9) assigned by USGS WAPI

(d) 95000 - 99999 assigned by USGS WAPI for non-

well samples (surface, outcrops, speleological,

mines, seeps, etc.)(World = 1, 3, 5, 7 or 9)

12-13	two digit side track code assigned by API (World = 9)

14-15	two digit hole change code assigned by API (World = 9)

16-19	four digit sample sequence number assigned by USGS WAPI

Note: digits 2-15 of the USGS API number are identically the fourteen digit unique API number for all wells within USA/EEZ (World = 9). The expanded API/WMO number was developed to assign unique numbers to specific samples collected worldwide.

WSC		World/State/County or World/Lat/Long portion of API (digits

1-6 of the API number) cf. API encoding scheme.

Appendix A

Definitions of Some Commonly Used Terms

ASCII	American Standard Code for Information Interchange; usually

refers to the characters, numbers and punctuation marks found on a typewriter or computer keyboard.

BIOMARKERS	Organic compounds found in crude oils and sedimentary rocks that are derived from living organisms.

CHROMATOGRAPHY		A method of separating complex mixtures into

individual chemical compounds or classes of

chemical compounds by differences in their chemical behavior.

EXTRACTION	The process of dissolution of particular chemical

compounds from a solid matrix (i.e., rock) into a liquid solution (i.e., bitumen or rock extract).

FRACTION	A group of chemical compounds with similar chemical and

physical properties (i.e., saturated hydrocarbons, aromatic hydrocarbons, resins, asphaltenes, kerogen)

GLOBAL	Applicable to all users.

KINETICS	The relationship between time, temperature and the rate of a chemical reaction (or group of parallel, serial or competing chemical reactions); expressed mathematically by the Arrhenius constant (frequency factor), energy of activation and reaction order.

LOCAL	Applicable to a small group of users (not global)

PYROLYSIS		The heating of a sample in the absence of air;

followed by subsequent analysis of the products obtained in order to determine quantities of products and/or reaction kinetic factors. Hydrous pyrolysis is done in the presence of an overabundance of water, anhydrous pyrolysis is done on the dry sample.

ROCK-EVAL		A rapid anhydrous pyrolysis technique used to semi-

quantitatively determine amounts of petroleum-like products obtained from a suspected oil or gas source rock. A less rapid Rock-Eval technique can also determine kinetic factors.

VITRINITE		A maceral derived from wood or coaly material that

exhibits higher optical reflectivity with increasing exposure to higher temperatures; a thermal maturity indicator.

Appendix B

Manufacturers of Products and Services Mentioned

American Petroleum Institute

Production Department

211 N. Ervay, suite 1700

Dallas, TX 75201 USA

MicroRim

3925 159th Ave NE

PO Box 97022

Redmond, WA 98073-9722 USA

MicroSoft Corporation

16011 NE 36th Way

PO Box 97017

Redmond, WA 98073-9717 USA

Perkin-Elmer / Nelson Chromatography

10061 Bubb Road

Cupertino, CA 95014 USA

Petroleum Information Corporation

4100 E. Dry Creek Road

Littleton, CO 80122 USA

Rock-Eval pyrolysis instrument

Contact:

Delsi Inc.

600 Kenrick, Suite D-7

Houston, TX 77060 USA

World Meterological Organization numbering system

Contact:

National Oceanographic Data Center

National Oceanographic and Atmospheric Administration

Washington, DC USA