Understanding Spaceport Functions

(Functions, Description, and Sub-Functions Taken from Vision Spaceport)

| Functions | Description | Sub-Functions and/or Elements/Components |
| --- | --- | --- |
| Offline Payload Processing | Functions required at the spaceport to prepare cargo for shipment into space and retrieval from space. | Receiving/inspection Verify payload functional Prepare payload for transport to the launch vehicle Perform fluids servicing Perform weight, CG & balance Package P/L in shipping container; ship |
| Element Receipt & Acceptance | Functions required at the spaceport to receive the flight element at the spaceport | Receiving and inspection Conditioning if required (purging, temperature and humidity control) |
| Vehicle Assembly & Integration | Includes the final assembly of the vehicle elements, and the integration of the elements into a total flight “stack” ready for launch activities | Mate flight element to ground element Assemble/mate flight elements if required Perform interface verification Perform servicing/close-out if desired Transfer elements and interface hardware non-flight items to storage location Transfer flight vehicle to next module |
| Launch/Departure Functions | Functions required to receive, service and launch the flight vehicle at the launch/departure point | Verify launch facility on-line and functional Position flight vehicle for/at launch site Mate with facility and verify functional interfaces (if any) Integrate payload and/or personnel module with vehicle and verify functional interfaces (if any) Provide vehicle weather protection (if required) wind, rain, ice, lightning, etc. Perform local servicing of commodities and close-out for flight if required at this module Perform remote servicing of commodities and close-out for flight if required at this module Ingress crew/passengers Launch the vehicle Recycle/ refurbish launch facility Service launch facility support systems |
| Landing & Recovery | Function that includes the arrival or return of a flight element during the course of a space flight. The arrival may its trip back from space, or perhaps a boost or assist stage returning. | Provide landing area Provide utilities to vehicle element at motion stop Perform minor safing and check out for return to spaceport Provide crew / passenger egress capability Provide down cargo removal capability Maintain / Verify landing facility and systems functional Provide ferry facility and fueling capability Return element to the spaceport Transfer vehicle element to next facility in flow |
| Flight Element Turnaround Functions | Functions required to receive and prepare reusable space vehicle element(s) for subsequent assembly/launch ops | Safing, if required (ordnance, cryos, etc.) Inspection/checkout to verify system health Cargo removal/Installation if desired Troubleshooting and repair as needed Service commodities and perform close-out if desired |
| Concept-Unique Logistics Functions | Functions required to ship, receive and repair flight line replaceable parts and materials after removal from the vehicle. Also Includes logistics support for concept-unique consumables, propellants and gases. Could include : On-site repair depots Offsite repair depots Vendor repair level | Propellants (acquisition, storage, distribution, conditioning verification) Other fluids and gases and unique consumables LRU replacement hardware (flight and ground systems) |
| Vehicle Depot Functions | Functions required to perform offline periodic inspections, checkout & upgrade of flight vehicles per a scheduled phased maintenance plan | Vehicle overhaul, inspection/verification, and modification (structural, flight controls, etc.) Modular element overhaul and Inspection/verification of major flight elements (e.g., OMS-RCS pods, SSME, wheels/tires TPS, etc.) Hot test propulsion hardware |
| Traffic and Flight Control Functions | Functions required monitor and control outbound and inbound space traffic, ground element movements within a spaceport , and also protect the public and high value assets during ground processing and space flight operations | Management & control of systems for Ground-to-Flight Vehicle communications Weather advisory for flight vehicle departure and returns (also for ground operations) Flight Safety monitor and control during Ascent, Reentry, and Approach & Landing phases Audio-Visual monitoring of ground operations |
| Spaceport Support Functions | Functions that may be needed to support flight systems processing functions. These may include a variety of host services needed to support flight production | Shops and Labs Photographic Services Fire Protection Medical Security Library (technical documents) Utilities Roads and Grounds Foods Services Heavy Equipment Communication/Information Services Ground Transportation Services Environmental Compatibility Management Pyrotechnical Storage and Handling Personal Environmental Protection Equipment Facility Maintenance Services and Shops |
| Operations Planning & Management | Functions that may be needed to support flight/ground systems processing. These may include a variety of host services needed to support flight production | Customer Relations Vehicle Manifesting and Scheduling Ground Systems Scheduling and Management Software Production Personnel Management Sustaining Operations Engineering Work Control Public Affairs Business Management Advanced Planning Safety, Reliability & Quality Assurance (SR&QA) |
| Connecting Infrastructure & Community Support Services | Functions that may be needed to connect to and sustain the overall spaceport enterprise | Shelter Connecting Utility Infrastructure Transportation Support Educational Support Community Police/Fire Protection Community Resources Infrastructure and Services Consumer Retail Support Community Medical Support/Hospitals, etc. Financial Institutions Economic Development |

Defining Performance Requirements for Functions

(Functions, Description, and Sub-Functions Taken from Vision Spaceport)

| Functions | Description | Sub-Functions and/or Elements/Components | Future Performance Requirements |
| --- | --- | --- | --- |
| Offline Payload Processing | Functions required at the spaceport to prepare cargo for shipment into space and retrieval from space. | Receiving/inspection Verify payload functional Prepare payload for transport to the launch vehicle Perform fluids servicing Perform weight, CG & balance Package P/L in shipping container; ship |  |
| Element Receipt & Acceptance | Functions required at the spaceport to receive the flight element at the spaceport | Receiving and inspection Conditioning if required (purging, temperature and humidity control) |  |
| Vehicle Assembly & Integration | Includes the final assembly of the vehicle elements, and the integration of the elements into a total flight “stack” ready for launch activities | Mate flight element to ground element Assemble/mate flight elements if required Perform interface verification Perform servicing/close-out if desired Transfer elements and interface hardware non-flight items to storage location Transfer flight vehicle to next module |  |
| Launch/Departure Functions | Functions required to receive, service and launch the flight vehicle at the launch/departure point | Verify launch facility on-line and functional Position flight vehicle for/at launch site Mate with facility and verify functional interfaces (if any) Integrate payload and/or personnel module with vehicle and verify functional interfaces (if any) Provide vehicle weather protection (if required) wind, rain, ice, lightning, etc. Perform local servicing of commodities and close-out for flight if required at this module Perform remote servicing of commodities and close-out for flight if required at this module Ingress crew/passengers Launch the vehicle Recycle/ refurbish launch facility Service launch facility support systems |  |
| Landing & Recovery | Function that includes the arrival or return of a flight element during the course of a space flight. The arrival may its trip back from space, or perhaps a boost or assist stage returning. | Provide landing area Provide utilities to vehicle element at motion stop Perform minor safing and check out for return to spaceport Provide crew / passenger egress capability Provide down cargo removal capability Maintain / Verify landing facility and systems functional Provide ferry facility and fueling capability Return element to the spaceport Transfer vehicle element to next facility in flow |  |
| Flight Element Turnaround Functions | Functions required to receive and prepare reusable space vehicle element(s) for subsequent assembly/launch ops | Safing, if required (ordnance, cryos, etc.) Inspection/checkout to verify system health Cargo removal/Installation if desired Troubleshooting and repair as needed Service commodities and perform close-out if desired |  |
| Concept-Unique Logistics Functions | Functions required to ship, receive and repair flight line replaceable parts and materials after removal from the vehicle. Also Includes logistics support for concept-unique consumables, propellants and gases. Could include : On-site repair depots Offsite repair depots Vendor repair level | Propellants (acquisition, storage, distribution, conditioning verification) Other fluids and gases and unique consumables LRU replacement hardware (flight and ground systems) |  |
| Vehicle Depot Functions | Functions required to perform offline periodic inspections, checkout & upgrade of flight vehicles per a scheduled phased maintenance plan | Vehicle overhaul, inspection/verification, and modification (structural, flight controls, etc.) Modular element overhaul and Inspection/verification of major flight elements (e.g., OMS-RCS pods, SSME, wheels/tires TPS, etc.) Hot test propulsion hardware |  |
| Traffic and Flight Control Functions | Functions required monitor and control outbound and inbound space traffic, ground element movements within a spaceport , and also protect the public and high value assets during ground processing and space flight operations | Management & control of systems for Ground-to-Flight Vehicle communications Weather advisory for flight vehicle departure and returns (also for ground operations) Flight Safety monitor and control during Ascent, Reentry, and Approach & Landing phases Audio-Visual monitoring of ground operations |  |
| Spaceport Support Functions | Functions that may be needed to support flight systems processing functions. These may include a variety of host services needed to support flight production | Shops and Labs Photographic Services Fire Protection Medical Security Library (technical documents) Utilities Roads and Grounds Foods Services Heavy Equipment Communication/Information Services Ground Transportation Services Environmental Compatibility Management Pyrotechnical Storage and Handling Personal Environmental Protection Equipment Facility Maintenance Services and Shops |  |
| Operations Planning & Management | Functions that may be needed to support flight/ground systems processing. These may include a variety of host services needed to support flight production | Customer Relations Vehicle Manifesting and Scheduling Ground Systems Scheduling and Management Software Production Personnel Management Sustaining Operations Engineering Work Control Public Affairs Business Management Advanced Planning Safety, Reliability & Quality Assurance (SR&QA) |  |
| Connecting Infrastructure & Community Support Services | Functions that may be needed to connect to and sustain the overall spaceport enterprise | Shelter Connecting Utility Infrastructure Transportation Support Educational Support Community Police/Fire Protection Community Resources Infrastructure and Services Consumer Retail Support Community Medical Support/Hospitals, etc. Financial Institutions Economic Development |  |