1. DRD Title

SSTF Fault Tree AnalysisIsolation Tables

2. Date of current

version

November 1996October 2001

3. DRL Line

Item No.

32 56

RFP/Contract No. (Procurement completes)

NAS 9 -18181

4. Use (Define need for, Intended use of, and/or anticipated results of data)

Provides Ffault Analysisisolation procedures for the Space Station Full Task Trainer (FTT).

5. DRD category: (check one)

X  Technical

€  Administrative

€ SR & QA

6.  References (Optional)

7. Interrelationships (e.g., with other DRDs) (Optional)

30, 31, 61

8.  Preparation Information (Include complete Instructions for document preparation)

A.  Fault Tree AnalysisIsolation Tables - This document shall provide a fault isolation tool procedures for the Space Station Full Task Trainer (SSFTT).  Fault Tree Analysis (FTA) uses deductive logic (Top Down) and focuses on the entire hardware system by assuming a system failure and determining the possible causes to isolation procedures provide a rapid and effective method of determining the source of a real-time fault in the FTT.  This document is meant to guide the Systems Analysts (SA) and/or the Maintenance Technician (MT) user from the initial problem recognition aat the system/subsystem level down to the individual lowest replaceable unit (LRU) responsible for the problem.  This will be done using the hardwarethe LRU  failure mode signatures identified in the FMECA.  There is no intention to completely list all levels of a LRU’s internal fault isolation aids and procedures in this document, nor is this document concerned with the actual repair or actions to be taken to accomplish service restoration.  The FTAfault isolation procedures will be a separate section of the M&O Manual (DRLI 61) and will include the following, where applicableinclude a section for each of the following:

1.	Introduction

2.	Guidelines and Definition

3.	Individual System/Subsystem Overview

4.	Individual System/Subsystem Fault Tree AnalysisFault Isolation Procedures

Note:  There is no requirement for a Fault Tree Analysis on the Interim Control Module.