STATEMENT OF WORK

REMOTE MAINTENANCE MONITORING SYSTEM (RMMS)

1.0	BACKGROUND.  The Remote Maintenance Monitoring System (RMMS) has been implemented to facilitate efficient management of NAS services in accordance with FAA Order 6000.30, National Airspace System Maintenance Policy. The purpose of RMMS is to support NAS Infrastructure Management, enhance the integrity of the NAS, reduce maintenance and support costs, and minimize the impact of equipment failures. The RMMS achieves automation of the Federal Aviation Administration’s (FAA) maintenance operation. This system allows performance monitoring, control, and certification to be accomplished from centralized work centers. The RMMS servers transmit appropriate messages to the Tandem Maintenance Processor Subsystem (MPS) to allow personnel at the Technical Operations Control Centers to monitor systems at unmanned sites for situations that could impede equipment operation.

2.0	SCOPE.  This Statement of Work defines the requirement for a contractor maintenance program of the RMMS at locations specified in Appendix 1. It is intended that the contract associated with this Statement of Work be a monthly firm-fixed price contract for each system with a period of performance for one (1) year, beginning January 21, 2008 and ending January 20, 2009 with four (4) additional option years in accordance with the General Services Administration (GSA) Schedule.

The Contract will encompass site and depot levels of maintenance, supply support for spares, and repair parts. As new systems are purchased, the Government has the right to add systems to this Contract. The Contractor shall provide the required maintenance for the additional systems. The Government also reserves the right to delete systems from maintenance coverage with applicable reduction in contract price upon thirty (30) days notice to the Contractor.

3.0	REQUIREMENTS.  The Contractor shall furnish all labor, supervision, tools, equipment, materials, replacement parts, and services to provide maintenance project management, corrective maintenance and logistics support, preventive maintenance, second level support, and configuration management on all RMMS equipment listed in Appendix 1.

3.1	Maintenance Program Management.  The Contractor’s management requirements for the maintenance of the RMMS equipment shall include the provision of a national trouble desk for the receipt of FAA request for repair, coordination of contractor maintenance with local FAA personnel, provision of fully trained and qualified technicians, provision of a single point of contact, and reporting of maintenance tasks accomplished.

3.1.1	National Trouble Desk.  The Contractor shall provide a National Trouble Desk for FAA facilities to request corrective maintenance services for the RMMS. This service shall be provided on a 24-hour per day, 7 days per week basis.

3.1.1.1	This trouble desk shall be equipped with an 800 telephone hotline service that will record and log calls requesting corrective maintenance service.

3.1.1.2	At the time of Contract award, the Contractor shall furnish the FAA Contracting Officer’s Technical Representative (COTR) with the telephone hotline number for the National Trouble Desk.

3.1.1.3	The FAA COTR will be notified immediately of any changes in the management or service of the National Trouble Desk.

3.1.2	Coordination of Maintenance Services. The Contractor shall coordinate and schedule all site visits for RMMS maintenance with the appropriate FAA site representative indicated in Appendix 1.

3.1.2.1	In the event of a scheduling conflict that cannot be resolved at the local level, the Contractor shall contact the FAA COTR for resolution.

3.1.2.2	The Contractor shall also contact the FAA site representative upon arrival at the site prior to performing any maintenance work.

3.1.3	Certified Technicians. The Contractor shall ensure that all service technicians used to maintain the RMMS are fully trained and certified on the RMMS System Components with a minimum of 5 years maintenance experience on these systems. System components would include such items but not limited to: servers, processors, work stations, tape backup systems, printers, network systems, etc. Technicians must be geographically located in order to expedite services to the sites listed in Appendix 1.

3.1.4	Single Point of Contact. The Contractor shall provide an administrative single point of contact for potential contractual requirement issues, reporting and invoicing issues, and problem resolution relating to delivery of maintenance service.

3.1.5	Specialized Reports. The Contractor shall provide the FAA COTR a quarterly activity report of site maintenance accomplished during the previous quarter. This report shall be in contractor format. All maintenance activities, including fault isolation, repair, removal and replacement of failed line replaceable units (LRUs) or components, adjustments, response time, and verification of system operation shall be identified in this report.

3.2	Corrective Maintenance. The Contractor shall accomplish RMMS repair to restore full operational capability to RMMS listed in Appendix 1, utilizing only personnel with maintenance and repair experience on all RMMS. The Contractor’s responsibilities are limited to hardware failures on equipment identified in Appendix 1.

3.2.1	Response/Repair Time.  For Tandem equipment located at sites 1-30 in Appendix 1-1 thru 1-5, the service technician shall arrive on-site within 4 hours after receipt of the trouble call. For hardware located greater than fifty miles of the Contractor service office, the technician shall arrive on-site within 8 hours. Tandem coverage shall be provided 8:00 a.m. to 5:00 p.m. local time, Monday through Friday, excluding Government holidays. For RMMS equipment located at the 4 OCC sites listed in Appendix 1-6, the service technician shall arrive on-site within 4 hours after receipt of the trouble call. OCC equipment coverage shall be provided 24 hours a day, 7 days a week.

3.2.2	Notice of Estimated Service Restoration. Upon arrival on the site, after determination as to required repair, the Contractor shall provide the FAA site representative with an estimated time of RMMS service restoration. For Tandem equipment, if it is anticipated that service restoration will exceed 72 hours, the Contractor shall advise the local FAA representative and contact the FAA COTR to discuss available options. For the OCC equipment, if it is anticipated that service restoration will exceed 4 hours, the Contractor shall advise the local FAA representative and contact the FAA COTR to discuss available options.

3.2.3	Logistics Support. The Contractor shall provide logistics support for the spare line replaceable units (LRU) provided as government furnished equipment (GFE). This logistics support shall include supply support and maintenance actions required to meet the response times specified with this SOW. In addition, the Contractor shall provide logistics support analysis if failure rates of components exceed requirements specified within the System Specification.

3.2.3.1	Spare Systems. The Contractor shall be responsible for storage, shipment, receiving, inspection, test, and repair of all parts and assemblies used to support the FAA RMMS. The Contractor is responsible for shipping the replacement components to the sites within 24 hours, and for providing shipping labels/containers to site personnel for the return of failed components to the Contractor’s facility for repair and return to stock. Replacement parts incorporated into the RMMS in conjunction with the Contractor’s restoration operation shall become the property of the Government.

3.2.3.2	Parts and Assemblies Used. The Contractor shall use only new OEM parts, OEM parts remanufactured to meet OEM specifications, or parts meeting or exceeding OEM specifications for the RMMS repair. The Contractor will be responsible for the disposal of parts that have been replaced.

3.2.4	Service Reports. The Contractor service personnel shall prepare a service report for each maintenance site visit and shall leave a copy of the service report at the FAA facility prior to departure of the maintenance site visit. Service reports shall be counter-signed by an FAA site representative acknowledging receipt of the service depicted in the report. This report shall be in Contractor format and shall include, at a minimum, the following data elements:

Date, time Contractor’s Service Center received request for service;

Date, time, location of failure notification;

FAA person requesting service;

Date, time of Contractor arrival;

Date, time FAA turned over system to Contractor for repair;

Repair time required;

Description of reported malfunction and corrective action accomplished;

Name of Contractor’s technician performing maintenance service;

Part number of failed LRU;

List of repair parts and components required to restore service;

FAA person verifying repair;

Date, time system repairs completed and Contractor departure.

A copy of the service report shall also be sent to FAA COTR.

3.3	Preventive Maintenance. Preventive maintenance requirements for the RMMS include periodic maintenance tasks and will be based on a firm-fixed price for each system. Preventive maintenance tasks to be accomplished are listed in Appendix 3.

3.4	Second Level Support. The Contractor shall provide engineering support for the RMMS. This engineering support shall include, but is not limited to, performance analysis, failure analysis, maintainability analysis, reliability analysis, and logistics supportability analysis to determine hardware, software, or system design and implementation efforts required to maintain the system with current technology available or to prevent RMMS hardware and/or software from becoming obsolete as deemed appropriate by the FAA’s Technical Officer.

3.5	Configuration Management. The Contractor shall ensure that hardware and software, as well as support materials, are maintained in a properly configured state. In this effort, all FAA approved hardware changes and the most current FAA baseline version of the operating system software shall be represented by associated documentation.

4.0	PERIOD OF PERFORMANCE. This Contract shall commence from January 21, 2008 through January 20, 2009, in accordance with the GSA Schedule. The Contractor shall perform the work under Article 3.0, REQUIREMENTS, at the FAA Headquarters and the identified sites listed in Appendix 1.

APPENDIX 1

FAA RMMS EQUIPMENT LIST

| TANDEM K2000 SERIES |  |
| --- | --- |
| SITE | SYSTEM | SYSTEM | LOCATION |
| NUMBER | NUMBER | CONFIG |  |
| 1 | 17910 | C | Federal Aviation Administration\ZKC |
|  |  |  | Kansas City ARTCC |
|  |  |  | 250 South Rogers Road |
|  |  |  | Olathe, KS 66062 |
|  |  |  | POC: Pat Daly |
|  |  |  | (913) 254-8664 |
| 2 | 17911 | B | Federal Aviation Administration\ZLA |
|  |  |  | Los Angeles ARTCC |
|  |  |  | 2555 East Avenue P |
|  |  |  | Palmdale, CA 93550 |
|  |  |  | POC: Leo Arizmendis |
|  |  |  | (661) 265-8481 |
| 3 | 17912 | A | Federal Aviation Administration\ZAN |
|  |  |  | Anchorage ARTCC |
|  |  |  | 5400 Davis Highway |
|  |  |  | Anchorage, AK 99506 |
|  |  |  | POC: James Lane |
|  |  |  | (907) 269-1128 |
| 4 | 17925 | A | Federal Aviation Administration\ZAU |
|  |  |  | Chicago ARTCC |
|  |  |  | 619 West New Indian Trail Road |
|  |  |  | Aurora, IL 60506 |
|  |  |  | POC: Sonia Taylor |
|  |  |  | (630) 906-8358 |
| 5 | 17913 | B | Federal Aviation Administration\ZTL |
|  |  |  | Atlanta ARTCC |
|  |  |  | 299 Woolsey Rd. |
|  |  |  | Hampton, GA 30228 |
|  |  |  | POC: David Jackson |
|  |  |  | (770) 210-7868 |
| 6 | 17914 | B | Federal Aviation Administration\ZFW |
|  |  |  | Fort Worth ARTCC |
|  |  |  | 13800 FAA Road |
|  |  |  | Fort Worth, TX 76155 |
|  |  |  | POC: Larry W Buchanan |
|  |  |  | (817) 858-7415 |
| 7 | 17862 | A | Federal Aviation Administration\SCT |
|  |  |  | Southern California TRACON |
|  |  |  | 9175 Kearny Villa Road |
|  |  |  | San Diego, CA 92126 |
|  |  |  | POC: Barbara Emerson |
|  |  |  | (858) 537-5612 |

| SITE | SYSTEM | SYSTEM | LOCATION |
| --- | --- | --- | --- |
| NUMBER | NUMBER | CONFIGG |  |
| 8 | 21212 | C | Federal Aviation Administration\ZHU |
|  |  |  | Houston ARTCC |
|  |  |  | 16600 J.F. Kennedy Blvd. |
|  |  |  | Houston, TX 77032 |
|  |  |  | POC: Mark A Lynch |
|  |  |  | (281) 230-5482 |
| 9 | 22070 | A | Federal Aviation Administration\ZJX |
|  |  |  | Jacksonville ARTCC |
|  |  |  | 37075 Aviation Lane |
|  |  |  | Hilliard, FL 32046 |
|  |  |  | POC: Clara Harden |
|  |  |  | (904) 549-1753 |
| 10 | 24098 | A | Federal Aviation Administration\ZAB |
|  |  |  | Albuquerque ARTCC |
|  |  |  | 8000 Louisiana Blvd. NE, Room 1014 |
|  |  |  | Albuquerque, NM 87109 |
|  |  |  | POC: Ron Reich |
|  |  |  | (505) 856-4424 |
| 11 | 21217 | B | Federal Aviation Administration\ZMA |
|  |  |  | Miami ARTCC |
|  |  |  | 7500 NW 58th St. |
|  |  |  | Miami, FL 33166 |
|  |  |  | POC: Ivan Correa |
|  |  |  | (305) 716-1637 |
| 12 | 23729 | A | Federal Aviation Administration\ZOA |
|  |  |  | Oakland ARTCC |
|  |  |  | 5125 Central Avenue |
|  |  |  | Fremont, CA 94536 |
|  |  |  | POC: Donna Lyseng |
|  |  |  | (510) 745-3389 |
| 13 | 21213 | A | Federal Aviation Administration\ZME |
|  |  |  | Memphis ARTCC |
|  |  |  | 3229 Democrat Rd . |
|  |  |  | Memphis, TN 38118 |
|  |  |  | POC: Wayne Ralph |
|  |  |  | (901) 368-8190 |
| 14 | 17915 | B | Federal Aviation Administration\ZSE |
|  |  |  | Seattle ARTCC |
|  |  |  | 3101 Auburn Way South |
|  |  |  | Auburn, WA 98092 |
|  |  |  | POC: Cathy Gronenthal |
|  |  |  | (253) 351-3362 |

| SITE | SYSTEM | SYSTEM | LOCATION |
| --- | --- | --- | --- |
| NUMBER | NUMBER | CONFIG |  |
| 15 | 23730 | A | Federal Aviation Administration\ZHN |
|  |  |  | Honolulu Control Facility(CCF) Rm 216 |
|  |  |  | OEP/District |
|  |  |  | 760 Worchester Avenue |
|  |  |  | Honolulu, HI 96818-5125 |
|  |  |  | POC: Adele Lau |
|  |  |  | (808) 840-6711 |
| 16 | 21214 | B | Federal Aviation Administration\ZLC |
|  |  |  | Salt Lake City ARTCC |
|  |  |  | 2150 West 700 North |
|  |  |  | Salt Lake City, UT 84116 |
|  |  |  | POC: Michael Whipple (Sept) |
|  |  |  | Jeffrey Gonzales (Oct) |
|  |  |  | Chris Sunderland (Nov) |
|  |  |  | (801) 320-2263 |
| 17 | 24099 | B | Federal Aviation Administration\ZDV |
|  |  |  | Denver ARTCC |
|  |  |  | 2211 17th Ave. |
|  |  |  | Longmont, CO 80501 |
|  |  |  | POC: Nikki Wyscaver |
|  |  |  | (303) 651-4320 |
| 18 | 22068 | A | Federal Aviation Administration\ZMP |
|  |  |  | Minneapolis ARTCC |
|  |  |  | 512 Division St. |
|  |  |  | Farmington, MN 55024 |
|  |  |  | POC: Russell Jacques |
|  |  |  | (651) 463-5657 |
| 19 | 24100 | A | Federal Aviation Administration\ZID |
|  |  |  | Indianapolis ARTCC |
|  |  |  | 1850 South Sigsbee St. |
|  |  |  | Indianapolis, IN 46241 |
|  |  |  | POC: Joel Terwin |
|  |  |  | (317) 247-2341 |
| 20 | 22069 | A | Federal Aviation Administration\ZOB |
|  |  |  | Cleveland ARTCC |
|  |  |  | 326 East Lorian St. |
|  |  |  | Oberlin, OH 44074 |
|  |  |  | POC: Paul Windham |
|  |  |  | (440) 774-0375 |
| 21 | 21216 | B | Federal Aviation Administration\ZDC |
|  |  |  | Washington ARTCC |
|  |  |  | 825 E. Market St. |
|  |  |  | Leesburg, VA 20176 |
|  |  |  | POC: Scott Brennan |
|  |  |  | (703) 779-3773 |

| SITE | SYSTEM | SYSTEM | LOCATION |
| --- | --- | --- | --- |
| NUMBER | NUMBER | CONFIG |  |
| 22 | 17917 | C | Federal Aviation Administration\ZNY |
|  |  |  | New York ARTCC |
|  |  |  | 4205 Johnson Ave. |
|  |  |  | Ronkonkoma, NY 1I779 |
|  |  |  | POC: Cyndie Soto |
|  |  |  | (631) 468-1125 |
| 23 | 17916 | B | Federal Aviation Administration\ZBW |
|  |  |  | Boston ARTCC |
|  |  |  | 35 Northeastern Blvd. |
|  |  |  | Nashua, NH 03062 |
|  |  |  | POC: Kurt Donnelly |
|  |  |  | (603) 879-6761 |
| 24 | 17861 | E | Federal Aviation Administration\ATCSCC AAdministration\ATCSCC |
|  |  |  | 13600 EDS Drive |
|  |  |  | Herndon, VA 20171 |
|  |  |  | POC: Curtis Shaw |
|  |  |  | (703) 925-3066 |
| 25 | 25802 | I | Federal Aviation Administration\ACT-A |
|  |  |  | William J Hughes Technical Center |
|  |  |  | Atlantic City International Airport |
|  |  |  | Atlantic City, NJ 08405 |
|  |  |  | POC: Andy Romanofsky |
|  |  |  | (609) 485-6092 |
| 26 | 17839 | D | Federal Aviation Administration\ACT-B |
|  |  |  | William J Hughes Technical Center |
|  |  |  | Atlantic City International Airport |
|  |  |  | Atlantic City, NJ 08405 |
|  |  |  | POC: Andy Romanofsky |
|  |  |  | (609) 485-6092 |
| 27 | 20715 | G | Federal Aviation Administration\AAC-B |
|  |  |  | Mike Monroney Aeronautical Center |
|  |  |  | Thomas P. Stafford Bldg. 27 |
|  |  |  | 6500 S. MacArthur |
|  |  |  | Oklahoma City, OK 73125 |
|  |  |  | POC: Howard Milburn |
|  |  |  | (405) 954-7992 |
| 28 | 24210 | H | Federal Aviation Administration\AAC-A |
|  |  |  | Mike Monroney Aeronautical Center |
|  |  |  | NAS Engineering Group |
|  |  |  | 6500 S. MacArthur, Bldg. 189 |
|  |  |  | Oklahoma City, OK 73125 |
|  |  |  | POC: Mel Eady |
|  |  |  | (405) 954-1902 |

| SITE | SYSTEM | SYSTEM | LOCATION |
| --- | --- | --- | --- |
| NUMBER | NUMBER | CONFIG |  |
| 29 | 17909 | I | Department of Transportation\AAC-C |
|  |  |  | Mike Monroney Aeronautical Center |
|  |  |  | FAA Academy |
|  |  |  | Thomas P. Stafford Bldg. 27 |
|  |  |  | 6500 S. MacArthur |
|  |  |  | Oklahoma City, OK 73125 |
|  |  |  | POC: Kevin Lamberth |
|  |  |  | (405) 954-0613 |
| 30 | 30603 | F | Federal Aviation Administration\ACT-1 |
|  |  |  | William J Hughes Technical Center |
|  |  |  | Atlantic City International Airport |
|  |  |  | Atlantic City, NJ 08405 |
|  |  |  | POC: Andy Romanofsky |
|  |  |  | (609) 485-6092 |

| OPERATIONS CONTROL CENTERS PLATFORM |
| --- |
| SITE | SYSTEM | SYSTEM | LOCATION |
| NUMBER | NUMBER | CONFIG |  |
| AOCC | N/A | J | Atlantic Operations Control Center |
|  |  |  | 41 Woolsey Rd. |
|  |  |  | Hampton, GA 30228 |
|  |  |  | POC: Timur Cudnohufsky |
|  |  |  | (770) 210-7087 |
|  |  |  | POC: Aubrey Stephens |
|  |  |  | (770) 210-7086 |
| MOCC | N/A | J | Mid-States Operations Control Center |
|  |  |  | 280 South Rogers Road |
|  |  |  | Olathe, KS 66062 |
|  |  |  | POC: Tony Sanchez |
|  |  |  | (913) 254-8029 |
|  |  |  | POC: David Turk |
|  |  |  | (913) 254-8029 |
| POCC | N/A | J | Pacific Operations Control Center |
|  |  |  | 9175 Kearny Villa Road |
|  |  |  | San Diego, CA 92126 |
|  |  |  | POC: Alvin Small |
|  |  |  | (858) 831-7526 |
|  |  |  | POC: Rob Maguire |
|  |  |  | (858) 831-7527 |
| NOCC | N/A | K | National Operations Control Center |
|  |  |  | 13660 EDS Drive, Suite 100 |
|  |  |  | Herndon, VA 20171 |
|  |  |  | POC: Curtis Shaw, Facility Manager |
|  |  |  | (703) 925-3066 |

APPENDIX 2

RMMS SYSTEM COMPONENTS

| MPS Configuration A |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| CIU Controller 3651 |  | 18 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 9 |
|  | Break Out Board | 18 |
|  | Power Supply | 18 |
|  | CLIP-1 57070 | 96 |
|  | CLIP-4 57080 | 39 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration B |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| CIU Controller 3651 |  | 24 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 12 |
|  | Break Out Board | 24 |
|  | Power Supply | 24 |
|  | CLIP-1 57070 | 128 |
|  | CLIP-4 57080 | 52 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration C |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| CIU Controller 3651 |  | 30 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 15 |
|  | Break Out Board | 30 |
|  | Power Supply | 30 |
|  | CLIP-1 57070 | 160 |
|  | CLIP-4 57080 | 65 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration D\System 17839\ACT |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 5 |
| CIU Controller 3651 |  | 6 |
| 1 GB disk Drive 4240 |  | 4 |
| 4GB Disk Drive 4260 |  | 46 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 3 |
|  | Break Out Board | 6 |
|  | Power Supply | 6 |
|  | CLIP-1 57070 | 32 |
|  | CLIP-4 57080 | 13 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration E\System 17861\FAA |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 3 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| 4GB Disk Drive 4260 |  | 32 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration F\System 30603\ACT1 |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 8 |
| Universal Controller 3601 |  | 1 |
| Asynchronous Controller 3606 |  | 1 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 1 |
| LAN Controller 3615 |  | 2 |
| CIU Controller 3651 |  | 2 |
| 4GB Disk Drive 4260 |  | 22 |
| 1 GB disk Drive 4240 |  | 4 |
| Cartridge Tape Drive |  | 1 |
| CSS 3650 |  | 1 |
|  | Break Out Board | 2 |
|  | Power Supply | 2 |
|  | CLIP-1 57070 | 10 |
|  | CLIP-4 57080 | 5 |
| Terminal 6530 |  | 1 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration G\System 20715\AACB |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 4 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 4 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 4 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 4 |
| CIU Controller 3651 |  | 18 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 3 |
|  | Break Out Board | 6 |
|  | Power Supply | 6 |
|  | CLIP-1 57070 | 32 |
|  | CLIP-4 57080 | 13 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 4 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration H\System 24210\AACA |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 4 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| CIU Controller 3651 |  | 6 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 3 |
|  | Break Out Board | 6 |
|  | Power Supply | 6 |
|  | CLIP-1 57070 | 32 |
|  | CLIP-4 57080 | 13 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| MPS Configuration I\System 25802\ACTA & System 17909\DOT |
| --- |
| Description | Quantity |
| Base Cabinet | Including SCP, PSs, Fans, Power Dist. Unit, Batteries, etc. | 1 |
| System Cabinet | Including PSs, Fans, Power Dist. Unit, Batteries, etc. | 3 |
| Expansion Cabinet | Including PSs, Fans, Power Dist. Unit, etc. | 4 |
| K2000 Processor |  | 8 |
| Memory Board |  | 8 |
| Multi-function Controller (MFC) 3681 |  | 16 |
| Universal Controller 3601 |  | 2 |
| Asynchronous Controller 3606 |  | 1 |
| Synchronous Controller 3605 |  | 1 |
| Tape Controller 3214 |  | 2 |
| LAN Controller 3615 |  | 3 |
| CIU Controller 3651 |  | 6 |
| 4GB Disk Drive 4260 |  | 22 |
| Cartridge Tape Drive |  | 1 |
| Printer 5518 |  | 2 |
| Printer 5515 |  | 2 |
| CSS 3650 |  | 3 |
|  | Break Out Board | 6 |
|  | Power Supply | 6 |
|  | CLIP-1 57070 | 32 |
|  | CLIP-4 57080 | 13 |
| Terminal TS-530 |  | 1 |
| KC-17 System Console |  | 1 |
| Terminal 6530 |  | 2 (plus) |
| 5145 DAT |  | 2 |

| OCC Configuration J\AOCC\MOCC\POCC |
| --- |
| Item | Component | Quantity |
| Operations Server | Hewlett Packard Proliant ML570 | 1 |
|  | Smart Array RAID Controller 3100ES | 1 |
|  | 18.2 GB, 15,000 (15k) Revolutions Per Minute (RPM), U320 hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 18.2 GB, 15k RPM, U320 hot pluggable hard drives setup in RAID5 configuration | 5 |
|  | 18.2 GB, 15k RPM, U3209 hot pluggable hard drive to be used as a spare | 1 |
|  | Xeon processor MP 2 GigaHertz (GHz)/2 Megabytes (MB) | 4 |
|  | 4 GB Random Access Memory (RAM) | 1 |
|  | Compaq NC6136 Gigabit Server Adapter, 64 bit/66 MegaHertz (MHz), Peripheral Component Interconnect (PCI) 100 | 1 |
|  | NC3123 PCI 10/100 Fast Ethernet NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |
| Distribution Server | Compaq Proliant 7000 | 1 |
|  | Smart Array RAID Controller 3100ES | 1 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 5 configuration | 5 |
|  | 9 GB, 10k RPM hot pluggable hard drive used as a spare | 1 |
|  | Xeon Pentium III processors | 4 |
|  | 4 GB RAM | 1 |
|  | Dual-ported fiber optic redundant NIC | 1 |
|  | Compaq NC6134 GB NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |
| Gateway Server | Compaq Proliant 7000 | 1 |
|  | Smart Array RAID Controller 3100ES | 1 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 5 configuration | 5 |
|  | 9 GB, 10k RPM hot pluggable hard drive used as a spare | 1 |
|  | Xeon Pentium III processors | 4 |
|  | 4 GB RAM | 1 |
|  | Dual-ported fiber optic redundant NIC | 1 |
|  | Compaq NC6134 GB NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |

| OCC Configuration J\AOCC\MOCC\POCC (Continued) |
| --- |
| Item | Component | Quantity |
| Support Server | Compaq Proliant 6000 | 1 |
|  | Smart Array RAID Controller 3100ES | 1 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 5 configuration | 5 |
|  | 9 GB, 10k RPM hot pluggable hard drive used as a spare | 1 |
|  | Xeon Pentium III processors | 4 |
|  | 4 GB RAM | 1 |
|  | Single-ported fiber optic redundant NIC | 1 |
|  | Compaq NC6134 GB NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |
| Tape Backup System | Compaq Proliant DL360 rack-mounted server | 1 |
|  | 18.2 GB 10k hard drives in RAID 1 configuration | 2 |
|  | 640 MB RAM | 1 |
|  | Cybernetics CY-TL8-2015 tape library | 1 |
|  | Cybernetics CY-8050-01/L tape drive | 1 |
| HUB/Switch Cisco Catalyst 6009 | 48 Port RJ-45 module | 2 |
|  | 8 port GB module | 1 |
|  | 1000 Base-SX GigaByte Interface card (GBIc) | 8 |
| Axis storepoint Compact Disk-Read Only Memory (CD-ROM) server | Axis Model 850/851 | 1 |
| Dell Optiplex GX270, Pentium 4, 2.8 GHz (Operations Workstations) | 1 GB Non-ECC 333 MHz DDR, 2x512 RAM | 60 |
|  | Intel Integrated DVMT Video |  |
|  | 40 GB EIDE 7200 RPM ATA/100 Hard Drive |  |
|  | 3.5-inch 1.33 MB floppy drive |  |
|  | Windows XP Professional SP1 |  |
|  | Dell PS/2 2 button mouse |  |
|  | Integrated Intel GB 10/100/1000 NIC |  |
|  | Integrated Sound Blaster compatible AC97 sound card |  |
|  | 24X IDE CD-ROM |  |
|  | Dell FP1900 flat panel monitor |  |

| OCC Configuration J\AOCC\MOCC\POCC (Continued) |
| --- |
| Item | Component | Quantity |
| Dell Optiplex GX240, Pentium 4, 1.7 GHz (Support Workstations) | 256 MB SDRAM | 22 |
|  | 32 MB ATI Rage Ultra 128 video card (full height) |  |
|  | 20 GB EIDE 7200 RPM ATA/100 Hard Drive |  |
|  | 3.5-inch 1.33 MB floppy drive |  |
|  | Windows NT4 SP6 |  |
|  | Microsoft PS/2 IntelliMouse |  |
|  | SoundBlaster audio PCI 64 Volts (V) |  |
|  | Integrated 10/100 3Com remote wake-up NIC |  |
|  | 48X EIDE CD-ROM |  |
|  | Harmon/Kardon 195 speakers |  |
|  | Conexant HCF Data/Fax 56 k V90 modem |  |
|  | Dell FP1900 flat panel monitor |  |
| Printers | Hewlett Packard (HP) Color LaserJet 4500n | 2 |
|  | HP LaserJet 4050n | 2 |
|  | OfficeJet 85xi print/copy/scan/fax | 1 |
|  | JetDirect 170x 10BT printer server | 1 |
|  | Mita AI-4040 digital copier | 1 |

| OCC Configuration K\NOCC |
| --- |
| Item | Component | Quantity |
| Operations Server | Hewlett Packard Proliant ML570 | 1 |
|  | Smart Array 642 Controller (RAID) | 1 |
|  | 18.2 GB, 15k RPM, U320 hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 18.2 GB, 15k RPM, U320 hot pluggable hard drives setup in RAID5 configuration | 5 |
|  | 18.2 GB, 15k RPM, U3209 hot pluggable hard drive to be used as a spare | 1 |
|  | Xeon processor MP 2 GHz/2 Megabytes (MB) | 4 |
|  | 4 GB RAM | 1 |
|  | Compaq NC6136 GB Server Adapter, 64 bit/66 MHz, PCI 100 | 1 |
|  | NC3123 PCI 10/100 Fast Ethernet NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |
| Support Server | Compaq Proliant 8000 | 1 |
|  | Integrated 4250ES RAID Array Controller | 1 |
|  | 9 GB, 10k RPM hot pluggable hard drives setup in RAID 1 configuration | 2 |
|  | 18 GB, 10k RPM hot pluggable hard drives setup in RAID 5 configuration | 5 |
|  | 18 GB, 10k RPM hot pluggable hard drive used as a spare | 1 |
|  | Xeon Pentium III processors | 4 |
|  | 4 GB RAM | 1 |
|  | Dual-ported fiber optic redundant NIC | 1 |
|  | Compaq NC6134 GB NIC | 1 |
|  | Compaq flat panel display rack mount | 1 |
| Dell Optiplex GX270, Pentium 4, 2.8 GHz (Workstations) | 1 GB Non-ECC 333 MHz DDR, 2x512 RAM | 21 |
|  | Intel Integrated DVMT Video |  |
|  | 40 GB EIDE 7200 RPM ATA/100 Hard Drive |  |
|  | 3.5-inch 1.33 MB floppy drive |  |
|  | Windows XP Professional SP1 |  |
|  | Dell PS/2 2 button mouse |  |
|  | Integrated Intel GB 10/100/1000 NIC |  |
|  | Integrated Sound Blaster compatible AC97 sound card |  |
|  | 24X IDE CD-ROM |  |
|  | Dell FP1900 flat panel monitor |  |
| Tape Backup System | Compaq Proliant DL360 rack-mounted server | 1 |
|  | 1.266 GHz processors | 2 |
|  | 18.2 GB 10k hard drives in RAID 1 configuration | 2 |
|  | 640 MB RAM | 1 |
|  | Cybernetics CY-TL8-2015 tape library | 1 |
|  | Cybernetics CY-8050-01/L tape drive | 1 |

APPENDIX 3

TANDEM K2000 PREVENTIVE MAINTENANCE TASKS OR ACTIONS

MONTHLY PREVENTIVE MAINTENANCE TASKS FOR THE MPS TANDEM HIMALAYA K2000

- Verify operation of dial modem (Not Applicable-modem was removed)

- Verify fans are operational

- Inspect LEDs for red condition

- Review Tandem Maintenance Diagnostic Subsystem (TMDS) for errors

- Verify subsystem status via TMDS

- Perform list bads out to each disc path

- Perform Pup primary on all disc paths

- Verify microcode levels on system

- Verify proper voltage levels

- Verify all CPUs are running

- Verify SYSHEALTH subsystem.  (Not Applicable-use TMDS, Remote Console Program (RCP)

- Clean filters

- Wipe down cabinets if necessary