January 11, 2005

MEMORANDUM

Subject:		Product Chemistry Science Chapter for Didecyl Dimethyl Ammonium Chloride   (DDAC)

To:		A .Najm Shamim,  Risk Assessor for DDAC

Regulatory Management Branch II

Antimicrobials Division (7510C)

And

Tracy Lantz, CRM for DDAC RED

Regulatory Management Branch I

Antimicrobials Division (7510C)

From:		Chris Jiang, Chemist

Product Science Branch

Antimicrobials Division (7510C)

Thru:		Karen P. Hicks, CTT Team Leader

Product Science Branch

Antimicrobials Division (7510C)

Michele Wingfield, Branch Chief

Product Science Branch

Antimicrobials Division (7510C)

DP Barcode:	D323311					Chemical Code:		069149

EPA Reg. No.:	3377-42						MRID #(s: 		44520301

44520302

44520303

Enclosed is the Science Chapter for Didecyl Dimethyl Ammonium Chloride Reregistration Eligibility Decision (RED).

Science Chapter on for Didecyl Dimethyl Ammonium Chloride (MRID #(s:  44520301, 44520302, 44520303)

Product Chemistry

Case Overview

Chemical Overview

The main ingredient covered for this Science Chapter is:  Didecyl Dimethyl Ammonium Chloride

Chemical Name:			Didecyl dimethyl ammonium chloride

Common/Trade Names:		Di-n-decyl dimethyl ammonium chloride, DDAC

Chemical Family:			Quaternary amines

CAS Registry Number:		7173-51-5

OPP Chemical Code:		069149

Molecular Formula:		R2C2H6NCl (R = n-decyl)

Molecular Weight:		362.08

SCIENCE ASSESSMENT

The Agency thoroughly reviewed the registrants( submissions (in-house literature) for the purpose of

determining the reregistration eligibility of didecyl dimethyl ammonium chloride for use in wood preservatives, in agricultural premises and equipment, in industrial processes and water systems, and in commercial, institutional, and residential premises.

Product Chemistry Assessment

The physical and chemical characteristics of didecyl dimethyl ammonium chloride are described below.

Technical Grade Active Ingredient (TGAI):

Chemical Name:			Didecyl dimethyl ammonium chloride

Molecular Wt.			362.08

Color:				100 APHA units

Physical State:			Liquid

Odor:				Ethanolic

*Melting Point:			228.81 oC

Boiling Point:			Please provide boiling point data

Could not be established because test article is a multi-component system with each component boiling at a different temperature?

Density:				0.9216 g/cm3 at 25 oC

Water Solubility:			Completely soluble

*Vapor Pressure:			2.33 x 10-11 mm Hg

Dissociation Constant:		Not applicable

*log Kow:			4.6581

pH:				6.31

Stability:			Stable with respect to metal, nonmetal, temperature, and light

Oxidizing/Reducing Potential:	Not applicable as product does not contain oxidizers or reducers

Flash Point:			38.0 oC

Explodability:			Not applicable for liquids which are not potentially explosive

Viscosity:			28.35 cSt at 25 oC

Miscibility:			Not applicable as product is not to be mixed with petroleum solvents

Corrosion Characteristics		Corrosive to stainless steel and no corrosion to HDPE

Dielectric breakdown voltage:	Not applicable as product is not to be used near electrical equipment

*-Values obtained from EpiSuite

Didecyl Dimethyl ammonium chloride

PRODUCT CHEMISTRY

BIBLIOGRAPHY

US EPA(s MRID #: 44520301, Albemarle DAQ-1010-5 Biocide—Product Chemistry, (1998) Albemarle Corp., Lab Project Number 8382-139 Quat 10, Albemarle Corporation.

US EPA(s MRID #: 44520302, Tolbert, A., Product Chemistry Chemical Characterization for Determining

Identity and Purity of  50% Di-N-Decyl Dimethyl Ammonium Chloride, (1998), Lab Project Number Quat 10B, Albemarle Corporation.

US EPA(s MRID #: 44520303, Tolbert, A., Product Chemistry Chemical Characterization for Determining

the Physical and Chemical Properties, and Accelerated Storage Stability of 50% Di-N-Decyl Dimethyl Ammonium Chloride, (1998), Lab Project Number Quat 10A, Albemarle Corporation.

EPISuite  Property Assessment Program

Appendix I:  Impurities evolved during the manufacture of Didecyl dimethyl ammonium chloride

Chemical name

Methyl chloride

Di-n-decylmethyl amine

Di-n-decylmethyl amine-hydrochloride

Methanol

No percentages of these impurities are given.