CAD

DELIVERABLES

POLICY

June 1, 2002

U.S. General Services Administration

Mid-Atlantic Region

Public Buildings Service

The Strawbridge Building

20 North 8th Street

Philadelphia, PA  19107-3191

CONTENTS

PAGE

1.	GENERAL INFORMATION	3

1.1	Government Ownership Statement	3

1.2	Validation Procedures	3

1.3	Contacts / Resources	3

2.	SOFTWARE AND DELIVERABLE MEDIA	3

2.1	Physical Media	3

2.2	Drawings	3

2.3	Word Processor Documents	4

2.4	Spread Sheets	4

2.5	Graphics	4

2.6	Schedules	4

2.7	Third Party Software	4

3.	DRAWING SETUP	4

3.1	General	4

3.2	Accuracy	4

3.3	Drawing Sheet Sizes	5

3.4	Drawing Scales	5

3.5	Title Blocks	5

4.	FILE NAMES AND STRUCTURES	8

4.1	Xref Assembly	8

4.2	Sheet File Drawing Numbers	9

4.3	Model File Drawing Numbers	10

4.4	File Names	12

5.	DATA STRUCTURE	13

5.1	Layering	13

5.2	Linetypes	14

5.3	Blocks	14

5.4	Hatching	14

5.5	Object Linking and Embedding (OLE)	14

5.6	AutoCAD Fonts	14

5.7	Fonts for Other Software	15

5.8	Plotting Parameters	15

6.	PROJECT AND DRAWING DOCUMENTATION	21

6.1	General	21

6.2	README.DOC File	21

6.3	Project Documentation and Drawing Audit Form	21

6.4	Other Project and Drawing Reference Files	22

PROJECT  DOCUMENTATION and DRAWING AUDIT FORM	23

# 1.	GENERAL INFORMATION

## 1.1	Government Ownership Statement

All drawings and related files, including specifications, shop drawings, renderings, photographs, and other materials generated by the contractor for the project, shall be the property of the General Services Administration upon their delivery to GSA, or at the termination of the contract, whichever occurs first.  This applies to content as well as physical media.  The government will not accept disclaimers nullifying this requirement.

## 1.2	Validation Procedures

The Prime A/E is responsible for ensuring that all submissions by sub-contractors meet the Deliverables Policy contained herein.  The Prime A/E, prior to the start of the design phase, shall transmit sample electronic submittals to GSA to verify that their software, and that of their subs, complies with the requirements herein.

## 1.3	Contacts / Resources

The A/E shall contact the project team with questions regarding the Mid-Atlantic Region’s CAD Deliverables Policy.  If necessary, the project team will contact the appropriate regional staff.

Rob Hopf, Systems CIFM Support

This document and the drawings referenced herein are available electronically at: http://www.gsa.gov/midatlanticcadpolicy

# 2.	SOFTWARE AND DELIVERABLE MEDIA

## 2.1	Physical Media

Files submitted to GSA shall not contain computer viruses.  Scan all media using current virus scanning software prior to submission.

All files shall be submitted on one of the following media:

3 ½” high density 1.44 MB floppy disks: Shall be formatted to be read by MS-DOS and Windows and may be compressed if readable by WinZip.  No submission shall exceed ten floppy disks.  Self-extracting files are acceptable provided they allow the user to specify the extraction location.

CD-R: May be 650MB or 700MB, but must be closed.  CDs may not contain compressed (ZIP or EXE) files.

CD-RW: May be 650MB or 700MB.  CDs may not contain compressed (ZIP or EXE) files.  This media type may be disallowed in the contract if the project is run from a field office which cannot read it.

email: Shall be no more than 5 MB.  May be compressed if readable by WinZip.  Self-extracting files are acceptable provided they allow the user to specify the extraction location.

## 2.2	Drawings

All drawings shall be readable by AutoCAD Release 2002 for Windows, and shall be DWG files, not DXF, DWF, etc.  Being “readable” is constituted by the ability to open a file without any errors, such as proxy errors, font substitution errors, xref resolution errors, etc., and the objects, layers, etc. in the file remaining in tact.  No add-ons which create non-native object types are accepted unless approved in writing by the GSA or required in supplemental policies.  This exclusion also applies to special object types created by Express Tools. If ADT (Architectural Desktop) or other add-on which adds non-native objects is used, the non-native objects must be converted to native AutoCAD objects all proxies must be removed.  If printed drawings are submitted, they must match prints produced by the electronic drawings.

## 2.3	Word Processor Documents

Word Processor documents shall be Microsoft Word 6, 7 (aka 95), 97, or 2000 format.

## 2.4	Spread Sheets

Spread sheet documents shall be Microsoft Excel 6, 7 (aka 95), 97, or 2000 format.

## 2.5	Graphics

Graphics may be submitted in any of the following formats:

TIF - uncompressed, packbits, group III, group IV, or LZW

GIF - interlaced or noninterlaced

JPG - standard only; no progressive; any compression level

BMP

Note: This is not to indicate that scanned drawings will be accepted in lieu of AutoCAD files; this is intended for photos, conceptual sketches, renderings, etc.

## 2.6	Schedules

Project Management Schedule documents shall be Microsoft Project 4.0, 4.1 (aka 95), 98, or 2000 format.  Project files shall be saved with a baseline.

## 2.7	Third Party Software

A written request must be submitted to GSA and permission granted by GSA in order to submit electronic data in a format other than those specifically named above, or any AutoCAD add-on application which leaves non-native objects in the drawings.  This also applies to AutoCAD-integrated applications, such as Architectural Desktop.  When it is considered in the best interest of the Government, third party software may be permitted by the Contracting Officer.  All third party software used which modifies or creates layers in AutoCAD shall adhere to the layering requirements in this standard.

# 3.	DRAWING SETUP

## 3.1	General

Drawing standards and symbology shall be in accordance with AIA Graphic Standards.

3 dimensional objects are permitted, but confine all objects to the Z=0 plane unless there is a specific reason for making 3 dimensional drawings.  3 dimensional drawings can cause incorrect distance measurements, due to the difference in elevation, which the person measuring may not be aware of.

## 3.2	Accuracy

All CAD drawings shall be drafted using precision input employing the most accurate source material available.  For all drawing entities, object snapping is required; all lines shall meet at intersections, tangents intersect at a single point, blocks are inserted properly without overlap, etc.

Contractors are responsible for the accuracy of all CAD drawings delivered to GSA, regardless of the accuracy of CAD drawings of previous projects furnished by GSA as a convenience to the contractor.

## 3.3	Drawing Sheet Sizes

All drawing sheets shall be submitted on sheets of one of the following standard metric dimensions, as specified in AIA Graphic Standards:

| SIZE | HORIZONTAL DIMENSION | VERTICAL DIMENSION |
| --- | --- | --- |
| A0 | 1190 mm | 840 mm |
| A1 | 840 mm | 595 mm |
| A2 | 595 mm | 420 mm |
| A3 | 420 mm | 295 mm |
| A4 | 280 mm | 216 mm |

## 3.4	Drawing Scales

Follow the GSA Metric Design Guide for all Design and Construction drawings.  Imperial units are required for assignment drawings.  The basic unit for metric drawings shall be millimeter.  The basic unit for Imperial drawings shall be inch.

The following drawings shall be drawn to full size (1:1); that is, all drawing elements shall be drawn to the exact dimensions of the object they represent.  Paper space may be used, but it is not required unless xrefs are used; see Section 4.1.  Drawing objects in imperial units in model space then scaling them to metric in a paper space viewport is also not acceptable.  If you are working from Imperial unit source CAD documents, you must scale them to full size in metric if the deliverables are required to be metric.

Architectural Plans

Mechanical Plans

Electrical Plans

Plumbing Plans

Structural Plans

Site Plans

Topographical Drawings

Industrial Engineering Drawings

Environmental Drawings

Waste Treatment Drawings

Details

Sections

Elevations

The following types of drawings may be drawn to any scale (or no scale):

Schedules

Riser Diagrams

Schematic Diagrams

Single Line Diagrams

## 3.5	Title Blocks

The following is a description of how to use GSA Region 3 standard titleblocks and layering system to set up your drawings.  These titleblocks are compliant with PBS 3490.1; each titleblock contains the disclaimer for each page, and the cover page inserts contain the disclaimer for cover pages.

1. Set Up Template Titleblock

- First, open the appropriate size titleblock for your project (below is a list of the titleblocks provided). The titleblock has been blocked and inserted for you; the block name is "TITLEBLOCK".  The titleblock contains attributed information for GSA use.  Since the titleblock has already been inserted, you must use the "DDATTE" command to edit the attributed information.  Note: H-A4.dwg does not contain a blocked titleblock; fill in the blanks with regular text.

- Once you have changed the necessary information, save the titleblock drawing as a drawing template file (DWT) or DWG, if you are using AutoCAD r14 or later.  Versions of AutoCAD prior to r14 dealt with templates differently, and they were referred to as prototypes.  (This will be used as a template for your project, saving you the time of reentering the same information for each new drawing in the same project).  You have now set up a template drawing for this project.  This method saves the time it would take to fill in all project-level information on each sheet separately, as well as ensures consistency of spelling and nomenclature.

- To start your project drawings using the template you have created, click File, New, Use a Template, and choose the titleblock drawing you created earlier, or if saved as a DWG, select File, Open.

- Drawing specific attributed information (such as drawing number, drawing title, etc.) can now be entered by again using the "DDATTE" command.  Fill in all known information.  Layer drawings can be inserted to create the layers needed for the specific drawing (see list below).  Save the drawing according the GSA file naming policy.

- The titleblock may not be submitted exploded.  The block name may not be changed.  The titleblock may not be nested within another block or brought in as an xref.  None of the attributes may be deleted or the tags renamed.  The titleblock may not be moved to a different layer.  The titleblock may be left in model space or moved to paper space.  Each drawing file may contain no more than one block insert called titleblock.  Drawings may not be placed side by side within the same file.  There is no restriction on how the floors are named in the drawing title, but use the floor number codes in section 4.3 for the floor number attribute.  If an attribute has no value, make it blank; do not leave the default value.  Do not allow values to extend beyond the edge of the titleblock area.

2. GSA PROVIDED TITLEBLOCKS

The following is a list of the GSA provided titleblocks; each contains blocked attribute information.

Each sheet file shall contain a sheet file titleblock.

H-A4 is 280mm x 216mm.  This size may be used for the convenience of printing a small drawing on a laser printer.  The A/E shall use this size only for the purpose of “information only” drawings, e.g. sketches.  All titleblock information must be completed.  The A4 size may not be used for official drawing submissions.

Each xref (model file) shall contain a model file information block.  It shall be frozen and reside in model space.  Other titleblock files are for sheet files.

TITLEBLOCK OPTIONS

Sheet file titleblocks:

X-YYr####.DWG

X: H indicates a horizontal titleblock; V indicates a vertical titleblock

YY: indicates the size

####: indicates the release of AutoCAD

Model file information blocks:

modelr14.dwg - for AutoCAD r14

modelr2000.dwg - for AutoCAD r2000 and later

3.  INSERT ADDITIONAL LAYERS

- After the titleblock information has been edited, you may add AIA layers by inserting the appropriate LAYER drawings provided, or by creating them manually.

- Layer drawing files have been provided for each of the disciplines which contain commonly used AIA 1997 layers.

The following is a list of those layer drawings and a brief description:

LYR_ARCH.DWG	Architectural drawing layers

LYR_ASSN.DWG	Assignment drawing layers

LYR_CIVL.DWG	Civil & Landscape drawing layers

LYR_FIRE.DWG	Fire protection drawing layers

LYR_MECH.DWG	Mechanical drawing layers

LYR_PLUM.DWG	Plumbing drawing layers

LYR_STRU.DWG	Structural drawing layers

LYR_T&E.DWG	Telecommunications & Electrical layers

- Once you have determined the discipline layers you require, just insert the appropriate layer drawing and this will load the corresponding layers.

The above layer drawings contain commonly used AIA layers; if other layers are needed, use the AIA CAD Layer Guidelines to create additional layers.  If you would like to include custom user-defined layers, permission must be granted by GSA, and a list and description of such layers must be submitted to GSA along with the drawing submission.

4.  MULTIPLE DRAWINGS PER FILE

- Multiple drawings may occur in a single file, but only where they are drawn on top of one another in model space and viewports are used to display different layers to generate each drawing sheet in a different layout.  Each drawing sheet shall be on a different layout.  The titleblocks shall reside in paper space.  Since each file may contain only one block named titleblock, it must be exploded or renamed on subsequent layouts.  (The BURST command, included with Autodesk Express Tools, is the most convenient way to explode attributes to text.)  Drawings laid next to each other in the same file are not acceptable.  Use of script files to turn on and off layers is prohibited.

- The drawing specific information in the titleblock such as file name, file date, drawing title, floor number and drawing number shall be entered according to the following priority:

1.	Assignment drawing

2.	Partition plan (if there is no assignment drawing)

3.	The first drawing in a sequence (if there is no assignment drawing and/or partition plan or there are multiple assignment drawings or partition plans).

5. GSA PROVIDED COVER SHEETS

The following is a list of the GSA provided cover sheet drawings.

H-COVRr####.dwg	Horizontal cover sheet drawing

V-COVRr####.dwg	Vertical cover sheet drawing

where #### indicates the release of AutoCAD

- Once the project specific template titleblock drawing has been created, insert the appropriate horizontal or vertical coversheet drawing.

- After the cover sheet has been inserted it may be necessary to scale the cover sheet to the size of the titleblock.  When you scale the cover sheet you should use the “REFERENCE” function within the “SCALE” command to ensure that it fits properly.

The cover sheet drawing may not be xrefed in.

6. CAD File Information

A box on the titleblocks has been created for CAD File Information; it is located next to, or below the KEY PLAN box.  This box shall contain the following if they apply:

A.  The names of any xrefs used in the drawing (including nested xrefs).

B.  A list of multiple-drawings per file if the drawing file contains more than one.

C. Any miscellaneous information necessary for GSA (drawing content information shall not be listed here).

Proceed with drafting.

# 4.	FILE NAMES AND STRUCTURES

## 4.1	Xref Assembly

Externally referenced files are not required, but may be used to produce more efficient, smaller drawing files, and provide easier drawing coordination.  Xrefs may be required for special types of drawings, such as assignment plans.  Xrefs shall be submitted in the same file directory as the sheet file(s) which reference them, and shall follow the 8.3 DOS convention.  Xref file names must not include a path or file directory.

If xrefs are used, they must be assembled in the following way:

Sheet file drawings are the “complete” drawings, which are plotted, as opposed to model file drawings, which are xrefed into the sheet files.

Xrefs, (also called model files), contain the drawing content, (the floor plans), drawn full size in model space.  Include the model file titleblock in the xref, as required in section 3.5.  There may be one or more model files for each sheet file.  Model file(s) are xrefed into the sheet file at full size, into model space.  The objects are then scaled through one (or more) paper space viewport(s), and seen in paper space at the size they will have on the printed page.  The sheet file titleblock resides in paper space.  The drawing can then be plotted from paper space at a scale of 1 to 1, in the units the drawing was drawn in.  For example, if the drawing is in metric, it shall be plotted from paper space at a scale of 1 drawing unit = 1 mm on paper, not 1 drawing unit = 1 inch on paper.  (There may be a special type of assembly used for assignment drawings, and additional requirements will be issued if that formatting is required.)  The following is an example:

## 4.2	Sheet File Drawing Numbers

All sheet file drawings shall be numbered using the following convention:  (Also, all files names must correspond to their respective drawing numbers.)

| - one letter | - one # | - - two #s |
| --- | --- | --- |
| DISCIPLINE | SHT. TYPE | SEQUENCE |

Discipline: shall be a letter code from the table below that most aptly describes the work shown on the drawing.

| Discipline | Code |
| --- | --- |
| General (including cover sheets) | G |
| Hazardous materials | H |
| Civil | C |
| Landscape | L |
| Structural | S |
| Architectural | A |
| Interiors | I |
| Equipment | Q |
| Fire Protection | F |
| Plumbing | P |
| Mechanical | M |
| Electrical | E |
| Telecommunications | T |
| Resource | R |
| Other disciplines | X |
| Contractor/shop drawing | Z |
| Survey/mapping | V |
| Civil work | W |
| Geotechnical | B |
| Process | D |
| Operations (includes facility and assignment drawing) | O (not zero) |

Sheet Type: shall be a code from the table below that most aptly describes the type of drawing.

| SHEET TYPE | CODE |
| --- | --- |
| General (cover sheets, symbols, legends, notes, etc.) | 0 (zero) |
| Plans (horizontal views) | 1 |
| Elevations (vertical views) | 2 |
| Sections (sectional views) | 3 |
| Large Scale (plans, elevations, or sections that are not details) | 4 |
| Details | 5 |
| Schedules and Diagrams | 6 |
| User Defined | 7 |
| User Defined | 8 |
| 3D Views (isometric, perspectives, photographs) | 9 |

Drawing Sequence: shall be a two-digit number indicating the sequence of drawings within a series.  “00” is not valid.  For drawing numbers 1 through 9, a 0 shall be the first digit.

SOME EXAMPLES:

This drawing number indicates a continuation (second sheet) of the cover sheet, perhaps for drawing legends or other general drawing information:

| G | 0 | 02 |
| --- | --- | --- |
| DISCIPLINE | SHT. TYPE | SEQUENCE |

This drawing number indicates the twelfth drawing in a series of architectural details.

| A | 5 | 12 |
| --- | --- | --- |
| DISCIPLINE | SHT. TYPE | SEQUENCE |

This drawing number indicates the second drawing in a series of utilities work  drawings:

| C | 1 | 02 |
| --- | --- | --- |
| DISCIPLINE | SHT. TYPE | SEQUENCE |

## 4.3	Model File Drawing Numbers

Xref file names are comprised of a one-character discipline code, followed by a two-letter drawing type, followed by a two-character floor code.  A floor number code is not required if it is not applicable, as with a detail drawing, for example.  If a drawing shows multiple floors, leave floor number blank.

| A | FP | B1 |
| --- | --- | --- |
| Discipline | Drawing Type | Floor Number |

Discipline Code - Two-character field with the second character as a hyphen.

| G | General |
| --- | --- |
| H | Hazardous materials |
| C | Civil |
| L | Landscape |
| S | Structural |
| A | Architectural |
| I | Interiors |
| Q | Equipment |
| F | Fire protection |
| P | Plumbing |
| M | Mechanical |
| E | Electrical |
| T | Telecommunications |
| R | Resource |
| X | Other disciplines |
| Z | Contractor/shop drawing |
| V | Survey/mapping |
| W | Civil work |
| B | Geotechnical |
| D | Process |
| O (not zero) | Operations (includes facility and assignment drawings) |

Drawing Type Codes – Apply to all disciplines.

| *-FP | Floor Plan |
| --- | --- |
| *-SP | Site Plan |
| *-DP | Demolition Plan |
| *-QP | Equipment Plan |
| *-XP | Existing Plan |
| *-RO | Roof plan |
| *-EL | Elevation |
| *-SC | Section |
| *-DT | Detail |
| *-SH | Schedule |
| *-3D | Isometric/3D |
| *-DG | Diagrams |

Drawing Type Code - Specific to Particular Disciplines.

| Architectural |
| --- |
| A-EP | Enlarged Plans |
| A-CP | Ceiling Plans |
| A-RP | Furniture Plans |
| A-NP | Finish Plans |
| Building/Facility Management |
| O-KY | Key drawing |
| O-SR | Source drawing |
| Interiors |
| I-EP | Enlarged Plans |
| I-CP | Ceiling Plans |
| I-RP | Furniture Plans |
| I-NP | Finish Plans |
| Structural |
| S-FP | Framing Plans |
| S-NP | Foundation Plans |
| Mechanical |
| M-HP | HVAC Ductwork Plans |
| M-PP | Piping Plans |
| M-CP | Control Plans |
| Plumbing |
| P-PP | Plumbing Plans |
| Fire Protection |
| F-KP | Sprinkler Plan |
| *-VP | Evacuation Plan |
| Electrical |
| E-LP | Lighting |
| E-PP | Power |
| E-GP | Grounding |
| E-CP | Communication |
| Telecommunications |
| T-TP | Telephone |
| T-DP | Data |
| Civil |
| C-RP | Roads/TOPO |
| C-GP | Grading |
| C-UP | Utility |
| C-EP | Environmental |
| C-SV | Survey |

Floor number

| 01 - 99 | First to 99th floor |
| --- | --- |
| GF | Ground Floor |
| LT | Loft |
| M1, M2, M3… | Mezzanine 1, 2, 3… |
| P1, P2, P3… | Penthouse 1, 2, 3… and Parking 1, 2, 3… If a building has both, start penthouse numbering where parking leaves off to avoid redundant file names |
| B1, B2, B3… | Basement 1, 2, 3… |
| L1, L2, L3… | Lower Level 1, 2, 3… |
| R1, R2, R3… | Roof Level 1, 2, 3… |
| SB | Sub-Basement |

## 4.4	File Names

All drawing file names shall correspond to their respective drawing number.  The file names of other file types, such as spreadsheets or specifications, shall indicate the content of the file.  All drawing file names shall follow the 8.3 DOS convention; other formats may have long file names.  If the file contains more than one drawing, the 3 user defined characters shall be MDF, (for Multiple Drawing File).  Supplemental CAD policies may require an alternate character instead of the hyphen.  No two files in the same submission set may have the same name.

SHEET FILE NAMES:

W-XYYZZZ.DWG	W	=	Discipline Code

-  	=  	Second character must be a hyphen*

X	= 	Sheet Type Code

YY	=	Drawing Sequence

ZZZ	=	User Defined Code (optional)

i.e. Submission Phase, Revision No.

*Supplemental CAD policies may require an alternate character instead of the hyphen.

Examples:

G-002-90.DWG		Cover sheet, 2nd sheet, 90% submission

A-512-R1.DWG		First revision of 12th Architectural details drawing

MODEL FILE NAMES:

W-XXYYZZ.DWG	W	=	Discipline Code

-  	=  	Second character must be a hyphen*

XX	= 	Drawing Type Code

YY	=	Floor Code

ZZ	=	User Defined Code (optional)

For example, A-FP01 would be the architectural, first floor plan.  A floor number code is not required if it is not applicable, as with a detail drawing, for example.

*Supplemental CAD policies may require an alternate character instead of the hyphen.

EXAMPLES OF OTHER FILES:

Refer to Section 6 - Project and Drawing Documentation

README.DOC	Word File

01010.DOC	Specification Word File

ESTIMATE.XLS	Excel File

SCHEDULE.MPP	Project File

# 5.	DATA STRUCTURE

## 5.1	Layering

All drawing files shall be produced using the long form layering conventions in the 1997 AIA CAD Layer Guidelines or the 2001 AIA CAD Layer Guidelines.  The 2001 Guide is part of the U.S. National CAD Standard Version 2.  The 2001 version is preferred, but the 1997 version is acceptable.  Specify which version was used in the README file.  In addition, layers “0” and “DEFPOINTS” are acceptable since they are part of AutoCAD.  Layers “G-ANNO-TTLB-TEXT”, “G-ANNO-TTLB-ATR1”, “G-ANNO-TTLB-ATR2”, and "G-ANNO-TTLB-SYMB" are also acceptable as they are referenced in the titleblock.  Do not use major or minor groups in conjunction with disciplines under which they are not listed.  For example, E-WALL is not a valid layer name; use A-WALL.

Since the AIA Layer Guidelines do not define any use for layer 0, do not place any objects on layer 0, unless required to do so by a supplemental policy document.  Layer 0 is a special layer which can be used to draw blocks on, if they are to inherit the properties of the layer which they are inserted on; but it is not required that blocks be drawn on layer 0.  (The “DEFPOINTS” layer is automatically created by AutoCAD when dimensioning is used.)

For all drawing entities, COLOR, LINETYPE, and LINEWEIGHT shall be BYLAYER; COLOR, LINETYPE, and LINEWEIGHT shall be assigned to each layer.

## 5.2	Linetypes

Use AutoCAD standard linetypes.  If other linetypes are needed, obtain permission from GSA, include the linetype definition files with the submission, and document this in the README.DOC.

## 5.3	Blocks

Block insertion points shall be located on the block at an intersection, end point, or mid point, or, for circles, at the center or a quadrant.  Nested blocks are blocks that contain one or more blocks.  It is preferred that nested blocks not be used, but if deemed necessary, they shall be documented in the README.DOC file.  Nested xrefs are permitted.

## 5.4	Hatching

Hatching patterns shall be used sparingly so as to minimize file size.  When used, hatching patterns shall be on their own layer(s) and shall be appropriately named: i.e. * - **** - PATT.  User-defined hatch patterns shall not be used.

## 5.5	Object Linking and Embedding (OLE)

Linked and embedded files shall be submitted in the same file directory as the drawing(s) to which they are linked or in which they are embedded.

## 5.6	AutoCAD Fonts

Drawings shall contain .SHX or .TTF (True Type Fonts) fonts only.  Plotted text must be legible at one-half the scale of the original drawing scale.  If fonts other than those listed below are to be used, permission must be granted by GSA and the font file must be included with the submission.

Arial

Arial Black

Arial Narrow

BankGothic Lt BT

BankGothic Md BT

Bookman Old Style

City Blueprint

Comic Scans MS

CommercialPi BT

CommercialScript BT

Complex

CountyBlueprint

Courier New

Dutch801 Rm BT

Dutch801 XBd BT

EuroRoman

Garamond

GDT

GothicE

GothicG

GothicI

GreekC

GreekS

Haettenschweiler

Impact

ISOCP

ISOCP2

ISOCP3

Italic

ItalicC

ItalicT

Monospac821 BT

Monotxt

PanRoman

RomanC

RomanD

RomanS

RomanT

Romantic

SansSerif

ScriptC

ScriptS

Simplex

Stylus BT

SuperFrench

Swis721 BdCnOul BT

Swis721 BdOul BT

Swis721 Blk BT

Swis721 BlkCn BT

Swis721 BlkEx BT

Swis721 BlkOul BT

Swis721 BT

Swis721 Cn BT

Swis721 Ex BT

Swis721 Lt BT

Swis721 LtCn BT

Swis721 LtEx BT

Syastro

Symap

Symath

Symol

Symeteo

Symusic

Tahoma

Technic

TechnicBold

TechnicLite

Times New Roman

Txt

UniversalMath  BT

Vineta BT

Wingdings

## 5.7	Fonts for Other Software

Other types of documents shall contain only the .TTF (True Type) fonts listed above.  In addition, Monotype Grotesque 1 (aka Grotesque MT - the official GSA font) may be used.

## 5.8	Plotting Parameters

Submitted hard copies are not required to be plotted from AutoCAD, but the electronic drawings are required to be able to accurately reproduce those hard copies when plotted from AutoCAD using ADI drivers and the following settings.

For your convenience, PCP and CTB files containing the standard pen tables are provided by GSA.

They are:

| standard r14 b&w.pcp | for plotting b&w r14 drawings in r14 |
| --- | --- |
| standard r14 color.pcp | for plotting color r14 drawings in r14 |
| standard r14 b&&w.ctb | for plotting b&w r14 drawings in r2000 |
| standard r14 color.ctb | for plotting color r14 drawings in r2000 |
| standard r2000 b&&w.ctb | for plotting b&w r2000 drawings in r2000 |
| standard r2000 color.ctb | for plotting color r2000 drawings in r2000 |

(the “&&” will appear as “&” in the pop list)

If any drawings are to be plotted in color, note this in the README file.

A. R2000 and later

Lineweights for R2000 and later shall be assigned to layers.  Any lineweight and any color may be assigned to any layer, unless prescribed by a supplemental standard.  All drawing object colors, linetypes, and lineweights shall be set to BYLAYER.

When plotting black and white drawings, set all plot colors to 7 in the style table.  For color drawings, set the plot color to “use object color”.

Set plot style table settings as follows:

| Style Table Parameter | Setting |
| --- | --- |
| plot color | For B&W: 7 For color plots: use object color |
| dither | off |
| grayscale | off |
| pen number | automatic (unless required by your plotter) |
| virtual pen | automatic (unless required by your plotter) |
| screening | 100 |
| linetype | use object linetype |
| adaptive | on |
| lineweight | use object lineweight |
| line end style | use object end style |
| line join style | use object join style |
| fill style | use object fill style |

Make sure the Plot with Plot Styles option is checked in the Plot dialog box.

B. R14 and earlier

The GSA Standard Pen Assignments shall be used to define lineweight for r14 and pre-r14 drawings.   The pen table also defines colors in the case of color plotting.  If black and white plotting is used, all plot colors shall be set to 7.  This will ensure consistency of all prints generated by a drawing file.  Pen Line Type shall be set to Continuous for all colors.  Generate various line types through assignment of the layers’ line type property.

The six standard line thicknesses are as follows:

| Line Thickness | Millimeters | Inches |
| --- | --- | --- |
| Thin | 0.18 | 0.007 |
| Medium | 0.25 | 0.010 |
| Medium Thick | 0.35 | 0.014 |
| Thick | 0.50 | 0.020 |
| Extra Thick | 0.70 | 0.028 |
| Optional | 1.00 | 0.040 |

Pen Table

| AutoCAD Color # | Width (mm) | Width (inches) | Plot Color for B&W DWGs | Plot Color for Color DWGs |
| --- | --- | --- | --- | --- |
| 1 | 0.18 | 0.007 | 7 | Black |
| 2 | 0.25 | 0.010 | 7 | Black |
| 3 | 0.35 | 0.014 | 7 | Black |
| 4 | 0.35 | 0.014 | 7 | Black |
| 5 | 0.50 | 0.020 | 7 | Black |
| 6 | 0.70 | 0.028 | 7 | Black |
| 7 | 0.25 | 0.010 | 7 | Black |
| 8 | 0.35 | 0.014 | 7 | Halftone |
| 9 | 1.00 | 0.040 | 7 | Black |
| 10 | 0.25 | 0.010 | 7 | Black |
| 11 | 0.35 | 0.014 | 7 | Black |
| 12 | 0.50 | 0.020 | 7 | Black |
| 13 | 0.70 | 0.028 | 7 | Black |
| 14 | 1.00 | 0.040 | 7 | Black |
| 15 | 0.50 | 0.020 | 7 | Black |
| 16 | 0.70 | 0.028 | 7 | Black |
| 17 | 0.70 | 0.028 | 7 | Halftone |
| 18 | 0.35 | 0.014 | 7 | Halftone |
| 19 | 1.00 | 0.040 | 7 | Black |
| 20 | 0.18 | 0.007 | 7 | Rust |
| 21 | 0.25 | 0.010 | 7 | Rust |
| 22 | 0.35 | 0.014 | 7 | Rust |
| 23 | 0.50 | 0.020 | 7 | Rust |
| 24 | 0.70 | 0.028 | 7 | Rust |
| 25 | 1.00 | 0.040 | 7 | Rust |
| 26 | 0.70 | 0.028 | 7 | Rust |
| 27 | 0.70 | 0.028 | 7 | Rust |
| 28 | 0.35 | 0.014 | 7 | Rust |
| 29 | 1.00 | 0.040 | 7 | Rust |
| 30 | 0.18 | 0.007 | 7 | Black |
| 31 | 0.25 | 0.010 | 7 | Black |
| 32 | 0.35 | 0.014 | 7 | Black |
| 33 | 0.50 | 0.020 | 7 | Black |
| 34 | 0.70 | 0.028 | 7 | Black |
| 35 | 1.00 | 0.040 | 7 | Black |
| 36 | 0.70 | 0.028 | 7 | Black |
| 37 | 0.70 | 0.028 | 7 | Halftone |
| 38 | 0.35 | 0.014 | 7 | Halftone |
| 39 | 1.00 | 0.040 | 7 | Black |
| 40 | 0.18 | 0.007 | 7 | Gold |
| 41 | 0.25 | 0.010 | 7 | Gold |
| 42 | 0.35 | 0.014 | 7 | Gold |
| 43 | 0.50 | 0.020 | 7 | Gold |
| 44 | 0.70 | 0.028 | 7 | Gold |
| 45 | 1.00 | 0.040 | 7 | Gold |
| 46 | 0.70 | 0.028 | 7 | Gold |
| 47 | 0.70 | 0.028 | 7 | Gold |
| 48 | 0.35 | 0.014 | 7 | Gold |
| 49 | 1.00 | 0.040 | 7 | Gold |
| 50 | 0.18 | 0.007 | 7 | Black |
| 51 | 0.25 | 0.010 | 7 | Black |
| 52 | 0.35 | 0.014 | 7 | Black |
| 53 | 0.50 | 0.020 | 7 | Black |
| 54 | 0.70 | 0.028 | 7 | Black |
| 55 | 1.00 | 0.040 | 7 | Black |
| 56 | 0.70 | 0.028 | 7 | Black |
| 57 | 0.70 | 0.028 | 7 | Halftone |
| 58 | 0.35 | 0.014 | 7 | Halftone |
| 59 | 1.00 | 0.040 | 7 | Black |
| 60 | 0.18 | 0.007 | 7 | Olive |
| 61 | 0.25 | 0.010 | 7 | Olive |
| 62 | 0.35 | 0.014 | 7 | Olive |
| 63 | 0.50 | 0.020 | 7 | Olive |
| 64 | 0.70 | 0.028 | 7 | Olive |
| 65 | 1.00 | 0.040 | 7 | Olive |
| 66 | 0.70 | 0.028 | 7 | Olive |
| 67 | 0.70 | 0.028 | 7 | Olive |
| 68 | 0.35 | 0.014 | 7 | Olive |
| 69 | 1.00 | 0.040 | 7 | Olive |
| 70 | 0.18 | 0.007 | 7 | Black |
| 71 | 0.25 | 0.010 | 7 | Black |
| 72 | 0.35 | 0.014 | 7 | Black |
| 73 | 0.50 | 0.020 | 7 | Black |
| 74 | 0.70 | 0.028 | 7 | Black |
| 75 | 1.00 | 0.040 | 7 | Black |
| 76 | 0.70 | 0.028 | 7 | Black |
| 77 | 0.70 | 0.028 | 7 | Halftone |
| 78 | 0.35 | 0.014 | 7 | Halftone |
| 79 | 1.00 | 0.040 | 7 | Black |
| 80 | 0.18 | 0.007 | 7 | Green |
| 81 | 0.25 | 0.010 | 7 | Green |
| 82 | 0.35 | 0.014 | 7 | Green |
| 83 | 0.50 | 0.020 | 7 | Green |
| 84 | 0.70 | 0.028 | 7 | Green |
| 85 | 1.00 | 0.040 | 7 | Green |
| 86 | 0.70 | 0.028 | 7 | Green |
| 87 | 0.70 | 0.028 | 7 | Green |
| 88 | 0.35 | 0.014 | 7 | Green |
| 89 | 1.00 | 0.040 | 7 | Green |
| 90 | 0.18 | 0.007 | 7 | Black |
| 91 | 0.25 | 0.010 | 7 | Black |
| 92 | 0.35 | 0.014 | 7 | Black |
| 93 | 0.50 | 0.020 | 7 | Black |
| 94 | 0.70 | 0.028 | 7 | Black |
| 95 | 1.00 | 0.040 | 7 | Black |
| 96 | 0.70 | 0.028 | 7 | Black |
| 97 | 0.70 | 0.028 | 7 | Halftone |
| 98 | 0.35 | 0.014 | 7 | Halftone |
| 99 | 1.00 | 0.040 | 7 | Black |
| 100 | 0.18 | 0.007 | 7 | Forest-Green |
| 101 | 0.25 | 0.010 | 7 | Forest-Green |
| 102 | 0.35 | 0.014 | 7 | Forest-Green |
| 103 | 0.50 | 0.020 | 7 | Forest-Green |
| 104 | 0.70 | 0.028 | 7 | Forest-Green |
| 105 | 1.00 | 0.040 | 7 | Forest-Green |
| 106 | 0.70 | 0.028 | 7 | Forest-Green |
| 107 | 0.70 | 0.028 | 7 | Forest-Green |
| 108 | 0.35 | 0.014 | 7 | Forest-Green |
| 109 | 1.00 | 0.040 | 7 | Forest-Green |
| 110 | 0.18 | 0.007 | 7 | Black |
| 111 | 0.25 | 0.010 | 7 | Black |
| 112 | 0.35 | 0.014 | 7 | Black |
| 113 | 0.50 | 0.020 | 7 | Black |
| 114 | 0.70 | 0.028 | 7 | Black |
| 115 | 1.00 | 0.040 | 7 | Black |
| 116 | 0.70 | 0.028 | 7 | Black |
| 117 | 0.70 | 0.028 | 7 | Halftone |
| 118 | 0.35 | 0.014 | 7 | Halftone |
| 119 | 1.00 | 0.040 | 7 | Black |
| 120 | 0.18 | 0.007 | 7 | Teal |
| 121 | 0.25 | 0.010 | 7 | Teal |
| 122 | 0.35 | 0.014 | 7 | Teal |
| 123 | 0.50 | 0.020 | 7 | Teal |
| 124 | 0.70 | 0.028 | 7 | Teal |
| 125 | 1.00 | 0.040 | 7 | Teal |
| 126 | 0.70 | 0.028 | 7 | Teal |
| 127 | 0.70 | 0.028 | 7 | Teal |
| 128 | 0.35 | 0.014 | 7 | Teal |
| 129 | 1.00 | 0.040 | 7 | Teal |
| 130 | 0.18 | 0.007 | 7 | Black |
| 131 | 0.25 | 0.010 | 7 | Black |
| 132 | 0.35 | 0.014 | 7 | Black |
| 133 | 0.50 | 0.020 | 7 | Black |
| 134 | 0.70 | 0.028 | 7 | Black |
| 135 | 1.00 | 0.040 | 7 | Black |
| 136 | 0.70 | 0.028 | 7 | Black |
| 137 | 0.70 | 0.028 | 7 | Halftone |
| 138 | 0.35 | 0.014 | 7 | Halftone |
| 139 | 1.00 | 0.040 | 7 | Black |
| 140 | 0.18 | 0.007 | 7 | Cyan |
| 141 | 0.25 | 0.010 | 7 | Cyan |
| 142 | 0.35 | 0.014 | 7 | Cyan |
| 143 | 0.50 | 0.020 | 7 | Cyan |
| 144 | 0.70 | 0.028 | 7 | Cyan |
| 145 | 1.00 | 0.040 | 7 | Cyan |
| 146 | 0.70 | 0.028 | 7 | Cyan |
| 147 | 0.70 | 0.028 | 7 | Cyan |
| 148 | 0.35 | 0.014 | 7 | Cyan |
| 149 | 1.00 | 0.040 | 7 | Cyan |
| 150 | 0.18 | 0.007 | 7 | Black |
| 151 | 0.25 | 0.010 | 7 | Black |
| 152 | 0.35 | 0.014 | 7 | Black |
| 153 | 0.50 | 0.020 | 7 | Black |
| 154 | 0.70 | 0.028 | 7 | Black |
| 155 | 1.00 | 0.040 | 7 | Black |
| 156 | 0.70 | 0.028 | 7 | Black |
| 157 | 0.70 | 0.028 | 7 | Halftone |
| 158 | 0.35 | 0.014 | 7 | Halftone |
| 159 | 1.00 | 0.040 | 7 | Black |
| 160 | 0.18 | 0.007 | 7 | Blue |
| 161 | 0.25 | 0.010 | 7 | Blue |
| 162 | 0.35 | 0.014 | 7 | Blue |
| 163 | 0.50 | 0.020 | 7 | Blue |
| 164 | 0.70 | 0.028 | 7 | Blue |
| 165 | 1.00 | 0.040 | 7 | Blue |
| 166 | 0.70 | 0.028 | 7 | Blue |
| 167 | 0.70 | 0.028 | 7 | Blue |
| 168 | 0.35 | 0.014 | 7 | Blue |
| 169 | 1.00 | 0.040 | 7 | Blue |
| 170 | 0.18 | 0.007 | 7 | Black |
| 171 | 0.25 | 0.010 | 7 | Black |
| 172 | 0.35 | 0.014 | 7 | Black |
| 173 | 0.50 | 0.020 | 7 | Black |
| 174 | 0.70 | 0.028 | 7 | Black |
| 175 | 1.00 | 0.040 | 7 | Black |
| 176 | 0.70 | 0.028 | 7 | Black |
| 177 | 0.70 | 0.028 | 7 | Halftone |
| 178 | 0.35 | 0.014 | 7 | Halftone |
| 179 | 1.00 | 0.040 | 7 | Black |
| 180 | 0.18 | 0.007 | 7 | Navy |
| 181 | 0.25 | 0.010 | 7 | Navy |
| 182 | 0.35 | 0.014 | 7 | Navy |
| 183 | 0.50 | 0.020 | 7 | Navy |
| 184 | 0.70 | 0.028 | 7 | Navy |
| 185 | 1.00 | 0.040 | 7 | Navy |
| 186 | 0.70 | 0.028 | 7 | Navy |
| 187 | 0.70 | 0.028 | 7 | Navy |
| 188 | 0.35 | 0.014 | 7 | Navy |
| 189 | 1.00 | 0.040 | 7 | Navy |
| 190 | 0.18 | 0.007 | 7 | Black |
| 191 | 0.25 | 0.010 | 7 | Black |
| 192 | 0.35 | 0.014 | 7 | Black |
| 193 | 0.50 | 0.020 | 7 | Black |
| 194 | 0.70 | 0.028 | 7 | Black |
| 195 | 1.00 | 0.040 | 7 | Black |
| 196 | 0.70 | 0.028 | 7 | Black |
| 197 | 0.70 | 0.028 | 7 | Halftone |
| 198 | 0.35 | 0.014 | 7 | Halftone |
| 199 | 1.00 | 0.040 | 7 | Black |
| 200 | 0.18 | 0.007 | 7 | Purple |
| 201 | 0.25 | 0.010 | 7 | Purple |
| 202 | 0.35 | 0.014 | 7 | Purple |
| 203 | 0.50 | 0.020 | 7 | Purple |
| 204 | 0.70 | 0.028 | 7 | Purple |
| 205 | 1.00 | 0.040 | 7 | Purple |
| 206 | 0.70 | 0.028 | 7 | Purple |
| 207 | 0.70 | 0.028 | 7 | Purple |
| 208 | 0.35 | 0.014 | 7 | Purple |
| 209 | 1.00 | 0.040 | 7 | Purple |
| 210 | 0.18 | 0.007 | 7 | Black |
| 211 | 0.25 | 0.010 | 7 | Black |
| 212 | 0.35 | 0.014 | 7 | Black |
| 213 | 0.50 | 0.020 | 7 | Black |
| 214 | 0.70 | 0.028 | 7 | Black |
| 215 | 1.00 | 0.040 | 7 | Black |
| 216 | 0.70 | 0.028 | 7 | Black |
| 217 | 0.70 | 0.028 | 7 | Halftone |
| 218 | 0.35 | 0.014 | 7 | Halftone |
| 219 | 1.00 | 0.040 | 7 | Black |
| 220 | 0.18 | 0.007 | 7 | Magenta |
| 221 | 0.25 | 0.010 | 7 | Magenta |
| 222 | 0.35 | 0.014 | 7 | Magenta |
| 223 | 0.50 | 0.020 | 7 | Magenta |
| 224 | 0.70 | 0.028 | 7 | Magenta |
| 225 | 1.00 | 0.040 | 7 | Magenta |
| 226 | 0.70 | 0.028 | 7 | Magenta |
| 227 | 0.70 | 0.028 | 7 | Magenta |
| 228 | 0.35 | 0.014 | 7 | Magenta |
| 229 | 1.00 | 0.040 | 7 | Magenta |
| 230 | 0.18 | 0.007 | 7 | Black |
| 231 | 0.25 | 0.010 | 7 | Black |
| 232 | 0.35 | 0.014 | 7 | Black |
| 233 | 0.50 | 0.020 | 7 | Black |
| 234 | 0.70 | 0.028 | 7 | Black |
| 235 | 1.00 | 0.040 | 7 | Black |
| 236 | 0.70 | 0.028 | 7 | Black |
| 237 | 0.70 | 0.028 | 7 | Halftone |
| 238 | 0.35 | 0.014 | 7 | Halftone |
| 239 | 1.00 | 0.040 | 7 | Black |
| 240 | 0.18 | 0.007 | 7 | Red |
| 241 | 0.25 | 0.010 | 7 | Red |
| 242 | 0.35 | 0.014 | 7 | Red |
| 243 | 0.50 | 0.020 | 7 | Red |
| 244 | 0.70 | 0.028 | 7 | Red |
| 245 | 1.00 | 0.040 | 7 | Red |
| 246 | 0.70 | 0.028 | 7 | Red |
| 247 | 0.70 | 0.028 | 7 | Red |
| 248 | 0.35 | 0.014 | 7 | Red |
| 249 | 1.00 | 0.040 | 7 | Red |
| 250 | 0.25 | 0.010 | 7 | Halftone |
| 251 | 0.35 | 0.014 | 7 | Halftone |
| 252 | 0.50 | 0.020 | 7 | Halftone |
| 253 | 0.70 | 0.028 | 7 | Halftone |
| 254 | 1.00 | 0.040 | 7 | Halftone |
| 255 | 1.00 | 0.040 | 7 | Black |

# 6.	PROJECT AND DRAWING DOCUMENTATION

## 6.1	General

With every submission, the A/E shall include a README.DOC, and shall be a Word document.  Label media with the project title, project number, submission stage, submission date, and any other pertinent information.

## 6.2	README.DOC File

The README.DOC file MUST include the following documentation:

- Project Documentation and Drawing Audit Form

- Description of user-defined code in drawing file names

- Inventory list of all sheet drawing file names, their xrefs, their description, what scale they are to be plotted at, and whether they should be plotted from paper or model space.  If this is the same for all, it only needs to be stated once.  Note any drawings which are to be plotted in color.

Any deviations from this policy must be approved by GSA and documented in the README file.

Other documentation that must be included (if applicable) in the README.DOC file include:

- List of user-defined layers

- List of user-defined linetypes

- List any nonstandard fonts

- Any third party software used to create the files

## 6.3	Project Documentation and Drawing Audit Form

This form is in Appendix A of this document.  The A/E shall complete this form and include it in the README.DOC file with each submission.  The A/E shall verify that all drawing files in the submittal package meet the requirements in the “Drawing Audit Checklist”.  At the Contracting Officer’s discretion, a submission containing one or more drawing files that do not meet the standard may be rejected.

## 6.4	Other Project and Drawing Reference Files

Other reference files include all non-DWG files that the A/E is including with the submission.  Such files might include:

- Specifications

- Cost Estimates

- Project Schedules

- Photographs

Note: Specifications must be the most recent version of AIA Master Specs at the time of contract award.

APPENDIX  A

# PROJECT  DOCUMENTATION and DRAWING AUDIT FORM

###### PROJECT DOCUMENTATION

BUILDING NAME:

BUILDING ADDRESS:

BUILDING NUMBER (S):

GSA PROJECT CONTROL NUMBER:

PROJECT TITLE:

SUBMITTAL STAGE:

SUBMITTAL DATE:

GSA PROJECT MANAGER:

PRIME A/E FIRM:

A/E’s ADDRESS:

A/E’s PHONE:

A/E PROJECT MANAGER:

A/E’s CONTRACT NO.:

VERSION OF CAD POLICY USED:

###### DRAWING INFORMATION

CAD SOFTWARE and VERSION:

VERSION OF AIA LAYERING STANDARD USED:

THIRD PARTY SOFTWARE and VERSION:

COMPRESSION SOFTWARE USED:

###### DRAWING AUDIT CHECKLIST

| ü | Item |
| --- | --- |
|  | AUDIT the drawing to ensure it is error-free |
|  | PURGE drawing of unused blocks, layers, linetypes, etc. (except for special layers which may be required for assignment drawings in supplemental CAD policies) |
|  | Select all objects and ensure COLOR, LINETYPE, and LINEWEIGHT (r2000) are set to BYLAYER |
|  | ZOOM drawing to EXTENTS and save drawing in the space from which it is to be plotted. |
|  | Delete any extraneous objects outside the titleblock unless they are there to position the titleblock on the paper. |
|  | Do not leave any unused layout tabs, except one is allowed if using none, since AutoCAD will not allow 0 layouts. |
|  | GRIDMODE is set to 0 |
|  | SNAPMODE is set to 0 |
|  | PDMODE is set to 0 |
|  | PDSIZE is set to 0 |
|  | QTEXTMODE is set to 0 |
|  | ATTMODE is set to 1 |
|  | For metric drawings, set LUNITS to 2. For Imperial drawings, set LUNITS to 4. |
|  | ISAVEPERCENT is set to 0 (system variable; one time only) |