# FINAL REPORT

on

Data Acquisition and Processing

for the

# Airborne Magnetic Survey

# of

# The Excelsior Mountains and South Wassuk Range of Western Nevada

on behalf of the

# United States Geological Survey

# Brian Schacht   P. Geoph.

# Ottawa, Ontario, Canada

# March, 2001

# TABLE OF CONTENTS

# 1.	INTRODUCTION	2

2.	TECHNICAL SPECIFICATIONS	3

  - SURVEY LOCATION	3

  - FLIGHT SPECIFICATIONS	3

2.3	TOLERANCES	3

2.4	SURVEY EQUIPMENT	4

3.	PERSONNEL	5

4.	SURVEY OPERATIONS	6

4.1	GENERAL	6

4.2	DIURNAL CONDITIONS	6

4.3	GENERAL WEATHER CONDITIONS	6

4.4	QUALITY CONTROL AND FIELD PROCESSING	6

5.	CALIBRATION AND TEST RESULTS	7

5.1	GPS BASE STATION	7

5.2	MAGNETIC LAG TEST	7

5.3	GPS LAG / ACCURACY TEST	8

5.4	FIGURE OF MERIT	10

  - ALTIMETER CALIBRATION	10

6.	FINAL MAGNETIC DATA PROCESSING	11

6.1	NOISE EDITING	11

6.2	NOISE FILTERING	11

6.3	DIURNAL SUBTRACTION	12

6.4	IGRF CORRECTION	12

6.5	UPWARD/DOWNWARD CONTINUATION	12

6.6	LEVELLING	12

6.7	GRIDDING	13

6.8	GRID LEVELLING	13

7.	DELIVERABLES	14

  - MAPS		14

7.2	REPORT	14

7.3	DIGITAL ARCHIVES	14

APPENDIX:	DIGITAL ARCHIVE FORMAT DESCRIPTION			 15

# 1.	INTRODUCTION

An aeromagnetic survey was flown over three conjoined areas within the Excelsior Mountains and Southern Wassuk Range of western Nevada.  This same survey covered part of Death Valley, California.  The flying was completed between December 5, 2000, and January 14, 2001, by Fugro Airborne Surveys on behalf of the United States Geological Survey (see figure 1).  A 1:100,000 scale contour map and digital grid of the total magnetic field were produced, as well as a digital grid of radar altimeter (ground clearance) data.

2.	TECHNICAL SPECIFICATIONS

This section describes in detail the guidelines followed throughout the performance of the project; tolerances and instruments are also presented here.

  - SURVEY LOCATION

The three conjoined western Nevada areas (1, 2, & 4) are bounded by the following co-ordinates (NAD27 UTM and degrees X 1,000,000):

404000.00  4255000.00    38262393  -118055996

409100.00  4237100.00    38164519  -118022131

412000.00  4237100.00    38164623  -118002197

412000.00  4212600.00    38033142  -118001106

361100.00  4212600.00    38030844  -118345912

361100.00  4248600.00    38223605  -118352448

340200.00  4248600.00    38222349  -118494545

331300.00  4259700.00    38281754  -118560163

331300.00  4264500.00    38305318  -118560580

347200.00  4264500.00    38310352  -118450957

356400.00  4255000.00    38260094  -118384281

# 2.2	FLIGHT SPECIFICATIONS

Traverse Line Direction		N - S

Traverse Line Spacing			250 m

Control Line Direction			E - W

Control Line Spacing			1,500 m

Terrain Clearance				168-1217 m+ - see section 2.3 - “Flying Height”.

Line kilometers:				11,259.77

Average Sampling Interval		7.5 m

# 2.3	TOLERANCES

Lines (or segments of lines crossing two control lines, or segments of control lines crossing several lines) were re-flown when any of the following tolerances were exceeded:

# Navigation

- Nominal line spacing must not be exceeded by more than 50% for a distance of more than 3.2 km.

Flight Height

- In order to maintain similar elevations at all traverse and control line intersections, even when climbing or descending steeply, the Fugro ACCUDRAPE system utilizes a pre-planned digital drape surface which the onboard computer compares with the GPS xyz to feed corrections to the pilot.

- Deviations from the pre-planned drape elevation must not exceed 100 m.  The precipitous mountains flanking all survey blocks necessitated pre-planned drape surfaces with ground clearance exceeding 1217 m (4000’) over the valleys (the radar altimeter maximum is 1217 m).  Less than 1% of the data could be flown below 213 m (700’).

Magnetic Diurnal

- Deviations must not be greater than 2 nT from a 40 second chord.  The ground station magnetometer operated during all data acquisition.

# Airborne Magnetometer Noise

- “Maneuver” noise must not exceed an envelope of ±0.1 nT over more than 10% of any line.  This was monitored on the analog chart with a fourth difference and a high-pass filter.

- A standard Figure of Merit must be less than 1.5 nT.

- Heading errors must be within 1 nT between reciprocal headings.

# 2.4	SURVEY EQUIPMENT

# Table 2.4.a lists major characteristics of the fixed-wing survey aircraft.

| Registration | Endurance | Engines | Manufacturer | Type | No. of Seats | Average Speed |
| --- | --- | --- | --- | --- | --- | --- |
| C-FZLK | 6.5 hours | 1 Turbine | Cessna | Caravan 208 | 3 | 75 m/sec |

## Table 2.4.a  Survey Aircraft

Table 2.4.b lists the geophysical equipment installed in C-FZLK throughout the survey.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| Data Acquisition System | Fugro Airborne Surveys | GeoDAS | Pentium computer based, real-time, data synchronization and recording |
| Magnetometer | Scintrex | CS-2 | Cesium Vapour,10 Hz Sampling, 0.005 nT Sensitivity,0.001 nT Resolution |
| Compensator | RMS | AADC | 27 Term |
| Digital Backup | Iomega | Zip Drive | 100 Mb removable hard drive |
| Analogue Recorder | RMS | GR-33a-1 | Dot Matrix |
| Radar Altimeter | TRT | AVH-8 | 10 Hz Sampling, Accuracy ±2% |
| Barometric Altimeter | Rosemount | 1241M | 10 Hz Sampling, Accuracy ±5 m |
| Omnistar Receiver | Trimble |  | Real-time differential GPS correction |
| GPS Receiver | Sercel | NR103 | 10 Channel |
| Video Camera | Panasonic | WVC 1302 | Colour |
| Video Cassette Recorder | Panasonic | AG2400 | NTSC |

# Table 2.4.b  Airborne Geophysical Equipment

# Table 2.4.c lists the components of the ground-based reference station.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| Magnetometer | Scintrex | CS-2 | Cesium Vapour, 2 Hz Sampling, 0.005 nT Sensitivity, 0.01 nT Resolution |
| GPS Receiver | Sercel | NR-103 | 10 Channel |

# Table 2.4.c  Ground Reference Station

The ground magnetometer was mounted in a magnetically quiet area; its clock was synchronized with the GPS time signal.  The GPS data logger records all of the raw range data stream.  The Trajecto differential correction software matches the output from the airborne GPS system and the ground GPS system during the data reduction process.

# Table 2.4.d lists the equipment and software used to perform the field processing.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| PC | Dell | Inspiron 7500 | 800 MHz Pentium |
| Printer | HP | HP950C | A4 Colour |
| Data Processing Software | Fugro Airborne Surveys | Gmaps | DOS & Windows |
| Image Processing Software | ERMapper | Version 5.5 | Windows 95/98 |
| GPS Processing Software | Sercel | Trajecto | DOS |

# Table 2.4.d  Field Processing System

3.	PERSONNEL

| NAME | TITLE | PROJECT POSITION |
| --- | --- | --- |
| Robb, Jeff | Aircraft Maintenance Engineer | Aircraft Maintenance |
| Lamirande, Ken | Electronics Technician | Electronics Operator |
| Reed, Travis | Electronics Technician | Electronics Operator |
| Lyall, Ron | Operations Manager | Processor, Logistics |
| Williston, Mark | Pilot | Survey Pilot |
| Thomas, Jeff | Pilot | Survey Pilot |

### Table 3   Field Project Personnel

4.	SURVEY OPERATIONS

  - GENERAL

The production phase of the project began in Bishop, California, on December 5th , 2000, and the final production flight was made on January 14th, 2001.  The Comfort Inn provided crew accommodation and space for the field processing office.

  - DIURNAL CONDITIONS

Magnetic diurnal variation was exceptionally quiet.  Deviations never reached the specification limit.

  - GENERAL WEATHER CONDITIONS

Weather conditions were frequently unfavourable for survey flying due to high turbulence or cloud cover in the mountains.  Ten days were lost.

  - QUALITY CONTROL AND FIELD PROCESSING

- To check the data for adherence to contract specifications and move the data closer to the final stage, the following procedures were followed for each flight (details in section 6):

- downloading and verification of aircraft data;

- downloading and verification of GPS and magnetic base station data;

- post-processing of GPS data using SERCEL TRAJECTOGRAPHY software;

- merging of navigation data with geophysical data including transformation of coordinates from WGS84 latitude/longitude to UTM x, y coordinates in the local spheroid;

- creation of flight path plots and evaluation of compliance with contract specifications;

- spike and null value location and removal from the magnetic and altimeter data;

- computing of a drape surface quality control field for evaluation of compliance with the contract specifications;

- computing of magnetic noise channel for evaluation of data quality and compliance with contract specifications;

- evaluation of diurnal data quality, and compliance with contract specifications;

- correction of magnetic data for I.G.R.F. gradient;

- noise filtering of magnetic and altimeter fields;

- correction of magnetic field for altitude deviations;

- backing-up of all field data.

At regular intervals, the corrected magnetic data were levelled and gridded for quality inspection including real-time shade enhancement.

5.	CALIBRATION AND TEST RESULTS

5.1	GPS BASE STATION

To apply post-flight differential GPS corrections to the survey data, a GPS base station was installed near the crew’s hotel.  The location of the GPS base station antenna was determined by averaging positions over a 24 hour period.  The location was 37o 22’ 17.28” N latitude, 118o 22’ 8.46” W longitude, elevation 1,255 m, on the WGS spheroid.

  - MAGNETIC LAG TEST

The camera on-board the aircraft records its position, A, relative to the ground, at time t0.  In fact the sensor will arrive over A at time t1 (>t0).  Furthermore, because of electronic delays, the reading at time t1 will not be recorded until time t2 (>t1).  The difference t2-t0 represents the lag between the actual aircraft position and the x y position tied to the magnetic reading on disk.  A lag test was performed by flying the aircraft at survey altitude in opposite directions over a sharp magnetic feature.  The position of the magnetic feature was referenced to a visible feature recorded by the video system, in this case a bridge, which was the anomaly source.  By superimposing a plot of the east-west anomaly over the west-east anomaly, the video-picked position of the bridge can be transposed onto its counterpart; and one-half the difference between the two video-picked positions equals the magnetic system lag.  The lag was 0.7 seconds, or 7 magnetic samples, for aircraft C-FZLK.  These values were used to correct for magnetic system lag throughout the survey.

5.3	GPS LAG / ACCURACY.TEST

A cloverleaf flown over the established co-ordinates of the Canadian Geological Survey test site was used to measure the lag in the GPS positioning, with regard to the video camera position.  A value of 0.2 seconds resulted in a best fit with the video position.  Once the lag is applied (as in figure 5.3) the cloverleaf intersection is used to test the accuracy of the GPS positioning.

| Aircraft: |  | Cessna Caravan |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Registration: |  | C-FZLK |  |  |  |
| Date: |  | November 25, 2000 |  |  |  |
| Location: |  | Bourget, Ontario, Canada |  |  |  |
| Altitude: |  | 400 ft mean terrain clearance |  |  |  |
| DIRECTION | FIDUCIAL CLOSEST TO TARGET | OFFSET FROM TARGET DUE TO PILOT ERROR | Line # on Video |  |  |
|  | (from video) | (estimate in metres & direction) |  |  |  |
| South | 66216.56 | 0 | Line 10 |  |  |
| West | 66326.92 | 3 N | Line 11 |  |  |
| North | 66413.50 | 20 E | Line 12 |  |  |
| East | 66506.22 | 5 N | Line 13 |  |  |
| South | 66595.44 | 5 W | Line 14 |  |  |
| West | 66709.76 | 5 N | Line 15 |  |  |
| East | 66884.10 | 0 | Line 17 |  |  |
| North | 66992.44 | 15 E | Line 18 |  |  |

TABLE 5.3 GPS LAG / ACCURACY TEST

5.4	FIGURE OF MERIT (FOM)

The figure of merit is the measurement of the ability of the compensation system to remove the effects of aircraft maneuvers from the total field data.  During the FOM test the aircraft is flown into a quiet magnetic area and put through a series of pitches (±5o), rolls (±10o) and yaws (±5o) to examine the noise remaining in the signal after the 27 term automatic compensation algorithm has been applied to the data.

|  | Figure of Merit |  |  |  |
| --- | --- | --- | --- | --- |
| Aircraft: |  | Cessna Caravan |  |  |
| Registration: |  | C-FZLK |  |  |
| Magnetometer: |  | Cesium vapor, stinger mounted |  |  |
| Sampling Rate: |  | 10 Hz |  |  |
| Date: |  | December 2, 2000 |  |  |
| Location: |  | Bishop, California |  |  |
| HEADING | MANOEUVER | VALUE (nT) | HEADING |  |
|  |  |  | TOTAL (nT) |  |
| NORTH | PITCH | 0.18 |  |  |
|  | ROLL | 0.08 |  |  |
|  | YAW | 0.06 | 0.32 |  |
| EAST | PITCH | 0.12 |  |  |
|  | ROLL | 0.07 |  |  |
|  | YAW | 0.08 | 0.27 |  |
| SOUTH | PITCH | 0.08 |  |  |
|  | ROLL | 0.06 |  |  |
|  | YAW | 0.04 | 0.18 |  |
| WEST | PITCH | 0.08 |  |  |
|  | ROLL | 0.06 |  |  |
|  | YAW | 0.06 | 0.20 |  |
|  |  | FOM VALUE | 0.97 | nT |
| AVERAGE MANEUVER NOISE ( FOM / 12 ) |  |  | 0.08 | nT |

# Table 5.4   C-FZLK Figure of Merit

# 5.5	ALTIMETER CALIBRATION

# On November 24, 2000, the radar, barometric, and GPS altimeters were compared by flying at terrain clearances of 200’, 300’, 400’, 500’, 600’, 800’, and 1000’ over a flat portion of the Ottawa river.  The results reconfirmed that all altimeters aboard C-FZLK are functioning normally.

# 6.	FINAL DATA PROCESSING

Final data reduction was undertaken at the Fugro Airborne Surveys processing center in Ottawa, Canada between January and February, 2001.  In general, final processing consisted of the following operations:

- final levelling of the total field magnetic data;

- image and 1:100,000 scale map analysis of the total field and levelling compensations by a geophysicist for any residual levelling or positioning errors or gridding artifacts;

- correction of errors;

- final gridding and micro-levelling;

- imaging and plotting of magnetic field;

- gridding of radar altimeter data

- archiving of final data.

The final projection is Universal Transverse Mercator, using the NAD27 (Clarke 1866) spheroid.  The datum shift from WGS 84 to Clarke 1866 (NAD27) was x = 8 m, y = -160 m, z = -176 m.  The false easting is 500,000 m, false northing is 0 m, scale factor is 0.9996 and the central meridian is 117o West.

Further details of the magnetic processing are provided below.

# 6.1	Noise Editing

An automatic editing routine, employing 4th differences of the magnetic field, removed nulls and spikes down to the noise level, and located abrupt level shifts.

6.2	Noise Filtering

We filtered  all data in the frequency domain with a cutoff 0.061 (wavelengths per sample interval) rolloff 0.030 (wavelengths per sample interval).  This filter approaches 100% removal of anomalies of wavelength 99 metres (13.2 samples x average speed of 7.5 metres/sample) or less. It approaches 0% removal of anomalies of wavelength 163 metres (21.7 samples x average speed of 7.5 metres/sample) or more.  This filter should have no effect on any real, geological-source anomalies; or even the narrowest anomaly from cultural sources on the ground surface.  The minimum ground clearance is about 150 metres (rarely encountered) and the minimum wavelength produced at 150 metres is roughly 2 x 150 = 300 metres.  Thus all real wavelengths are a safe distance from the effective limit of the filter (163 metres).

In the relatively quiet magnetic field recorded at high ground clearance over the valleys (flight lines 101 to 167) a slightly longer wavelength noise was found – beyond the limit of the aforementioned filter.  There were several days of high wind turbulence; and noise from sudden aircraft maneuvers can reach 4 second periods.  Thus, a wider filter was applied to these lines: cutoff 0.0193, rolloff 0.0100.  This frequency domain filter achieves near 100% removal of periods up to 4.1 seconds; and its effect is near 0% at wavelengths of 524 metres or more.  The ground clearance was sufficient to ensure that all real wavelengths would significantly exceed 524 metres; and this was verified by extensive examination of profile data before and after filtering.  To reduce the likelihood of this filter change being visible in any derivative image, a block of adjacent, high-ground-clearance lines (169 to 339) was smoothed with a third frequency domain filter (cutoff 0.0313, rolloff 0.0160), intermediate between the other two.  As before, the ground clearance was sufficient to ensure that all real wavelengths would significantly exceed the effective limit of the filter (322 metres); and this was verified by extensive examination of profile data before and after filtering.

# 6.3	Diurnal Subtraction

A test was made to verify the effectiveness of diurnal subtraction: Long period diurnal variations were subtracted from the air data, as they are more likely to correlate, and the residual magnetic field was leveled.  As no improvement was noted in the required levelling compensations, diurnal subtraction was not employed.

6.4	IGRF Correction

The IGRF regional value was calculated using the 1995 model updated to the mid-survey date (2000.9) using the corrected GPS elevations.  Using the actual elevations for IGRF correction has the added benefit of correcting for the magnetic effect of altitude variations within the Earth’s primary field.  Corrections for vertical movements within the secondary magnetic field induced by the Earth’s crust is discussed in the following section, 6.5.

  - Upward/Downward Continuation

As the terrain clearance drops, the vertical magnetic gradients can become very high; and even minor deviations from the prescribed drape surface may produce significant changes in the measured magnetic field.  The Taylor Expansion applies the required upward and downward continuations to the magnetic field to simulate measurements from the prescribed altitude.  The resulting magnetic field profiles were input to the levelling process.

  - Levelling

The lines (traverse lines) and tie-lines (control lines) of an aeromagnetic survey form a network, and the points where they cross are called intersections.  At each intersection the magnetic values should be identical.  In practice they differ as a result of:

-	time variations of the magnetic field;

-	heading effects;

-	altitude differences;

-	position errors;

-	cultural or instrument noise.

In the levelling process, it is assumed that most of the required level adjustments will vary smoothly along each line or tie-line.  The network of line minus tie-line differences at the intersections is analyzed to produce a matrix of misclosures.  These misclosures were reduced to zero through an iterative process of tilting the profile baselines and moving the intersection locations.  Compensation values applied at adjacent tie-lines were not allowed to differ by more than 5 nT.  Intersection movements were restricted to a maximum of 4 samples (about 30 metres).  These maximums were very rarely required.  Of the 6,717 intersections, less than 87 could not be closed with these compensations.  These intersections were carefully checked and corrected manually.

# 6.7	Gridding

Gridding was done by the Akima method, using data from all lines and tie-lines.  A gridding interval of 1/3 the line spacing was used (133 m).

# 6.8	Grid Levelling

The final stage of levelling consisted of applying a grid-levelling routine to the gridded data to remove small residual errors that are not properly removed by conventional levelling of the line data

7.	DELIVERABLES

7.1	MAPS

Two copies of the magnetic field contour map are presented at 1:100,000 scale with UTM registration plus screened flight path, in black and white, on mylar.

7.2	REPORT

This report covers data acquisition and processing, and is provided in two hard copies plus a digital archive in Microsoft Word format.

7.3	DIGITAL ARCHIVES

Files:		raw and final processed profile data, and final magnetic and radar altitude grids;

Format:	The ASCII  format is used for profiles, and Geosoft binary format is used for grids.  A full format description is included in the appendix .

Media:	CD-ROM.

Copies:	two

We trust this survey will assist your mapping program; and we remain available for questions at any time.

Respectfully Submitted,

Brian Schacht   P. Geoph.

APPENDIX

DIGITAL ARCHIVE FORMAT DESCRIPTOR

DIGITAL ARCHIVE DESCRIPTION OF PROFILE DATA

Digital Archive is Ascii.

Ascii filename: nevada.archive

250 bytes I 10 format

1-10 Line number X 100 + part number

11-20 Flight number

21-30 Latitude   NAD27 (decimal degrees)

31-40 Longitude

41-50 UTM metres NAD27 (CM 117 degrees west)

51-60 UTM metres

61-70 Latitude   WGS84 (decimal degrees)

71-80 Longitude

81-90 UTM metres WGS84 (CM 117 degrees west)

91-100 UTM metres

101-110 Fiducial (seconds UTC X 10 increments by 1)

111-120 Date (ddmmyy)

121-130 Radar (m X 100)

131-140 Baro  (m X 100)

141-150 GPS elevation (m X 100)

151-160 Diurnal (.001 nT)

161-170 Raw Magnetics (.001 nT) edited, lag applied.

171-180 Filtered Magnetics (.001 nT)

181-190 Filtered Magnetics - I.G.R.F. (.001 nT)

191-200 I.G.R.F. (2000.9)

201-210 Differential Up/Down corr. Magnetics (.001 nT)

211-220 Levelled Magnetics (.001 nT)

221-230 Final Magnetics (.001 nT)

231-240 Compensation (.001 nT) from TL levelling

241-250 Compensation (.001 nT) from micro levelling

Fugro Airborne Survey's direction codes are as follows:

1: Northbound

2: Eastbound

3: Southbound

4: Westbound

The archive file contains the following lines:

ARCHIVE FILE: nevada.archive

LINE-ID   DIR FST-FID LST-FID TAPE   BLOCK    REC  SAMPLES

----------- ---   (X10)   (X10) ----   -----    ---  -------

10101   3   70026   70106    1         1     1     801

10301   1   70252   70339    1       802     1     871

10501   3   70515   70606    1      1673     1     911

10701   1   70726   70822    1      2584     1     961

10901   3   70945   71048    1      3545     1    1031

11101   1   71179   71286    1      4576     1    1071

11301   3   71438   71565    1      5647     1    1271

11502   1   76602   76709    1      6918     1    1071

11701   3   59673   59773    1      7989     1    1001

11901   1   59906   60011    1      8990     1    1051

12101   3   60146   60248    1     10041     1    1021

12301   1   60376   60490    1     11062     1    1141

12501   3   60627   60739    1     12203     1    1121

12701   1   60871   60994    1     13324     1    1231

12901   3   61131   61250    1     14555     1    1191

13101   1   61378   61510    1     15746     1    1321

13301   3   61655   61781    1     17067     1    1261

13502   3   76791   76927    1     18328     1    1361

13701   3   62202   62336    1     19689     1    1341

13901   1   62456   62604    1     21030     1    1481

14101   3   62759   62899    1     22511     1    1401

14301   1   63029   63178    1     23912     1    1491

14501   3   63330   63485    1     25403     1    1551

14702   1   77077   77252    1     26954     1    1751

14901   3   63937   64095    1     28705     1    1581

15101   1   64227   64401    1     30286     1    1741

15301   3   64739   64905    1     32027     1    1661

15501   1   65036   65213    1     33688     1    1771

15701   3   65363   65537    1     35459     1    1741

15901   1   65666   65853    1     37200     1    1871

16102   3   77382   77558    1     39071     1    1761

16301   1   66297   66486    1     40832     1    1891

16501   3   66643   66830    1     42723     1    1871

16701   1   66955   67157    1     44594     1    2021

16901   3   67308   67501    1     46615     1    1931

17101   1   67623   67829    1     48546     1    2061

17301   3   67986   68175    1     50607     1    1891

17501   1   68318   68522    1     52498     1    2041

17701   3   68949   69154    1     54539     1    2051

17901   1   69305   69509    1     56590     1    2041

18101   1   77097   77309    1     58631     1    2121

18301   3   77483   77679    1     60752     1    1961

18501   1   77823   78025    1     62713     1    2021

18701   3   78180   78377    1     64734     1    1971

18901   1   78528   78736    1     66705     1    2081

19101   3   78891   79091    1     68786     1    2001

19301   1   79269   79483    1     70787     1    2141

19501   1   78113   78319    1     72928     1    2061

19701   3   78459   78658    1     74989     1    1991

19901   1   78807   79007    1     76980     1    2001

20101   3   56671   56896    1     78981     1    2251

20301   1   57068   57301    1     81232     1    2331

20501   3   57466   57694    1     83563     1    2281

20701   1   57880   58118    1     85844     1    2381

20901   3   58563   58793    1     88225     1    2301

21101   1   58968   59206    1     90526     1    2381

21301   3   59361   59602    1     92907     1    2411

21501   1   59762   59991    1     95318     1    2291

21701   3   60210   60434    1     97609     1    2241

21901   1   60589   60815    1     99850     1    2261

22101   3   60995   61209    1    102111     1    2141

22301   1   61369   61598    1    104252     1    2291

22501   3   61771   61995    1    106543     1    2241

22701   1   62142   62371    1    108784     1    2291

22901   3   62810   63049    1    111075     1    2391

23101   1   63210   63445    1    113466     1    2351

23301   3   63636   63879    1    115817     1    2431

23501   1   64037   64253    1    118248     1    2161

23701   3   64426   64656    1    120409     1    2301

23901   1   64808   65022    1    122710     1    2141

24101   3   65206   65430    1    124851     1    2241

24301   1   65593   65800    1    127092     1    2071

24501   3   65983   66197    1    129163     1    2141

24701   1   66340   66541    1    131304     1    2011

24901   3   66820   67034    1    133315     1    2141

25101   1   67174   67360    1    135456     1    1861

25301   3   67545   67736    1    137317     1    1911

25501   1   67876   68057    1    139228     1    1811

25701   1   74360   74519    1    141039     1    1591

25901   3   74676   74844    1    142630     1    1681

26101   1   74989   75136    1    144311     1    1471

26301   3   75286   75448    1    145782     1    1621

26501   1   75580   75721    1    147403     1    1411

26701   3   75875   76032    1    148814     1    1571

26902   1   77826   77967    1    150385     1    1411

27101   3   76464   76621    1    151796     1    1571

27301   1   76750   76876    1    153367     1    1261

27501   3   77035   77178    1    154628     1    1431

27701   1   77304   77423    1    156059     1    1191

27901   3   77568   77708    1    157250     1    1401

28101   1   77838   77948    1    158651     1    1101

28301   3   78092   78224    1    159752     1    1321

28501   1   78354   78458    1    161073     1    1041

28701   3   78627   78745    1    162114     1    1181

28901   1   78875   78974    1    163295     1     991

29101   3   79114   79230    1    164286     1    1161

29301   1   79355   79446    1    165447     1     911

29501   3   79588   79695    1    166358     1    1071

29701   1   79828   79916    1    167429     1     881

29901   3   80056   80166    1    168310     1    1101

30101   1   80289   80369    1    169411     1     801

30301   3   80515   80613    1    170212     1     981

30501   1   80736   80811    1    171193     1     751

30701   3   80953   81055    1    171944     1    1021

30901   1   81182   81261    1    172965     1     791

31101   3   81398   81494    1    173756     1     961

31301   1   81622   81701    1    174717     1     791

31501   3   81843   81939    1    175508     1     961

31701   1   82067   82142    1    176469     1     751

31901   3   82273   82370    1    177220     1     971

32101   1   82488   82563    1    178191     1     751

32301   3   82699   82798    1    178942     1     991

32501   1   82918   82991    1    179933     1     731

32701   3   83135   83232    1    180664     1     971

32901   1   83364   83441    1    181635     1     771

33101   3   83583   83680    1    182406     1     971

33301   1   83810   83886    1    183377     1     761

33501   3   74089   74192    1    184138     1    1031

33701   3   76673   76774    1    185169     1    1011

33901   3   58884   58980    1    186180     1     961

34101   1   57161   57677    1    187141     1    5161

34301   3   69985   70506    1    192302     1    5211

34501   1   76005   76513    1    197513     1    5081

34701   3   80461   81036    1    202594     1    5751

34901   3   79681   80180    1    208345     1    4991

35101   1   58460   59065    1    213336     1    6051

35302   1   55198   55802    1    219387     1    6041

35501   3   68335   68939    1    225428     1    6041

35701   1   73472   73968    1    231469     1    4961

35901   3   84018   84555    1    236430     1    5371

36101   1   81171   81684    1    241801     1    5131

36301   3   81886   82457    1    246932     1    5711

36501   1   82608   83136    1    252643     1    5281

36701   3   83353   83938    1    257924     1    5851

36901   1   84190   84622    1    263775     1    4321

36902   1   75887   76000    1    268096     1    1131

37101   3   84820   85421    1    269227     1    6011

37301   1   85675   86230    1    275238     1    5551

37501   3   86433   87050    1    280789     1    6171

37701   1   84660   85143    1    286960     1    4831

37901   3   85293   85844    1    291791     1    5511

38101   1   57165   57722    1    297302     1    5571

38301   3   58326   58982    1    302873     1    6561

38501   1   59179   59738    1    309434     1    5591

38701   3   60079   60699    1    315025     1    6201

38901   1   60885   61458    1    321226     1    5731

39101   3   61619   62216    1    326957     1    5971

39301   1   62379   62978    1    332928     1    5991

39501   3   63147   63751    1    338919     1    6041

39701   1   63920   64506    1    344960     1    5861

39901   3   64864   65484    1    350821     1    6201

40101   1   65667   66254    1    357022     1    5871

40301   3   66477   67099    1    362893     1    6221

40501   1   67263   67844    1    369114     1    5811

40701   3   67992   68615    1    374925     1    6231

40901   1   68794   69365    1    381156     1    5711

41101   3   68735   69297    1    386867     1    5621

41301   1   67960   68587    1    392488     1    6271

41501   3   67214   67792    1    398759     1    5781

41701   1   66440   67039    1    404540     1    5991

41901   3   65693   66257    1    410531     1    5641

42101   1   63690   64294    1    416172     1    6041

42301   3   62946   63515    1    422213     1    5691

42501   1   62159   62784    1    427904     1    6251

42701   3   61393   62002    1    434155     1    6091

42901   1   60582   61209    1    440246     1    6271

43101   3   59844   60404    1    446517     1    5601

43301   1   58825   59427    1    452118     1    6021

43501   3   58106   58663    1    458139     1    5571

43701   1   57214   57817    1    463710     1    6031

43901   3   86452   86986    1    469741     1    5341

44101   1   85795   86310    1    475082     1    5151

44301   3   85148   85672    1    480233     1    5241

44501   1   84493   85006    1    485474     1    5131

44701   3   83607   83740    1    490605     1    1331

44702   3   83945   84374    1    491936     1    4291

44901   1   82954   83477    1    496227     1    5231

45101   3   82281   82830    1    501458     1    5491

45301   1   81623   82141    1    506949     1    5181

45501   3   80938   81489    1    512130     1    5511

45701   1   80282   80793    1    517641     1    5111

45901   3   79611   80151    1    522752     1    5401

46101   1   78961   79472    1    528153     1    5111

46301   3   78169   78707    1    533264     1    5381

46501   1   77309   77825    1    538645     1    5161

46701   3   76639   77188    1    543806     1    5491

46901   1   75993   76510    1    549297     1    5171

47101   3   75309   75864    1    554468     1    5551

47301   1   74674   75180    1    560019     1    5061

47501   3   68251   68918    1    565080     1    6671

47701   1   67511   68067    1    571751     1    5561

47901   3   66753   67350    1    577312     1    5971

48101   1   65852   66416    1    583283     1    5641

48301   3   65084   65713    1    588924     1    6291

48501   1   64339   64921    1    595215     1    5821

48701   3   63565   64194    1    601036     1    6291

48902   3   56419   56988    1    607327     1    5691

49101   3   62089   62702    1    613018     1    6131

49301   1   61160   61745    1    619149     1    5851

49501   3   60379   61007    1    625000     1    6281

49701   1   59622   60208    1    631281     1    5861

49901   3   58880   59477    1    637142     1    5971

50101   1   58113   58711    1    643113     1    5981

50301   3   57360   57973    1    649094     1    6131

50502   1   55650   56306    1    655225     1    6561

50701   3   86365   86886    1    661786     1    5211

50901   1   85708   86234    1    666997     1    5261

51101   3   84741   85278    1    672258     1    5371

51301   1   84094   84613    1    677629     1    5191

51501   3   83440   83969    1    682820     1    5291

51701   1   82784   83311    1    688111     1    5271

51901   3   82117   82657    1    693382     1    5401

52101   1   81471   81991    1    698783     1    5201

52301   3   80808   81348    1    703984     1    5401

52501   1   80147   80662    1    709385     1    5151

52701   3   79495   80021    1    714536     1    5261

52901   1   79110   79360    1    719797     1    2501

52903   3   79360   79658    1    722298     1    2981

53101   3   78167   78702    1    725279     1    5351

53301   1   77507   78030    1    730630     1    5231

53501   3   76839   77368    1    735861     1    5291

53701   1   76450   76713    1    741152     1    2631

53702   3   70320   70631    1    743783     1    3111

53901   3   75528   75790    1    746894     1    2621

53902   3   80280   80582    1    749515     1    3021

54101   1   74865   75386    1    752536     1    5211

54301   3   74199   74729    1    757747     1    5301

54501   1   73531   74044    1    763048     1    5131

54701   3   68288   68893    1    768179     1    6051

54901   1   67508   68083    1    774230     1    5751

55101   3   66736   67363    1    779981     1    6271

55301   1   65843   66408    1    786252     1    5651

55501   3   65035   65704    1    791903     1    6691

55701   1   64273   64842    1    798594     1    5691

55901   3   63493   64111    1    804285     1    6181

56101   1   62492   63079    1    810466     1    5871

56301   3   61683   62335    1    816337     1    6521

56501   1   60931   61507    1    822858     1    5761

56701   3   60128   60789    1    828619     1    6611

56901   1   59406   59955    1    835230     1    5491

57101   3   58361   59002    1    840721     1    6411

57301   1   57630   58180    1    847132     1    5501

57501   3   56850   57477    1    852633     1    6271

57701   1   56116   56670    1    858904     1    5541

57901   3   86163   86646    1    864445     1    4831

58101   1   85492   86034    1    869276     1    5421

58301   3   84865   85350    1    874697     1    4851

58501   1   84201   84745    1    879548     1    5441

58701   3   83572   84064    1    884989     1    4921

58901   1   82879   83429    1    889910     1    5501

59101   3   82018   82520    1    895411     1    5021

59301   1   81344   81891    1    900432     1    5471

59501   3   80713   81201    1    905903     1    4881

59701   1   80028   80576    1    910784     1    5481

59901   3   79396   79883    1    916265     1    4871

60101   1   78714   79266    1    921136     1    5521

60301   3   78022   78514    1    926657     1    4921

60501   1   77359   77899    1    931578     1    5401

60701   3   76704   77203    1    936979     1    4991

60901   1   76030   76320    1    941970     1    2901

60902   3   69813   70100    1    944871     1    2871

61101   3   75347   75857    1    947742     1    5101

61301   1   74647   75194    1    952843     1    5471

61501   3   69643   70238    1    958314     1    5951

61701   1   68880   69489    1    964265     1    6091

61901   3   67874   68482    1    970356     1    6081

62101   1   66893   67501    1    976437     1    6081

62301   3   66137   66729    1    982518     1    5921

62501   1   65146   65746    1    988439     1    6001

62701   3   64384   64985    1    994440     1    6011

62901   1   63499   64093    1   1000451     1    5941

63101   3   76094   76696    1   1006392     1    6021

63301   1   75068   75679    1   1012413     1    6111

63501   3   74234   74909    1   1018524     1    6751

63701   1   73441   74059    1   1025275     1    6181

63901   3   72641   73269    1   1031456     1    6281

64101   3   85335   85972    1   1037737     1    6371

64301   1   84493   85170    1   1044108     1    6771

64501   3   83720   84316    1   1050879     1    5961

64701   1   82860   83515    1   1056840     1    6551

64901   3   81936   82520    1   1063391     1    5841

65101   1   81102   81769    1   1069232     1    6671

65301   3   80341   80924    1   1075903     1    5831

65501   1   79490   80134    1   1081734     1    6441

65701   1   77666   78315    1   1088175     1    6491

65901   3   58249   58880    1   1094666     1    6311

66101   1   57440   58076    1   1100977     1    6361

66301   3   77010   77621    1   1107338     1    6111

66501   1   76125   76829    1   1113449     1    7041

66701   3   75133   75745    1   1120490     1    6121

66901   1   74301   74956    1   1126611     1    6551

67101   3   73186   73865    1   1133162     1    6791

67301   1   72350   73006    1   1139953     1    6561

67501   3   71117   71785    1   1146514     1    6681

67701   1   70291   70956    1   1153195     1    6651

67901   3   69471   70104    1   1159846     1    6331

68101   1   68651   69294    1   1166177     1    6431

68301   3   67639   68294    1   1172608     1    6551

68501   1   66862   67483    1   1179159     1    6211

68701   3   66067   66690    1   1185370     1    6231

68901   1   65324   65908    1   1191601     1    5841

69101   3   64254   64874    1   1197442     1    6201

69301   1   63538   64111    1   1203643     1    5731

69501   3   62730   63346    1   1209374     1    6161

69701   1   62000   62576    1   1215535     1    5761

69901   3   85972   86556    1   1221296     1    5841

70101   1   85324   85844    1   1227137     1    5201

70301   3   84589   85159    1   1232338     1    5701

70501   1   83911   84423    1   1238039     1    5121

70701   3   83175   83742    1   1243160     1    5671

70901   1   82505   83019    1   1248831     1    5141

71101   3   81511   82032    1   1253972     1    5211

71301   1   80936   81396    1   1259183     1    4601

71501   3   80256   80765    1   1263784     1    5091

71701   1   79697   80138    1   1268875     1    4411

71901   3   79033   79515    1   1273286     1    4821

72101   1   78453   78869    1   1278107     1    4161

72301   3   77568   78017    1   1282268     1    4491

72501   1   77022   77412    1   1286759     1    3901

72701   3   76406   76823    1   1290660     1    4171

72901   1   75831   76212    1   1294831     1    3811

73101   3   75239   75645    1   1298642     1    4061

73301   1   74632   75002    1   1302703     1    3701

73502   3   66293   66693    1   1306404     1    4001

73702   1   65675   66067    1   1310405     1    3921

73902   3   65035   65478    1   1314326     1    4431

74102   1   64386   64785    1   1318757     1    3991

74303   3   63620   64052    1   1322748     1    4321

74503   1   63023   63415    1   1327069     1    3921

500102   2   61915   62736    1   1330990     1    8211

500301   4   65300   66006    1   1339201     1    7061

500501   2   67035   67700    1   1346262     1    6651

500701   4   62953   63618    1   1352913     1    6651

500901   2   63740   64370    1   1359564     1    6301

501101   4   59654   60375    1   1365865     1    7211

501301   4   64520   65169    1   1373076     1    6491

501501   2   65290   65925    1   1379567     1    6351

501701   2   60576   61271    1   1385918     1    6951

501901   4   66012   66674    1   1392869     1    6621

502101   2   66793   67420    1   1399490     1    6271

502301   4   61575   62300    1   1405761     1    7251

502501   4   67500   68154    1   1413012     1    6541

502701   2   68268   68911    1   1419553     1    6431

502901   2   62573   63280    1   1425984     1    7071

503101   4   69013   69648    1   1433055     1    6351

503301   2   69775   70402    1   1439406     1    6271

503501   4   63456   64152    1   1445677     1    6961

503701   4   70537   71127    1   1452638     1    5901

503901   2   71255   71811    1   1458539     1    5561

504101   2   64310   64978    1   1464100     1    6681

504301   4   71915   72471    1   1470781     1    5561

504501   2   72595   73154    1   1476342     1    5591

504701   4   65177   65868    1   1481933     1    6911

504901   4   73253   74056    1   1488844     1    8031

505101   2   74167   74957    1   1496875     1    7901

505301   2   66375   67301    1   1504776     1    9261

505501   4   75056   75908    1   1514037     1    8521

505701   4   76466   76731    1   1522558     1    2651

505901   2   68908   69214    1   1525209     1    3061

506101   2   76836   77083    1   1528270     1    2471

506301   4   77253   77473    1   1530741     1    2201

506501   4   69426   69666    1   1532942     1    2401

506701   4   67706   68696    1   1535343     1    9901

506901   2   76053   76324    1   1545244     1    2711

507101   3   77751   77955    1   1547955     1    2041

507301   1   81025   81272    1   1549996     1    2471

507501   3   79185   79340    1   1552467     1    1551

DIGITAL ARCHIVE DESCRIPTION OF GRID DATA

CLIENT                       U.S.G.S

NAME OF SURVEY               AEROMAGNETIC SURVEY of WESTERN NEVADA

AREA NAME                    EXCELSIOR MOUNTAINS, SOUTHERN WASSUK RANGE and EXCELSIOR ADD-ON

CONTRACTOR                   FUGRO AIRBORNE SURVEYS

JOB CODE                     655

GRID ARCHIVE NAME            NEVADA_TF.GRD

FORMAT                       GEOSOFT BINARY GRID

CONTENT                      TOTAL MAGNETIC INTENSITY

CREATION DATE                February 15, 2001

NUMBER of ROWS and COLUMNS   640 1024

PIVOTAL POSITION (X,Y)       331087 4212084

CELL SIZE                    83m

UNIT                         nT

UNIT FACTOR                  0.001

MINIMUM VALUE (nT)           -555.284

MAXIMUM VALUE (nT)            846.571

MEAN VALUE (nT)               -71.181

GRID ARCHIVE NAME            NEVADA_RADAR.GRD

FORMAT                       GEOSOFT BINARY GRID

CONTENT                      RADAR

CREATION DATE                March 7, 2001

NUMBER of ROWS and COLUMNS   640 1024

PIVOTAL POSITION (X,Y)       331087 4212167

CELL SIZE                    83m

UNIT                         m

UNIT FACTOR                  0.01

MINIMUM VALUE (m)            157

MAXIMUM VALUE (m)            1217 (instrument maximum)

MEAN VALUE (m)               536

PROJECTION INFORMATION :

DATUM                                 NAD27

SHEROID                               CLARKE 1866

PROJECTION                            UTM

CENTRAL MERIDIEN                      117 West

FALSE EASTING                         500000 m

FALSE NORTHING                        0 m

SCALE FACTOR                          0.9996

# Footnotes

Pilkington, M., and Thurston, J. B., 2001.  Draping corrections for aeromagnetic data: line versus grid based approaches; Exploration Geophysics, in press.

Minty, B.R.S., 1991: Simple micro-levelling for aeromagnetic data; Exploration Geophysics, v.22, p. 591-592.