Attachment A

Goals of Radioactive Contamination Control

- The Goals of Contamination Control are to Prevent the Spread of Radioactive Materials from:

- The patient.

- In most circumstances the victim will be the source of the contamination; however, in rescue and extrication, some contamination may have been transferred to others.

- The rescue personnel.

- The gurney and equipment used in patient care (stethoscope, BP cuff, etc.).

- The ambulance.

- This Contamination Can be Transferred to:

- Care providers as they touch or move the patient to correct the medical problem.

- The equipment used to assess the patient's condition and to treat the medical emergency.

- The surrounding area (treatment gurney, floor, etc.)

- In rare cases where dust or powders are present, the air could contain radioactive particles.

- Techniques of Contamination Control:

- Set up a controlled area large enough to hold the anticipated number of victims.

- Prevent tracking of contaminants by covering floor areas and monitoring at exits of controlled areas.

- Restrict access to the controlled area.

- Monitoring anyone or anything leaving the controlled area.

- Use strict isolation precautions, including protective clothing and double bagging.

- Use a buffer zone or secondary control line for added security.

- Control waste by using large, plastic-lined containers for clothing, linens, dressings, etc.

- Control ventilation.

- Change instruments, outer gloves, drapes, etc., when they become contaminated.

- Use waterproof materials to limit the spread of contaminated liquids; for example, waterproof aperture drapes.

- If Radioactive Contamination Is Discovered After Patient Has Been Admitted:

- Continue attending to the patient's medical needs.

- Secure entire area where victim and attending staff have been.

- Do not allow anyone or anything to leave area until cleared by the Radiation Safety Officer.

- Establish control lines, and prevent the spread of contamination.

- Completely assess patient's radiological status.

- Personnel should remove contaminated clothing before exiting area; they should be surveyed, shower, dress in clean clothing, and be re-surveyed before leaving area.