CCRP Practice

CP5A Field Windbreak Establishment

The purpose of this practice is to establish windbreaks to improve the environmental benefits on a farm or ranch to, first, reduce cropland erosion below soil loss tolerance and, second, enhance wildlife habitat.

The maximum allowable practice width will consist of 1 to 3 rows of trees and/or shrubs spaced according to guidance in the Windbreak/Shelterbelt Standard, Code 380.  The spacing between rows (row-to-row width) depends on the total number of rows, the species of trees or shrubs to be planted, and the type of weed control to be used.  Row spacing may vary and row spacing guidance and spacing maximums are listed in the standard.  Multiple field windbreaks in the same field will be spaced according to the contributing erosion factors using WEQ*.  See Diagram 2 for field windbreak examples.

At the participant’s option, an additional area up to one rod in width is eligible for enrollment adjacent to the outside row of any windbreak.  This area will provide access to maintain the windbreak and allow the tree canopy to develop over the life of the contract.

Field windbreaks must be located, positioned, and documented to provide wind erosion control benefits.  Wind erosion potential for the CP5A site will be documented on the CP5A eligibility sheet.  Eligible fields must be determined to have potential wind erosion (PE) that exceeds “T”, the tolerable soil loss rate.  Potential wind erosion will be calculated using EI (erosion index) found in the National Food Security Act Manual HEL determination for wind erosion, NFSAM 180, Part 511.01.

A temporary cover crop, not to exceed 2 years, is allowed if the following circumstances are justified: 1) seedlings are not available; 2) the normal planting period has passed or the practice will not be completed within 12 months from the CRP-1 effective starting date; 3) chemical residues are likely to carry-over in the soil.  Longer cover crops may be considered if: 1) steep slopes are present; 2) water or wind erosion is present; or 3) other unique site conditions exist.  For all situations where grass cover will be established (both temporary and long term) with the CP-5A practice the table below lists the only approved species that can be used.

Crop      						Rate/acre

Small grains (Oats, Wheat, Barley, Rye)		1 ½ to 2 ½ bu.

Perennial rye					8 lbs.

Timothy 					2 to 3 lbs.

All grasses and weeds located within the row must be controlled for the life of the contract.  If within-row soil erosion control or weed suppression is needed, use as appropriate, mulch, fabric, mechanical and/or chemical control methods.  Annual mowing of CRP acreage for generic weed control is prohibited after a final status review has been received from NRCS.  According to 2-CRP (Rev. 4) Paragraph 442B, cost share is allowed for one weed and/or insect control treatment within 24 months after the planting of trees/shrubs if approved by the COC and it is a part of the conservation plan.

* WEQ information is located in Section I of the FOTG.  When more than one windbreak is planned for the same field the spacing between windbreaks will be determined using the WEQ critical period procedure.

Diagram 2			Field Windbreaks

Natural Resources Conservation Service (NRCS)

APPLICANT:      		COUNTY:      			Resource Concerns for Eligibility

Wind Erosion

FSA TRACT NO.:      		FSA FIELD NO.:

Practice Eligibility (Need and feasibility):

Soil Map Unit Symbol*       or     Soil Map Unit Name*

*Use predominant soil of significant extent for planning purposes

Soil Loss Tolerance for the Map Unit (T) tons/acre/year

C Factor (expressed as a %) for County   		I Factor for Soil Map Unit

Potential Erodibility (PE**) (PE=C*I/T)      tons/acre/year

**Refer to the NFSAM 180, Part 511.01

Documented potential wind erodibility is equal to or greater than T?  Yes	 No*

When more then one windbreak is planned in the same field the distance between windbreaks will be determined using WEQ critical period procedure.

Ineligible Practice:

*Documented potential wind erodibility is less than T.

Site Suitability (from site visit):

Acreage is suitable for the practice? 	 Yes	 No**

(Use the Conservation Tree and Shrub Groups from Section I of the FOTG to determine tree or shrub suitability for the offered acres)

Notes:

**The site is unsuitable for the practice

Extent of Windbreak (# of rows, check one, and width)

One: Width    ft. (Max. width is up to 33 ft. including maintenance area*)

Two: Width    ft. (Max. width is up to 53 ft. including maintenance area*)

Three: Width    ft. (Max. width is up to 73 ft. including maintenance area*)

*One rod width (16.5 ft) may, at the participant’s option, be enrolled along the outside row(s) of the windbreak for maintenance access and canopy development.

# Text boxes

Prevailing

Wind

Direction

Example 1: A 2-Row Field Windbreak

Not to scale

Area between rows and maintenance

area could be approved for long term

cover.

Row 1

Distance between rows,

10- 20 Ft.

NTE 20 Ft.

Row 2

Optional Maintenance Area Outside of rows

NTE 1-Rod (16.5 ft) Wide

Crop Field

outside windbreak

Example 2: A Series of 1-3 Row Field Windbreaks

Not to scale

Prevailing

Wind Direction

Windbreak 1-3 Rows Allowable

Maintenance Area

Outside of rows

NTE 1-Rod (16.5 ft) Wide

Crop Field

Distance between windbreak rows determined by WEQ.

Windbreak 1-3 Rows Allowable

Crop Field

Windbreak 1-3 Rows Allowable

Documentation of Eligibility and Suitability for				     CP5A

Field Windbreaks									  Version 11/07