Airborne Information for Lateral Separation (AILS)

Vernol Battiste, Walter Johnson, Terry Rager, NASA ARC; David Brown, Diane Carpenter,

Eric Gardner, Nabil Hanania, Jerry Jones, Rod Ketchum, Dave Lambert, lan Maclure, George Mitchell,

Craig Pires, Tom Prehm, Fritz Renema, Ghislain Saillant, Gary Uyehara, ManTech

Summary

This study examined the operational implementation of an airborne system that would support Closely Spaced Parallel Approach (CSPA) operations at airports with parallel runways during Instrument Meteorological Conditions (IMC). Data analyses are in progress. Introduction

Several major airports in the United States have parallel runways that are in close proximity. When visual contact between aircraft is possible, capacity is greatly increased by having aircraft fly closely spaced parallel visual approaches. Under IMC, airports with runways closer than 4300 ft are required to revert to a single runway operation or to run dependent approaches, each greatly reducing the number of landing aircraft.

This study investigated the utility and viability of a flight-deck-based display and alerting system that supports flight crews' situational and traffic awareness during all phases of an ILS approach. The study also examined flight deck and ATC final controller roles and responses during dual independent parallel approach operations at Seattle-Tacoma Airport (SEATAC).

PFD depicting an armed AILS approach.

Simulation

This simulation was conducted with scenarios using the airspace in and around SEATAC. This site was selected to evaluate the Airborne Information for Lateral Separation (AILS) concept because the airport is undergoing a new runway addition which will give the primary runways approximately 2500 ft centerline separation. This configuration lends itself

to use of the AILS and CSPA technologies. Additionally, the FAA and managers at SEATAC were interested in supporting and implementing the results of this study.

The CVSRF's B747 full-mission simulator was adapted to accept AILS symbology on the PFD and to present CSPA information on the navigation display. Initial positions were created to allow the B747 simulator to enter the scenario at desired points. The SEATAC runway scene depicted in the B747 simulator's visual system was modified to represent the new runway. Additionally, a custom FMS navigation database was designed and loaded into the FMS for use with the new approaches.

PAS was heavily modified to incorporate changes required to support traffic flow realism into SEATAC. The CVSRF's ATC Lab was configured to represent the SEATAC feeder sectors, departure sectors, a tower position, and adjacent airspace positions; all used PAS. A separate final approach controller position was created in an isolated area of the lab for controller evaluation. Based on controller estimates of normal traffic flow to dual parallel runways, a single controller handled 48 aircraft per hour.

Additional video cameras, video splitters, routers, and other hardware were installed to collect audio and video data for both the B747 flight deck crew and the isolated ATC position.

Scenarios began with air traffic routed to runways 17 L/R. The B747 simulator was released into this traffic flow via automated software programs that also "paired" conflict traffic for a subsequent "blunder" or breakout maneuver.

Results

The flight crew's assessment of the AILS concept was of primary interest for this experiment. This included all aspects of the AILS concept from system initialization and display status through the responses of the flight crew and the aircraft systems to an intruding or "blundering" aircraft.

Flight crew workload and performance data were collected using both objective and subjective assessment methodologies. Data analyses are in progress.

Investigative Team NASAARC ManTech SEATAC

30       Aviation Systems Division