SPECIAL SPECIFICATION

SECTION 09800

SPECIAL COATINGS

Page

PART 1 - GENERAL

1.01  Summary.	2

1.02  Submittals.	2

1.03  Quality assurance..	2

1.04  Delivery Storage and Handling.	2

1.05  Project Conditions	3

PART 2 - PRODUCTS

2.01  Acceptable Manufacturers.	4

2.02  Special Coatings.	4

PART 3 - EXECUTION

3.01  Examination.	5

3.02  Preparation	5

3.03  Application.	5

3.04  Cleaning and Protection.	5

SPECIAL SPECIFICATION

SECTION 09800

SPECIAL COATINGS

PART 1 - GENERAL

1.01 	SUMMARY

A. 	This Section includes non-skid special coating for Building 870C.

1.02 	SUBMITTALS

A. 	Submit in accordance with provisions of Section 01300.

B. 	Product data coating system.

1.  	Provide the manufacturer's technical information, including label analysis and instructions for handling, storing, and applying each material proposed for use.

2.  	Certification by the manufacturer that products supplied comply with local regulations controlling use of volatile organic compounds (VOCs).

1.03  	QUALITY ASSURANCE

A. 	Applicator Qualifications:  Engage an experienced applicator who has successfully completed five special coating applications similar to this Project.

1.04 	DELIVERY, STORAGE, AND HANDLING

A. 	Deliver materials to the job site in the manufacturer's original, new, unopened packages, and containers bearing manufacturer's name and label, and the following information:

1.  	Name or title of material.

2.  	Product description (generic classification or binder type).

3.  	Manufacturer's name, stock number and date of manufacture.

4.  	Contents by volume, for major pigment and vehicle constituents.

5.  	Thinning instructions.

6.  	Application instructions.

7.  	Color name and number.

8.  	Handling instructions and precautions.

B. 	Store materials not in use in tightly covered containers in a well-ventilated area at a minimum ambient temperature of 45 deg F (7 deg C).  Maintain containers used in storage in a clean condition, free of foreign materials and residue.

1.05 	PROJECT CONDITIONS

A. 	Apply coatings only when the temperature of surfaces to be coated and surrounding air temperatures are between 50 deg F (7 deg C) and 60 deg.

PART 2 - PRODUCTS

2.01 	MANUFACTURERS

A. 	Manufacturers:  Subject to compliance with requirements, provide products of one of the following:

1.  	PPG Industries, Pittsburgh Paints.

2.  	Sherwin-Williams Company.

3.  	Tnemec Company, Inc.

2.02 	SPECIAL COATINGS

A. 	Provide Series 67 Tneme-Tread, epoxy-polyamide floor coating manufactured by Tnemec Company, Inc.

1.  	Self priming.

2.  	Finish: Semi-gloss

3.  	Surface: Non-skid

4.  	Solids by volume: 49.0 plus or minus 2 percent.

5.  	Dry Film Thickness: 2.0 to 3.0 mils per coat.

6.  	Color: Light Gray

PART 3 - EXECUTION

3.01 	EXAMINATION

A. 	Examine substrates and conditions under which coatings will be applied for compliance with requirements on applying coatings.  Surfaces to receive coatings must be thoroughly dry before coatings are applied.

1.  	Do not proceed with coating application until unsatisfactory conditions have been corrected.

3.02 	PREPARATION

A. 	Cleaning:  Before applying coatings, clean the substrates of substances that could impair bond.

B. 	Surface Preparation:  Clean and prepare surfaces to be coated according to the manufacturer's instructions.

3.03 	APPLICATION

A. 	Apply special coatings by brush or roller, according to manufacturer's directions.  Use brushes best suited for the material being applied.

B. 	Allow sufficient drying time between successive coats.

C. 	Minimum Coating Thickness:  Apply at the manufacturer's recommended spreading rate.

D. 	Brush Application:  Brush-out and work brush coats into surfaces in an even film.  Eliminate cloudiness, spotting, holidays, laps, brush marks, runs, sags, ropiness, or other surface imperfections.

3.04 	CLEANING AND PROTECTION

A. 	Cleanup:  At completion of the work, remove rubbish and other discarded materials from the site.

B. 	Protect surface from traffic during remainder of construction period.

END OF SECTION