November 21, 1997

Contract # TW-0928

SPECIAL SPECIFICATION

SECTION 09800-S

SPECIAL COATINGS

Page

PART 1 - GENERAL

1.01	Summary	2

1.02	Submittals	2

1.03	Quality assurance	2

1.04	Delivery Storage and Handling	2

1.05	Project Conditions	3

PART 2 - PRODUCTS

2.01	Acceptable Manufacturers	4

2.02	Special Coatings	4

PART 3 - EXECUTION

3.01	Examination	5

3.02	Preparation	5

3.03	Application	5

3.04	Cleaning and Protection	5

SPECIAL SPECIFICATION

SECTION 09800-S

SPECIAL COATINGS

PART 1 - GENERAL

1.01.	SUMMARY

A.	This Section includes traffic coating for exterior balconies.

1.02		SUBMITTALS

A.	Submit in accordance with provisions of Section 01300-S.

B.	Product data coating system.

1.	Provide the manufacturer's technical information, including label analysis and instructions for handling, storing, and applying each material proposed for use.

DELETE THE FOLLOWING REQUIREMENT IF THE LOCAL JURISDICTION DOES NOT HAVE REGULATIONS RESTRICTING VOLATILE ORGANIC COMPOUNDS.

2.	Certification by the manufacturer that products supplied comply with local regulations controlling use of volatile organic compounds (VOCs).

3.	Manufacturer’s standard colors.

DELETE THE NEXT PARA IF COLORS ARE PRESELECTED AND SPECIFIED OR SCHEDULED.

1.03		QUALITY ASSURANCE

A.	Applicator Qualifications:  Engage an experienced applicator who has successfully completed five special coating applications similar to this Project.

ALWAYS RETAIN THE NEXT REQUIREMENT.  COATING SYSTEMS COULD FAIL IF THE COATS ARE INCOMPATIBLE.

1.04.	DELIVERY, STORAGE, AND HANDLING

A.	Deliver materials to the job site in the manufacturer's original, new, unopened packages, and containers bearing manufacturer's name and label, and the following information:

ADD OTHER LABEL REQUIREMENTS AS NECESSARY TO SUIT SPECIFIC PROJECT CIRCUMSTANCES.

1.	Name or title of material.

2.	Product description (generic classification or binder type).

3.	Manufacturer's name, stock number and date of manufacture.

4.	Contents by volume, for major pigment and vehicle constituents.

5.	Thinning instructions.

6.	Application instructions.

7.	Color name and number.

8.	Handling instructions and precautions.

B.	Store materials not in use in tightly covered containers in a well-ventilated area at a minimum ambient temperature of 45 deg. F (7 deg. C) and a maximum temperature of 90 deg. F.  Maintain containers used in storage in a clean condition, free of foreign materials and residue.

1.05		PROJECT CONDITIONS

A.	Apply coatings only when the temperature of surfaces to be coated and surrounding air temperatures are between 70 deg. F (7 deg. C) and 90 deg.

PART 2 - PRODUCTS

2.01		MANUFACTURERS

DELETE THIS ARTICLE IF OWNER-IMPOSED OR OTHER PRODUCT REQUIREMENTS PROHIBIT MENTIONING MFRS' NAMES.

A.	Manufacturers:  Subject to compliance with requirements, provide products of one of the following:

MFRS BELOW PRODUCE AN EXTENSIVE LINE OF SPECIALTY COATINGS; THEIR PRODUCTS ARE DISTRIBUTED NATIONALLY AND GENERALLY AVAILABLE.  ADD REGIONAL MFRS IF APPROPRIATE.  NOTE THAT NOT EVERY MFR PRODUCES EVERY COATING TYPE CONTAINED IN THIS SECTION.  EDIT THE LIST TO SUIT PROJECT REQUIREMENTS AND LOCAL AVAILABILITY.  SEE EDITING INSTRUCTION NO. 1 IN THE EVALUATIONS FOR CAUTIONS ABOUT NAMING PRODUCTS AND MFRS.

1.	PPG Industries, Pittsburgh Paints.

2.	Sherwin-Williams Company.

3.	Tnemec Company, Inc.

B.	Substitutions: only under provisions of Section 1600-S.

2.02		SPECIAL COATINGS

A.	Provide Series 280 Tneme-Glaze, polyamine epoxy floor coating manufactured by Tnemec Company, Inc.

1.	Primer:  Epoxoprime Series 201, 8 mils dft/coat

2.	Finish: Gloss

3.	Surface: Non-skid

4.	Solids by volume: 98 plus or minus 2 percent.

5.	Dry Film Thickness: 8 mils per coat.

6.	Color: Selected from manufacturer’s standard colors by SDR.

PART 3 - EXECUTION

3.01		EXAMINATION

A.	Examine substrates and conditions under which coatings will be applied for compliance with requirements on applying coatings.  Surfaces to receive coatings must be thoroughly dry before coatings are applied.

1.	Do not proceed with coating application until unsatisfactory conditions have been corrected.

3.02		PREPARATION

A.	Cleaning:  Before applying coatings, clean the substrates of substances that could impair bond.

ALWAYS RETAIN THE FOLLOWING REQUIREMENTS FOR SURFACE PREPARATION.  AMPLIFY EACH REQUIREMENT, IF NECESSARY, TO INCLUDE SPECIAL PROCEDURES REQUESTED BY THE MFRS OR TO SATISFY UNUSUAL PROJECT CONDITIONS.

B.	Surface Preparation:  Mechanically abrade, clean and prepare surfaces to be coated according to the manufacturer's instructions.

COORDINATION OF SHOP-APPLIED PRIME COATS WITH SPECIAL COATINGS IS CRITICAL.  SEE EXAMINATION ARTICLE, COORDINATING WORK PARA.  IF COMPATIBILITY PROBLEMS EXIST, IT MIGHT BE NECESSARY TO PROVIDE BARRIER COATS OVER PRIMERS, OR TO REMOVE THE PRIMER AND REPRIME SUBSTRATE.

3.03		APPLICATION

REVISE REQUIREMENTS IN THIS ARTICLE TO SUIT PROJECT CIRCUMSTANCES.  INCLUDE RESTRICTIONS ON APPLICATION METHODS, IF REQUIRED.

A.	Apply special coatings by brush or roller, according to manufacturer's directions.  Use brushes best suited for the material being applied.

B.	Allow sufficient drying time between successive coats.

C.	Minimum Coating Thickness:  1 coat at 8 mils DFT/coat for primer and 2 coats of topcoat at 8 mils DFT/coat.  Total DFT = 24 mils.

D.	Brush Application:  Brush-out and work brush coats into surfaces in an even film.  Eliminate cloudiness, spotting, holidays, laps, brush marks, runs, sags, ropiness, or other surface imperfections.

Apply additional coats to provide complete hiding and good overall appearance.

3.04		CLEANING AND PROTECTION

A.	Cleanup:  At completion of the work, remove rubbish and other discarded materials from the site.

DELETE THE NEXT PARA IF CLEANING IS THE CONTRACTOR'S RESPONSIBILITY.

B.	Protect surface from traffic during remainder of construction period.

END OF SECTION