POLAR Spacecraft Status As of: Tues May 17  12:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM: 1651=AN STIP data only | NOAA-14J AM: 2039=AN STIP data only | NOAA-15K AM: 1806=AN GAC data only | NOAA-16L PM: 1441=AN GAC&LAC data | NOAA-17M AM: 2225=AN GAC&LAC data | NOAA-N18 Planned PM Plan AN=14:00 |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 20May05 10:30Z Various slips |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | Dress Rehearse #1 Completed 13Jan |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | Dress Rehearse #2 Completed 14Apr05 |
| BUS VETO | NO | NO | NO | NO | NO | Dress rehearse #3 Completed 9 May 05 |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB | New ring laser gyro |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Au04 | PRI Daily Bias –5.5 mS -100 mS 31Au04 | PRI Daily Bias –3 mS |  |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |  |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled |  |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting |  |
| DTRs | 3A, 4, 5B Safestate 5B | 1, 2B, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B STIP only | 1,2,3,4 Safestate=1B DTR2-SSR | All solid state digital recorders |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF Since 8/14/02 | #1 ON (16 May 18:15Z) End N12 Conflict | INOP OFF since 11/15/00 | #2 ON 137.62 MHZ | #1=137.1 MHZ #2=137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #1 137.35 MHZ | #2 137.77 MHZ |  |
| STX #1=1698.0 mhz #2=1702.5 mhz #3=1707.0 mhz #4=2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 4-Playback 1,2,3-Degraded | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 output power drop TOAR 443. | STX-3 Replaced at VAFB |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +50 since 8/31/04 Eclipse season 21Apr-17Aug Batt UVtrip 7/25/04 Sun Angle 33 up to 37 mid-June Batts 1&2=LRC V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Eclipse all year Sun angle 50 up trend to 52 in June Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Eclipse Season started 16 May Sun Angle 28, up- trend to 32 in June Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 56 Steady trend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs SADPOS timer increased 5 Apr | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 71 Uptrend to 72 at the end of May Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs SADPOS timer increased 5 Apr |  |
| AVHRR | Nominal | INOP Scan motor stalled 14 Apr 04 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Operational TCE24 OFF 4/14/04 Occasional Image Wave patterns and MIRP rephases Chan 3B only. | Nominal 3A-B switch enabled | New brushless scan motors |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative Record low component temps reversed trend | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop Channel 9-14 noise worsened recently | OFF/INOP Since 10/30/03 Survival heat on. |  |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal |  |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 IPD Reports of degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | ON / INOP Turned on 8/30/04 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | INPROVED Upgraded to Yellow status 16 May 05 FW Abrupt return to nomial at 09:00Z TOAR 445 submitted FW mode=Hi Powr FW Heater OFF Frequent Filter Excessively high FM temps and currents continue | DEGRADED Longwave channel imagery improved radiometric noise level is still high TOAR 441 submitted 11 Jan05 Considering high power mode Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | HIRS-4 replacing HIRS-3 |
| MHS/MIU |  |  |  |  |  | Replaces AMSUB |
| MSU | ON / INOP On For power balance Scan Motor OFF since 3/12/03 | Operational Scan motor and antenna problems |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal |  |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Switched back to mode AA 26Apr05 14:10Z A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode |  |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal |  |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 |  |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure change starting 17 May |  |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer changed to 12 (from 8 mins 5 Apr | ON ENABLED Timer changed to 12 (from 8 mins 5 Apr |  |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 |  |
|  | N12 | N14 | N15 | N16 | N17 | NOAA-N18 |

COMMENTS/CHANGES:

NOAA-12	There were no changes on N12 during the past reporting period.

NOAA-14:	Spacecraft is operating nominally and power subsystem remains stable and above safe state threshold values as the

long slow increase in percentage darkness time per orbit continues through mid-June 05 (illustration 1).  Otherwise there were no changes to N14 during the past reporting period.

NOAA-15:	At 07:21z on 16 May, the N15 HIRS experienced a 1.5 degree jump in filter motor temperature which was almost immediately followed by an abrupt drop in filter motor current of over half an amp and a rapid decline in filter motor temperature as well.  Within an hour and a half of this event, the HIRS filter motor current had fallen even more significantly and returned all the way back to its nominal value of approximately 240 mAmps (earlier in the day it had been almost 400), while filter motor temperature continued a steady decline, also reaching its nominal value of approximately 22 degrees C (it had been almost 34 earlier in the day) by days end.  In addition, during this same time frame, the HIRS period monitor returned to nominal, the filter wheel synch locked back up for the first time in a month and imagery cleared up completely.  EMOSS engineers hypothesize that the initial jump in filter motor temp followed by the rapid decline immediately thereafter might have been an indicator that the filter wheel had possibly broken through the obstruction which had originally caused it to become anomalous in mid-April 05.  In response NOAA upgraded the HIRS (and its filter wheel component) Status to YELLOW.  As of the publication of this report, it remains operational and nominal (see illustrations 2-8).

EMOSS engineers analyzed other subsystems to gauge their response to the significant change in N15’s HIRS temperatures and currents.  The AVHRR appears to have slowed and even reversed a thermal uptrend at about the same time the HIRS was making its improvement (illustration 9).  However, this change may also be attributed to the N15 eclipse season which started at almost the same time that the HIRS situation began.  This same situation may apply to the AMSU-B scan motor temp which also reversed an upward thermal trend on the day HIRS improved (and eclipse season began).  However, the AMSU-B scan motor current has been showing a tendency to operate in a slightly more erratic manner than is preferred although it remains within generally nominal ranges (illustration 10).  The N15 AMSU-A1 and A2 payloads remained operating nominally throughout the past reporting period and showed little to no response to the HIRS situation (illustration 11).

As was stated previously, the N15 eclipse season started on 16 May, at almost the same time that the HIRS was improving (coincidence?)  Analysis of the EPS shows a natural progression into this new environment and no obvious response to the HIRS improvement event (although bus current did increase, perhaps due to eclipse onset, perhaps due to changes in HIRS health profile, perhaps a bit of both.)   See illustrations 12 and 13.

The RF conflict between N12 and N15 ended on 16 May.  In response, VTX-1 on N15 was commanded back on and appears to be operating nominally (illustration 14).  N15 APT data is once again was transmitting after a 1 month absence.

NOAA-16:	The N16 AVHRR scan motor current remained generally stable at less than optimum levels during the past week while

synch delta value continued to exhibit behavior that probably (but not confirmed with imagery) has resulted in a number of MIRP rephases in the past week.  In addition, much of the HRPT imagery analyzed by EMOSS engineers was showing wave patterns in recent days although none had any indications of bar codes.  On the positive side the AVHRR scan motor and baseplate temps have remained nominal and stable even though the AVHRR TCE remains powered off.   (See illustrations 15-16.)

According to AMSU products personnel (Florence Rabier) monitoring statistics have recently been showing an “alarming increase” in noise for channels 9 and 10 of the NOAA16 AMSU-A instrument.  This would not be the first time such problems have occurred on this payload, especially for these channels.  EMOSS analysis of AMSU-A1 health telemetry shows no problems or concerns whatsoever at any time that coincides with this degraded imagery (illustration 17).  AMSU products personnel have highlighted some of the problems which can be reviewed in this report in illustration 18.  This payload is already considered YELLOW in status because of these past data problems and other component failures (notable the PLLO).

The N16 HIRS was nominal and stable last week (illustration 19) as was the ADACS subsystem.

NOAA-17:	The N17 AVHRR scan motor current and temps were both very stable during the past week as was synch delta and

and imagery remained nominal (illustrations 20).  The N17 HIRS was also generally stable during the past week although its period monitor appeared to be slightly less stable than the week before and the filter motor current is just slightly less stable than would be preferred (illustration 21).  On the other hand HIRS temperatures remain nominal and stable and there are no reports of any problems with imagery.

At the request of the Polar Program Office EMOSS is overseeing a change in the N17 SBUV standard operating procedure which is scheduled to begin today, 17 May 05.  The NOAA-17 SBUV currently spends 14 orbits in sweep mode every Tuesday.  This will be reduced to 4 orbits in sweep mode.  These orbits should not cross over the CONUS,

N17 (cont)

or at least not do so in daylight.  The SOMS procedure SBSWMODE will be run every Tuesday and the wait time in this procedure must be changed to 24240 seconds.  These schedule changes are intended to be permanent.

NOAA-N:	EMOSS is a go.  Launch slipped on 11 May due to high winds at VAFB, it slipped on 12 May because of ground

equipment problems (water pumps) and it slipped on 13 May because of a possible kerosene vapor leak into the spacecraft faring.  As of this report being generated, the launch is scheduled for 20 May pending assessment of possible contamination of the spacecraft due to the kerosene leak.

Illustration 1:  N14 EPS Analysis:

(Stable and nominal)

Illustration 2:  N15 HIRS Health Analysis

(An abrupt return to nominal.)

Illustration 3:  N15 HIRS Recovery Analysis (a closer look)

(Note the surge in the temperature, top graph, followed by a rapid improvement in the current and temperature.  Perhaps, the temp surge was the result of the filter wheel breaking through some obstruction.)

Illustration 4:  N15 HIRS Recovery Analysis (cont)

(It took nearly an hour and 20 minutes for the improvement in filter motor current to be reflected in Filter wheel synch and period monitor improvement.  But once it happened, it was sustained.)

Illustration 5:  N15 HIRS Recovery Analysis (Imagery Comparison)

(On the right is the first image following the period monitor recovery.  Imagery remains nominal as of this reports distribution.)

Illustration 6:  N15 HIRS Component Analysis

(A noticeable change in thermal profile is apparent from the time the scan motor improvement occurred, depicted on the above graphs as an “X”.  HIRS Heaters are all off.)

Illustration 7:  N15 HIRS Analysis in perspective

(Depicting what is obviously the most significant and abrupt HIRS anomaly and recovery since at least 2001 began.)

Illustration 8:  N15 HIRS Analysis in perspective (cont)

(Reinforcing the conclusion stated on the previous page.)

Illustration 9:  N15 AVHRR Health

(Looking for HIRS influences on the AVHRR.  Possible some minor thermal improvement occurred on this AVHRR following the HIRS improvement, marked as “X” on the graphs.  Scan motor current improvement occurred well before the HIRS filter wheel current improvement occurred.

Illustration 10:  N15 AMSU-B Analysis (Long and recent term)

(AMSU-B scan motor appears to be performing with a little less stability than desired although it is within historical “nominal” values.  The scan motor temp appears to have been slightly influenced by the HIRS filter wheel improvement.)

Illustration 11:  N15 AMSU-A1 & 2 Health Analysis

(Appear to be nominal and stable and not influenced by HIRS improvement in any way.)

Illustration 12:  N15 Eclipse Season Onset

(Coincided with the HIRS improvement event depicted as “X” above)

Illustration 13:  N15, the Onset of Eclipse Season (cont)

(So far a nominal progression)

Illustration 14:  N15 VTX-1 Turnon Analysis

(Nominal, APT once again flows to the users.)

Illustration 15:  N16 AVHRR Analysis

(Stable at higher levels, not necessarily nominal but it has been much worse also.)

Illustration  16: N16 AVHRR Imagery & Synch Delta Analysis

(Synch delta trend is not favorable and, although they are occurring, no MIRP rephases are apparent in recent GAC imagery because of timing.  They ARE occurring.)

Illustration 17:  N16 AMSU-A1 Health Analysis

(As nominal and stable as it has ever been.  Nothing here to explain the degradation in products being experienced by products personnel.)

Illustration 18:  N16 AMSU-A1 Products Analysis

(as outlined by Michael Chalfant)

Illustration 19:  N17 HIRS Analysis

(Generally stable and nominal)

Illustration 20:  N17 AVHRR Analysis

(stable and nominal)

Illustration 21:  N17 HIRS Health Analysis

(Slightly less stable on the filter wheel current than is typical but otherwise nominal.)

# N17 MEMORY SCRUB REPORT

# Last week

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING May 13, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- |
| FRI. 05/06 | N/A | +178 msec | -160 msec | +089 msec | +037 msec |
| SAT. 05/07 | N/A | +178 msec | -161 msec | +088 msec | +037 msec |
| SUN. 05/08 | -721 msec | +183 msec | -161 msec | +089 msec | +038 msec |
| MON. 05/09 | -720 msec | +183 msec | -162 msec | +089 msec | +038 msec |
| TUE. 05/10 | -727 msec | +183 msec | -163 msec | +090 msec | +040 msec |
| WED. 05/11 | N/A | +178 msec | -164 msec | +089 msec | +040 msec |
| THU. 05/12 | N/A | +180 msec | -165 msec | +090 msec | +040 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12  	*Alternating +/- 500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily ETCUP is utilized to manage clock drift..

Daily ETCUP bias of +6.5 mSec started on 12/10/03.

NOAA-14:  	As of 1223/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

Subtracted 150 mSecs on 30 June

NOAA-15:  	As of 04/23/03 the TIP clock is corrected daily by –8 msec to compensate for drift.

Added 100 msec to spacecraft command clock on 31 Aug 04

NOAA-16:  	As of 12/23/03 the TIP clock is corrected daily by –5.5 msec to compensate for drift.

Subtracted 100 msec from spacecraft command clock on 31 Aug 04.

NOAA-17:  	As of 12/23/03 the TIP clock is corrected daily by –3 msec to compensate for drift.

Added 125 Msecs3 Feb 04.

EMOSS ON CONSOLE SCHEDULE FOR 20 MAY LAUNCH OF N18

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Micky Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Angelique Riley, EMOSS, POES Comm and DHS			301-817-4028

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015