# OPERATIONAL PROCEDURES FOR THE

# RICH TEST BEAM STAND AT THE

# MESON TEST BEAM FACILITY

# BTEV ENGINEERING NOTE 8918.130-EN-XXX

Author: Herman Cease, PPD/MECH. DEPT/BTEV

March 15, 2002

Edited June 11, 2004

Edited August 18, 2004

# Approved By:___________________

PPD/MECH. DEPT/BTeV Project Mech. Support Leader

### LIST OF PROCEDURES

N2 Fill Procedure

C4F8O Fill Procedure

Drain Procedure

Operating Procedure

Purge Procedure

Failure mode Analysis

1) What if a power outage occurs during normal operation?

2) What if a power outage occurs during a gas fill operation?

3) What if a power outage occurs during a purge/recycle operation?

4) What if a valve is CLOSEd by mistake and the recirculating pump deadheads?

5) What if the 15 psi backpressure valve fails?

6) What if the gas fill procedure is not followed?

7) What if the gas purge/recycle procedure is not followed?

# N2 Fill Procedure

# Purpose:

The purpose of this procedure is to fill the system with the nitrogen gas the first time the system is used. The nitrogen gas is used as a gas to initially purge the system of contaminates and water vapor.

# Procedure:

Inert gas is plumbed into the system via a manifold in the gas shed at MV-1103.

- Prepare the system by OPENing valves MV1104, MV1106, MV-1119, and MV 1301. CLOSE valves MV-1201, MV-1202, MV-1214, MV-1103, MV-1217 and MV-1302.  Open MV-1305 as a vent. The expansion volume should be deflated – at its smallest volume.  FI-1104 can be used to monitor the flow rate.

- Turn on the nitrogen vent purge line by OPENing the metering valve on FI-1104. The flow should be small, about 20 scfh air.

- The nitrogen should flow for a minimum of 2 hrs to completely purge the system with one exchange volume. Independently OPEN and CLOSE valves MV-1201 and MV-1202 to ensure nitrogen has been purged through the plumbing lines and Cerenkov tank.  Humidity sensor 1114 can also be monitored.

- Once the system has been purged, CLOSE valve MV-1305, MV-1201 and MV-1202. Inflate the expansion volume until the height gage HT-1119 is reading appropriately for the current barometric pressure. (HT-1119 should be in the middle of its scale when the current barometric pressure is reading 14.7 psia). Then CLOSE valve the metering valve on FI-1104 and MV-1103.

- The system should be stable.

# C4F8O Fill Procedure, and Purification

# Purpose:

The purpose of this procedure is to fill the system with the C4F8O gas with purity better than 99%. This procedure assumes the system was backfilled with dry nitrogen gas.

# Procedure:

- Prepare the system in a purging configuration, OPEN valves MV-1104, MV-1106, MV-1119, MV-1214, MV-1301 and MV-1201. CLOSE valves, MV-1101, MV-1202, and MV-1300. Turn OFF the circulating pump-1099.

- Start filling the system with C4F8O by opening valve MV-1103 and regulating the flow with PRV-1102 and the metering valve on FI-1104.

- Turn on the automatic control loop. The loop turns on pump 1240 if the expansion volume becomes full and turns the pump off when the expansion pump is low. C4F8O is flowing into the system at a low flow rate. Make sure that the flow rate thru FI-1303 is greater than FI-1104 when the pump is operating.

- Monitor the differential pressure gage DPT-1118 and PT-1111, when the gage indicates a static head of C4F8O the system has been filled.

- Monitor DPT-1233, when liquid has formed in the condensation tank, it can be re-evaporated and used to fill the cerenkov tank. Open valves MV-1217 and PRV-1218.

- The purity of the gas can be monitored by taking samples from MV-1305 and checking the density of the gas. A simple method is to weigh a known volume of the gas using a small sample bottle.

Drain Procedure

# Purpose:

The purpose of this procedure is to have a method to drain and recapture as much of the C4F8O gas as possible, while backfilling the tank with an inert dry gas like nitrogen.

# Procedure:

- Operate the system using the fill procedure, however substitute C4F8O supply bottle with a N2 gas bottle.

- Once the condensation tank 1219 is full, stop the system and close all valves.

- Attach a DOT approved empty cylinder to sample port MV-1219. OPEN MV-1219 and allow the liquid to be transferred into the DOT cylinder.

- Repeat steps 1, 2 and 3 until all of the condensed gas has been transferred into the DOT cylinder.

# FAILURE MODE ANALYSIS –OLD VERSION

# Summary:

A failure mode analysis is performed on the system. In the event a failure does occur, the failure mode analysis will indicate what the possible actions are for the different failure modes.

## Failure mode Analysis

1) What if a power outage occurs during normal operation?

Risk: Re-circulating pump turns OFF.

Result:	Possible increase in radiator gas contamination.

Risk: Instrumentation turns OFF.

Result: Operator may not understand exact gas properties during power outage.

2) What if a power outage occurs during a gas fill operation?

Risk: May overfill tank.

Result: Tank cannot be overfilled/pressurized because it has a relief valve.

Risk: May waste gas by overfilling tank.

Result: Operator knows to stop the gas fill by closing the gas fill manual valve.

3) What if a power outage occurs during a purge/recycle operation?

Risk: Condensation tank warms up.

Result: Gas vaporization cannot overfill/pressurize the Cerenkov tank because it has a relief valve.

Risk: May waste gas by overfilling Cerenkov tank.

Result: Operator should stop the gas fill, CLOSE the gas fill manual valve and CLOSE the condensation tank manual isolation valve.

4) What if a valve is CLOSEd by mistake and the re-circulating pump deadheads?

Risk: Excessive head pressure at the pump could damage the pump.

Result: A relief valve is located on the discharge side of the pump, if the pressure becomes excessive, the valve vents to the pump suction.

5) What if water condenses out in the condensation tanks?

Risk: Water vapor contamination in the Cerenkov tank.

Result: All gas entering the Cerenkov tank is first filtered through a desiccant dryer, and the gas is monitored with a humidity sensor before entering the Cernekov tank.

6) What if the Condensation tanks overfill?

Risk: Wasting C4F8O Gas.

Result: The operator should monitor the level in the condensation tanks to prevent over filling and wasting the c4f8o.

7) What if there is a fire?

Risk: Flammable gas?

Result: This gas is a non-toxic non-flammable gas.

8) What if there is a leak?

Risk: ODH concerns.

Result: The system contains a fixed volume of gas that is approximately 250 ft^3. The system is located at Meson Test Beam Facility where the room volume is very large (~30,000 cu. Feet.). The gas will not displace enough oxygen to become an ODH concern.

9) What if the condensation tank warms up and the C4F8O starts to vaporize and backfills into the Cerenkov tank?

Risk: Wasting C4F8O gas, contamination of the Cerenkov tank.

Result: The Cerenkov tank will overfill, causing the C4F8O gas to be vented out the relief valve in the expansion volume. The operator should realize an error has occurred when the expansion volume starts inflating which would be observed by monitoring the height gage HT-119.

The vapor could also be vented out the relief valve on the condensation tank.

Appendix A

Tables:

| Calculate static head of c4f8o |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | 8.46117 | kg/m^3 | density of gas relative to air) |
| height |  |  |  |  |  |
| of column | static head |  |  |  |
| m | Pascals | feet | inches | psid | inches h20 |
| 0 | 0 | 0 | 0 | 0 | 0 |
| 0.015206424 | 1.27249 | 0.04989 | 0.598678 | 0.000185 | 0.005108 |
| 0.6096 | 51.0119 | 2 | 24 | 0.007398 | 0.204788 |
| 1.2192 | 102.024 | 4 | 48 | 0.014797 | 0.409575 |
| 1.1938 | 99.8984 | 3.916667 | 47 | 0.014489 | 0.401042 |
| 1.4986 | 125.404 | 4.916667 | 59 | 0.018188 | 0.503436 |
| 0.4318 | 36.1335 | 1.416667 | 17 | 0.005241 | 0.145058 |
| 0.7366 | 61.6394 | 2.416667 | 29 | 0.00894 | 0.247452 |
| 1.0414 | 87.1454 | 3.416667 | 41 | 0.012639 | 0.349845 |
| 1.3462 | 112.651 | 4.416667 | 53 | 0.016338 | 0.452239 |
| 1.524 | 127.53 | 5 | 60 | 0.018496 | 0.511969 |

Vapor pressure

29.5 psia  (14.8 psig) at @20C

Appendix B

C4F8O MSDS

Page 1

Page 1 of 6

MATERIAL SAFETY DATA SHEET

1. CHEMICAL PRODUCT AND COMPANY IDENTIFICATION

MATHESON TRI-GAS, INC.

EMERGENCY CONTACT:

959 ROUTE 46 EAST

CHEMTREC 1-800-424-9300

PARSIPPANY, NEW JERSEY 07054-0624

INFORMATION CONTACT:

973-257-1100

SUBSTANCE: OCTAFLUOROTETRAHYDROFURAN

TRADE NAMES/SYNONYMS:

MTG MSDS 249; PERFLUOROTETRAHYDROFURAN; C4F8O; 00227392

CHEMICAL FAMILY: cyclic, halogenated, ethers

CREATION DATE: Oct 26 2001

REVISION DATE: Mar 19 2003

2. COMPOSITION, INFORMATION ON INGREDIENTS

COMPONENT: OCTAFLUOROTETRAHYDROFURAN

CAS NUMBER: 773-14-8

PERCENTAGE: 100

3. HAZARDS IDENTIFICATION

NFPA RATINGS (SCALE 0-4): HEALTH=2 FIRE=0 REACTIVITY=0

EMERGENCY OVERVIEW:

COLOR: colorless

PHYSICAL FORM: compressed, liquefied gas

ODOR: odorless

MAJOR HEALTH HAZARDS: difficulty breathing

PHYSICAL HAZARDS: Containers may rupture or explode if exposed to heat.

POTENTIAL HEALTH EFFECTS:

INHALATION:

SHORT TERM EXPOSURE: nausea, vomiting, irregular heartbeat, headache, drowsiness, fatigue,

dizziness, tingling sensation, loss of coordination, suffocation, convulsions, unconsciousness, coma

LONG TERM EXPOSURE: no information is available

Page 2 of 6

SKIN CONTACT:

SHORT TERM EXPOSURE: frostbite

LONG TERM EXPOSURE: no information is available

EYE CONTACT:

SHORT TERM EXPOSURE: frostbite, blurred vision

LONG TERM EXPOSURE: no information is available

INGESTION:

SHORT TERM EXPOSURE: frostbite

LONG TERM EXPOSURE: no information on significant adverse effects

4. FIRST AID MEASURES

INHALATION: If adverse effects occur, remove to uncontaminated area. Give artificial respiration if not

breathing. If breathing is difficult, oxygen should be administered by qualified personnel. Get immediate

medical attention.

SKIN CONTACT: If frostbite or freezing occur, immediately flush with plenty of lukewarm water (105-

115 F; 41-46 C). DO NOT USE HOT WATER. If warm water is not available, gently wrap affected parts in

blankets. Get immediate medical attention.

EYE CONTACT: Contact with liquid: Immediately flush eyes with plenty of water for at least 15 minutes.

Then get immediate medical attention.

INGESTION: If a large amount is swallowed, get medical attention.

NOTE TO PHYSICIAN: For inhalation, consider oxygen.

5. FIRE FIGHTING MEASURES

FIRE AND EXPLOSION HAZARDS: Negligible fire hazard. Containers may rupture or explode if

exposed to heat.

EXTINGUISHING MEDIA: carbon dioxide, regular dry chemical

Large fires: Use regular foam or flood with fine water spray.

FIRE FIGHTING: Move container from fire area if it can be done without risk. Cool containers with water

spray until well after the fire is out. Stay away from the ends of tanks. Withdraw immediately in case of

rising sound from venting safety device or any discoloration of tanks due to fire. For tank, rail car or tank

truck, evacuation radius: 800 meters (1/2 mile). Use extinguishing agents appropriate for surrounding fire.

Cool containers with water spray until well after the fire is out. Apply water from a protected location or

from a safe distance. Do not get water directly on material. Reduce vapors with water spray. Avoid

inhalation of material or combustion by-products. Stay upwind and keep out of low areas. Consider

downwind evacuation if material is leaking.

Page 3

Page 3 of 6

FLASH POINT: not flammable

LOWER FLAMMABLE LIMIT: not flammable

UPPER FLAMMABLE LIMIT: not flammable

HAZARDOUS COMBUSTION PRODUCTS:

Thermal decomposition products or combustion: oxides of carbon, hydrogen fluoride, perfluoroisobutylene

6. ACCIDENTAL RELEASE MEASURES

OCCUPATIONAL RELEASE:

Stop leak if possible without personal risk. Keep unnecessary people away, isolate hazard area and deny

entry. Stay upwind and keep out of low areas.

7. HANDLING AND STORAGE

STORAGE: Store and handle in accordance with all current regulations and standards. Store in a well-

ventilated area. Avoid heat, flames, sparks and other sources of ignition. Avoid direct sunlight. Subject to

storage regulations: U.S. OSHA 29 CFR 1910.101. Keep separated from incompatible substances.

8. EXPOSURE CONTROLS, PERSONAL PROTECTION

EXPOSURE LIMITS:

OCTAFLUOROTETRAHYDROFURAN:

No occupational exposure limits established.

VENTILATION: Provide local exhaust ventilation system. Ensure compliance with applicable exposure

limits.

EYE PROTECTION: For the gas: Eye protection not required, but recommended. For the liquid: Wear

splash resistant safety goggles. Contact lenses should not be worn. Provide an emergency eye wash fountain

and quick drench shower in the immediate work area.

CLOTHING: For the gas: Protective clothing is not required. For the liquid: Wear appropriate protective,

cold insulating clothing.

GLOVES: Wear insulated gloves.

PROTECTIVE MATERIAL TYPES: neoprene

RESPIRATOR: Under conditions of frequent use or heavy exposure, respiratory protection may be needed.

Respiratory protection is ranked in order from minimum to maximum. Consider warning properties before

use.

For Unknown Concentrations or Immediately Dangerous to Life or Health -

Page 4

Page 4 of 6

Any supplied-air respirator with full facepiece and operated in a pressure-demand or other positive-pressure

mode in combination with a separate escape supply.

Any self-contained breathing apparatus with a full facepiece.

9. PHYSICAL AND CHEMICAL PROPERTIES

PHYSICAL STATE: gas

COLOR: colorless

PHYSICAL FORM: compressed, liquefied gas

ODOR: odorless

MOLECULAR WEIGHT: 216.03

MOLECULAR FORMULA: C4-F8-O

BOILING POINT: 31 F (-0.8 C)

FREEZING POINT: Not available

VAPOR PRESSURE: 29.5 psia @ 20 C

VAPOR DENSITY: Not available

SPECIFIC GRAVITY: Not applicable

DENSITY: 1.52 g/mL

WATER SOLUBILITY: Not available

PH: Not applicable

VOLATILITY: 100%

ODOR THRESHOLD: Not available

EVAPORATION RATE: Not applicable

VISCOSITY: 0.1 cP

COEFFICIENT OF WATER/OIL DISTRIBUTION: Not applicable

10. STABILITY AND REACTIVITY

REACTIVITY: Stable at normal temperatures and pressure.

CONDITIONS TO AVOID: Protect from physical damage and heat. Containers may rupture or explode if

exposed to heat.

INCOMPATIBILITIES: oxidizing materials

HAZARDOUS DECOMPOSITION:

Thermal decomposition products or combustion: oxides of carbon, hydrogen fluoride, perfluoroisobutylene

POLYMERIZATION: Will not polymerize.

11. TOXICOLOGICAL INFORMATION

Not available

Page 5

Page 5 of 6

12. ECOLOGICAL INFORMATION

Not available

13. DISPOSAL CONSIDERATIONS

Dispose in accordance with all applicable regulations.

14. TRANSPORT INFORMATION

U.S. DOT 49 CFR 172.101:

PROPER SHIPPING NAME: Compressed gas, n.o.s.

(OCTAFLUOROTETRAHYDROFURAN)

ID NUMBER: UN1956

HAZARD CLASS OR DIVISION: 2.2

LABELING REQUIREMENTS: 2.2

CANADIAN TRANSPORTATION OF DANGEROUS GOODS:

SHIPPING NAME: Compressed gas, n.o.s. (OCTAFLUOROTETRAHYDROFURAN)

UN NUMBER: UN1956

CLASS: 2.2

15. REGULATORY INFORMATION

U.S. REGULATIONS:

CERCLA SECTIONS 102a/103 HAZARDOUS SUBSTANCES (40 CFR 302.4): Not regulated.

SARA TITLE III SECTION 302 EXTREMELY HAZARDOUS SUBSTANCES (40 CFR 355.30): Not

regulated.

SARA TITLE III SECTION 304 EXTREMELY HAZARDOUS SUBSTANCES (40 CFR 355.40): Not

regulated.

SARA TITLE III SARA SECTIONS 311/312 HAZARDOUS CATEGORIES (40 CFR 370.21):

ACUTE: Yes

CHRONIC: No

FIRE: No

REACTIVE: No

SUDDEN RELEASE: Yes

SARA TITLE III SECTION 313 (40 CFR 372.65): Not regulated.

Page 6

Page 6 of 6

OSHA PROCESS SAFETY (29CFR1910.119): Not regulated.

STATE REGULATIONS:

California Proposition 65: Not regulated.

CANADIAN REGULATIONS:

WHMIS CLASSIFICATION: Not determined.

NATIONAL INVENTORY STATUS:

U.S. INVENTORY (TSCA): Listed on inventory.

TSCA 12(b) EXPORT NOTIFICATION: Not listed.

CANADA INVENTORY (DSL/NDSL): Not determined.

16. OTHER INFORMATION

©Copyright 1984-2004 MDL Information Systems, Inc. All rights reserved.

MATHESON TRI-GAS, INC. MAKES NO EXPRESS OR IMPLIED WARRANTIES,

GUARANTEES OR REPRESENTATIONS REGARDING THE PRODUCT OR THE

INFORMATION HEREIN, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY

OF MERCHANTABILITY OR FITNESS FOR USE. MATHESON TRI-GAS, INC. SHALL NOT BE

LIABLE FOR ANY PERSONAL INJURY, PROPERTY OR OTHER DAMAGES OF ANY

NATURE, WHETHER COMPENSATORY, CONSEQUENTIAL, EXEMPLARY, OR

OTHERWISE, RESULTING FROM ANY PUBLICATION, USE OR RELIANCE UPON THE

INFORMATION HEREIN.