SVX II Upgrade Readout Electronics

Fast Control, Timing, Data &

Resynchronization Links

&

Aborts, Resets,

Errors, Error Detection

& System Recovery

Ed Barsotti & Sergio Zimmerman

August 17, 1995

Version  0.0

Document # ESE-SVX-950805

DRAFT DOCUMENT

Table Of Contents

1. Introduction

2. Fast Controls (Trigger System Interface) & Timing (Master Clock) Links

2.1. Fast Controls (Trigger System Interface) Link

2.1.1. Fiber Optic Serial Command Link To The Silicon Readout Controller (SRC)

2.1.1.1. Signal Definitions

2.1.1.2. Connectors & Cables

2.1.1.3. Examples Of Link Use

2.1.1.4. Error Detection & System Recovery

2.1.2. Coax Control Signals To The Trigger System Interface

2.1.2.1. Signal Definitions

2.1.2.2. Connectors & Cables

2.1.2.3. Examples Of Link Use

2.1.2.4. Error Detection & System Recovery

2.2. Master Clock Interface Link

2.2.1. Signal Definitions & Levels

2.2.2. Connectors & Cables

2.2.3. Terminations (If Any)

2.2.4. Examples Of Link Use

2.2.5. Error Detection & System Recovery

2.3. SRC To/From SRC Fanout Links

2.3.1. Fast Control Signals From The SRC Module

2.3.1.1. Signal Definitions & Levels

2.3.1.2. Connectors & Cables

2.3.1.3. Terminations (If Any)

2.3.1.4. Examples Of Link Use

2.3.1.5. Error Detection & System Recovery

2.3.2. Fast Control Signals To The SRC Module

2.3.2.1. Signal Definition & Level

2.3.2.2. Connectors & Cables

2.3.2.3. Terminations (If Any)

2.3.2.4. Examples Of Link Use

2.3.2.5. Error Detection & System Recovery

2.4. VRB Crate (Fast Control) Backplane Link

2.4.1. Fast Control Signals From The SRC Fanout Module

2.4.1.1. Signal Definitions & Levels

2.4.1.2. Backplane Connector Pin Assignments

2.4.1.3. Backplane Signal DC Bias & Termination Networks

2.4.1.4. Examples Of Link Use

2.4.1.5. Error Detection & System Recovery

2.4.2. Fast Control Signals To The SRC Fanout Module

2.4.2.1. Signal Definition & Level

2.4.2.2. Connectors & Cables

2.4.2.3. Terminations (If Any)

2.4.2.4. Examples Of Link Use

2.4.2.5. Error Detection & System Recovery

2.5. VRB Crate J1 (Slow Control) Backplane (Serial) Link

2.5.1. Signal Definitions & Levels

2.5.2. Connectors & Cables

2.5.3. Terminations (If Any)

2.5.4. Examples Of Link Use

2.5.5. Error Detection & System Recovery

2.6. SRC To FIB Crate (Fast Control & Timing) Links

2.6.1. Signal Definitions

2.6.2. Link Transmission Format

2.6.3. Connectors & Cables

2.6.4. Examples Of Link Use

2.6.5. Error Detection & System Recovery

2.7. FIB Crate (Fast Control & Timing) Backplane Link

2.7.1. Signal Definitions & Levels

2.7.2. Backplane Connector Pin Assignments

2.7.3. Backplane Signal DC Bias & Termination Networks

2.7.4. Examples Of Link Use

2.7.5. Error Detection & System Recovery

2.8. FIB To PC (Fast Control & Timing) Link

2.8.1. Signal Definitions & Levels

2.8.2. Connectors & Cables

2.8.3. Terminations (If Any)

2.8.4. Examples Of Link Use

2.8.5. Error Detection & System Recovery

3. SVX 3 IC Event Data/Control Link

3.1. Signal Definitions & Levels

3.2. Connectors & Cables

3.3. Terminations (If Any)

3.4. Examples Of Link Use

3.5. Error Detection & System Recovery

4. Additional Event Data Links

4.1. PC To FIB Event Data Link

4.1.1. Signal Definitions & Levels

4.1.2. Connectors & Cables

4.1.3. Terminations (If Any)

4.1.4. Examples Of Link Use

4.1.5. Error Detection & System Recovery

4.2. FIB to Optical Distribution Box (Splitter) Event Data Link

4.2.1. Signal Definitions & Levels

4.2.2. Connectors & Cables

4.2.3. Terminations (If Any)

4.2.4. Examples Of Link Use

4.2.5. Error Detection & System Recovery

4.3. Optical Distribution Box To ERB Module Event Data Link

4.3.1. Signal Definitions & Levels

4.3.2. Connectors & Cables

4.3.3. Terminations (If Any)

4.3.4. Examples Of Link Use

4.3.5. Error Detection & System Recovery

4.4. Optical Distribution Box To SVT Trigger Event Data Link

4.4.1. Signal Definitions & Levels

4.4.2. Connectors & Cables

4.4.3. Terminations (If Any)

4.4.4. Examples Of Link Use

4.4.5. Error Detection & System Recovery

5. (Event Data) Resynchronization Link

5.1. Signal Definitions & Levels

5.2. Connectors & Cables

5.3. Terminations (If Any)

5.4. Examples Of Link Use

5.5. Error Detection & System Recovery

6. Aborting SVX Readout & System Recovery

Introduction

This document gives details of all fast control, timing, event data & resynchronization links used in the SVX II Upgrade readout electronics project.  The intention of this document is not to include all implementation details for each link but to provide a single document containing information for each link such that proper integrated systems engineering is more easily accomplished.  For example, this document can be used as a guide for studying how the system is initialized, readout is aborted, event data links are resynchronized, link errors and system recovery techniques, etc.

Fast Controls (Trigger System Interface) & Timing (Master Clock) Links

Fast Controls (Trigger System Interface) Link

The Ôfast controlsÕ link between the Trigger System Interface (TSI) and the SRC module consists of one 175 MHz fiber optic ÔTaxiÕ command link from the TSI to the Silicon Readout Controller (SRC) and three copper coax control signals from the SRC to the TSI.

For a more complete definition of these command link words and control signals and an explanation of their use in a front-end readout system such as SVX, refer to the February 8, 1995 Yale Trigger Note #1 ÒConceptual Design of the Trigger System Interface for the Run II UpgradeÓ and a subsequent August 14, 1995 CDF Group/Yale University draft note ÒTrigger Supervisor Protocols for Run IIÓ.

Fiber Optic Serial Command Link To The Silicon Readout Controller (SRC)

There are four different types of control ÔwordsÕ sent by the TSI to the SRC as given in the following four tables:

| Bit | Definition |
| --- | --- |
| 0 | C0 (Always 0 for Level 1 word) |
| 1 | C1 (Always 0 for Level 1 word) |
| 2 | L1A (1 for Level 1 Accept) |
| 3 | L1RO (1 for Level 1 Reject) |
| 4 | L1B0 (Buffer address for L1A, LSB) |
| 5 | L1B1 (Buffer address for L1A, MSB) |
| 6 | RSRV1 (Reserved) |
| 7, 8 | Spare |

Table 1

Level 1 Word

Level 1 Accepts (L1A) are passed on by the SRC to all on-detector FIB crates whereas Level 1 Rejects are not used by the SVX readout electronics.  L1B0 & L1B1 along with gated RSRV1 are passed through SVX Fanout Modules to all VME Readout Buffer (VRB) modules as the three least significant bits of Store Buffer ID (see Table 7).

Question 1:	What does D0 need passed to VRB modules as a result of L1As or L1Rs?

If the SRC received two or more Level 1 Accepts in a row (e.g., two consecutive bunch crossings result in Level 1 Accepts), the SRC always immediately forwards the L1A to the FIB crates but does not send the ÒRead pipeline/digitize/readoutÓ command (see Table 10) for the second L1A and subsequent L1As until data from the previous L1A has been sent to VRB modules (SVX_DONE signal in the SRC returned to logic Ô1Õ {see Section 2.3.2}).

Question 2:	Can D0 operate in an identical manner?

Question 3:	Assuming the SRC keeps statistics of available buffers in the VRB modules, what should the SRC do if it is told by the TSI of a L1A and given a Ônot-freeÕ buffer to use for that L1AÕs event data fragments?  Should ERROR be sent to the TSI and this condition logges by the SRC for later VME monitoring readout?  Should WAIT be sent to the TSI (for how long?) until the buffer becomes free?  How does D0 (or calorimetry, etc.) want to handle this situation?

| Bit | Definition |
| --- | --- |
| 0 | C0 (Always 0 for SES word) |
| 1 | C1 (Always 1 for SES word) |
| 2 | SESB0 (Buffer Address for SES, LSB) |
| 3 | SESB1 (Buffer Address for SES, MSB) |
| 4 | RSRV2 (Reserved) |
| 5 | EVID0 (Bit 0 of DAQ Event ID, LSB) |
| 6 | EVID1 (Bit 1 of DAQ Event ID, LSB) |
| 7 | EVID2 (Bit 2 of DAQ Event ID, LSB) |
| 8 | EVID3 (Bit 3 of DAQ Event ID, LSB) |

Table 2

Start Event Scan Word

Why did D0 want to send buffer ID through J3?  because their VBD canÕt do it over VME.  EVID passed through J3 backplane to VRB.  Who checks this SVT, VRB  ... or FIB.

Abort of Readout ... how?  Who decides there should be an abort?  How is this accomplished?  Maybe we need another line from SVT to SRC for Abort.  FIB sends an artificial EOR after ABORT command from SRC.  SVT does not send L2A.

| Bit | Name | Definition |
| --- | --- | --- |
| 0 | C0 | Always 1 for CALIBEN word |
| 1 | C1 | Always 0 for CALIBEN word |
| 2-4 | CALIB0-CALIB2 |

Currently defined as follows:

000 Scope trigger

001 Charge injection

010 Laser

| 111 No action |
| --- |
| 5-8 | Spare |

Table 3

Calibration Enable Word

| Bit | Name | Definition |
| --- | --- | --- |
| 0 | C0 | Always 1 for Control word |
| 1 | C1 | Always 1 for Control word |
| 2 | HALT | Stop Input to Level 1 buffer |
| 3 | RESET | Reset of pipeline buffers, pointers, etc. |
| 4 | TEST |

For testing TSI to SRC link as follows:

| Upon receipt of first TEST=1, SRC sets DONE=0 and ERROR & WAIT=1. Upon receipt of the second TEST=1, SRC sets DONE=1 and ERROR & WAIT=0. |
| --- |
| 5 | RUN | Start input to Level 1 pipeline upon receipt of next Bunch Zero |
| 6-8 | SCN0-SCN2 |

Scan list bits; determines which scan list the SRC should use

For the Scan List to change, bits 2 through 5 must be zero.

The Scan Lists currently defined are as follows:

000 Default

001 YMON

010 Plug Calorimeter

011 Trigger Dump

Table 4

Control Word

Bunch Zero is received from the Master Clock System less than or equal to 21 microseconds after the SRC received Run from the Trigger System Interface.  When Bunch Zero is received, the Level 1 pipeline in the SVX 3 ICs can start to be filled and be waiting for Level 1 Accepts.

Question 4:	What do we (CDF SVX) do with all these bits especially SCN0-SCN2?  For example, do we reset pipeline capacitor to zero when RESET is received?

Question 5:	When the TSI goes through a HALT-RESET-RUN sequence, how do we operate?  There is talk of using DONE or WAIT in another capacity during this sequence.  When RESET is received, DONE possible would be set to logic zero until the SVX system is reset whereupon DONE would be set to logic one.  Do we disable sending any signals (e.g., SYNCs) to the detector during this sequence?  How does D0 operate when resetting and are there any features needed in the VRB to accomodate D0s ÔHALT-RESET-RUNÕ sequence?

Signal Definitions

Connectors & Cables

Examples Of Link Use

Error Detection & System Recovery

Coax Control Signals To The Trigger System Interface

Fast controls link control signals returned by the SRC to the Trigger System Interface (TSI) consists of three coax cable signals as given in the following table:

| Name | Definition |
| --- | --- |
| DONE | Deasserted at receipt of Start Event Scan word & reasserted when internal (Level 2) buffer is again EMPTY |
| ERROR | Asserted if a Fatal Error is detected in the SVX system |
| WAIT | Asserted if a potential busy condition is detected in the SVX system |

Table 5

Control Signals To The TSI

Question 6:	Does DONE only come from the SRC or is there a DONE from each VRB module?

Question 7:	Should ERROR or WAIT be asserted when Ôloss of synchronizationÕ in either an event data link or the SRC_Fanout is detected?

Note 1:	It was decided that ERROR used.  Loss of synchronization should be a rare error.

Question 8:	Should there be one DONE line for the whole SVX system?  Power on sets DONE.  VME command set and reset DONE.

Signal Definitions

Connectors & Cables

Examples Of Link Use

Error Detection & System Recovery

Master Clock Interface Link

The Master Clock System is designed to provide signals of any frequency or wave shape based on the acceleratorÕs 53 MHz clock.  The frequency, wave shape and phase, relative to the acceleratorÕs 53 MHz clock, of each signal is controllable via VME.  Phase adjustments are in one nanosecond increments.  The signals are transmitted using differential PECL logic levels.

Signal Definitions & Levels

The following four signals are transmitted by the Master Clock System to the SRC module:

| Name | Definition |
| --- | --- |
| SVX Clock | 53 MHz clock signal synchronized to the accelerator 53 MHz clock |
| SYNC | Signal synchronized to the accelerator 53 MHz clock, one SVX Clock period in duration, centered at the low to high transition of SVX Clock, occuring once every 132 nanoseconds and indicating the possible presense of a proton-antiproton bunch crossing |
| Bunch Crossing | Signal synchronized to the accelerator 53 MHz clock, one SVX Clock period in duration, centered at the low to high transition of SVX Clock, occuring whenever there is a proton-antiproton bunch crossing (excluding beam gaps, Bunch Crossings occur every 132 or 396 nanoseconds depending upon the current accelerator operation mode) |
| Bunch Zero | Signal synchronized to the accelerator 53 MHz clock, one SVX Clock period in duration, centered at the low to high transition of SVX Clock, occuring once every revolution of beam in the accelerator main ring at ???? time |

Table 6

Master Clock Signals To The SRC

Question 9:	Should ÔSVX ClockÕ be changed to ÔCDF ClockÕ?

Question 10:	What is the CDF_CLK described in the CDF Synchronization proposal?

Question 11:	Is the SRC the only SVX device with a 8-bit Bunch Counter?  If so, how is global checking accomplished?  Also since all data has to be tagged with the Bunch Crossing number unless the SVT has a Bunch Counter, the FIBs have to send the Bunch Counter number to the SVT.

Question 12:	Should the FIB or the SVT and VRBs tag data with the Bunch Crossing number?

Question 13:	Is it the Bunch Crossing or the Beam Crossing signal?

Note 2:	The Bunch Counter counting should not be gated by the Bunch Crossing signal.

Abort gaps ... preamp reset during big abort gaps ... ³ two syncs without bunch crossing

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

SRC To/From SRC Fanout Links

Fast Control Signals From The SRC Module

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

Fast Control Signals To The SRC Module

SVX_DONE, SYNC_ERROR, (other errors?), WAIT? (calorimeter BUSY instead of it being from on-detector crate?)

Signal Definition & Level

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

VRB Crate (Fast Control) Backplane Link

The following sections describe Fast Control signals sent between a VME Readout Buffer (VRB) crateÕs SRC Fanout module and its VME Readout Buffer modules.

Fast Control Signals From The SRC Fanout Module

Signal Definitions & Levels

The following two tables list signals, signal definitions & signal levels on the VRB Crate (Fast Control) J3 Backplane Link:

| Signal Name | Signal Definition | Signal Level |
| --- | --- | --- |
| Store Buffer ID (3:0) | Buffer in which to store next received event data fragments (Level 1 accepted event data) | Differential RS-485 |
| Store Buffer ID Strobe | Signal used to load Store Buffer ID (3:0) | Differential RS-485 |
| Read Buffer ID (3:0) {Note 2} | Buffer from which to read next event data fragments | Differential RS-485 |
| Read Buffer ID Strobe | Signal used to load Read Buffer ID (3:0) | Differential RS-485 |
| Bunch Counter Number (7:0) {Note 3} | CDF system-wide beam bunch counter | Differential RS-485 |
| Bunch Counter Strobe | Signal used to load Bunch Counter (7:0) | Differential RS-485 |

Table 7

Signals From SRC Module To SRC Fanout Module

& VME Readout Buffer (VRB) Modules

Note 3:	Read Buffer ID (3:0) is only needed if the VME bus cannot be used by the system to specify the buffer from which to read next event data fragments.

Question 14:	Is Read buffer ID (3:0) required because of the capabilities of the D0 readout controller?

Note 4:	Only needed if VRB modules check that FIB modules correctly append Bunch Counter to event data fragments.  If this data integrity check is done, what is being checked at the VRB modules is the correct Bunch Counter data transmission from the SRC to the FIB Crate Fanout modules, from the Fanout modules to the FIB modules, FIB appending of the Bunch Counter to their event data fragments, and data transmission from the FIB modules to the VRB modules.

Note 5:	Store Buffer ID, Read Buffer ID (if needed) & Bunch Counter could be sent on shared lines via encoded commands with a common strobe ... to reduce signal line count.

| Signal Name | Signal Definition | Signal Level |
| --- | --- | --- |
| SYNC_ERR | Loss of G-link synchronization detected in VRB module | Differential RS-485 {Note 3} |
| BC_ERR | Bunch crossing data integrity error detected in VRB module | Differential RS-485 {Note 4} |

Table 8

Signals From VRB Modules To SRC Fanout Module To SRC Module

Note 6:	SYNC_ERR RS-485 lines biased such that SYNC_ERR = 0 when all VBR module SYNC_ERR RS-485 drivers are in tri-state mode.  VRB module only puts its SYNC_ERR RS-485 driver in non tri-state mode when it drives SYCN_ERR = 1.  SYNC_ERR remains asserted until loss of G-link synchronization is no longer detected by the VRB module.

Note 7:	BC_ERR RS-485 lines biased such that BC_ERR = 0 when all VBR module BC_ERR RS-485 drivers are in tri-state mode.  VRB module only puts its SYNC_ERR RS-485 driver in non tri-state mode when it drives BC_ERR = 1.  Only needed if VRB modules check that FIB modules correctly append Bunch Counter to event data fragments.  See Note 3 above.

Question 15:	How long is BC_ERR asserted and how is it reset?

Backplane Connector Pin Assignments

******** 160-pin DIN for J3 connector ********

Backplane Signal DC Bias & Termination Networks

In order to ensure that backplane signals are both at a pre-defined state when not driven and are not unduly susceptible to noise, all VRB Crate differential RS-485 backplane signals are terminated at one end with a DC bias network and at the other end with a resistor termination as follows:

DC  Bias Network:

Each differential RS-485 pair has a DC bias network consisting of a 120 ohm resistor connected at one end to +5 volts and at its other end to a 240 ohm resistor.  The opposite end of the 240 ohm resistor is connected to ground through another 120 ohm resistor.  Each differential RS-485 pair connects across the 240 ohm resistor.  Receivers are connected such that logic 0 is received at the output of receivers when the RS-485 pair is not driven by a driver.  If the receivers contain internal bias circuitry, they are connected such that the DC bias network aids this circuitry to produce a specific logic level at the output of the receivers when a differential RS-485 pair is not driven.  Drivers are connected such that they are logically consistant with the above.

For signals driven by the SRC Fanout module, the DC bias network is at the opposite end of the backplane from the SRC Fanout module.  For signals received by the SRC Fanout module, the DC bias network is nearest the SRC Fanout module.

Termination Network:

The termination network consists of a 120 ohm resistor connected across each differential RS-485 pair.

For signals driven by the SRC Fanout module, the termination network is at the end nearest the SRC Fanout module.  For signals received by the SRC Fanout module, the termination network is at the opposite end of the backplane from the SRC Fanout module.

Examples Of Link Use

Error Detection & System Recovery

Fast Control Signals To The SRC Fanout Module

Signal Definition & Level

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

VRB Crate J1 (Slow Control) Backplane (Serial) Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

SRC To FIB Crate (Fast Control & Timing) Links

The SRC To FIB Crate Link transmits both Fast Control information from the Trigger System Interface (and the SRC module) and Timing information from the Master Clock over a 1.06 Gigabits/second fiber optic link inmpemented with HP 2nd generation G-link ICs.  Multiple outputs on the SRC module are used to transmit fast control and timing information from the SRC module to each FIB Crate Fanout module.   The following sections gives details of these links.

Signal Definitions

The following table lists all Fast Control signals and Timing signals transmitted from the SRC module to each FIB crates over the SRC To FIB Crate links:

| # | Signal Name | Signal Definition |
| --- | --- | --- |
| 1 | SVX Clock | (See Table 6) |
| 2 | SYNC | (See Table 6) |
| 3 | Pipeline Capacitor Number (5:0) | 6-bit (0 - 41) SVX 3 IC pipeline capacitor number from ??? |
| 4 | Bunch Crossing Number (7:0) | 8-bit accelerator bunch crossing number from ??? |
| 5 | Advance Pipeline | ??? from ??? |
| 6 | Level 1 Trigger Accept | Indication from the Trigger System Interface of an accepted Level 1 trigger |
| 7 | Command (4:0) | ??? from Trigger System Interface and/or SRC module |

Table 9

SRC To FIB Crate Fast Control & Timing Signals

Question 16:	Should the Bunch Crossing Number be included?  See Table 7 and Note 3.

Who checks for P Cap # integrity and how is error indicated?  SRC has the Bunch Crossing # and sends it to FIBs where FIBs append it to data.  Bunch crossing COULD be sent to VRBs but ...  Pipeline Cap # sent only after SRC sends digitize & readout after sending L1A.  After

Advance Pipeline ... SRC always sending SYNC pulses.  If 132 ns, acquisition and readout EVERY time if 396 ns, 1/3 times.

Definitions of the Command (4:0) signals listed in Table 9 are given in Table 10.

| Command (4:0) | Command Definition |
| --- | --- |
| 00000 (0x00) | No operation |
| 00001 (0x01) | No operation |
| 00010 (0x02) | Preamplifier stop reset |
| 00011 (0x03) | Enter into data sampling mode |
| 00100 (0x04) | Preamplifier start reset |
| 00101 (0x05) | Read pipeline/digitize/readout |
| 00110 (0x06) | No operation |
| 00111 (0x07) | No operation |
| 01000 (0x08) | Stop data sampling clocks |
| 01001 (0x09) | Calibration inject |
| 01010 (0x0A) - 10000 (0x10) | No operation |
| 10001 (0x11) | Latch status |
| 10010 (0x12) | Reset SVX 3 ICs |
| 10011 (0x13) | Reset FIB module |
| 10100 (0x14) | Reset Port Card controller |
| 10101 (0x15) | Send Fill Frames on all G-links |
| 10110 (0x16) - 11111 (0x1F) | No operation |

Table 10

SRC To FIB Crate Commands

Question 17:	Does Table 10 contain correct and all commands needed in production components?

Note 8:	Wherever information is from another document/source (e.g., Table 10), add complete reference to that document/source.

Note 9:	The 53 MHz SVX Clock is derived at each FIB Crate Fanout module from the receipt of each Control/Timing Word and its G-link receiver phase-locked-loop.  The signalÕs duty cycle is 50% also because of the phase-locked-loop.

Control of the phase of the 53 MHz SVX Clock and SYCN signals relative to the master accelerator clock signal is accomplished within  the Master Clock System.  Phase of each signal can be individually varied in one nanosecond increments.

SYNC is true for one SVX Clock cycle whenever there is a potential p-pbar collision.  Depending upon the running conditions of the accelerator, this signal will occur in bursts each separated by either 132 or 396 nanoseconds.

Pipeline Capacitor Number is generated within the SRC module and is sent towards the detector as a global SVX system check that each SVX 3 IC is using the same Ôpipeline capacitor numberÕ and that this number is the same as that generated by the SRC module.  Each SVX 3 IC containing one or more hits transmits its Ôpipeline capacitor numberÕ used to attain the transmitted data.

Bunch Crossing Number ????

Advance Pipeline ????

Level 1 Trigger Accept is received by the SRC from the Trigger System Interface whenever the Level 1 Trigger System detects an accepted Level 1 trigger.

Command is a five-bit word sent by the Trigger System Interface.  ????

Link Transmission Format

****** Include link speed and word transmission rate information as well ******

The G-link ICs used in this link are configured to send a 16-bit data word every 18.9 nanoseconds (1 / 53 MHz).  Possible word configurations are given in Table 11.

| Control/Timing Word Bit # --> | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Control/Timing Word 3 | 1 | 1 |

S

Y

N

C

L

1

A

A

D

V

P

C

M

D

| 4 | CMD3 | CMD2 | CMD1 | CMD0 |
| --- | --- | --- | --- | --- |
| Control/Timing Word 2 | 1 | 0 |

S

Y

N

C

L

1

A

A

D

V

P

B

C

N

7

B

C

N

6

B

C

N

5

B

C

N

4

B

C

N

3

B

C

N

2

B

C

N

1

B

C

N

| 0 |
| --- |
| Control/Timing Word 1 | 0 | 1 |

S

Y

N

C

L

1

A

A

D

V

P

P

C

N

4

P

C

N

3

P

C

N

2

P

C

N

1

P

C

N

0

Control/Timing Word 0

| (No Operation) | 0 | 0 |
| --- | --- | --- |

Table 11

SRC To FIB Crate Control & Timing Words

Question 18:	Table 11 gives only possible Control/Timing words and their bit maps.  Is this the flexibility desired and/or required?  Is there a simpler implementation?

Connectors & Cables

Examples Of Link Use

Error Detection & System Recovery

FIB Crate (Fast Control & Timing) Backplane Link

****** Same signals as Table 9 but probably with AT&T PECL drivers & signal levels ******

Signal Definitions & Levels

Backplane Connector Pin Assignments

Backplane Signal DC Bias & Termination Networks

Examples Of Link Use

Error Detection & System Recovery

FIB To PC (Fast Control & Timing) Link

Test Port Card will be on WWW by Wednesday (see page 8 for commands)

Enter initialization mode, reset pre-amp, perform digitization and readout.

SM_CLK ... to send serial commands to PC

SR_CMD

SVX_FE_CLK ... analog acquisition

SVX_BE_CLK ... digital readout

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

SVX 3 IC Event Data/Control Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

Additional Event Data Links

PC To FIB Event Data Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

FIB to Optical Distribution Box (Splitter) Event Data Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

Optical Distribution Box To ERB Module Event Data Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

Optical Distribution Box To SVT Trigger Event Data Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

(Event Data) Resynchronization Link

Signal Definitions & Levels

Connectors & Cables

Terminations (If Any)

Examples Of Link Use

Error Detection & System Recovery

Aborting SVX Readout & System Recovery